# TOOL FOR PERFORMING PERIODIC INSPECTION OF ENERGY CONTROL PROCEDURES

Document #:      					Date of Inspection:

Actual Equipment Performed On:

Name of Authorized Worker(s) Performing Procedure:

Name of Authorized Inspector Performing Inspection:

Review and verify the following:

| Note: This Periodic Inspection is to be performed as an observation of actual work in progress. A demonstration or walkthrough is not an adequate means to determine the effectiveness of the procedure and the authorized worker’s understanding of the procedural implementation. |
| --- |
| Item | Yes | No | Comments |
| The procedure adequately removes all energy sources that prevent a hazard to the worker under the scope of the LOTO Procedure |  |  |  |
| The procedure is administratively accurate and complete. |  |  |  |
| The procedure includes all of the following elements: Scope, Purpose, Authorization, Steps that specify Shutdown procedures, isolation procedures, blocking procedures, procedures for placement and removal of locks/locking devices, specific requirements to test a machine and verify the effectiveness of energy control measures. |  |  |  |
| The lockout devices used conform to requirements (i.e red banded Master lock, tags of durable material, locking devices that prevent the removal without use of excessive force or unusual techniques, materials that are suited for the environment, specifically identifiable) |  |  |  |
| The authorized worker is current in LOTO training. |  |  |  |
| Comments: |

Observe the following:

| Item | Yes | No | Comments |
| --- | --- | --- | --- |
| The worker properly follows the procedure. |  |  |  |
| The worker properly applies the locks and tags. |  |  |  |
| The worker’s methods of verification that no hazards exist in the equipment are adequate. |  |  |  |
| For electrical zero energy verification, the worker tested the meter on a known source before and after the verification. |  |  |  |
| The worker informed affected workers appropriately before the equipment was shutdown and immediately after locks and tags were removed. |  |  |  |

Determine the adequacy of the Authorized Worker’s knowledge via discussion of the following items upon completion of the procedure:

| Item | Yes | No | Comments |
| --- | --- | --- | --- |
| The authorized worker’s responsibilities under this procedure. |  |  |  |
| The authorized worker’s responsibilities under the LOTO program. |  |  |  |

General Comments:

Strengths:

Weaknesses:

Corrective Actions Required (Each weakness identified must have a corrective action.  Except for specific non-compliance issues, the corrective actions should include the receipt of review of roles and responsibilities prior to allowing the authorized worker to perform additional LOTO procedures):

Periodic Inspection Completed:

Authorized Inspector Signature: ________________________

Return to the Authorized Worker’s Manager for review and retention.