## Slide 1: Improving spatial coverage while preserving blue noise
Mohamed S. Ebeida1
M. A. Awad2, X. Ge3, A. H. Mahmoud2, S. A. Mitchell1, P.M. Knupp1, and L. -Y. Wei4
1Sandia National Laboratories, 2Alexandria University,
3Ohio-State Univ, 4University of Hong Kong
Siam Conference on Geometric and Phsyical Modeling
November, 13th 2013

## Slide 2: Point Sets: Well-spaced
Well-spaced =
  Farthest Voronoi vertex (coverage) not much farther than closest Delaunay neighbor (free)
  Measured by Voronoi cell aspect ratio (A) or beta = rc / rf
  beta <= 1 is often the goal for uniform distributions
rc
rf/2
rf
rc = coverage farthest distance from domain point to sample point
rf = free
shortest distance between
sample points

## Slide 3: Point Sets: Random
Random with minimum separation (blue noise)
rf = rc
Random with no
constraints
(white noise)
Correlated
Points rf = rc

## Slide 4: Why Do We Care?!
Applications for Random Well Spaced point Sets

## Slide 5: Provably Good Meshing
Seismic Simulations
maximal helps Δ quality
  Physics simulations
    Voronoi mesh, cell = points closest to a sample
    Fractures occur on Voronoi cell boundaries
      Mesh variation models material strength variation
      CVT, regular lattices give unrealistic cracks
        Unbiased sampling gives realistic cracks
    Ensembles of simulations
    Domains: non-convex, internal boundaries
Courtesy of Joe Bishop (SNL)

## Slide 6: Motivating from Modern Graphics: Texture Synthesis
Real-time environment exploration. Games! Movies!
Algorithm to create output image from input sample
  Arbitrary size
  Similar to input
  No visible seams, blocks
  No visible, regular repeated patterns examples from wikipedia:
Spaghetti Li Yi Wei
SIGGRAPH 2011

## Slide 7: Robot Motion Planning
Real time motion planning 23 DOF
Pictures and results provided by: Chonhyon Park (Dinesh’s group)
Precomputed Well-Spaced points directs parallel tree expansion and enables real-time motion planning in higher dimensions

## Slide 8
  That was the applications!
…
Now for the algorithms!
How can we generate a random well spaced point set?

## Slide 9: … So We Need to Generate Random Well-Spaced Points. But How?!!  Maximal Poisson-Disk Sampling (MPS)
What is MPS?
  Insert random points into a domain, build set X
Ω
x4?
Disk-free condition
Bias-free condition
Maximal condition

## Slide 10: Simple Problem?!
My initial thoughts (2010):
Generate a bunch of disks in a box, sounds too
simple with minor impact!
Probably I will forget about it after this project.
I was Completely wrong!

## Slide 11: Main Published Results
First E(n log n) algorithm with provably correct output
  Efficient Maximal Poisson-Disk Sampling, Ebeida, Patney, Mitchell, Davidson, Knupp, Owens, SIGGRAPH 2011
Simpler, less memory, provably correct, faster in practice but no run-time proof
  A Simple Algorithm for Maximal Poison-Disk Sampling in High Dimensions, Ebeida, Mitchell, Patney, Davidson, Owens Eurographics 2012
Voronoi Meshes
  Sites interior, close to domain boundary are OK, not the dual of a body-fitted Delaunay Mesh
  Uniform Random Voronoi Meshes Ebeida, Mitchell IMR 2011
Delaunay Meshes
  Protect boundary with random balls
  Efficient and Good Delaunay Meshes from Random Points Ebeida, Mitchell, Davidson, Patney, Knupp, Owens SIAM GD/SPM 2011  Computer Aided Design
MPS with varying radii
  Adaptive and Hierarchical Point Clouds
  Variable Radii Poisson-disk sampling Mitchell, Rand, Ebeida, Bajaj CCCG 2012

## Slide 12: Main Published Results
Simulation of Propagating fractures
  Mesh Generation for modeling and simulation of carbon sequestration processes Ebeida, Knupp, Leung, Bishop, Martinez SciDAC 2011
Hyperplanes for integration, MPS and UQ
  K-d darts, Ebeida, Patney, Mitchell, Dalbey, Davidson, Owens, TOG “to appear”
Rendering using line darts
  High quality parallel depth of field using line samples, Tzeng, Patney, Davidson, Ebeida, Mitchell, Owens HPG 2012
Reducing Sample size while respecting sizing function
  A simple algorithm that replaces 2 disks with one while maintaining coverage and conflict conditions
  Sifted Disks Ebeida, Mahmoud, Awad, Mohammad, Mitchell, Rand, Owens EG 2013
MPS with improved Coverage
  Using rc < rf
  Improving spatial coverage while preserving blue noise Ebeida, Awad, Ge, Mahmoud, Mitchell, Knupp, Wei SIAM GD/SPM 2013  Computer Aided Design

## Slide 13: Prior Results: CCCG’11 How fast can radii vary?
If varies slowly
  bounded # neighbors for disk conflict checks <-> bounded-angle DT
If shrink too fast
  Unbounded # neighbors
  Infinite run-time
  Zero angles in triangulation
Still big, OK
Vanishing radius, infinite neighbors
α
α

## Slide 14: Q. How fast can it vary? A. Depends how Conflict is defined.
L is Lipschitz constant: f(x)-f(y) < L |x-y|
Bigger: small disk center inside big disk center
Smaller: big disk center inside small disk center
Bigger is stricter than
Sphere packing:
½ radius disks overlap distance: sum(r(x),r(y))/2
Four common methods in Graphics
Prior: new candidate disk center inside an old prior disk
Current: old prior disk center inside a new candidate disk
new
new
new
old
old
old
new
old

## Slide 15: Prior Results: CCCG’11 Decoupling coverage and conflict-free radii
Disk coverage radius larger than free radius
  Rc > Rf (yellow > green)
New disks must cover some unique uncovered area
  Else maximal (limit) distribution would be the same
  Contrast to Hard-core Strauss disc process: coverage disks are observed, no effect on process
Process:
New candidate point uniform at random
(f) Rejected if center inside a small green disk
(c) Accepted if its yellow disk covers some white area
reject, yellow already covered
OK, covers some white
reject, inside a green disk
Alg:
Only generate points in an outer approximation to regions satisfying (c) and (f) in the first place.

## Slide 16: Two-radii MPS output
Classic MPS Rf = Rc
Two-radii MPS 2 Rf = Rc
Rf = min center dist
Rc =max Vor dist
Uniform R = 0 non-maximal

## Slide 17: This Research: Improving spatial coverage
rc > rf increase randomness while degrading mesh quality
Here we try the opposite direction rf < rc
Question:
Can we decouple coverage radius
from disk-free radius such r_c < r_f ?

## Slide 18: Current Research: Sparse MPS (under preparation)
Answer: Yes, If the algorithm doesn’t lead to configurations
Like this.
Unfortunately!
Vey hard to achieve
via sampling due to
global constraints
Impact of solution:
A tune-up parameter
to trade randomness
For better space coverage
e.g. better mesh quality

## Slide 19: Our poor-man’s solution
Generate an MPS as usual and relocate points to optimize beta directly using Nelder Mead
Four rules for relocating a point:
Reflection
Expansion
Contraction
Reduction

## Slide 20: Results

## Slide 21: Results: Impact on Mesh Quality

## Slide 22: Impact on Noise

## Slide 23: Impact on Noise

## Slide 24: Results: Non-convex domains

## Slide 25: Results: Curved Surfaces

## Slide 26: Results: Curved Surfaces

## Slide 27: Results: Impact on bilateral filtering
Sub-sampling accelerated bilateral filtering. β = 0.75 achieves the right balance between uniformity (reducing noise) and randomness (avoiding aliasing). Notice the noisier results with less uniform sampling (β = 2.0) and more aliasing with more regular sampling (CVT and triangle tiling). For the skull and reflection cases, we show both the whole images and partial zoom-ins.

## Slide 28: Summary and Future Work
This paper introduced a Well-spaced Blue-noise Distribution WBD, with β = rc/rf measuring coverage uniformity or well-spacedness.
We proposed the Opt-β algorithm to change a random point set to a WBD; blue noise is preserved up to β ≈ 0.75.
Extension to higher dimensions esp. impact on slivers is our next step
Investigate sampling solutions to the Sparse MPS problem.

## Slide 29: Thanks! … Questions?