## Slide 1: Exploring High Dimensional Spaces with Hyperplane Sampling
Sandia is a multiprogram laboratory operated by Sandia Corporation, a Lockheed Martin Company, for the United States Department of Energy’s National Nuclear Security Administration under contract DE-AC04-94AL85000.
Speaker: Scott A. Mitchell
Appeared in journal
ACM Transactions on Graphics
January 2014
Notes: POF = probability of failure
Keep dart throwing game

## Slide 2: Major Points of Presentation
Connection to techniques, and applications, from fields besides UQ
Concepts
  Hyperplane sampling
    motivation, capture small thin regions
  Formula for changing point sampling to flat sampling
  Unbiased – provable
  Variance – experiments, efficiency
    hyperplane intersection with the object needs to be computable, efficient
    volume estimation experiments
      efficiency
      dart type
  Framework
    function averaging, integration
    finding a point with a function value (e.g. outside disks)
  Three applications
    Volume estimation
      function integration
    Generate a well-spaced point sampling a.k.a. Relaxed MPS
      find domain points with function values
    Depth of field with antialiasing
      function integration

## Slide 3
Motivation
Recall Mohamed Ebeida’s Talk

## Slide 4: Integration, Optimization and UQ
Sampling for
  Integration
  Uncertainty Quantification
  Global Optimization
  Surrogates
Probablity Of Failure (POF) Darts
Bridge Collapse safety calculations
  Dimensions: temperature, load, time of day, material strength, age…
  Run a simulation at a point,
  Disk radius = how far from failure you are
    Need more samples outside disks
    Overlap is inefficient, but OK
  Union Volume estimates failure probability
    Or integrate parameter distributions over the volume if non-uniform.
“Puff and Darts” game, circa 1902, courtesy FCIT.
Mohamed Ebeida
Scott Mitchell
Laura Swiler
“POF Darts” researchers hard at work, circa 2013.

## Slide 5
Reliability calculations
  Identify and measure tiny failure subspaces in a vast parametric space
    10+ dimensions (parameters)
    <10-6 PoF (small volume region)
    Expensive simulations – faster surrogate
  POF-Darts was adaptive sampling (to find small regions with particular properties)
  This talk is mainly about uniform sampling of regions (to measure them)
Approach
  Other sampling methods based on statistics and analysis
  We borrow Computational Geometry, Graphics concepts:
    line searches
    sample-neighborhoods, geometric balls
    functional integration

## Slide 6: Intuition Who’s going to hit the target (orange )?
public domain clip art
Clker.com
point sampling
line sampling
coin-shaped target
same volume, more surface
line sampling

## Slide 7: More precisely d=20, PoF = 10-6 (uniform distributions throughout talk)
16 parameters don’t matter 4 parameters matter
(½)5
domain
failure
1/2
all parameters equal
  Lines are more likely to hit than points
    better if coin-like (bigger surface area)
    better if tilted (surface area subtended by each line)
  Intersection length is more information than binary point inside/outside
    Planes are even better, hyperplanes...
1 in 106 points
7 in 106 axis lines
hit failure region
1 in 106 points
2 in 106 axis lines
hit failure region
ditto and tilted
1 in 106 points
30 in 106 axis lines
hit failure region
(½)5

## Slide 8: Hyperplane sampling to hit regions
99 points
6 line darts
1 plane dart
Lines, hyperplanes, are more likely to intersect these regions,
and they give more information
But they are more expensive.
Is it worth it?
The point of our paper is to answer “yes.”

## Slide 9
Approach, definitions

## Slide 10: k-d Dart
k-dimensional hyperplanes (flats)
  k free coordinates
  d-k fixed coordinates
dart = (d choose k) flats, one for every possible axis-aligned orientation
  free coordinates (orientations) deterministically uniform
  fixed coordinates (positions) uniform random, identically and independently distributed
one 1-d dart in a 2-d domain
= two 1-d lines: x-aligned, y-aligned

## Slide 11: k-d darts are unbiased
  I.e. the mean estimate is the true mean
Because each flat is unbiased
  because uniform point sampling of a height function is unbiased
f=1
f=0
height fDfixed
Dfree
Dfixed

## Slide 12: Variance? Efficiency?
We have no formal proof for the variance
Test problem:
  estimating the volume of an ellipsoid
  known analytic volume.
Results: variance is well behaved
  dropping as 1/number_of_samples^2
  dropping by k

## Slide 13: Mean error reduction by 1 / # samples^2 Vary 10-d domain aspect ratio, orientation; k-dart-dimension. lower error for higher-k darts
coin-like
needle-like
randomly oriented object
axis-aligned object
k
k
object orientation doesn’t matter very much
error needle ≈ coin > ball with bigger volume, small efffect
slope 1/2
Notes: As k increases, the error goes down
top row
Needles and coins with 1-axis stetched did about the same
Points+ did better for the ball, because it had bigger volume.
bottom row
Object orientation had little effect

## Slide 14: Estimate/true volume histograms for 1 million darts Vary 10-d domain aspect ratio, orientation; k-dart-dimension normal-like, sharper peaks for higher-k darts
coin-like
needle-like
k
randomly oriented object
axis-aligned object
object orientation unaligned with axes helps a little, but not much
Squish matters a little bit, but volume matters much more. We did 1-axis short, 1-axis long. Squish farther?
Notes: histograms, constant number of samples
sharper for increased k, consistent with more information per sample
Squish, orientation, tiny effect compared to volume

## Slide 15: Trends by k
Conclusion
Higher k darts = less error, less variance
  Because each dart gives more information
Use a higher k if
  You can compute its intersection with the object
  And that computation is not too much slower

## Slide 16: Sample-Orientation Effects? Axis-aligned flats just as accurate as randomly oriented darts...
...and faster and simpler.
Axis-aligned best.
Mean error by #samples
Histogram of estimate, 1 million samples
black=point samples
red=axis-aligned,
one per direction
blue=random orientation,
independent
green=random orientation,
one per orthogonal
coin-like
needle-like
randomly oriented object
axis-aligned object
Notes: (top line is points)
aligned-darts better, for aligned objects
aligned-darts same as randomly oriented darts, for randomly oriented objects

## Slide 17: Dart orientation effects
Conclusion
(d choose k) orthogonal flats deterministically ≈ randomly
  perhaps because we used so many samples.
  random simpler?
axis-aligned provides
  good quality answers
  simple, fast, through parameter substitution
Use random-axis orientations, of independent flats
1st
2nd
p=1/2
p=1/2
≈
deterministic
random

## Slide 18
Application 1 of 3
Volume Estimation
LHS patterns
More interesting functions

## Slide 19: Volume Estimation Speedup 3-d ball, simple analytic
0-d
1-d
2-d
Algorithm: average lengths of lines (area of planes) inside sphere.
Why did this work so well?

## Slide 20: Volume Estimation Speedup Circular Parabola
i.e. 2d domain
1E-5 analytic value
speedup
Notes: lines vs. points
more speedup the more accurate you want your answer
more speedup in low dimensions than high, because lines reduce problem by 1-d, and d/(1-d) is a more significant fraction in low-d than high-d

## Slide 21: Volume Estimation Speedup Planar Cross
Estimate volume of y(x) < 0
i.e. 2d domain
1E-5 analytic value
Notes: Ultimate coin-like shape, every line intersects

## Slide 22
Application 2 of 3
Well-spaced points
Use line sampling to generate a point sampling,
of a type popular in Graphics texture mapping

## Slide 23: Maximal Poisson-Disk Sampling
Defined as the limit distribution of a statistical “dart-throwing” process
  Random disks arive with Poisson-distributed arrival times, equivalent to random arrival order:
Ω
x4?

## Slide 24: Main Challenge of Solving MPS in Higher Dimensions (Curse-Of-Dimensionality)
It is too expensive to build the uncovered regions
  or even an approximation to them
Curse of dimensionality
  Natural: Kissing Number grows exponentially with dimension
  Artificial: Grid based methods (state of the art) to retrieve neighbors, and track remaining voids
    grid size is 2^d
Generalization of Sampling Entities
  k-d darts: Random sampling using hyperplanes
   void capturing, integration and UQ

## Slide 25: k-d Dart based Relaxed Poisson-Disk Sampling
Dart-based
  search space using lines, planes, ...
Relaxed
  stop after many successive dart fails
  expected uncovered volume is small

## Slide 26: Spectral Quality Evaluation of Point Sets
Maximal Poisson Disks
White noise
Maximal Correlated Disks

## Slide 27: MPS vs. line-dart vs. point-dart Can you tell them apart?
distance non-uniformity
angular non-uniformity
line darts
point darts
true MPS

## Slide 28: k-d Dart Relaxed MPS Properties
better quality line darts produce fewer large gaps
than point darts
line darts add disks faster
than point darts
line darts are faster or slower than MPS in d=4,
depending on relaxed maximality
Simple MPS requires 2d memory, intractable in d>6
but line-darts are linear memory

## Slide 29
Application 3 of 3
Graphics, depth of field blur
Integration

## Slide 30: Graphics Application Depth of Field Sampling
Pixar’s Toy Story 3
Depth-of-Field blur
requires many point samples
per pixel !
movie frame rendering is overnight, not realtime, as many simulation and UQ studies
blurred
far from lens
focal plane
Notes: Because our eyes have lenses we can only see one distance clearly at a time
Is this a defect?
Putting this into movies makes them seem more realistic
clues us to object depth
clues us to where director wants our attention (opening scene of Avitar)

## Slide 31: Line-sampling for Depth of Field Blur
  Solution: point sampling
  For every (a,b) pixel
  4-d: (u,v) lens plane, (x,y) scene space
    z scene space is dependent
Solution: our algorithm
  Lines sample and compute
  occlusion depth (decision) color contribution (integration)
  (x,y,z) scene
  (u,v) lens
  (a,b) pixel
  For each pixel,
  1 Dart = 4 axis-aligned sample lines in (u, v, x, y)
    1 varied u, fixed x, y, v
    1 varied v, fixed x, y, u
    1 varied x, fixed y, u, v
    1 varied y, fixed x, u, v

## Slide 32: Blur, line-darts vs. point samples
64 points
4 points
256 points
16 lines
30 lines
4 lines

## Slide 33
16 lines / pixel
1024 points /pixel
8x runtime
256 points /pixel
2x runtime
Notes: 16 lines faster than 1024 points
16 lines better quality than 256 points

## Slide 34: Summary
Any point-sampling algorithm depending on function averages can be converted to a line-sampling algorithm
  Including indicator functions e.g. volume estimation
f=1
f=0
height fDfixed
Dfixed
  Need to evaluate function along a flat (line)
  Efficiency depends on evaluation speed
    This is the challenge for practical k-dimensional flats
  Axis-aligned flats (lines)
    efficient and random-enough
Application variants
  Generate a well-spaced disk packing
    Although line samples are not uniform by area, effect on output distribution is unoticable.
  Depth of Field blur
    Intrusive line-sampling
    Efficient function integration without artifacts

## Slide 35: Extra stuff

## Slide 36: Heilmeier’s Catechism
What is the problem, why is it hard?
  Uncertainty quantification, small failure regions in vast spaces, expensive functions
How is it solved today?
  Many sampling methods based on statistics and analysis
What is the new technical idea; why can we succeed now?
  Borrowing Computational Geometry, Graphics concepts:
    line searches
    sample-neighborhoods, geometric balls
    functional integration
What is the impact if successful?
  Increased convergence rates, fewer parallel simulations

## Slide 37: a computational geometer’s view Space for All Point Sampling Methods
Spatial Randomness
Geometric Density
Discrete Density
injection
sifting
off-centers
uniform-random coordinates
MPS
jittering
optimization
CVT
Dimension
Delaunay refinement
maximal Poisson-disk sampling
Opt-β, spatially-varying MPS
bubble mesh
joint position and sample optimization
two-radii MPS
Process randomness is a hidden axis,
merely a means to obtain spatial randomness.

## Slide 38: k-d Darts for Solving MPS