## Slide 1: The Schwarz Alternating Method for Multi-Scale Coupling and Contact in Solid Mechanics
Alejandro Mota1, Irina Tezaur1, Jonathan Hoy2
1Sandia National Laboratories, 2University of Southern California
PANACM 2021
November 9-12, 2021
SAND2021-12680C

## Slide 2: Motivation
Existing methods for contact enforcement (penalty, Lagrange multiplier, augmented Lagrangian) suffer from poor performance!
  Long simulation times
  Lack of accuracy
  Lack of robustness
Large scale structural failure frequently originates from small scale phenomena (e.g, defects, microcracks, inhomogeneities), which grow quickly in unstable manner
  Concurrent multi-scale methods are essential to capture correctly the multi-scale behavior!
  Stable, accurate and robust methods for simulating mechanical contact (touching surfaces, sliding, tightened bolts, impact) are equally important!
Above: roof failure of Boeing 737 aircraft due to fatigue cracks. From imechanica.org
This talk: new approach for simulating multi-scale mechanical contact using the Schwarz alternating method.
Above: gears in contact within MEMS device. From sandia.gov/media

## Slide 3: Schwarz Alternating Method for Domain Decomposition
Proposed in 1870 by H. Schwarz for solving Laplace PDE on irregular domains.
H. Schwarz (1843–1921)
Initialize:
Solve PDE by any method on w/ initial guess for transmission BCs on .
Iterate until convergence:
Solve PDE by any method on w/ transmission BCs on based on values just obtained for .
Solve PDE by any method on w/ transmission BCs on based on values just obtained for .
Crux of Method: if the solution is known in regularly shaped domains, use those as pieces to iteratively build a solution for the more complex domain.
Basic Schwarz Algorithm
2Lions, 1990. 3Zanolli et al., 1987.
overlapping
non-overlapping

## Slide 4: Schwarz Alternating Method for Domain Decomposition
Proposed in 1870 by H. Schwarz for solving Laplace PDE on irregular domains.
H. Schwarz (1843–1921)
Initialize:
Solve PDE by any method on w/ initial guess for transmission BCs on .
Iterate until convergence:
Solve PDE by any method on w/ transmission BCs on based on values just obtained for .
Solve PDE by any method on w/ transmission BCs on based on values just obtained for .
Crux of Method: if the solution is known in regularly shaped domains, use those as pieces to iteratively build a solution for the more complex domain.
2Lions, 1990. 3Zanolli et al., 1987.
Overlapping Schwarz: convergent with all-Dirichlet transmission BCs1 if .
Non-overlapping Schwarz: convergent with Robin-Robin2 or alternating Neumann-Dirichlet3 transmission BCs.
1Schwarz, 1870; Lions, 1988.
overlapping
Basic Schwarz Algorithm

## Slide 5: Schwarz Alternating Method for Domain Decomposition
Proposed in 1870 by H. Schwarz for solving Laplace PDE on irregular domains.
H. Schwarz (1843–1921)
Initialize:
Solve PDE by any method on w/ initial guess for transmission BCs on .
Iterate until convergence:
Solve PDE by any method on w/ transmission BCs on based on values just obtained for .
Solve PDE by any method on w/ transmission BCs on based on values just obtained for .
Crux of Method: if the solution is known in regularly shaped domains, use those as pieces to iteratively build a solution for the more complex domain.
2Lions, 1990. 3Zanolli et al., 1987.
Overlapping Schwarz: convergent with all-Dirichlet transmission BCs1 if .
Non-overlapping Schwarz: convergent with Robin-Robin2 or alternating Neumann-Dirichlet3 transmission BCs.
z: convergent with Robin-Robin2 or alternating Neumann-Dirichlet3 transmission BCs.
1Schwarz, 1870; Lions, 1988.
2Lions, 1990. 3Zanolli et al., 1987.
non-overlapping
Basic Schwarz Algorithm

## Slide 6: How We Use the Schwarz Alternating Method
AS A PRECONDITIONER FOR THE LINEARIZED SYSTEM
AS A SOLVER FOR THE COUPLED
FULLY NONLINEAR PROBLEM
6

## Slide 7: Overlapping Schwarz for Multi-scale Coupling in Solid Mechanics
The Schwarz alternating method has been developed/implemented for concurrent multi-scale quasistatic & dynamic modeling in Sandia’s Albany/LCM and Sierra/SM codes.
Displacement
Velocity
1Mota et al., 2017; Mota et al., 2021.
Coupling is concurrent (two-way)
No nonphysical artifacts and theoretical convergence properties1
“Plug-and-play” framework: couples different meshes, element types, solvers, integrators
Easy to implement in existing HPC codes, and scalable, fast, robust
 | CPU times | # Schwarz iters
Single | 3h 34m | 
Schwarz | 2h 42m | 3.22
 | CPU times | # Schwarz iters
 | 3h 34m | 
Schwarz | 2h 42m | 3.22

## Slide 8: Non-Overlapping Schwarz Formulation for Contact Mechanics
Before contact: simulation proceeds as usual
Detection of contact: proximity search and application of contact conditions to determine contact
Overlap condition: triggered when two or more objects/domains have begun to overlap/penetrate each other
Push condition: triggered when both of the following properties hold
  Compression: the tractions at the interface are compressive
  Sustainability: there was contact in the previous time step
Enforcement of contact: alternating Schwarz iteration with Dirichlet-Neumann transmission BCs
Key idea: a contact problem can be viewed as coupled problem while 2+ bodies are in contact
Notes: Key idea: the contact problem can be viewed as a coupled problem while the 2+ bodies are in contact

## Slide 9: Non-Overlapping Schwarz Formulation for Contact Mechanics
Before contact: simulation proceeds as usual
Detection of contact: proximity search and application of contact conditions to determine contact
Overlap condition: triggered when two or more objects/domains have begun to overlap/penetrate each other
Push condition: triggered when both of the following properties hold
  Compression: the tractions at the interface are compressive
  Sustainability: there was contact in the previous time step
Enforcement of contact: alternating Schwarz iteration with Dirichlet-Neumann transmission BCs
There are no contact constraints!
Contact constraints replaced with BCs applied iteratively at contact boundaries.
Notes: Key idea: the contact problem can be viewed as a coupled problem while the 2+ bodies are in contact

## Slide 10: Numerical Results: 1D Impact Problem1
Impact of two 1D identical linear elastic prismatic rods discretized using linear elements with exact analytic solution [Carpenter et al., 1991]
Schwarz alternating method compared to three conventional contact algorithms with a zero gap contact constraint
  Implicit and explicit penalty method with penalty parameter
  Forward increment (explicit) Lagrange multiplier (LM) method [Carpenter et al., 1991]
Time stepper: Newmark-beta
  Schwarz couplings included Explicit-Explicit, Implicit-Explicit and Implicit-Implicit
  used for all methods except Implicit-Explicit Schwarz, which uses in explicit domain.
1Hoy et al., 2021; Mota et al. (in prep), 2021.

## Slide 11: Numerical Results: 1D Impact Problem1
Penalty methods overpredict contact point location between impact and release times
Explicit LM method under-predicts release time
Schwarz methods capture release time to an accuracy of 0.1%.
1Hoy et al., 2021; Mota et al. (in prep), 2021.
Contact point position: of the right-most node of left bar () as a function of time

## Slide 12: Numerical Results: 1D Impact Problem1
1Hoy et al., 2021; Mota et al. (in prep), 2021.
Mass-averaged velocity: of the left bar () as a function of time
Similar conclusions can be drawn from mass-averaged velocity
Schwarz variants calculate mass-averaged velocity to a sufficiently greater accuracy than any of the conventional methods, especially near the time of release

## Slide 13: Numerical Results: 1D Impact Problem1
Total energy relative error: for the left bar () as a function of time
1Hoy et al., 2021; Mota et al. (in prep), 2021.
Total energy should be conserved for this problem
Total energy error is negative for all 6 methods all methods are stable.
All three conventional methods exhibit total energy loss of up to 9% following contact.
Unlike conventional contact methods, Schwarz achieves an error of at most 0.25% in the total energy!
  Explicit-Explicit Schwarz gives most accurate total energy, followed by Implicit-Implicit Schwarz and Implicit-Explicit Schwarz

## Slide 14: Numerical Results: 1D Impact Problem1
1Hoy et al., 2021; Mota et al. (in prep), 2021.
Contact point force: for the left bar () as a function of time
Three conventional methods exhibit some undesirable artifacts in contact point force but deliver in general a smooth solution
Schwarz solutions exhibit oscillations following instantiation of contact “chatter” problem
  Schwarz method with largest total energy loss (Implicit-Explicit) exhibits least amount of chatter
  Energy dissipation is necessary for establishment of persistent contact [Solberg et al., 1998]
    Chatter problem can likely be mitigated through addition of numerical dissipation
Notes: Chatter = loss/subsequent reestablishment of contact

## Slide 15: Summary & Future Work
Summary:
The Schwarz alternating method was shown to be an effective multi-scale coupling method in solid mechanics
The Schwarz alternating method has shown promise as a novel technique for simulating multi-scale mechanical contact
  Contact constraints are replaced with transmission BCs applied iteratively on contact boundaries
  Schwarz method delivers substantially more accurate solution than conventional contact approaches in contact point displacement, mass-averaged velocity, impact time, release time, and kinetic, potential total energies
  An unfortunate consequence of the method’s ability to conserve energy so well appears to be the introduction of chatter in contact point velocity and force.
Ongoing/future work:
Introduction of dissipation and/or numerical relaxation to mitigate chatter problem
Introduction of additional or alternate contact constraints into Schwarz formulation
Comparison to conventional contact formulations with zero gap rate constraint
Implementation/evaluation of the Schwarz alternating method in multi-D
  Requires the development of operators for consistent transfer of contact traction BCs using concept of prolongation/restriction

## Slide 16: References
H. Schwarz, Uber einen Grenzubergang durch alternierendes verfahren, Vierteljahrsschriftder Naturforschenden Gesellschaft in Zurich, 15 (1870), pp. 272–286.
P.L. Lions. “On the Schwarz alternating method I.” In: 1988, First International Symposium on Domain Decomposition methods for Partial Differential Equations, SIAM, Philadelphia.
P. L. Lions, On the Schwarz alternating method III: A variant for nonoverlapping subdomains, in Third International Symposium on Domain Decomposition Methods for Partial Differential Equations, T. F. Chan, R. Glowinski, J. P´eriaux, and O. B. Widlund, eds., Society for Industrial and Applied Mathematics, 1990, pp. 202–223
P. Zanolli, Domain decomposition algorithms for spectral methods, CALCOLO, 24 (1987), pp. 201–240.
A. Mota, I. Tezaur, and C. Alleman, The Schwarz alternating method, Comput. Meth. Appl. Mech. Engng., 319 (2017), pp. 19–51.
A. Mota, I. Tezaur, and G. Phlipot, The Schwarz alternating method for transient solid dynamics, Int. J. Numer. Meth. Engng. (under review).
N. J. Carpenter, R. L. Taylor, and M. G. Katona, Lagrange constraints for transient finite element surface contact, International journal for numerical methods in engineering, 32 (1991), pp. 103–128.
J. Hoy, I. Tezaur, A. Mota. The Schwarz alternating method for multi-scale contact mechanics. CSRI Summer Proceedings 2021 (in press).
A. Mota, I. Tezaur, J. Hoy. The Schwarz alternating method for multi-scale contact mechanics. Mathematical & Computational Applications (MCA) (in prep).
J. M. Solberg and P. Papadopoulos, A finite element method for contact/impact, Finite Elements in Analysis and Design, 30 (1998), pp. 297–311.
I. Tezaur, T. Voth, J. Niederhaus, J. Robbins, and J. Sanchez, An extended finite element method (XFEM) formulation for multi-material Eulerian solid mechanics in the Alegra code (in preparation).

## Slide 17: Start of Backup Slides

## Slide 18: Motivation
Two-step process to the computational simulation of contact:
Proximity search: computer science problem, has received much attention due to importance in video game development 
Contact enforcement step: existing methods (penalty, Lagrange multiplier, augmented Lagrangian) suffer from poor performance 
  Long simulation times 
  Lack of accuracy 
  Lack of robustness 
Large scale structural failure frequently originates from small scale phenomena (e.g, defects, microcracks, inhomogeneities), which grow quickly in unstable manner
  Concurrent multiscale methods are essential to capture correctly the multiscale behavior!
  Stable, accurate and robust methods for simulating mechanical contact (touching surfaces, sliding, tightened bolts, impact) are equally important!
Above: roof failure of Boeing 737 aircraft due to fatigue cracks. From imechanica.org
This talk.
Above: gears in contact within MEMS device. From sandia.gov/media

## Slide 19: Schwarz Alternating Method for Domain Decomposition
Proposed in 1870 by H. Schwarz for solving Laplace PDE on irregular domains.
H. Schwarz (1843 – 1921)
Initialize:
Solve PDE by any method on w/ initial guess for Dirichlet BCs on .
Iterate until convergence:
Solve PDE by any method (can be different than for ) on w/ transmission BCs on that are the values just obtained for .
Solve PDE by any method (can be different than for ) on w/ transmission BCs on that are the values just obtained for .
Crux of Method: if the solution is known in regularly shaped domains, use those as pieces to iteratively build a solution for the more complex domain.
Basic Schwarz Algorithm
Schwarz alternating method most commonly used as a preconditioner for Krylov iterative methods to solve linear algebraic equations.
Novel idea: using the Schwarz alternating as a discretization method for solving multi-scale partial differential equations (PDEs).

## Slide 20: Enforcement of Contact via Alternating Schwarz
Step 0: Initialize
Controller time stepper
Time integrator for W1
Time integrator for W2
Key idea: a contact problem can be viewed as coupled problem while 2+ bodies are in contact

## Slide 21: Enforcement of Contact via Alternating Schwarz
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Controller time stepper
Time integrator for W1
Time integrator for W2
Integrate using
Interpolate from to
Key idea: a contact problem can be viewed as coupled problem while 2+ bodies are in contact

## Slide 22: Enforcement of Contact via Alternating Schwarz
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Step 2: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times .
Controller time stepper
Time integrator for W1
Time integrator for W2
Integrate using
Interpolate from to
Key idea: a contact problem can be viewed as coupled problem while 2+ bodies are in contact

## Slide 23: Enforcement of Contact via Alternating Schwarz
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Step 2: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times .
Step 3: Check for convergence at time .
Controller time stepper
Time integrator for W1
Time integrator for W2
Key idea: a contact problem can be viewed as coupled problem while 2+ bodies are in contact

## Slide 24: Enforcement of Contact via Alternating Schwarz
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Step 2: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times .
Step 3: Check for convergence at time .
If unconverged, return to Step 1.
Controller time stepper
Time integrator for W1
Time integrator for W2
Interpolate from to
Integrate using
Key idea: a contact problem can be viewed as coupled problem while 2+ bodies are in contact
Notes: Controller time-stepper – defines global dTs at which subdomains are synchronized

## Slide 25: Enforcement of Contact via Alternating Schwarz
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Step 2: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times .
Step 3: Check for convergence at time .
If unconverged, return to Step 1.
If converged, set and return to Step 1.
Controller time stepper
Time integrator for W1
Time integrator for W2
Integrate using
Interpolate from to
Can use different integrators with different time steps within each domain!
Key idea: a contact problem can be viewed as coupled problem while 2+ bodies are in contact

## Slide 26: Numerical Results: 1D Impact Problem1
Potential energy: for the left bar () as a function of time
1Hoy et al., 2021; Mota et al. (in prep), 2021.
Similar conclusions can be drawn from potential energy plots.
All three conventional methods underpredict peak potential energy by 10%.
Schwarz solutions capture peak potential energy with relative error 0.1%

## Slide 27: Numerical Results: 1D Impact Problem1
Potential energy: for the left bar () as a function of time
1Hoy et al., 2021; Mota et al. (in prep), 2021.
Similar conclusions can be drawn from potential energy plots.
All three conventional methods underpredict peak potential energy by 10%.
Schwarz solutions capture peak potential energy with relative error 0.1%

## Slide 28: Numerical Results: 1D Impact Problem1
Contact point velocity: for the left bar () as a function of time
1Hoy et al., 2021; Mota et al. (in prep), 2021.
Similar results are seen in the contact point velocity
It may be possible to reduce amount of chatter in Schwarz solutions by introducing numerical dissipation into the method.
Notes: Chatter = loss/subsequent reestablishment of contact

## Slide 29: Numerical Results: 1D Impact Problem1
Convergence of Schwarz methods
1Hoy et al., 2021; Mota et al. (in prep), 2021.
Mesh convergence of kinetic energy for left bar () when
# Schwarz iterations required for convergence (200, )
Convergence rates are comparable to published results [Tezaur et al., 2021]
At most 5 Schwarz iterations are needed for convergence
  Explicit-Explicit Schwarz variant requires fewest # iterations for convergence
Notes: Chatter = loss/subsequent reestablishment of contact