## Slide 1: The Schwarz Alternating Method for Concurrent Multiscale Coupling in Solid Mechanics
Beam geometry that is clamped on both sides and has a Gaussian initial condition for the z-displacement.
Alejandro Mota1, Irina Tezaur2, Coleman Alleman1
Motivation for Concurrent Multiscale Coupling
Schwarz Alternating Method for Domain Decomposition
Schwarz Alternating Method for Multiscale Coupling
Four Variants of Schwarz Alternating Method for Quasistatics
Schwarz Alternating Method for Dynamics
Implementation within Albany Finite Element Code
Proof of Convergence for Finite-Deformation Solid Mechanics
Large scale structural failure frequently originates from small scale phenomena such as defects, microcracks, inhomogeneities and more, which grow quickly in unstable manner.
Failure occurs due to tightly coupled interaction between small scale (stress concentrations, material instabilities, cracks, etc.) and large scale (vibration, impact, high loads and other perturbations).
Roof failure of Boeing 737 aircraft due to fatigue cracks. From imechanica.org
Surface flaw in pressure vessel: interacts with microstructure, which may or may not lead to failure.
Concurrent multiscale methods are essential for understanding and prediction of behavior of engineering systems when a small scale failure determines the performance of the entire system.
Simple idea: if the solution is known in regularly shaped domains, use those as pieces to iteratively build a solution for the more complex domain.
Initialize:
Solve PDE by any method on W1 w/ initial guess for Dirichlet BCs on G1.
Iterate until convergence:
Solve PDE by any method (can be different than for W1) on W2 w/ Dirichlet BCs on G2 that are the values just obtained for W1.
Solve PDE by any method (can be different than for W2) on W1 w/ Dirichlet BCs on G1 that are the values just obtained for W2.
Requirement for convergence:
Basic Schwarz Algorithm
Proposed in 1870 by H. Schwarz for solving Laplace PDE on irregular domains.
H. Schwarz (1843 – 1921)
Schwarz alternating method most commonly used as a preconditioner for Krylov iterative methods to solve linear algebraic equations.
Novel idea: using the Schwarz alternating as a discretization method for solving multi-scale partial differential equations (PDEs).
Conceptually very simple.
Allows the coupling of regions with different non-conforming meshes, different element types, and different levels of refinement.
Information is exchanged among two or more regions, making coupling concurrent.
Different solvers can be used for the different regions.
Different material models can be coupled provided that they are compatible in the overlap region.
Simplifies the task of meshing complex geometries for the different scales.
Advantages:
Pseudo-code for Quasistatics:
S. L. Sobolev (1936): posed Schwarz method for linear elasticity in variational form and proved method’s convergence by proposing a convergent sequence of energy functionals.
S. G. Mikhlin (1951): proved convergence of Schwarz method for general linear elliptic PDEs.
A. Mota, I. Tezaur, C. Alleman (2017)*: derived a proof of convergence of the alternating Schwarz method for the finite deformation quasistatic nonlinear PDEs (assuming the energy functional defined below is quasi-convex), and determined a geometric convergence rate for the finite deformation quasistatic problem.
-
Using the Schwarz alternating as a discretization method for PDEs is natural idea with a sound theoretical foundation.
* A. Mota, I. Tezaur, C. Alleman. "The Schwarz Alternating Method in Solid Mechanics", Comput. Meth. Appl. Mech. Engng. 319 (2017), 19-51.
Full Schwarz
Least-intrusive variant: by-passes Schwarz iteration, no need for block solver.
Inexact Schwarz
Modified Schwarz
Monolithic Schwarz
In the literature, Schwarz method is applied to dynamics by using space-time discretizations – unfeasible given design of our current codes and size of simulations.
Our extension of Schwarz coupling to dynamics uses a governing time stepping algorithm that controls time integrators within each domain.
Can use different integrators (e.g., implicit, explicit) with different time steps in each domain.
Controller time stepper
Time integrator for W1
Time integrator for W2
Component-based design for rapid development of capabilities.
Extensive use of libraries from the open-source Trilinos project.
  Use of the Phalanx package to decompose complex problem into simpler problems with managed dependencies.
  Use of the Sacado package for automatic differentiation.
  Use of Teko package for block preconditioning.
  Performance portability to GPUs and KNLs via Kokkos.
Parallel implementation of Schwarz uses the Data Transfer Kit (DTK).
https://github.com/trilinos/trilinos
https://github.com/gahansen/Albany
https://github.com/ORNL-CEES/DataTransferKit
Numerical Results: Quasistatics
Numerical Results: Dynamics
1D bar with area proportional to square root of length with strong singularity on left end of bar and simple hyperelestic material model with no damage.
Test case goals: explore viability of 4 variants of Schwarz alternating method, test convergence (expect faster convergence in less iterations w/ increased overlap).
Foulk’s Singular Bar
Cuboid
Notched Cylinder
Notched cylinder stretched along its axial direction, Neohookean-type material model.
Coupling of fine tetrahedral mesh (near notch) with coarse hexahedral mesh.
Relative errors
Rubik’s Cube
Two distinct bodies, the component scale & the microstructural scale, are coupled iteratively with alternating Schwarz
microstructural
scale
axial
stress
component
scale
Laser Weld
Clamped Beam
Bolted Joint
Isotropic elasticity & J2 plasticity with linear isotropic hardening.
3 subdomains.
50% reduction in problem size.
Near perfect strong scaling.
Linear elastic clamped beam with Gaussian initial condition for the -displacement.
Nonlinear elastic bar subjected to high degree of torsion.
Dynamic Schwarz method is used to couple two regions of the bar using different mesh resolutions, different element types, and different time integration schemes, once more without introducing any dynamic artifacts.
Relative errors are O(1%) w.r.t. reference solution for composite tet 10 - hex coupling.
Torsion
1 Mechanics of Materials Department, Sandia National Laboratories, Livermore, CA USA.
2 Extreme Scale Data Science & Analytics, Sandia National Laboratories, Livermore, CA USA.
SAND2018-1489C
Multi-scale problem of practical scale: coupling 85K composite tet 10 element mesh (bolts, ) with 56K hex element mesh (parts, ).
Neohookean material model: steel bolts and base, remaining parts are aluminum.
Lateral displacement load applied at top: applies compression to 2 bolts, tension to remaining 2.
(a)
(b)
Acknowledgements: Support for this work was received through the DOE ASC program at SNL. The writers wish to acknowledge J. Foulk, G. Hansen, J. Ostien, A. Salinger and D. Ibanez for their contributions to this work.
Coupling of two cuboids with square base w/ Neohookean-type material model.
Schwarz alternating method converges linearly.
There is faster linear convergence with increasing overlap volume fraction.
(a) Schematic
(b) Entire domain
(c) Fine region
(d) Coarse region
(a) Schematic showing geometry and domain decomposition
(b) Equivalent plastic strain: plastic deformation concentrated at top of notch.
-displacement
-displacement
-displacement
Coupling introduces no dynamic artifacts & energy is conserved throughout simulation!
(a)
(b)