## Slide 1: Stabilization of Galerkin Reduced Order Models (ROMs) for LTI Systems Using Controllers
Irina Kalashnikova1, Bart G. van Bloemen Waanders1, Srinivasan Arunajatesan2, Matthew F. Barone2
1 Numerical Analysis & Applications Department, Sandia National Laboratories, Albuquerque, NM, U.S.A.
2 Aerosciences Department, Sandia National Laboratories, Albuquerque NM, U.S.A.
SIAM Conference on Control and Its Applications (CT13)
San Diego, California
July 8 - 10, 2013

## Slide 2
Why Develop a Reduced Order Model
(ROM)?
High-fidelity modeling is often too expensive for use in a design or analysis setting!
A Reduced Order Model (ROM) is a surrogate model that aims to capture the essential dynamics of a full numerical model but with far fewer dofs.
Example Applications of ROMs:
Aeroelastic flutter analysis.
System modeling for active flow control.
Design/analysis of microelectromechanical devices and systems (MEMS) under electric actuation.
1/21

## Slide 3
Proper Orthogonal Decomposition (POD)/Galerkin
Method to Model Reduction
2/21

## Slide 4
Step 1: Proper Orthogonal Decomposition (POD)
Algorithm (a.k.a., “Method of Snapshots”)
Collect snapshots of a solution vector . Place these snapshots into the columns of a matrix defined by
, …,
2. Select an inner product to build the reduced basis in, e.g., the inner product.
3. Compute the SVD of the matrix
4. A reduced POD basis of size is given by
)
5. Orthonormalize and return the reduced basis.
Truncated POD basis describes more energy (on average) of the snapshot set than any other linear basis of the same dimension .
# of dofs in high-fidelity simulation
# of snapshots
# of dofs in ROM
(, )
3/21

## Slide 5
Step 2: Galerkin Projection
LTI Full Order Model (FOM)
Approximate solution as a linear combination of the POD modes obtained in Step 1:
2. Project FOM system onto the modes in some inner product, e.g., the inner product to obtain…
ROM solution
LTI Reduced Order Model (ROM)
dofs
dofs
4/21

## Slide 6
Stability Issues of POD/Galerkin ROMs
LTI Full Order Model (FOM)
LTI Reduced Order Model (ROM)
ROM LTI system matrices given by:
,
Problem: stable stable!
There is no a priori stability guarantee for POD/Galerkin ROMs.
Stability of a ROM is commonly evaluated a posteriori – RISKY!
ROM instability of POD/Galerkin ROMs is a real problem in some applications (e.g., compressible flow).
5/21

## Slide 7
1. ROMs which derive a priori a stability-preserving model reduction framework (usually specific to an equation set).
  ROMs based on projection in special ‘energy-based’ (not ) inner products, e.g., Rowley et al. (2004), Barone & Kalashnikova et al. (2009), Serre et al. (2012).
2. ROMs which stabilize an unstable ROM through an a posteriori post-processing stabilization step applied to the algebraic ROM system.
  Petrov-Galerkin ROMs that solve an optimization problem for the test basis given a trial POD basis, e.g., Amsallem et al. (2012), Bond et al. (2008).
  ROMs with increased numerical stability due to inclusion of ‘stabilizing’ terms (e.g., LES terms) in the ROM equations, e.g., Wang, Akhtar, Borggaard, Iliescu (2012)
Inconsistencies between ROM and FOM physics
Potentially
intrusive implemetation
Stability Preserving Model Reduction Approaches:
Literature Review
Approaches for building stability-preserving POD/Galerkin
ROMs found in the literature fall into two categories:
6/21

## Slide 8
New ROM Stabilization Approach:
ROM Stabilization via Pole Placement
New ROM Stabilization Idea
(falling under second category of ROM stabilization methods):
Make ROM system matrix stable through pole (eigenvalue) placement
LTI FOM: stable
LTI ROM: unstable
Pick a control matrix .
Modify LTI ROM by adding to it the control :
Assume linear control of the form :
Compute the feedback matrix such that
has desired (stable) poles.
Open Questions:
How to pick ?
What eigenvalues should have?
Does solution to pole placement problem exist?
How does stabilization affect ROM accuracy?
7/21

## Slide 9
Algorithm #1: ROM Stabilization via Pole Placement
Theorem (from Aström et al. 2009): If the pair (AM,BC) is controllable, there exists a feedback such that the eigenvalues of can be arbitrarily assigned.
Ensures the solution to the pole placement problem exists.
Algorithm #1 Outline
Given , use Kalman decomposition to isolate controllable and observable part of and , call them , .
Compute eigenvalues of .
Reassign unstable eigenvalues of , e.g., set
Compute such that has these eigenvalues using pole placement algorithms from control theory.
Set ).
8/21

## Slide 10
Numerical Results: International Space Station (ISS)
Benchmark Stabilized via Algorithm #1
FOM: structural model of component 1r (Russian service module) of the International Space Station (ISS).
matrices defining FOM downloaded from NICONET model reduction benchmark repository.
No inputs (unforced) 1 output; FOM is stable
9/21
Component 1r

## Slide 11
POD/Galerkin ROM constructed using snapshots collected until time .
POD/Galerkin ROM has 4 unstable eigenvalues.
(stabilization matrix selected to be vector of all 1s).
Numerical Results: ISS Benchmark Stabilized via Algorithm #1 (continued)
ROM | 
Unstabilized POD | 1737.8
ROM | 
Unstabilized POD | 1737.8
ROM | 
Stabilized POD #1 | 0.1151
ROM | 
 | 0.1151
ROM | 
Stabilized POD #2 | 
ROM | 
ROM | 
Stabilized POD #3 | 
ROM | 
10/21

## Slide 12
Selecting ROM Eigenvalues (Poles)
11/21
If ROM is stable, ROM eigenvalues will lie on same manifold as FOM eigenvalues.
In fact, if and ROM is stable, , so eig()=eig().
However: if ROM is unstable, ROM eigenvalues can be chaotic.
Could try to place ROM poles to match FOM poles…
…but this does not ensure accuracy of ROM!

## Slide 13
Recall that the ROM LTI system is given by
Algorithm #2: ROM Stabilization Optimization Problem
Ensures stabilized ROM solution deviates minimally from FOM solution.
Key Idea: An exact solution to the ROM LTI system can be derived using the matrix exponential.
12/21
The solution to the ROM LTI system is:

## Slide 14
Algorithm #2: ROM Stabilization Optimization Problem
(continued)
ROM Stabilization Optimization Problem
(Constrained Nonlinear Least Squares):
= unstable eigenvalues of original ROM matrix .
snapshot output at
ROM output at .
ROM stabilization optimization problem is small:
ROM stabilization optimization problem can be solved by standard optimization algorithms, e.g., interior point method.
  We use fmincon function in MATLAB’s optimization toolbox.
  We implement ROM stabilization optimization problem in characteristic variables where .
13/21

## Slide 15
Algorithm #2 Is Equivalent to Specific Instance of
Algorithm #1 (Pole Placement Problem)
Can show: Algorithm #2 is equivalent to Algorithm #1 (Pole Placement Problem) for a specific and .
One can show that where (WLOG, if 2 eigenvalues were stabilized):
Here:
  denotes the original (unstable) eigenvalue of
  denotes the new (stable) eigenvalue of computed by Algorithm #2.
  denotes matrix of eigenvectors of .
14/21
Let be the new ROM matrix following stabilization by Algorithm #2:
, stabilized by Algorithm #2

## Slide 16
Numerical Results: ISS Benchmark Stabilized via
Algorithm #2
POD/Galerkin ROM has 4 unstable eigenvalues: 2 real, 2 complex
  Two options for ROM stabilization optimization problem:
    Option 1: Solve for s.t. the constraint .
    Option 2: Solve for , , , s.t. the constraint
Initial guess for fmincon interior point method: .
15/21
ROM | 
Unstabilized POD | 1737.8
Optimization Stabilized POD (Real Poles) | 0.0259
Optimization Stabilized POD (Complex-Conjugate Poles) | 0.0252
ROM | 
Unstabilized POD | 1737.8
Optimization Stabilized POD (Real Poles) | 0.0259
Optimization Stabilized POD (Complex-Conjugate Poles) | 0.0252

## Slide 17
Numerical Results: Electrostatically Actuated Beam
Benchmark Stabilized via Algorithm #2
FOM = 1D model of electrostatically actuated beam.
Application of model: microelectromechanical systems (MEMS) devices such as electromechanical radio frequency (RF) filters.
1 input corresponding to periodic on/off switching, 1 output, initial condition .
Second order linear semi-discrete system of the form:
Matrices , , , , specifying the problem downloaded from the Oberwolfach model reduction repository.
2nd order linear system re-written as 1st order LTI system for purpose of analysis/model reduction.
16/21
FOM is stable.

## Slide 18
Numerical Results: Electrostatically Actuated Beam
Benchmark Stabilized via Algorithm #2 (continued)
17/21
POD/Galerkin ROM constructed from snapshots up to time .
POD/Galerkin ROM has 4 unstable eigenvalues (all real).
  Two options for ROM stabilization optimization problem:
    Option 1: Solve for s.t. the constraint .
    Option 2: Solve for , , , s.t. the constraint
Initial guess for fmincon interior point method: .
ROM | 
Unstabilized POD | 
Optimization Stabilized POD (Real Poles) | 0.0194
Optimization Stabilized POD (Complex-Conjugate Poles) | 0.0205
Balanced Truncation | 
ROM | 
Unstabilized POD | 
Optimization Stabilized POD (Real Poles) | 0.0194
Optimization Stabilized POD (Complex-Conjugate Poles) | 0.0205
Balanced Truncation | 

## Slide 19
Numerical Results: Electrostatically Actuated Beam
Benchmark Stabilized via Algorithm #2
(continued: stabilized poles)
Unstable Eigenvalues
Unstable Eigenvalues
Stabilized Eigenvalues (Real) | Stabilized Eigenvalues (Complex Conjugates)
Stabilized Eigenvalues (Real) | Stabilized Eigenvalues (Complex Conjugates)
18/21

## Slide 20
Summary & Future Work
A new ROM stabilization approach that modifies a posteriori an unstable ROM LTI system by changing the system’s unstable eigenvalues is proposed.
It is demonstrated how an unstable ROM’s eigenvalues may be placed using ideas from control theory, i.e., pole placement assuming a linear control (Algorithm #1).
It is unclear how stabilization via Algorithm #1 will affect the accuracy of the ROM.
To address this, a constrained nonlinear least squares optimization problem for the ROM eigenvalues is formulated (Algorithm #2).
It is shown that Algorithm #2 is equivalent to Algorithm #1 for a specific linear control.
Performance of the proposed algorithms is evaluated on two benchmarks.
Ongoing/Future work
Journal article on the ideas presented in this talk is in preparation.
Performance/robustness studies of algorithms for solving ROM optimization
problem (e.g., sensitivity to initial guess, etc.).
Studies of predictive capabilities of stabilized ROMs.
Extensions to nonlinear problems.
19/21

## Slide 21
Acknowledgements
This work was funded by Laboratories’ Directed Research and Development (LDRD) Program at Sandia National Laboratories.
Special thanks to
  Prof. Lou Cattafesta (Florida State University)
  Prof. Karen Willcox (MIT)
for useful discussions that led to some of the ideas presented here.
Thank You! Questions?
ikalash@sandia.gov
http://www.sandia.gov/~ikalash
20/21

## Slide 22
References
M.F. Barone, I. Kalashnikova, D.J. Segalman, H. Thornquist. Stable Galerkin reduced order models for linearized compressible flow. J. Comput. Phys. 288: 1932-1946, 2009.
C.W. Rowley, T. Colonius, R.M. Murray. Model reduction for compressible flows using POD and Galerkin projection. Physica D. 189: 115-129, 2004.
G. Serre, P. Lafon, X. Gloerfelt, C. Bailly. Reliable reduced-order models for time-dependent linearized Euler equations. J. Comput. Phys. 231(15): 5176-5194, 2012.
Z. Wang, I. Akhtar, J. Borggaard, T. Iliescu. Proper orthogonal decomposition closure models for turbulent flows: a numerical comparison. Comput. Methods Appl. Mech. Engrg. 237-240:10-26, 2012.
B. Bond, L. Daniel, Guaranteed stable projection-based model reduction for indefinite and unstable linear systems, In: Proceedings of the 2008 IEEE/ACM International Conference on Computer-Aided Design, 728–735, 2008.
K.J. Aström, R.M. Murray. Feedback systems: an introduction for scientists and engineers. Princeton University Press, 2008.
NICONET model reduction benchmark repository: www.icm.tu-bs.de/NICONET/benchmodred.html.
Oberwolfach model reduction benchmark repository: http://simulation.uni-freiburg.de/downloads/benchmark
21/21

## Slide 23
Appendix: ISS Benchmark Details
Original benchmark: , 3 inputs, 3 outputs
Physics: 2nd order semi-discrete system for flexible structure
All 3 inputs and 3 outputs are the same.
Inputs = outputs = velocities at all discretization points (?)
Component 1r

## Slide 24
Appendix: ISS Benchmark Stabilized via
Algorithm #2 (fmincon performance)
 | Real Poles | Complex-Conjugate Poles
# upper bound constraints | 4 | 3
# iterations | 29 | 27
# function evaluations | 150 | 142
max constraint violation | 0 | 0
Current Function Value
Current Function Value
First-Order Optimality
0.00640948
5.50885e-07
0.00683859
4.00842e-07
First-Order Optimality

## Slide 25
Appendix: 1D Beam Benchmark Details
, 1 input, 1 output.
Dofs: flexural displacement and flexural rotation.
Beam is supported on both sides (simply
supported), and a node in the middle is loaded.
Damping matrix is linear combination of mass and stiffness matrices:
B (input) is an matrix with the only nonzero entry at the flexural dof of the middle node.
C (output) is a matrix with the only nonzero entry at the flexural dof of the middle node.
A typical input to this system is a step response; periodic on/off switching is also possible.

## Slide 26
Appendix: Electrostatically Actuated Beam
Benchmark Stabilized via Algorithm #2
fmincon performance)
 | Real Poles | Complex-Conjugate Poles
# upper bound constraints | 4 | 2
# iterations | 37 | 29
# function evaluations | 190 | 150
max constraint violation | 0 | 0
Current Function Value
Current Function Value
First-Order Optimality
First-Order Optimality
1.23985
5.5167e-07
9.02338e-06
23/21
1.2717