## Slide 1: Concurrent multiscale coupling in solid mechanics using the Schwarz alternating method
SAND2020-10789C
Sandia National Laboratories is a multi-mission laboratory managed and operated by National Technology and Engineering Solutions of Sandia, LLC., a wholly owned subsidiary of Honeywell International, Inc., for the U.S. Department of Energy’s National Nuclear Security Administration under contract DE-NA0003525.
Irina Tezaur1, Alejandro Mota1, Coleman Alleman1, Greg Phlipot2
1Sandia National Labs, Livermore, CA 2MSC Software, Newport Beach, CA
2020 Pacific Northwest Numerical Analysis Seminar October 17, 2020

## Slide 2
Outline
Motivation & Background
Schwarz Alternating Method for Concurrent Multiscale Coupling for Quasistatics
  Formulation
  Implementation
  Numerical Examples
Schwarz Alternating Method for Concurrent Multiscale Coupling for Dynamics
  Formulation
  Implementation
  Numerical Examples
Summary
Ongoing/Future Work

## Slide 3
Outline
Motivation & Background
Schwarz Alternating Method for Concurrent Multiscale Coupling for Quasistatics
  Formulation
  Implementation
  Numerical Examples
Schwarz Alternating Method for Concurrent Multiscale Coupling for Dynamics
  Formulation
  Implementation
  Numerical Examples
Summary
Ongoing/Future Work

## Slide 4
Motivation for Concurrent Multiscale Coupling
Large scale structural failure frequently originates from small scale phenomena such as defects, microcracks, inhomogeneities and more, which grow quickly in unstable manner.
Failure occurs due to tightly coupled interaction between small scale (stress concentrations, material instabilities, cracks, etc.) and large scale (vibration, impact, high loads and other perturbations).
Roof failure of Boeing 737 aircraft due to fatigue cracks. From imechanica.org
Concurrent multiscale methods are essential for understanding and prediction of behavior of engineering systems when a small scale failure determines the performance of the entire system.
Surface flaw in pressure vessel: interacts with microstructure, which may or may not lead to failure.
Notes: A lot of the problems of interest to Sandia National Labs require us to simulate and understand the large scale structural failure of engineered components, for instance, components comprising weapons systems.

## Slide 5
Previous Multiscale Coupling Work

## Slide 6
Previous Multiscale Coupling Work
Three-field multiscale coupling formulation with compatibility enforced weakly using Lagrange multipliers.

## Slide 7
Previous Multiscale Coupling Work
Method works well, but is difficult to implement into existing codes.

## Slide 8
Requirements for Multiscale Coupling Method
Coupling is concurrent (two-way).
Ease of implementation into existing massively-parallel HPC codes.
Scalable, fast, robust (we target real engineering problems, e.g., analyses involving failure of bolted components!).
“Plug-and-play” framework: simplifies task of meshing complex geometries
  Ability to couple regions with different non-conformal meshes, different element types and different levels of refinement.
  Ability to use different solvers/time-integrators in different regions.
Coupling does not introduce nonphysical artifacts.
Theoretical convergence properties/guarantees.

## Slide 9
Schwarz Alternating Method for Domain Decomposition
Proposed in 1870 by H. Schwarz for solving Laplace PDE on irregular domains.
H. Schwarz (1843 – 1921)
Initialize:
Solve PDE by any method on W1 w/ initial guess for Dirichlet BCs on G1.
Iterate until convergence:
Solve PDE by any method (can be different than for W1) on W2 w/ Dirichlet BCs on G2 that are the values just obtained for W1.
Solve PDE by any method (can be different than for W2) on W1 w/ Dirichlet BCs on G1 that are the values just obtained for W2.
Crux of Method: if the solution is known in regularly shaped domains, use those as pieces to iteratively build a solution for the more complex domain.
Basic Schwarz Algorithm

## Slide 10
Schwarz Alternating Method for Domain Decomposition
Proposed in 1870 by H. Schwarz for solving Laplace PDE on irregular domains.
H. Schwarz (1843 – 1921)
Initialize:
Solve PDE by any method on W1 w/ initial guess for Dirichlet BCs on G1.
Iterate until convergence:
Solve PDE by any method (can be different than for W1) on W2 w/ Dirichlet BCs on G2 that are the values just obtained for W1.
Solve PDE by any method (can be different than for W2) on W1 w/ Dirichlet BCs on G1 that are the values just obtained for W2.
Crux of Method: if the solution is known in regularly shaped domains, use those as pieces to iteratively build a solution for the more complex domain.
Basic Schwarz Algorithm
Requirement for convergence:

## Slide 11
Schwarz Alternating Method for Domain Decomposition
Proposed in 1870 by H. Schwarz for solving Laplace PDE on irregular domains.
H. Schwarz (1843 – 1921)
Initialize:
Solve PDE by any method on W1 w/ initial guess for Dirichlet BCs on G1.
Iterate until convergence:
Solve PDE by any method (can be different than for W1) on W2 w/ Dirichlet BCs on G2 that are the values just obtained for W1.
Solve PDE by any method (can be different than for W2) on W1 w/ Dirichlet BCs on G1 that are the values just obtained for W2.
Crux of Method: if the solution is known in regularly shaped domains, use those as pieces to iteratively build a solution for the more complex domain.
Basic Schwarz Algorithm
Requirement for convergence:
Schwarz alternating method most commonly used as a preconditioner for Krylov iterative methods to solve linear algebraic equations.

## Slide 12
Schwarz Alternating Method for Domain Decomposition
Proposed in 1870 by H. Schwarz for solving Laplace PDE on irregular domains.
H. Schwarz (1843 – 1921)
Initialize:
Solve PDE by any method on W1 w/ initial guess for Dirichlet BCs on G1.
Iterate until convergence:
Solve PDE by any method (can be different than for W1) on W2 w/ Dirichlet BCs on G2 that are the values just obtained for W1.
Solve PDE by any method (can be different than for W2) on W1 w/ Dirichlet BCs on G1 that are the values just obtained for W2.
Crux of Method: if the solution is known in regularly shaped domains, use those as pieces to iteratively build a solution for the more complex domain.
Basic Schwarz Algorithm
Requirement for convergence:
Schwarz alternating method most commonly used as a preconditioner for Krylov iterative methods to solve linear algebraic equations.
Novel idea: using the Schwarz alternating as a discretization method for solving multiscale partial differential equations (PDEs).

## Slide 13
Outline
Motivation & Background
Schwarz Alternating Method for Concurrent Multiscale Coupling for Quasistatics
  Formulation
  Implementation
  Numerical Examples
Schwarz Alternating Method for Concurrent Multiscale Coupling for Dynamics
  Formulation
  Implementation
  Numerical Examples
Summary
Ongoing/Future Work

## Slide 14
Schwarz for Multiscale Coupling in Quasistatics
Advantages:
Conceptually very simple.
Allows the coupling of regions with different non-conforming meshes, different element types, and different levels of refinement.
Information is exchanged among two or more regions, making coupling concurrent.
Different solvers can be used for the different regions.
Different material models can be coupled if they are compatible in the overlap region.
Simplifies the task of meshing complex geometries for the different scales.
outer quasistatic loop

## Slide 15
S.L. Sobolev (1936): posed Schwarz method for linear elasticity in variational form and proved method’s convergence by proposing a convergent sequence of energy functionals.
S.G. Mikhlin (1951): proved convergence of Schwarz method for general linear elliptic PDEs.
P.-L. Lions (1988): studied convergence of Schwarz for nonlinear monotone elliptic problems using max principle.
A. Mota, I. Tezaur, C. Alleman (2017): proved convergence of the alternating Schwarz method for finite deformation quasi-static nonlinear PDEs (with energy functional ) with a geometric convergence rate.
S.G. Mikhlin
(1908 – 1990)
S.L. Sobolev (1908 – 1989)
A. Mota, I. Tezaur, C. Alleman
Using the Schwarz alternating as a discretization method for PDEs is natural idea with a sound theoretical foundation.
Theoretical Foundation
P.- L. Lions (1956-)
Notes: A(F,Z) = Helmholtz free-energy density, Z = collection of internal variables, F = grad(phi) = deformation gradient, B = body force, T = traction on boundary
P = \partial A/\partial F = first Piola-Kirchoff stress
2nd equation is Euler-Lagrange equation

## Slide 16
Convergence Proof*
*A. Mota, I. Tezaur, C. Alleman. "The Schwarz Alternating Method in Solid Mechanics", CMAME 319 (2017), 19-51.
Notes: The proof effectively constructs a sequence of solutions phi^n and demonstrates that this sequence converges to the unique minimizer of the energy functional \Phi defining the single-domain problem, and combines concepts used in the analysis of Sobolev, Lions, and others, in studying the convergence of the Schwarz method.

## Slide 17
Outline
Motivation & Background
Schwarz Alternating Method for Concurrent Multiscale Coupling for Quasistatics
  Formulation
  Implementation
  Numerical Examples
Schwarz Alternating Method for Concurrent Multiscale Coupling for Dynamics
  Formulation
  Implementation
  Numerical Examples
Summary
Ongoing/Future Work

## Slide 18
Implementation in Albany LCM Code
Component-based design for rapid development.
Contains a wide variety of constitutive models.
Extensive use of libraries from the open-source Trilinos project.
  Use of the Phalanx package to decompose complex problem into simpler problems with managed dependencies.
  Use of the Sacado package for automatic differentiation.
  Use of Teko package for block preconditioning for Modified and Monolithic Schwarz variants.
Parallel implementation of Schwarz alternating method uses the Data Transfer Kit (DTK).
All software available on GitHub.
https://github.com/trilinos/trilinos
https://github.com/SNLComputation/LCM
https://github.com/ORNL-CEES/DataTransferKit
The proposed quasistatic alternating Schwarz method is implemented within the Albany LCM open-source parallel, C++, multi-physics, finite element code.

## Slide 19
Outline
Motivation & Background
Schwarz Alternating Method for Concurrent Multiscale Coupling for Quasistatics
  Formulation
  Implementation
  Numerical Examples
Schwarz Alternating Method for Concurrent Multiscale Coupling for Dynamics
  Formulation
  Implementation
  Numerical Examples
Summary
Ongoing/Future Work

## Slide 20
Schwarz Iteration
Quasistatic Example #1: Cuboid Problem
Coupling of two cuboids with square base (above).
Neohookean-type material model.

## Slide 21
Below: Convergence of the cuboid problem for different mesh sizes and fixed overlap volume fraction. The Schwarz alternating method converges linearly.
Above: Convergence factor as a function of overlap volume and different mesh. There is faster linear convergence with increasing overlap volume fraction.
Cuboid Problem: Convergence with Overlap & Refinement

## Slide 22: Cuboid Problem: Schwarz Error

## Slide 23
Quasistatic Example #2: Notched Cylinder
Notched cylinder that is stretched along its axial direction.
Domain decomposed into two subdomains.
Neohookean-type material model.

## Slide 24
The Schwarz alternating method is capable of coupling different mesh topologies.
The notched region, where stress concentrations are expected, is finely meshed with tetrahedral elements.
The top and bottom regions, presumably of less interest, are meshed with coarser hexahedral elements.
Notched Cylinder: TET - HEX Coupling

## Slide 25
Notched Cylinder: TET - HEX Coupling

## Slide 26
Notched Cylinder: TET - HEX Coupling

## Slide 27
Notched cylinder subjected to tensile load with an elastic and J2 elasto-plastic regions.
Coarse region is elastic and fine region is elasto-plastic.
The overlap region in the first mesh is nearer the notch, where plastic behavior is expected.
Overlap far from notch.
Overlap near notch.
Coupled regions
Coarse, elastic region
Fine, elasto-plastic region
Notched Cylinder: Coupling Different Materials
The Schwarz method is capable of coupling regions with different material models.

## Slide 28
When the overlap region is far from the notch, no plastic deformation exists in it: the coarse and fine regions predict the same behavior.
When the overlap region is near the notch, plastic deformation spills onto it and the two models predict different behavior, affecting convergence adversely.
Overlap far from notch.
Overlap near notch.
Notched Cylinder: Coupling Different Materials
Need to be careful to do domain decomposition so that material models are consistent in overlap region.

## Slide 29: Quasistatic Example #3: Laser Weld
Laser weld specimen
Problem of practical scale.
Isotropic elasticity and J2 plasticity with linear isotropic hardening.
Identical parameters for weld and base materials for proof of concept, to become independent models.
Coupled Schwarz discretization
(50% reduction in model size)
Single domain discretization
Notes: ~200K dofs

## Slide 30: Laser Weld: Strong Scalability of Parallel Schwarz with DTK
Near-ideal linear speedup (64-1024 cores).
Data Transfer Kit (DTK)

## Slide 31: Quasistatic Example #4: Tensile Bar
The alternating Schwarz method can be used as part of a homogenization (upscaling) process to bridge gap b/w microscopic and macroscopic regions
macro-scale
micro-structure
macro-scale
Work by C. Alleman, J. Foulk,
D. Littlewood, G. Bergel
  Microstructure embedded in ASTM tensile geometry (right).
  Fix microstructure, investigate ensemble of uniaxial loads.
  Fit flow curves with a macroscale J2 plasticity model (below).
  Goal: study strain localization in microstructure.
Notes: The last quasistatic example is another production-type problem known as the tensile bar problem and is courtesy of my colleagues Coleman Alleman, Jay Foulk, Dave Littlewood and Guy Bergel. This problem illustrates an interesting use of the Schwarz alternating method, in particular, that the method can be used as a part of a homogenization or upscaling process to bridge the gap between microscopic and macroscopic regions. Here, Coleman and his collaborators took a tensile geometry and embedded in it a microstructure, shown in the middle, with the goal of studying strain localization in the microstructure. The crystal plasticity microscale model in the microstructure was coupled to a J2 plasticity macroscale model in the rest of the domain using Schwarz, and a set of calculations were performed under an ensemble of uniaxial loads. Upscaling was performed by fitting flow curves to this set of ensembles using the J2 plasticity macroscale model.

## Slide 32
Outline
Motivation & Background
Schwarz Alternating Method for Concurrent Multiscale Coupling for Quasistatics
  Formulation
  Implementation
  Numerical Examples
Schwarz Alternating Method for Concurrent Multiscale Coupling for Dynamics
  Formulation
  Implementation
  Numerical Examples
Summary
Ongoing/Future Work

## Slide 33
Schwarz Alternating Method for Dynamics
In the literature the Schwarz method is applied to dynamics by using space-time discretizations.
Overlapping non-matching meshes and time steps in dynamics.

## Slide 34
In the literature the Schwarz method is applied to dynamics by using space-time discretizations.
Overlapping non-matching meshes and time steps in dynamics.
Pro : Can use non-matching meshes and time-steps (see right figure).
Con : Unfeasible given the design of our current codes and size of simulations.
Schwarz Alternating Method for Dynamics

## Slide 35
Controller time stepper
Time integrator for W1
Time integrator for W2
Step 0: Initialize
Schwarz Alternating Method for Dynamic Multiscale Coupling
Controller time stepper: defines global s at which subdomains are synchronized
Notes: The final ingredient is what we call the ‘controller time-stepper’. The goal of the controller time-stepper is to define global time steps shown in blue in the figure at the top. It is at these controller time steps that the Schwarz subdomains will be synchronized, as will hopefully become apparent as I go through the algorithm.

## Slide 36
Integrate using
Interpolate from to
Controller time stepper
Time integrator for W1
Time integrator for W2
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Schwarz Alternating Method for Dynamic Multiscale Coupling
Controller time stepper: defines global s at which subdomains are synchronized

## Slide 37
Controller time stepper
Time integrator for W1
Time integrator for W2
Integrate using
Interpolate from to
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Step 2: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times .
Schwarz Alternating Method for Dynamic Multiscale Coupling
Controller time stepper: defines global s at which subdomains are synchronized

## Slide 38
Controller time stepper
Time integrator for W1
Time integrator for W2
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Step 2: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times .
Step 3: Check for convergence at time .
Schwarz Alternating Method for Dynamic Multiscale Coupling
Controller time stepper: defines global s at which subdomains are synchronized

## Slide 39
Controller time stepper
Time integrator for W1
Time integrator for W2
Interpolate from to
Integrate using
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Step 2: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times .
Step 3: Check for convergence at time .
If unconverged, return to Step 1.
Schwarz Alternating Method for Dynamic Multiscale Coupling
Controller time stepper: defines global s at which subdomains are synchronized

## Slide 40
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Step 2: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times .
Step 3: Check for convergence at time .
If unconverged, return to Step 1.
If converged, set and return to Step 1.
Controller time stepper
Time integrator for W1
Time integrator for W2
Integrate using
Interpolate from to
Schwarz Alternating Method for Dynamic Multiscale Coupling
Controller time stepper: defines global s at which subdomains are synchronized

## Slide 41
Schwarz Alternating Method for Dynamic Multiscale Coupling
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Step 2: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times .
Step 3: Check for convergence at time .
If unconverged, return to Step 1.
If converged, set and return to Step 1.
Controller time stepper
Time integrator for W1
Time integrator for W2
Integrate using
Interpolate from to
Can use different integrators with different time steps within each domain!
Controller time stepper: defines global s at which subdomains are synchronized

## Slide 42
Schwarz Alternating Method for Dynamic Multiscale Coupling: Theory
Like for quasistatics, dynamic alternating Schwarz method converges provided each single-domain problem is well-posed and overlap region is non-empty, under some conditions on .
Well-posedness for the dynamic problem requires that action functional be strictly convex or strictly concave, where is the Lagrangian.
  This is studied by looking at its second variation
We can show assuming a Newmark time-integration scheme that for the fully-discrete problem:
can always be made positive by choosing a sufficiently small
Numerical experiments reveal that requirements for stability/accuracy typically lead to automatic satisfaction of this bound.
*A. Mota, I. Tezaur, G. Phlipot. "The Schwarz alternating method for dynamic solid mechanics", CMAME (under review).

## Slide 43
Outline
Motivation & Background
Schwarz Alternating Method for Concurrent Multiscale Coupling for Quasistatics
  Formulation
  Implementation
  Numerical Examples
Schwarz Alternating Method for Concurrent Multiscale Coupling for Dynamics
  Formulation
  Implementation
  Numerical Examples
Summary
Ongoing/Future Work

## Slide 44
Implementation in Albany LCM & Sierra/SM
Numerical results shown here for dynamic Schwarz are from two codes: Albany LCM and Sierra/Solid Mechanics (Sierra/SM)
Albany LCM: Trilinos-based open-source* parallel, C++, multi-physics, FE code.
Sierra Mechanics Framework: Sandia Lagrangian 3D code for FEA of solids & structures.
Sierra/SM: quasistatics, implicit/explicit dynamics + loose coupling via Arpeggio
* https://github.com/SNLComputation/LCM
Notes: For the dynamical case, I am going to show results from two codes. The first of these, Albany LCM, I talked about earlier when I discussed the quasistatic case. Albany LCM is a Trilinos-based open-source parallel, C++ Multiphysics finite element code. After we did an initial implementation and prototyping of our Schwarz algorithm in Albany LCM, we proceeded to implement the method in Sandia’s production code, known as Sierra Solid Mechanics, or Sierra/SM. Sierra is a Sandia Lagrangian code for finite element analysis of solids and structures. It has a number of different modules, listed here. Sierra/SM consists of 3 modules known as Adagio, Presto and Arpeggio, which enable quasistatic, implicit/explicit dynamic, and loosely coupled solid mechanics analyses, respectively.

## Slide 45
Implementation in Albany LCM & Sierra/SM
Numerical results shown here for dynamic Schwarz are from two codes: Albany LCM and Sierra/Solid Mechanics (Sierra/SM)
Albany LCM: Trilinos-based open-source* parallel, C++, multi-physics, FE code.
Sierra Mechanics Framework: Sandia Lagrangian 3D code for FEA of solids & structures.
Sierra/SM: quasistatics, implicit/explicit dynamics + loose coupling via Arpeggio
Schwarz alternating method was “implemented” in Sierra/SM using Arpeggio loose coupling framework
* https://github.com/SNLComputation/LCM

## Slide 46
Implementation in Albany LCM & Sierra/SM
Numerical results shown here for dynamic Schwarz are from two codes: Albany LCM and Sierra/Solid Mechanics (Sierra/SM)
Albany LCM: Trilinos-based open-source* parallel, C++, multi-physics, FE code.
Sierra Mechanics Framework: Sandia Lagrangian 3D code for FEA of solids & structures.
Sierra/SM: quasistatics, implicit/explicit dynamics + loose coupling via Arpeggio
Schwarz alternating method was “implemented” in Sierra/SM using Arpeggio loose coupling framework
We did not have to write any code in Sierra/SM to implement Schwarz!
* https://github.com/SNLComputation/LCM

## Slide 47
Outline
Motivation
Schwarz Alternating Method for Concurrent Multiscale Coupling for Quasistatics
  Formulation
  Implementation
  Numerical Examples
Schwarz Alternating Method for Concurrent Multiscale Coupling for Dynamics
  Formulation
  Implementation
  Numerical Examples
Summary
Future Work

## Slide 48
Dynamic Example #1: Elastic Wave Propagation
Linear elastic clamped beam with Gaussian initial condition for the 𝑧-displacement.
Simple problem with analytical exact solution but very stringent test for discretization methods.
Test Schwarz with 2 subdomains: .
Left: Initial condition (blue) and final solution (red). Wave profile is negative of initial profile at time T = 1.0e-3.
Time-discretizations: Newmark (implicit, explicit)
Meshes: HEX, TET

## Slide 49
z-displacement
Table 1: Averaged (over times + domains) relative errors in z–displacement (blue) and z-velocity (green) for several different Schwarz couplings, 50% overlap volume fraction
LM = Lumped Mass, CM = Consistent Mass
z-velocity
 | Implicit-Implicit |  | Explicit(CM)-Implicit |  | Explicit(LM)-Implicit | 
Conformal HEX - HEX | 2.79e-3 | 7.32e-3 | 3.53e-3 | 8.70e-3 | 4.72e-3 | 1.19e-2
Nonconformal HEX - HEX | 2.90e-3 | 7.10e-3 | 2.82e-3 | 7.29e-3 | 2.84e-3 | 7.33e-3
TET - HEX | 2.79e-3 | 7.58e-3 | 3.52e-3 | 8.92e-3 | 4.72e-3 | 1.19e-2
Dynamic Schwarz coupling introduces no dynamic artifacts that are pervasive in other coupling methods!
Elastic Wave: Diff. Integrators, Same s

## Slide 50
Elastic Wave: Diff. Integrators, Diff. s
Figures above: Plots of displacement, velocity and acceleration for the elastic wave propagation problem using different time integrators (implicit and explicit) and different time steps (1e-2s and 2e-7s) for each subdomain, superimposed over the analytic single domain solution.
The analytic solution is indistinguishable from Schwarz solutions (hidden behind the solutions for (red) and (green))!
Displacement
Velocity
Acceleration

## Slide 51
Dynamic Example #2: Tension Specimen
+
Uniaxial aluminum cylindrical tensile specimen with inelastic J2 material model.
Domain decomposition into two subdomains (right): = ends, = gauge.
Nonconformal HEX + composite TET10 coupling via Schwarz.
Implicit Newmark time-integration with adaptive time-stepping algorithm employed in both subdomains.
Slight imperfection introduced at center of gauge to force necking upon pulling in vertical direction.

## Slide 52
Tension Specimen: Expected Result

## Slide 53
Tension Specimen: Disp. & Nodal EQPS*
Average of ~3 Schwarz iterations/time step required for convergence to Schwarz tolerance of 1e-6.
y-displacement
Nodal EQPS*
*Nodal EQPS = Equivalent Plastic Strain (computed via weighted volume average).
Notes: So, lets see what happens. The plots are showing the y-displacement and the nodal equivalent plastic strain in the specimen. You see a nice smooth transition of the solution between the two subdomains, and the method is able to simulate the necking behavior in the middle. It takes on average 3 Schwarz iterations/time step to achieve a relatively tight convergence tolerance of 1e-6.

## Slide 54
Tension Specimen: Domain Decomposition

## Slide 55
Tension Specimen: Nodal EQPS*
*Nodal EQPS = Equivalent Plastic Strain (computed via weighted volume average).

## Slide 56
Tension Specimen: Cauchy Stress

## Slide 57
Dynamic Example #3: Bolted Joint Problem
bolts (Composite TET10), parts (HEX).
Inelastic J2 material model in both subdomains.
  steel
  steel component, aluminum (bottom) plate
Schwarz solution compared to single-domain solution on composite TET10 mesh.
BC: x-disp = 0.02 at T = 1.0e-3 on top of parts.
Run until T = 5.0e-4 w/ dt = 1e-5 + implicit Newmark with analytic mass matrix for composite tet 10s.
Problem of practical scale.

## Slide 58
Single
Schwarz
Bolted Joint Problem: Displacement

## Slide 59
Bolted Joint Problem: Nodal EQPS*
Single
Schwarz
*Nodal EQPS = Equivalent Plastic Strain (computed via weighted volume average).

## Slide 60
Bolted Joint Problem: Convergence Rate
Figure above: Convergence behavior of the dynamic Schwarz algorithm for the bolted joint problem
Linear convergence rate is observed for dynamic Schwarz algorithm, as for the quasistatic Schwarz algorithm.

## Slide 61
Bolted Joint Problem: Performance
 | CPU times (64 procs*) | Avg # Schwarz iters | Max # Schwarz iters
Single Domain | 3h 34m |  | 
Schwarz | 2h 42m | 3.22 | 4
Single Domain (finer) | 17h 00m |  | 
Schwarz (finer mesh of bolts) | 29h 29m | 3.28 | 4
 | CPU times (64 procs*) | Avg # Schwarz iters | Max # Schwarz iters
Single Domain | 3h 34m |  | 
Schwarz | 2h 42m | 3.22 | 4
Single Domain (finer) | 17h 00m |  | 
Schwarz (finer mesh of bolts) | 29h 29m | 3.28 | 4
* On SNL ascicgpu15, 16, 17 machines (Intel Skylake CPU processor), Schwarz tol = 1e-6.
61

## Slide 62
Bolted Joint Problem: Performance
 | CPU times (64 procs*) | Avg # Schwarz iters | Max # Schwarz iters
Single Domain | 3h 34m |  | 
Schwarz | 2h 42m | 3.22 | 4
Single Domain (finer) | 17h 00m |  | 
Schwarz (finer mesh of bolts) | 29h 29m | 3.28 | 4
 | CPU times (64 procs*) | Avg # Schwarz iters | Max # Schwarz iters
Single Domain | 3h 34m |  | 
Schwarz | 2h 42m | 3.22 | 4
Single Domain (finer) | 17h 00m |  | 
Schwarz (finer mesh of bolts) | 29h 29m | 3.28 | 4
Despite its iterative nature, Schwarz can actually be faster than single domain run for discretizations having comparable # of elements in the bolts.
* On SNL ascicgpu15, 16, 17 machines (Intel Skylake CPU processor), Schwarz tol = 1e-6.
62

## Slide 63
Bolted Joint Problem: Performance
 | CPU times (64 procs*) | Avg # Schwarz iters | Max # Schwarz iters
Single Domain | 3h 34m |  | 
Schwarz | 2h 42m | 3.22 | 4
Single Domain (finer) | 17h 00m |  | 
Schwarz (finer mesh of bolts) | 29h 29m | 3.28 | 4
 | CPU times (64 procs*) | Avg # Schwarz iters | Max # Schwarz iters
Single Domain | 3h 34m |  | 
Schwarz | 2h 42m | 3.22 | 4
Single Domain (finer) | 17h 00m |  | 
Schwarz (finer mesh of bolts) | 29h 29m | 3.28 | 4
Despite its iterative nature, Schwarz can actually be faster than single domain run for discretizations having comparable # of elements in the bolts.
  Even if the method is more computationally expensive for some resolutions, it may be preferred for its ability to rapidly change and evaluate a variety of engineering designs (our typical use case).
* On SNL ascicgpu15, 16, 17 machines (Intel Skylake CPU processor), Schwarz tol = 1e-6.

## Slide 64
Bolted Joint Problem: Performance
Despite its iterative nature, Schwarz can actually be faster than single domain run for discretizations having comparable # of elements in the bolts.
  Even if the method is more computationally expensive for some resolutions, it may be preferred for its ability to rapidly change and evaluate a variety of engineering designs (our typical use case).
* On SNL ascicgpu15, 16, 17 machines (Intel Skylake CPU processor), Schwarz tol = 1e-6.
 | CPU times (64 procs*) | Avg # Schwarz iters | Max # Schwarz iters
Single Domain | 3h 34m |  | 
Schwarz | 2h 42m | 3.22 | 4
Single Domain (finer) | 17h 00m |  | 
Schwarz (finer mesh of bolts) | 29h 29m | 3.28 | 4
 | CPU times (64 procs*) | Avg # Schwarz iters | Max # Schwarz iters
Single Domain | 3h 34m |  | 
Schwarz | 2h 42m | 3.22 | 4
Single Domain (finer) | 17h 00m |  | 
Schwarz (finer mesh of bolts) | 29h 29m | 3.28 | 4
Dynamic Schwarz converges in between 2-4 Schwarz iterations per time-step despite the overlap region being very small for this problem.
overlap region

## Slide 65
Outline
Motivation & Background
Schwarz Alternating Method for Concurrent Multiscale Coupling for Quasistatics
  Formulation
  Implementation
  Numerical Examples
Schwarz Alternating Method for Concurrent Multiscale Coupling for Dynamics
  Formulation
  Implementation
  Numerical Examples
Summary
Ongoing/Future Work

## Slide 66
Summary
The Schwarz alternating method has been developed/implemented for concurrent multiscale quasistatic & dynamic modeling in Sandia’s Albany LCM and Sierra/SM codes.
Coupling is concurrent (two-way).
Ease of implementation into existing massively-parallel HPC codes.
Scalable, fast, robust (we target real engineering problems, e.g., analyses involving failure of bolted components!).
“Plug-and-play” framework: simplifies task of meshing complex geometries!
  Ability to couple regions with different non-conformal meshes, different element types and different levels of refinement.
  Ability to use different solvers/time-integrators in different regions.
Coupling does not introduce nonphysical artifacts.
Theoretical convergence properties/guarantees.









## Slide 67
Outline
Motivation & Background
Schwarz Alternating Method for Concurrent Multiscale Coupling for Quasistatics
  Formulation
  Implementation
  Numerical Examples
Schwarz Alternating Method for Concurrent Multiscale Coupling for Dynamics
  Formulation
  Implementation
  Numerical Examples
Summary
Ongoing/Future Work

## Slide 68
Current work:
Continuing to apply the Schwarz alternating method to problems of interest to production using Sierra/SM.
Advancing the Schwarz alternating method to enable coupling of structural elements to continuum elements.
Developing a Schwarz-like algorithm for simulating contact to address well-known challenges (contact constraint enforcement, multiple scales).
  Done by introducing a combination of Dirichlet and Neumann boundary conditions into different subdomains in a non-overlapping alternating fashion.
Further down the line:
Development of a multi-physics coupling framework based on variational formulations and the Schwarz alternating method.
Develop a hybrid FOM-ROM (full-order-model – reduced-order-model) framework using the Schwarz alternating method.
Ongoing/Future Work

## Slide 69
References
[1] M.A. Heroux et al. “An overview of the Trilinos project.” ACM Trans. Math. Softw. 31(3) (2005)
[2] A. Salinger, et al. "Albany: Using Agile Components to Develop a Flexible, Generic Multiphysics Analysis Code", Int. J. Multiscale Comput. Engng. 14(4) (2016) 415-438.
[3] H. Schwarz. “Über einen Grenzübergang durch alternierendes Verfahren”. In: Vierteljahrsschriftder Naturforschenden Gesellschaft in Zurich 15 (1870), pp. 272–286.
[4] S.L. Sobolev. “Schwarz’s Algorithm in Elasticity Theory”. In: Selected Works of S.L Sobolev. Volume I: equations of mathematical physics, computational mathematics and cubature formulats. Ed. By G.V. Demidenko and V.L. Vaskevich. New York: Springer, 2006.
[5] S. Mikhlin. “On the Schwarz algorithm”. In: Proceedings of the USSR Academy of Sciences (in Russian) 77 (1951), pp. 569–571.
[6] D.J. Evans et al. “The convergence rate of the Schwarz alternating procedure (II): For two-dimensional problems”. In: International Journal for Computer Mathematics 20.3–4 (1986), pp. 325–339.
[7] P.L. Lions. “On the Schwarz alternating method I.” In: 1988, First International Symposium on Domain Decomposition methods for Partial Differential Equations, SIAM, Philadelphia.
[8] SIERRA Solid Mechanics Team. Sierra/Solid Mechanics 4.48 User’s Guide. Tech. rep. SAND2018-2961. Sandia National Laboratories Report, Oct. 2018.
[9] A. Mota, I. Tezaur, C. Alleman. "The Schwarz Alternating Method in Solid Mechanics", Comput. Meth. Appl. Mech. Engng. 319 (2017), 19-51.
[10] A. Mota, I. Tezaur, G. Phlipot. "The Schwarz Alternating Method for Dynamic Solid Mechanics”, Comput. Meth. Appl. Mech. Engng. (under review). [http://www.sandia.gov/~ikalash/journal.html]

## Slide 70
Full Schwarz
Modified Schwarz
Inexact Schwarz
Monolithic Schwarz
*A. Mota, I. Tezaur, C. Alleman. "The Schwarz Alternating Method in Solid Mechanics", CMAME 319 (2017), 19-51.
Appendix. Four Variants* of Schwarz

## Slide 71
Appendix. Four Variants* of Schwarz
Full Schwarz
Modified Schwarz
Inexact Schwarz
Monolithic Schwarz
Modified and Monolithic Schwarz variants create and solve a block system.
*A. Mota, I. Tezaur, C. Alleman. "The Schwarz Alternating Method in Solid Mechanics", CMAME 319 (2017), 19-51.

## Slide 72
Appendix. Four Variants* of Schwarz
Full Schwarz
Modified Schwarz
Inexact Schwarz
Monolithic Schwarz
Most performant method: monotonic convergence, theoretical convergence guarantee.
*A. Mota, I. Tezaur, C. Alleman. "The Schwarz Alternating Method in Solid Mechanics", CMAME 319 (2017), 19-51.

## Slide 73
Appendix. Full Schwarz Method
Classical algorithm originally proposed by Schwarz with outer Schwarz loop and inner Newton loop, each converged to a tight tolerance (

## Slide 74
Appendix. Inexact Schwarz Method
Classical algorithm originally proposed by Schwarz with outer Schwarz loop and inner Newton loop, with Newton step converged to a loose tolerance

## Slide 75
Appendix. Monolithic Schwarz Method
Combines Schwarz and Newton loop into since Newton-Schwarz loop, with elimination of Schwarz boundary DOFs, and tight convergence tolerance.
Advantages:
By-passes Schwarz loop.
Disadvantages:
Off-diagonal coupling terms block linear solver is needed.

## Slide 76
Appendix. Modified Schwarz Method
Combines Schwarz and Newton loop into since Newton-Schwarz loop, with Schwarz boundaries at Dirichlet boundaries and tight convergence tolerance.
Least-intrusive variant: by-passes Schwarz iteration, no need for block solver.
Advantages:
By-passes Schwarz loop.
No diagonal coupling (conventional linear solver can be used in each subdomain).

## Slide 77: Appendix. Foulk’s Singular Bar
1D proof of concept problem:
  1D bar with area proportional to square root of length.
  Strong singularity on left end of bar.
  Simple hyperelestic material model with no damage.
  MATLAB implementation.
Problem goals:
  Explore viability of 4 variants of the Schwarz alternating method.
  Test convergence and compare with literature (Evans, 1986).
    Expect faster convergence in fewer iterations with increased overlap.

## Slide 78: Appendix. Singular Bar and Schwarz Variants
Notes: Linear convergence for all methods (bottom left)
Monolithic Schwarz converges faster but timings are similar -> all implementations are interchangeable (bottom right)
Amount of overlap critical for convergence (top right)

## Slide 79: Appendix. Multiscale Modeling of Localization
Region of localization (necking)
  Goals:
  Connect physical length scales to engineering scale models.
  Investigate importance of microstructural detail.
  Develop bridging technologies for spatial multiscale/ multiphysics.
Region of localization (fracture)
  Strain localization can cause localized necking (left) and ultimately fracture (above).
Notes: Strain localization is a ubiquitous feature of elastoplastic materials undergoing nonhomogeneous deformation. The phenomenon manifests in the form of a shear band, a narrow zone of intense straining across which some kinematical fields in a deforming body may be discontinuous.
Strain localization can cause local necking and ultimately fracture.

## Slide 80: Appendix. Parallelization via DTK: Weak Scaling on Cubes Problem
1 Processor,
2.5*103 DOF / proc
8 Processors,
2.1*103 DOF / proc
64 Processors,
1.9*103 DOF / proc

## Slide 81: Appendix. Parallelization via DTK: Strong Scaling on Cubes Problem
Small problem (2.5*103 DOFs)
Medium problem (1.7*104 DOFs)
176 DOF/processor
107 DOF/processor
Large problem (1.6*105 DOFs)
5124 DOF/processor

## Slide 82
Appendix. Notched Cylinder: HEX-HEX Coupling
Notes: For completeness, I will show results for several different discretizations of these two regions, Omega1 and Omega2. In the first one, we discretize each region using a conformal hex mesh, and compute errors with respect to a solution on a single domain mesh that is conformal with each of these meshes. The table at the bottom of the slide shows displacement relative errors as a function of the Schwarz tolerance. You can see that as you decrease the Schwarz tolerance, the errors approach machine precision, meaning in the absence of other sources of error such as geometric error, the Schwarz method does not introduce any error into the discretization.

## Slide 83
Appendix. Notched Cylinder: Nonconformal HEX - HEX Coupling
Notes: We next look at a coupling in which Omega1 and Omega2 are discretized using hex meshes of comparable resolution but that are nonconformal with each other.

## Slide 84
Appendix. Notched Cylinder: Nonconformal HEX - HEX Coupling
Notes: Here, the errors in each of the subdomains are of the order of 10^(-4)-10^(-3) regardless of the Schwarz tolerance. It may seem that there is a problem here, but if you plot the errors in each of the subdomains (shown here), it’s clear what is happening: the dominant error is geometric error due to the Schwarz meshes not being able to represent the curved geometry as well as the single-domain reference mesh. This geometric error has nothing to do with the Schwarz coupling.

## Slide 85
Appendix. Rubiks Cube Problem
plotting axial
stress
concurrent coupling
Two distinct bodies, the component scale and the microstructural scale, are coupled iteratively with alternating Schwarz
component
scale
distinct
models
microstructural
scale
Work by J. Foulk, D. Littlewood, C. Battaile, H. Lim

## Slide 86: Appendix. Tensile Bar
Embed microstructure in ASTM tensile geometry

## Slide 87: Appendix. Tensile Bar: Meso-Macroscale Coupling
+
Mesoscale
Macroscale
SPARKS-generated microstructure (F. Abdeljawad)
Fix microstructure, investigate ensembles
151 axial vectors from 3 of the 10 ensembles of random rotations
(blue, green, red)
Load microstructural ensembles in uniaxial stress
Fit flow curves with a macroscale J2 plasticity model
Notes: \text{cubic elastic constant}: C_{11} = 204.6 \; \text{GPa} \\
\text{cubic elastic constant}: C_{12} = 137.7 \; \text{GPa} \\
\text{cubic elastic constant}: C_{44} = 126.2 \; \text{GPa} \\
\text{reference shear rate}: \dot{\gamma}_{0} = 1.0 \; \text{1/s} \\
\text{rate sensitivity factor}: m = 20 \\
\text{hardening rate parameter}: \dot{g_{0}} = 2.0 \times 10^{4} \; \text{1/s} \\
\text{initial hardness}: g_{0} = 90 \; \text{MPa} \\
\text{saturation hardness}: g_{s} = 202 \; \text{MPa} \\
\text{saturation exponent}: \omega = 0.01
\text{Young's modulus}: E = 195.0 \; \text{GPa} \\
\text{Poission's ratio}: \nu = 0.3 \\
\text{yield stress}: \sigma_{0} = 144 \; \text{MPa} \\
\text{hardening modulus}: H = 300 \; \text{MPa} \\
\text{saturation modulus}: S = 170 \; \text{MPa} \\
\text{saturation exponent}: \alpha = 190
\sigma_{y} = \sigma_{0} + H \epsilon_{p} + S (1 - e^{-\alpha \epsilon_{p}})

## Slide 88: Appendix. Tensile Bar: Results
Reduction in cross-sectional area over time

## Slide 89
Appendix. Schwarz Alternating Method
for Dynamics
In the literature the Schwarz method is applied to dynamics by using space-time discretizations.
This was deemed unfeasible given the design of our current codes and size of simulations.
Overlapping non-matching meshes and time steps in dynamics.

## Slide 90
Appendix. A Schwarz-like Time Integrator
We developed an extension of Schwarz coupling to dynamics using a governing time stepping algorithm that controls time integrators within each domain.
Can use different integrators with different time steps within each domain.
1D results show smooth coupling without numerical artifacts such as spurious wave reflections at boundaries of coupled domains.
Controller time stepper
Time integrator for W1
Time integrator for W2

## Slide 91
Schwarz Alternating Method for Dynamic Multiscale Coupling: Theory
Our dynamic alternating Schwarz algorithm can be interpreted as applying the traditional Schwarz alternating iterations in space-time between and
This interpretation does not require the method to be implemented using a space-time framework.
Notes: As before, lets talk about theory, this time for the dynamic case. In deriving a proof of convergence for our dynamic Schwarz algorithm, it is helpful to recognize that the algorithm can be interpreted as applying the traditional Schwarz alternating iterations in space-time between Omega1 x I_k and Omega2 x I_k, wher I_k is a particular time-slap, as shown in the picture on the right. I emphasize that this interpretation does not require the method to be implemented using a space-time framework, which we do not do.

## Slide 92: Appendix. Sierra/SM: Dynamic Schwarz Coupling
tension.i

## Slide 93: Appendix. Sierra/SM: Dynamic Schwarz Coupling
ends.i
gauge.i

## Slide 94: Appendix. Sierra/SM: Dynamic Schwarz Coupling
schwarz_funcs.i
schwarz_vars.i
solver.i

## Slide 95
Appendix. Dynamic Singular Bar
Inelasticity masks problems by introducing energy dissipation.
Schwarz does not introduce numerical artifacts.
Can couple domains with different time integration schemes (Explicit-Implicit below).

## Slide 96
Appendix. Elastic Wave: Energy Conservation
For clamped beam problem, total energy (TE = ) should be conserved.
Total energy is calculated in 2 ways: with most of contribution from and from
Total energy is conserved and matches single-domain total energy.

## Slide 97
Appendix. Elastic Wave Propagation
Left figure shows # of iterations as a function of overlap region size for 2 subdomains. The method does not converge for 0% overlap. If the overlap is 100% then the single-domain solution is recovered for each of the subdomains.
Right figure shows linear convergence rate of dynamic Schwarz implementation (for small overlap fraction of 0.2%).
Some Performance Results

## Slide 98
Appendix. Torsion Problem
Nonlinear elastic bar (Neohookean material model) subjected to a high degree of torsion.
The domain is .
We evaluate dynamic Schwarz with 2 subdomains: .
Time-discretizations: Newmark (implicit, explicit) with same .
Meshes: HEX, Composite TET10.
Notes: Example 2 is again from the Albany LCM implementation and is slightly more sophisticated. We have a nonlinear elastic bar subjected to a high degree of torsion, so we basically twist the bar. We decompose the domain into 2 subdomains, shown on the right, and evaluate coupling of different elements (HEX, Composite TET10) as well as different time-discretizations (implicit and explicit Newmark).

## Slide 99
Appendix. Torsion: HEX - HEX Coupling
Schwarz and single-domain results agree to almost machine-precision!
Each subdomain discretized using uniform HEX mesh with , and advanced in time using implicit Newmark-Beta scheme with 1e-6.
Results compared to single-domain solution on mesh conformal with Schwarz domain meshes.
Displacement relative errors at final time (T=0.002)
Velocity relative errors at final time (T=0.002)
Notes: As for the quasistatic examples I showed, we start by discretizing the two meshes using uniform conformal hex meshes and compute errors w.r.t. a single domain solution computed on a mesh that is conformal to the two Schwarz meshes. This study reveals that the solutions agree to almost machine precision.

## Slide 100
Appendix. Torsion: HEX - CTET10 Coupling
Coupling of Composite TET10 elements + explicit Newmark with consistent mass in with HEX elements + implicit Newmark in
Reference solution is computed on fine hex mesh + implicit Newmark
Movie of |displacement|
Left: Single-domain,
Right: Schwarz
No dynamic artifacts!
Relative error <1% and does not grow in time!
Notes: Having done this initial verification, we proceed to couple two different element types: hex elements in Omega0 and composite tet10 elements in Omega1 (the composite tet10 is a 10-node tetrahedral element designed in our group specifically for solid mechanics problems). We also use different time-integrators (explicit Newmark in Omega0 and implicit Newmark in Omega1). The movie shows the norm of the displacement for the single domain solution on the left and the Schwarz solution on the right. The solutions are indistinguishable and their relative difference is <1% for all times, and does not grow in time.

## Slide 101
Appendix. Bolted Joint Problem: Performance
Schwarz tolerance = 1e-6
Dynamic Schwarz converges in between 2-4 Schwarz iterations per time-step despite the overlap region being very small for this problem.
* On SNL ascicgpu15, 16, 17 machines (Intel Skylake CPU processor).