## Slide 1
Irina K. Tezaur1, Matt Barone1, Jeff Fike1, Maciej Balajewicz2, Srini Arunajatesan1,
Bart van Bloemen Waanders1, Earl Dowell3
1 Sandia National Laboratories, Livermore CA and Albuquerque, NM
2 University of Illinois Urbana-Champaign 3 Duke University
Virginia Tech Math Department Seminar – May 1, 2017
SAND2017-4018 PE
Approaches for building stable projection-based
reduced order models for compressible flow

## Slide 2
Outline
Motivation.
Projection-based model order reduction.
3. Targeted application: compressible cavity flow.
4. Approaches for building a priori stable ROMs.
  (a) Energy-stable linearized compressible flow ROMs.
  (b) Energy-stable nonlinear compressible flow ROMs.
5. Approaches for stabilizing a posteriori unstable ROMs.
  (a) Eigenvalue reassignment (Linear Time-Invariant systems).
  (b) Basis rotation (nonlinear compressible flow).
Summary/perspectives.
7. Ongoing/future work.

## Slide 3
Outline
Motivation.
Projection-based model order reduction.
3. Targeted application: compressible cavity flow.
4. Approaches for building a priori stable ROMs.
  (a) Energy-stable linearized compressible flow ROMs.
  (b) Energy-stable nonlinear compressible flow ROMs.
5. Approaches for stabilizing a posteriori unstable ROMs.
  (a) Eigenvalue reassignment (Linear Time-Invariant systems).
  (b) Basis rotation (nonlinear compressible flow).
Summary/perspectives.
7. Ongoing/future work.
I have worked on model reduction for compressible flows since 2007.
  focus on ROM stability
This talk surveys some of the approaches for building stable ROMs I have helped to develop.

## Slide 4
Outline
Motivation.
Projection-based model order reduction.
3. Targeted application: compressible cavity flow.
4. Approaches for building a priori stable ROMs.
  (a) Energy-stable linearized compressible flow ROMs.
  (b) Energy-stable nonlinear compressible flow ROMs.
5. Approaches for stabilizing a posteriori unstable ROMs.
  (a) Eigenvalue reassignment (Linear Time-Invariant systems).
  (b) Basis rotation (nonlinear compressible flow).
Summary/perspectives.
7. Ongoing/future work.

## Slide 5
Motivation
Despite improved algorithms and powerful supercomputers, “high-fidelity” models are often too expensive for use in a design or analysis setting.

## Slide 6
Motivation
Application areas in which this situation arises:
Captive-carry and re-entry environments: Large Eddy Simulations (LES) runs require very fine meshes and can take on the order of weeks.
Despite improved algorithms and powerful supercomputers, “high-fidelity” models are often too expensive for use in a design or analysis setting.

## Slide 7
Motivation
Application areas in which this situation arises:
Captive-carry and re-entry environments: Large Eddy Simulations (LES) runs require very fine meshes and can take on the order of weeks.
Despite improved algorithms and powerful supercomputers, “high-fidelity” models are often too expensive for use in a design or analysis setting.
Climate modeling (e.g., land-ice, atmosphere): high-fidelity simulations too costly for uncertainty quantification (UQ); Bayesian inference of high-dimensional parameter fields is intractable.

## Slide 8
Motivation
Application areas in which this situation arises:
Captive-carry and re-entry environments: Large Eddy Simulations (LES) runs require very fine meshes and can take on the order of weeks.
Despite improved algorithms and powerful supercomputers, “high-fidelity” models are often too expensive for use in a design or analysis setting.
Wind plant simulations: wind turbines need to be controlled in real-time to attain optimal energy capture for wind plant system.
Climate modeling (e.g., land-ice, atmosphere): high-fidelity simulations too costly for uncertainty quantification (UQ); Bayesian inference of high-dimensional parameter fields is intractable.

## Slide 9
Surrogate models for time-critical prediction
Surrogate low-dimensional models can enable time-critical prediction and many-query analyses (e.g., design, optimization, control, UQ).

## Slide 10
Surrogate models for time-critical prediction
Three flavors of “surrogate models” for time-critical prediction:
  Data-fit models (e.g., response surfaces, Kriging): directly model I/O map
    Upsides: easy to implement, low complexity
    Downsides: blind to problem physics, impractical for large-dimensional input spaces
  2. Lower-fidelity/reduced-physics models (e.g., coarse mesh, Euler vs. Navier-Stokes)
    Upsides: physics-based, no training required, easy to implement in existing codes.
    Downsides: evaluation times generally not fast enough for time-critical problems, may have inconsistency with higher fidelity models.
  3. Projection-based reduced order models (ROMs): approximately solve state dd equations, then compute outputs
    Upsides: physics-based, can be evaluated in real or near-real time.
    Downsides: intrusive to implement, robustness across wide range of parameters not guaranteed
Surrogate low-dimensional models can enable time-critical prediction and many-query analyses (e.g., design, optimization, control, UQ).

## Slide 11
Surrogate models for time-critical prediction
Three flavors of “surrogate models” for time-critical prediction:
  Data-fit models (e.g., response surfaces, Kriging): directly model I/O map
    Upsides: easy to implement, low complexity
    Downsides: blind to problem physics, impractical for large-dimensional input spaces
  2. Lower-fidelity/reduced-physics models (e.g., coarse mesh, Euler vs. Navier-Stokes)
    Upsides: physics-based, no training required, easy to implement in existing codes.
    Downsides: evaluation times generally not fast enough for time-critical problems, may have inconsistency with higher fidelity models.
  3. Projection-based reduced order models (ROMs): approximately solve state dd equations, then compute outputs
    Upsides: physics-based, can be evaluated in real or near-real time.
    Downsides: intrusive to implement, robustness across wide range of parameters not guaranteed
Surrogate low-dimensional models can enable time-critical prediction and many-query analyses (e.g., design, optimization, control, UQ).
This talk

## Slide 12
Outline
Motivation.
Projection-based model order reduction.
3. Targeted application: compressible cavity flow.
4. Approaches for building a priori stable ROMs.
  (a) Energy-stable linearized compressible flow ROMs.
  (b) Energy-stable nonlinear compressible flow ROMs.
5. Approaches for stabilizing a posteriori unstable ROMs.
  (a) Eigenvalue reassignment (Linear Time-Invariant systems).
  (b) Basis rotation (nonlinear compressible flow).
Summary/perspectives.
7. Ongoing/future work.

## Slide 13
Offline/online strategy
Three underlying mathematical premises of projection-based model order reduction (MOR):

## Slide 14
Offline/online strategy
Compression
Three underlying mathematical premises of projection-based model order reduction (MOR):
  Compression: solution of governing parametric PDE or system of PDEs lies in a subspace of significantly lower dimension.

## Slide 15
Offline/online strategy
High-fidelity simulator
Data collection
Compression
Reduced Order Model (ROM)
projection (dimension reduction)
Offline
Three underlying mathematical premises of projection-based model order reduction (MOR):
  Compression: solution of governing parametric PDE or system of PDEs lies in a subspace of significantly lower dimension.
  Offline training: subspace can be identified/learned offline via training simulation and high-fidelity model can be reformulated with respect to this subspace.

## Slide 16
Offline/online strategy
High-fidelity simulator
Data collection
Compression
Reduced Order Model (ROM)
projection (dimension reduction)
Offline
Online
Real-time analysis
Three underlying mathematical premises of projection-based model order reduction (MOR):
  Compression: solution of governing parametric PDE or system of PDEs lies in a subspace of significantly lower dimension.
  Offline training: subspace can be identified/learned offline via training simulation and high-fidelity model can be reformulated with respect to this subspace.
  Online prediction: identified parametric ROMs are capable of providing new solutions at a fraction of the computational cost.

## Slide 17
Proper Orthogonal Decomposition (POD)/
Galerkin method to model reduction
Snapshot matrix: , …,
SVD:
Truncation: )
FOM = full order model
# of dofs in FOM
# of snapshots
# of dofs in ROM
(, )
High fidelity CFD simulations:
Snapshot 1
Snapshot 2
Snapshot K
Fluid modal decomposition (POD):
Galerkin projection
of fluid PDEs:
“Small” ROM ODE system:
)
Step 1
Step 2
Basis energy =

## Slide 18
Continuous vs. discrete Galerkin projection
Continuous Projection
Discrete Projection
Governing PDEs
Governing PDEs
High-fidelity model
High-fidelity model
Discrete modal basis
Continuous modal basis*
Projection of FOM
(matrix operation)
Projection of governing PDEs (numerical integration)
ROM
ROM
* Continuous function space defined using e.g., finite elements.
If PDEs are linear or have polynomial non-linearities, projection can be calculated in offline stage of MOR.

## Slide 19
Continuous vs. discrete Galerkin projection
Continuous Projection
Discrete Projection
Governing PDEs
Governing PDEs
High-fidelity model
High-fidelity model
Discrete modal basis
Continuous modal basis*
Projection of FOM
(matrix operation)
Projection of governing PDEs (numerical integration)
ROM
ROM
If PDEs are linear or have polynomial non-linearities, projection can be calculated in offline stage of MOR.
Most of my ROM work
* Continuous function space defined using e.g., finite elements.

## Slide 20
Outline
Motivation.
Projection-based model order reduction.
3. Targeted application: compressible cavity flow.
4. Approaches for building a priori stable ROMs.
  (a) Energy-stable linearized compressible flow ROMs.
  (b) Energy-stable nonlinear compressible flow ROMs.
5. Approaches for stabilizing a posteriori unstable ROMs.
  (a) Eigenvalue reassignment (Linear Time-Invariant systems).
  (b) Basis rotation (nonlinear compressible flow).
Summary/perspectives.
7. Ongoing/future work.

## Slide 21
Targeted application: compressible flow
We are interested in the compressible captive-carry problem.

## Slide 22
Targeted application: compressible flow
We are interested in the compressible captive-carry problem.
Of primary interest are long-time predictive simulations: ROM run at same parameters as FOM but much longer in time.

## Slide 23
Targeted application: compressible flow
We are interested in the compressible captive-carry problem.
Of primary interest are long-time predictive simulations: ROM run at same parameters as FOM but much longer in time.
  QoIs: statistics of flow, e.g., pressure Power Spectral Densities (PSDs) [right].

## Slide 24
Targeted application: compressible flow
We are interested in the compressible captive-carry problem.
Secondary interest: ROMs robust w.r.t. parameter changes (e.g., Reynolds, Mach number) for enabling uncertainty quantification.
Of primary interest are long-time predictive simulations: ROM run at same parameters as FOM but much longer in time.
  QoIs: statistics of flow, e.g., pressure Power Spectral Densities (PSDs) [right].

## Slide 25
Targeted application: compressible flow
Compressible flow equations:

## Slide 26
Targeted application: compressible flow
Compressible flow equations:
Majority of fluid ROMs in literature are for incompressible flow.

## Slide 27
Targeted application: compressible flow
Compressible flow equations:
Compressible flow solutions can exhibit the following complex features:
  Sharp boundary layers.
  Turbulence/chaotic dynamics.
  Shocks.
Majority of fluid ROMs in literature are for incompressible flow.

## Slide 28
Targeted application: compressible flow
Compressible flow solutions can exhibit the following complex features:
  Sharp boundary layers.
  Turbulence/chaotic dynamics.
  Shocks.
Desired numerical properties of ROMs:
  Consistency (w.r.t. the continuous PDEs).
  Stability: if full order model (FOM) is stable, ROM should be stable.
  Convergence: requires consistency and stability.
  Accuracy (w.r.t. FOM).
  Efficiency.
  Robustness (w.r.t. time or parameter changes).
Compressible flow equations:
Majority of fluid ROMs in literature are for incompressible flow.

## Slide 29
Targeted application: compressible flow
Compressible flow solutions can exhibit the following complex features:
  Sharp boundary layers.
  Turbulence/chaotic dynamics.
  Shocks.
Desired numerical properties of ROMs:
  Consistency (w.r.t. the continuous PDEs).
  Stability: if full order model (FOM) is stable, ROM should be stable.
  Convergence: requires consistency and stability.
  Accuracy (w.r.t. FOM).
  Efficiency.
  Robustness (w.r.t. time or parameter changes).
Compressible flow equations:
Focus of this talk is ROM stability.
Majority of fluid ROMs in literature are for incompressible flow.

## Slide 30
ROM instability problem
Stability can be a real problem for compressible flow ROMs!

## Slide 31
ROM instability problem
A compressible fluid POD/Galerkin ROM might be stable for a given number of modes, but unstable for other choices of basis size (Bui-Tanh et al. 2007; Barone et al. 2009).
Stability can be a real problem for compressible flow ROMs!

## Slide 32
ROM instability problem
A compressible fluid POD/Galerkin ROM might be stable for a given number of modes, but unstable for other choices of basis size (Bui-Tanh et al. 2007, Barone et al. 2009).
  Instability can manifest itself in different ways, e.g., blow-up during time-integration, spurious oscillations, ROM computes non-physical quantities.
Stability can be a real problem for compressible flow ROMs!
Top right: FOM
\
Bottom right: ROM

## Slide 33
ROM instability problem
A compressible fluid POD/Galerkin ROM might be stable for a given number of modes, but unstable for other choices of basis size (Bui-Tanh et al. 2007, Barone et al. 2009).
  Instability can manifest itself in different ways, e.g., blow-up during time-integration, spurious oscillations, ROM computes non-physical quantities.
Stability can be a real problem for compressible flow ROMs!
There is no a priori stability guarantee for POD/Galerkin ROMs for compressible flow!
Top right: FOM
\
Bottom right: ROM

## Slide 34
ROM instability problem
A compressible fluid POD/Galerkin ROM might be stable for a given number of modes, but unstable for other choices of basis size (Bui-Tanh et al. 2007, Barone et al. 2009).
  Instability can manifest itself in different ways, e.g., blow-up during time-integration, spurious oscillations, ROM computes non-physical quantities.
Stability can be a real problem for compressible flow ROMs!
There is no a priori stability guarantee for POD/Galerkin ROMs for compressible flow!
Stability of a ROM is commonly evaluated a posteriori – RISKY!
Top right: FOM
\
Bottom right: ROM

## Slide 35
ROM instability problem
Instability can be due to:

## Slide 36
ROM instability problem
Instability can be due to:
  1. Choice of inner product: Galerkin projection + inner product is unstable.

## Slide 37
ROM instability problem
Instability can be due to:
  1. Choice of inner product: Galerkin projection + inner product is unstable.
  2. Basis truncation: destroys balance between energy production & hhhdissipation.

## Slide 38
ROM instability problem
Instability can be due to:
  1. Choice of inner product: Galerkin projection + inner product is unstable.
  2. Basis truncation: destroys balance between energy production & hhhdissipation.
Some* remedies:
 | Continuous Projection | Discrete Projection
Change projection (a priori) | Energy inner products (Rowley et al., Serre et al., IKT et al.) | Energy inner products (Rowley, et al.), Petrov-Galerkin Projection (Carlberg et al.)
Change ROM equations (a posteriori) | Linear/nonlinear turbulence modeling (Iliescu, Borggaard, Xie, Wang, …) | Eigenvalue reassignment (IKT et al.)
Change ROM basis (a posteriori) | Basis rotation (Balajewicz, IKT, et al.) | Optimization-based right basis modification (Amsallem et al.)
* This is not a complete list!

## Slide 39
ROM instability problem
Instability can be due to:
  1. Choice of inner product: Galerkin projection + inner product is unstable.
  2. Basis truncation: destroys balance between energy production & hhhdissipation.
This talk is on a priori (intrusive) and a posteriori (non-intrusive) approaches for remedying ROM instability for POD/Galerkin ROMs.
Some* remedies:
 | Continuous Projection | Discrete Projection
Change projection (a priori) | Energy inner products (Rowley et al., Serre et al., IKT et al.) | Energy inner products (Rowley, et al.), Petrov-Galerkin Projection (Carlberg et al.)
Change ROM equations (a posteriori) | Linear/nonlinear turbulence modeling (Iliescu, Borggaard, Xie, Wang, …) | Eigenvalue reassignment (IKT et al.)
Change ROM basis (a posteriori) | Basis rotation (Balajewicz, IKT, et al.) | Optimization-based right basis modification (Amsallem et al.)
* This is not a complete list!

## Slide 40
Outline
Motivation.
Projection-based model order reduction.
3. Targeted application: compressible cavity flow.
4. Approaches for building a priori stable ROMs.
  (a) Energy-stable linearized compressible flow ROMs.
  (b) Energy-stable nonlinear compressible flow ROMs.
5. Approaches for stabilizing a posteriori unstable ROMs.
  (a) Eigenvalue reassignment (Linear Time-Invariant systems).
  (b) Basis rotation (nonlinear compressible flow).
Summary/perspectives.
7. Ongoing/future work.
 | Continuous Projection | Discrete Projection
Change projection (a priori) | Energy inner products (Rowley et al., Serre et al., IKT et al.) | Energy inner products (Rowley, et al.), Petrov-Galerkin Projection (Carlberg et al.)
Change ROM equations (a posteriori) | Linear/nonlinear turbulence modeling (Iliescu, Borggaard, Xie, Wang, …) | Eigenvalue reassignment (IKT et al.)
Change ROM basis (a posteriori) | Basis rotation (Balajewicz, IKT, et al.) | Optimization-based right basis modificatiOon (Amsallem)

## Slide 41
Energy-stability

## Slide 42
Energy-stability
Practical Definition: Numerical solution does not “blow up” in finite time.

## Slide 43
Energy-stability
Practical Definition: Numerical solution does not “blow up” in finite time.
More Precise Definition: Numerical discretization does not introduce any spurious instabilities inconsistent with natural instability modes supported by the governing continuous PDEs.

## Slide 44
Energy-stability
Practical Definition: Numerical solution does not “blow up” in finite time.
More Precise Definition: Numerical discretization does not introduce any spurious instabilities inconsistent with natural instability modes supported by the governing continuous PDEs.
Numerical solutions must maintain proper energy balance.

## Slide 45
Energy-stability
Practical Definition: Numerical solution does not “blow up” in finite time.
More Precise Definition: Numerical discretization does not introduce any spurious instabilities inconsistent with natural instability modes supported by the governing continuous PDEs.
Numerical solutions must maintain proper energy balance.
Stability of ROM is intimately tied to choice of inner product for the Galerkin projection (Rowley et al., 2004; Barone & IKT, 2009; Serre et al., 2012).

## Slide 46
Energy-stability
Practical Definition: Numerical solution does not “blow up” in finite time.
More Precise Definition: Numerical discretization does not introduce any spurious instabilities inconsistent with natural instability modes supported by the governing continuous PDEs.
Numerical solutions must maintain proper energy balance.
Stability of ROM is intimately tied to choice of inner product for the Galerkin projection (Rowley et al., 2004; Barone & IKT, 2009; Serre et al., 2012).
  Norm induced by inner product in which ROM is constructed should correspond to energy measure for system.

## Slide 47
Energy-stability
Practical Definition: Numerical solution does not “blow up” in finite time.
More Precise Definition: Numerical discretization does not introduce any spurious instabilities inconsistent with natural instability modes supported by the governing continuous PDEs.
Numerical solutions must maintain proper energy balance.
Stability of ROM is intimately tied to choice of inner product for the Galerkin projection (Rowley et al., 2004; Barone & IKT, 2009; Serre et al., 2012).
  Norm induced by inner product in which ROM is constructed should correspond to energy measure for system.
  Incompressible flow: solution vector is inner product induces norm representing global kinetic energy ().

## Slide 48
Energy-stability
Practical Definition: Numerical solution does not “blow up” in finite time.
More Precise Definition: Numerical discretization does not introduce any spurious instabilities inconsistent with natural instability modes supported by the governing continuous PDEs.
Numerical solutions must maintain proper energy balance.
Stability of ROM is intimately tied to choice of inner product for the Galerkin projection (Rowley et al., 2004; Barone & IKT, 2009; Serre et al., 2012).
  Norm induced by inner product in which ROM is constructed should correspond to energy measure for system.
  Incompressible flow: solution vector is inner product induces norm representing global kinetic energy ().
    inner product is physically sensible, since POD modes represent optimally kinetic energy present in the ensemble from which they are constructed:

## Slide 49
Energy-stability
Practical Definition: Numerical solution does not “blow up” in finite time.
More Precise Definition: Numerical discretization does not introduce any spurious instabilities inconsistent with natural instability modes supported by the governing continuous PDEs.
Numerical solutions must maintain proper energy balance.
Stability of ROM is intimately tied to choice of inner product for the Galerkin projection (Rowley et al., 2004; Barone & IKT, 2009; Serre et al., 2012).
  Norm induced by inner product in which ROM is constructed should correspond to energy measure for system.
  Incompressible flow: solution vector is inner product induces norm representing global kinetic energy ().
    inner product is physically sensible, since POD modes represent optimally kinetic energy present in the ensemble from which they are constructed:
Not the case for compressible flow!

## Slide 50
Energy-stability
Energy inner product is one that
  For linear system: leads to semi-boundedness of linear operator w.r.t. inner product , i.e.,
  = ,
    leads to stability estimate
  For nonlinear system: induces norm that represents global energy quantity (e.g., kinetic energy, stagnation energy, total energy, etc.).

## Slide 51
Energy-stability
Energy inner product is one that
  For linear system: leads to semi-boundedness of linear operator w.r.t. inner product , i.e.,
  = ,
    leads to stability estimate
  For nonlinear system: induces norm that represents global energy quantity (e.g., kinetic energy, stagnation energy, total energy, etc.).
Practical implication of energy-stability analysis:
energy inner product ensures that any “bad” modes will not introduce spurious non-physical numerical instabilities into the Galerkin approximation.

## Slide 52
Energy-stability
Energy inner product is one that
  For linear system: leads to semi-boundedness of linear operator w.r.t. inner product , i.e.,
  = ,
    leads to stability estimate
  For nonlinear system: induces norm that represents global energy quantity (e.g., kinetic energy, stagnation energy, total energy, etc.).
Practical implication of energy-stability analysis:
energy inner product ensures that any “bad” modes will not introduce spurious non-physical numerical instabilities into the Galerkin approximation.
Stability-preserving inner product derived using the energy method:
  Defines numerical solution energy || 2 and bounds it in a physical way.
  Borrowed from spectral methods community.
  Analysis is straightforward for ROMs constructed via continuous projection.

## Slide 53
Outline
Motivation.
Projection-based model order reduction.
3. Targeted application: compressible cavity flow.
4. Approaches for building a priori stable ROMs.
  (a) Energy-stable linearized compressible flow ROMs.
  (b) Energy-stable nonlinear compressible flow ROMs.
5. Approaches for stabilizing a posteriori unstable ROMs.
  (a) Eigenvalue reassignment (Linear Time-Invariant systems).
  (b) Basis rotation (nonlinear compressible flow).
Summary/perspectives.
7. Ongoing/future work.
with: Matt Barone (SNL),
Srini Arunajatesan (SNL)
 | Continuous Projection | Discrete Projection
Change projection (a priori) | Energy inner products (Rowley et al., Serre et al., IKT et al.) | Energy inner products (Rowley, et al.), Petrov-Galerkin Projection (Carlberg et al.)
Change ROM equations (a posteriori) | Linear/nonlinear turbulence modeling (Iliescu, Borggaard, Xie, Wang, …) | Eigenvalue reassignment (IKT et al.)
Change ROM basis (a posteriori) | Basis rotation (Balajewicz, IKT, et al.) | Optimization-based right basis modificatiOon (Amsallem)

## Slide 54
Linearized compressible flow equations
Energy-Stability for Linearized PDEs:
FOM linearly stable ROM built in energy inner product linearly stable ()
(Barone et al. 2009, IKT et al. 2012)

## Slide 55
Linearized compressible flow equations
Energy-Stability for Linearized PDEs:
FOM linearly stable ROM built in energy inner product linearly stable ()
(Barone et al. 2009, IKT et al. 2012)
Linearized compressible Euler/Navier-Stokes equations are appropriate when a compressible fluid system can be described by small-amplitude perturbations about a steady-state mean flow.

## Slide 56
Linearized compressible flow equations
Energy-Stability for Linearized PDEs:
FOM linearly stable ROM built in energy inner product linearly stable ()
(Barone et al. 2009, IKT et al. 2012)
Full non-linear compressible flow equations

## Slide 57
Linearized compressible flow equations
Linearization of full compressible Euler/Navier-Stokes equations obtained as follows:
  Decompose fluid field as steady mean plus unsteady fluctuation
  Linearize full nonlinear compressible Navier-Stokes equations around steady mean to yield linear hyperbolic/incompletely parabolic system
Energy-Stability for Linearized PDEs:
FOM linearly stable ROM built in energy inner product linearly stable ()
(Barone et al. 2009, IKT et al. 2012)
fluid solution vector (e.g., )
Full non-linear compressible flow equations

## Slide 58
Energy-stable ROMs for linearized
compressible flow
Linearized compressible Euler/Navier-Stokes equations are symmetrizable (Barone & IKT, 2009; IKT & Arunajatesan, 2012).

## Slide 59
Energy-stable ROMs for linearized
compressible flow
There exists a symmetric positive definite matrix (system “symmetrizer”) s.t.:
  The convective flux matrices are symmetric
  The following augmented viscosity matrix is symmetric positive semi-definite
Linearized compressible Euler/Navier-Stokes equations are symmetrizable (Barone & IKT, 2009; IKT & Arunajatesan, 2012).

## Slide 60
Energy-stable ROMs for linearized
compressible flow
There exists a symmetric positive definite matrix (system “symmetrizer”) s.t.:
  The convective flux matrices are symmetric
  The following augmented viscosity matrix is symmetric positive semi-definite
Symmetry Inner Product (weighted inner product):
Linearized compressible Euler/Navier-Stokes equations are symmetrizable (Barone & IKT, 2009; IKT & Arunajatesan, 2012).

## Slide 61
Energy-stable ROMs for linearized
compressible flow
There exists a symmetric positive definite matrix (system “symmetrizer”) s.t.:
  The convective flux matrices are symmetric
  The following augmented viscosity matrix is symmetric positive semi-definite
Symmetry Inner Product (weighted inner product):
If ROM is built in symmetry inner product, Galerkin approximation will satisfy the same energy expression as continuous PDEs, e.g., it will be energy-stable:
Linearized compressible Euler/Navier-Stokes equations are symmetrizable (Barone & IKT, 2009; IKT & Arunajatesan, 2012).

## Slide 62
Symmetrizers for several hyperbolic/
incompletely parabolic systems
Wave equation: or where
Linearized shallow water equations:
Linearized compressible Euler:
  Linearized compressible Navier-Stokes:
Barone & IKT, JCP, 2009.
IKT & Arunajatesan, WCCM X, 2012.
IKT et al., SAND report, 2014.

## Slide 63
Consider linear discrete (i.e., discretized in space) stable full order model
Lyapunov function for this FOM: where is the solution of the Lyapunov equation
S.p.d. solution to Lyapunov equation exists if is s.p.d. and is stable.
There are solvers for solving the Lyapunov equation, e.g., lyap function in MATLAB control toolbox.
Discrete analog of symmetry inner product: Lyapunov inner product (Rowley et al., 2004):
Can show: if ROM is constructed in Lyapunov inner product, it is energy-stable, i.e.,
Discrete counterpart of symmetry-inner
product: Lyapunov inner product

## Slide 64
Consider linear discrete (i.e., discretized in space) stable full order model
Lyapunov function for this FOM: where is the solution of the Lyapunov equation
S.p.d. solution to Lyapunov equation exists if is s.p.d. and is stable.
There are solvers for solving the Lyapunov equation, e.g., lyap function in MATLAB control toolbox.
Discrete analog of symmetry inner product: Lyapunov inner product (Rowley et al., 2004):
Can show: if ROM is constructed in Lyapunov inner product, it is energy-stable, i.e.,
Discrete counterpart of symmetry-inner
product: Lyapunov inner product
Intractable for large problems (ops!

## Slide 65
Steps to obtain stable ROM in symmetry i.p.
Galerkin-project equations using symmetry inner product:

## Slide 66
Steps to obtain stable ROM in symmetry i.p.
Galerkin-project equations using symmetry inner product:
Remark: Galerkin projection in symmetry inner product is equivalent to Petrov-Galerkin projection with

## Slide 67
Steps to obtain stable ROM in symmetry i.p.
Remark: Galerkin projection in symmetry inner product is equivalent to Petrov-Galerkin projection with
Substitute BCs
Galerkin-project equations using symmetry inner product:
Integrate second term by parts and apply boundary conditions weakly:

## Slide 68
Steps to obtain stable ROM in symmetry i.p.
Remark: Galerkin projection in symmetry inner product is equivalent to Petrov-Galerkin projection with
Substitute BCs
Galerkin-project equations using symmetry inner product:
Integrate second term by parts and apply boundary conditions weakly:
Substitute modal decomposition to obtain an linear dynamical system of the form .

## Slide 69
Continuous projection implementation:
“Spirit” code
POD modes defined using piecewise smooth finite elements.
Gauss quadrature rules of sufficient accuracy are used to compute exactly inner products with the help of the libmesh library.
Physics in Spirit:
  Linearized compressible Euler (, energy inner product).
  Linearized compressible Navier-Stokes (, energy inner product).
  Nonlinear isentropic compressible Navier-Stokes (, stagnation energy, stagnation enthalpy inner product).
  Nonlinear compressible Navier-Stokes (, energy inner product).
“Spirit” ROM Code = 3D parallel C++ POD/Galerkin test-bed ROM code that uses data-structures and eigensolvers from Trilinos to build energy-stable ROMs for compressible flow problems
stand-alone code that can be synchronized with any high-fidelity code!
“SIGMA CFD” High-Fidelity Code = Sandia in-house finite volume flow solver derived from LESLIE3D (Genin & Menon, 2010), an LES flow solver originally developed in the Computational Combustion Laboratory at Georgia Tech.

## Slide 70
Continuous projection implementation:
“Spirit” code
POD modes defined using piecewise smooth finite elements.
Gauss quadrature rules of sufficient accuracy are used to compute exactly inner products with the help of the libmesh library.
Physics in Spirit:
  Linearized compressible Euler (, energy inner product).
  Linearized compressible Navier-Stokes (, energy inner product).
  Nonlinear isentropic compressible Navier-Stokes (, stagnation energy, stagnation enthalpy inner product).
  Nonlinear compressible Navier-Stokes (, energy inner product).
“Spirit” ROM Code = 3D parallel C++ POD/Galerkin test-bed ROM code that uses data-structures and eigensolvers from Trilinos to build energy-stable ROMs for compressible flow problems
stand-alone code that can be synchronized with any high-fidelity code!
“SIGMA CFD” High-Fidelity Code = Sandia in-house finite volume flow solver derived from LESLIE3D (Genin & Menon, 2010), an LES flow solver originally developed in the Computational Combustion Laboratory at Georgia Tech.
First, testing of ROMs for these physics

## Slide 71
Numerical results: random basis example
Uniform base flow: physically stable to any linear disturbance.
Each mode is random disturbance field that decays to 0 at domain boundaries.
Model problem for modes determined by numerical error: extreme case of “bad” modes.

## Slide 72
Numerical results: 2D inviscid pressure pulse
Inviscid pulse in a uniform base flow.
High-fidelity simulation run on mesh with 3362 nodes, up to time seconds.
200 snapshots of solution used to construct mode ROM in and symmetry inner products.
vs. for
ROM
Symmetry ROM

## Slide 73
Inviscid pulse in a uniform base flow (linear dynamics).
High-fidelity simulation run on mesh with 3362 nodes, up to time seconds.
200 snapshots of solution used to construct mode ROM in and symmetry inner products.
p’: ROM
p’: Symmetry ROM
p’: High-fidelity
time of snapshot 10
Numerical results: 2D inviscid pressure pulse

## Slide 74
p’: ROM
p’: Symmetry ROM
p’: High-fidelity
time of snapshot 0
time of snapshot 160
Inviscid pulse in a uniform base flow (linear dynamics).
High-fidelity simulation run on mesh with 3362 nodes, up to time seconds.
200 snapshots of solution used to construct mode ROM in and symmetry inner products.
Numerical results: 2D inviscid pressure pulse

## Slide 75
Outline
Motivation.
Projection-based model order reduction.
3. Targeted application: compressible cavity flow.
4. Approaches for building a priori stable ROMs.
  (a) Energy-stable linearized compressible flow ROMs.
  (b) Energy-stable nonlinear compressible flow ROMs.
5. Approaches for stabilizing a posteriori unstable ROMs.
  (a) Eigenvalue reassignment (Linear Time-Invariant systems).
  (b) Basis rotation (nonlinear compressible flow).
Summary/perspectives.
7. Ongoing/future work.
with: Matt Barone (SNL), Jeff Fike (SNL), Srini Arunajatesan (SNL)
 | Continuous Projection | Discrete Projection
Change projection (a priori) | Energy inner products (Rowley et al., Serre et al., IKT et al.) | Energy inner products (Rowley, et al.), Petrov-Galerkin Projection (Carlberg et al.)
Change ROM equations (a posteriori) | Linear/nonlinear turbulence modeling (Iliescu, Borggaard, Xie, Wang, …) | Eigenvalue reassignment (IKT et al.)
Change ROM basis (a posteriori) | Basis rotation (Balajewicz, IKT, et al.) | Optimization-based right basis modificatiOon (Amsallem)

## Slide 76
Nonlinear compressible flow equations
Compressible isentropic Navier-Stokes equations (cold flows, moderate Mach #):
Full compressible Navier-Stokes equations:
enthalpy
velocity vector
density
temperature
viscous stress tensor
Energy-Stability for Nonlinear PDEs:
ROM built in energy inner product will preserve stability of an equilibrium point at 0 for the governing nonlinear system of PDEs (Rowley et al., 2004; IKT et al., 2014).

## Slide 77
Energy-stable ROMs for nonlinear compressible
flow: isentropic NS (Rowley et al., 2004)
In (Rowley et al., 2004), Rowley et al. showed that energy inner product for the compressible isentropic Navier-Stokes equations can be defined following a transformation of these equations.

## Slide 78
Energy-stable ROMs for nonlinear compressible
flow: isentropic NS (Rowley et al., 2004)
In (Rowley et al., 2004), Rowley et al. showed that energy inner product for the compressible isentropic Navier-Stokes equations can be defined following a transformation of these equations.
Transformed compressible isentropic Navier-Stokes equations:
speed of sound
()
velocity

## Slide 79
Energy-stable ROMs for nonlinear compressible
flow: isentropic NS (Rowley et al., 2004)
In (Rowley et al., 2004), Rowley et al. showed that energy inner product for the compressible isentropic Navier-Stokes equations can be defined following a transformation of these equations.
Transformed compressible isentropic Navier-Stokes equations:
Family of inner products:
speed of sound
()
velocity

## Slide 80
Energy-stable ROMs for nonlinear compressible
flow: isentropic NS (Rowley et al., 2004)
Transformed compressible isentropic Navier-Stokes equations:
Family of inner products:
If Galerkin projection step of model reduction is performed in inner product, then the Galerkin projection will preserve the stability of an equilibrium point at the origin (Rowley et al., 2004).
speed of sound
()
velocity
In (Rowley et al., 2004), Rowley et al. showed that energy inner product for the compressible isentropic Navier-Stokes equations can be defined following a transformation of these equations.

## Slide 81
Energy-stable ROMs for nonlinear compressible
flow: full NS
Our work extends ideas in (Rowley et al., 2004) to full compressible N-S equations.
Requirement: transformation/inner product yields PDEs with only polynomial non-linearities.

## Slide 82
Energy-stable ROMs for nonlinear compressible
flow: full NS
First, full compressible Navier-Stokes equations are transformed into the following variables:
, ,
internal energy
Our work extends ideas in (Rowley et al., 2004) to full compressible N-S equations.
Requirement: transformation/inner product yields PDEs with only polynomial non-linearities.

## Slide 83
Energy-stable ROMs for nonlinear compressible
flow: full NS
First, full compressible Navier-Stokes equations are transformed into the following variables:
Next, the following “total energy” inner product is defined:
Norm induced by total energy inner product is the total energy of the fluid system:
, ,
internal energy
Our work extends ideas in (Rowley et al., 2004) to full compressible N-S equations.
Requirement: transformation/inner product yields PDEs with only polynomial non-linearities.

## Slide 84
Energy-stable ROMs for nonlinear compressible
flow: full NS
First, full compressible Navier-Stokes equations are transformed into the following variables:
Next, the following “total energy” inner product is defined:
If Galerkin projection step of model reduction is performed in total energy inner product, then the Galerkin projection will preserve the stability of an equilibrium point at the origin
(IKT et al., 2014)
Norm induced by total energy inner product is the total energy of the fluid system:
, ,
internal energy
Our work extends ideas in (Rowley et al., 2004) to full compressible N-S equations.
Requirement: transformation/inner product yields PDEs with only polynomial non-linearities.

## Slide 85
Energy-stable ROMs for nonlinear compressible
flow: full NS
First, full compressible Navier-Stokes equations are transformed into the following variables:
Next, the following “total energy” inner product is defined:
If Galerkin projection step of model reduction is performed in total energy inner product, then the Galerkin projection will preserve the stability of an equilibrium point at the origin
(IKT et al., 2014)
Norm induced by total energy inner product is the total energy of the fluid system:
 Transformed equations have only polynomial non-linearities (projection of which can be computed in offline stage of MOR and stored).
, ,
internal energy
Our work extends ideas in (Rowley et al., 2004) to full compressible N-S equations.
Requirement: transformation/inner product yields PDEs with only polynomial non-linearities.

## Slide 86
Energy-stable ROMs for nonlinear compressible
flow: full NS
First, full compressible Navier-Stokes equations are transformed into the following variables:
Next, the following “total energy” inner product is defined:
If Galerkin projection step of model reduction is performed in total energy inner product, then the Galerkin projection will preserve the stability of an equilibrium point at the origin
(IKT et al., 2014)
Norm induced by total energy inner product is the total energy of the fluid system:
 Transformed equations have only polynomial non-linearities (projection of which can be computed in offline stage of MOR and stored).
 Transformation introduces higher order polynomial non-linearities for viscous case.
, ,
internal energy
Our work extends ideas in (Rowley et al., 2004) to full compressible N-S equations.
Requirement: transformation/inner product yields PDEs with only polynomial non-linearities.

## Slide 87
Energy-stable ROMs for nonlinear compressible
flow: full NS
First, full compressible Navier-Stokes equations are transformed into the following variables:
Next, the following “total energy” inner product is defined:
If Galerkin projection step of model reduction is performed in total energy inner product, then the Galerkin projection will preserve the stability of an equilibrium point at the origin
(IKT et al., 2014)
Norm induced by total energy inner product is the total energy of the fluid system:
 Transformed equations have only polynomial non-linearities (projection of which can be computed in offline stage of MOR and stored).
 Transformation introduces higher order polynomial non-linearities for viscous case.
   Efficiency of online stage of MOR can be recovered using hyper-reduction (e.g., DEIM, gappy POD).
, ,
internal energy
Our work extends ideas in (Rowley et al., 2004) to full compressible N-S equations.
Requirement: transformation/inner product yields PDEs with only polynomial non-linearities.

## Slide 88
Continuous projection
Implementation: “Spirit” Code
POD modes defined using piecewise smooth finite elements.
Gauss quadrature rules of sufficient accuracy are used to compute exactly inner products with the help of the libmesh library.
Physics in spirit:
  Linearized compressible Euler (, energy inner product).
  Linearized compressible Navier-Stokes (, energy inner product).
  Nonlinear isentropic compressible Navier-Stokes (, stagnation energy, stagnation enthalpy inner product).
  Nonlinear compressible Navier-Stokes (, energy inner product).
“Spirit” ROM Code = 3D parallel C++ POD/Galerkin test-bed ROM code that uses data-structures and eigensolvers from Trilinos to build energy-stable ROMs for compressible flow problems
stand-alone code that can be synchronized with any high-fidelity code!
“SIGMA CFD” High-Fidelity Code = Sandia in-house finite volume flow solver derived from LESLIE3D (Genin & Menon, 2010), a LES flow solver originally developed in the Computational Combustion Laboratory at Georgia Tech.
Now, testing of ROMs for these physics

## Slide 89
Numerical results: viscous laminar cavity
Viscous cavity problem at , (laminar regime).
High-fidelity simulation: DNS based on full nonlinear compressible Navier-Stokes equations with nodes (right).
snapshots collected, every seconds.
Snapshots used to construct mode ROM for nonlinear compressible Navier-Stokes equations in and total energy inner products.
mode POD bases capture of snapshot energy.
Figure above: viscous laminar cavity problem domain/mesh.

## Slide 90
Numerical results: viscous laminar cavity
High-Fidelity
5 mode total energy ROM
ROM ( modes) | Error ( norm)
Nonlinear ROM | 
Total Energy ROM | 
Total Energy ROM | 
L2 ROM blows up; energy ROM remains stable.
Future work: improving efficiency of total energy ROMs through incorporation of hyper-reduction (e.g., DEIM, gappy POD).
Figure above: -component of velocity as a function of time

## Slide 91
Outline
Motivation.
Projection-based model order reduction.
3. Targeted application: compressible cavity flow.
4. Approaches for building a priori stable ROMs.
  (a) Energy-stable linearized compressible flow ROMs.
  (b) Energy-stable nonlinear compressible flow ROMs.
5. Approaches for stabilizing a posteriori unstable ROMs.
  (a) Eigenvalue reassignment (Linear Time-Invariant systems).
  (b) Basis rotation (nonlinear compressible flow).
Summary/perspectives.
7. Ongoing/future work.
with: Matt Barone (SNL), Srini Arunajatesan (SNL), Bart van Bloemen Waanders (SNL)
 | Continuous Projection | Discrete Projection
Change projection (a priori) | Energy inner products (Rowley et al., Serre et al., IKT et al.) | Energy inner products (Rowley, et al.), Petrov-Galerkin Projection (Carlberg et al.)
Change ROM equations (a posteriori) | Linear/nonlinear turbulence modeling (Iliescu, Borggaard, Xie, Wang, …) | Eigenvalue reassignment (IKT et al.)
Change ROM basis (a posteriori) | Basis rotation (Balajewicz, IKT, et al.) | Optimization-based right basis modificatiOon (Amsallem)

## Slide 92
Stable ROMs for Linear Time-Invariant (LTI) systems
Attention restricted to Linear Time Invariant (LTI) systems
as a first step towards the more general nonlinear case.

## Slide 93
Stable ROMs for Linear Time-Invariant (LTI) systems
Attention restricted to Linear Time Invariant (LTI) systems
as a first step towards the more general nonlinear case.
LTI Full Order Model (FOM)
LTI Reduced Order Model (ROM)

## Slide 94
Stable ROMs for Linear Time-Invariant (LTI) systems
Attention restricted to Linear Time Invariant (LTI) systems
as a first step towards the more general nonlinear case.
LTI Full Order Model (FOM)
LTI Reduced Order Model (ROM)
Problem: stable stable!

## Slide 95
Stable ROMs for Linear Time-Invariant (LTI) systems
Attention restricted to Linear Time Invariant (LTI) systems
as a first step towards the more general nonlinear case.
LTI Full Order Model (FOM)
LTI Reduced Order Model (ROM)
Problem: stable stable!
Unstable ROM ( unstable)
Stabilization Algorithm
( )
Stable and Accurate ROM ( stable)
Solution:
Black box

## Slide 96
ROM stabilization via optimization-based
eigenvalue reassignment (IKT et al., 2014)
ROM Stabilization Optimization Problem
(Constrained Nonlinear Least Squares):
= unstable eigenvalues of original ROM matrix .
snapshot output at .
ROM output at .
(1)
Replace unstable
with stable .
Idea: modify ROM system s.t. is stable and discrepancy b/w ROM output and FOM output is minimal.

## Slide 97
ROM stabilization via optimization-based
eigenvalue reassignment (IKT et al., 2014)
ROM Stabilization Optimization Problem
(Constrained Nonlinear Least Squares):
= unstable eigenvalues of original ROM matrix .
snapshot output at .
ROM output at .
ROM stabilization optimization problem is small:
(1)
Replace unstable
with stable .
Idea: modify ROM system s.t. is stable and discrepancy b/w ROM output and FOM output is minimal.

## Slide 98
ROM stabilization via optimization-based
eigenvalue reassignment (IKT et al., 2014)
ROM Stabilization Optimization Problem
(Constrained Nonlinear Least Squares):
= unstable eigenvalues of original ROM matrix .
snapshot output at .
ROM output at .
ROM stabilization optimization problem is small:
ROM stabilization optimization problem can be solved by standard optimization algorithms, e.g., interior point method.
  We use fmincon function in MATLAB’s optimization toolbox.
  We implement ROM stabilization optimization problem in characteristic variables where .
(1)
Replace unstable
with stable .
Idea: modify ROM system s.t. is stable and discrepancy b/w ROM output and FOM output is minimal.

## Slide 99
Algorithm
Diagonalize the ROM matrix : .
Initialize a diagonal matrix . Set .
for to
  if , set
  else, set .
Increment .
Solve the optimization problem (1) for the eigenvalues using an optimization algorithm (e.g., interior point method).
Evaluate at the solution of the optimization problem (1).
Return the stabilized ROM system, given by .
ROM stabilization via optimization-based
eigenvalue reassignment

## Slide 100
Algorithm
Diagonalize the ROM matrix : .
Initialize a diagonal matrix . Set .
for to
  if , set
  else, set .
Increment .
Solve the optimization problem (1) for the eigenvalues using an optimization algorithm (e.g., interior point method).
Evaluate at the solution of the optimization problem (1).
Return the stabilized ROM system, given by .
Solution to optimization problem (1) may not be unique.
Can solve (1) for real or complex-conjugate pair eigenvalues:
  s.t. constraint .
  = , = where s.t. constraint .
ROM stabilization via optimization-based
eigenvalue reassignment

## Slide 101
Numerical results: electrostatically actuated beam benchmark
FOM = 1D model of electrostatically actuated beam.
Application of model: microelectromechanical systems (MEMS) devices such as electromechanical radio frequency (RF) filters.
1 input corresponding to periodic on/off switching, 1 output, initial condition .
Second order linear semi-discrete system of the form:
Matrices , , , , specifying the problem downloaded from the Oberwolfach ROM repository*.
2nd order linear system re-written as 1st order LTI system for purpose of analysis/model reduction.
FOM is stable.
* Oberwolfach ROM benchmark repository: http://simulation.uni-freiburg.de/downloads/benchmark.

## Slide 102
POD/Galerkin ROM constructed from snapshots up to time .
POD/Galerkin ROM has 4 unstable eigenvalues (all real).
  Two options for ROM stabilization optimization problem:
    Option 1: Solve for s.t. the constraint .
    Option 2: Solve for , , , s.t. the constraint
Initial guess for fmincon interior point method: .
ROM | 
Unstabilized POD | 
Optimization Stabilized POD (Real Poles) | 0.0194
Optimization Stabilized POD (Complex-Conjugate Poles) | 0.0205
Balanced Truncation | 
ROM | 
Unstabilized POD | 
Optimization Stabilized POD (Real Poles) | 0.0194
Optimization Stabilized POD (Complex-Conjugate Poles) | 0.0205
Balanced Truncation | 
Numerical results: electrostatically actuated
beam benchmark

## Slide 103
Consistency?
One can show that from the algorithm on the previous slide is given by:
for a specific and (IKT et al. 2014).

## Slide 104
Consistency?
One can show that from the algorithm on the previous slide is given by:
for a specific and (IKT et al. 2014).
Modifying system as can be viewed as adding a linear “controller” to the system:
where .

## Slide 105
Consistency?
One can show that from the algorithm on the previous slide is given by:
for a specific and (IKT et al. 2014).
Modifying system as can be viewed as adding a linear “controller” to the system:
where .
Deficiencies of approach:
  ROM is inconsistent with FOM.
  Efficient extensions to nonlinear case are unclear.

## Slide 106
Consistency?
One can show that from the algorithm on the previous slide is given by:
for a specific and (IKT et al. 2014).
Modifying system as can be viewed as adding a linear “controller” to the system:
where .
Deficiencies of approach:
  ROM is inconsistent with FOM.
  Efficient extensions to nonlinear case are unclear.
Next section of talk (basis rotation): method for modifying a posteriori an unstable ROM that maintains consistency (and is applicable to nonlinear problems).

## Slide 107
Outline
Motivation.
Projection-based model order reduction.
3. Targeted application: compressible cavity flow.
4. Approaches for building a priori stable ROMs.
  (a) Energy-stable linearized compressible flow ROMs.
  (b) Energy-stable nonlinear compressible flow ROMs.
5. Approaches for stabilizing a posteriori unstable ROMs.
  (a) Eigenvalue reassignment (Linear Time-Invariant systems).
  (b) Basis rotation (nonlinear compressible flow).
Summary/perspectives.
7. Ongoing/future work.
with: Maciej Balajewicz (UIUC),
Earl Dowell (Duke)
 | Continuous Projection | Discrete Projection
Change projection (a priori) | Energy inner products (Rowley et al., Serre et al., IKT et al.) | Energy inner products (Rowley, et al.), Petrov-Galerkin Projection (Carlberg et al.)
Change ROM equations (a posteriori) | Linear/nonlinear turbulence modeling (Iliescu, Borggaard, Xie, Wang, …) | Eigenvalue reassignment (IKT et al.)
Change ROM basis (a posteriori) | Basis rotation (Balajewicz, IKT, et al.) | Optimization-based right basis modificatiOon (Amsallem)

## Slide 108
Extreme model reduction
Most realistic applications (e.g., high Re compressible cavity): basis that captures 99% snapshot energy is required to accurately reproduce snapshots.
  leads to >except for toy problems and/or low-fidelity models.
We are looking for an approach that enables extreme model reduction:
ROM basis size is or .
Higher order modes are in general unreliable for prediction, so including them in the basis is unlikely to improve the predictive capabilities of a ROM.
Figure (right) shows projection error for POD basis constructed using 800 snapshots for cavity problem.
Dashed line = end of snapshot collection period.

## Slide 109
Mode truncation instability
Projection-based MOR necessitates truncation.

## Slide 110
Mode truncation instability
POD is, by definition and design, biased towards the large, energy producing scales of the flow (i.e., modes with large POD eigenvalues).
Projection-based MOR necessitates truncation.

## Slide 111
Mode truncation instability
POD is, by definition and design, biased towards the large, energy producing scales of the flow (i.e., modes with large POD eigenvalues).
Truncated/unresolved modes are negligible from a data compression point of view (i.e., small POD eigenvalues) but are crucial for the dynamical equations.
Projection-based MOR necessitates truncation.

## Slide 112
Mode truncation instability
POD is, by definition and design, biased towards the large, energy producing scales of the flow (i.e., modes with large POD eigenvalues).
Truncated/unresolved modes are negligible from a data compression point of view (i.e., small POD eigenvalues) but are crucial for the dynamical equations.
For fluid flow applications, higher-order modes are associated with energy dissipation
Projection-based MOR necessitates truncation.

## Slide 113
Mode truncation instability
POD is, by definition and design, biased towards the large, energy producing scales of the flow (i.e., modes with large POD eigenvalues).
Truncated/unresolved modes are negligible from a data compression point of view (i.e., small POD eigenvalues) but are crucial for the dynamical equations.
For fluid flow applications, higher-order modes are associated with energy dissipation
low-dimensional ROMs can be inaccurate and unstable.
Projection-based MOR necessitates truncation.

## Slide 114
Mode truncation instability
POD is, by definition and design, biased towards the large, energy producing scales of the flow (i.e., modes with large POD eigenvalues).
Truncated/unresolved modes are negligible from a data compression point of view (i.e., small POD eigenvalues) but are crucial for the dynamical equations.
For fluid flow applications, higher-order modes are associated with energy dissipation
For a low-dimensional ROM to be stable and accurate, the truncated/unresolved subspace must be accounted for.
Projection-based MOR necessitates truncation.
low-dimensional ROMs can be inaccurate and unstable.

## Slide 115
Mode truncation instability
POD is, by definition and design, biased towards the large, energy producing scales of the flow (i.e., modes with large POD eigenvalues).
Truncated/unresolved modes are negligible from a data compression point of view (i.e., small POD eigenvalues) but are crucial for the dynamical equations.
For fluid flow applications, higher-order modes are associated with energy dissipation
For a low-dimensional ROM to be stable and accurate, the truncated/unresolved subspace must be accounted for.
Turbulence Modeling
(traditional approach)
Subspace Rotation
(our approach)
Projection-based MOR necessitates truncation.
low-dimensional ROMs can be inaccurate and unstable.

## Slide 116
Governing equations and ROM
3D compressible Navier-Stokes equations in primitive specific volume form:
[PDEs]
(2)
Notes: Add equation numbers (1) and (2)!

## Slide 117
Governing equations and ROM
3D compressible Navier-Stokes equations in primitive specific volume form:
(2)
POD discretization Galerkin projection applied to (2) yields a system of coupled quadratic ODEs:
(3)
[ROM]
[PDEs]
where and for all
Notes: Add equation numbers (1) and (2)!

## Slide 118
Dissipative dynamics of truncated higher-order modes are modeled using an additional linear term:
Traditional linear eddy-viscosity approach
to account for modal truncation

## Slide 119
Dissipative dynamics of truncated higher-order modes are modeled using an additional linear term:
Traditional linear eddy-viscosity approach
to account for modal truncation

## Slide 120
Dissipative dynamics of truncated higher-order modes are modeled using an additional linear term:
is designed to decrease magnitude of positive eigenvalues and increase magnitude of negative eigenvalues of (for stability).
Traditional linear eddy-viscosity approach
to account for modal truncation

## Slide 121
Dissipative dynamics of truncated higher-order modes are modeled using an additional linear term:
is designed to decrease magnitude of positive eigenvalues and increase magnitude of negative eigenvalues of (for stability).
Disadvantages of this approach:
  Additional term destroys consistency between ROM and Navier-Stokes equations.
  Calibration is necessary to derive optimal and optimal value is flow dependent.
  Inherently a linear model cannot be expected to perform well for all classes of problems (e.g., nonlinear).
Traditional linear eddy-viscosity approach
to account for modal truncation

## Slide 122
Proposed new approach for modal truncation: basis rotation
Instead of modeling truncation via additional linear term, model the truncation by “rotating” the projection subspace into a more dissipative regime

## Slide 123
Proposed new approach for modal truncation: basis rotation
Illustrative example
Standard approach: retain only the most energetic POD modes, i.e., ,
Proposed approach: choose some higher order basis modes to increase dissipation, i.e.,
Instead of modeling truncation via additional linear term, model the truncation by “rotating” the projection subspace into a more dissipative regime

## Slide 124
Proposed new approach for modal truncation: basis rotation
(4)
More generally: approximate the solution using a linear superposition of (with ) most energetic modes:
,
where is an orthonormal () “rotation” matrix.
Illustrative example
Standard approach: retain only the most energetic POD modes, i.e., ,
Proposed approach: choose some higher order basis modes to increase dissipation, i.e.,
Instead of modeling truncation via additional linear term, model the truncation by “rotating” the projection subspace into a more dissipative regime

## Slide 125
Goals of proposed new approach to account for modal truncation
Find such that:
  New modes remain good approximations of the flow
  minimize the “rotation” angle, i.e., minimize
  New modes produce stable and accurate ROMs.
    ensure appropriate balance between energy production and energy dissipation.

## Slide 126
Goals of proposed new approach to account for modal truncation
Find such that:
  New modes remain good approximations of the flow
  minimize the “rotation” angle, i.e., minimize
  New modes produce stable and accurate ROMs.
    ensure appropriate balance between energy production and energy dissipation.

## Slide 127
Goals of proposed new approach to account for modal truncation
Find such that:
  New modes remain good approximations of the flow
  minimize the “rotation” angle, i.e., minimize
  New modes produce stable and accurate ROMs.
    ensure appropriate balance between energy production and energy dissipation.

## Slide 128
Goals of proposed new approach to account for modal truncation
Find such that:
  New modes remain good approximations of the flow
  minimize the “rotation” angle, i.e., minimize
  New modes produce stable and accurate ROMs.
    ensure appropriate balance between energy production and energy dissipation.
Once is found, the result is a system of the form (3) with:
,

## Slide 129
Minimal subspace rotation
Trace minimization problem on the Stiefel manifold:
is the Stiefel manifold.
  Constraint is traditional linear eddy-viscosity closure model ansatz involves overall balance between linear energy production and dissipation / vanishing of averaged total power ( energy transfer).
    : proxy for the balance between linear energy production and energy dissipation (calculated iteratively using modal energy).
Equation (5) is solved efficiently offline using the method of Lagrange multipliers (Manopt MATLAB toolbox).
See (Balajewicz, IKT, Dowell, 2016) and Appendix slide for Algorithm.
(5)

## Slide 130
Basis rotation: remarks
Proposed approach may be interpreted as a consistent formulation of the eddy-viscosity turbulence modeling approach.

## Slide 131
Basis rotation: remarks
Advantages of proposed approach:
  Retains consistency between ROM and Navier-Stokes equations no additional turbulence terms required.
Proposed approach may be interpreted as a consistent formulation of the eddy-viscosity turbulence modeling approach.

## Slide 132
Basis rotation: remarks
Advantages of proposed approach:
  Retains consistency between ROM and Navier-Stokes equations no additional turbulence terms required.
  Inherently a nonlinear model should be expected to outperform linear models.
Proposed approach may be interpreted as a consistent formulation of the eddy-viscosity turbulence modeling approach.

## Slide 133
Basis rotation: remarks
Advantages of proposed approach:
  Retains consistency between ROM and Navier-Stokes equations no additional turbulence terms required.
  Inherently a nonlinear model should be expected to outperform linear models.
  Works with any basis and Petrov-Galerkin projection.
Proposed approach may be interpreted as a consistent formulation of the eddy-viscosity turbulence modeling approach.

## Slide 134
Basis rotation: remarks
Advantages of proposed approach:
  Retains consistency between ROM and Navier-Stokes equations no additional turbulence terms required.
  Inherently a nonlinear model should be expected to outperform linear models.
  Works with any basis and Petrov-Galerkin projection.
Disadvantages of proposed approach:
  Off-line calibration of free parameter is required.
Proposed approach may be interpreted as a consistent formulation of the eddy-viscosity turbulence modeling approach.

## Slide 135
Basis rotation: remarks
Advantages of proposed approach:
  Retains consistency between ROM and Navier-Stokes equations no additional turbulence terms required.
  Inherently a nonlinear model should be expected to outperform linear models.
  Works with any basis and Petrov-Galerkin projection.
Disadvantages of proposed approach:
  Off-line calibration of free parameter is required.
  Stability cannot be proven like for incompressible case.
Proposed approach may be interpreted as a consistent formulation of the eddy-viscosity turbulence modeling approach.

## Slide 136
Numerical results: low Re number cavity
Flow over square cavity at Mach 0.6, Re = 1453.9, Pr = 0.72 ROM (91% snapshot energy).
Above: domain and mesh for viscous channel driven cavity problem.

## Slide 137
Figure (a) shows evolution of modal energy. Standard ROM is unstable.
Figure (b) shows phase plot of first and second temporal basis and Stabilized ROM computes stable limit cycle; standard ROM computes unstable spiral.
Figure (c) is an illustration of the stabilizing rotation matrix. Rotation is small:
-- standard ROM (M=4)
stabilized ROM (M=P=4)
DNS
Numerical results: low Re number cavity

## Slide 138
Pressure power spectral density (PSD) at location
-- standard ROM (M=4)
stabilized ROM (M=P=4)
DNS
Numerical results: low Re number cavity

## Slide 139
Numerical results: moderate Re number cavity
Above: domain and mesh for viscous channel driven cavity problem.
Flow over square cavity at Mach 0.6, Re = 5452.1, Pr = 0.72 ROM (71.8% snapshot energy).

## Slide 140
Figure (a) shows evolution of modal energy. Stabilized ROM energy closer to FOM.
Figure (b) illustrates stabilizing rotation matrix. Rotation is small:
-- standard ROM (M=20)
stabilized ROM (M=P=20)
DNS
Numerical results: moderate Re number cavity

## Slide 141
Power and phase lag at fundamental frequency, and first two super harmonics are predicted accurately using the fine-tuned ROM ( stabilized ROM, DNS)
Figures show pressure cross PSD of of and where Left: power; right: phase lag.
stabilized ROM (M=P=20)
DNS
Numerical results: moderate Re number cavity

## Slide 142
Future work (basis rotation)
Application to higher Reynolds number problems.
Extension of the proposed approach to problems with generic nonlinearities, where the ROM involves some form of hyper-reduction (e.g., DEIM, gappy POD).
Extension of the method to minimal-residual-based nonlinear ROMs.
Extension of the method to predictive applications, e.g., problems with varying Reynolds number and/or Mach number.
Selecting different goal-oriented objectives and constraints in our optimization problem:
e.g.,
  Maximize parametric robustness:
        .
  ODE constraints:

## Slide 143
Outline
Motivation.
Projection-based model order reduction.
3. Targeted application: compressible cavity flow.
4. Approaches for building a priori stable ROMs.
  (a) Energy-stable linearized compressible flow ROMs.
  (b) Energy-stable nonlinear compressible flow ROMs.
5. Approaches for stabilizing a posteriori unstable ROMs.
  (a) Eigenvalue reassignment (Linear Time-Invariant systems).
  (b) Basis rotation (nonlinear compressible flow).
Summary/perspectives.
7. Ongoing/future work.

## Slide 144
Summary/perspectives
Energy inner product + continuous projection
  Pros: consistent, inner product known analytically in closed form.
  Cons: inner product is problem specific, expensive for nonlinear problems, BC implementation important for stability.
Eigenvalue reassignment
  Pros: black-box, easy-to-solve offline optimization problem
  Cons: inconsistent, work required to extend to nonlinear and predictive problems.
Basis rotation
  Pros: black-box, consistent, works with any basis, applicable to nonlinear flow problems.
  Cons: work required to extend to generic nonlinear PDEs.
 | Continuous Projection | Discrete Projection
Change projection (a priori) | Energy inner products (Rowley et al., Serre et al., IKT et al.) | Energy inner products (Rowley, et al.), Petrov-Galerkin Projection (Carlberg et al.)
Change ROM equations (a posteriori) | Linear/nonlinear turbulence modeling (Iliescu, Borggaard, Xie, Wang, …) | Eigenvalue reassignment (IKT et al.)
Change ROM basis (a posteriori) | Basis rotation (Balajewicz, IKT, et al.) | Optimization-based right basis modification (Amsallem et al.)

## Slide 145
Outline
Motivation.
Projection-based model order reduction.
3. Targeted application: compressible cavity flow.
4. Approaches for building a priori stable ROMs.
  (a) Energy-stable linearized compressible flow ROMs.
  (b) Energy-stable nonlinear compressible flow ROMs.
5. Approaches for stabilizing a posteriori unstable ROMs.
  (a) Eigenvalue reassignment (Linear Time-Invariant systems).
  (b) Basis rotation (nonlinear compressible flow).
Summary/perspectives.
7. Ongoing/future work.

## Slide 146
Ongoing/future work
Extension of basis rotation approach to problems with generic nonlinearities and LSPG ROMs [with Maciej Balajewicz (UIUC)].

## Slide 147
Ongoing/future work
Extension of basis rotation approach to problems with generic nonlinearities and LSPG ROMs [with Maciej Balajewicz (UIUC)].
Implementation of Least-Squares Petrov-Galerkin (LSPG) ROMs within SPARC finite volume flow solver and Albany* open-source multi-physics code [with Jeff Fike (SNL), Kevin Carlberg (SNL)].
* https://github.com/gahansen/Albany.

## Slide 148
Ongoing/future work
Extension of basis rotation approach to problems with generic nonlinearities and LSPG ROMs [with Maciej Balajewicz (UIUC)].
Implementation of Least-Squares Petrov-Galerkin (LSPG) ROMs within SPARC finite volume flow solver and Albany* open-source multi-physics code [with Jeff Fike (SNL), Kevin Carlberg (SNL)].
Introduction of energy-based constraints (e.g., Clausius-Duhem inequality) into ROMs [with Kevin Carlberg (SNL), Danielle Maddix (Stanford), Margot Gerritsen (Stanford)].
* https://github.com/gahansen/Albany.

## Slide 149
Ongoing/future work
Extension of basis rotation approach to problems with generic nonlinearities and LSPG ROMs [with Maciej Balajewicz (UIUC)].
Implementation of Least-Squares Petrov-Galerkin (LSPG) ROMs within SPARC finite volume flow solver and Albany* open-source multi-physics code [with Jeff Fike (SNL), Kevin Carlberg (SNL)].
Introduction of energy-based constraints (e.g., Clausius-Duhem inequality) into ROMs [with Kevin Carlberg (SNL), Danielle Maddix (Stanford), Margot Gerritsen (Stanford)].
Extension of filtering and LES-ROMs to compressible flow problems [with Traian Iliescu (VT), Xuping Xie (VT), Kevin Carlberg (SNL)].
* https://github.com/gahansen/Albany.

## Slide 150
Ongoing/future work
Extension of basis rotation approach to problems with generic nonlinearities and LSPG ROMs [with Maciej Balajewicz (UIUC)].
Implementation of Least-Squares Petrov-Galerkin (LSPG) ROMs within SPARC finite volume flow solver and Albany* open-source multi-physics code [with Jeff Fike (SNL), Kevin Carlberg (SNL)].
Introduction of energy-based constraints (e.g., Clausius-Duhem inequality) into ROMs [with Kevin Carlberg (SNL), Danielle Maddix (Stanford), Margot Gerritsen (Stanford)].
Extension of filtering and LES-ROMs to compressible flow problems [with Traian Iliescu (VT), Xuping Xie (VT), Kevin Carlberg (SNL)].
Improvement of previous techniques for time-predictive problems.
* https://github.com/gahansen/Albany.

## Slide 151
Ongoing/future work
Extension of basis rotation approach to problems with generic nonlinearities and LSPG ROMs [with Maciej Balajewicz (UIUC)].
Implementation of Least-Squares Petrov-Galerkin (LSPG) ROMs within SPARC finite volume flow solver and Albany* open-source multi-physics code [with Jeff Fike (SNL), Kevin Carlberg (SNL)].
Introduction of energy-based constraints (e.g., Clausius-Duhem inequality) into ROMs [with Kevin Carlberg (SNL), Danielle Maddix (Stanford), Margot Gerritsen (Stanford)].
Extension of filtering and LES-ROMs to compressible flow problems [with Traian Iliescu (VT), Xuping Xie (VT), Kevin Carlberg (SNL)].
Improvement of previous techniques for time-predictive problems.
Hybrid ROM-FOMs via domain-decomposition-based coupling methods.
  A. Mota, I. Tezaur, C. Alleman. "The Schwarz alternating method in solid mechanics", Comput. Meth. Appl. Mech. Engng. 319 (2017), 19-51.
* https://github.com/gahansen/Albany.

## Slide 152
Ongoing/future work
Extension of basis rotation approach to problems with generic nonlinearities and LSPG ROMs [with Maciej Balajewicz (UIUC)].
Implementation of Least-Squares Petrov-Galerkin (LSPG) ROMs within SPARC finite volume flow solver and Albany* open-source multi-physics code [with Jeff Fike (SNL), Kevin Carlberg (SNL)].
Introduction of energy-based constraints (e.g., Clausius-Duhem inequality) into ROMs [with Kevin Carlberg (SNL), Danielle Maddix (Stanford), Margot Gerritsen (Stanford)].
Extension of filtering and LES-ROMs to compressible flow problems [with Traian Iliescu (VT), Xuping Xie (VT), Kevin Carlberg (SNL)].
Improvement of previous techniques for time-predictive problems.
Hybrid ROM-FOMs via domain-decomposition-based coupling methods.
  A. Mota, I. Tezaur, C. Alleman. "The Schwarz alternating method in solid mechanics", Comput. Meth. Appl. Mech. Engng. 319 (2017), 19-51.
More info: www.sandia.gov/~ikalash
Thank you!
* https://github.com/gahansen/Albany.

## Slide 153
Careers at Sandia
Students: please consider Sandia and other national labs as a potential employer for summer internships and when you graduate!
Sandia is a great place to work!
  Lots of interesting problems that require fundamental research in mathematics/computational science and impact mission-critical applications.
  Great work/life balance!
Sandia has openings for:
  Summer internships.
  Post docs Kevin Carlberg and I are seeking a post doc* now in ROM!
  Staff.
Sandia has two locations:
  Albuquerque, NM.
  Livermore, CA.
Please see: www.sandia.gov/careers and/or email me: ikalash@sandia.gov about opportunities.
* For this particular position, U.S. citizenship is required.

## Slide 154
References
D. Amsallem, C. Farhat. Stabilization of projection-based reduced order models. IJNME (2011).
M. Balajewicz, E. Dowell. Stabilization of projection-based reduced order models of the Navier-Stokes equation. Nonlinear Dynamics 70 (2), 1619-1632 (2012).
M. Balajewicz, I. Tezaur, E. Dowell. Minimal subspace rotation on the Stiefel manifold for stabilization and enhancement of projection-based reduced order models for the compressible Navier-Stokes equations. JCP 321 224-241 (2016).
M. Barone, I. Kalashnikova, D. Segalman, H. Thornquist. Stable Galerkin reduced order models for linearized compressible flow. JCP 228 (6) 1932-1946 (2009).
K. Carlberg, C. Farhat, J. Cortial, D. Amsallem. The GNAT method for nonlinear modele reduction: effective implementation and application to computational fluid dynamics and turbulent flows. JCP 242 623-647 (2013).
I. Kalashnikova, M.F. Barone. On the Stability and Convergence of a Galerkin Reduced Order Model (ROM) of Compressible Flow with Solid Wall and Far-Field Boundary Treatment. IJNME 83 1345-1375 (2010).
I. Kalashnikova, B.G. van Bloemen Waanders, S. Arunajatesan, M.F. Barone. Stabilization of Projection-Based Reduced Order Models for Linear Time-Invariant Systems via Optimization-Based Eigenvalue Reassignment. Comput. Meth. Appl. Mech. Engng. 272 (2014) 251-270.
I. Kalashnikova, S. Arunajatesan, M. Barone, B. van Bloemen Waanders, J. Fike. Reduced order modeling for prediction and control of large-scale systems. Sandia Tech Report (2014).
C. Rowley, T. Colonius, R. Murray. Model reduction for compressible flows using POD and Galerkin projection. Physica D 189 (1) 115-129 (2004).
G. Serre, P. Lafon, X. Gloerfelt, C. Bailly. Reliable reduced order models for time-dependent linearized Euler equations. JCP 231 (15) 5176-5194 (2012).

## Slide 155
Appendix: Connection to Lyapunov stability
Lyapunov stability: if there exists a Lyapunov function such that
  (positive definite), and
in , then is locally stable in the sense of Lyapunov.
Energy stability: Let denote the system energy. If
||2
is energy-stable.
Remark: the system energy satisfies the definition of a Lyapunov function!

## Slide 156
Appendix: Symmetry (continuous) vs. Lyapunov
(discrete) inner product
Symmetry Inner Product
(Continuous)
Lyapunov Inner Product
(Discrete)
For linear systems:
Defined for unstable systems, but stability of ROM not guaranteed.
Induced by Lyapunov function for system.
Equation-specific ( embedded algorithm).
Known analytically in closed form.
For linear systems:
Undefined for unstable systems.
Induced by Lyapunov function for system.
Black-box.
Computed numerically by solving Lyapunov equation (ops).
Intractable for large problems!

## Slide 157
Appendix: Accounting for modal truncation
Stabilization algorithm: returns stabilizing rotation matrix .
SAND2016-6345 C

## Slide 158
-velocity at time of final snapshot for low Reynolds number cavity. Left: FOM, middle: standard ROM, right: stabilized ROM.
Standard ROM ()
Stabilized ROM ()
DNS
Appendix: Numerical results: low Re number cavity

## Slide 159
Standard ROM ()
Stabilized ROM (20)
DNS
Appendix: Numerical results: moderate Re number cavity
-velocity at time of final snapshot for low Reynolds number cavity. Left: FOM, middle: standard ROM, right: stabilized ROM.

## Slide 160
Appendix: CPU times
Tables gives CPU times (CPU-hours) for offline and online computations
Procedure | Low Re Cavity | Moderate Re Cavity
FOM # of DOF | 288,250 | 243,750
Time-integration of FOM | 72 hrs | 179 hrs
Basis construction (size ROM) | 0.88 hrs | 3.44 hrs
Galerkin projection (size ROM) | 5.44 hrs | 14.8 hrs
Stabilization | 14 sec | 170 sec
ROM # of DOF | 4 | 20
Time-integration of ROM | 0.16 sec | 0.83 sec
Online computational speed-up | 1.6e6 | 7.8e5
Procedure | Low Re Cavity | Moderate Re Cavity
FOM # of DOF | 288,250 | 243,750
Time-integration of FOM | 72 hrs | 179 hrs
 | 0.88 hrs | 3.44 hrs
 | 5.44 hrs | 14.8 hrs
Stabilization | 14 sec | 170 sec
ROM # of DOF | 4 | 20
Time-integration of ROM | 0.16 sec | 0.83 sec
Online computational speed-up | 1.6e6 | 7.8e5
online
offline
Stabilization is fast ((sec) or (min)).
Significant online computational speed-up!