## Slide 1: Development of a strongly-coupled thermo-mechanical model of permafrost for the simulation of Arctic coastal erosion d Alejandro Mota, Jenn Frederick, Charles Choens, Diana Bull, Irina Tezaur g Sandia National Laboratories, U.S.A.
SAND2020-5151C
European Seminar on COmputing (ESCO) 2020
Pilsen, CZ Online Meeting, June 8-12, 2020

## Slide 2: Motivation
2
Wainwright
Barrow
Bullen Point
Oliktok
Barter Island
Active DOD sites
~200 m (~2 football fields in length) in a decade!
Erosion is threatening:
  Coastal communities
  Coastal infrastructure
  Global carbon balance
Since 1979 sea-ice has lost 51% in area and 75% in volume
  Increasing ice-free season
  Increasing wave energy and storm surge
Increasing sea water temperatures
Warming permafrost
  Coastal erosion rates in Alaskan Arctic among the highest in the world and accelerating.
The Arctic is warming at 2-3 times the rate of the rest of the U.S. resulting in accelerated rates of coastal erosion!
Gibbs & Richmond, 2015.

## Slide 3: Permafrost erosion
What is permafrost?
Ground that remains frozen for 2 or more consecutive years.
Comprised of soil, rock, silt, clay and sand, held together by ice.
24% of ice-free land area in Northern Hemisphere and 85% of Alaska, Greenland, Canada and Siberia sits on top of permafrost.
Unique coastal permafrost erosion process in Arctic:
Predominant geomorphology: ice-wedge polygons
  Ice acts to bind unconsolidated soils in permafrost forming ice wedges.
  Ice wedges grow/expand up to ms wide and 10s meters deep.
Melting ice causes permafrost failure.
  Storm surges accelerate ice melt by delivering heat to ice/permafrost*.
Left: schematic illustrating formation of ice wedges and ice-wedge polygon landscapes. Right: map of permafrost distribution in Arctic
Martin et al. 2009.
Brown et al. 1998.
* Thermo-abrasion: permafrost material is warmed by ocean and removed by mechanical action of waves.

## Slide 4: Permafrost failure mechanisms
4
Retrogressive thaw slumping: a slope failure characterized by thaw of exposed ground ice and slumping of thawed soil, typically caused by thermo-denundation*.
Active layer detachment: failures are translational landslides that occur in summer in thawing soil overlying permafrost, typically caused by thermo-denundation*.
Block failure: a niche (recess at bluff base) progresses landward until the overhanging material fails in a shearing or toppling mode known as block failure.
  Fallen blocks can disintegrate in the near-shore environment within 1-2 weeks!
Retrogressive thaw slumping
Active layer detachment
Block failure
Lantuit et al. 2008
Lantuit et al. 2008
Ravens et al. 2012
* Subaerial erosion triggered by thawing of permafrost bluffs that proceeds under the influence of gravity.

## Slide 5: Permafrost failure mechanisms
5
Retrogressive thaw slumping: a slope failure characterized by thaw of exposed ground ice and slumping of thawed soil, typically caused by thermo-denundation*.
Active layer detachment: failures are translational landslides that occur in summer in thawing soil overlying permafrost, typically caused by thermo-denundation*.
Block failure: a niche (recess at bluff base) progresses landward until the overhanging material fails in a shearing or toppling mode known as block failure.
  Fallen blocks can disintegrate in the near-shore environment within 1-2 weeks!
Retrogressive thaw slumping
Active layer detachment
Block failure
Lantuit et al. 2008
Lantuit et al. 2008
Ravens et al. 2012
* Subaerial erosion triggered by thawing of permafrost bluffs that proceeds under the influence of gravity.
Dominant failure mechanism in northern Alaska

## Slide 6: Example of bluff erosion during 2019 UAV surveys*
6
  Fallen blocks can disintegrate in near-shore environment within 1-2 weeks!
*Images courtesy of Ben Jones, UAF

## Slide 7: State-of-the-art in permafrost modeling
Existing models* are primitive: trend projection, empirical relationships, 1D steady state heat flow,…
  Primarily thermal models (no mechanics/deformation)
  Most models assume particular type of erosion (e.g. block failure)
Efforts have been put towards integrating permafrost models into earth system models (ESMs): CLM, VAMPERS, CryoGrid3, ...
Modeling typically estimates BCs and does not account for geomorphologies or geophysics.
Comprehensive understanding of erosion dynamics in the Arctic has not yet emerged.
When this project began in 2017, tools to accurately predict Arctic coastal erosion did not exist!
To obtain an accurate, predictive Arctic coastal erosion model, a coupling of the influences of evolving wave dynamics, thermodynamics and mechanics must be developed.
* See (Frederick et al. 2016), Chapter 5, for extensive overview.
Koven et al. 2013

## Slide 8
Multi-physics finite element model of an archetype of the coastline coupled with high-fidelity model of storm intensities
  Input variables define geomorphology & geophysics
  Plastic deformation model of material (J2 class)
  Geomechanical testing to determine coupled thermal-mechanical strength characteristics
  Time-varying ocean BCs (water level, temp, salinity)
  Eroded sediment and biogeochemical flux tracking
Goal of the Arctic Coastal Erosion (ACE) project is to deliver a field-validated predictive model of thermo-abrasive erosion for the permafrost Arctic coastline
A “catalog” of micro-scale models that represent the statistical distributions of input variables along a ~10km stretch of coastline.
  Probability distribution functions of geomorphology and geophysics used to weight erosion output
    Will validate approach with decade long annual measurements at Drew Point.
  Evaluating ocean “exposure metrics” to represent time-varying ocean
2018-2019
2019-2020
Micro-scale Model
Meso-scale Model
10’s of meters & storm duration
30m
5m
Ice wedge
Permafrost
30m
ocean water
0.0 0.5 1.0 1.5 2.0 2.5 3.0
Significant Wave Height (m)
July 23rd 2017. 6am.
WW3 polar stereographic model initially developed by NRL (Erick Rogers) and NOAA (Arun Chawla)
oceanographic model
field measurements
thermo-chemical-mechanical terrestrial model
10’s of km’s & seasonal duration
Proposed solution
This talk

## Slide 9: ACE Model Component Coupling
(Drew Point, Alaska)
ACE project has many pieces!
Terrestrial model: thermo-mechanical coupled FEM model that can simulate transient niche development.
Oceanographic model: WW3 + SWAN + Delft3D wave models for providing oceanic BCs (ocean temp/height) to terrestrial model.
Geomechanical testing: for characterization of permafrost parameters in terrestrial model.
Field campaign: offshore oceanographic measurements, bathymetric survey, niche measurements, etc.

## Slide 10: ACE Model Component Coupling
ACE project has many pieces!
Terrestrial model: thermo-mechanical coupled FEM model that can simulate transient niche development.
Oceanographic model: WW3 + SWAN + Delft3D wave models for providing oceanic BCs (ocean temp/height) to terrestrial model.
Geomechanical testing: for characterization of permafrost parameters in terrestrial model.
Field campaign: offshore oceanographic measurements, bathymetric survey, niche measurements, etc.
(Drew Point, Alaska)
This talk

## Slide 11: Anatomy of a canonical computational domain
Bluff face (exposed to ocean)
Permafrost
Ice
Cryopeg*
* Layer of unfrozen ground that is perennially cryotic (forming part of the permafrost) in which freezing is prevented.
30 m
30 m
5 m
ocean water

## Slide 12: Mechanical model
Finite deformation variational formulation for solid mechanics problem obtained by minimizing the energy functional :
Helmholtz free-energy density
: material variables
: deformation gradient ()
: density
: body force
: prescribed traction
J2 plasticity extended to large-deformation regime constitutive model for ice and permafrost
  Incorporates all mechanisms that lead to deformation, plastic flow and creep of polycrystalline materials like ice; minimal calibration parameters; simplest material model w/ plastic behavior.
Yield stress:
: ice saturation ()
: yield stress of soil/ice
soil/ice volume fraction
Used in erosion failure criteria
Symmetry boundary conditions on lateral sides
Computes displacements and new computational geometry (following erosion)
Symmetry BCs
Symmetry BCs

## Slide 13: Erosion failure criteria
Erosion criterion: when material exposed to water reaches a critical exposure time.
Stress criterion: when material reaches a critical value of the yield stress.
Once failure criterion is reached, “failed” elements are removed from mesh.
Kinematic criterion: when material has tilted excessively, it is assumed to have fallen as part of block erosion.

## Slide 14: Erosion failure criteria
Bluff face
Once failure criterion is reached, “failed” elements are removed from mesh.
Kinematic criterion: when material has tilted excessively, it is assumed to have fallen as part of block erosion.
Erosion criterion: when material exposed to water reaches a critical exposure time.
Stress criterion: when material reaches a critical value of the yield stress.

## Slide 15: Erosion failure criteria
Bluff face
Once failure criterion is reached, “failed” elements are removed from mesh.
Kinematic criterion: when material has tilted excessively, it is assumed to have fallen as part of block erosion.
Erosion criterion: when material exposed to water reaches a critical exposure time.
Stress criterion: when material reaches a critical value of the yield stress.

## Slide 16: Erosion failure criteria
Bluff face
Once failure criterion is reached, “failed” elements are removed from mesh.
Kinematic criterion: when material has tilted excessively, it is assumed to have fallen as part of block erosion.
Erosion criterion: when material exposed to water reaches a critical exposure time.
Stress criterion: when material reaches a critical value of the yield stress.

## Slide 17: Erosion failure criteria
Bluff face
Niche
Once failure criterion is reached, “failed” elements are removed from mesh.
Kinematic criterion: when material has tilted excessively, it is assumed to have fallen as part of block erosion.
Erosion criterion: when material exposed to water reaches a critical exposure time.
Stress criterion: when material reaches a critical value of the yield stress.

## Slide 18: Thermal model
Transient heat conduction in a non-homogeneous porous media with water-ice phase change:
where incorporates phase changes through soil freezing curve, .
Computes temperature and ice saturation
Bluff face
Below
Above
Boundary conditions (from wave model/data)
  Local geothermal heat flux from below
  Mean annual air temp from above
  Air/ocean temp at bluff face
Temperature [C]
Ice Saturation
Permafrost control volume
Soil freezing curve only during phase change, which occurs in narrow temp zone (~-1C)
: density from mixture model
: specific heat from mixture model
: thermal diffusivity tensor
: ice density
: latent heat of water-ice phase change
: ice saturation ()
soil freezing curve (depends on salinity)

## Slide 19: Parameters & inputs
Parameters estimated from observational data at Drew Point, AK:
Skin temp w/ time, initial bluff temp (USGS weather station data)
Geothermal heat flux (borehole at Barrow, AK)
Polygon dimension, ice wedge thickness and depth, bluff height, living organic layer thickness (Aug. 2019 field campaign)
Parameters from wave model (WW3+SWAN+Delft3D):
Ocean temperature, salinity and sea-level w/ time (for thermal BCs)
Parameters estimated from lab experiments:
Elastic modulus, Poisson’s ratio, yield strength
Sand/silt/clay fractions with depth
Porosity with depth
Parameters from literature:
Ice/water/sediment densities, thermal conductivities, heat capacities
Freezing curve/width as function of sediment type
Bluff salinity with depth
Deep borehole
BC Data for Drew Point

## Slide 20: Coupled thermo-mechanical formulation
Potential key advantages:
Tightly coupled strength and thermo-chemical states
Failure modes develop from constitutive relationships in FEM model (no empirical relationships!)
3D unsteady heat flow can include chemistry
Thermal:
Inputs: geometry, sediment type, ice volume, water volume, pore size, salinity
Outputs: temperature field, ice saturation
Mechanical:
Inputs: ice saturation, strength relationship as function of thermal state, stress-strain relationships of permafrost and ice
Outputs: displacements, eroded geometry
Ice saturation
Eroded geometry
Unique characteristic of coupled model: coupling happens at the level of material model

## Slide 21
Finite element implementation within Albany
https://github.com/trilinos/trilinos
https://github.com/ SNLComputation/LCM
The thermo-mechanical Arctic Coastal Erosion (ACE) model is implemented within the LCM project in Sandia’s open-source parallel, C++, multi-physics, finite element code, Albany.
Component-based design for rapid development.
Contains a wide variety of constitutive models.
Extensive use of libraries from the open-source Trilinos project.
  Use of the Phalanx package to decompose complex problem into simpler problems with managed dependencies.
  Use of the Sacado package for automatic differentiation.
Coupled to the DOE’s Energy Exascale Earth System Model (E3SM) through Albany Land-Ice (ALI) component.
All software available on GitHub.

## Slide 22: Mechanics-only simulation*
* M. Thomas et al. Frontiers in Earth Science 8, April 2020.
From recently-published Frontiers in Earth Science special issue.

## Slide 23: Mechanics-only simulation*
3D elastic mechanics-only simulations assessed impact of bluff geometry and material variability on stress states leading up to bluff failure
  Only load is gravitational.
Simulations facilitated examination of stress patterns within bluff and identification of location and magnitude of max tensile stress ()
* M. Thomas et al. Frontiers in Earth Science 8, April 2020.

## Slide 24: Mechanics-only simulation*: main takeaways
Niche dimension affects location and magnitude of simulated max tensile stress () more than the bluff height, ice wedge polygon size, ice wedge geometry, bulk density and Poisson’s ratio
Taller and narrower erosional niches promote smaller failure masses compared to those with shorter and deeper niches
Inland extent of niche was advanced for 6 erosional niche heights from 0.1-3 m
Lower bound for tensile stress from lab measurements: 100 kPa
Orange/green shading highlights potential failure areas.
* M. Thomas et al. Frontiers in Earth Science 8, April 2020.
Notes: Question: are results in paper draft also mechanics-only? What is the difference??
Stars indicate value of 𝜎_(𝑇_max )
Yellow shading highlights potential failure areas.
High-intensity, short-duration storms may create tall/narrow niches, whereas low-intensity, long-duration storm energy may create short/deep niches.

## Slide 25: Mechanics-only simulation*: main takeaways
Taller and narrower erosional niches promote smaller failure masses compared to those with shorter and deeper niches
50x exaggeration
Distance from back (m)
0 2 4 6 8 10 12 14 16 18 20 24 26
(1,1) stress component (kPa)
100
As niche advances into the block, an overhanging section in the block acts as cantilever.
Highest tensile stresses develop on top surface where cantilever meets rest of block
* M. Thomas et al. Frontiers in Earth Science 8, April 2020.

## Slide 26: Mechanics-only simulation*: main takeaways
It has been observed that failure can occur along tension cracks in ice wedge polygon centers.
: fracture depth
Simulations suggest tension cracks can form within the range of niche depths/heights considered here.
Even relatively shallow vertical cracks can concentrate strain within ice-bonded permafrost bluffs.
* M. Thomas et al. Frontiers in Earth Science 8, April 2020.

## Slide 27: Thermo-mechanical coupling: cuboid problem
Cuboid is comprised of block of ice material, wedged between two blocks of permafrost material.
Cuboid subjected to simultaneous heating and stretching from the top
Cuboid is affixed to the bottom and with symmetry boundary conditions on the sides.
Temperature is initialized to 265K.
permafrost
ice
permafrost
3.0 m
1.0 m
1.0 m

## Slide 28: Thermo-mechanical coupling: cuboid problem
permafrost
ice
permafrost
3.0 m
1.0 m
1.0 m
Temp = 280 K
Disp = 0.2 m
Temp
Ice Saturation
Water Saturation
Temperature
Plots (right) show quantities along vertical line as a function of in the ice block

## Slide 29: Thermo-mechanical coupling: cuboid problem
permafrost
ice
permafrost
Temp = 280 K
Disp = 0.2 m
Temp
3.2 m
<1.0 m
<1.0 m
Ice Saturation
Water Saturation
Temperature
226 days
Plots (right) show quantities along vertical line as a function of in the ice block

## Slide 30: Thermo-mechanical coupling: cuboid problem
permafrost
ice
permafrost
3.0 m
1.0 m
1.0 m
Temp
As cuboid is heated and stretched at top, heat propagates down, melting ice and causing failure.

## Slide 31: Thermo-mechanical coupling: 2.5D slice
3 m
2 m
bluff face
2D bluff cross section
water level
0 – 1.2 m
Computational domain is 2.5D cross-section of archetypal 3D bluff geometry
Time period: May-Dec. 2011
Air (skin) temperature from ASR dataset at 3hr resolution
Ocean temp & height from WW3+SWAN at 20 min resolution
Ice-free period: July-Oct.
Material properties: from laboratory experiments
Our initial verification study uses real oceanic/ atmospheric BC data but assumes material is ice only.

## Slide 32: Thermo-mechanical coupling: 2.5D slice
Monolithic thermo-mechanical model simulates ~22 days and performs 26 erosion steps. Formation of small niche is observed.
Figure above: z-displacement scaled 20K for m resolution mesh

## Slide 33: Thermo-mechanical coupling: 2.5D slice
As erosion proceeds, highest tensile stress occurs around corners, suggesting this is where cracks will initiate.
Figure above: for m resolution mesh

## Slide 34: Thermo-mechanical coupling: 2.5D slice
Atmospheric and oceanic boundary conditions are driving the melting of the ice
Figure above: temperature for m resolution mesh

## Slide 35: Thermo-mechanical coupling: 2.5D slice
Some issues to resolve:
Results are very mesh dependent.
For finer mesh resolutions, “teeth” patterns are observed in the eroded geometry.
  These do not seem to be physical and need to be understood.
Regardless of the mesh resolution, simulations do not make it past ~22 days.
  Nonlinear solver struggles and fails, likely due to large differences in scales between the mechanical and thermal equations.
  Sequential thermo-mechanical coupling approach is expected to alleviate this difficulty.
meters
meters

## Slide 36: Summary
We have developed a thermo-mechanical coupled FEM model, ACE, that can simulate transient niche development and permafrost erosion within Albany.
The model was calibrated using data from a series of experiments on frozen soil samples from Drew Point, Alaska that were performed at SNL’s Geomechanics Laboratory to estimate, as well as observational data collected at the same location.
The model incorporates boundary conditions from the WW3+SWAN+Delft3D wave models and observational data from an August 2019 field campaign at Drew Point, Alaska.
30m
5m
30m
z
y
x

## Slide 37: Ongoing/future work
Near term:
Resolve numerical difficulties with ACE thermo-mechanical model.
  Mitigating approach: sequential coupling between mechanics and thermal equations
Integrate chemical transport into ACE model.
Realistic erosion calculations using ACE model and Drew Point data.
Tuning/sensitivity studies to determine sensitivity ranges at Drew Point.
Validation runs to illustrate model skill using FY18-19 data from Drew Point.
Longer term:
Use ACE model to understand coastal processes in the Arctic.
Infer statistical meso-scale model and relevant physics-based parameterizations from ACE micro-model, towards integration into ESMs.
  ACE is member of the newly-funded DOE sponsored InteRFACE project* focused on coastal processes in Arctic.
* Interdisciplinary Research for Arctic Coastal Environments

## Slide 38: References
[1] J. Frederick, M. Thomas, D. Bull, C. Jones, J. Robers. “The Arctic Coastal Erosion Problem”. Sandia National Laboratories Report, SAND2016-9762, 2016.
[2] A. Gibbs, B. Richmond. “National assessment of shoreline change – historical shoreline change along the north coast of Alaska, U.S.-Canadian border to Icy Cape”. U.S. Geological Survey Open-File Report, 2015-1048, 2015.
[3] P. Martin et al. “Wildlife response to environmental Arctic change: predicting future habitats of Arctic Alaska”. Report to WildREACH: Predicting Future Habitats of Arctic Alaska Workshop, Farbanks, Alaska, 2008.
[4] J. Brown and O. Ferrians and J. Heginbottom, E. Melnikov. “Circum-Arctic map of permafrost and ground conditions. Boulder, CO: National Snow and Ice Data Center, Digital Media, 1998.
[5] H. Lantuit, W. Pollard. Fifty years of coastal erosion and retrogressive thaw slump activity on Herschel Island, southern Beaufort Sea, Yukon Territory, Canada. Geomorphology, 95, 84-102, 2008.
[6] T. Ravens, B. Jones, J. Zhang, C. Arp, J. Schmutz. “Process-based coastal erosion modeling for Drew Point, North Slope, Alaska”. Journal of Waterway, Port, Coastal, and Ocean Engineering, 138, 2, 122-130, 2012.
[7] C. Koven, J. Riley, A. Stern. “Analysis of permafrost thermal dynamics and response to climate change in the CMPI5 Earth system models”. J Climate, 26, 1877-2900, 2009.
[8] M. Thomas, A. Mota, B. Jones, C. Choens, J. Frederick, D. Bull. “Bluff geometry and material properties influence stress rates relevant to coastal permafrost block failure”. Frontiers in Earth Science 8, 2020.
[9] A. Mota, J. Frederick, D. Bull, I. Tezaur. “Thermo-chemo-mechanical coupling for Arctic Coastal Erosion”, in preparation.

## Slide 39
Research Team
SNL: D. Bull (PI), J. Frederick, A. Mota, C. Choens, I. Tezaur, L. Criscenti
USGS: M. Thomas, B. Jones
UAF: J. Kasper, E. Brown
Integral Consulting: C. Jones, C. Flanary
U Texas: J. McClelland, E. Bristol, C. Connolly
Acknowledgements

## Slide 40: Start of Backup Slides

## Slide 41: Potential impacts
PC: Andrew Burton, NPR
3D model capable of predicting erosion from the material’s constitutive relationships capturing all types of deformation (block & denudation) leading to:
  Data-driven understanding of the characteristics that cause erosion
  A tool to guide military and civil infrastructure investments
  An improved understanding of coastal food web impacts and carbon-climate feedbacks
Redistributed eroded sediment in the environment enables:
  Prediction of deposition locations
  Estimates of fluxes (biogeochemical, toxins, etc.)
Approach for moving from mechanistic micro-scale to stochastic meso-scale model sets stage for integration into global climate models built upon parametric analyses of input variables

## Slide 42: Oceanography in Mechanistic Model
WW3
SWAN
Wave set-up conditions 2-way coupled with circulation
Delft3D
Circulation and thermodynamic mixing 2-way coupled with waves
ice cover
temperature (surface and ocean)
surface winds
solar radiation
persistent currents
capture set-up (storm surge and runup)
wave energy inclusive of induced current effects
capture induced currents in nearshore
ability to model mixing of temperature and salinity clines
Development of wave field in the Arctic to develop nearshore BCs
high resolution near shore environment
Potential Key Advances
  Inclusion of ice coverage for fetch limited wave growth
  Knowledge of wave energy along broad coastline
  Set-up determination inclusive of bathymetry and wave energy
  Ability to accurately predict temperature at bluff face through mixing of clines in the ocean
WW3 polar stereographic model initially developed by NRL (Erick Rogers) and NOAA (Arun Chawla)

## Slide 43: Multi-scale approach
Micro-Scale Model | Meso-Scale Model | Macro-Scale Model
10’s of meters & storm duration | 10’s of kilometers & monthly duration | 100’s of kilometers & annual (+) durations
One set of input variables defining the geomorphology and geophysics of the terrestrial model. | A number of micro-scale models that represent the stochastic distributions of input variables along a confined coastline. | A number of meso-scale models that represent the diversity of coastline types (delta, exposed bluffs, lagoons, etc.) along the AK coastline.
  Working towards a series of fully coupled studies to determine terrestrial model sensitivities to:
    Height of water on bluff face
    Exposure time of bluff face to water
    Temperature of water
    Salinity of water

## Slide 44: Multi-scale approach
Micro-Scale Model | Meso-Scale Model | Macro-Scale Model
10’s of meters & storm duration | 10’s of kilometers & monthly duration | 100’s of kilometers & annual (+) durations
One set of input variables defining the geomorphology and geophysics of the terrestrial model. | A number of micro-scale models that represent the stochastic distributions of input variables along a confined coastline. | A number of meso-scale models that represent the diversity of coastline types (delta, exposed bluffs, lagoons, etc.) along the AK coastline.
  Working towards a series of fully coupled studies to determine terrestrial model sensitivities to:
    Height of water on bluff face
    Exposure time of bluff face to water
    Temperature of water
    Salinity of water
This talk
Notes: -Q for Alejandro: what timescales are we looking at? How big of a geometry would we run? I think 1 summer or 1 month with microscale model, to simulate Drew Point (how big?) – correct?
- Q: is there plan for integration into global ESM/global calculations?
- Q for Alejandro: plans for upscaling?

## Slide 45: Parameters & inputs
Permafrost properties depend on ice content, unfrozen water content and frost susceptibility.
Few mathematical relationships exist that describe changes in tensile strength, shear strength and cohesion of ice/permafrost with changes in temperature.
Series of experiments (UCS1, BTS2, DT3) on frozen soil samples at different temps (-6C, -3C, -1C) and ice content from Drew Point, AK were performed at SNL’s Geomechanics Laboratory to estimate:
  Strength: 1-3 MPa
  Young’s modulus: 0.01-0.16 GPa
  Poisson’s ratio: 0.1-0.35
  Porosity values: 40-95%
1 Unconfined compressive test. 2 Brazilian tensile tests. 3 Direct tensile tests.
BTS (MPa)
IceVolFrac
y=-1.872*x
R2=0.3908
Lots of noise in data!
Notes: So, the mechanical and thermal models we have developed contain a number of parameters and other inputs like boundary condition. Where do these come from? I’ll start with the mechanical parameters. There is limited data for mechanical parameters of permafrost in the literature, so we ended up performing a series of experiments on frozen soil samples at different temperatures and having different ice contents to estimate things like strength, Young’s modulus, Poisson’s ratio and porosity. These were done by my colleague, Charles Choens, at Sandia’s geomechanics laboratory, and the samples tested came from Drew Point in northern Alaska, the region we are currently targeting with the ACE model

## Slide 46: Thermo-mechanical coupling: cuboid problem
permafrost
ice
permafrost
Temp = 280 K
Disp = 0.2 m
Temp
4 days
3.0 m
1.0 m
1.0 m
Ice Saturation
Water Saturation
Temperature
Plots (right) show quantities along vertical line as a function of in the ice block
Notes: Now, we advance the simulation. You can see after 4 days, the temperature of the ice has gone up in the top part of the ice, past the melting point of 273K. As soon as this happens, you see the ice saturation go down, and the water saturation go up, meaning that the ice is melting.

## Slide 47: Thermo-mechanical coupling: cuboid problem
permafrost
ice
permafrost
Temp = 280 K
Disp = 0.2 m
Temp
3.2 m
<1.0 m
<1.0 m
Ice Saturation
Water Saturation
Temperature
24 days
Plots (right) show quantities along vertical line as a function of in the ice block
Notes: At 24 days, you see the trend continue – more ice at the top is melting.