## Slide 1: Preconditioned Least-Squares Petrov-Galerkin Reduced Order Models for Fluid and Solid Mechanics Problems
Payton Lindsay1, Jeff Fike1, Kevin Carlberg2, Irina Tezaur1
1Sandia National Labs, 2Facebook Reality Labs
MMLDT-CSET2021
Wednesday, September 28, 2021
SAND2021-11141C

## Slide 2: Motivation
Despite improved algorithms and powerful supercomputers, “high-fidelity” models are often too expensive for use in a design or analysis setting.
Sandia application areas in which this situation arises:
Captive-carry and re-entry environments: Large Eddy Simulations (LES) runs require very fine meshes and can take on the order of weeks.
Fastener failure modeling: modeling fastener behavior in a full system presents meshing and computational challenges, which limits the number of configurations that can be studied.
Climate modeling (e.g., land-ice, atmosphere): high-fidelity simulations too costly for uncertainty quantification (UQ); Bayesian inference of high-dimensional parameter fields is intractable.

## Slide 3: POD/LSPG* Approach to Model Reduction
Full Order Model (FOM) = Ordinary Differential Equation (ODE):
Proper Orthogonal Decomposition (POD):
Solve ODE at different design points
1. Acquisition
2. Learning
3. Reduction
Number of time steps
Number of State Variables
Save solution data
Choose ODE Temporal Discretization
Reduce the number of unknowns
Minimize
the Residual
*Least-Squares Petrov-Galerkin Projection [K. Carlberg et al., 2011; K. Carlberg et al., 2017]
Hyper-reduction/sample mesh

## Slide 4: POD/LSPG Approach to Model Reduction
Advantages of POD/LSPG projection:
Computes a solution that minimizes the l2-norm of the time-discrete residual arising in each
  Ensures that adding basis vectors yields a monotonic decrease in the least-squares objective function defining the underlying minimization problem [Carlberg et al., 2011]
Possesses better stability and accuracy than POD/Galerkin for certain classes of problems (e.g., compressible flow) [Carlberg et al., 2013; Carlberg et al., 2017; Tezaur et al., 2018].
Accuracy for predictive problems can be inadequate
Method may fail to converge for some realistic problems run in the predictive regime
Method may struggle when applied to problems with disparate scales [Washabaugh, 2016]
Solution: introduction of preconditioning into LSPG ROM formulation.
FOM
-- 1000 mode POD/LSPG ROM
2000 mode POD/LSPG ROM
3000 mode POD/LSPG ROM
Time
Pressure
Predictive
Reproductive
Room for improvement for realistic predictive applications:

## Slide 5: Preconditioned LSPG ROMs
LSPG Formulation:
Preconditioned LSPG Formulation:
Gauss-Newton iteration
Normal equations
Optimization problem
Gauss-Newton iteration
Normal equations
Optimization problem

## Slide 6: Preconditioned LSPG ROMs
Adding preconditioning to the POD/LSPG formulation can improve not only ROM efficiency but also ROM accuracy.
Ideal preconditioned ROM emulates projection of FOM solution increment onto POD basis.
Minimizing the raw (unweighted) residual can be problematic for systems of PDEs where different variables have drastically different magnitudes (e.g., dimensional PDEs, multi-physics) [Washabaugh, 2016].
Adding a preconditioner amounts to scaling the ROM residual to get all the equations to be roughly the same order.
Ideal preconditioned ROM ( ) gives rise to “projected solution increment” solution (1)
As quality of preconditioner is improved ( ), the ROM solution approaches the most accurate ROM solution possible for a given basis .
Preconditioning ensures all residual components are on approximately the same scale.
Upper limit on ROM accuracy is obtained by taking solution increment computed by FOM, at each time step and projecting it onto the POD basis:
(1)

## Slide 7: Numerical Examples: Albany and SPARC codes
multi-physics finite element code
Open-source1, parallel, C++ code
Component-based design for rapid development
Contains a wide variety of constitutive models for mechanical/thermo-mechanical problems.
Makes extensive use of libraries from the open-source Trilinos project2, including preconditioners from the Ifpack library
1https://github.com/SNLComputation/Albany/releases/tag/MOR_support_end 2https://github.com/trilinos/trilinos
Problems tested: quasi-static mechanical and thermo-mechanical with prediction across material parameter space.
SPARC3 Flow Solver
Next-generation transonic and hypersonic C++ CFD code developed at Sandia
Simulates compressible flow
Used for analyses involving captive carry and reentry vehicles
Primary discretization is cell-centered finite volume method
Leverages libraries from the Trilinos project2
Problems tested: transient compressible laminar flow over an open cavity with prediction in time
3Sandia Parallel Aerodynamics and Reentry Code

## Slide 8: Thermo-Mechanical Pressure Vessel (Albany)
Coupled thermo-mechanical problem involving Neohookean material
  Multi-physics problem: temperature and displacement solutions differ by 9 orders of magnitude
2 sets of material blocks, and , each having set of material params
  Material parameters in block (magenta, cyan) are fixed
  Material parameters in block (green, yellow, blue) are varied
Pressure vessel is heated and pressurized from the inside
Problem is run quasi-statically to pseudo-time 720s with 370K dofs
Training is performed for 4 sets of parameters; testing/prediction is performed for 2 sets of parameters (see Table 1)
Table 1. Parameters in block for thermo-mechanical pressure vessel problem.
[Lindsay et al., in prep.]
Testing 1
Testing 2

## Slide 9: Thermo-Mechanical Pressure Vessel (Albany)
FOM
LSPG ROM
PC-LSPG ROM
Global relative error:
Preconditioned LSPG ROMs are up to 5 orders of magnitude more accurate than LSPG ROMs.
LSPG ROMs do not converge for larger basis sizes.
Accuracy is improved by improving the preconditioner.
Seven basis sizes evaluated: 2,4,8,16, 32,79,790

## Slide 10: Thermo-Mechanical Pressure Vessel (Albany)
Top figures: CPU times
Bottom figures: # nonlinear iterations
Preconditioned LSPG ROMs are up to 12x faster than vanilla LSPG ROMs
More sophisticated preconditioners lead to greater CPU times
Speed-ups are largely due to reduction in # nonlinear iterations (by factor of >12x)

## Slide 11: Thermo-Mechanical Pressure Vessel (Albany)
Pareto plot confirms competitiveness of preconditioned LSPG ROMs.

## Slide 12: Compressible Cavity Flow (SPARC)
2D viscous laminar flow around an open cavity geometry
  Simple model for the captive carry scenario
Mach number = 0.6, Reynolds number 3000
Problem is run non-dimensionally
Domain is discretized using 104,500 hexahedral cells (right)
Of primary interest are long-time predictive simulations
  ROM is run at same parameters as FOM but much longer in time
  Relevant QOIs: statistics of the flow (e.g., pressure power spectral densities or PSDs)
-axis
-axis
[Tezaur et al. 2017; Fike et al. 2018]

## Slide 13: Compressible Cavity Flow (SPARC)
Method | RMS OASPL1 in dB | % Difference from FOM
FOM | 66.176 | 
Ideal | 67.552 | 2.08%
LSPG | N/A | N/A
LSPG + Jacobi PC | 68.033 | 2.80%
Method | RMS OASPL1 in dB | % Difference from FOM
FOM | 66.176 | 
Ideal | 67.552 | 2.08%
LSPG | N/A | N/A
LSPG + Jacobi PC | 68.033 | 2.80%
1Overall sound pressure level
Figure top left: pressure time history for a point halfway up the downstream wall of the cavity for an LSPG ROM having 327 modes with a Jacobi preconditioner
Figure bottom left: pressure PSD for the signal in the top left figure (solid line is mean PSD, shaded regions indicate range of values used to construct the mean)
Preconditioned LSPG ROM captures well the pressure PSD, including its peaks (Rossiter modes) and the RMS OASPL1
Vanilla LSPG ROM did not run successfully

## Slide 14: Summary & Future Work
Summary:
Adding preconditioning to the LSPG formulation gives rise to ROMs with improved accuracy and robustness, especially in the predictive regime
  Preconditioning attempts to emulate projection of FOM solution increment onto POD basis (the ROM “best-case scenario” for a given basis)
  Preconditioning ensures all components of residual being minimized are of the same magnitude
  Results on predictive (across parameter space) thermo-mechanical and predictive (in time) compressible flow problems are compelling
Ongoing/future work:
Two manuscripts on this work are in preparation
  P. Lindsay, J. Fike, K. Carlberg, I. Tezaur. “Preconditioned LSPG Reduced Order Models”, in prep.
  J. Fike, P. Lindsay, K. Carlberg, I. Tezaur. “Preconditioned Least-Squares Petrov-Galerkin Reduced Order Models for Compressible Flows”, in prep.
Application of preconditioned LSPG approach to more sophisticated problems relevant to Sandia’s mission spaces
  Preconditioning LSPG ROMs has been helpful for hypersonic aero, thermal/ablation and reacting hypersonic flow problems

## Slide 15
Start of Backup Slides

## Slide 16: Mechanical Beam (Albany)
Mechanical problem involving Neohookean material
2 sets of material blocks, and , each having set of material params
  Material parameters in block are fixed
  Material parameters in block are varied (see Table 2)
Linearly varying time-dependent pressure BC is prescribed on ; other boundaries are fixed
Problem is run quasi-statically to pseudo-time 7200s with 1340 dofs
Table 2. Parameters in block for mechanical beam problem.
Training is performed for 6 sets of parameters; testing/prediction is performed for 4 sets of parameters (see Table 2)
  Nontrivial variations in displacement (up to 20%) are observed with the parameter variations considered (right figure)
[Lindsay et al., in prep.]

## Slide 17: Mechanical Beam (Albany)
Figure plots global relative error in approximate ROM solutions:
Preconditioners evaluated: Jacobi, Gauss-Seidel, ILU and (denoted by “Ideal”)
Nonlinear solver for unpreconditioned LSPG ROM did not converge for any of the basis sizes considered.
More sophisticated preconditioners deliver smaller errors.

## Slide 18: Mechanical Beam (Albany)
Figure plots condition numbers of reduced Jacobian ( or ) for each ROM.
A moderate reduction in condition number is obtained through preconditioning strategies.
Most sophisticated ILU preconditioner gives rise to a reduced Jacobian with the smallest condition number.

## Slide 19: Mechanical Beam (Albany)
Figures shows CPU-times for all ROMs considered
As expected, the projected solution increment is the most expensive to compute

## Slide 20: Mechanical Beam (Albany)
The best preconditioner given error/CPU-time requirements can be inferred from Pareto plot shown here.

## Slide 21: Thermo-Mechanical Beam (Albany)
Coupled thermo-mechanical problem involving Neohookean material
2 sets of material blocks, and , each having set of material params
  Material parameters in block are fixed
  Material parameters in block are varied (see Table 3)
Linearly varying time-dependent pressure and temperature BC is prescribed on and , respectively; other boundaries are fixed
Problem is run quasi-statically to pseudo-time 7200s with 2100 dofs
Table 3. Parameters in block for thermo-mechanical beam problem.
Training is performed for 6 sets of parameters; testing/prediction is performed for 4 sets of parameters (see Table 3)
  Significant variations in displacement (up to 60%) are observed with the parameter variations considered (right figure)
[Lindsay et al., in prep.]

## Slide 22: Thermo-Mechanical Beam (Albany)

## Slide 23: Thermo-Mechanical Beam (Albany)

## Slide 24: Thermo-Mechanical Beam (Albany)

## Slide 25: Thermo-Mechanical Beam (Albany)

## Slide 26: Thermo-Mechanical Beam (Albany)
Figure plots condition numbers of reduced Jacobian ( or ) for each ROM.
Reduced Jacobians for regular LSPG ROM are very ill-conditioned ()
  Ill-conditioning is due to extreme differences in scale b/w displacement and temperature solutions (9 orders of magnitude)
Results demonstrate that simple preconditioning strategy can reduce condition numbers by as many as 10 orders of magnitude
As expected, projected solution increment reduced Jacobian has perfect condition number

## Slide 27: Thermo-Mechanical Beam (Albany)
Figures shows CPU-times for all ROMs considered
In general, preconditioned LSPG ROMs achieve CPU-times smaller than unpreconditioned LSPG ROM
As expected, the projected solution increment is the most expensive to compute in general

## Slide 28: Thermo-Mechanical Beam (Albany)
Pareto plot results confirm that there is a significant computational advantage in applying preconditioning