## Slide 1: The Schwarz Alternating Method for Multiscale Coupling in Solid Mechanics
SAND2019-5577 C
Sandia National Laboratories is a multi-mission laboratory managed and operated by National Technology and Engineering Solutions of Sandia, LLC., a wholly owned subsidiary of Honeywell International, Inc., for the U.S. Department of Energy’s National Nuclear Security Administration under contract DE-NA0003525.
Alejandro Mota1, Irina Tezaur1, Coleman Alleman1, Greg Phlipot2
1Sandia National Laboratories, Livermore, CA, USA. 2California Institute of Technology, Pasadena, CA, USA.
COUPLED 2019 Sitges, Spain June 3-5, 2019

## Slide 2
Outline
Motivation
Schwarz Alternating Method for Concurrent Multiscale Coupling for Quasistatics
  Formulation
  Implementation
  Numerical Examples
Schwarz Alternating Method for Concurrent Multiscale Coupling for Dynamics
  Formulation
  Implementation
  Numerical Examples
Summary
Future Work

## Slide 3
Outline
Motivation
Schwarz Alternating Method for Concurrent Multiscale Coupling for Quasistatics
  Formulation
  Implementation
  Numerical Examples
Schwarz Alternating Method for Concurrent Multiscale Coupling for Dynamics
  Formulation
  Implementation
  Numerical Examples
Summary
Future Work
COUPLED 2017 talk

## Slide 4
Outline
Motivation
Schwarz Alternating Method for Concurrent Multiscale Coupling for Quasistatics
  Formulation
  Implementation
  Numerical Examples
Schwarz Alternating Method for Concurrent Multiscale Coupling for Dynamics
  Formulation
  Implementation
  Numerical Examples
Summary
Future Work
NEW!

## Slide 5
Outline
Motivation
Schwarz Alternating Method for Concurrent Multiscale Coupling for Quasistatics
  Formulation
  Implementation
  Numerical Examples
Schwarz Alternating Method for Concurrent Multiscale Coupling for Dynamics
  Formulation
  Implementation
  Numerical Examples
Summary
Future Work

## Slide 6
Motivation for Concurrent Multiscale Coupling
Large scale structural failure frequently originates from small scale phenomena such as defects, microcracks, inhomogeneities and more, which grow quickly in unstable manner.
Failure occurs due to tightly coupled interaction between small scale (stress concentrations, material instabilities, cracks, etc.) and large scale (vibration, impact, high loads and other perturbations).
Roof failure of Boeing 737 aircraft due to fatigue cracks. From imechanica.org
Concurrent multiscale methods are essential for understanding and prediction of behavior of engineering systems when a small scale failure determines the performance of the entire system.
Surface flaw in pressure vessel: interacts with microstructure, which may or may not lead to failure.
Notes: Fuselage failure: small flaws grow quickly in unstable manner
Pressure vessel: flaw in surface interacts with microstructure, which can lead to failure or microstructure or not; determining which one happens is complex
If the activity score is YELLOW or RED then be prepared to address issues, cause, and
path forward.

## Slide 7
Requirements for Multiscale Coupling Method
Coupling is concurrent (two-way).
Ease of implementation into existing massively-parallel HPC codes.
Scalable, fast, robust (we target real engineering problems, e.g., analyses involving failure of bolted components!).
“Plug-and-play” framework: simplifies task of meshing complex geometries!
  Ability to couple regions with different non-conformal meshes, different element types and different levels of refinement.
  Ability to use different solvers/time-integrators in different regions.
Coupling does not introduce nonphysical artifacts.
Theoretical convergence properties/guarantees.

## Slide 8
Schwarz Alternating Method for Domain Decomposition
Proposed in 1870 by H. Schwarz for solving Laplace PDE on irregular domains.
H. Schwarz (1843 – 1921)
Initialize:
Solve PDE by any method on W1 w/ initial guess for Dirichlet BCs on G1.
Iterate until convergence:
Solve PDE by any method (can be different than for W1) on W2 w/ Dirichlet BCs on G2 that are the values just obtained for W1.
Solve PDE by any method (can be different than for W2) on W1 w/ Dirichlet BCs on G1 that are the values just obtained for W2.
Crux of Method: if the solution is known in regularly shaped domains, use those as pieces to iteratively build a solution for the more complex domain.
Basic Schwarz Algorithm
Notes: If the activity score is YELLOW or RED then be prepared to address issues, cause, and
path forward.

## Slide 9
Schwarz Alternating Method for Domain Decomposition
Proposed in 1870 by H. Schwarz for solving Laplace PDE on irregular domains.
H. Schwarz (1843 – 1921)
Initialize:
Solve PDE by any method on W1 w/ initial guess for Dirichlet BCs on G1.
Iterate until convergence:
Solve PDE by any method (can be different than for W1) on W2 w/ Dirichlet BCs on G2 that are the values just obtained for W1.
Solve PDE by any method (can be different than for W2) on W1 w/ Dirichlet BCs on G1 that are the values just obtained for W2.
Crux of Method: if the solution is known in regularly shaped domains, use those as pieces to iteratively build a solution for the more complex domain.
Basic Schwarz Algorithm
Requirement for convergence:
Notes: If the activity score is YELLOW or RED then be prepared to address issues, cause, and
path forward.

## Slide 10
Schwarz Alternating Method for Domain Decomposition
Proposed in 1870 by H. Schwarz for solving Laplace PDE on irregular domains.
H. Schwarz (1843 – 1921)
Initialize:
Solve PDE by any method on W1 w/ initial guess for Dirichlet BCs on G1.
Iterate until convergence:
Solve PDE by any method (can be different than for W1) on W2 w/ Dirichlet BCs on G2 that are the values just obtained for W1.
Solve PDE by any method (can be different than for W2) on W1 w/ Dirichlet BCs on G1 that are the values just obtained for W2.
Crux of Method: if the solution is known in regularly shaped domains, use those as pieces to iteratively build a solution for the more complex domain.
Basic Schwarz Algorithm
Requirement for convergence:
Schwarz alternating method most commonly used as a preconditioner for Krylov iterative methods to solve linear algebraic equations.
Notes: If the activity score is YELLOW or RED then be prepared to address issues, cause, and
path forward.

## Slide 11
Schwarz Alternating Method for Domain Decomposition
Proposed in 1870 by H. Schwarz for solving Laplace PDE on irregular domains.
H. Schwarz (1843 – 1921)
Initialize:
Solve PDE by any method on W1 w/ initial guess for Dirichlet BCs on G1.
Iterate until convergence:
Solve PDE by any method (can be different than for W1) on W2 w/ Dirichlet BCs on G2 that are the values just obtained for W1.
Solve PDE by any method (can be different than for W2) on W1 w/ Dirichlet BCs on G1 that are the values just obtained for W2.
Crux of Method: if the solution is known in regularly shaped domains, use those as pieces to iteratively build a solution for the more complex domain.
Basic Schwarz Algorithm
Requirement for convergence:
Schwarz alternating method most commonly used as a preconditioner for Krylov iterative methods to solve linear algebraic equations.
Novel idea: using the Schwarz alternating as a discretization method for solving multiscale partial differential equations (PDEs).
Notes: If the activity score is YELLOW or RED then be prepared to address issues, cause, and
path forward.

## Slide 12
Outline
Motivation
Schwarz Alternating Method for Concurrent Multiscale Coupling for Quasistatics
  Formulation
  Implementation
  Numerical Examples
Schwarz Alternating Method for Concurrent Multiscale Coupling for Dynamics
  Formulation
  Implementation
  Numerical Examples
Summary
Future Work

## Slide 13
Schwarz Alternating Method for Multiscale Coupling in Quasistatics
Advantages:
Conceptually very simple.
Allows the coupling of regions with different non-conforming meshes, different element types, and different levels of refinement.
Information is exchanged among two or more regions, making coupling concurrent.
Different solvers can be used for the different regions.
Different material models can be coupled if they are compatible in the overlap region.
Simplifies the task of meshing complex geometries for the different scales.

## Slide 14
S. L. Sobolev (1936): posed Schwarz method for linear elasticity in variational form and proved method’s convergence by proposing a convergent sequence of energy functionals.
S. G. Mikhlin (1951): proved convergence of Schwarz method for general linear elliptic PDEs.
A. Mota, I. Tezaur, C. Alleman (2017)*: derived a proof of convergence of the alternating Schwarz method for the finite deformation quasi-static nonlinear PDEs (with energy functional defined below), and determined a geometric convergence rate for the finite deformation quasi-static problem.
S. G. Mikhlin (1908 – 1990)
S. L. Sobolev (1908 – 1989)
-
*A. Mota, I. Tezaur, C. Alleman. "The Schwarz Alternating Method in Solid Mechanics", CMAME 319 (2017), 19-51.
A. Mota, I. Tezaur, C. Alleman
Using the Schwarz alternating as a discretization method for PDEs is natural idea with a sound theoretical foundation.
Theoretical Foundation
Notes: If the activity score is YELLOW or RED then be prepared to address issues, cause, and
path forward.

## Slide 15
Full Schwarz
Modified Schwarz
Inexact Schwarz
Monolithic Schwarz
*A. Mota, I. Tezaur, C. Alleman. "The Schwarz Alternating Method in Solid Mechanics", CMAME 319 (2017), 19-51.
Four Variants* of Schwarz
Notes: Monolithic: elimination of Schwarz BC dofs
Modified: treat Schwarz BCs at Dirichlet BCs

## Slide 16
Four Variants* of Schwarz
Full Schwarz
Modified Schwarz
Inexact Schwarz
Monolithic Schwarz
Most performant method: monotonic convergence, theoretical convergence guarantee.
*A. Mota, I. Tezaur, C. Alleman. "The Schwarz Alternating Method in Solid Mechanics", CMAME 319 (2017), 19-51.

## Slide 17
Outline
Motivation
Schwarz Alternating Method for Concurrent Multiscale Coupling for Quasistatics
  Formulation
  Implementation
  Numerical Examples
Schwarz Alternating Method for Concurrent Multiscale Coupling for Dynamics
  Formulation
  Implementation
  Numerical Examples
Summary
Future Work

## Slide 18
Implementation within Albany Code
Component-based design for rapid development of capabilities.
Contains a wide variety of constitutive models.
Extensive use of libraries from the open-source Trilinos project.
  Use of the Phalanx package to decompose complex problem into simpler problems with managed dependencies.
  Use of the Sacado package for automatic differentiation.
  Use of Teko package for block preconditioning.
Parallel implementation of Schwarz alternating method uses the Data Transfer Kit (DTK).
All software available on GitHub.
https://github.com/trilinos/trilinos
https://github.com/gahansen/Albany
https://github.com/ORNL-CEES/DataTransferKit
The proposed quasistatic alternating Schwarz method is implemented within the LCM project in Sandia’s open-source parallel, C++, multi-physics, finite element code, Albany.

## Slide 19
Outline
Motivation
Schwarz Alternating Method for Concurrent Multiscale Coupling for Quasistatics
  Formulation
  Implementation
  Numerical Examples
Schwarz Alternating Method for Concurrent Multiscale Coupling for Dynamics
  Formulation
  Implementation
  Numerical Examples
Summary
Future Work

## Slide 20
Schwarz Iteration
Quasistatic Example #1: Cuboid Problem
Coupling of two cuboids with square base (above).
Neohookean-type material model.

## Slide 21
Below: Convergence of the cuboid problem for different mesh sizes and fixed overlap volume fraction. The Schwarz alternating method converges linearly.
Above: Convergence factor as a function of overlap volume and different mesh. There is faster linear convergence with increasing overlap volume fraction.
Cuboid Problem: Convergence with Overlap & Refinement

## Slide 22: Cuboid Problem: Schwarz Error

## Slide 23
Quasistatic Example #2: Notched Cylinder
Notched cylinder that is stretched along its axial direction.
Domain decomposed into two subdomains.
Neohookean-type material model.

## Slide 24
The Schwarz alternating method is capable of coupling different mesh topologies.
The notched region, where stress concentrations are expected, is finely meshed with tetrahedral elements.
The top and bottom regions, presumably of less interest, are meshed with coarser hexahedral elements.
Notched Cylinder: TET-HEX Coupling

## Slide 25
Notched Cylinder: TET-HEX Coupling

## Slide 26
Notched Cylinder: Conformal TET-HEX Coupling
Notes: - Geometric error

## Slide 27
Notched cylinder subjected to tensile load with an elastic and J2 elasto-plastic regions.
Coarse region is elastic and fine region is elasto-plastic.
The overlap region in the first mesh is nearer the notch, where plastic behavior is expected.
Overlap far from notch.
Overlap near notch.
Coupled regions
Coarse, elastic region
Fine, elasto-plastic region
Notched Cylinder: Coupling Different Materials
The Schwarz method is capable of coupling regions with different material models.

## Slide 28
When the overlap region is far from the notch, no plastic deformation exists in it: the coarse and fine regions predict the same behavior.
When the overlap region is near the notch, plastic deformation spills onto it and the two models predict different behavior, affecting convergence adversely.
Overlap far from notch.
Overlap near notch.
Notched Cylinder: Coupling Different Materials
Need to be careful to do domain decomposition so that material models are consistent in overlap region.

## Slide 29: Quasistatic Example #3: Laser Weld
Laser weld specimen
Problem of practical scale (~200K dofs).
Isotropic elasticity and J2 plasticity with linear isotropic hardening.
Identical parameters for weld and base materials for proof of concept, to become independent models.
Coupled Schwarz discretization
(50% reduction in model size)
Single domain discretization
Notes: Stress contours show Cauchy stress in the loading direction; total strain is approximately 2%.

## Slide 30: Laser Weld: Strong Scalability of Parallel Schwarz with DTK
Near-ideal linear speedup (64-1024 cores).
Data Transfer Kit (DTK)

## Slide 31
Outline
Motivation
Schwarz Alternating Method for Concurrent Multiscale Coupling for Quasistatics
  Formulation
  Implementation
  Numerical Examples
Schwarz Alternating Method for Concurrent Multiscale Coupling for Dynamics
  Formulation
  Implementation
  Numerical Examples
Summary
Future Work

## Slide 32
Schwarz Alternating Method for Dynamics
In the literature the Schwarz method is applied to dynamics by using space-time discretizations.
Overlapping non-matching meshes and time steps in dynamics.
Notes: FIXME: add refs?
FIXME: have Alejandro explain picture

## Slide 33
In the literature the Schwarz method is applied to dynamics by using space-time discretizations.
Overlapping non-matching meshes and time steps in dynamics.
Pro : Can use non-matching meshes and time-steps (see right figure).
Con : Unfeasible given the design of our current codes and size of simulations.
Schwarz Alternating Method for Dynamics
Notes: FIXME: add refs?
FIXME: have Alejandro explain picture

## Slide 34
Schwarz Alternating Method for Dynamic Multiscale Coupling
Controller time stepper
Time integrator for W1
Time integrator for W2
Step 0: Initialize
Controller time stepper = convenient checkpoint to facilitate implementation
Notes: FIXME: add algorithm?

## Slide 35
Schwarz Alternating Method for Dynamic Multiscale Coupling
Integrate using
Interpolate from to
Controller time stepper
Time integrator for W1
Time integrator for W2
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Controller time stepper = convenient checkpoint to facilitate implementation
Notes: FIXME: add algorithm?

## Slide 36
Schwarz Alternating Method for Dynamic Multiscale Coupling
Controller time stepper
Time integrator for W1
Time integrator for W2
Integrate using
Interpolate from to
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Step 2: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times .
Controller time stepper = convenient checkpoint to facilitate implementation
Notes: FIXME: add algorithm?

## Slide 37
Schwarz Alternating Method for Dynamic Multiscale Coupling
Controller time stepper
Time integrator for W1
Time integrator for W2
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Step 2: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times .
Step 3: Check for convergence at time .
Controller time stepper = convenient checkpoint to facilitate implementation
Notes: FIXME: add algorithm?

## Slide 38
Schwarz Alternating Method for Dynamic Multiscale Coupling
Controller time stepper
Time integrator for W1
Time integrator for W2
Interpolate from to
Integrate using
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Step 2: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times .
Step 3: Check for convergence at time .
If unconverged, return to Step 1.
Controller time stepper = convenient checkpoint to facilitate implementation
Notes: FIXME: add algorithm?

## Slide 39
Schwarz Alternating Method for Dynamic Multiscale Coupling
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Step 2: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times .
Step 3: Check for convergence at time .
If unconverged, return to Step 1.
If converged, set and return to Step 1.
Controller time stepper
Time integrator for W1
Time integrator for W2
Integrate using
Interpolate from to
Controller time stepper = convenient checkpoint to facilitate implementation
Notes: FIXME: add algorithm?

## Slide 40
Schwarz Alternating Method for Dynamic Multiscale Coupling
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Step 2: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times .
Step 3: Check for convergence at time .
If unconverged, return to Step 1.
If converged, set and return to Step 1.
Controller time stepper
Time integrator for W1
Time integrator for W2
Integrate using
Interpolate from to
Controller time stepper = convenient checkpoint to facilitate implementation
Can use different integrators with different time steps within each domain!
Notes: FIXME: add algorithm?

## Slide 41
Schwarz Alternating Method for Dynamic Multiscale Coupling: Theory
For quasistatics, we derived a proof of convergence of the alternating Schwarz method for the finite deformation problem, and determined a geometric convergence rate [(Mota, Tezaur, Alleman, CMAME, 2017) and previous talk].
  Quasistatic proof extends naturally assuming conformal meshes and the same time step is used in each Schwarz subdomain.
  Some analysis of Schwarz for evolution problems was performed in (Lions, 1988) and may be possible to leverage.
  Our numerical results suggest theoretical analysis is possible.
Extending these results to dynamics is work in progress.
Notes: FIXME: add some discussion of theory?

## Slide 42
Outline
Motivation
Schwarz Alternating Method for Concurrent Multiscale Coupling for Quasistatics
  Formulation
  Implementation
  Numerical Examples
Schwarz Alternating Method for Concurrent Multiscale Coupling for Dynamics
  Formulation
  Implementation
  Numerical Examples
Summary
Future Work

## Slide 43
Implementation within Albany Code
Component-based design for rapid development of capabilities.
Contains a wide variety of constitutive models.
Extensive use of libraries from the open-source Trilinos project.
  Use of the Phalanx package to decompose complex problem into simpler problems with managed dependencies.
  Use of the Sacado package for automatic differentiation.
  Use of Tempus package for time-integration*.
Parallel implementation of Schwarz alternating method uses the Data Transfer Kit (DTK).
All software available on GitHub.
https://github.com/trilinos/trilinos
https://github.com/gahansen/Albany
https://github.com/ORNL-CEES/DataTransferKit
The proposed dynamic alternating Schwarz method is implemented within the LCM project in Sandia’s open-source parallel, C++, multi-physics, finite element code, Albany.
* Current dynamic Schwarz implementation in Albany requires same in different subdomains.

## Slide 44
Outline
Motivation
Schwarz Alternating Method for Concurrent Multiscale Coupling for Quasistatics
  Formulation
  Implementation
  Numerical Examples
Schwarz Alternating Method for Concurrent Multiscale Coupling for Dynamics
  Formulation
  Implementation
  Numerical Examples
Summary
Future Work

## Slide 45
Dynamic Example #1: Elastic Wave Propagation
Linear elastic clamped beam with Gaussian initial condition for the 𝑧-displacement (see figures to the right and below).
Simple problem with analytical exact solution but very stringent test for discretization methods.
Test Schwarz with 2 subdomains: .
Left: Initial condition (blue) and final solution (red). Wave profile is negative of initial profile at time T = 1.0e-3.
Time-discretizations: Newmark-Beta (implicit, explicit) with same .
Meshes: hexes, tets

## Slide 46
z-displacement
Table 1: Averaged (over times + domains) relative errors in z–displacement (blue) and z-velocity (green) for several different Schwarz couplings, 50% overlap volume fraction
LM = Lumped Mass, CM = Consistent Mass
z-velocity
 | Implicit-Implicit |  | Explicit(CM)-Implicit |  | Explicit(LM)-Implicit | 
Conformal hex-hex | 2.79e-3 | 7.32e-3 | 3.53e-3 | 8.70e-3 | 4.72e-3 | 1.19e-2
Nonconformal hex-hex | 2.90e-3 | 7.10e-3 | 2.82e-3 | 7.29e-3 | 2.84e-3 | 7.33e-3
Tet-hex | 2.79e-3 | 7.58e-3 | 3.52e-3 | 8.92e-3 | 4.72e-3 | 1.19e-2
Dynamic Schwarz coupling introduces no dynamic artifacts that are pervasive in other coupling methods!
Elastic Wave Propagation

## Slide 47
Elastic Wave Propagation
For clamped beam problem, total energy (TE = ) should be conserved.
Total energy is calculated in 2 ways: with most of contribution from and from
Energy Conservation
Total energy is conserved and matches single-domain total energy.

## Slide 48
Example #2: Tension Specimen
+
Uniaxial aluminum cylindrical tensile specimen with inelastic J2 material model.
Domain decomposition into two subdomains (right): = ends, = gauge.
Nonconformal hex + composite tet 10 coupling via Schwarz.
Implicit Newmark time-integration with adaptive time-stepping algorithm employed in both subdomains.
Slight imperfection introduced at center of gauge to force necking upon pulling in vertical direction.

## Slide 49
Tension Specimen
Average of ~7 Schwarz iterations/time step required for convergence to Schwarz tolerance of 1e-6.
y-displacement
Nodal eqps*
*Nodal eqps = equivalent plastic strain computed via weighted volume average.
Notes: Schwarz iters is b/w 3-15 depending on time step

## Slide 50
Example #3: Bolted Joint Problem
bolts (composite tet 10), parts (hex).
Inelastic J2 material model in both subdomains.
  steel
  steel component, aluminum (bottom) plate
Schwarz solution compared to single-domain solution on composite tet 10 mesh.
BC: x-disp = 0.02 at T = 1.0e-3 on top of parts.
Run until T = 5.0e-4 w/ dt = 1e-5 + implicit Newmark with analytic mass matrix for composite tet 10s.
Problem of practical scale.

## Slide 51
Single
Schwarz
Bolted Joint Problem
x-displacement

## Slide 52
Cross-section of bolts obtained via clip (right)
Bolted Joint Problem
Nodal Equivalent Plastic Strain (eqps)

## Slide 53
Schwarz / solver settings
Relatively loose Schwarz tolerances were used:
  Relative Tolerance: 1.0e-3.
  Absolute Tolerance: 1.0e-4.
Newton tolerance on NormF: 1e-8
Linear solver tolerance: 1e-5
MueLu preconditioner
Top right plot: # Schwarz iterations for each time step.
  After start-up, # Schwarz iterations / time step is ~9-10. This is not bad given how small is the size of the overlap region for this problem.
Bolted Joint Problem
Some Performance Results

## Slide 54
Outline
Motivation
Schwarz Alternating Method for Concurrent Multiscale Coupling for Quasistatics
  Formulation
  Implementation
  Numerical Examples
Schwarz Alternating Method for Concurrent Multiscale Coupling for Dynamics
  Formulation
  Implementation
  Numerical Examples
Summary
Future Work

## Slide 55
Summary
Coupling is concurrent (two-way).
Ease of implementation into existing massively-parallel HPC codes.
Scalable, fast, robust (we target real engineering problems, e.g., analyses involving failure of bolted components!).
“Plug-and-play” framework: simplifies task of meshing complex geometries!
  Ability to couple regions with different non-conformal meshes, different element types and different levels of refinement.
  Ability to use different solvers/time-integrators in different regions.
Coupling does not introduce nonphysical artifacts.
Theoretical convergence properties/guarantees ( for quasistatics).







The alternating Schwarz coupling method has been developed/implemented for concurrent multiscale quasistatic & dynamic modeling in Sandia’s Albany/LCM code.


## Slide 56
Outline
Motivation
Schwarz Alternating Method for Concurrent Multiscale Coupling for Quasistatics
  Formulation
  Implementation
  Numerical Examples
Schwarz Alternating Method for Concurrent Multiscale Coupling for Dynamics
  Formulation
  Implementation
  Numerical Examples
Summary
Future Work

## Slide 57
Develop theory for dynamic alternating Schwarz formulation.
Journal article on dynamic Schwarz formulation.
Extension of Albany/LCM dynamic Schwarz implementation to allow for different time steps in different subdomains.
Apply dynamic Schwarz to problem of interest to production.
Implement alternating Schwarz method in Sandia production codes (Sierra Solid Mechanics).
Development of a multi-physics coupling framework based on variational formulations and the Schwarz alternating method.
Ongoing/Future Work

## Slide 58
References
[1] M.A. Heroux et al. “An overview of the Trilinos project.” ACM Trans. Math. Softw. 31(3) (2005).
[2] A. Salinger, et al. "Albany: Using Agile Components to Develop a Flexible, Generic Multiphysics Analysis Code", Int. J. Multiscale Comput. Engng. 14(4) (2016) 415-438.
[3] H. Schwarz. “Über einen Grenzübergang durch alternierendes Verfahren”. In: Vierteljahrsschriftder Naturforschenden Gesellschaft in Zurich 15 (1870), pp. 272–286.
[4] S.L. Sobolev. “Schwarz’s Algorithm in Elasticity Theory”. In: Selected Works of S.L Sobolev. Volume I: equations of mathematical physics, computational mathematics and cubature formulats. Ed. By G.V. Demidenko and V.L. Vaskevich. New York: Springer, 2006.
[5] S. Mikhlin. “On the Schwarz algorithm”. In: Proceedings of the USSR Academy of Sciences (in Russian) 77 (1951), pp. 569–571.
[6] D.J. Evans et al. “The convergence rate of the Schwarz alternating procedure (II): For two-dimensional problems”. In: International Journal for Computer Mathematics 20.3–4 (1986), pp. 325–339.
[7] P.L. Lions. “On the Schwarz alternating method I.” In: 1988, First International Symposium on Domain Decomposition methods for Partial Differential Equations, SIAM, Philadelphia.
[8] A. Mota, I. Tezaur, C. Alleman. "The Schwarz Alternating Method in Solid Mechanics", Comput. Meth. Appl. Mech. Engng. 319 (2017), 19-51. [http://www.sandia.gov/~ikalash/journal.html].
[9] A. Mota, I. Tezaur, G. Phlipot. "The Schwarz alternating method for dynamic solid mechanics”, in prep.

## Slide 59
Appendix. Previous Work
Notes: - Three-field formulation with weak compatibility enforced weakly using LMs.
If the activity score is YELLOW or RED then be prepared to address issues, cause, and
path forward.

## Slide 60
Appendix. Previous Work
Three-field multiscale coupling formulation with compatibility enforced weakly using Lagrange multipliers.
Notes: - Three-field formulation with weak compatibility enforced weakly using LMs.
If the activity score is YELLOW or RED then be prepared to address issues, cause, and
path forward.

## Slide 61
Appendix. Previous Work
Method works well, but is difficult to implement into existing codes.
Notes: - Three field multiscale coupling formulation, with compatibility enforced weakly using LMs.
If the activity score is YELLOW or RED then be prepared to address issues, cause, and
path forward.

## Slide 62
Appendix. Full Schwarz Method
Classical algorithm originally proposed by Schwarz with outer Schwarz loop and inner Newton loop, each converged to a tight tolerance (

## Slide 63
Appendix. Inexact Schwarz Method
Classical algorithm originally proposed by Schwarz with outer Schwarz loop and inner Newton loop, with Newton step converged to a loose tolerance

## Slide 64
Appendix. Monolithic Schwarz Method
Combines Schwarz and Newton loop into since Newton-Schwarz loop, with elimination of Schwarz boundary DOFs, and tight convergence tolerance.
Advantages:
By-passes Schwarz loop.
Disadvantages:
Off-diagonal coupling terms block linear solver is needed.

## Slide 65
Appendix. Modified Schwarz Method
Combines Schwarz and Newton loop into since Newton-Schwarz loop, with Schwarz boundaries at Dirichlet boundaries and tight convergence tolerance.
Least-intrusive variant: by-passes Schwarz iteration, no need for block solver.
Advantages:
By-passes Schwarz loop.
No diagonal coupling (conventional linear solver can be used in each subdomain).

## Slide 66
Appendix. Convergence Proof

## Slide 67: Appendix. Foulk’s Singular Bar
1D proof of concept problem:
  1D bar with area proportional to square root of length.
  Strong singularity on left end of bar.
  Simple hyperelestic material model with no damage.
  MATLAB implementation.
Problem goals:
  Explore viability of 4 variants of the Schwarz alternating method.
  Test convergence and compare with literature (Evans, 1986).
    Expect faster convergence in fewer iterations with increased overlap.

## Slide 68: Appendix. Singular Bar and Schwarz Variants
Notes: Linear convergence for all methods (bottom left)
Monolithic Schwarz converges faster but timings are similar -> all implementations are interchangeable (bottom right)
Amount of overlap critical for convergence (top right)

## Slide 69
Appendix. Notched Cylinder: HEX-HEX Coupling

## Slide 70
Appendix. Notched Cylinder: Nonconformal HEX-HEX Coupling

## Slide 71
Appendix. Notched Cylinder: Nonconformal HEX-HEX Coupling
Notes: - Geometric error

## Slide 72: Appendix. Multiscale Modeling of Localization
Region of localization (necking)
  Goals:
  Connect physical length scales to engineering scale models.
  Investigate importance of microstructural detail.
  Develop bridging technologies for spatial multiscale/ multiphysics.
Region of localization (fracture)
  Strain localization can cause localized necking (left) and ultimately fracture (above).
Notes: Strain localization is a ubiquitous feature of elastoplastic materials undergoing nonhomogeneous deformation. The phenomenon manifests in the form of a shear band, a narrow zone of intense straining across which some kinematical fields in a deforming body may be discontinuous.
Strain localization can cause local necking and ultimately fracture.

## Slide 73: Appendix. Parallelization via DTK: Weak Scaling on Cubes Problem
1 Processor,
2.5*103 DOF / proc
8 Processors,
2.1*103 DOF / proc
64 Processors,
1.9*103 DOF / proc

## Slide 74: Appendix. Parallelization via DTK: Strong Scaling on Cubes Problem
Small problem (2.5*103 DOFs)
Medium problem (1.7*104 DOFs)
176 DOF/processor
107 DOF/processor
Large problem (1.6*105 DOFs)
5124 DOF/processor

## Slide 75
Appendix. Rubiks Cube Problem
plotting axial
stress
concurrent coupling
Two distinct bodies, the component scale and the microstructural scale, are coupled iteratively with alternating Schwarz
component
scale
distinct
models
microstructural
scale
Work by J. Foulk, D. Littlewood, C. Battaile, H. Lim

## Slide 76: Appendix. Tensile Bar
Embed microstructure in ASTM tensile geometry

## Slide 77: Appendix. Tensile Bar: Meso-Macroscale Coupling
+
Mesoscale
Macroscale
SPARKS-generated microstructure (F. Abdeljawad)
Fix microstructure, investigate ensembles
151 axial vectors from 3 of the 10 ensembles of random rotations
(blue, green, red)
Load microstructural ensembles in uniaxial stress
Fit flow curves with a macroscale J2 plasticity model
Notes: \text{cubic elastic constant}: C_{11} = 204.6 \; \text{GPa} \\
\text{cubic elastic constant}: C_{12} = 137.7 \; \text{GPa} \\
\text{cubic elastic constant}: C_{44} = 126.2 \; \text{GPa} \\
\text{reference shear rate}: \dot{\gamma}_{0} = 1.0 \; \text{1/s} \\
\text{rate sensitivity factor}: m = 20 \\
\text{hardening rate parameter}: \dot{g_{0}} = 2.0 \times 10^{4} \; \text{1/s} \\
\text{initial hardness}: g_{0} = 90 \; \text{MPa} \\
\text{saturation hardness}: g_{s} = 202 \; \text{MPa} \\
\text{saturation exponent}: \omega = 0.01
\text{Young's modulus}: E = 195.0 \; \text{GPa} \\
\text{Poission's ratio}: \nu = 0.3 \\
\text{yield stress}: \sigma_{0} = 144 \; \text{MPa} \\
\text{hardening modulus}: H = 300 \; \text{MPa} \\
\text{saturation modulus}: S = 170 \; \text{MPa} \\
\text{saturation exponent}: \alpha = 190
\sigma_{y} = \sigma_{0} + H \epsilon_{p} + S (1 - e^{-\alpha \epsilon_{p}})

## Slide 78: Appendix. Tensile Bar: Results
Reduction in cross-sectional area over time

## Slide 79
Appendix. Schwarz Alternating Method
for Dynamics
In the literature the Schwarz method is applied to dynamics by using space-time discretizations.
This was deemed unfeasible given the design of our current codes and size of simulations.
Overlapping non-matching meshes and time steps in dynamics.

## Slide 80
Appendix. A Schwarz-like Time Integrator
We developed an extension of Schwarz coupling to dynamics using a governing time stepping algorithm that controls time integrators within each domain.
Can use different integrators with different time steps within each domain.
1D results show smooth coupling without numerical artifacts such as spurious wave reflections at boundaries of coupled domains.
Controller time stepper
Time integrator for W1
Time integrator for W2

## Slide 81
Appendix. Dynamic Singular Bar
Inelasticity masks problems by introducing energy dissipation.
Schwarz does not introduce numerical artifacts.
Can couple domains with different time integration schemes (Explicit-Implicit below).

## Slide 82
Appendix. Elastic Wave Propagation
Left figure shows # of iterations as a function of overlap region size for 2 subdomains. The method does not converge for 0% overlap. If the overlap is 100% then the single-domain solution is recovered for each of the subdomains.
Right figure shows linear convergence rate of dynamic Schwarz implementation (for small overlap fraction of 0.2%).
Some Performance Results

## Slide 83
Appendix. Torsion
Nonlinear elastic bar (Neohookean material model) subjected to a high degree of torsion.
The domain is .
We evaluate dynamic Schwarz with 2 subdomains: .
Time-discretizations: Newmark-Beta (implicit, explicit) with same .
Meshes: hexes, composite tet 10s.

## Slide 84
Appendix. Torsion
Schwarz and single-domain results agree to almost machine-precision!
Conformal Hex + Hex Coupling
Each subdomain discretized using uniform hex mesh with , and advanced in time using implicit Newmark-Beta scheme with 1e-6.
Results compared to single-domain solution on mesh conformal with Schwarz domain meshes.
Displacement relative errors at final time (T=0.002)
Velocity relative errors at final time (T=0.002)

## Slide 85
Appendix. Torsion
Hex + Composite Tet 10 Coupling
Coupling of composite tet 10s + explicit Newmark with consistent mass in with hexes + implicit Newmark in
Reference solution is computed on fine hex mesh + implicit Newmark
Movie of |displacement|
Left: Single-domain,
Right: Schwarz
No dynamic artifacts!
Relative error <1% and does not grow in time!

## Slide 86
Appendix. Torsion
Convergence behavior of the dynamic Schwarz algorithm for the torsion problem for small overlap volume fraction (2%) in which each subdomain is discretized using a hexahedral mesh. The plot shows that a linear convergence rate is achieved.
Some Performance Results

## Slide 87
Single
Schwarz
Appendix. Bolted Joint Problem
y-displacement

## Slide 88
Single
Schwarz
z-displacement
Appendix. Bolted Joint Problem