## Slide 1
A minimal subspace rotation approach for obtaining stable & accurate low-order projection-based reduced order models for nonlinear compressible flow
I. Tezaur1, M. Balajewicz2
1 Quantitative Modeling & Analysis Department, Sandia National Laboratories
2 Aerospace Engineering Department, University of Illinois Urbana-Champaign
ECCOMAS 2016 Crete, Greece June 6-10, 2016
SAND2016-4892C

## Slide 2
Outline
Motivation
2. Projection-based model order reduction
3. Accounting for modal truncation
  Traditional linear eddy-viscosity approach
  New proposed approach via subspace rotation
Applications
  High angle of attack laminar airfoil
  Low Reynolds number channel driven cavity
  Moderate Reynolds number channel driven cavity
Summary
6. Future work
7. References
SAND2016-4892C

## Slide 3
Outline
Motivation
2. Projection-based model order reduction
3. Accounting for modal truncation
  Traditional linear eddy-viscosity approach
  New proposed approach via subspace rotation
Applications
  High angle of attack laminar airfoil
  Low Reynolds number channel driven cavity
  Moderate Reynolds number channel driven cavity
Summary
6. Future work
7. References
SAND2016-4892C

## Slide 4
Motivation
Targeted application: compressible fluid flow (e.g., captive-carry)
SAND2016-4892C

## Slide 5
Motivation
Targeted application: compressible fluid flow (e.g., captive-carry)
Majority of fluid MOR approaches in the literature are for incompressible flow.
SAND2016-4892C

## Slide 6
Motivation
Targeted application: compressible fluid flow (e.g., captive-carry)
Majority of fluid MOR approaches in the literature are for incompressible flow.
There has been some on MOR for compressible flows.
SAND2016-4892C

## Slide 7
Motivation
Targeted application: compressible fluid flow (e.g., captive-carry)
Majority of fluid MOR approaches in the literature are for incompressible flow.
There has been some on MOR for compressible flows.
  Energy-based inner products: Rowley et al., 2004 (isentropic); Barone et al., 2007 (linear); Serre et al., 2012 (linear); Kalashnikova et al., 2014 (nonlinear).
SAND2016-4892C

## Slide 8
Motivation
Targeted application: compressible fluid flow (e.g., captive-carry)
Majority of fluid MOR approaches in the literature are for incompressible flow.
There has been some on MOR for compressible flows.
  Energy-based inner products: Rowley et al., 2004 (isentropic); Barone et al., 2007 (linear); Serre et al., 2012 (linear); Kalashnikova et al., 2014 (nonlinear).
  GNAT method/Petrov-Galerkin projection: Carlberg et al., 2014 (nonlinear).
SAND2016-4892C

## Slide 9
Motivation
Targeted application: compressible fluid flow (e.g., captive-carry)
Majority of fluid MOR approaches in the literature are for incompressible flow.
There has been some on MOR for compressible flows.
  Energy-based inner products: Rowley et al., 2004 (isentropic); Barone et al., 2007 (linear); Serre et al., 2012 (linear); Kalashnikova et al., 2014 (nonlinear).
  GNAT method/Petrov-Galerkin projection: Carlberg et al., 2014 (nonlinear).
MOR for nonlinear, compressible fluid flows is still in its infancy!
SAND2016-4892C

## Slide 10
Projection-based model order reduction
Snapshot matrix: , …,
SVD:
Truncation: )
# of dofs in high-fidelity simulation
# of snapshots
# of dofs in ROM
(, )
POD/Galerkin Method to Model Order Reduction
SAND2016-4892C
Notes: Add equation numbers (1) and (2)!

## Slide 11
Projection-based model order reduction
Governing equations
3D compressible Navier-Stokes equations in primitive specific volume form:
(1)
[PDEs]
SAND2016-4892C
Notes: Add equation numbers (1) and (2)!

## Slide 12
Projection-based model order reduction
Governing equations
3D compressible Navier-Stokes equations in primitive specific volume form:
(1)
Spectral discretization Galerkin projection applied to (1) yields a system of coupled quadratic ODEs:
(2)
[ROM]
[PDEs]
where and for all
SAND2016-4892C
Notes: Add equation numbers (1) and (2)!

## Slide 13
Projection-based model order reduction
Summary of technical challenges
Projection-based MOR necessitates truncation.
SAND2016-4892C

## Slide 14
Projection-based model order reduction
Summary of technical challenges
Projection-based MOR necessitates truncation.
POD is, by definition and design, biased towards the large, energy producing scales of the flow (i.e., modes with large POD eigenvalues).
SAND2016-4892C

## Slide 15
Projection-based model order reduction
Summary of technical challenges
Projection-based MOR necessitates truncation.
POD is, by definition and design, biased towards the large, energy producing scales of the flow (i.e., modes with large POD eigenvalues).
Truncated/unresolved modes are negligible form a data compression point of view (i.e., small POD eigenvalues) but are crucial for the dynamical equations.
SAND2016-4892C

## Slide 16
Projection-based model order reduction
Summary of technical challenges
Projection-based MOR necessitates truncation.
POD is, by definition and design, biased towards the large, energy producing scales of the flow (i.e., modes with large POD eigenvalues).
Truncated/unresolved modes are negligible form a data compression point of view (i.e., small POD eigenvalues) but are crucial for the dynamical equations.
For fluid flow applications, higher-order modes are associated with energy dissipation low-dimensional ROMs are often inaccurate and sometimes unstable.
SAND2016-4892C

## Slide 17
Projection-based model order reduction
Summary of technical challenges
Projection-based MOR necessitates truncation.
POD is, by definition and design, biased towards the large, energy producing scales of the flow (i.e., modes with large POD eigenvalues).
Truncated/unresolved modes are negligible form a data compression point of view (i.e., small POD eigenvalues) but are crucial for the dynamical equations.
For fluid flow applications, higher-order modes are associated with energy dissipation low-dimensional ROMs are often inaccurate and sometimes unstable.
For a ROM to be stable and accurate, the truncated/unresolved subspace must be accounted for.
SAND2016-4892C

## Slide 18
Projection-based model order reduction
Summary of technical challenges
Projection-based MOR necessitates truncation.
POD is, by definition and design, biased towards the large, energy producing scales of the flow (i.e., modes with large POD eigenvalues).
Truncated/unresolved modes are negligible form a data compression point of view (i.e., small POD eigenvalues) but are crucial for the dynamical equations.
For fluid flow applications, higher-order modes are associated with energy dissipation low-dimensional ROMs are often inaccurate and sometimes unstable.
For a ROM to be stable and accurate, the truncated/unresolved subspace must be accounted for.
Turbulence Modeling
(traditional approach)
Subspace Rotation
(our approach)
SAND2016-4892C

## Slide 19
Outline
Motivation
2. Projection-based model order reduction
3. Accounting for modal truncation
  Traditional linear eddy-viscosity approach
  New proposed approach via subspace rotation
Applications
  High angle of attack laminar airfoil
  Low Reynolds number channel driven cavity
  Moderate Reynolds number channel driven cavity
Summary
6. Future work
7. References
SAND2016-4892C

## Slide 20
Outline
Motivation
2. Projection-based model order reduction
3. Accounting for modal truncation
  Traditional linear eddy-viscosity approach
  New proposed approach via subspace rotation
Applications
  High angle of attack laminar airfoil
  Low Reynolds number channel driven cavity
  Moderate Reynolds number channel driven cavity
Summary
6. Future work
7. References
SAND2016-4892C

## Slide 21
Accounting for modal truncation
Traditional linear eddy-viscosity approach
Dissipative dynamics of truncated higher-order modes are modeled using an additional linear term:
SAND2016-4892C

## Slide 22
Accounting for modal truncation
Traditional linear eddy-viscosity approach
Dissipative dynamics of truncated higher-order modes are modeled using an additional linear term:
SAND2016-4892C

## Slide 23
Accounting for modal truncation
Traditional linear eddy-viscosity approach
Dissipative dynamics of truncated higher-order modes are modeled using an additional linear term:
is designed to decrease magnitude of positive eigenvalues and increase magnitude of negative eigenvalues of (for stability).
SAND2016-4892C

## Slide 24
Accounting for modal truncation
Traditional linear eddy-viscosity approach
Dissipative dynamics of truncated higher-order modes are modeled using an additional linear term:
is designed to decrease magnitude of positive eigenvalues and increase magnitude of negative eigenvalues of (for stability).
Disadvantages of this approach:
SAND2016-4892C

## Slide 25
Accounting for modal truncation
Traditional linear eddy-viscosity approach
Dissipative dynamics of truncated higher-order modes are modeled using an additional linear term:
is designed to decrease magnitude of positive eigenvalues and increase magnitude of negative eigenvalues of (for stability).
Disadvantages of this approach:
  Additional term destroys consistency between ROM and Navier-Stokes equations.
SAND2016-4892C

## Slide 26
Accounting for modal truncation
Traditional linear eddy-viscosity approach
Dissipative dynamics of truncated higher-order modes are modeled using an additional linear term:
is designed to decrease magnitude of positive eigenvalues and increase magnitude of negative eigenvalues of (for stability).
Disadvantages of this approach:
  Additional term destroys consistency between ROM and Navier-Stokes equations.
  Calibration is necessary to derive optimal and optimal value is flow dependent.
SAND2016-4892C

## Slide 27
Accounting for modal truncation
Traditional linear eddy-viscosity approach
Dissipative dynamics of truncated higher-order modes are modeled using an additional linear term:
is designed to decrease magnitude of positive eigenvalues and increase magnitude of negative eigenvalues of (for stability).
Disadvantages of this approach:
  Additional term destroys consistency between ROM and Navier-Stokes equations.
  Calibration is necessary to derive optimal and optimal value is flow dependent.
  Inherently a linear model cannot be expected to perform well for all classes of problems (e.g., nonlinear).
SAND2016-4892C

## Slide 28
Outline
Motivation
2. Projection-based model order reduction
3. Accounting for modal truncation
  Traditional linear eddy-viscosity approach
  New proposed approach via subspace rotation
Applications
  High angle of attack laminar airfoil
  Low Reynolds number channel driven cavity
  Moderate Reynolds number channel driven cavity
Summary
6. Future work
7. References
SAND2016-4892C

## Slide 29
Accounting for modal truncation
Proposed new approach
Instead of modeling truncation via additional linear term, model the truncation a priori by “rotating” the projection subspace into a more dissipative regime
SAND2016-4892C

## Slide 30
Accounting for modal truncation
Proposed new approach
Instead of modeling truncation via additional linear term, model the truncation a priori by “rotating” the projection subspace into a more dissipative regime
Illustrative example
Standard approach: retain only the most energetic POD modes, i.e., , ,
Proposed approach: choose some higher order basis modes to increase dissipation, i.e., , ,
SAND2016-4892C

## Slide 31
Accounting for modal truncation
Proposed new approach
(3)
Instead of modeling truncation via additional linear term, model the truncation a priori by “rotating” the projection subspace into a more dissipative regime
Illustrative example
Standard approach: retain only the most energetic POD modes, i.e., , ,
Proposed approach: choose some higher order basis modes to increase dissipation, i.e., , ,
More generally: approximate the solution using a linear superposition of (with ) most energetic modes:
,
where is an orthonormal () “rotation” matrix.
SAND2016-4892C

## Slide 32
Accounting for modal truncation
Find such that:
  New modes remain good approximations of the flow.
  2. New modes produce stable and accurate ROMs.
Goals of proposed new approach
SAND2016-4892C

## Slide 33
Accounting for modal truncation
Goals of proposed new approach
Find such that:
  New modes remain good approximations of the flow.
  2. New modes produce stable and accurate ROMs.
We formulate and solve a constrained optimization problem for :
where is the Stiefel manifold.
SAND2016-4892C

## Slide 34
Accounting for modal truncation
Goals of proposed new approach
Find such that:
  New modes remain good approximations of the flow.
  2. New modes produce stable and accurate ROMs.
We formulate and solve a constrained optimization problem for :
where is the Stiefel manifold.
Once is found, the result is a system of the form (2) with:
,
SAND2016-4892C

## Slide 35
Accounting for modal truncation
Objective function
We have considered two objectives in (5):
(5)
SAND2016-4892C

## Slide 36
Accounting for modal truncation
Objective function
We have considered two objectives in (5):
  Minimize subspace rotation
(5)
(6)
SAND2016-4892C

## Slide 37
Accounting for modal truncation
Objective function
We have considered two objectives in (5):
  Minimize subspace rotation
(5)
Maximize resolved turbulent kinetic energy (TKE)
(6)
(7)
SAND2016-4892C

## Slide 38
Accounting for modal truncation
Objective function
We have considered two objectives in (5):
  Minimize subspace rotation
(5)
Maximize resolved turbulent kinetic energy (TKE)
TKE objective (7) comes from earlier work (Balajewicz et al., 2013) involving stabilization of incompressible flow ROMs
  POD modes associated with low KE are important dynamically even though they contribute little to overall energy of the fluid flow.
(6)
(7)
SAND2016-4892C

## Slide 39
Accounting for modal truncation
Objective function
We have considered two objectives in (5):
  Minimize subspace rotation
(5)
Maximize resolved turbulent kinetic energy (TKE)
Numerical experiments reveal objective (6) produces better results than objective (7) for compressible flow.
(6)
(7)
SAND2016-4892C

## Slide 40
Accounting for modal truncation
Constraint
We use the traditional linear eddy-viscosity closure model ansatz for the constraint in (5):
(5)
(8)
SAND2016-4892C

## Slide 41
Accounting for modal truncation
Constraint
We use the traditional linear eddy-viscosity closure model ansatz for the constraint in (5):
(5)
Specifically, constraint (8) involves overall balance between linear energy production and dissipation.
  proxy for the balance between linear energy production and energy dissipation.
(8)
SAND2016-4892C

## Slide 42
Accounting for modal truncation
Constraint
We use the traditional linear eddy-viscosity closure model ansatz for the constraint in (5):
(5)
Specifically, constraint (8) involves overall balance between linear energy production and dissipation.
  proxy for the balance between linear energy production and energy dissipation.
Constraint comes from property that averaged total power ( energy transfer) has to vanish.
(8)
SAND2016-4892C

## Slide 43
Accounting for modal truncation
Minimal subspace rotation: trace minimization on Stiefel manifold
  : proxy for the balance between linear energy production and energy dissipation (calculated iteratively using modal energy).
is the Stiefel manifold.
Equation (9) is solved efficiently offline using the method of Lagrange multipliers (Manopt MATLAB toolbox).
See (Balajewicz, Tezaur, Dowell, 2016) and Appendix slide for Algorithm.
(9)
SAND2016-4892C

## Slide 44
Accounting for modal truncation
Remarks
Proposed approach may be interpreted as an a priori consistent formulation of the eddy-viscosity turbulence modeling approach.
SAND2016-4892C

## Slide 45
Accounting for modal truncation
Remarks
Proposed approach may be interpreted as an a priori consistent formulation of the eddy-viscosity turbulence modeling approach.
Advantages of proposed approach:
SAND2016-4892C

## Slide 46
Accounting for modal truncation
Remarks
Proposed approach may be interpreted as an a priori consistent formulation of the eddy-viscosity turbulence modeling approach.
Advantages of proposed approach:
  Retains consistency between ROM and Navier-Stokes equations no additional turbulence terms required.
SAND2016-4892C

## Slide 47
Accounting for modal truncation
Remarks
Proposed approach may be interpreted as an a priori consistent formulation of the eddy-viscosity turbulence modeling approach.
Advantages of proposed approach:
  Retains consistency between ROM and Navier-Stokes equations no additional turbulence terms required.
  Inherently a nonlinear model should be expected to outperform linear models.
SAND2016-4892C

## Slide 48
Accounting for modal truncation
Remarks
Proposed approach may be interpreted as an a priori consistent formulation of the eddy-viscosity turbulence modeling approach.
Advantages of proposed approach:
  Retains consistency between ROM and Navier-Stokes equations no additional turbulence terms required.
  Inherently a nonlinear model should be expected to outperform linear models.
  Works with any basis and Petrov-Galerkin projection.
SAND2016-4892C

## Slide 49
Accounting for modal truncation
Remarks
Proposed approach may be interpreted as an a priori consistent formulation of the eddy-viscosity turbulence modeling approach.
Advantages of proposed approach:
  Retains consistency between ROM and Navier-Stokes equations no additional turbulence terms required.
  Inherently a nonlinear model should be expected to outperform linear models.
  Works with any basis and Petrov-Galerkin projection.
Disadvantages of proposed approach:
SAND2016-4892C

## Slide 50
Accounting for modal truncation
Remarks
Proposed approach may be interpreted as an a priori consistent formulation of the eddy-viscosity turbulence modeling approach.
Advantages of proposed approach:
  Retains consistency between ROM and Navier-Stokes equations no additional turbulence terms required.
  Inherently a nonlinear model should be expected to outperform linear models.
  Works with any basis and Petrov-Galerkin projection.
Disadvantages of proposed approach:
  Off-line calibration of free parameter is required.
SAND2016-4892C

## Slide 51
Accounting for modal truncation
Remarks
Proposed approach may be interpreted as an a priori consistent formulation of the eddy-viscosity turbulence modeling approach.
Advantages of proposed approach:
  Retains consistency between ROM and Navier-Stokes equations no additional turbulence terms required.
  Inherently a nonlinear model should be expected to outperform linear models.
  Works with any basis and Petrov-Galerkin projection.
Disadvantages of proposed approach:
  Off-line calibration of free parameter is required.
  Stability cannot be proven like for incompressible case.
SAND2016-4892C

## Slide 52
Outline
Motivation
2. Projection-based model order reduction
3. Accounting for modal truncation
  Traditional linear eddy-viscosity approach
  New proposed approach via subspace rotation
Applications
  High angle of attack laminar airfoil
  Low Reynolds number channel driven cavity
  Moderate Reynolds number channel driven cavity
Summary
6. Future work
7. References
SAND2016-4892C

## Slide 53
Outline
Motivation
2. Projection-based model order reduction
3. Accounting for modal truncation
  Traditional linear eddy-viscosity approach
  New proposed approach via subspace rotation
Applications
  High angle of attack laminar airfoil
  Low Reynolds number channel driven cavity
  Moderate Reynolds number channel driven cavity
Summary
6. Future work
7. References
SAND2016-4892C

## Slide 54
Applications
High angle of attack laminar airfoil
2D flow around an inclined NACA0012 airfoil at Mach 0.7,
Re = 500, Pr = 0.72, AOA = 20° ROM (86% snapshot energy).
Figure 1: Contours of velocity magnitude at time of final snapshot.
SAND2016-4892C

## Slide 55
Applications
High angle of attack laminar airfoil
Figure 2: (a) evolution of modal energy, (b) phase plot of first and second temporal basis and , (c) illustration of stabilizing rotation showing that rotation is small:
Minimizing subspace rotation:
-- standard ROM (n=4)
stabilized ROM (n=p=4)
DNS
SAND2016-4892C

## Slide 56
Applications
High angle of attack laminar airfoil
Figure 3: High angle of attack laminar airfoil contours of velocity magnitude at time of final snapshot.
Standard ROM ()
Stabilized ROM ()
DNS
Minimizing subspace rotation:
SAND2016-4892C

## Slide 57
Outline
Motivation
2. Projection-based model order reduction
3. Accounting for modal truncation
  Traditional linear eddy-viscosity approach
  New proposed approach via subspace rotation
Applications
  High angle of attack laminar airfoil
  Low Reynolds number channel driven cavity
  Moderate Reynolds number channel driven cavity
Summary
6. Future work
7. References
SAND2016-4892C

## Slide 58
Applications
Channel driven cavity: low Reynolds number case
Flow over square cavity at Mach 0.6, Re = 1453.9, Pr = 0.72 ROM (91% snapshot energy).
Figure 4: Domain and mesh for viscous channel driven cavity problem.
SAND2016-4892C

## Slide 59
Channel driven cavity: low Reynolds number case
Applications
Figure 5: (a) evolution of modal energy, (b) phase plot of first and second temporal basis and , (c) illustration of stabilizing rotation showing that rotation is small:
Minimizing subspace rotation:
-- standard ROM (n=4)
stabilized ROM (n=p=4)
DNS
SAND2016-4892C

## Slide 60
Applications
Channel driven cavity: low Reynolds number case
Figure 6: Pressure power spectral density (PSD) at location ; stabilized ROM minimizes subspace rotation.
Minimizing subspace rotation:
-- standard ROM (n=4)
stabilized ROM (n=p=4)
DNS
SAND2016-4892C

## Slide 61
Applications
Channel driven cavity: low Reynolds number case
Figure 7: Pressure power spectral density (PSD) at location ; stabilized ROM maximizes resolved TKE.
-- standard ROM (n=4)
stabilized ROM (n=p=4)
DNS
Maximizing resolved TKE:
SAND2016-4892C

## Slide 62
Applications
Channel driven cavity: low Reynolds number case
Figure 8: Channel driven cavity Re 1500 contours of -velocity at time of final snapshot.
Standard ROM ()
Stabilized ROM ()
DNS
Minimizing subspace rotation:
SAND2016-4892C

## Slide 63
Outline
Motivation
2. Projection-based model order reduction
3. Accounting for modal truncation
  Traditional linear eddy-viscosity approach
  New proposed approach via subspace rotation
Applications
  High angle of attack laminar airfoil
  Low Reynolds number channel driven cavity
  Moderate Reynolds number channel driven cavity
Summary
6. Future work
7. References
SAND2016-4892C

## Slide 64
Applications
Channel driven cavity: moderate Reynolds number case
Figure 9: Domain and mesh for viscous channel driven cavity problem.
Flow over square cavity at Mach 0.6, Re = 5452.1, Pr = 0.72 ROM (71.8% snapshot energy).
SAND2016-4892C

## Slide 65
Applications
Channel driven cavity: moderate Reynolds number case
Figure 10: (a) evolution of modal energy, (b) illustration of stabilizing rotation showing that rotation is small:
-- standard ROM (n=20)
stabilized ROM (n=p=20)
DNS
Minimizing subspace rotation:
SAND2016-4892C

## Slide 66
Channel driven cavity: moderate Reynolds number case
Applications
Power and phase lag at fundamental frequency, and first two super harmonics are predicted accurately using the fine-tuned ROM ( stabilized ROM, DNS)
Figure 11: Pressure cross PSD of of and where
Minimizing subspace rotation:
stabilized ROM (n=p=20)
DNS
SAND2016-4892C

## Slide 67
Applications
Channel driven cavity: moderate Reynolds number case
Figure 12: Channel driven cavity Re 5500 contours of -velocity at time of final snapshot.
Standard ROM ()
Stabilized ROM (20)
DNS
Minimizing subspace rotation:
SAND2016-4892C

## Slide 68
Applications
CPU times (CPU-hours) for offline and online computations*
* For minimizing subspace rotation.
Procedure | Airfoil | Low Re Cavity | Moderate Re Cavity
FOM # of DOF | 360,000 | 288,250 | 243,750
Time-integration of FOM | 7.8 hrs | 72 hrs | 179 hrs
Basis construction (size ROM) | 0.16 hrs | 0.88 hrs | 3.44 hrs
Galerkin projection (size ROM) | 0.74 hrs | 5.44 hrs | 14.8 hrs
Stabilization | 28 sec | 14 sec | 170 sec
ROM # of DOF | 4 | 4 | 20
Time-integration of ROM | 0.31 sec | 0.16 sec | 0.83 sec
Online computational speed-up | 9.1e4 | 1.6e6 | 7.8e5
Procedure | Airfoil | Low Re Cavity | Moderate Re Cavity
FOM # of DOF | 360,000 | 288,250 | 243,750
Time-integration of FOM | 7.8 hrs | 72 hrs | 179 hrs
 | 0.16 hrs | 0.88 hrs | 3.44 hrs
 | 0.74 hrs | 5.44 hrs | 14.8 hrs
Stabilization | 28 sec | 14 sec | 170 sec
ROM # of DOF | 4 | 4 | 20
Time-integration of ROM | 0.31 sec | 0.16 sec | 0.83 sec
Online computational speed-up | 9.1e4 | 1.6e6 | 7.8e5
online
offline
SAND2016-4892C

## Slide 69
Applications
CPU times (CPU-hours) for offline and online computations*
Stabilization is fast ((sec) or (min)).
* For minimizing subspace rotation.
Procedure | Airfoil | Low Re Cavity | Moderate Re Cavity
FOM # of DOF | 360,000 | 288,250 | 243,750
Time-integration of FOM | 7.8 hrs | 72 hrs | 179 hrs
Basis construction (size ROM) | 0.16 hrs | 0.88 hrs | 3.44 hrs
Galerkin projection (size ROM) | 0.74 hrs | 5.44 hrs | 14.8 hrs
Stabilization | 28 sec | 14 sec | 170 sec
ROM # of DOF | 4 | 4 | 20
Time-integration of ROM | 0.31 sec | 0.16 sec | 0.83 sec
Online computational speed-up | 9.1e4 | 1.6e6 | 7.8e5
Procedure | Airfoil | Low Re Cavity | Moderate Re Cavity
FOM # of DOF | 360,000 | 288,250 | 243,750
Time-integration of FOM | 7.8 hrs | 72 hrs | 179 hrs
 | 0.16 hrs | 0.88 hrs | 3.44 hrs
 | 0.74 hrs | 5.44 hrs | 14.8 hrs
Stabilization | 28 sec | 14 sec | 170 sec
ROM # of DOF | 4 | 4 | 20
Time-integration of ROM | 0.31 sec | 0.16 sec | 0.83 sec
Online computational speed-up | 9.1e4 | 1.6e6 | 7.8e5
online
offline
SAND2016-4892C

## Slide 70
Applications
CPU times (CPU-hours) for offline and online computations*
Stabilization is fast ((sec) or (min)).
Significant online computational speed-up!
* For minimizing subspace rotation.
Procedure | Airfoil | Low Re Cavity | Moderate Re Cavity
FOM # of DOF | 360,000 | 288,250 | 243,750
Time-integration of FOM | 7.8 hrs | 72 hrs | 179 hrs
Basis construction (size ROM) | 0.16 hrs | 0.88 hrs | 3.44 hrs
Galerkin projection (size ROM) | 0.74 hrs | 5.44 hrs | 14.8 hrs
Stabilization | 28 sec | 14 sec | 170 sec
ROM # of DOF | 4 | 4 | 20
Time-integration of ROM | 0.31 sec | 0.16 sec | 0.83 sec
Online computational speed-up | 9.1e4 | 1.6e6 | 7.8e5
Procedure | Airfoil | Low Re Cavity | Moderate Re Cavity
FOM # of DOF | 360,000 | 288,250 | 243,750
Time-integration of FOM | 7.8 hrs | 72 hrs | 179 hrs
 | 0.16 hrs | 0.88 hrs | 3.44 hrs
 | 0.74 hrs | 5.44 hrs | 14.8 hrs
Stabilization | 28 sec | 14 sec | 170 sec
ROM # of DOF | 4 | 4 | 20
Time-integration of ROM | 0.31 sec | 0.16 sec | 0.83 sec
Online computational speed-up | 9.1e4 | 1.6e6 | 7.8e5
online
offline
SAND2016-4892C

## Slide 71
Outline
Motivation
2. Projection-based model order reduction
3. Accounting for modal truncation
  Traditional linear eddy-viscosity approach
  New proposed approach via subspace rotation
Applications
  High angle of attack laminar airfoil
  Low Reynolds number channel driven cavity
  Moderate Reynolds number channel driven cavity
Summary
6. Future work
7. References
SAND2016-4892C

## Slide 72
Summary
We have developed a non-intrusive approach for stabilizing and fine-tuning projection-based ROMs for compressible flows.
The standard POD modes are “rotated” into a more dissipative regime to account for the dynamics in the higher order modes truncated by the standard POD method.
The new approach is consistent and does not require the addition of empirical turbulence model terms unlike traditional approaches.
Mathematically, the approach is formulated as a quadratic matrix program on the Stiefel manifold.
The constrained minimization problem is solved offline and small enough to be solved in MATLAB.
The method is demonstrated on several compressible flow problems and shown to deliver stable and accurate ROMs.
SAND2016-4892C

## Slide 73
Outline
Motivation
2. Projection-based model order reduction
3. Accounting for modal truncation
  Traditional linear eddy-viscosity approach
  New proposed approach via subspace rotation
Applications
  High angle of attack laminar airfoil
  Low Reynolds number channel driven cavity
  Moderate Reynolds number channel driven cavity
Summary
6. Future work
7. References
SAND2016-4892C

## Slide 74
Future work
Application to higher Reynolds number problems.
Extension of the proposed approach to problems with generic nonlinearities, where the ROM involves some form of hyper-reduction (e.g., DEIM, gappy POD).
Extension of the method to minimal-residual-based nonlinear ROMs.
Extension of the method to predictive applications, e.g., problems with varying Reynolds number and/or Mach number.
Selecting different goal-oriented objectives and constraints in our optimization problem:
e.g.,
  Maximize parametric robustness: .
  ODE constraints:
SAND2016-4892C

## Slide 75
Outline
Motivation
2. Projection-based model order reduction
3. Accounting for modal truncation
  Traditional linear eddy-viscosity approach
  New proposed approach via subspace rotation
Applications
  High angle of attack laminar airfoil
  Low Reynolds number channel driven cavity
  Moderate Reynolds number channel driven cavity
Summary
6. Future work
7. References
SAND2016-4892C

## Slide 76
References
SAND2016-4892C

## Slide 77
Outline
Motivation
2. Projection-based model order reduction
3. Accounting for modal truncation
  Traditional linear eddy-viscosity approach
  New proposed approach via subspace rotation
4. Applications
  Low Reynolds number channel driven cavity
  Moderate Reynolds number channel driven cavity
Summary
6. Future work
7. References
8. Appendix
SAND2016-4892C

## Slide 78
Appendix: Accounting for modal truncation
Stabilization algorithm: returns stabilizing rotation matrix .
SAND2016-4892C