## Slide 1
Large-scale Deterministic Inversion and Bayesian Calibration in Land-Ice Modeling
I. Tezaur1, J. Jakeman1, M. Eldred1, M. Perego1, S. Price2, A. Salinger1
1 Sandia National Laboratories, Albuquerque, NM and Livermore, CA, USA.
2 Los Alamos National Laboratory, Los Alamos, NM, USA.
USNCCM 2017 Montreal, Quebec July 17-20, 2017
SAND2017-6948C
Sandia National Laboratories is a multi-mission laboratory managed and operated by National Technology and Engineering Solutions of Sandia, LLC., a wholly owned subsidiary of Honeywell International, Inc., for the U.S. Department of Energy’s National Nuclear Security Administration under contract DE-NA0003525.

## Slide 2
Outline
Background.
  PISCEES project for land-ice modeling.
  Land-ice model.
UQ problem definition.
Inversion/calibration.
  Deterministic inversion.
  Bayesian inference.
Summary & future work.

## Slide 3
Outline
Background.
  PISCEES project for land-ice modeling.
  Land-ice model.
UQ problem definition.
Inversion/calibration.
  Deterministic inversion.
  Bayesian inference.
Summary & future work.

## Slide 4: PISCEES Project for Land-Ice Modeling
  Sandia’s Role in the PISCEES Project: to develop and support a robust and scalable land ice solver based on the “First-Order” (FO) Stokes equations Albany/FELIX*
Requirements for Albany/FELIX:
  Unstructured grid finite elements.
  Scalable, fast and robust.
  Verified and validated.
  Portable to new architecture machines.
  Advanced analysis capabilities: deterministic inversion, calibration, uncertainty quantification.
*Finite Elements for Land Ice eXperiments
As part of ACME DOE Earth System Model, solver will provide actionable predictions of 21st century sea-level change (including uncertainty bounds).
  “PISCEES” = Predicting Ice Sheet Climate Evolution at Extreme Scales
  5 year SciDAC3 project began in June 2012; proposal for 5 year continuation project submitted to SciDAC4 call.

## Slide 5: PISCEES Project for Land-Ice Modeling
  Sandia’s Role in the PISCEES Project: to develop and support a robust and scalable land ice solver based on the “First-Order” (FO) Stokes equations Albany/FELIX*
Requirements for Albany/FELIX:
  Unstructured grid finite elements.
  Scalable, fast and robust.
  Verified and validated.
  Portable to new architecture machines.
  Advanced analysis capabilities: deterministic inversion, calibration, uncertainty quantification.
*Finite Elements for Land Ice eXperiments
  “PISCEES” = Predicting Ice Sheet Climate Evolution at Extreme Scales
  5 year SciDAC3 project began in June 2012; proposal for 5 year continuation project submitted to SciDAC4 call.
This talk
As part of ACME DOE Earth System Model, solver will provide actionable predictions of 21st century sea-level change (including uncertainty bounds).

## Slide 6
Outline
Background.
  PISCEES project for land-ice modeling.
  Land-ice model.
UQ problem definition.
Inversion/calibration.
  Deterministic inversion.
  Bayesian inference.
Summary & future work.

## Slide 7
The First-Order Stokes Model
Ice behaves like a very viscous shear-thinning fluid (similar to lava flow).
Quasi-static model with momentum balance given by “First-Order” Stokes PDEs: “nice” elliptic approximation* to Stokes’ flow equations.
, in
Albany/FELIX
Relevant boundary conditions:
  Stress-free BC: on
  Floating ice BC:
  Basal sliding BC:
  Basal boundary
)
Lateral boundary
Ice sheet
Viscosity is nonlinear function given by “Glen’s law”:
  Surface boundary
*Assumption: aspect ratio is small and normals to upper/lower surfaces are almost vertical.
  =
  , on

## Slide 8
The First-Order Stokes Model
Ice behaves like a very viscous shear-thinning fluid (similar to lava flow).
Quasi-static model with momentum balance given by “First-Order” Stokes PDEs: “nice” elliptic approximation* to Stokes’ flow equations.
, in
Albany/FELIX
Relevant boundary conditions:
  Stress-free BC: on
  Floating ice BC:
  Basal sliding BC:
  Basal boundary
)
Lateral boundary
Ice sheet
Viscosity is nonlinear function given by “Glen’s law”:
  Surface boundary
*Assumption: aspect ratio is small and normals to upper/lower surfaces are almost vertical.
  =
  , on

## Slide 9
The First-Order Stokes Model
Ice behaves like a very viscous shear-thinning fluid (similar to lava flow).
Quasi-static model with momentum balance given by “First-Order” Stokes PDEs: “nice” elliptic approximation* to Stokes’ flow equations.
, in
Albany/FELIX
Relevant boundary conditions:
  Stress-free BC: on
  Floating ice BC:
  Basal sliding BC:
  Basal boundary
)
Lateral boundary
Ice sheet
Viscosity is nonlinear function given by “Glen’s law”:
  Surface boundary
*Assumption: aspect ratio is small and normals to upper/lower surfaces are almost vertical.
  =
  , on

## Slide 10: Thickness & Temperature Equations
Model for evolution of the boundaries (thickness evolution equation):
where = vertically averaged velocity, = surface mass
balance (conservation of mass).
Temperature equation (advection-diffusion):
(energy balance).
Flow factor in Glen’s law depends on temperature : .
Ice sheet grows/retreats depending on thickness .
Ice-covered (“active”) cells shaded in white
()

## Slide 11
Outline
Background.
  PISCEES project for land-ice modeling.
  Land-ice model.
UQ problem definition.
Inversion/calibration.
  Deterministic inversion.
  Bayesian inference.
Summary & future work.

## Slide 12
Uncertainty Quantification Problem Definition
QoI in Ice Sheet Modeling: total ice mass loss/gain during 21st century sea level change prediction.

## Slide 13
Uncertainty Quantification Problem Definition
QoI in Ice Sheet Modeling: total ice mass loss/gain during 21st century sea level change prediction.
Sources of uncertainty affecting this QoI include:
  Climate forcings (e.g., surface mass balance).
  Basal friction ().
  Ice sheet thickness (h).
  Geothermal heat flux.
  Model parameters (e.g., Glen’s flow law exponent).
  Basal boundary
)
Ice sheet
= Glen’s law exponent
thickness
(h)
  Basal sliding BC:
  , on

## Slide 14
Uncertainty Quantification Problem Definition
QoI in Ice Sheet Modeling: total ice mass loss/gain during 21st century sea level change prediction.
Sources of uncertainty affecting this QoI include:
  Climate forcings (e.g., surface mass balance).
  Basal friction ().
  Ice sheet thickness (h).
  Geothermal heat flux.
  Model parameters (e.g., Glen’s flow law exponent).
  Basal boundary
)
Ice sheet
= Glen’s law exponent
thickness
(h)
  As a first step, we focus on effect of uncertainty in only.
  Basal sliding BC:
  , on

## Slide 15
Uncertainty Quantification Problem Definition
QoI in Ice Sheet Modeling: total ice mass loss/gain during 21st century sea level change prediction.
Sources of uncertainty affecting this QoI include:
  Climate forcings (e.g., surface mass balance).
  Basal friction ().
  Ice sheet thickness (h).
  Geothermal heat flux.
  Model parameters (e.g., Glen’s flow law exponent).
  Basal boundary
)
Ice sheet
= Glen’s law exponent
thickness
(h)
Stage 1:
Estimate ice sheet initial condition (MAP point).
Stage 2:
Update prior uncertainty in ice sheet initial condition
using observational data
and steady state model
Stage 3:
Propagate uncertain initial condition through ice-sheet evolution model
UQ Workflow
  As a first step, we focus on effect of uncertainty in only.
  Basal sliding BC:
  , on

## Slide 16
Uncertainty Quantification Problem Definition
QoI in Ice Sheet Modeling: total ice mass loss/gain during 21st century sea level change prediction.
Sources of uncertainty affecting this QoI include:
  Climate forcings (e.g., surface mass balance).
  Basal friction ().
  Ice sheet thickness (h).
  Geothermal heat flux.
  Model parameters (e.g., Glen’s flow law exponent).
  Basal boundary
)
Ice sheet
= Glen’s law exponent
thickness
(h)
Stage 1:
Estimate ice sheet initial condition (MAP point).
Stage 2:
Update prior uncertainty in ice sheet initial condition
using observational data
and steady state model
Stage 3:
Propagate uncertain initial condition through ice-sheet evolution model
UQ Workflow
Deterministic inversion
Bayesian calibration
  As a first step, we focus on effect of uncertainty in only.
  Basal sliding BC:
  , on
Forward propagation

## Slide 17
Uncertainty Quantification Problem Definition
QoI in Ice Sheet Modeling: total ice mass loss/gain during 21st century sea level change prediction.
Sources of uncertainty affecting this QoI include:
  Climate forcings (e.g., surface mass balance).
  Basal friction ().
  Ice sheet thickness (h).
  Geothermal heat flux.
  Model parameters (e.g., Glen’s flow law exponent).
  Basal boundary
)
Ice sheet
= Glen’s law exponent
thickness
(h)
Stage 1:
Estimate ice sheet initial condition (MAP point).
Stage 2:
Update prior uncertainty in ice sheet initial condition
using observational data
and steady state model
Stage 3:
Propagate uncertain initial condition through ice-sheet evolution model
UQ Workflow
Deterministic inversion
Bayesian calibration
  As a first step, we focus on effect of uncertainty in only.
  Basal sliding BC:
  , on
Forward propagation

## Slide 18
Outline
Background.
  PISCEES project for land-ice modeling.
  Land-ice model.
UQ problem definition.
Inversion/calibration.
  Deterministic inversion.
  Bayesian inference.
Summary & future work.

## Slide 19
Estimation of Ice Sheet Initial Condition
Stage 3:
Propagate uncertain initial condition through ice-sheet evolution model
UQ Workflow
Stage 1:
Estimate ice sheet initial condition (MAP point).
Stage 2:
Update prior uncertainty in ice sheet initial condition
using observational data
and steady state model
matches observations (e.g. surface velocity, temperature, etc.).
matches present-day geometry (elevation, thickness).
is in “equilibrium” with climate forcings (SMB).
Goal: find ice sheet initial state that:

## Slide 20
  β
Ice sheet
Ocean
Bedrock
Available Data & Assumptions
Available data/measurements:
  ice extent and surface topography.
  surface velocity.
  surface mass balance (SMB).
  ice thickness (sparse measurements).
Fields to be estimated:
  ice thickness (allowed to vary but weighted by observational uncertainties).
  basal friction (spatially variable proxy for all basal processes).
Modeling Assumptions:
  ice flow described by nonlinear first-order Stokes equations.
  ice close to mechanical equilibrium.
Sources of data: satellite infrarometry, radar, altimetry, etc.

## Slide 21
Deterministic Inversion
First-Order Stokes PDE-Constrained optimization problem for initial condition*:
s.t. FO Stokes PDEs
surface velocity mismatch
SMB mismatch
thickness mismatch
regularization terms
: computed depth averaged velocity
: ice thickness
: basal sliding friction coefficient
: surface mass balance (SMB)
: regularization term
* Perego, Stadler, Price, JGR, 2014.

## Slide 22
Deterministic Inversion
First-Order Stokes PDE-Constrained optimization problem for initial condition*:
s.t. FO Stokes PDEs
surface velocity mismatch
SMB mismatch
thickness mismatch
regularization terms
: computed depth averaged velocity
: ice thickness
: basal sliding friction coefficient
: surface mass balance (SMB)
: regularization term
Solving FO Stokes PDE-constrained optimization problem for initial condition significantly reduces non-physical model transients!
* Perego, Stadler, Price, JGR, 2014.

## Slide 23
Deterministic Inversion Algorithm & Software
Algorithm | Software
Finite Element Method discretization | Albany
Quasi-Newton optimization (L-BFGS) | ROL
Nonlinear solver (Newton) | NOX
Krylov linear solvers | AztecOO+Ifpack/ML
Some details:
  Regularization: Tikhonov.
  Total derivatives of objective functional computed using adjoints and automatic differentiation (Sacado package of Trilinos).
  Gradient-based optimization: limited memory BFGS initialized with Hessian of regularization terms (ROL) with backtrack linesearch.
First-Order Stokes PDE-Constrained optimization problem for initial condition*:
s.t. FO Stokes PDEs
Solved via embedded adjoint-based PDE-constrained optimization algorithm in Albany/FELIX.
* Perego, Stadler, Price, JGR, 2014.

## Slide 24: Deterministic Inversion: 1km Greenland Initial Condition
|| observed
|| computed
Error in || computed

## Slide 25
Outline
Background.
  PISCEES project for land-ice modeling.
  Land-ice model.
UQ problem definition.
Inversion/calibration.
  Deterministic inversion.
  Bayesian inference.
Summary & future work.

## Slide 26
Bayesian Inference
Stage 3:
Propagate uncertain initial condition through ice-sheet evolution model
UQ Workflow
Stage 1:
Estimate ice sheet initial condition (MAP point).
Stage 2:
Update prior uncertainty in ice sheet initial condition
using observational data
and steady state model
Goal: solve inverse problem for ice sheet initial state but in Bayesian framework

## Slide 27
Bayesian Inference
Stage 3:
Propagate uncertain initial condition through ice-sheet evolution model
UQ Workflow
Stage 1:
Estimate ice sheet initial condition (MAP point).
Stage 2:
Update prior uncertainty in ice sheet initial condition
using observational data
and steady state model
Naïve parameterization: represent each degree of freedom on mesh be an uncertain variable
Goal: solve inverse problem for ice sheet initial state but in Bayesian framework

## Slide 28
Bayesian Inference
Stage 3:
Propagate uncertain initial condition through ice-sheet evolution model
UQ Workflow
Stage 1:
Estimate ice sheet initial condition (MAP point).
Stage 2:
Update prior uncertainty in ice sheet initial condition
using observational data
and steady state model
Naïve parameterization: represent each degree of freedom on mesh be an uncertain variable
Intractable due to curse of dimensionality:
Goal: solve inverse problem for ice sheet initial state but in Bayesian framework

## Slide 29
Bayesian Inference
Stage 3:
Propagate uncertain initial condition through ice-sheet evolution model
UQ Workflow
Stage 1:
Estimate ice sheet initial condition (MAP point).
Stage 2:
Update prior uncertainty in ice sheet initial condition
using observational data
and steady state model
Naïve parameterization: represent each degree of freedom on mesh be an uncertain variable
Intractable due to curse of dimensionality:
Goal: solve inverse problem for ice sheet initial state but in Bayesian framework
  To circumvent this difficulty: assume can be represented in reduced basis (e.g., KLE modes, Hessian eigenvectors*) centered around mean :
* Isaac, Petra, Stadler, Ghattas, JCP, 2015.

## Slide 30
Bayesian Inference
Stage 3:
Propagate uncertain initial condition through ice-sheet evolution model
UQ Workflow
Stage 1:
Estimate ice sheet initial condition (MAP point).
Stage 2:
Update prior uncertainty in ice sheet initial condition
using observational data
and steady state model
Naïve parameterization: represent each degree of freedom on mesh be an uncertain variable
Intractable due to curse of dimensionality:
Goal: solve inverse problem for ice sheet initial state but in Bayesian framework
  To circumvent this difficulty: assume can be represented in reduced basis (e.g., KLE modes, Hessian eigenvectors*) centered around mean :
Mean field = initial condition.
* Isaac, Petra, Stadler, Ghattas, JCP, 2015.

## Slide 31
Bayesian Inference
Stage 3:
Propagate uncertain initial condition through ice-sheet evolution model
UQ Workflow
Stage 1:
Estimate ice sheet initial condition (MAP point).
Stage 2:
Update prior uncertainty in ice sheet initial condition
using observational data
and steady state model
Naïve parameterization: represent each degree of freedom on mesh be an uncertain variable
Intractable due to curse of dimensionality:
Goal: solve inverse problem for ice sheet initial state but in Bayesian framework
  To circumvent this difficulty: assume can be represented in reduced basis (e.g., KLE modes, Hessian eigenvectors*) centered around mean :
Mean field = initial condition.
* Isaac, Petra, Stadler, Ghattas, JCP, 2015.
Deterministic inversion is consistent with Bayesian analog: it is used to find the MAP point of posterior.
Notes: Mean field = 0. Find MAP point of posterior
Using AS to build approximation of subspace.
Can build full Hessian approximation

## Slide 32
Bayesian Inference Assumptions
  Additive Gaussian noise model:
Mismatch functional to be minimized:
Gaussian prior with exponential covariance and mean = .
* Constantine, Kent, Bui-Thanh, SISC, 2016.
Notation*:
= observations
= random params
= deterministic map from params to observables.
Notes: Apply Bayes rule + linearization at MAP point for nonlinear model => Laplace posterior.
New work: Laplace prior.
Covariance is exponential kernel
Mistake: no regularization

## Slide 33
Bayesian Inference Assumptions
  Likelihood is:
Normal Laplace posterior given by:
where
  Additive Gaussian noise model:
Mismatch functional to be minimized:
Gaussian prior with exponential covariance and mean = .
Bayes’ rule
* Constantine, Kent, Bui-Thanh, SISC, 2016.
Notation*:
= observations
= random params
= deterministic map from params to observables.
+ linearization of around
Notes: Apply Bayes rule + linearization at MAP point for nonlinear model => Laplace posterior.
New work: Laplace prior.
Covariance is exponential kernel
Mistake: no regularization

## Slide 34
Bayesian Inference Assumptions
  Likelihood is:
Normal Laplace posterior given by:
where
  Additive Gaussian noise model:
Mismatch functional to be minimized:
Gaussian prior with exponential covariance and mean = .
Bayes’ rule
* Constantine, Kent, Bui-Thanh, SISC, 2016. **Bui-Thanh, Ghattas, Martin, Stadler, SISC, 2013.
Notation*:
= observations
= random params
= deterministic map from params to observables.
Covariance of Gaussian posterior related to inverse of misfit Hessian at MAP point**.
+ linearization of around
Notes: Apply Bayes rule + linearization at MAP point for nonlinear model => Laplace posterior.
New work: Laplace prior.
Covariance is exponential kernel
Mistake: no regularization

## Slide 35
Bayesian Inference Assumptions
  Likelihood is:
Normal Laplace posterior given by:
where
  Additive Gaussian noise model:
Mismatch functional to be minimized:
Gaussian prior with exponential covariance and mean = .
Bayes’ rule
* Constantine, Kent, Bui-Thanh, SISC, 2016. **Bui-Thanh, Ghattas, Martin, Stadler, SISC, 2013.
Notation*:
= observations
= random params
= deterministic map from params to observables.
Covariance of Gaussian posterior related to inverse of misfit Hessian at MAP point**.
Evaluation of misfit Hessian is expensive!
further approximation required.
+ linearization of around
Notes: Apply Bayes rule + linearization at MAP point for nonlinear model => Laplace posterior.
New work: Laplace prior.
Covariance is exponential kernel
Mistake: no regularization

## Slide 36
Bayesian Inference Workflow
*
* Bui-Thanh, Ghattas, Martin, Stadler, SISC, 2013.
Two-part dimension reduction procedure to obtain modes
Procedure for computing covariance of normal Laplace posterior,
KLE = Karhunen-Loeve Expansion
AS = Active Subspace
PCE = Polynomial Chaos Expansion
MAP = Maximum a Posteriori
*
Notes: Quadratic PCE over active variables to form Hessian.

## Slide 37
Karhunen-Loeve Expansion (KLE)
KLE modes are eigenvectors of assumed exponential covariance kernel:
KLE modes
Best fit
dimensional inversion problem can be reduced to smaller dimensional problem using Karhunen-Loeve Expansion (KLE)

## Slide 38
Karhunen-Loeve Expansion (KLE)
KLE modes are eigenvectors of assumed exponential covariance kernel:
KLE modes
Best fit
dimensional inversion problem can be reduced to smaller dimensional problem using Karhunen-Loeve Expansion (KLE)
Parameters to be selected: correlation length , basis size .

## Slide 39
Karhunen-Loeve Expansion (KLE)
KLE modes are eigenvectors of assumed exponential covariance kernel:
KLE modes
Best fit
dimensional inversion problem can be reduced to smaller dimensional problem using Karhunen-Loeve Expansion (KLE)
Parameters to be selected: correlation length , basis size .
and can be estimated “rigorously” by solving LLS problem:
d
LLS representation error decay is independent of L

## Slide 40
Karhunen-Loeve Expansion (KLE)
KLE modes are eigenvectors of assumed exponential covariance kernel:
KLE modes
Best fit
dimensional inversion problem can be reduced to smaller dimensional problem using Karhunen-Loeve Expansion (KLE)
Parameters to be selected: correlation length , basis size .
and can be estimated “rigorously” by solving LLS problem:
d
LLS representation error decay is independent of L
  should be

## Slide 41
Active Subspaces (AS)
KLE eigenvalue analysis suggests = – still large for MCMC!

## Slide 42
Active Subspaces (AS)
KLE eigenvalue analysis suggests = – still large for MCMC!
Idea: combine KLE with Active Subspace (AS) information for further (and better) data-informed dimension reduction.

## Slide 43
Active Subspaces (AS)
KLE eigenvalue analysis suggests = – still large for MCMC!
Idea: combine KLE with Active Subspace (AS) information for further (and better) data-informed dimension reduction.
Active Subspace (AS) = directions along which objective function has strongest variability.

## Slide 44
Active Subspaces (AS)
KLE eigenvalue analysis suggests = – still large for MCMC!
Idea: combine KLE with Active Subspace (AS) information for further (and better) data-informed dimension reduction.
Active Subspace (AS) = directions along which objective function has strongest variability.
Active subspace approach: mismatch approximated by related function of fewer variables:
= “active variables” = rotation of coords
* Constantine, Dow, Wang, SISC, 2014.
Example*:
(i) Rotate coords s.t. directions of strongest variation are aligned with the rotated coords.
(ii) Construct response surface using only most important rotated coords.
Bivariate function is effectively univariate in rotated coordinate system
Dimension reduction via AS:

## Slide 45
Active Subspaces (AS)
KLE eigenvalue analysis suggests = – still large for MCMC!
Idea: combine KLE with Active Subspace (AS) information for further (and better) data-informed dimension reduction.
Active Subspace (AS) = directions along which objective function has strongest variability.
Active subspace approach: mismatch approximated by related function of fewer variables:
= “active variables” = rotation of coords
* Constantine, Dow, Wang, SISC, 2014.
Example*:
(i) Rotate coords s.t. directions of strongest variation are aligned with the rotated coords.
(ii) Construct response surface using only most important rotated coords.
Bivariate function is effectively univariate in rotated coordinate system
Dimension reduction via AS:
AS identified using gradients of mismatch function

## Slide 46
Greenland Bayesian Inference via KLE + AS
KLE modes
Data-informed (AS) directions (=*)
Gradients of mismatch function obtained via adjoint solve in Albany/FELIX.
Above, left: fewer modes are needed to build the basal friction parameter map when using KLE + AS methods than when using straight KLE.
Above, right: relative clustering of large values towards smaller indices implies KLE coefficients corresponding to larger singular values contribute most to variability in .
KLE and AS amplitudes
AS principal component
index
* Value of was obtained via cross-validation.
Notes: ~73 modes
Principal component:
Find rotation matrix.
Columns of matrix are eigenvecs of Hessian. Each entry is weight associated with variable in original space. Dots are associated with linear reconstruction.
Marginal distributions: variance is smaller

## Slide 47
Active Subspaces for Inference
Various levels of approximation can be employed:
  Reduce dimension but no surrogate of misfit
    Perform MCMC in active subspace to improve mixing
  Surrogate of misfit with rotation but no dimension reduction
    Leverage increased sparsity induced by rotation
  Surrogate of misfit and dimension reduction
    Combine MCMC in active subspaces with surrogates that adaptively target regions of high probability
Notes: Down: more tractable

## Slide 48
Quadratic PCE over Active Variables
Idea: approximate misfit using quadratic PCE for efficient computation of misfit Hessian.
= quadratic PCE function
Approximate misfit over active variables using a quadratic function obtained via compressed sensing (using = 733 samples and a PCE with 20,301 terms)*:
Approximate misfit with quadratic PCE in rotated = space:
Approximate misfit with quadratic PCE in rotated and truncated = space:
* Ratios are improvements relative to using mean of data; want ratio close to 0.
Notes: Mhat(z)

## Slide 49
Low Rank Laplace-Based Covariance*
Linearize parameter-to-observable map around MAP point:
where = Frechet derivative of .
* Bui-Thanh, Ghattas, Martin, Stadler, SISC, 2013.
,
Notes: FIXME: What is motivation for Laplace-like prior covariance?

## Slide 50
Low Rank Laplace-Based Covariance*
Linearize parameter-to-observable map around MAP point:
where = Frechet derivative of .
* Bui-Thanh, Ghattas, Martin, Stadler, SISC, 2013.
,
Covariance of Gaussian Laplace posterior given by:
Notes: FIXME: What is motivation for Laplace-like prior covariance?

## Slide 51
Low Rank Laplace-Based Covariance*
Linearize parameter-to-observable map around MAP point:
where = Frechet derivative of .
Covariance of Gaussian Laplace posterior given by:
* Bui-Thanh, Ghattas, Martin, Stadler, SISC, 2013.
,
is dense!
prohibitively expensive to store & construct.
Notes: FIXME: What is motivation for Laplace-like prior covariance?

## Slide 52
Low Rank Laplace-Based Covariance*
Linearize parameter-to-observable map around MAP point:
where = Frechet derivative of .
Covariance of Gaussian Laplace posterior given by:
* Bui-Thanh, Ghattas, Martin, Stadler, SISC, 2013.
,
is dense!
prohibitively expensive to store & construct.
Low-rank approximation of obtained using Sherman-Morrison-Woodbury formula:
and its EV decomposition can be computed efficiently using a parallel matrix-free Lanczos method.
Rank of = # of modes that informed directions of posterior (AS vectors).
Symbols*:
eigenvecs, eigenvals of
= prior-preconditioned Hessian of data misfit =
= Gauss-Newton portion of Hessian misfit =
= , = adjoint of
= = Laplace stiffness.
Notes: FIXME: What is motivation for Laplace-like prior covariance?

## Slide 53
Greenland Bayesian Inference via KLE + AS
KLE modes
Data-informed (AS) directions (=*)
Above: marginal distributions of Gaussian posterior computed using KLE vs. KLE+AS; any shift from mean of 0 is due to observations.
  KLE eigenvectors have variance and mean close to prior.
  Data-informed eigenvectors have smaller variance and are most shifted w.r.t. prior distribution (as expected).
KLE and AS amplitudes
AS principal component
index
Gradients of mismatch function obtained via adjoint solve in Albany/FELIX.
* Value of was obtained via cross-validation.
Notes: ~73 modes
Principal component:
Find rotation matrix.
Columns of matrix are eigenvecs of Hessian. Each entry is weight associated with variable in original space. Dots are associated with linear reconstruction.
Marginal distributions: variance is smaller

## Slide 54
Outline
Background.
  PISCEES project for land-ice modeling.
  Land-ice model.
UQ problem definition.
Inversion/calibration.
  Deterministic inversion.
  Bayesian inference.
Summary & future work.

## Slide 55: Summary & future work
This talk described our workflow for quantifying uncertainties in expected aggregate ice sheet mass change and its demonstration on a Greenland ice sheet problem, focusing on inversion.

## Slide 56: Summary & future work
Future work:
  Execute full UQ workflow (inversion + forward propagation) on realistic Greenland/Antarctic ice sheet problems.
  Squared Laplace covariance operator approach* (no KLE)
    Less expensive than building PCE.
    Allows higher dimensional parameter spaces.
  Incorporate effects of other sources of uncertainty, e.g., surface height, surface mass balance.
* Bui-Thanh, Ghattas, Martin, Stadler, SISC, 2013.
This talk described our workflow for quantifying uncertainties in expected aggregate ice sheet mass change and its demonstration on a Greenland ice sheet problem, focusing on inversion.

## Slide 57: Summary & future work
Future work:
  Execute full UQ workflow (inversion + forward propagation) on realistic Greenland/Antarctic ice sheet problems.
  Squared Laplace covariance operator approach* (no KLE)
    Less expensive than building PCE.
    Allows higher dimensional parameter spaces.
  Incorporate effects of other sources of uncertainty, e.g., surface height, surface mass balance.
This talk described our workflow for quantifying uncertainties in expected aggregate ice sheet mass change and its demonstration on a Greenland ice sheet problem, focusing on inversion.
* Bui-Thanh, Ghattas, Martin, Stadler, SISC, 2013.
We are well-positioned to
do these efforts in parallel!

## Slide 58: Funding/acknowledgements
Support for this work was provided through Scientific Discovery through Advanced Computing (SciDAC) projects funded by the U.S. Department of Energy, Office of Science (OSCR), Advanced Scientific Computing Research and Biological and Environmental Research (BER) PISCEES SciDAC Application Partnership.
PISCEES team members: K. Evans, M. Gunzburger, M. Hoffman, C. Jackson, P. Jones, W. Lipscomb, M. Perego, S. Price, A. Salinger, I. Tezaur, R. Tuminaro, P. Worley.
Trilinos/DAKOTA collaborators: M. Eldred, J. Jakeman, E. Phipps, L. Swiler.
  Computing resources: NERSC, OLCF.

## Slide 59: References
[1] M.A. Heroux et al. “An overview of the Trilinos project.” ACM Trans. Math. Softw. 31(3) (2005).
[2] A. Salinger, et al. "Albany: Using Agile Components to Develop a Flexible, Generic Multiphysics Analysis Code", Int. J. Multiscale Comput. Engng. 14(4) (2016) 415-438.
[3] I. Tezaur, M. Perego, A. Salinger, R. Tuminaro, S. Price. "Albany/FELIX: A Parallel, Scalable and Robust Finite Element Higher-Order Stokes Ice Sheet Solver Built for Advanced Analysis", Geosci. Model Develop. 8 (2015) 1-24.
[4] M. Perego, S. Price, G. Stadler. “Optimal initial conditions for coupling ice sheet models to Earth system models”. J. Geophys. Res. Earth Surf. 119 (2014) 1894-1917.
[5] P. Constantine, E. Dow, Q. Wang. “Active subspace methods in theory and practice: applications to Kriging surfaces”. SIAM J. Sci. Comput. 36(4) (2014) A1500-A1524.
[6] P. Constantine, C. Kent, T. Bui-Thanh. “Accelerating Markov Chain Monte Carlo with Active Subspaces”. SIAM J. Sci. Comput. 38 (5) (2016) A2779-A2805.
[7] T. Bui-Thanh, O. Ghattas. J. Martin. G. Stadler. “A computational framework for infinite-dimensional Bayesian inverse problems part I: the linearized case, with application to global seismic inversion”. SIAM J. Sci. Comput. 35(6) (2013) A2494-2523.
[8] T. Isaac, N. Petra, G. Stadler, O. Ghattas. “Scalable and efficient algorithms for the propagation of uncertainty from data through inference to prediction for large-scale problems, with application to flow of the Antarctic ice sheet”. J. Comput. Phys. 296 (2015) 348-368.
[9] J. Jakeman, M. Eldred, K. Sargsyan. “Enhancing l1-minimization estimates of polynomial chaos expansions using basis selection”, J. Comp. Phys. 289 (2015) 18-34.
[10] N. Petra, J. Martin, G. Stadler, O. Ghattas. “A computational framework for infinite dimensional Bayesian inverse problems. Part II: stochastic Newton with application to ice sheet flow inverse problems”. SIAM J. Sci. Comput. 36 (4) (2014) A1525-1555.
[11] J. Jakeman, I. Tezaur, M. Perego, S. Price. "Probabalistic Projections of Sea-Level Change from the Greenland Ice Sheet", in preparation.

## Slide 60: Multiphysics Code
Component-based design for rapid development of new physics & capabilities.
Extensive use of libraries from the open-source Trilinos project:
  Automatic differentiation.
  Discretizations/meshes, mesh adaptivity.
  Solvers, time-integration schemes.
  Performance-portable kernels.
Advanced analysis capabilities:
  Parameter estimation.
  Uncertainty quantification (DAKOTA).
  Optimization (DAKOTA, ROL).
  Sensitivity analysis.
Albany = Sandia open-source* parallel, C++, multi-physics finite element code.
40+ packages; 120+ libraries
* https://github.com/gahansen/Albany.
  The Albany/FELIX land-ice solver is implemented within the Albany multi-physics code.

## Slide 61
Computing the Active Subspace
Gradients of mismatch can be used to identify subspace that controls variation in likelihood function (active subspace)
Mismatch approximated by related function of fewer variables :
Active subspace computed using
  Sample gradient using MC: .
  Form Gauss-Newton approx. of Hessian averaged over prior:
  Compute eigenvalue decomposition:
    eigenvectors define rotation of
Partition into active and inactive variables:
Linear transformation (rotation) of coords
Perturbing along columns of changes more.
= “active variables”
Notes: FIXME:

## Slide 62: Full UQ Workflow: Varying Levels of Approx.
As with Bayesian inference:
Future work: compare errors as accuracy of approximation is increased to gain insight into viability of lower-dimensional approximations.
Lessons can be learned by avoiding use of highest fidelity model.