## Slide 1: The Schwarz Alternating Method for Multi-Scale Contact Mechanics
Alejandro Mota1, Irina Tezaur1, Daria Koliesnikova1, Jonathan Hoy2
1Sandia National Laboratories, 2University of Southern California
Congress on Numerical Methods in Engineering (CMN) 2022
Las Palmas de Gran Canaria, Spain September 12-14, 2022
SAND2022-11528C

## Slide 2: Motivation
Stable, accurate and robust methods for simulating mechanical contact are extremely important in computational solid mechanics
  Example scenarios where contact arises: touching surfaces, sliding, tightened bolts, impact, …
Above: gears in contact within MEMS device. From sandia.gov/media
Below: oblique cylinder impact simulated using Sandia’s ALEGRA code.
Notes: MEMS = microelectromechanical systems

## Slide 3: Motivation
Stable, accurate and robust methods for simulating mechanical contact are extremely important in computational solid mechanics
  Example scenarios where contact arises: touching surfaces, sliding, tightened bolts, impact, …
Two-step process to the computational simulation of contact:
Proximity search: computer science problem, has received much attention due to importance in video game development 
Contact enforcement step: existing methods (penalty, Lagrange multiplier, augmented Lagrangian) suffer from poor performance 
  Long simulation times 
  Lack of accuracy 
  Lack of robustness 
Above: gears in contact within MEMS device. From sandia.gov/media
Below: oblique cylinder impact simulated using Sandia’s ALEGRA code.
Notes: MEMS = microelectromechanical systems

## Slide 4: Motivation
Stable, accurate and robust methods for simulating mechanical contact are extremely important in computational solid mechanics
  Example scenarios where contact arises: touching surfaces, sliding, tightened bolts, impact, …
Two-step process to the computational simulation of contact:
Proximity search: computer science problem, has received much attention due to importance in video game development 
Contact enforcement step: existing methods (penalty, Lagrange multiplier, augmented Lagrangian) suffer from poor performance 
  Long simulation times 
  Lack of accuracy 
  Lack of robustness 
Above: gears in contact within MEMS device. From sandia.gov/media
Below: oblique cylinder impact simulated using Sandia’s ALEGRA code.
Notes: MEMS = microelectromechanical systems

## Slide 5: Motivation
Stable, accurate and robust methods for simulating mechanical contact are extremely important in computational solid mechanics
  Example scenarios where contact arises: touching surfaces, sliding, tightened bolts, impact, …
Two-step process to the computational simulation of contact:
Proximity search: computer science problem, has received much attention due to importance in video game development 
Contact enforcement step: existing methods (penalty, Lagrange multiplier, augmented Lagrangian) suffer from poor performance 
  Long simulation times 
  Lack of accuracy 
  Lack of robustness 
Above: gears in contact within MEMS device. From sandia.gov/media
Below: oblique cylinder impact simulated using Sandia’s ALEGRA code.
Notes: MEMS = microelectromechanical systems

## Slide 6: Motivation
Stable, accurate and robust methods for simulating mechanical contact are extremely important in computational solid mechanics
  Example scenarios where contact arises: touching surfaces, sliding, tightened bolts, impact, …
Two-step process to the computational simulation of contact:
Proximity search: computer science problem, has received much attention due to importance in video game development 
Contact enforcement step: existing methods (penalty, Lagrange multiplier, augmented Lagrangian) suffer from poor performance 
  Long simulation times 
  Lack of accuracy 
  Lack of robustness 
Above: gears in contact within MEMS device. From sandia.gov/media
This talk: new approach for simulating multi-scale mechanical contact using the Schwarz alternating method.
Below: oblique cylinder impact simulated using Sandia’s ALEGRA code.
Notes: MEMS = microelectromechanical systems

## Slide 7: Schwarz Alternating Method for Domain Decomposition
Proposed in 1870 by H. Schwarz for solving Laplace PDE on irregular domains.
H. Schwarz (1843–1921)
Initialize:
Solve PDE by any method on w/ initial guess for transmission BCs on .
Iterate until convergence:
Solve PDE by any method on w/ transmission BCs on based on values just obtained for .
Solve PDE by any method on w/ transmission BCs on based on values just obtained for .
Crux of Method: if the solution is known in regularly shaped domains, use those as pieces to iteratively build a solution for the more complex domain.
Basic Schwarz Algorithm
2Lions, 1990. 3Zanolli et al., 1987.
overlapping
non-overlapping

## Slide 8: Schwarz Alternating Method for Domain Decomposition
Proposed in 1870 by H. Schwarz for solving Laplace PDE on irregular domains.
H. Schwarz (1843–1921)
Initialize:
Solve PDE by any method on w/ initial guess for transmission BCs on .
Iterate until convergence:
Solve PDE by any method on w/ transmission BCs on based on values just obtained for .
Solve PDE by any method on w/ transmission BCs on based on values just obtained for .
Crux of Method: if the solution is known in regularly shaped domains, use those as pieces to iteratively build a solution for the more complex domain.
2Lions, 1990. 3Zanolli et al., 1987.
Overlapping Schwarz: convergent with all-Dirichlet transmission BCs1 if .
Non-overlapping Schwarz: convergent with Robin-Robin2 or alternating Neumann-Dirichlet3 transmission BCs.
1Schwarz, 1870; Lions, 1988.
overlapping
Basic Schwarz Algorithm

## Slide 9: Schwarz Alternating Method for Domain Decomposition
Proposed in 1870 by H. Schwarz for solving Laplace PDE on irregular domains.
H. Schwarz (1843–1921)
Initialize:
Solve PDE by any method on w/ initial guess for transmission BCs on .
Iterate until convergence:
Solve PDE by any method on w/ transmission BCs on based on values just obtained for .
Solve PDE by any method on w/ transmission BCs on based on values just obtained for .
Crux of Method: if the solution is known in regularly shaped domains, use those as pieces to iteratively build a solution for the more complex domain.
2Lions, 1990. 3Zanolli et al., 1987.
Overlapping Schwarz: convergent with all-Dirichlet transmission BCs1 if .
Non-overlapping Schwarz: convergent with Robin-Robin2 or alternating Dirichlet-Neumann3 transmission BCs.
z: convergent with Robin-Robin2 or alternating Neumann-Dirichlet3 transmission BCs.
1Schwarz, 1870; Lions, 1988.
2Lions, 1990. 3Zanolli et al., 1987.
non-overlapping
Basic Schwarz Algorithm

## Slide 10: How We Use the Schwarz Alternating Method
AS A PRECONDITIONER FOR THE LINEARIZED SYSTEM
AS A SOLVER FOR THE COUPLED
FULLY NONLINEAR PROBLEM
10

## Slide 11: Overlapping Schwarz for Multi-Scale Coupling in Solid Mechanics
The Schwarz alternating method has been developed/implemented for concurrent multi-scale quasistatic & dynamic modeling in Sandia’s Albany/LCM* and Sierra/SM codes.
Displacement
Velocity
1Mota et al., 2017; Mota et al., 2022.
Coupling is concurrent (two-way)
“Plug-and-play” framework: couples different meshes, element types, solvers, integrators
No nonphysical artifacts
Theoretical convergence properties1
Easy to implement in existing HPC codes
Scalable, fast, robust
 | CPU times | # Schwarz iters
Single | 3h 34m | 
Schwarz | 2h 42m | 3.22
 | CPU times | # Schwarz iters
 | 3h 34m | 
Schwarz | 2h 42m | 3.22
*https://github.com/sandialabs/LCM

## Slide 12: Solid Mechanics Problem Formulation
Kinetic Energy:
Potential Energy:
Lagrangian:
Action Functional:
12
Euler-Lagrange Equations:
Semi-Discrete Problem:
FEM

## Slide 13: Traditional Solid Mechanics Contact Formulation
Kinetic Energy:
Potential Energy Augmented with Contact Constraint:
Lagrangian:
Action Functional:
13
Indicator function for admissible set :
:
The set of admissible configurations in which interpenetration does not occur
Contact constraint can be enforced strictly or approximately
Strict enforcement: Lagrange multiplier methods
Approximate enforcement: penalty methods

## Slide 14: Non-Overlapping Schwarz Contact Formulation
Can use different integrators with different time steps within each domain!
Ingredients:
  Domain decomposition
  Discretization and time-stepper in (red)
  Discretization and time-stepper in (green)
  Controller time-stepper (blue): defines global time-steps at which subdomains are synchronized
14

## Slide 15: Non-Overlapping Schwarz Contact Formulation
Can use different integrators with different time steps within each domain!
Ingredients:
  Domain decomposition
  Discretization and time-stepper in (red)
  Discretization and time-stepper in (green)
  Controller time-stepper (blue): defines global time-steps at which subdomains are synchronized
Problem is solved without any Schwarz iteration in time intervals and , as there is no contact.
15

## Slide 16: Non-Overlapping Schwarz Contact Formulation
Ingredients:
  Domain decomposition
  Discretization and time-stepper in (red)
  Discretization and time-stepper in (green)
  Controller time-stepper (blue): defines global time-steps at which subdomains are synchronized
Problem is solved without any Schwarz iteration in time intervals and , as there is no contact.
Non-overlapping Schwarz algorithm only applied in control time interval , when contact is detected.
Contact Criteria
Overlap: interpenetration of subdomains
Compression: positive normal traction
Persistence: was in contact previous step
16

## Slide 17: Non-Overlapping Schwarz Contact Formulation
Key idea: a contact problem can be viewed as coupled problem while 2+ bodies are in contact
  Alternating Dirichlet-Neumann (traction) Schwarz iteration is applied once interpenetration has been detected, to correct the interpenetration.
17
There are no contact constraints!
Contact constraints replaced with BCs applied iteratively at contact boundaries.

## Slide 18: Numerical Results: 1D Impact Problem1
Impact of two 1D identical linear elastic prismatic rods discretized using linear elements with exact analytic solution [Carpenter et al., 1991]
Schwarz alternating method compared to three conventional contact algorithms with a zero gap contact constraint
  Implicit and explicit penalty method with penalty parameter
  Forward increment (explicit) Lagrange multiplier (LM) method [Carpenter et al., 1991]
Time stepper: Newmark-beta
  Schwarz couplings included Explicit-Explicit, Implicit-Explicit and Implicit-Implicit
  used for all methods except Implicit-Explicit Schwarz, which uses in explicit domain.
1Hoy et al., 2021; Mota et al., 2022 (under review).

## Slide 19: Numerical Results: 1D Impact Problem1
Penalty methods overpredict contact point location between impact and release times
Explicit LM method under-predicts release time
Schwarz methods capture release time to an accuracy of 0.1%.
Contact point position: of the right-most node of left bar () as a function of time
1Hoy et al., 2021; Mota et al., 2022 (under review).

## Slide 20: Numerical Results: 1D Impact Problem1
Mass-averaged velocity: of the left bar () as a function of time
Similar conclusions can be drawn from mass-averaged velocity
Schwarz variants calculate mass-averaged velocity to a sufficiently greater accuracy than any of the conventional methods, especially near the time of release
1Hoy et al., 2021; Mota et al., 2022 (under review).

## Slide 21: Numerical Results: 1D Impact Problem1
Total energy relative error: for the left bar () as a function of time
Total energy should be conserved for this problem
Total energy error is negative for all 6 methods all methods are stable.
All three conventional methods exhibit total energy loss of up to 9% following contact.
Unlike conventional contact methods, Schwarz achieves an error of at most 0.25% in the total energy!
  Explicit-Explicit Schwarz gives most accurate total energy, followed by Implicit-Implicit Schwarz and Implicit-Explicit Schwarz
1Hoy et al., 2021; Mota et al., 2022 (under review).

## Slide 22: Numerical Results: 1D Impact Problem1
Contact point force: for the left bar () as a function of time
Three conventional methods exhibit some undesirable artifacts in contact point force but deliver in general a smooth solution
Schwarz solutions exhibit oscillations following instantiation of contact “chatter” problem
  Schwarz method with largest total energy loss (Implicit-Explicit) exhibits least amount of chatter
  Energy dissipation is necessary for establishment of persistent contact [Solberg et al., 1998]
    Chatter problem can likely be mitigated through addition of numerical dissipation
1Hoy et al., 2021; Mota et al., 2022 (under review).
WIP: mitigating chatter problem.
Notes: Chatter = loss/subsequent reestablishment of contact

## Slide 23: Numerical Results: 1D Impact Problem1
Convergence of Schwarz methods
1Hoy et al., 2021; Mota et al., 2021 (under review).
Mesh convergence of kinetic energy for left bar () when
# Schwarz iterations required for convergence (200, )
Convergence rates are comparable to published results [Tezaur et al., 2021]
At most 5 Schwarz iterations are needed for convergence
  Explicit-Explicit Schwarz variant requires fewest # iterations for convergence
Notes: Chatter = loss/subsequent reestablishment of contact

## Slide 24: Summary & Future Work
Summary:
The Schwarz alternating method has shown promise as a novel technique for simulating multi-scale mechanical contact
  Contact constraints are replaced with transmission BCs applied iteratively on contact boundaries
  Schwarz method delivers substantially more accurate solution than conventional contact approaches in contact point displacement, mass-averaged velocity, impact time, release time, and kinetic, potential total energies
  An unfortunate consequence of the method’s ability to conserve energy so well appears to be the introduction of chatter in contact point velocity and force.
Ongoing/future work:
Introduction of dissipation and/or numerical relaxation to mitigate chatter problem.
Robin-Robin transmission condition formulation of non-overlapping Schwarz promising preliminary results!
Introduction of additional or alternate contact conditions into Schwarz formulation
Implementation/evaluation of the Schwarz alternating method in multi-D
  Requires the development of operators for consistent transfer of contact traction BCs using concept of prolongation/restriction

## Slide 25: References
H. Schwarz, Uber einen Grenzubergang durch alternierendes verfahren, Vierteljahrsschriftder Naturforschenden Gesellschaft in Zurich, 15 (1870), pp. 272–286.
P.L. Lions. “On the Schwarz alternating method I.” In: 1988, First International Symposium on Domain Decomposition methods for Partial Differential Equations, SIAM, Philadelphia.
P. L. Lions, On the Schwarz alternating method III: A variant for nonoverlapping subdomains, in Third International Symposium on Domain Decomposition Methods for Partial Differential Equations, T. F. Chan, R. Glowinski, J. P´eriaux, and O. B. Widlund, eds., Society for Industrial and Applied Mathematics, 1990, pp. 202–223
P. Zanolli, Domain decomposition algorithms for spectral methods, CALCOLO, 24 (1987), pp. 201–240.
A. Mota, I. Tezaur, and C. Alleman, The Schwarz alternating method, Comput. Meth. Appl. Mech. Engng., 319 (2017), pp. 19–51.
A. Mota, I. Tezaur, and G. Phlipot, The Schwarz alternating method for transient solid dynamics, Int. J. Numer. Meth. Engng. 1-35, 2022.
N. J. Carpenter, R. L. Taylor, and M. G. Katona, Lagrange constraints for transient finite element surface contact, International journal for numerical methods in engineering, 32 (1991), pp. 103–128.
J. Hoy, I. Tezaur, A. Mota. The Schwarz alternating method for multi-scale contact mechanics. CSRI Summer Proceedings, E. Galvan and D. Smith, eds., Technical Report SAND2021-9886C, Sandia National Laboratories, 2021.
A. Mota, I. Tezaur, J. Hoy. The Schwarz alternating method for multi-scale contact mechanics. Mathematical & Computational Applications (MCA) (under review).
J. M. Solberg and P. Papadopoulos, A finite element method for contact/impact, Finite Elements in Analysis and Design, 30 (1998), pp. 297–311.
I. Tezaur, T. Voth, J. Niederhaus, J. Robbins, and J. Sanchez, An extended finite element method (XFEM) formulation for multi-material Eulerian solid mechanics in the Alegra code (in preparation).

## Slide 26: Start of Backup Slides

## Slide 27: Motivation
Two-step process to the computational simulation of contact:
Proximity search: computer science problem, has received much attention due to importance in video game development 
Contact enforcement step: existing methods (penalty, Lagrange multiplier, augmented Lagrangian) suffer from poor performance 
  Long simulation times 
  Lack of accuracy 
  Lack of robustness 
Large scale structural failure frequently originates from small scale phenomena (e.g, defects, microcracks, inhomogeneities), which grow quickly in unstable manner
  Concurrent multiscale methods are essential to capture correctly the multiscale behavior!
  Stable, accurate and robust methods for simulating mechanical contact (touching surfaces, sliding, tightened bolts, impact) are equally important!
Above: roof failure of Boeing 737 aircraft due to fatigue cracks. From imechanica.org
This talk.
Above: gears in contact within MEMS device. From sandia.gov/media

## Slide 28: Schwarz Alternating Method for Domain Decomposition
Proposed in 1870 by H. Schwarz for solving Laplace PDE on irregular domains.
H. Schwarz (1843 – 1921)
Initialize:
Solve PDE by any method on w/ initial guess for Dirichlet BCs on .
Iterate until convergence:
Solve PDE by any method (can be different than for ) on w/ transmission BCs on that are the values just obtained for .
Solve PDE by any method (can be different than for ) on w/ transmission BCs on that are the values just obtained for .
Crux of Method: if the solution is known in regularly shaped domains, use those as pieces to iteratively build a solution for the more complex domain.
Basic Schwarz Algorithm
Schwarz alternating method most commonly used as a preconditioner for Krylov iterative methods to solve linear algebraic equations.
Novel idea: using the Schwarz alternating as a discretization method for solving multi-scale partial differential equations (PDEs).

## Slide 29: Non-Overlapping Schwarz Contact Formulation
Notes: Key idea: the contact problem can be viewed as a coupled problem while the 2+ bodies are in contact

## Slide 30: Non-Overlapping Schwarz Contact Formulation
Before contact: simulation proceeds as usual
Detection of contact: proximity search and application of contact conditions to determine contact
Overlap condition: triggered when two or more objects/domains have begun to overlap/penetrate each other
Compression condition: positive normal traction
Persistence condition: contact occurred in the previous step
Enforcement of contact: alternating Schwarz iteration with Dirichlet-Neumann transmission BCs
Key idea: a contact problem can be viewed as coupled problem while 2+ bodies are in contact
Notes: Key idea: the contact problem can be viewed as a coupled problem while the 2+ bodies are in contact

## Slide 31: Non-Overlapping Schwarz Contact Formulation
Before contact: simulation proceeds as usual
Enforcement of contact: alternating Schwarz iteration with Dirichlet-Neumann transmission BCs
There are no contact constraints!
Contact constraints replaced with BCs applied iteratively at contact boundaries.
Detection of contact: proximity search and application of contact conditions to determine contact
Overlap condition: triggered when two or more objects/domains have begun to overlap/penetrate each other
Compression condition: positive normal traction
Persistence condition: contact occurred in the previous step
Notes: Key idea: the contact problem can be viewed as a coupled problem while the 2+ bodies are in contact

## Slide 32: Enforcement of Contact via Alternating Schwarz
Step 0: Initialize
Controller time stepper
Time integrator for W1
Time integrator for W2
Key idea: a contact problem can be viewed as coupled problem while 2+ bodies are in contact

## Slide 33: Enforcement of Contact via Alternating Schwarz
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times to apply Dirichlet BC.
Controller time stepper
Time integrator for W1
Time integrator for W2
Integrate using
Interpolate from to
Key idea: a contact problem can be viewed as coupled problem while 2+ bodies are in contact

## Slide 34: Enforcement of Contact via Alternating Schwarz
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times to apply Dirichlet BC
Step 2: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times to apply Neumann (traction) BC.
Controller time stepper
Time integrator for W1
Time integrator for W2
Integrate using
Interpolate from to
Key idea: a contact problem can be viewed as coupled problem while 2+ bodies are in contact

## Slide 35: Enforcement of Contact via Alternating Schwarz
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times to apply Dirichlet BC.
Step 2: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times to apply Neumann (traction) BC.
Step 3: Check for convergence at time .
Controller time stepper
Time integrator for W1
Time integrator for W2
Key idea: a contact problem can be viewed as coupled problem while 2+ bodies are in contact

## Slide 36: Enforcement of Contact via Alternating Schwarz
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times to apply Dirichlet BC
Step 2: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times to apply Neumann (traction) BC.
Step 3: Check for convergence at time .
If unconverged, return to Step 1.
Controller time stepper
Time integrator for W1
Time integrator for W2
Interpolate from to
Integrate using
Key idea: a contact problem can be viewed as coupled problem while 2+ bodies are in contact
Notes: Controller time-stepper – defines global dTs at which subdomains are synchronized

## Slide 37: Enforcement of Contact via Alternating Schwarz
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times to apply Dirichlet BC.
Step 2: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times to apply Neumann (traction) BC.
Step 3: Check for convergence at time .
If unconverged, return to Step 1.
If converged, set and return to Step 1.
Controller time stepper
Time integrator for W1
Time integrator for W2
Integrate using
Interpolate from to
Key idea: a contact problem can be viewed as coupled problem while 2+ bodies are in contact

## Slide 38: Schwarz Algorithm for Contact
Contact criteria:
Overlap: interpenetration of subdomains
Compression: Positive normal traction
Persistence: Was in contact previous step
38

## Slide 39: A Canonical 1D Problem – 2 Colliding Elastic Bars
Position and velocity of left contact point:
Impact & release times:
Contact force:
39

## Slide 40: Comparison of Results
Analytic solution
Lagrange multiplier method with implicit time integration
Lagrange multiplier method with explicit time integration
Penalty method with implicit time integration
Penalty method with explicit time integration
Schwarz method with implicit-implicit integration
Schwarz method with implicit-explicit time integration
Schwarz method with explicit-explicit time integration

## Slide 41: Contact Point Position
41

## Slide 42: Mass-Averaged Velocity
42

## Slide 43: Kinetic Energy
43

## Slide 44: Potential Energy
44

## Slide 45: Total Energy
45

## Slide 46: Contact Force
46

## Slide 47: Contact Velocity
47