## Slide 1: The Schwarz alternating method as a means for concurrent multi-scale coupling of conventional and data-driven models
SAND2023-11341A
Sandia National Laboratories is a multi-mission laboratory managed and operated by National Technology and Engineering Solutions of Sandia, LLC., a wholly owned subsidiary of Honeywell International, Inc., for the U.S. Department of Energy’s National Nuclear Security Administration under contract DE-NA0003525.
Irina Tezaur1, Alejandro Mota1, Coleman Alleman1, Greg Phlipot2, Joshua Barnett1,3
1Sandia National Labs 2MSC Software 3Stanford University
University of Nevada, Reno DMS Colloquium February 2, 2023

## Slide 2
Outline
Alternating Schwarz Method for Coupling of Full Order Models (FOMs) in Solid Mechanics
  Motivation & Background
  Quasistatics
  Extension to Dynamics
  Summary & Next Steps
Alternating Schwarz Method for FOM-ROM* and ROM-ROM Coupling
  Motivation & Background
  Demonstration
  Ongoing & Future Work
* Projection-based Reduced Order Model

## Slide 3
Outline
Alternating Schwarz Method for Coupling of Full Order Models (FOMs) in Solid Mechanics
  Motivation & Background
  Quasistatics
  Extension to Dynamics
  Summary & Next Steps
Alternating Schwarz Method for FOM-ROM* and ROM-ROM Coupling
  Motivation & Background
  Demonstration
  Ongoing & Future Work
* Projection-based Reduced Order Model

## Slide 4
Motivation for Concurrent Multiscale Coupling
Large scale structural failure frequently originates from small scale phenomena such as defects, microcracks, inhomogeneities and more, which grow quickly in unstable manner.
Failure occurs due to tightly coupled interaction between small scale (stress concentrations, material instabilities, cracks, etc.) and large scale (vibration, impact, high loads and other perturbations).
Roof failure of Boeing 737 aircraft due to fatigue cracks. From imechanica.org
Concurrent multiscale methods are essential for understanding and prediction of behavior of engineering systems when a small scale failure determines the performance of the entire system.
Surface flaw in pressure vessel: interacts with microstructure, which may or may not lead to failure.
Notes: A lot of the problems of interest to Sandia National Labs require us to simulate and understand the large scale structural failure of engineered components, for instance, components comprising weapons systems.
GTS = Gas Transfer Systems

## Slide 5
Previous Multiscale Coupling Work

## Slide 6
Previous Multiscale Coupling Work
Three-field multiscale coupling formulation with compatibility enforced weakly using Lagrange multipliers.

## Slide 7
Previous Multiscale Coupling Work
Method works well, but is difficult to implement into existing codes.

## Slide 8
Requirements for Multiscale Coupling Method
Coupling is concurrent (two-way).
Ease of implementation into existing massively-parallel HPC codes.
Scalable, fast, robust (we target real engineering problems, e.g., analyses involving failure of bolted components!).
“Plug-and-play” framework: simplifies task of meshing complex geometries
  Ability to couple regions with different non-conformal meshes, different element types and different levels of refinement.
  Ability to use different solvers/time-integrators in different regions.
Coupling does not introduce nonphysical artifacts.
Theoretical convergence properties/guarantees.

## Slide 9
overlapping
non-overlapping
Proposed in 1870 by H. Schwarz for solving Laplace PDE on irregular domains.
H. Schwarz (1843–1921)
Initialize:
Solve PDE by any method on w/ initial guess for transmission BCs on .
Iterate until convergence:
Solve PDE by any method on w/ transmission BCs on based on values just obtained for .
Solve PDE by any method on w/ transmission BCs on based on values just obtained for .
Crux of Method: if the solution is known in regularly shaped domains, use those as pieces to iteratively build a solution for the more complex domain.
Basic Schwarz Algorithm
2Lions, 1990. 3Zanolli et al., 1987.
Schwarz Alternating Method for Domain Decomposition

## Slide 10
overlapping
Proposed in 1870 by H. Schwarz for solving Laplace PDE on irregular domains.
H. Schwarz (1843–1921)
Initialize:
Solve PDE by any method on w/ initial guess for transmission BCs on .
Iterate until convergence:
Solve PDE by any method on w/ transmission BCs on based on values just obtained for .
Solve PDE by any method on w/ transmission BCs on based on values just obtained for .
Crux of Method: if the solution is known in regularly shaped domains, use those as pieces to iteratively build a solution for the more complex domain.
Basic Schwarz Algorithm
2Lions, 1990. 3Zanolli et al., 1987.
Schwarz Alternating Method for Domain Decomposition
Overlapping Schwarz: convergent with all-Dirichlet transmission BCs1 if .
Non-overlapping Schwarz: convergent with Robin-Robin2 or alternating Neumann-Dirichlet3 transmission BCs.
1Schwarz, 1870; Lions, 1988.

## Slide 11
non-overlapping
Proposed in 1870 by H. Schwarz for solving Laplace PDE on irregular domains.
H. Schwarz (1843–1921)
Initialize:
Solve PDE by any method on w/ initial guess for transmission BCs on .
Iterate until convergence:
Solve PDE by any method on w/ transmission BCs on based on values just obtained for .
Solve PDE by any method on w/ transmission BCs on based on values just obtained for .
Crux of Method: if the solution is known in regularly shaped domains, use those as pieces to iteratively build a solution for the more complex domain.
Basic Schwarz Algorithm
2Lions, 1990. 3Zanolli et al., 1987.
Schwarz Alternating Method for Domain Decomposition
Overlapping Schwarz: convergent with all-Dirichlet transmission BCs1 if .
Non-overlapping Schwarz: convergent with Robin-Robin2 or alternating Neumann-Dirichlet3 transmission BCs.
2Lions, 1990. 3Zanolli et al., 1987.

## Slide 12
overlapping
non-overlapping
Proposed in 1870 by H. Schwarz for solving Laplace PDE on irregular domains.
H. Schwarz (1843–1921)
Initialize:
Solve PDE by any method on w/ initial guess for transmission BCs on .
Iterate until convergence:
Solve PDE by any method on w/ transmission BCs on based on values just obtained for .
Solve PDE by any method on w/ transmission BCs on based on values just obtained for .
Crux of Method: if the solution is known in regularly shaped domains, use those as pieces to iteratively build a solution for the more complex domain.
Basic Schwarz Algorithm
2Lions, 1990. 3Zanolli et al., 1987.
Schwarz Alternating Method for Domain Decomposition
Overlapping Schwarz: convergent with all-Dirichlet transmission BCs1 if .
Non-overlapping Schwarz: convergent with Robin-Robin2 or alternating Neumann-Dirichlet3 transmission BCs.
2Lions, 1990. 3Zanolli et al., 1987.
1Schwarz, 1870; Lions, 1988.
Common use of Schwarz: preconditioner for Krylov iterative methods to solve linear systems.

## Slide 13
How we use the Schwarz Alternating Method
AS A PRECONDITIONER FOR THE LINEARIZED SYSTEM
AS A SOLVER FOR THE COUPLED
FULLY NONLINEAR PROBLEM

## Slide 14
Outline
Alternating Schwarz Method for Coupling of Full Order Models (FOMs) in Solid Mechanics
  Motivation & Background
  Quasistatics
  Extension to Dynamics
  Summary & Next Steps
Alternating Schwarz Method for FOM-ROM* and ROM-ROM Coupling
  Motivation & Background
  Demonstration
  Ongoing & Future Work
* Projection-based Reduced Order Model

## Slide 15
Quasistatic Solid Mechanics Formulation
Energy functional defining weak form of the governing PDEs
: Helmholtz free-energy density
deformation gradient
: collection of internal variables (for plastic materials)
: density, : body force
Euler-Lagrange equations, obtained by minimizing :
Quasistatics solves sequence of problems in which loading (body force) is incremented quasistatically w.r.t. pseudo time :
For
Solve with appropriate boundary conditions (BCs)
Increment pseudo time to obtain

## Slide 16
Overlapping Domain Decomposition
Non-overlapping Domain Decomposition
Relevant for multi-material and multi-physics coupling
Alternating Dirichlet-Neumann transmission BCs [Zanolli et al., 1987]
Robin-Robin transmission BCs also lead to convergence [Lions,1990]
relaxation parameter (can help convergence)
Dirichlet-Dirichlet transmission BCs [Schwarz, 1870; Lions, 1988]
Spatial Coupling via Alternating Schwarz
Model PDE:

## Slide 17
Overlapping Domain Decomposition
Non-overlapping Domain Decomposition
Relevant for multi-material and multi-physics coupling
Alternating Dirichlet-Neumann transmission BCs [Zanolli et al., 1987]
Robin-Robin transmission BCs also lead to convergence [Lions,1990]
relaxation parameter (can help convergence)
Dirichlet-Dirichlet transmission BCs [Schwarz, 1870; Lions, 1988]
Spatial Coupling via Alternating Schwarz
Model PDE:
Part 1 of talk
Part 2 of talk

## Slide 18
Overlapping Schwarz Coupling in Quasistatics
Advantages:
Conceptually very simple.
Allows the coupling of regions with different non-conforming meshes, different element types, and different levels of refinement.
Information is exchanged among two or more regions, making coupling concurrent.
Different solvers can be used for the different regions.
Different material models can be coupled if they are compatible in the overlap region.
Simplifies the task of meshing complex geometries for the different scales.
outer quasistatic loop

## Slide 19
S.L. Sobolev (1936): posed Schwarz method for linear elasticity in variational form and proved method’s convergence by proposing a convergent sequence of energy functionals.
S.G. Mikhlin (1951): proved convergence of Schwarz method for general linear elliptic PDEs.
P.-L. Lions (1988): studied convergence of Schwarz for nonlinear monotone elliptic problems using max principle.
A. Mota, I. Tezaur, C. Alleman (2017): proved convergence of the alternating Schwarz method for finite deformation quasi-static nonlinear PDEs (with energy functional ) with a geometric convergence rate.
S.G. Mikhlin
(1908 – 1990)
S.L. Sobolev (1908 – 1989)
A. Mota, I. Tezaur, C. Alleman
Using the Schwarz alternating as a discretization method for PDEs is natural idea with a sound theoretical foundation.
Theoretical Foundation
P.- L. Lions (1956-)
Notes: A(F,Z) = Helmholtz free-energy density, Z = collection of internal variables, F = grad(phi) = deformation gradient, B = body force, T = traction on boundary
P = \partial A/\partial F = first Piola-Kirchoff stress
2nd equation is Euler-Lagrange equation

## Slide 20
Convergence Proof*
*A. Mota, I. Tezaur, C. Alleman. "The Schwarz Alternating Method in Solid Mechanics", CMAME 319 (2017), 19-51.
Notes: The proof effectively constructs a sequence of solutions phi^n and demonstrates that this sequence converges to the unique minimizer of the energy functional \Phi defining the single-domain problem, and combines concepts used in the analysis of Sobolev, Lions, and others, in studying the convergence of the Schwarz method.

## Slide 21
Implementation in Albany LCM Code
Component-based design for rapid development.
Contains a wide variety of constitutive models.
Extensive use of libraries from the open-source Trilinos project.
  Use of the Phalanx package to decompose complex problem into simpler problems with managed dependencies.
  Use of the Sacado package for automatic differentiation.
  Use of Teko package for block preconditioning for Modified and Monolithic Schwarz variants.
Parallel implementation of Schwarz alternating method uses the Data Transfer Kit (DTK).
All software available on GitHub.
https://github.com/trilinos/trilinos
https://github.com/SNLComputation/LCM
https://github.com/ORNL-CEES/DataTransferKit
The proposed quasistatic alternating Schwarz method is implemented within the Albany LCM open-source parallel, C++, multi-physics, finite element code.

## Slide 22
Schwarz Iteration
Quasistatic Example #1: Cuboid Problem
Coupling of two cuboids with square base (above).
Neohookean-type material model.

## Slide 23
Below: Convergence of the cuboid problem for different mesh sizes and fixed overlap volume fraction. The Schwarz alternating method converges linearly.
Above: Convergence factor as a function of overlap volume and different mesh. There is faster linear convergence with increasing overlap volume fraction.
Cuboid Problem: Convergence with Overlap & Refinement

## Slide 24: Cuboid Problem: Schwarz Error

## Slide 25
Quasistatic Example #2: Notched Cylinder
Notched cylinder that is stretched along its axial direction.
Domain decomposed into two subdomains.
Neohookean-type material model.

## Slide 26
The Schwarz alternating method is capable of coupling different mesh topologies.
The notched region, where stress concentrations are expected, is finely meshed with tetrahedral elements.
The top and bottom regions, presumably of less interest, are meshed with coarser hexahedral elements.
Notched Cylinder: TET - HEX Coupling

## Slide 27
Notched Cylinder: TET - HEX Coupling

## Slide 28
Notched Cylinder: TET - HEX Coupling

## Slide 29
Notched cylinder subjected to tensile load with an elastic and J2 elasto-plastic regions.
Coarse region is elastic and fine region is elasto-plastic.
The overlap region in the first mesh is nearer the notch, where plastic behavior is expected.
Overlap far from notch.
Overlap near notch.
Coupled regions
Coarse, elastic region
Fine, elasto-plastic region
Notched Cylinder: Coupling Different Materials
The Schwarz method is capable of coupling regions with different material models.

## Slide 30
When the overlap region is far from the notch, no plastic deformation exists in it: the coarse and fine regions predict the same behavior.
When the overlap region is near the notch, plastic deformation spills onto it and the two models predict different behavior, affecting convergence adversely.
Overlap far from notch.
Overlap near notch.
Notched Cylinder: Coupling Different Materials
Need to be careful to do domain decomposition so that material models are consistent in overlap region.

## Slide 31: Quasistatic Example #3: Laser Weld
Laser weld specimen
Problem of practical scale.
Isotropic elasticity and J2 plasticity with linear isotropic hardening.
Identical parameters for weld and base materials for proof of concept, to become independent models.
Coupled Schwarz discretization
(50% reduction in model size)
Single domain discretization
Notes: ~200K dofs

## Slide 32: Laser Weld: Strong Scalability of Parallel Schwarz with DTK
Near-ideal linear speedup (64-1024 cores).
Data Transfer Kit (DTK)

## Slide 33: Quasistatic Example #4: Tensile Bar
The alternating Schwarz method can be used as part of a homogenization (upscaling) process to bridge gap b/w microscopic and macroscopic regions
macro-scale
micro-structure
macro-scale
Work by C. Alleman, J. Foulk,
D. Littlewood, G. Bergel
  Microstructure embedded in ASTM tensile geometry (right).
  Fix microstructure, investigate ensemble of uniaxial loads.
  Fit flow curves with a macroscale J2 plasticity model (below).
  Goal: study strain localization in microstructure.
Notes: The last quasistatic example is another production-type problem known as the tensile bar problem and is courtesy of my colleagues Coleman Alleman, Jay Foulk, Dave Littlewood and Guy Bergel. This problem illustrates an interesting use of the Schwarz alternating method, in particular, that the method can be used as a part of a homogenization or upscaling process to bridge the gap between microscopic and macroscopic regions. Here, Coleman and his collaborators took a tensile geometry and embedded in it a microstructure, shown in the middle, with the goal of studying strain localization in the microstructure. The crystal plasticity microscale model in the microstructure was coupled to a J2 plasticity macroscale model in the rest of the domain using Schwarz, and a set of calculations were performed under an ensemble of uniaxial loads. Upscaling was performed by fitting flow curves to this set of ensembles using the J2 plasticity macroscale model.

## Slide 34
Outline
Alternating Schwarz Method for Coupling of Full Order Models (FOMs) in Solid Mechanics
  Motivation & Background
  Quasistatics
  Extension to Dynamics
  Summary & Next Steps
Alternating Schwarz Method for FOM-ROM* and ROM-ROM Coupling
  Motivation & Background
  Demonstration
  Ongoing & Future Work
* Projection-based Reduced Order Model

## Slide 35
Dynamic Solid Mechanics Formulation
Kinetic energy:
Potential Energy:
Lagrangian:
Action functional:
Euler-Lagrange equations:
Semi-discrete problem following FEM discretization in space:

## Slide 36
Schwarz Alternating Method for Dynamics
In the literature the Schwarz method is applied to dynamics by using space-time discretizations.
Overlapping non-matching meshes and time steps in dynamics.

## Slide 37
In the literature the Schwarz method is applied to dynamics by using space-time discretizations.
Overlapping non-matching meshes and time steps in dynamics.
Pro : Can use non-matching meshes and time-steps (see right figure).
Con : Unfeasible given the design of our current codes and size of simulations.
Schwarz Alternating Method for Dynamics

## Slide 38
Controller time stepper
Time integrator for W1
Time integrator for W2
Step 0: Initialize
Schwarz Alternating Method for Dynamic Multiscale Coupling
Controller time stepper: defines global s at which subdomains are synchronized
Notes: The final ingredient is what we call the ‘controller time-stepper’. The goal of the controller time-stepper is to define global time steps shown in blue in the figure at the top. It is at these controller time steps that the Schwarz subdomains will be synchronized, as will hopefully become apparent as I go through the algorithm.

## Slide 39
Integrate using
Interpolate from to
Controller time stepper
Time integrator for W1
Time integrator for W2
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Schwarz Alternating Method for Dynamic Multiscale Coupling
Controller time stepper: defines global s at which subdomains are synchronized

## Slide 40
Controller time stepper
Time integrator for W1
Time integrator for W2
Integrate using
Interpolate from to
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Step 2: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times .
Schwarz Alternating Method for Dynamic Multiscale Coupling
Controller time stepper: defines global s at which subdomains are synchronized

## Slide 41
Controller time stepper
Time integrator for W1
Time integrator for W2
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Step 2: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times .
Step 3: Check for convergence at time .
Schwarz Alternating Method for Dynamic Multiscale Coupling
Controller time stepper: defines global s at which subdomains are synchronized

## Slide 42
Controller time stepper
Time integrator for W1
Time integrator for W2
Interpolate from to
Integrate using
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Step 2: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times .
Step 3: Check for convergence at time .
If unconverged, return to Step 1.
Schwarz Alternating Method for Dynamic Multiscale Coupling
Controller time stepper: defines global s at which subdomains are synchronized

## Slide 43
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Step 2: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times .
Step 3: Check for convergence at time .
If unconverged, return to Step 1.
If converged, set and return to Step 1.
Controller time stepper
Time integrator for W1
Time integrator for W2
Integrate using
Interpolate from to
Schwarz Alternating Method for Dynamic Multiscale Coupling
Controller time stepper: defines global s at which subdomains are synchronized

## Slide 44
Schwarz Alternating Method for Dynamic Multiscale Coupling
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Step 2: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times .
Step 3: Check for convergence at time .
If unconverged, return to Step 1.
If converged, set and return to Step 1.
Controller time stepper
Time integrator for W1
Time integrator for W2
Integrate using
Interpolate from to
Can use different integrators with different time steps within each domain!
Controller time stepper: defines global s at which subdomains are synchronized

## Slide 45
Schwarz Alternating Method for Dynamic Multiscale Coupling: Theory
Like for quasistatics, dynamic alternating Schwarz method converges provided each single-domain problem is well-posed and overlap region is non-empty, under some conditions on .
Well-posedness for the dynamic problem requires that action functional be strictly convex or strictly concave, where is the Lagrangian.
  This is studied by looking at its second variation
We can show assuming a Newmark time-integration scheme that for the fully-discrete problem:
can always be made positive by choosing a sufficiently small
Numerical experiments reveal that requirements for stability/accuracy typically lead to automatic satisfaction of this bound.
*A. Mota, I. Tezaur, G. Phlipot. "The Schwarz alternating method for dynamic solid mechanics", IJNME, 2022.

## Slide 46
Implementation in Albany LCM & Sierra/SM
Numerical results shown here for dynamic Schwarz are from two codes: Albany LCM and Sierra/Solid Mechanics (Sierra/SM)
Albany LCM: Trilinos-based open-source* parallel, C++, multi-physics, FE code.
Sierra Mechanics Framework: Sandia Lagrangian 3D code for FEA of solids & structures.
Sierra/SM: quasistatics, implicit/explicit dynamics + loose coupling via Arpeggio
* https://github.com/SNLComputation/LCM
Notes: For the dynamical case, I am going to show results from two codes. The first of these, Albany LCM, I talked about earlier when I discussed the quasistatic case. Albany LCM is a Trilinos-based open-source parallel, C++ Multiphysics finite element code. After we did an initial implementation and prototyping of our Schwarz algorithm in Albany LCM, we proceeded to implement the method in Sandia’s production code, known as Sierra Solid Mechanics, or Sierra/SM. Sierra is a Sandia Lagrangian code for finite element analysis of solids and structures. It has a number of different modules, listed here. Sierra/SM consists of 3 modules known as Adagio, Presto and Arpeggio, which enable quasistatic, implicit/explicit dynamic, and loosely coupled solid mechanics analyses, respectively.

## Slide 47
Implementation in Albany LCM & Sierra/SM
Numerical results shown here for dynamic Schwarz are from two codes: Albany LCM and Sierra/Solid Mechanics (Sierra/SM)
Albany LCM: Trilinos-based open-source* parallel, C++, multi-physics, FE code.
Sierra Mechanics Framework: Sandia Lagrangian 3D code for FEA of solids & structures.
Sierra/SM: quasistatics, implicit/explicit dynamics + loose coupling via Arpeggio
Schwarz alternating method was “implemented” in Sierra/SM using Arpeggio loose coupling framework
* https://github.com/SNLComputation/LCM

## Slide 48
Implementation in Albany LCM & Sierra/SM
Numerical results shown here for dynamic Schwarz are from two codes: Albany LCM and Sierra/Solid Mechanics (Sierra/SM)
Albany LCM: Trilinos-based open-source* parallel, C++, multi-physics, FE code.
Sierra Mechanics Framework: Sandia Lagrangian 3D code for FEA of solids & structures.
Sierra/SM: quasistatics, implicit/explicit dynamics + loose coupling via Arpeggio
Schwarz alternating method was “implemented” in Sierra/SM using Arpeggio loose coupling framework
We did not have to write any code in Sierra/SM to implement Schwarz!
* https://github.com/SNLComputation/LCM

## Slide 49
Dynamic Example #1: Elastic Wave Propagation
Linear elastic clamped beam with Gaussian initial condition for the 𝑧-displacement.
Simple problem with analytical exact solution but very stringent test for discretization methods.
Test Schwarz with 2 subdomains: .
Left: Initial condition (blue) and final solution (red). Wave profile is negative of initial profile at time T = 1.0e-3.
Time-discretizations: Newmark (implicit, explicit)
Meshes: HEX, TET

## Slide 50
z-displacement
Table 1: Averaged (over times + domains) relative errors in z–displacement (blue) and z-velocity (green) for several different Schwarz couplings, 50% overlap volume fraction
LM = Lumped Mass, CM = Consistent Mass
z-velocity
 | Implicit-Implicit |  | Explicit(CM)-Implicit |  | Explicit(LM)-Implicit | 
Conformal HEX - HEX | 2.79e-3 | 7.32e-3 | 3.53e-3 | 8.70e-3 | 4.72e-3 | 1.19e-2
Nonconformal HEX - HEX | 2.90e-3 | 7.10e-3 | 2.82e-3 | 7.29e-3 | 2.84e-3 | 7.33e-3
TET - HEX | 2.79e-3 | 7.58e-3 | 3.52e-3 | 8.92e-3 | 4.72e-3 | 1.19e-2
Dynamic Schwarz coupling introduces no dynamic artifacts that are pervasive in other coupling methods!
Elastic Wave: Diff. Integrators, Same s

## Slide 51
Elastic Wave: Diff. Integrators, Diff. s
Figures above: Plots of displacement, velocity and acceleration for the elastic wave propagation problem using different time integrators (implicit and explicit) and different time steps (1e-2s and 2e-7s) for each subdomain, superimposed over the analytic single domain solution.
The analytic solution is indistinguishable from Schwarz solutions (hidden behind the solutions for (red) and (green))!
Displacement
Velocity
Acceleration

## Slide 52
Dynamic Example #2: Tension Specimen
+
Uniaxial aluminum cylindrical tensile specimen with inelastic J2 material model.
Domain decomposition into two subdomains (right): = ends, = gauge.
Nonconformal HEX + composite TET10 coupling via Schwarz.
Implicit Newmark time-integration with adaptive time-stepping algorithm employed in both subdomains.
Slight imperfection introduced at center of gauge to force necking upon pulling in vertical direction.

## Slide 53
Tension Specimen: Expected Result

## Slide 54
Tension Specimen: Disp. & EQPS
Average of ~3 Schwarz iterations/time step required for convergence to Schwarz tolerance of 1e-6.
y-displacement
EQPS*
*EQPS = Equivalent Plastic Strain
Notes: So, lets see what happens. The plots are showing the y-displacement and the nodal equivalent plastic strain in the specimen. You see a nice smooth transition of the solution between the two subdomains, and the method is able to simulate the necking behavior in the middle. It takes on average 3 Schwarz iterations/time step to achieve a relatively tight convergence tolerance of 1e-6.

## Slide 55
Tension Specimen: Domain Decomposition

## Slide 56
Tension Specimen: EQPS

## Slide 57
Tension Specimen: Cauchy Stress

## Slide 58
Dynamic Example #3: Bolted Joint Problem
bolts (Composite TET10), parts (HEX).
Inelastic J2 material model in both subdomains.
  steel
  steel component, aluminum (bottom) plate
Schwarz solution compared to single-domain solution on composite TET10 mesh.
BC: x-disp = 0.02 at T = 1.0e-3 on top of parts.
Run until T = 5.0e-4 w/ dt = 1e-5 + implicit Newmark with analytic mass matrix for composite tet 10s.
Problem of practical scale.

## Slide 59
Single
Schwarz
Bolted Joint Problem: Displacement

## Slide 60
Bolted Joint Problem: EQPS
Single
Schwarz

## Slide 61
Bolted Joint Problem: Convergence Rate
Figure above: Convergence behavior of the dynamic Schwarz algorithm for the bolted joint problem
Linear convergence rate is observed for dynamic Schwarz algorithm, as for the quasistatic Schwarz algorithm.

## Slide 62
Bolted Joint Problem: Performance
 | CPU times (64 procs*) | Avg # Schwarz iters | Max # Schwarz iters
Single Domain | 3h 34m |  | 
Schwarz | 2h 42m | 3.22 | 4
Single Domain (finer) | 17h 00m |  | 
Schwarz (finer mesh of bolts) | 29h 29m | 3.28 | 4
 | CPU times (64 procs*) | Avg # Schwarz iters | Max # Schwarz iters
Single Domain | 3h 34m |  | 
Schwarz | 2h 42m | 3.22 | 4
Single Domain (finer) | 17h 00m |  | 
Schwarz (finer mesh of bolts) | 29h 29m | 3.28 | 4
* On SNL ascicgpu15, 16, 17 machines (Intel Skylake CPU processor), Schwarz tol = 1e-6.
62

## Slide 63
Bolted Joint Problem: Performance
 | CPU times (64 procs*) | Avg # Schwarz iters | Max # Schwarz iters
Single Domain | 3h 34m |  | 
Schwarz | 2h 42m | 3.22 | 4
Single Domain (finer) | 17h 00m |  | 
Schwarz (finer mesh of bolts) | 29h 29m | 3.28 | 4
 | CPU times (64 procs*) | Avg # Schwarz iters | Max # Schwarz iters
Single Domain | 3h 34m |  | 
Schwarz | 2h 42m | 3.22 | 4
Single Domain (finer) | 17h 00m |  | 
Schwarz (finer mesh of bolts) | 29h 29m | 3.28 | 4
Despite its iterative nature, Schwarz can actually be faster than single domain run for discretizations having comparable # of elements in the bolts.
* On SNL ascicgpu15, 16, 17 machines (Intel Skylake CPU processor), Schwarz tol = 1e-6.
63

## Slide 64
Bolted Joint Problem: Performance
 | CPU times (64 procs*) | Avg # Schwarz iters | Max # Schwarz iters
Single Domain | 3h 34m |  | 
Schwarz | 2h 42m | 3.22 | 4
Single Domain (finer) | 17h 00m |  | 
Schwarz (finer mesh of bolts) | 29h 29m | 3.28 | 4
 | CPU times (64 procs*) | Avg # Schwarz iters | Max # Schwarz iters
Single Domain | 3h 34m |  | 
Schwarz | 2h 42m | 3.22 | 4
Single Domain (finer) | 17h 00m |  | 
Schwarz (finer mesh of bolts) | 29h 29m | 3.28 | 4
Despite its iterative nature, Schwarz can actually be faster than single domain run for discretizations having comparable # of elements in the bolts.
  Even if the method is more computationally expensive for some resolutions, it may be preferred for its ability to rapidly change and evaluate a variety of engineering designs (our typical use case).
* On SNL ascicgpu15, 16, 17 machines (Intel Skylake CPU processor), Schwarz tol = 1e-6.

## Slide 65
Bolted Joint Problem: Performance
Despite its iterative nature, Schwarz can actually be faster than single domain run for discretizations having comparable # of elements in the bolts.
  Even if the method is more computationally expensive for some resolutions, it may be preferred for its ability to rapidly change and evaluate a variety of engineering designs (our typical use case).
* On SNL ascicgpu15, 16, 17 machines (Intel Skylake CPU processor), Schwarz tol = 1e-6.
 | CPU times (64 procs*) | Avg # Schwarz iters | Max # Schwarz iters
Single Domain | 3h 34m |  | 
Schwarz | 2h 42m | 3.22 | 4
Single Domain (finer) | 17h 00m |  | 
Schwarz (finer mesh of bolts) | 29h 29m | 3.28 | 4
 | CPU times (64 procs*) | Avg # Schwarz iters | Max # Schwarz iters
Single Domain | 3h 34m |  | 
Schwarz | 2h 42m | 3.22 | 4
Single Domain (finer) | 17h 00m |  | 
Schwarz (finer mesh of bolts) | 29h 29m | 3.28 | 4
Dynamic Schwarz converges in between 2-4 Schwarz iterations per time-step despite the overlap region being very small for this problem.
overlap region

## Slide 66
Outline
Alternating Schwarz Method for Coupling of Full Order Models (FOMs) in Solid Mechanics
  Motivation & Background
  Quasistatics
  Extension to Dynamics
  Summary & Next Steps
Alternating Schwarz Method for FOM-ROM* and ROM-ROM Coupling
  Motivation & Background
  Demonstration
  Ongoing & Future Work
* Projection-based Reduced Order Model

## Slide 67
Summary
The Schwarz alternating method has been developed/implemented for concurrent multiscale quasistatic & dynamic modeling in Sandia’s Albany LCM and Sierra/SM codes.
Coupling is concurrent (two-way).
Ease of implementation into existing massively-parallel HPC codes.
Scalable, fast, robust (we target real engineering problems, e.g., analyses involving failure of bolted components!).
“Plug-and-play” framework: simplifies task of meshing complex geometries!
  Ability to couple regions with different non-conformal meshes, different element types and different levels of refinement.
  Ability to use different solvers/time-integrators in different regions.
Coupling does not introduce nonphysical artifacts.
Theoretical convergence properties/guarantees.









## Slide 68
Continuing to apply the Schwarz alternating method to problems of interest to production using Sierra/SM.
Advancing the Schwarz alternating method to enable coupling of structural elements to continuum elements.
Developing a Schwarz-like algorithm for simulating contact to address well-known challenges (contact constraint enforcement, multiple scales).
  Done by introducing a combination of Dirichlet and Neumann boundary conditions into different subdomains in a non-overlapping alternating fashion.
  See the following reference for more info:
Ongoing Work and Next Steps
J. Hoy, I. Tezaur, A. Mota. "The Schwarz alternating method for multiscale contact mechanics". in Computer Science Research Institute Summer Proceedings 2021, J.D. Smith and E. Galvan, eds., Technical Report SAND2021-0653R, Sandia National Labs, 360-378, 2021.
(https://www.sandia.gov/ccr/csri-summer-programs/2021-proceedings/)
Journal article with D. Koliesnikova in preparation.

## Slide 69
References – Part 1
[1] M.A. Heroux et al. “An overview of the Trilinos project.” ACM Trans. Math. Softw. 31(3) (2005)
[2] A. Salinger, et al. "Albany: Using Agile Components to Develop a Flexible, Generic Multiphysics Analysis Code", Int. J. Multiscale Comput. Engng. 14(4) (2016) 415-438.
[3] H. Schwarz. “Über einen Grenzübergang durch alternierendes Verfahren”. In: Vierteljahrsschriftder Naturforschenden Gesellschaft in Zurich 15 (1870), pp. 272–286.
[4] S.L. Sobolev. “Schwarz’s Algorithm in Elasticity Theory”. In: Selected Works of S.L Sobolev. Volume I: equations of mathematical physics, computational mathematics and cubature formulats. Ed. By G.V. Demidenko and V.L. Vaskevich. New York: Springer, 2006.
[5] S. Mikhlin. “On the Schwarz algorithm”. In: Proceedings of the USSR Academy of Sciences (in Russian) 77 (1951), pp. 569–571.
[6] D.J. Evans et al. “The convergence rate of the Schwarz alternating procedure (II): For two-dimensional problems”. In: International Journal for Computer Mathematics 20.3–4 (1986), pp. 325–339.
[7] P.L. Lions. “On the Schwarz alternating method I.” In: 1988, First International Symposium on Domain Decomposition methods for Partial Differential Equations, SIAM, Philadelphia.
[8] SIERRA Solid Mechanics Team. Sierra/Solid Mechanics 4.48 User’s Guide. Tech. rep. SAND2018-2961. Sandia National Laboratories Report, Oct. 2018.
[9] A. Mota, I. Tezaur, C. Alleman. "The Schwarz Alternating Method in Solid Mechanics", Comput. Meth. Appl. Mech. Engng. 319 (2017), 19-51.
[10] A. Mota, I. Tezaur, G. Phlipot. "The Schwarz Alternating Method for Dynamic Solid Mechanics”, Comput. Meth. Appl. Mech. Engng. 121 (21) (2022) 5036-5071.

## Slide 70
Outline
Alternating Schwarz Method for Coupling of Full Order Models (FOMs) in Solid Mechanics
  Motivation & Background
  Quasistatics
  Extension to Dynamics
  Summary & Next Steps
Alternating Schwarz Method for FOM-ROM* and ROM-ROM Coupling
  Motivation & Background
  Demonstration
  Ongoing & Future Work
* Projection-based Reduced Order Model

## Slide 71
The past decades have seen tremendous investment in simulation frameworks for coupled multi-scale and multi-physics problems.
Monolithic (Lagrange multipliers)
Partitioned (loose) coupling
Iterative (Schwarz, optimization)
M1
M2
M3
M4
N3
N4
N1
N2
N5
N3
N4
N5
N2
N1
PDEs, ODEs
Nonlocal integral
Classical DFT
Atomistic, …
Mesh-based (FE, FV, FD)
Meshless (SPH, MLS)
Implicit, explicit
Eulerian, Lagrangian, …
Complex System Model
Traditional Methods
Coupled Numerical Model
Ocean
(MPAS-O)
Atmos.
(EAM)
Sea Ice
(MPAS-SI)
Land Ice
(MALI)
Land
(ALM)
Traditional + Data-Driven Methods
PINNs
Neural ODEs
Projection-based ROMs, …
Motivation
Frameworks rely on established mathematical theories to couple physics components.
Most existing coupling frameworks are based on traditional discretization methods.

## Slide 72
The past decades have seen tremendous investment in simulation frameworks for coupled multi-scale and multi-physics problems.
Frameworks rely on established mathematical theories to couple physics components.
Most existing coupling frameworks are based on traditional discretization methods.
Monolithic (Lagrange multipliers)
Partitioned (loose) coupling
Iterative (Schwarz, optimization)
M1
M2
M3
M4
N3
N4
N1
N2
N5
N3
N4
N5
N2
N1
PDEs, ODEs
Nonlocal integral
Classical DFT
Atomistic, …
Mesh-based (FE, FV, FD)
Meshless (SPH, MLS)
Implicit, explicit
Eulerian, Lagrangian, …
Complex System Model
Traditional Methods
Coupled Numerical Model
Ocean
(MPAS-O)
Atmos.
(EAM)
Sea Ice
(MPAS-SI)
Land Ice
(MALI)
Land
(ALM)
DMD=N3
ROM=N4
N1
PINN=N2
UDE=N5
Traditional + Data-Driven Methods
PINNs
Neural ODEs
Projection-based ROMs, …
Unfortunately, existing algorithmic and software infrastructures are ill-equipped to handle plug-and-play integration of non-traditional, data-driven models!
There is currently a big push to integrate data-driven methods into modeling & simulation toolchains.
Motivation

## Slide 73
Alternating Schwarz-based coupling
Optimization-based coupling
Coupling via generalized mortar methods
Principal research objective:
Discover mathematical principles guiding the assembly of standard and data-driven numerical models in stable, accurate and physically consistent ways.
Principal research challenges: we lack mathematical and algorithmic understanding of how to
“Mix-and-match” standard and data-driven models from three-classes
  Class A: projection-based reduced order models (ROMs)
  Class B: machine-learned models, i.e., Physics-Informed Neural Networks (PINNs)
  Class C: flow map approximation models, i.e., dynamic model decomposition (DMD) models
Ensure well-posedness & physical consistency of resulting heterogeneous models.
Solve such heterogeneous models efficiently.
Three coupling methods:
Flexible Heterogeneous Numerical Methods (fHNM) Project
This talk.
This talk.
Notes: Class A and B are equation-based DDMs: they seek restrict a weak or strong form of the PDE to a finite-dimensional function space 𝑈_𝑖, spanned by a basis {𝑏_𝑖^𝑘 }_(𝑘=1)^(𝑁_𝑖 )
Class C DDMs are equation-free I/O relations 𝑢_𝑖 (𝑡)=〖𝐺_𝑖 (𝑓〗_𝑖,𝑢_(𝑖,0);𝑝_(𝑖,1),⋯,𝑝_(𝑖,𝑃)) with inputs (“ports”) 𝑝_(𝑖,𝑗).
TODO: add refs to other talks in MS.

## Slide 74: Projection-Based Model Order Reduction via the POD/Galerkin Method
Full Order Model (FOM):
Proper Orthogonal Decomposition (POD):
Solve ODE at different design points
1. Acquisition
2. Learning
3. Projection-Based Reduction
Number of time steps
Number of State Variables
Save solution data
Reduce the number of unknowns
Perform Galerkin projection
+
Hyper-reduce nonlinear terms
Hyper-reduction/sample mesh
ROM = Projection-Based Reduced Order Model. HROM = Hyper-Reduced ROM

## Slide 75: Schwarz Extensions to FOM-ROM and ROM-ROM Couplings
Enforcement of Dirichlet boundary conditions (DBCs) in ROM at indices
Method I in [Gunzburger et al. 2007] is employed
Choice of domain decomposition
Error-based indicators that help decide in what region of the domain a ROM can be viable should drive domain decomposition (future work) [Bergmann et al. 2018]
,
POD modes made to satisfy homogeneous DBCs:
BCs imposed by modifying , , : , ,
Snapshot collection and reduced basis construction
Ideally, generate snapshots/reduced bases separately in each subdomain [Hoang et al. 2021, Smetana et al., 2022]
POD results presented herein use snapshots obtained via FOM-FOM coupling on
For nonlinear problems, hyper-reduction needs to preserve Hamiltonian structure
We employ Energy-Conserving Sampling & Weighting Method (ECSW) [Farhat et al. 2015]
Investigating structure-preserving coupling is near-term future work.

## Slide 76
Outline
Alternating Schwarz Method for Coupling of Full Order Models (FOMs) in Solid Mechanics
  Motivation & Background
  Quasistatics
  Extension to Dynamics
  Summary & Next Steps
Alternating Schwarz Method for FOM-ROM* and ROM-ROM Coupling
  Motivation & Background
  Demonstration
  Ongoing & Future Work
* Projection-based Reduced Order Model

## Slide 77: Numerical Example: 1D Dynamic Wave Propagation Problem
1D beam geometry , clamped at both ends, with Gaussian initial condition discretized using FEM + Newmark-
Simple problem but very stringent test for discretization/ coupling methods.
Two constitutive models considered:
  Linear elastic (problem has exact analytical solution)
  Nonlinear hyperelastic Henky
ROMs results are reproductive and predictive, and are based on the POD/Galerkin method, with POD calculated from FOM-FOM coupled model.
  50 POD modes capture 100% snapshot energy for linear variant of this problem.
  536 POD modes capture ~100% snapshot energy for Henky variant of this problem.
Hyper-reduced ROMs (HROMs) perform hyper-reduction using ECSW [Farhat et al., 2015]
  Ensures that Lagrangian structure of problem is preserved in HROM.
Couplings tested: overlapping, non-overlapping, FOM-FOM, FOM-ROM, ROM-ROM, FOM-HROM, HROM-HROM, implicit-explicit, implicit-implicit, explicit-explicit.
Figure: POD energy decay for nonlinear Henky problem
This talk.
This talk.

## Slide 78: Numerical Example: 1D Dynamic Wave Propagation Problem
Two variants of problem, with different initial conditions (ICs):
  Symmetric Gaussian IC (top right)
  Rounded Square IC (bottom right)
Non-overlapping domain decomposition (DD) of where = [0, 0.6] and = [0.6, 1.0]
  DD based on heuristics: during time-interval considered (), sharper gradient forms in , suggesting FOM or larger ROM is needed there.
Reproductive problem:
  Displacement snapshots collected using FOM-FOM non-overlapping coupling with Symmetric Gaussian IC
  FOM-ROM, FOM-HROM, ROM-ROM and HROM-HROM run with Symmetric Gaussian IC
Predictive problem:
  Snapshots same as for reproductive problem.
  FOM-ROM, FOM-HROM, ROM-ROM and HROM-HROM run with Rounded Square IC
Figure above: Symmetric Gaussian IC
Figure below: Rounded Square IC

## Slide 79: Numerical Example: Reproductive Results
All coupled models evaluated converged on average in 3 Schwarz iterations per time-step
FOM-ROM coupling has same total # Schwarz iters () as FOM-FOM coupling
Other couplings require more Schwarz iters than FOM-FOM coupling to converge
  More Schwarz iters required when coupling less accurate models
  Larger 300/80 mode ROM-ROM takes less time than smaller 200/80 mode ROM-ROM
FOM-HROM & HROM-HROM couplings outperform FOM-FOM coupling in CPU time by 12.5-32.6%
All couplings involving ROMs/HROMs are at least as accurate as single-domain ROMs/HROMs
Green shading highlights most competitive coupled models

## Slide 80: Numerical Example: Reproductive Results
Single-domain ROM and HROM are most efficient
Couplings involving ROMs and HROMs enable one to achieve smaller errors
Benefits of hyper-reduction are limited on 1D problem

## Slide 81
Figure left: FOM (green) – HROM (cyan) coupling compared with single-domain FOM solution (blue). HROM has 200 modes.
Figure below: ECSW algorithm samples 253/400 elements
Numerical Example: Reproductive Results

## Slide 82: Numerical Example: Predictive Results
Predictive accuracy/robustness can be improved by coupling ROM or HROM to FOM
  FOM-ROM coupling is remarkably accurate, achieving displacement error O()
  FOM-HROM and ROM-ROM couplings are more accurate than single-domain ROMs
  HROM-HROM on par with single-domain HROM in terms of accuracy
Wall-clock times of coupled models can be improved
  FOM-HROM, ROM-ROM and HROM-HROM models are slower than FOM-FOM model as more Schwarz iterations required to achieve convergence
  Hyper-reduction samples 60% of total mesh points
    Greater gains from hyper-reduction anticipated for 2D/3D problems

## Slide 83: Numerical Example: Predictive Results
Predictive single-domain ROM (= 300) solution at final time
Predictive FOM-HROM (= 200) solution at final time
Predictive single-domain ROM solution exhibits spurious oscillations in velocity and acceleration
Predictive FOM-HROM solution is smooth and oscillation-free
  Highlights coupling method’s ability to improve ROM predictive accuracy
Single-domain FOM solution
Solution in Solution in

## Slide 84: Numerical Example: Predictive Results
Predictive single-domain ROM (= 300)
Predictive FOM-HROM (= 200)
Single-domain FOM solution
Solution in Solution in

## Slide 85
Outline
Alternating Schwarz Method for Coupling of Full Order Models (FOMs) in Solid Mechanics
  Motivation & Background
  Quasistatics
  Extension to Dynamics
  Summary & Next Steps
Alternating Schwarz Method for FOM-ROM* and ROM-ROM Coupling
  Motivation & Background
  Demonstration
  Ongoing & Future Work
* Projection-based Reduced Order Model

## Slide 86: Ongoing & Future Work
Ongoing Work
Extension to multi-material problems (method works; results not shown herein).
Development of additive Schwarz variant, which has more potential for parallelization and speed-ups (preliminary FOM-FOM results show promise).
Extension of method to multi-D through newly-developed Python code, pressio-demoapps1 library and/or 3D solid mechanics Julia code2.
  Multi-D implementation requires transfer operators for transmission BCs
Journal publication on results presented here + 2D/3D results.
Alternating Schwarz-based coupling of Physics-Informed Neural Networks (PINNs)
Next Steps
Development of smart DD approaches based on error indicators, to determine optimal placement of ROM and FOM (including on-the-fly ROM-FOM switching).
Analysis of method’s convergence properties for non-overlapping and ROM/HROM coupling cases.
Extension of coupling approach to POD modes built from snapshots on independently-simulated subdomains.
Application to other problems, including multi-physics problems.
Structure-preservation within ROMs and couplings involving ROMs
1 https://github.com/Pressio/pressio-demoapps, 2 https://github.com/lxmota/norma

## Slide 87
References – Part 2
[11] M. Gunzburger, J. Peterson, J. Shadid. “Reduced-order modeling of time-dependent PDEs with multiple parameters in the boundary data”. CMAME 196 (2007) 1030-1047.
[12] C. Hoang, Y. Choi, K. Carlberg. “Domain-decomposition least-squares Petrov–Galerkin (DD-LSPG) nonlinear model reduction”. CMAME 384 (2021) 113997.
[13] K. Smetana, T. Taddei. “Localized model reduction for nonlinear elliptic partial differential equations: localized training, partition of unity, and adaptive enrichment”, ArXiV pre-print, 2022.
[14] C. Farhat, T. Chapman, P. Avery. “Structure-preserving, stability, and accuracy properties of the energy-conserving sampling and weighting method for the hyper reduction of nonlinear finite element dynamic models”, IJNME 102 (2015) 1077-1110.
[15] M. Bergmann, A. Ferrero, A. Iollo, E. Lombardi, A. Scardigli, H. Telib. “A zonal Galerkin-free POD model for incompressible flows.” JCP 352 (2018) 301-325.
[16] A. Iollo, G. Sambataro, T. Taddei. “A one-shot overlapping Schwarz method for component-based model reduction: application to nonlinear elasticity”, CMAME 404 (2023) 115786.
[17] J. Hoy, I. Tezaur, A. Mota. "The Schwarz alternating method for multiscale contact mechanics". in Computer Science Research Institute Summer Proceedings 2021, J.D. Smith and E. Galvan, eds., Technical Report SAND2021-0653R, Sandia National Labs, 360-378, 2021.
[18] J. Barnett, I. Tezaur, A. Mota. "The Schwarz alternating method for the seamless coupling of nonlinear reduced order models and full order models", in Computer Science Research Institute Summer Proceedings 2022, S.K. Seritan and J.D. Smith, eds., Technical Report SAND2022-10280R, Sandia National Laboratories, 2022, pp. 31-55.

## Slide 88: Careers at Sandia National Labs
Students: please consider Sandia and other national labs as a potential employer for summer internships and when you graduate!
Sandia is a multidisciplinary national lab and Federally Funded Research & Development Center (FFRDC).
Contractor for U.S. DOE’s National Nuclear Security Administration (NNSA).
Two main sites: Albuquerque, NM and Livermore, CA

## Slide 89: Careers at Sandia National Labs
Students: please consider Sandia and other national labs as a potential employer for summer internships and when you graduate!
Sandia is a great place to work!
  Lots of interesting problems that require fundamental research in applied math/computational science and impact mission-critical applications.
  Great work/life balance.
Opportunities at/with Sandia:
  Interns (summer, year-round)
  Post docs
  Several prestigious post doctoral fellowships (von Neumann, Truman, Hruby, Data Science)
  Staff
Please see: www.sandia.gov/careers for info about current opportunities.

## Slide 90: Careers at Sandia National Labs
Left: current postings from www.sandia.gov/careers for Summer 2023. Summer interns are hired by early March.
I am hiring interns to help with ROM-ROM/ROM-FOM coupling work!
If interested, email me (ikalash@sandia.gov) and apply to the CSRI Internship Posting (left).

## Slide 91
Start of Backup Slides

## Slide 92
Full Schwarz
Modified Schwarz
Inexact Schwarz
Monolithic Schwarz
*A. Mota, I. Tezaur, C. Alleman. "The Schwarz Alternating Method in Solid Mechanics", CMAME 319 (2017), 19-51.
Appendix. Four Variants* of Schwarz

## Slide 93
Appendix. Four Variants* of Schwarz
Full Schwarz
Modified Schwarz
Inexact Schwarz
Monolithic Schwarz
Modified and Monolithic Schwarz variants create and solve a block system.
*A. Mota, I. Tezaur, C. Alleman. "The Schwarz Alternating Method in Solid Mechanics", CMAME 319 (2017), 19-51.

## Slide 94
Appendix. Four Variants* of Schwarz
Full Schwarz
Modified Schwarz
Inexact Schwarz
Monolithic Schwarz
Most performant method: monotonic convergence, theoretical convergence guarantee.
*A. Mota, I. Tezaur, C. Alleman. "The Schwarz Alternating Method in Solid Mechanics", CMAME 319 (2017), 19-51.

## Slide 95
Appendix. Full Schwarz Method
Classical algorithm originally proposed by Schwarz with outer Schwarz loop and inner Newton loop, each converged to a tight tolerance (

## Slide 96
Appendix. Inexact Schwarz Method
Classical algorithm originally proposed by Schwarz with outer Schwarz loop and inner Newton loop, with Newton step converged to a loose tolerance

## Slide 97
Appendix. Monolithic Schwarz Method
Combines Schwarz and Newton loop into since Newton-Schwarz loop, with elimination of Schwarz boundary DOFs, and tight convergence tolerance.
Advantages:
By-passes Schwarz loop.
Disadvantages:
Off-diagonal coupling terms block linear solver is needed.

## Slide 98
Appendix. Modified Schwarz Method
Combines Schwarz and Newton loop into since Newton-Schwarz loop, with Schwarz boundaries at Dirichlet boundaries and tight convergence tolerance.
Least-intrusive variant: by-passes Schwarz iteration, no need for block solver.
Advantages:
By-passes Schwarz loop.
No diagonal coupling (conventional linear solver can be used in each subdomain).

## Slide 99: Appendix. Foulk’s Singular Bar
1D proof of concept problem:
  1D bar with area proportional to square root of length.
  Strong singularity on left end of bar.
  Simple hyperelestic material model with no damage.
  MATLAB implementation.
Problem goals:
  Explore viability of 4 variants of the Schwarz alternating method.
  Test convergence and compare with literature (Evans, 1986).
    Expect faster convergence in fewer iterations with increased overlap.

## Slide 100: Appendix. Singular Bar and Schwarz Variants
Notes: Linear convergence for all methods (bottom left)
Monolithic Schwarz converges faster but timings are similar -> all implementations are interchangeable (bottom right)
Amount of overlap critical for convergence (top right)

## Slide 101: Appendix. Multiscale Modeling of Localization
Region of localization (necking)
  Goals:
  Connect physical length scales to engineering scale models.
  Investigate importance of microstructural detail.
  Develop bridging technologies for spatial multiscale/ multiphysics.
Region of localization (fracture)
  Strain localization can cause localized necking (left) and ultimately fracture (above).
Notes: Strain localization is a ubiquitous feature of elastoplastic materials undergoing nonhomogeneous deformation. The phenomenon manifests in the form of a shear band, a narrow zone of intense straining across which some kinematical fields in a deforming body may be discontinuous.
Strain localization can cause local necking and ultimately fracture.

## Slide 102: Appendix. Parallelization via DTK: Weak Scaling on Cubes Problem
1 Processor,
2.5*103 DOF / proc
8 Processors,
2.1*103 DOF / proc
64 Processors,
1.9*103 DOF / proc

## Slide 103: Appendix. Parallelization via DTK: Strong Scaling on Cubes Problem
Small problem (2.5*103 DOFs)
Medium problem (1.7*104 DOFs)
176 DOF/processor
107 DOF/processor
Large problem (1.6*105 DOFs)
5124 DOF/processor

## Slide 104
Appendix. Notched Cylinder: HEX-HEX Coupling
Notes: For completeness, I will show results for several different discretizations of these two regions, Omega1 and Omega2. In the first one, we discretize each region using a conformal hex mesh, and compute errors with respect to a solution on a single domain mesh that is conformal with each of these meshes. The table at the bottom of the slide shows displacement relative errors as a function of the Schwarz tolerance. You can see that as you decrease the Schwarz tolerance, the errors approach machine precision, meaning in the absence of other sources of error such as geometric error, the Schwarz method does not introduce any error into the discretization.

## Slide 105
Appendix. Notched Cylinder: Nonconformal HEX - HEX Coupling
Notes: We next look at a coupling in which Omega1 and Omega2 are discretized using hex meshes of comparable resolution but that are nonconformal with each other.

## Slide 106
Appendix. Notched Cylinder: Nonconformal HEX - HEX Coupling
Notes: Here, the errors in each of the subdomains are of the order of 10^(-4)-10^(-3) regardless of the Schwarz tolerance. It may seem that there is a problem here, but if you plot the errors in each of the subdomains (shown here), it’s clear what is happening: the dominant error is geometric error due to the Schwarz meshes not being able to represent the curved geometry as well as the single-domain reference mesh. This geometric error has nothing to do with the Schwarz coupling.

## Slide 107
Appendix. Rubiks Cube Problem
plotting axial
stress
concurrent coupling
Two distinct bodies, the component scale and the microstructural scale, are coupled iteratively with alternating Schwarz
component
scale
distinct
models
microstructural
scale
Work by J. Foulk, D. Littlewood, C. Battaile, H. Lim

## Slide 108: Appendix. Tensile Bar
Embed microstructure in ASTM tensile geometry

## Slide 109: Appendix. Tensile Bar: Meso-Macroscale Coupling
+
Mesoscale
Macroscale
SPARKS-generated microstructure (F. Abdeljawad)
Fix microstructure, investigate ensembles
151 axial vectors from 3 of the 10 ensembles of random rotations
(blue, green, red)
Load microstructural ensembles in uniaxial stress
Fit flow curves with a macroscale J2 plasticity model
Notes: \text{cubic elastic constant}: C_{11} = 204.6 \; \text{GPa} \\
\text{cubic elastic constant}: C_{12} = 137.7 \; \text{GPa} \\
\text{cubic elastic constant}: C_{44} = 126.2 \; \text{GPa} \\
\text{reference shear rate}: \dot{\gamma}_{0} = 1.0 \; \text{1/s} \\
\text{rate sensitivity factor}: m = 20 \\
\text{hardening rate parameter}: \dot{g_{0}} = 2.0 \times 10^{4} \; \text{1/s} \\
\text{initial hardness}: g_{0} = 90 \; \text{MPa} \\
\text{saturation hardness}: g_{s} = 202 \; \text{MPa} \\
\text{saturation exponent}: \omega = 0.01
\text{Young's modulus}: E = 195.0 \; \text{GPa} \\
\text{Poission's ratio}: \nu = 0.3 \\
\text{yield stress}: \sigma_{0} = 144 \; \text{MPa} \\
\text{hardening modulus}: H = 300 \; \text{MPa} \\
\text{saturation modulus}: S = 170 \; \text{MPa} \\
\text{saturation exponent}: \alpha = 190
\sigma_{y} = \sigma_{0} + H \epsilon_{p} + S (1 - e^{-\alpha \epsilon_{p}})

## Slide 110: Appendix. Tensile Bar: Results
Reduction in cross-sectional area over time

## Slide 111
Appendix. Schwarz Alternating Method
for Dynamics
In the literature the Schwarz method is applied to dynamics by using space-time discretizations.
This was deemed unfeasible given the design of our current codes and size of simulations.
Overlapping non-matching meshes and time steps in dynamics.

## Slide 112
Appendix. A Schwarz-like Time Integrator
We developed an extension of Schwarz coupling to dynamics using a governing time stepping algorithm that controls time integrators within each domain.
Can use different integrators with different time steps within each domain.
1D results show smooth coupling without numerical artifacts such as spurious wave reflections at boundaries of coupled domains.
Controller time stepper
Time integrator for W1
Time integrator for W2

## Slide 113
Schwarz Alternating Method for Dynamic Multiscale Coupling: Theory
Our dynamic alternating Schwarz algorithm can be interpreted as applying the traditional Schwarz alternating iterations in space-time between and
This interpretation does not require the method to be implemented using a space-time framework.
Notes: As before, lets talk about theory, this time for the dynamic case. In deriving a proof of convergence for our dynamic Schwarz algorithm, it is helpful to recognize that the algorithm can be interpreted as applying the traditional Schwarz alternating iterations in space-time between Omega1 x I_k and Omega2 x I_k, wher I_k is a particular time-slap, as shown in the picture on the right. I emphasize that this interpretation does not require the method to be implemented using a space-time framework, which we do not do.

## Slide 114: Appendix. Sierra/SM: Dynamic Schwarz Coupling
tension.i

## Slide 115: Appendix. Sierra/SM: Dynamic Schwarz Coupling
ends.i
gauge.i

## Slide 116: Appendix. Sierra/SM: Dynamic Schwarz Coupling
schwarz_funcs.i
schwarz_vars.i
solver.i

## Slide 117
Appendix. Dynamic Singular Bar
Inelasticity masks problems by introducing energy dissipation.
Schwarz does not introduce numerical artifacts.
Can couple domains with different time integration schemes (Explicit-Implicit below).

## Slide 118
Appendix. Elastic Wave: Energy Conservation
For clamped beam problem, total energy (TE = ) should be conserved.
Total energy is calculated in 2 ways: with most of contribution from and from
Total energy is conserved and matches single-domain total energy.

## Slide 119
Appendix: Some Schwarz Performance Data
Max / Avg # Schwarz iterations during run
 | Impl-impl dt=1e-6, Schwarz tol=1e-6 | Impl-impl dt=1e-7, Schwarz tol=1e-6 | Impl-impl dt=1e-7, Schwarz tol=1e-10 | Impl-impl dt=1e-7, Schwarz tol=1e-15 | Expl-impl dt=1e-7 Schwarz tol=1e-6 | Expl-impl dt=1e-8 Schwarz tol=1e-6
Hex-Hex | 3 / 2.23 | 3 / 2.08 |  | 4 / 2.83 | 2 / 2.0 | 
Tet-Hex |  |  |  |  | 2 / 2.0 | 
Nonconformal Hex-Hex |  | 2 / 2.0 | 3 / 2.36 |  | 2 / 2.0 | 2 / 1.54

## Slide 120
Appendix: Some Schwarz Performance Data
Max / Avg # Schwarz iterations during run
 | Impl-impl dt=1e-6, Schwarz tol=1e-6 | Impl-impl dt=1e-7, Schwarz tol=1e-6 | Impl-impl dt=1e-7, Schwarz tol=1e-10 | Impl-impl dt=1e-7, Schwarz tol=1e-15 | Expl-impl dt=1e-7 Schwarz tol=1e-6 | Expl-impl dt=1e-8 Schwarz tol=1e-6
Hex-Hex | 3 / 2.23 | 3 / 2.08 |  | 4 / 2.83 | 2 / 2.0 | 
Tet-Hex |  |  |  |  | 2 / 2.0 | 
Nonconformal Hex-Hex |  | 2 / 2.0 | 3 / 2.36 |  | 2 / 2.0 | 2 / 1.54
As Schwarz tolerance is tightened, number of Schwarz iterations goes up (as expected)

## Slide 121
Appendix: Some Schwarz Performance Data
Max / Avg # Schwarz iterations during run
 | Impl-impl dt=1e-6, Schwarz tol=1e-6 | Impl-impl dt=1e-7, Schwarz tol=1e-6 | Impl-impl dt=1e-7, Schwarz tol=1e-10 | Impl-impl dt=1e-7, Schwarz tol=1e-15 | Expl-impl dt=1e-7 Schwarz tol=1e-6 | Expl-impl dt=1e-8 Schwarz tol=1e-6
Hex-Hex | 3 / 2.23 | 3 / 2.08 |  | 4 / 2.83 | 2 / 2.0 | 
Tet-Hex |  |  |  |  | 2 / 2.0 | 
Nonconformal Hex-Hex |  | 2 / 2.0 | 3 / 2.36 |  | 2 / 2.0 | 2 / 1.54
Left: time vs. # Schwarz iterations (per time step) – behavior is as expected given nature of solution/domain decomposition

## Slide 122
Appendix: Some Schwarz Performance Data
Max / Avg # Schwarz iterations during run
 | Impl-impl dt=1e-6, Schwarz tol=1e-6 | Impl-impl dt=1e-7, Schwarz tol=1e-6 | Impl-impl dt=1e-7, Schwarz tol=1e-10 | Impl-impl dt=1e-7, Schwarz tol=1e-15 | Expl-impl dt=1e-7 Schwarz tol=1e-6 | Expl-impl dt=1e-8 Schwarz tol=1e-6
Hex-Hex | 3 / 2.23 | 3 / 2.08 |  | 4 / 2.83 | 2 / 2.0 | 
Tet-Hex |  |  |  |  | 2 / 2.0 | 
Nonconformal Hex-Hex |  | 2 / 2.0 | 3 / 2.36 |  | 2 / 2.0 | 2 / 1.54

## Slide 123
Appendix: Some Schwarz Performance Data
Max / Avg # Schwarz iterations during run
 | Impl-impl dt=1e-6, Schwarz tol=1e-6 | Impl-impl dt=1e-7, Schwarz tol=1e-6 | Impl-impl dt=1e-7, Schwarz tol=1e-10 | Impl-impl dt=1e-7, Schwarz tol=1e-15 | Expl-impl dt=1e-7 Schwarz tol=1e-6 | Expl-impl dt=1e-8 Schwarz tol=1e-6
Hex-Hex | 3 / 2.23 | 3 / 2.08 |  | 4 / 2.83 | 2 / 2.0 | 
Tet-Hex |  |  |  |  | 2 / 2.0 | 
Nonconformal Hex-Hex |  | 2 / 2.0 | 3 / 2.36 |  | 2 / 2.0 | 2 / 1.54

## Slide 124
Appendix: Some Schwarz Performance Data
Max / Avg # Schwarz iterations during run
 | Impl-impl dt=1e-6, Schwarz tol=1e-6 | Impl-impl dt=1e-7, Schwarz tol=1e-6 | Impl-impl dt=1e-7, Schwarz tol=1e-10 | Impl-impl dt=1e-7, Schwarz tol=1e-15 | Expl-impl dt=1e-7 Schwarz tol=1e-6 | Expl-impl dt=1e-8 Schwarz tol=1e-6
Hex-Hex | 3 / 2.23 | 3 / 2.08 |  | 4 / 2.83 | 2 / 2.0 | 
Tet-Hex |  |  |  |  | 2 / 2.0 | 
Nonconformal Hex-Hex |  | 2 / 2.0 | 3 / 2.36 |  | 2 / 2.0 | 2 / 1.54

## Slide 125
Appendix: Some Schwarz Performance Data
Max / Avg # Schwarz iterations during run
 | Impl-impl dt=1e-6, Schwarz tol=1e-6 | Impl-impl dt=1e-7, Schwarz tol=1e-6 | Impl-impl dt=1e-7, Schwarz tol=1e-10 | Impl-impl dt=1e-7, Schwarz tol=1e-15 | Expl-impl dt=1e-7 Schwarz tol=1e-6 | Expl-impl dt=1e-8 Schwarz tol=1e-6
Hex-Hex | 3 / 2.23 | 3 / 2.08 |  | 4 / 2.83 | 2 / 2.0 | 
Tet-Hex |  |  |  |  | 2 / 2.0 | 
Nonconformal Hex-Hex |  | 2 / 2.0 | 3 / 2.36 |  | 2 / 2.0 | 2 / 1.54

## Slide 126
Appendix: Some Schwarz Performance Data
Max / Avg # Schwarz iterations during run
 | Impl-impl dt=1e-6, Schwarz tol=1e-6 | Impl-impl dt=1e-7, Schwarz tol=1e-6 | Impl-impl dt=1e-7, Schwarz tol=1e-10 | Impl-impl dt=1e-7, Schwarz tol=1e-15 | Expl-impl dt=1e-7 Schwarz tol=1e-6 | Expl-impl dt=1e-8 Schwarz tol=1e-6
Hex-Hex | 3 / 2.23 | 3 / 2.08 |  | 4 / 2.83 | 2 / 2.0 | 
Tet-Hex |  |  |  |  | 2 / 2.0 | 
Nonconformal Hex-Hex |  | 2 / 2.0 | 3 / 2.36 |  | 2 / 2.0 | 2 / 1.54

## Slide 127
Appendix. Elastic Wave Propagation
Left figure shows # of iterations as a function of overlap region size for 2 subdomains. The method does not converge for 0% overlap. If the overlap is 100% then the single-domain solution is recovered for each of the subdomains.
Right figure shows linear convergence rate of dynamic Schwarz implementation (for small overlap fraction of 0.2%).
Some Performance Results

## Slide 128
Appendix. Torsion Problem
Nonlinear elastic bar (Neohookean material model) subjected to a high degree of torsion.
The domain is .
We evaluate dynamic Schwarz with 2 subdomains: .
Time-discretizations: Newmark (implicit, explicit) with same .
Meshes: HEX, Composite TET10.
Notes: Example 2 is again from the Albany LCM implementation and is slightly more sophisticated. We have a nonlinear elastic bar subjected to a high degree of torsion, so we basically twist the bar. We decompose the domain into 2 subdomains, shown on the right, and evaluate coupling of different elements (HEX, Composite TET10) as well as different time-discretizations (implicit and explicit Newmark).

## Slide 129
Appendix. Torsion: HEX - HEX Coupling
Schwarz and single-domain results agree to almost machine-precision!
Each subdomain discretized using uniform HEX mesh with , and advanced in time using implicit Newmark-Beta scheme with 1e-6.
Results compared to single-domain solution on mesh conformal with Schwarz domain meshes.
Displacement relative errors at final time (T=0.002)
Velocity relative errors at final time (T=0.002)
Notes: As for the quasistatic examples I showed, we start by discretizing the two meshes using uniform conformal hex meshes and compute errors w.r.t. a single domain solution computed on a mesh that is conformal to the two Schwarz meshes. This study reveals that the solutions agree to almost machine precision.

## Slide 130
Appendix. Torsion: HEX - CTET10 Coupling
Coupling of Composite TET10 elements + explicit Newmark with consistent mass in with HEX elements + implicit Newmark in
Reference solution is computed on fine hex mesh + implicit Newmark
Movie of |displacement|
Left: Single-domain,
Right: Schwarz
No dynamic artifacts!
Relative error <1% and does not grow in time!
Notes: Having done this initial verification, we proceed to couple two different element types: hex elements in Omega0 and composite tet10 elements in Omega1 (the composite tet10 is a 10-node tetrahedral element designed in our group specifically for solid mechanics problems). We also use different time-integrators (explicit Newmark in Omega0 and implicit Newmark in Omega1). The movie shows the norm of the displacement for the single domain solution on the left and the Schwarz solution on the right. The solutions are indistinguishable and their relative difference is <1% for all times, and does not grow in time.

## Slide 131
Appendix. Bolted Joint Problem: Performance
Schwarz tolerance = 1e-6
Dynamic Schwarz converges in between 2-4 Schwarz iterations per time-step despite the overlap region being very small for this problem.
* On SNL ascicgpu15, 16, 17 machines (Intel Skylake CPU processor).

## Slide 132: Appendix. Numerical Example: 1D Dynamic Wave Propagation Problem
Alternating Dirichlet-Neumann Schwarz BCs with no relaxation () on Schwarz boundary
A parameter sweep study revealed gave best performance (min # Schwarz iters)
All couplings were implicit-implicit with and
  Time-step and spatial resolution chosen to be small enough to resolve propagating wave
All reproductive and predictive cases run on the same RHEL8 and RHEL7 machines.
 | Min # Schwarz Iters | Max # Schwarz Iters | Total # Schwarz Iters
1.10 | 3 | 9 | 59,258
1.00 | 1 | 4 | 24,630
0.99 | 1 | 5 | 35,384
0.95 | 3 | 6 | 45,302
0.90 | 3 | 8 | 56,114
 | Min # Schwarz Iters | Max # Schwarz Iters | Total # Schwarz Iters
1.10 | 3 | 9 | 59,258
1.00 | 1 | 4 | 24,630
0.99 | 1 | 5 | 35,384
0.95 | 3 | 6 | 45,302
0.90 | 3 | 8 | 56,114
Model accuracy evaluated w.r.t. analogous FOM-FOM coupling via mean square error (MSE):