## Slide 1
CLDERA: Developing a Novel Foundational Approach for Attributing Localized Source Forcings in the Climate
SAND2023-02095C
Principal Investigators: Diana Bull, Kara Peterson
Thrust Leads: Irina Tezaur, Lyndsay Shand, Laura Swiler
Sandia National Laboratories
22nd IACM Computational Fluids Conference (CFC) 2023
Cannes, France. April 25-28, 2023.

## Slide 2: Outline
Background
  Motivation
  The CLDERA Project
  Driving Exemplar: Mt. Pinatubo & Stratospheric Aerosol Injection (SAI)
CLDERA Research Composition
  Simulations
  Simulated Pathways Thrust
  Observed Pathways Thrust
  Attribution Thrust
Verification & Validation
Summary
CLDERA
observed pathways
simulated pathways
attribution
2

## Slide 3: Outline
Background
  Motivation
  The CLDERA Project
  Driving Exemplar: Mt. Pinatubo & Stratospheric Aerosol Injection (SAI)
CLDERA Research Composition
  Simulations
  Simulated Pathways Thrust
  Observed Pathways Thrust
  Attribution Thrust
Verification & Validation
Summary
CLDERA
observed pathways
simulated pathways
attribution
3

## Slide 4: Motivation Climate Change is a Growing Global Security Concern!
Governments are interested in climate risk assessments toward informing decision making (policies, treaties, security posture, etc.)
requires identifying impacts from climate change sources:
  Anthropogenic climate change (natural or human-caused)
  Climate interventions (a.k.a., geoengineering*)
* Deliberate manipulation of the Earth system to try to counteract effects of climate change.
4
China’s ‘Sky River’ cloud seeding project launched unilaterally
Challenges in tackling climate attribution problem:
  High internal variability in the Earth system
  Complex coupling of processes in Earth System Models (ESMs), which obscures the connective relationships between sources and impacts
  Limited ESM ensembles
  Historically limited observational data
  Multiple sources contributing to an impact
Currently, confident scientific attribution of a source (e.g., Sky River) to a physical impact (e.g., regional drought over Southeast Asia) is at best onerous and at worst impossible!
Notes: Climate change can result from a number of different sources, including non-persistent natural forcing, policy choices and climate interventions.
As part of the Sky River project, China has installed tens of thousands of fuel-burning chambers across the Tibetan mountains, which will produce silver iodide particles, expected to seed moisture clouds capable of producing rain and snow over the Tibetan Plateau.
FFRDC = federally funded research and development centers
As noted in National Academies of Sciences Engineering Medicine (NASEM) [12], detecting a unilateral launch of SAI will likely be trivial because of the change in aerosol optical depth, but questions of impacts that can be attributed to the SAI event is an outstanding and critical research topic to be addressed for governance and equity around climate intervention techniques.
For instance, the inability to attribute secondary and tertiary climate impacts to the development of China’s ‘Sky River’ cloud-seeding arrays—being developed to control rainfall over the Tibetan Plateau [10]—highlights the disincentive to establish multilateral agreements in which spatially distant negative impacts would be criteria in design development and optimization.

## Slide 5: Outline
Background
  Motivation
  The CLDERA Project
  Driving Exemplar: Mt. Pinatubo & Stratospheric Aerosol Injection (SAI)
CLDERA Research Composition
  Simulations
  Simulated Pathways Thrust
  Observed Pathways Thrust
  Attribution Thrust
Verification & Validation
Summary
CLDERA
observed pathways
simulated pathways
attribution
5

## Slide 6: The CLDERA Grand Challenge LDRD Project A Novel Foundational Approach to Understanding the Causation of Impacts
Thrust 2: observed pathways
Thrust 1: simulated pathways
Thrust 3: attribution
Determine how a geographically and temporally localized source drives the climate system to respond with particular impacts to enable downstream impact attribution.
Tracing pathways between source and impacts will increase certainty of attribution and deepen understanding of dependent causal-like relationships.
Need
Hypothesis
Outcome
Build upon key strengths of Sandia (modeling & simulation, detection & attribution, data science)
Develop novel methods and tools in three cross-validating thrusts
Use the 1991 eruption of Mt. Pinatubo as exemplar
CLDERA
Technical Approach
Advance climate attribution science by identifying impacts from localized sources.
Pathways represent the spatio-temporally evolving chain of physical processes that connects a source to impacts.
CLDERA: CLimate impact Determining Etiology thRough pAthways
Duration: FY22-FY24
Budget: $5M-$6M/year
Staffing: 45 Sandians,
4 Academic Partners
Notes: We propose to develop methods that enable the discovery of source-impact pathways in simulated and observational data. Pathways represent the spatio-temporally evolving chain of physical processes that connects a source to its impacts. The uncovered pathways will elucidate connective relationships, enabling a deeper understanding of etiology in the climate, and offer much needed constraints for the mathematical techniques to achieve attribution in this highly complex climate system with nonlinearities, stochasticity and high-dimensionality.
Addressing this challenging problem requires integrating foundational research to improve the intelligibility of ESMs and fuse disparate observational data sources in order to bridge the gap between observations and models and enable reliable attribution.

## Slide 7: Outline
Background
  Motivation
  The CLDERA Project
  Driving Exemplar: Mt. Pinatubo & Stratospheric Aerosol Injection (SAI)
CLDERA Research Composition
  Simulations
  Simulated Pathways Thrust
  Observed Pathways Thrust
  Attribution Thrust
Verification & Validation
Summary
CLDERA
observed pathways
simulated pathways
attribution
7

## Slide 8: Mt. Pinatubo Eruption Stratospheric Aerosol Injection (SAI)
Mt. Pinatubo before eruption
Large Eruption (June 12, 1991)
Main Eruption (June 15, 1991)
June 15, 1991: largest eruption of the satellite era
Released 18-19 Tg SO2 gas (1 Tg = 1 Mt = 1012 g)
“Fast” reactions and ice/ash fallout reduced the “climatically-relevant” SO2 injection to 10 Tg SO2 gas.
SO2 gas released by Mt. Pinatubo converted to SO4 , H2SO4, H2O and aerosols via oxidation, nucleation and chemical reactions
CLDERA R&D is be driven using an exemplar of Stratospheric Aerosol Injection (SAI): the 1991 eruption of Mt. Pinatubo.
Philippines: 15.08° N, 120.21° E
Notes: Mt. Pinatubo injected 5-10 Tg of sulfur [18], primarily as SO2 gas, into the stratosphere where the gas reacted with water to form a hazy layer of aerosol particles composed mostly of sulfuric acid droplets (H2SO4) [19].
The volcanic stratospheric sulfate aerosols increased the aerosol optical depth by a factor of five over the tropical Pacific in mid-August [15], resulting in a decrease in monthly mean clear-sky total solar irradiance over the first 10 months [21]. This aerosol direct effect, notionally shown in Figure 1 as the red dashed line, is responsible for the scattering of incoming shortwave radiation and absorption of longwave outgoing radiation [14, 20-22], which led to negative forcing observed until mid-1993 [18]. This change in radiative flux caused a 0.6° C global cooling of the lower troposphere [16, 23], but also a warming of the stratosphere where the particles resided [14, 16] (the dark orange dash-dot downstream impact shown in Figure 1).
Further downstream impacts from the eruption of Mt. Pinatubo have been documented to include reductions in precipitation [27] and global mean sea level [28]. These downstream impacts are triggered by the overall cooling resulting in decreased evaporation [28], and lower sea surface temperatures / ocean heat content [29] that—due to thermal expansion—decreased the global sea level [30].
Aerosol indirect effects occur when sulfate aerosols enter the troposphere via stratosphere-troposphere exchange and sedimentation. . Here there are multiple processes by which sulfate aerosols can then affect clouds through the microphysics, MG2 [34],and chemistry parameterizations. Aerosol activation (acting as nuclei for condensation) can affect cloud reflectivity and lifetime [35]. Ice homogenous nucleation (the formation of ice from supercooled liquid) affects cirrus clouds and their forcing with high uncertainty [36].

## Slide 9: Mt. Pinatubo Eruption Stratospheric Aerosol Injection (SAI)
McCormick et al., 1995
Effects of sulfate aerosols:
Scatter incoming solar (long-wave) radiation: increases planetary albedo, cools the climate system (less energy in)
Absorb infrared (short-wave) radiation emitted at surface: heats the stratosphere
Net results:
0.4-0.6C global cooling at Earth’s surface that lasted through 1993.
Warming of the stratosphere up to 3C.
Important nodes in pathway: SAI secondary aerosols (sulfate) radiation effects temperature
Schematic of Immediate Effects post SAI
Notes: It took 22 days to circle the globe in the tropics
It took ~1 year to attain global coverage
Mt. Pinatubo injected 5-10 Tg of sulfur [18], primarily as SO2 gas, into the stratosphere where the gas reacted with water to form a hazy layer of aerosol particles composed mostly of sulfuric acid droplets (H2SO4) [19].
The volcanic stratospheric sulfate aerosols increased the aerosol optical depth by a factor of five over the tropical Pacific in mid-August [15], resulting in a decrease in monthly mean clear-sky total solar irradiance over the first 10 months [21]. This aerosol direct effect, notionally shown in Figure 1 as the red dashed line, is responsible for the scattering of incoming shortwave radiation and absorption of longwave outgoing radiation [14, 20-22], which led to negative forcing observed until mid-1993 [18]. This change in radiative flux caused a 0.6° C global cooling of the lower troposphere [16, 23], but also a warming of the stratosphere where the particles resided [14, 16] (the dark orange dash-dot downstream impact shown in Figure 1).
Further downstream impacts from the eruption of Mt. Pinatubo have been documented to include reductions in precipitation [27] and global mean sea level [28]. These downstream impacts are triggered by the overall cooling resulting in decreased evaporation [28], and lower sea surface temperatures / ocean heat content [29] that—due to thermal expansion—decreased the global sea level [30].
Aerosol indirect effects occur when sulfate aerosols enter the troposphere via stratosphere-troposphere exchange and sedimentation. . Here there are multiple processes by which sulfate aerosols can then affect clouds through the microphysics, MG2 [34],and chemistry parameterizations. Aerosol activation (acting as nuclei for condensation) can affect cloud reflectivity and lifetime [35]. Ice homogenous nucleation (the formation of ice from supercooled liquid) affects cirrus clouds and their forcing with high uncertainty [36].

## Slide 10: Mt. Pinatubo Eruption Impact Space & Notional Representation of Pathways
“Known” pathways/impacts:
Tropospheric cooling; stratospheric warming; northern-hemisphere winter warming
Increase in planetary albedo
Effects on soil, agriculture, vegetation
Global reduction in precipitation, evaporation, water vapor
Interactions with atmospheric modes of variability (e.g., NAO)
Interactions with coupled modes of variability (e.g., ENSO, AMOC)
Interactions with Asian monsoon
Stratospheric chemistry (e.g., ozone depletion)
Aerosol indirect effects (e.g., cirrus clouds)
Sea level decrease
SOURCE
Atmospheric Circulation
IMPACTS
Notional Representation of Subset of Physical Processes
General Pathway
Aerosol Direct Effect
Aerosol Indirect Effect
Downstream Impacts
Radiation Diffusivity
Aerosol Sedimentation
Air Temperature
Net Primary Productivity
Cloud Brightness
H2O Nuclei
Combustion Aerosols
Volcanic
Eruption
Other Source Event
Other Source Event
Sulfate Aerosol Production
Sea
Level
Radiative Flux
Dust Storms
Notes: Aerosol indirect effects: Mt. Pinatubo eruption sulfate aerosol production aerosol sedimentation transports aerosols into the troposphere modification of cloud optical properties increased cloud brightness/decreased rainfall.
Besides air temperature changes, another downstream impact of Mt. Pinatubo was decreased global sea level, caused by thermal expansion due to lower sea surface temperatures / ocean heat content.
This is because Mt. Pinatubo caused lower sea surface temperatures / ocean heat content that—due to thermal expansion—decreased the global sea level.
We subselected 3 impacts to call our “science questions”
The volcanic stratospheric sulfate aerosols increased the aerosol optical depth by a factor of five over the tropical Pacific in mid-August [15], resulting in a decrease in monthly mean clear-sky total solar irradiance over the first 10 months [21].
The aerosol direct effect, notionally shown in Figure 1 as the red dashed line, is responsible for the scattering of incoming shortwave radiation and absorption of longwave outgoing radiation [14, 20-22], which led to negative forcing observed until mid-1993 [18]. This change in radiative flux caused a 0.6 C global cooling of the lower troposphere [16, 23], but also a warming of the stratosphere where the particles resided [14, 16] (the dark orange dash-dot downstream impact shown in Figure 1).
Further downstream impacts from the eruption of Mt. Pinatubo have been documented to include reductions in precipitation [27] and global mean sea level [28]. These downstream impacts are triggered by the overall cooling resulting in decreased evaporation [28], and lower sea surface temperatures / ocean heat content [29] that—due to thermal expansion—decreased the global sea level [30].
Aerosol indirect effects occur when sulfate aerosols enter the troposphere via stratosphere-troposphere exchange and sedimentation. . Here there are multiple processes by which sulfate aerosols can then affect clouds through the microphysics, MG2 [34],and chemistry parameterizations. Aerosol activation (acting as nuclei for condensation) can affect cloud reflectivity and lifetime [35]. Ice homogenous nucleation (the formation of ice from supercooled liquid) affects cirrus clouds and their forcing with high uncertainty [36].
Mt. Pinatubo injected 5-10 Tg of sulfur [18], primarily as SO2 gas, into the stratosphere where the gas reacted with water to form a hazy layer of aerosol particles composed mostly of sulfuric acid droplets (H2SO4) [19].
The volcanic stratospheric sulfate aerosols increased the aerosol optical depth by a factor of five over the tropical Pacific in mid-August [15], resulting in a decrease in monthly mean clear-sky total solar irradiance over the first 10 months [21]. This aerosol direct effect, notionally shown in Figure 1 as the red dashed line, is responsible for the scattering of incoming shortwave radiation and absorption of longwave outgoing radiation [14, 20-22], which led to negative forcing observed until mid-1993 [18]. This change in radiative flux caused a 0.6° C global cooling of the lower troposphere [16, 23], but also a warming of the stratosphere where the particles resided [14, 16] (the dark orange dash-dot downstream impact shown in Figure 1).
Further downstream impacts from the eruption of Mt. Pinatubo have been documented to include reductions in precipitation [27] and global mean sea level [28]. These downstream impacts are triggered by the overall cooling resulting in decreased evaporation [28], and lower sea surface temperatures / ocean heat content [29] that—due to thermal expansion—decreased the global sea level [30].
Aerosol indirect effects occur when sulfate aerosols enter the troposphere via stratosphere-troposphere exchange and sedimentation. . Here there are multiple processes by which sulfate aerosols can then affect clouds through the microphysics, MG2 [34],and chemistry parameterizations. Aerosol activation (acting as nuclei for condensation) can affect cloud reflectivity and lifetime [35]. Ice homogenous nucleation (the formation of ice from supercooled liquid) affects cirrus clouds and their forcing with high uncertainty [36].

## Slide 11: Mt. Pinatubo Eruption Stratospheric Aerosol Injection (SAI)
McCormick et al., 1995
Exemplar Strengths:
The source is external to climate feedbacks
    Its impacts are large enough to rise above internal variability of climate system
    It provides ample observational data demonstrating the event’s direct and indirect effects for validation of pathways
It possesses a climate intervention analog (1 Tg SO2/yr may produce 0.1 cooling)
SAI as climate intervention
Notes: Mt. Pinatubo injected 5-10 Tg of sulfur [18], primarily as SO2 gas, into the stratosphere where the gas reacted with water to form a hazy layer of aerosol particles composed mostly of sulfuric acid droplets (H2SO4) [19].
The volcanic stratospheric sulfate aerosols increased the aerosol optical depth by a factor of five over the tropical Pacific in mid-August [15], resulting in a decrease in monthly mean clear-sky total solar irradiance over the first 10 months [21]. This aerosol direct effect, notionally shown in Figure 1 as the red dashed line, is responsible for the scattering of incoming shortwave radiation and absorption of longwave outgoing radiation [14, 20-22], which led to negative forcing observed until mid-1993 [18]. This change in radiative flux caused a 0.6° C global cooling of the lower troposphere [16, 23], but also a warming of the stratosphere where the particles resided [14, 16] (the dark orange dash-dot downstream impact shown in Figure 1).
Further downstream impacts from the eruption of Mt. Pinatubo have been documented to include reductions in precipitation [27] and global mean sea level [28]. These downstream impacts are triggered by the overall cooling resulting in decreased evaporation [28], and lower sea surface temperatures / ocean heat content [29] that—due to thermal expansion—decreased the global sea level [30].
Aerosol indirect effects occur when sulfate aerosols enter the troposphere via stratosphere-troposphere exchange and sedimentation. . Here there are multiple processes by which sulfate aerosols can then affect clouds through the microphysics, MG2 [34],and chemistry parameterizations. Aerosol activation (acting as nuclei for condensation) can affect cloud reflectivity and lifetime [35]. Ice homogenous nucleation (the formation of ice from supercooled liquid) affects cirrus clouds and their forcing with high uncertainty [36].

## Slide 12: Outline
Background
  Motivation
  The CLDERA Project
  Driving Exemplar: Mt. Pinatubo & Stratospheric Aerosol Injection (SAI)
CLDERA Research Composition
  Simulations
  Simulated Pathways Thrust
  Observed Pathways Thrust
  Attribution Thrust
Verification & Validation
Summary
CLDERA
observed pathways
simulated pathways
attribution
12

## Slide 13: Energy Exascale Earth System Model (E3SM)* For Simulating Mt. Pinatubo & SAI
E3SM: U.S. DOE-funded Earth system model
Collaboration among 8 national labs and 12 academic institutions
Designed to run on DOE’s advanced computing platforms and address energy-relevant science questions
CLDERA uses E3SM version 2 (v2), obtained in late 2021 through collaboration agreement with the E3SM project
Capabilities to model Mt. Pinatubo eruption and impacts
Resolves stratosphere: 72 vertical levels with 0.1 hPa (64 km) model top
Includes key process models for clouds, ozone and aerosols [Golaz et al., 2019]
* www.e3sm.org, https://github.com/E3SM-Project/E3SM
Key limitation before CLDERA: no prognostic volcanic aerosols in E3SM (radiative forcing due to aerosols from volcanic eruptions was prescribed)
Simulation Lead: Kara Peterson
Notes: E3SM also includes key process models for clouds, ozone and aerosols [Golaz, et al. 2019].
  Turbulence closure: Cloud Layers Unified By Binormals (CLUBB) [Larson & Golaz 2005].
  Cloud Microphysics: Morrison and Gettleman version 2 (MG2) [Gettleman, et al. 2015].
  Linearized ozone photochemistry: Linoz v2 [Hsu & Prather 2009].
  Aerosols: Modal Aerosol Model (MAM4) [Liu, et al. 2016].

## Slide 14: Simulating Mt. Pinatubo in E3SM
Implemented prognostic volcanic aerosols in E3SMv2 MAM4 aerosol model
  Changed aerosol coarse and accumulation mode properties to match stratospheric size distributions
  Validated against High resolution Infrared Radiation Sounder (HIRS) data and CESM2/WACCM
Evaluated E3SM simulation capabilities
  Assessed Quasi-Biennial Oscillation (QBO): QBO in E3SMv2 has slightly short period
  Evaluated E3SM’s Brewer-Dobson circulation via Age-of-Air tracers and water vapor tape recorder: E3SMv2 underestimates upward transport of water
Water vapor tape recorder: E3SMv1 CMIP6
Mt. Pinatubo
Team: B. Wagman, H. Brown, X. Liu [TAMU], A. Hu [TAMU], C. Jablonowski [U Michigan], J. Hollowed [U Michigan]
Default E3SMv2
CLDERA-E3SM*
* https://github.com/sandialabs/CLDERA-E3SM
Notes: Movie right: stratospheric sulfate burden from Mt. Pinatubo eruption for default E3SMv2 (left) and CLDERA-E3SM simulation with tuned aerosols (right) 1 month before 30 months after Mt. Pinatubo eruption.
Figure right: CLDERA-E3SM prognostic model tuned to better represent stratospheric aerosol lifetime and evolution, and agrees better with observations (red curve in figure above).
Middle plot:
- HIRS observations have ±1.4 Tg uncertainty in H2SO4 background conditions
Our Prognostic Model simulations agree well with HIRS in 1992, tending to overestimate in 1993 (red).
Only modifying size changes (tuning) appears to agree better with HIRS in 1993 (cyan).
  However, still need to compare to observations of AOD and aerosol size
QBO: quasiperiodic oscillation of the equatorial zonal wind between easterlies and westerlies in the tropic stratosphere; mean period of 28-29 months
Brewer-Dobson circulation: global atmospheric circulation pattern in tropical tropospheric air rising into the stratosphere and then moving poleward as it descends.
Changes to aerosol coarse and accumulation mode properties to better match aerosol size distributions of volcanic aerosol in stratosphere.
  Tuned dust and sea salt emissions to account for reduced coarse mode removal in troposphere
  Validated against data from HIRS (High resolution Infrared Radiation Sounder) data and CESM/WACCM
Also evaluating E3SM’s ability to simulate stratospheric circulation and comparing against observed features of the circulation including QBO.
Movie right: stratospheric sulfate burden from Mt. Pinatubo eruption for default E3SMv2 (left) and CLDERA-E3SM simulation with tuned aerosols (right) 1 month before → 30 months after Mt. Pinatubo eruption.
Figure right: CLDERA-E3SM prognostic model tuned to better represent stratospheric aerosol lifetime and evolution, and agrees better with observations (red curve in figure above).
Middle plot:
- HIRS observations have ±1.4 Tg uncertainty in H2SO4 background conditions
Our Prognostic Model simulations agree well with HIRS in 1992, tending to overestimate in 1993 (red).
Only modifying size changes (tuning) appears to agree better with HIRS in 1993 (cyan).
  However, still need to compare to observations of AOD and aerosol size
QBO: quasiperiodic oscillation of the equatorial zonal wind between easterlies and westerlies in the tropic stratosphere; mean period of 28-29 months
Brewer-Dobson circulation: global atmospheric circulation pattern in tropical tropospheric air rising into the stratosphere and then moving poleward as it descends.
Changes to aerosol coarse and accumulation mode properties to better match aerosol size distributions of volcanic aerosol in stratosphere.
  Tuned dust and sea salt emissions to account for reduced coarse mode removal in troposphere
  Validated against data from HIRS (High resolution Infrared Radiation Sounder) data and CESM/WACCM
Also evaluating E3SM’s ability to simulate stratospheric circulation and comparing against observed features of the circulation including QBO.

## Slide 15: Outline
Background
  Motivation
  The CLDERA Project
  Driving Exemplar: Mt. Pinatubo & Stratospheric Aerosol Injection (SAI)
CLDERA Research Composition
  Simulations
  Simulated Pathways Thrust
  Observed Pathways Thrust
  Attribution Thrust
Verification & Validation
Summary
CLDERA
observed pathways
simulated pathways
attribution
15

## Slide 16: Simulated Pathways Thrust Finding Impacts from a Source
Atmospheric Circulation
1. Statistical Approaches: use and extend Random Forest Regression and sensitivity analysis to identify and rank physical pathways while establishing susceptibility to initial conditions and E3SM representations
2. Computational Monitoring: instrument E3SM with tracers and profiling capabilities to enable pathway detection.
3. Signature-based Clustering: find and track non-stationary variable clusters for use as features in pathways identification
IMPACTS
SOURCE
Research Composition:
IDENTIFY Driving Pathways
16
16
Radiation Diffusivity
Aerosol Sedimentation
Sulfate Aerosol Production
Net Primary Productivity
Cloud Brightness
Combustion Aerosols
Volcanic
Eruption
Other Source Event
Air Temperature
Other Source Event
Dust Storms
Radiative Flux
H2O Nuclei
Sea
Level
Thrust Lead: Irina Tezaur

## Slide 17: Simulated Pathways Thrust What is a Simulated Pathway?
17
Heuristic definition: a pathway is the chain of physical processes from a source to impacts and their evolution in space and time.
Mathematical definition: a pathway is a time-dependent directed acyclic graph (DAG) representing the dynamics of a physical system.
Edge from Qi to Qj Qj is impacted by Qi at time
Qi = impacts = “nodes” on pathway graph
  Example: Mt. Pinatubo eruption sulfate aerosol production sedimentation transport of aerosols into the troposphere modification of cloud optical properties increased cloud brightness/decreased rainfall.

## Slide 18: Simulated Pathways Thrust Sub-thrusts
Extract
Info
Development of the proposed framework for identifying & ranking pathways will be pursued using three complementary research sub-thrusts that fuse Sandia’s strengths in data analytics, computational modeling and E3SM/climate science.
  Random forest regression (RFR)
  (b) Sensitivity analysis
  Profiling
  Tracing
Sub-thrust 2: Computational monitoring
Sub-thrust 3: Clustering
Sub-thrust 1: Statistical methods
Component feature generation
Data
Data
Data
E3SM Simulations
Data
Data
Simulated pathways thrust will generate simulation data for CLDERA.
Methods developed in one sub-thrust will feed into the others.
Multiple sub-thrusts minimize risk.
Identifying same pathway with different methods will provide confidence.

## Slide 19: Simulated Pathways Thrust Statistical Methods
x
Random forest regression (RFR): use feature importances from Random Forests (RFs) to identify weighted pathways from one variable to another and determine pathways strengths
19
Team: I. Tezaur, K. Peterson, H. Brown, B. Wagman
Sensitivity analyses (SA): vary eruption elements, e.g., mass, time, height, location
  Generate data for RFR, Signature-based Clustering and Attribution thrust
  Provide insight into how Mt. Pinatubo could have been
  Determine robustness of pathways to changes in SAI-related inputs
  Answer “how low can you go?” question in terms of attribution
F1,1
F1,2
FG,N
Fi,j
 | F1,1 | … | FG,N
F1,1 | 0.1 | … | 0.5
 | … | … | …
FG,N | 0.99 | … | 0.1
 | F1,1 | … | FG,N
F1,1 | 0.1 | … | 0.5
 | … | … | …
FG,N | 0.99 | … | 0.1
Train RF Regressors
Calculate Pairwise Feature Importances
Spatially-partitioned time series data/features
Convert to Pathway Graph
Sensitivity study perturbing various characteristics of Pinatubo-like volcanic eruption [Marshall et al. 2019]
Team: M. Peterson, M. Brown, J. Nichol, W. Davis, I. Tezaur
Notes: RFR is an approach for classification is regression.
Let me now dive into each of the sub-thrusts I mentioned a couple slides back, starting with statistical methods.
There are two classes of methods that will be pursued here.
The first is random forest regression or RFR. RFR is a technique for determining feature importance and finding associations in datasets using groups of decision trees trained using available data.
Often RFR is used as a prediction tool, but this is not what we are doing here. Here, the goal is to use feature importances from random forests to identify weighted pathways from one variable or feature, to another. The basic workflow we envision is shown here.
One starts with some raw climate data with N variables or features on a given grid.
The data gets grouped or clustered into G groups and a random forest is trained for each feature and each group.
Next, feature importances are calculated for each feature and group using the random forests.
Based on these feature importances, one can construct a pathways graph, as shown on the right.
By traversing this graph and looking at the relative values of the feature importances, one can identify not only pathways but also pathways strengths.
RFR has several synergies with other parts of the project. There is a synergy with the observational thrust, as RFR is applicable to both simulation as well as observational data. Additionally, there is a synergy with sub-thrust 3, anomaly detection as anomaly detection can help with the grouping part of the workflow, as well as with generating features for RFR.
Finally, I wanted to mention that we are not new to RFR – we have extensive experience with using RFR feature importance under an LDRD project that ended a year ago led by Kara Peterson. We will be leveraging a lot of our experience gained under this project.
RFR = technique for determining feature importance and finding associations in datasets
can extract which input features Fi,j contribute the most to output prediction
Determine pathway components strengths
Discover pathways: (i) perform a full pairwise analysis of input features generated by anomaly detection, (ii) ID dominant pairwise connections, (iii) connect them to obtain full pathway
Globe is gridded up in M cells - each cell has a set of N features
Combine cells into G groups, combine features within groups (average or sum)
Some Features may be redundant and need to be combined and/or removed - this could impact feature importance calculations
  Splitting the importance across multiple features
Train multiple RFs, one for each feature output
  The input is all the other features
  G x N total RFRs
Each Feature will have an importance from all the other features
We can identify the potential “strongest” pathways from one feature to another by traversing the graph
The vision here is to extend this approach for the purpose of discovering pathways by using it to perform a full pairwise analysis of input features generated by our anomaly detection thrust, identify dominant pairwise connections and connect them to give a full pathway.

## Slide 20: Simulated Pathways Thrust Computational Monitoring
Profiling: finding pathways in-situ while running E3SM
Instrument E3SM and develop DAGs of process interactions executed in situ within code
CLDERA-tools performs statistical analysis by comparing QOIs inside code with baseline and tracking propagation of “anomalies” in real time.
Base DAG
Relevant physics dependencies
CLDERA-tools
In-situ operation
Pathway DAG
Anomalous dependency chain
Subroutine DAG
E3SM function dependencies
Team: A. Steyer, J. Watkins, L. Bertagna, G. Harper, I. Tezaur
Tracers: add tracers to E3SM, use them to evaluate E3SM & explore ways to repurpose them to identify source-impact pathways
Passive tracers: evaluate climatological dynamics (e.g., “Age-of-Air”, Brewer-Dobson circulation) and changes to those dynamics
  Lagrangian coherent structures (LCS): surfaces of trajectories that exponentially attract/repel tracers, anomalies in which may represent elements in pathway
Active (source-tagged) tracers: enable partitioning of impacts due to different aerosol sources, towards tracking of relative contributions along nodes in a pathway
Age-of-Air clock tracer from HSW idealized-climate test
Team: B. Hillman, E. Wenzel, B. Wagman, C. Jablonowski [U Michigan], J. Hollowed [U. Michigan], I. Tezaur
(a) LCS traced out by velocity field in E3SM simulation. (b) Finite Time Lyapunov Exponent (FTLE) for E3SM simulation.
See talk by E. Wenzel for more on analyses using Lagrangian Coherent Structures
Small overhead (<1% for idealized HSW++ E3SM test)!
(a)
(b)

## Slide 21: Simulated Pathways Thrust Signature-based Clustering
Goal: find & track non-stationary variable clusters for use as features in pathway identification
Approach: combine existing anomaly (event) detection algorithms [Davis et al. 2021] with clustering to enable spatio-temporal anomaly progression, defining pathways
  Use signatures (compressed representation of data) for clustering
  User clusters to inform pathway analyses
Team: W. Davis, M. Carlson, I. Tezaur
Space-time varying cluster identification in response to Mt. Pinatubo source
Force-directed graph of cluster transition probabilities over Mt. Pinatubo simulation
Notes: Anomaly detection: finds “interesting” (localized in space or time) events or outliers
Will be used in this project to also create features for others to use to describe the evolution of the climate system, and identify structure/causality within data
Changepoint detection: separates data into segments, find sudden abrupt changes that persist, not necessarily outliers

## Slide 22: Outline
Background
  Motivation
  The CLDERA Project
  Driving Exemplar: Mt. Pinatubo & Stratospheric Aerosol Injection (SAI)
CLDERA Research Composition
  Simulations
  Simulated Pathways Thrust
  Observed Pathways Thrust
  Attribution Thrust
Verification & Validation
Summary
CLDERA
observed pathways
simulated pathways
attribution
22

## Slide 23: Observed Pathways Thrust Finding Impacts from a Source
1. Data Fusion: strategically source and fuse relevant data of varying resolutions and fidelities to create a “near-global” picture of the relevant processes
2. Changepoint Detection: identify the underlying fundamental shifts in climate processes
3. Dynamic space-time models: adapt Bayesian hierarchical approaches to incorporate multiple nodes and establish correlations between nodes
4. Explainable Echo State Networks (ESNs): develop explainable and interpretable methods to quantify relationships between pathway nodes as modeled by recurrent neural networks
Research Composition:
23
Atmospheric Circulation
IMPACTS
SOURCE
Radiation Diffusivity
Aerosol Sedimentation
Aerosol
Optical
Depth
Net Primary Productivity
Cloud Brightness
Combustion Aerosols
Volcanic
Eruption
Other Source Event
Air Temperature
Other Source Event
Dust Storms
Radiative Flux
H2O Nuclei
Sea
Level
IDENTIFY Driving Pathways
Thrust Lead: Lyndsay Shand
Notes: No slides on data fusion – what is being done there?

## Slide 24: Observed Pathways Thrust What is an Observed Pathway?
24
Definition: observed pathways are interpreted as relationships (or correlations) between dependent climate processes (pathway nodes).
SO2
H2SO4
Net Radiative Flux
Temperature Changes
TIROS Operational Vertical Sounder (TOVS)
Weather Balloons with tethered instruments collect high-res but sparse atmospheric data
Total Ozone Mapping Spectrometer (TOMS)
Objective: rather than finding pathways that have not been postulated, validate proposed pathways and quantify changes in the relationship between pathway nodes.
\
Approach: develop statistical methods that can account for the dynamic evolution of aerosols over space and time, multiple complementary sources of data and uncertainty.

## Slide 25: Observed Pathways Thrust Available Satellite Data for Mt. Pinatubo
Instrument | Satellite | Measurements | Satellite Orbit | Data Collected
Total Ozone Mapping Spectrometer (TOMS) | Nimbus-7 | UV albedo (nadir) | Polar, sun-synchronous | SO2 mass and ozone [Bluth et al. 1992; McPeters et al. 1992]
Solar Backscatter Ultraviolet Spectral Radiometer (SBUV) | NOAA-11 | UV albedo (nadir) | Polar, sun-synchronous | SO2 mass and ozone [McPeters et al.1992]
NOAA Advanced Very High Resolution Radiometer (AVHRR) | NOAA-10, -11, -12 | 4 Vis-IR channels (nadir) | Polar, sun-synchronous | Aerosol optical depth [Stowe et al. 1992; Long and Stowe 1994], plume height [Lynch and Stephens 1996], cloud cover [Stowe et al. 1999]
High Resolution Radiation Sounder (HIRS) | NOAA 6-17 | 19 IR channels (nadir) | Polar, sun-synchronous | SO2 mass and cloud-top height [Miles et al. 2017]
Stratospheric Aerosol and Gas Experiment (SAGE II) | Earth Radiation Budget Satellite (ERBS) | 5 channels, Vis—IR (limb scanning) | Polar | Aerosol optical depth/extinction, aerosol max heights, Ozone [McCormick and Veiga 1992]
Microwave Sounding Unit (MSU) | NOAA-10,-11,-12 | 4 MW channels (nadir) | Polar, sun-synchronous | Surface-Upper Stratospheric temperature anomalies [Spencer et al. 1990; Dutton and Christy 1992]
Improved Stratospheric and Mesospheric Sounder (ISAMS) | Upper Atmosphere Research Satellite (UARS) | 8 IR channels (limb scanning) | Near-Polar | Aerosol extinction, mass, and height [Lamberte et al. 1993]
Microwave Limb Sounder (MLS) | UARS | 4 MW channels (limb scanning) | Near-Polar | SO2 mass and temperature profiles [Read et al. 1993]
25
+ Reanalysis data, e.g., ERA-5, MERRA (observations filled in with model run data)

## Slide 26: Observed Pathways Thrust Changepoint Detection
Team: D. Tucker, L. Shand, B. Li [UIUC], S. Jun [UIUC]
Space-time Changepoint Detection: establish dependence between local climate shifts & distance from source using “epidemic” changepoint model
Goal: inform pathways by finding significant changes/shifts in climate processes, towards accounting for them in statistical models
Phase shift (left) and amplitude (right) changepoints identified in ERA-5 Reanalysis Data (1986-1995). Phase shift changepoint and majority of amplitude changepoints are in 1991.
26
Elastic Functional Changepoint Detection: identify climate shift using functional time series methodologies, elastic distance & diffeomorphisms, to account for phase variability
Model can reconstruct spatial pattern and magnitude of changepoints in synthetic dataset with known changepoints
True change
Estimated change
Model allows for and finds multiple changepoint times using test statistic, unlike traditional “at most one change” changepoint model.
New approach [Tucker at al. 2023] can handle multiple changepoint locations.
Notes: [10:00 AM] Tezaur, Irina
I have one more question on the changepoint. Did I get it right that the elastic changepoint approaches can't handle more than 1 spatial location?
[10:01 AM] Tucker, James Derek
No it works over all spatial locations to determine change points at each spatial location
[10:01 AM] Shand, Lyndsay
Drew and Derek's approach can which is one of the many novel contributions of their method
like 1
Goal: inform pathways, by identifying regions in inference solutions to evaluate further
Anomaly detection: Finds “interesting” (localized in space or time) events or outliers
Elastic changepoint: uses elastic distance, concept of diffeomorphisms – gives measure of bending/stretching to align spatial data at time 0 and N
Changepoint should happen later in time as you move farther away from the source
Derek’s results – amplitude shift:
Looked a grid of locations (100x100)
Computed changepoint at each location
Interpolated estimated changepoint across entire globe
Most changepoints around 1991, with a few points at 1989
Space-time changepoint methods can detect when and where climate shifts are observed.
Developed novel framework dependent on distance from event.
Tested on synthetic data

## Slide 27: Observed Pathways Thrust Dynamic Space-Time Models
Team: R. Garrett, G. Huerta, L. Shand
Goal: adopt space-time dynamic models to detect pathway changes following the Mt. Pinatubo eruption.
Approach: develop a multivariate evolution-based space-time dynamic model for variables on a pathway
27
Estimate with Multiresolution Basis Functions [Nychka et al. 2017] to represent the complex spatial patterns
Kalman filtering used to sample from posteriors of time-varying basis functions
Basis function coefficients are space- and time-varying, borrowing information from space-time neighbors
matrix represents correlation between basis coefficients and captures dependence across variables
Linear temporal dynamics model with multivariate inputs/outputs.
Notes: Dynamic space-time models are also known as state-space or Kalman filter models
The DLM (dynamic linear model) is a true multivariate model where Y is a multivariate vector and the relationship between the variables will be captured in the correlation between basis coefficients.
We are now implementing a nonparametric DLM, also leveraging basis functions representation (simpler case of what is implemented in LatticeKrig). We use Kalman filtering to sample from posteriors of time-varying basis coefficients. The top plot is an example of fitted values (U) and the corresponding basis coefficients plotted at the center of the radial basis functions for a single time point.
U is the basis expansion representation of the mean of the process or the fitted process. You can think of Y~GP(U,sigma^2) where U= PHI x alpha_t, alpha_t are the time-varying basis coefficients and PHI are the user defined radial basis functions.

## Slide 28: Observed Pathways Thrust Explainable Echo State Networks (ESNs)
Team: D. Ries, K. Goode, K. McClernon, L. Shand
“Black-Box” Echo-State Networks (ESNs)
Use reservoir computing to efficiently estimate recurrent neural networks (RNNs), which can capture short-term/long-term spatio-temporal dependence
All params learned from data, very fast since few params
Goal: characterize (quantify) relationships between pathway variables in observed data using machine learning
28
Zero Feature Importance (ZFI) new approach!
Determines which variables at which times are important for forecasting.
Based on permutation feature importance (PFI)
Increases explainability of ESNs
Data stage , spatio-temporal residual
Output stage
Hidden stage
RNN
ZFI of lagged AOD and lagged temperature: importance of AOD increases dramatically after Pinatubo eruption while importance of temperature corresponds to seasons.
Effect of variable [xxx] on
Nonlinear temporal dynamics model with multivariate (EOF) inputs, univariate (EOF) outputs.
Notes: Reservoir computing is a framework for computation derived from recurrent neural network theory that maps input signals into higher dimensional computational spaces through the dynamics of a fixed, non-linear system called a reservoir.
The term 'reservoir' refers to a dynamical system.
Yes ZFI is a new term – good question, I think because instead of permuting values, they are just setting them to zero? I will ask.
The ESN, however is assuming a one-direction relationship such that Y is univariate (surface temps) and the other nodes, strat temp and AOD are considered predictors through the EOFs.
RNN = output + hidden stages
- All parameters in ESN are learned from data.
- adding spatio-temporal residual accounts for regional spatial trends not captured by temperature or AOD effects and makes the model more explainable
The choice to add a spatial residual came from the existence of spatial correlation in the model residuals after some initial data fittings.
RNNs are used to estimate the quadratic parameters at the 2nd level of the model used to model the EOF coefficients.
Z_t = temperature
Phi = EOF
Alpha_t = ESN
Xtilde_t = lagged temperature
Delta_t(s) = spatial temporal residual -> makes network explainable; spatial residual is interpretable (accounts for regional spatial trends not captured by temperature or AOD effects).
Echo-State Network (ESN) – developed work flow and
ESNs are efficient networks that have been shown to be capable of representing dependent processes on different time scales.
Developed workflow for ESNs applied to univariate data
Tested sensitivities on synthetic data
Adding interpretability through spatially dependent parameters
The concept of reservoir computing stems from the use of recursive connections within neural networks to create a complex dynamical system
Permutation Feature Importance (PFI)
PFI is intended to make black-box ESNs explainable but has never been applied to deep networks.
Developed workflow for PFI applied to ESNs

## Slide 29: Outline
Background
  Motivation
  The CLDERA Project
  Driving Exemplar: Mt. Pinatubo & Stratospheric Aerosol Injection (SAI)
CLDERA Research Composition
  Simulations
  Simulated Pathways Thrust
  Observed Pathways Thrust
  Attribution Thrust
Verification & Validation
Summary
CLDERA
observed pathways
simulated pathways
attribution
29

## Slide 30: Attribution Finding Predominant Source Driving Impact
1. Enhanced Fingerprinting: use pathway information to expand multi-variate analyses, sharpening the signal-to-noise ratios and enabling significant correlations between source-impact
2. Causal Modeling: identify causal relationships and dominant pathways by developing causal networks through iterative independence tests and the resulting directed acyclic graphs
3. Inverse Optimization: develop deep operator neural networks (DONNs) to model parts of E3SM to enable PDE-constrained optimization without intrusion into the E3SM code directly; pathways will act as penalty terms or constraints
Research Composition
What precipitates the impact?
30
Atmospheric Circulation
IMPACTS
SOURCE
Net Primary Productivity
Cloud Brightness
Combustion Aerosols
Volcanic
Eruption
Other Source Event
Other Source Event
Dust Storms
Sea
Level
Radiation Diffusivity
Aerosol Sedimentation
H2O Nuclei
Air Temperature
Radiative Flux
Sulfate Aerosol Production
Thrust Lead: Laura Swiler

## Slide 31: Attribution Enhanced Fingerprinting
Team: B. Wagman, L. Swiler, K. Tsigaridis [Columbia]
“Fingerprint” = a spatial and/or temporal pattern that highlights an impact
  Commonly the first principal component or empirical orthogonal function (EOF) from an SVD of a data matrix
Detection involves identifying if the signal projected back onto the EOF goes out of 2𝜎 limits.
Attribution involves examining the magnitude of the fingerprint in a regression formulation and checking its significance (signal-to-noise ratio).
Enhanced Fingerprinting Approach:
  Investigate advanced PCA (tensor-based, non-negative, Joint & Individual Fingerprints or JIF, etc.)
  Employ multiple variables along a pathway to sharpen signal-to-noise ratios & enable downstream attribution
  Use pathway info to refine fingerprints for use within a short-term SAI event with a more regional impact
Fingerprints from varying volcanic forcings: non-negative PCA strengthens Pinatubo effect on temperature [Weyland et al 2023 (in prep)].
Notes: JIF: based on Joint & Individual Variance Explained (JIVE). X_i = J + I_i. J part of fingerprint is always the same, I_i will change.
The non-negative PCA is only one of the approaches. The main point of the slide is that it heightens or strengthens the Pinatubo effect on temperature and (for example) makes it clearer to see that there is little effect for the “zero X” Pinatubo case in the greyish line. This example is discussed more in Figure 3 of the attached paper.
The approaches Michael has examined are all linear but do require some optimization to get the bases: it is not just one decomposition. Another thing which he has done is some careful analysis of the scaling and variance so that when you project the data back onto the right singular vectors, the values (for us, typically in time) are in units which are meaningful such as degrees K, not in some unit-less “score space.” I did not put that in the slides but is something we should consider using and being consistent across CLDERA. Finally, Michael is looking at the JIF method he mentioned on Monday where he is decomposing the EOFs into a “joint” effect basis and individual “ensemble” effects. If this approach works, it will be novel in the fingerprinting community, I think, but this is too early to say anything about it at the CFC conference.
Detection = the process of demonstrating that climate has changed in some defined statistical sense w/o providing a reason for that change.
Attribution = the process of evaluating the relative contributions of multiple causal factors to a change or impact with an assignment of statistical confidence
-> calculate the slope of the fingerprint beta from initial time (1900) to various times
-> calculate uncertainty in the slope and the signal/noise ratio beta/sigma
-> smaller uncertainty => larger signal to noise ratio given same slope
Beta = slope of fingerprint
Sigma(beta) = std. dev. of trend (noise), calculated from long piControl run (1000 years).
S/N ratio = beta / sigma -> assume to be normally distributed; assess probability
For a multivariate fingerprint, the plan is to normalize multiple variables and simply concatenate the data into one larger matrix over which we would perform the SVD. An example of this is shown with reference height temperature and net short wave flux on slide 8 of the attached.
Fingerprinting: Establish we can reproduce SoA analysis. Establish workflow.
Developed workflow and applied to both the detection of a change in temperature (lat, lon average over a month & detrended per pressure level) (EOF represents data at every pressure level, the projection of the data onto the EOF gives the amplitudes as a time series. BLUE line represents the data projected onto the first EOF (first principal component) from the singular value decomposition of the data

## Slide 32: Attribution Causal Modeling
Tropical SO2 causes Tropical H2SO4 (over a 1 and 3 month lag)
Tropical SO2 causes a change in aerosol optical depth (AEROD)
Tropical AEROD shows a negative contemporaneous dependence with global surface radiation flux.
Team: J. Nichol, M. Smith, L. Swiler, C. Wentland, M. Weylandt
Goal: establish relationships between a set of variables to discover or confirm a causal relationship
Causal Network Learning Approach:
    Fit a graphical model of covariates by iterative conditional independence tests.
    PCMCI algorithm: Peter Clark Momentary Conditional Independence [Runge, 2019]
    Allows for and detects contemporaneous dependencies, removes spurious associations
Preliminary Causal Network Results on Mt. Pinatubo Simulation Data with Prognostic Aerosols
Nonlinear attractor
variables/features
Notes: Contemporaneous dependencies = temporal dependencies (pure contemporaneous dependencies means model represents relationships within fixed time frame).
Causal modeling takes in large-scale time series data and discovers a causal network, represented by a graph like the one on the right. This network can account for both linear and nonlinear dependencies in the data, as well as time lags. The nodes in the graph are important variables or features identified in creating the causal network., and you can see that the network graph is directed, so you can infer causality.
Structural causal modeling: involves positing a causal relationship or causal model and confirming / refuting it.
What we are doing is more data-driven causal discorvery

## Slide 33: Attribution Inverse Optimization
(test case for initial prototyping)
Team: J. Hart, M. Gulian, I. Manickam, L. Swiler
Goal: identify magnitude, height and location of the source is a large-scale, PDE constrained inverse problem
s.t.
Approach:
Develop deep operator neural networks (DONNs) to enable PDE-constrained optimization
Bayesian approach to deal with ill-posedness & incorporate UQ
Add pathway information as penalty terms in the objective and/or additional constraints
Approximated by DONNs
Gaussian Plume+: Advection-Diffusion-Reaction with Gaussian Plume Source
Find source parameters that minimize the difference between simulated and observed aerosol concentration s.t. atmosphere PDEs as constraints:
See next talk by M. Gulian for more details on inverse optimization using DONNs.
[Hart et al. 2023]
Notes: Goal: estimate SO2 source given downrange concentration measurements
Use PCA to create a reduced operator
Use TensorFlow to approximate this operator via a NN trained on time-step pairs
Use ROL to perform optimization with NN-based constraints.
Inverse Optimization – develop the software interfaces, establish verification, and test viability of deep-operator neural networks.
Working to train a surrogate operator on gaussian plume + data
Neural network construction for the operator proved more challenging than anticipated due to strong advection properties of the example
Using ideas from ResNet (Residual neural network), plus weighting of information from early times, to improve the training process. We now have pipeline established to do hyperparameter studies to help find an “optimal” neural network to model the evolution operator.
Establishing that ROL is working
Irina’s notes:
Inverse problem to estimate SO2 source given downrange concentration msrts.
Test operator regression surrogates within inverse problem
Connect Tensorflow models with ROL
Use optimization tools to facilitate sampling of Bayesian posterior

## Slide 34: Outline
Background
  Motivation
  The CLDERA Project
  Driving Exemplar: Mt. Pinatubo & Stratospheric Aerosol Injection (SAI)
CLDERA Research Composition
  Simulations
  Simulated Pathways Thrust
  Observed Pathways Thrust
  Attribution Thrust
Verification & Validation
Summary
CLDERA
observed pathways
simulated pathways
attribution
34

## Slide 35: Tiered Verification Approach
Coupled ODEs devoid of governing physics that enable exploration of tool/method sensitivities
Gaussian Plume+
Basic physics (advection-diffusion-reaction), reduced dimensionality, reduced coupling
Full complexity of Earth’s climate verify method solution against known pathways
Synthetic
Idealized
Pinatubo Pathways (WIP)
HSW++
Realistic Earth circulation, idealized forcings/ topography/chemistry, controllable relationships
Method form informed by Real Data
Refine Method Formulation
Apply to Synthetic Cases
Apply to idealized cases
Refine Method Formulation
Apply to Mt. Pinatubo
Sensitivity Analyses
Refine Method Formulation
Establish Viability of Method
FY23
Test Sensitivity of Method
FY22
Prove Usefulness of Method
FY23/FY24
HSW = Held-Suarez-Williamson [Williamson et al., 1998]



## Slide 36: Outline
Background
  Motivation
  The CLDERA Project
  Driving Exemplar: Mt. Pinatubo & Stratospheric Aerosol Injection (SAI)
CLDERA Research Composition
  Simulations
  Simulated Pathways Thrust
  Observed Pathways Thrust
  Attribution Thrust
Verification & Validation
Summary
CLDERA
observed pathways
simulated pathways
attribution
36

## Slide 37: Summary of CLDERA
Simulated Pathways
Observed Pathways
Attribution
SOURCE FORCINGS IN THE CLIMATE
IMPACTS ARISING FROM SOURCES

## Slide 38: Outline
Motivation
The CLDERA Grand Challenge LDRD Project
Mt. Pinatubo & Stratospheric Aerosol Injection (SAI)
Energy Exascale Earth System Model (E3SM) & Simulating Mt. Pinatubo in E3SM
The Three CLDERA Thrusts
  Simulated Pathways Thrust
  Observed Pathways Thrust
  Attribution Thrust
Verification & Validation
Summary
CLDERA
observed pathways
simulated pathways
attribution
38

## Slide 39: CLDERA Team
L. Bertagna
H. Brown
M. Carlson
W. Davis
G. Harper
B. Houchens
J. Lien
D. Krofchek
J. Nichol
M. Peterson
A. Steyer
J. Watkins
E. Wenzel
C. Jablonowski (U Michigan)
J. Hollowed (U Michigan)
X. Liu (TAMU)
A. Hu (TAMU)
M. Gulian
M. Brown
J. Hart
I. Manickam
K. Maupin
M. Smith
B. Wagman
C. Wentland
M. Weylandt
K. Tsigaridis (Columbia U)
K. Goode
R. Garrett
J. Hickey
B. Hillman
G. Huerta
J. Li
K. McClernon
D. Ries
D. Tucker
A. McCombs
B. Li (UIUC)
S. Jun (UIUC)
CLDERA PI: D. Bull
CLDERA Deputy PI: K. Peterson
Simulated Pathways Lead: I. Tezaur
Observed Pathways Lead: L. Shand
Attribution Lead: L. Swiler
Thank you for your attention!
CLDERA Leadership Team

## Slide 40: References
Caldwell, P., et al., Statistical significance of climate sensitivity predictors obtained by data mining. Geophysical Research Letters, 2014. 41.
Finley, Andrew, Banerjee, Sudipto,Gelfand, Alan. (2012). Bayesian Dynamic Modeling for Large Space–Time Datasets Using Gaussian Predictive Processes. Journal of Geographical Systems. 14. 29-47.
Golaz, J.-C., et al., The DOE E3SM Coupled Model Version 1: Overview and Evaluation at Standard Resolution. Journal of Advances in Modeling Earth Systems, 2019. 11(7): p. 2089-2129.
Goode, K., Ries, D., and Zollweg, J. “Explaining Neural Networks with Functional Data Using PCA and Feature Importance”. AAAI 2020 Fall Symposium on AI in the Government and Public Sector. November 13-14, 2020. https://arxiv.org/abs/2010.12063.
Hall, A. et al., Progressing emergent constraints on future climate change. Nature Climate Change, 2019. 9, p 269-278.
Hasselmann, K., Multi-pattern fingerprint method for detection and attribution of climate change. Climate Dynamics, 1997. 13(9): p. 601-611.
Hegerl, G.C. and G.R. North, Comparison of Statistically Optimal Approaches to Detecting Anthropogenic Climate Change. Journal of Climate, 1997. 10(5): p. 1125-1133.
Kravitz, B., et al., First Simulations of Designing Stratospheric Sulfate Aerosol Geoengineering to Meet Multiple Simultaneous Climate Objectives. Journal of Geophysical Research: Atmospheres, 2017. 122(23): p. 12,616-12,634.
Marvel, K., M. Biasutti, and C. Bonfils, Fingerprints of external forcings on Sahel rainfall: aerosols, greenhouse gases, and model-observation discrepancies. Environmental Research Letters, 2020: p. Medium: ED; Size: Article No. 084023.
McDermott, Patrick & Wikle, Christopher. (2018). Deep echo state networks with uncertainty quantification for spatio‐temporal forecasting. Environmetrics. 30. 10.1002/env.2553.
National Academies of Sciences Engineering Medicine (NASEM), Reflecting Sunlight: Recommendations for Solar Geoengineering Research and Research Governance. 2021, Washington, DC: The National Academies Press. 328.
Nowack, P., et al., Causal networks for climate model evaluation and constrained projections. Nature Communications, 2020. 11(1): p. 1415.
Runge, J., et al., Inferring causation from time series in Earth system sciences. Nature Communications 2019. 10(1).
Tezaur, I., et al., Global sensitivity analysis of ultra-low resolution E3SM. Submitted to JAMES, 2022.
Wagman, B. M., L. P. Swiler, K. Chowdhary, B. Hillman. “The Fingerprints of Stratospheric Aerosol Injection in E3SM.” LDRD project 224535 final report, Sept. 2021.
Williamson, MS et al., Emergent constraints on climate sensitivities. Reviews of Modern Physics, 2021. 93 (2) 2021.
40

## Slide 41: References (cont’d)
J. Hart, M. Gulian, I. Manickam, L. Swiler. Solving High-Dimensional Inverse Problems with Auxiliary Uncertainty via Operator Learning with Limited Data, ArXiv pre-print: https://arxiv.org/abs/2303.11379.
D. Tucker, D. Yarger. Elastic Functional Changepoint Detection. ArXiv pre-print: https://arxiv.org/abs/2211.12687.
M. Weylandt, L. Swiler. Beyond PCA: Additional Dimension Reduction Techniques to Consider for Climate Data. J. Climate, 2023 (in prep).
41

## Slide 42: Start of Backup Slides
42

## Slide 43: Current State-of-the-Art In Establishing Connective Relationships in Earth’s Climate
High internal variability in the Earth system
Limited ESM ensembles
Historically limited observational data
Multiple sources contributing to an impact
Confounding characteristics of the climate attribution* problem:
Techniques currently applied to climate attribution:
“Connective relationships are often unbounded from etiological relationships allowing physically meaningless source-impact correlations.” [Caldwell et al., 2014]
Fingerprinting (e.g., Hasselmann, 1997; Hegerl & North, 1997; Marvel et al., 2020)
Structural Causal Modeling (e.g., Runge et al., 2019; Nowack et al., 2020)
Emergent Constraints (e.g., Hall et al., 2019; Williamson et al., 2021)
Under CLDERA, we are moving beyond a correlative approach establishing connective relationships.
“Pecking Order”, Edgar Hunt
* Process of evaluating relative contributions of multiple causal factors to a change/impact with an assignment of statistical confidence
Notes: Due to the innate complexity of the climate, enough data must be available to overcome large sources of variability and uncover complex, often nonlinear, correlations; this is an underlying hurdle to the successful discovery of source-impact relationships
Current evaluation techniques often posit these source-impact pairs and then employ standard statistical methods on simulation and observational data to infer connective, often linear, relationships between the posited source-impact pair.
We intend to build on the current research to develop multivariate approaches that encode pathways information.

## Slide 44
What are the downstream impacts from large, spatio-temporally localized sources within the climate?
How do changes in the global climate system affect the relative frequency and severity of extreme events?
Sector-specific emissions
Long-term, slowly accumulating GHG emissions
What is the question?
What is the
source?
Examples
Volcanic eruptions, wildfires
Likelihood of Hurricane Katrina
Cement industry, transportation
How do rising concentrations of GHGs in the atmosphere affect climate state variables?
What are the relative contributions of different sectors, activities, and entities to concentrations of GHGs in the atmosphere?
Changes to global climate system
Geographically and temporally localized source forcings in the climate
WG1 and WG2 IPCC reports
CLDERA
Attribution in Climate
The goal of CLDERA is to develop new tools to enable downstream impact attribution from geographically and temporally localized source forcings in the climate.
Is the attribution direct/ quantitative?
WG1- yes (temp/precip/…)
WG2 – normally no, notional linkage
yes
no, notional connection
yes, linked through multiple process-nodes
44

## Slide 45: The CLDERA Grand Challenge LDRD Project A Novel Foundational Approach to Understanding the Causation of Impacts
Motivating Research Questions:
Can pathways be discovered within simulation and observation datasets that reveal the connective relationships between source and impacts?
Can pathways inform contributory ranking of sources to an impact?
Can pathways cull the included space while preserving complex climate features to more confidently enable attribution?
CLDERA
Thrust 2: observed pathways
Thrust 1: simulated pathways
Thrust 3: attribution
Hypothesis: tracing pathways between sources and impacts will increase certainty of attribution.
Notes: Can pathways provide a constraint for the inverse problem
A big part of a successful inverse problem is taking a high dimensional problem and reducing it in a smart way so that we can traverse the manifold containing good solutions.

## Slide 46: Connection to Sandia Capabilities & Other Applications
“Always/ Never” Ethos
Materials Science
Engineering Science
Earth Science
Nanodevices & Microsystems
Radiation, Electrical, & High Energy Density Science
Computing & Information Science
Foundational Research that Enables Climate Work
CLDERA-Critical Capabilities
Uncertainty Quantification
Computational Science
Multi-Physics Modeling
Regulatory
Frameworks
Analysis of Extremes
Bioscience
Inverse Optimization
Multi-component Sensor Systems
Information Sciences
Modeling & Simulation
Detection & Attribution
Dual-Nature National Security Issues
Risk Analysis & High-Reliability Engineering
Bio-Security
Cyber-Security
46
Notes: Under CLDERA, we will be leveraging tools and methods developed previously under a variety of different investment areas (e.g., E3SM, optimization libraries such as ROL, regulatory frameworks such as the Waste Isolation Pilot Plant or WIPP). We will also be creating new tools and capabilities that can be relevant for other applications beyond climate science. These include tools for multi-physics modeling, tools for dimension reduction / ML, tools for uncertainty quantification and inversion, tools for fusing observational data,
Can you help establish concrete examples of our heritage in:
Computational science: (e3sm comp lead)
Uncertainty quantification
Multi-physics modeling
Multi-component sensor systems – USNDS / IMS treaty verification --weapons
All source fusing of observations -- information sciences /
Systems approach & engineering
Regulatory frameworks – WIPP
Analysis of extremes --
Always / never ethos.

## Slide 47: Exemplar: June 1991 Mt. Pinatubo Eruption Stratospheric Aerosol Injection (SAI) Exemplar
Largest eruption of the satellite era, releasing 18-19 Tg SO2 gas
  Impacts large enough to rise above internal variability of climate system
  Led to 0.4-0.6°C global cooling 1993.
The source is an analog for a climate intervention technique
  1 Tg SO2 per yr may produce on the order of 0.1°C cooling [Kravitz et al., 2017]
The source forcing is external to the feedbacks within the Earth’s climate
It provides ample observational data and, because the impacts and pathways are relatively well characterized it offers validation of our analysis techniques within the approach
Why this exemplar?
SOURCE
Atmospheric Circulation
IMPACTS
Notional Representation of Subset of Processes
General Pathway
Aerosol Direct Effect
Aerosol Indirect Effect
Downstream Impacts
Radiation Diffusivity
Aerosol Sedimentation
Air Temperature
Net Primary Productivity
Cloud Brightness
H2O Nuclei
Combustion Aerosols
Volcanic
Eruption
Other Source Event
Other Source Event
Sulfate Aerosol Production
Sea
Level
Radiative Flux
Dust Storms
Notes: It took 22 days to circle the globe in the tropics
Impacts:
Tropospheric cooling; stratospheric warming; northern-hemisphere winter warming
Increase in planetary albedo
Effects on soil, agriculture, vegetation
Global reduction in precipitation, evaporation, water vapor
Interactions with atmospheric modes of variability (e.g., NAO)
Interactions with coupled modes of variability (e.g., ENSO, AMOC)
Interactions with Asian monsoon
Stratospheric chemistry (e.g., ozone depletion)
Aerosol indirect effects (e.g., cirrus clouds)
Sea level decrease
Mt. Pinatubo injected 5-10 Tg of sulfur [18], primarily as SO2 gas, into the stratosphere where the gas reacted with water to form a hazy layer of aerosol particles composed mostly of sulfuric acid droplets (H2SO4) [19].
The volcanic stratospheric sulfate aerosols increased the aerosol optical depth by a factor of five over the tropical Pacific in mid-August [15], resulting in a decrease in monthly mean clear-sky total solar irradiance over the first 10 months [21]. This aerosol direct effect, notionally shown in Figure 1 as the red dashed line, is responsible for the scattering of incoming shortwave radiation and absorption of longwave outgoing radiation [14, 20-22], which led to negative forcing observed until mid-1993 [18]. This change in radiative flux caused a 0.6° C global cooling of the lower troposphere [16, 23], but also a warming of the stratosphere where the particles resided [14, 16] (the dark orange dash-dot downstream impact shown in Figure 1).
Further downstream impacts from the eruption of Mt. Pinatubo have been documented to include reductions in precipitation [27] and global mean sea level [28]. These downstream impacts are triggered by the overall cooling resulting in decreased evaporation [28], and lower sea surface temperatures / ocean heat content [29] that—due to thermal expansion—decreased the global sea level [30].
Aerosol indirect effects occur when sulfate aerosols enter the troposphere via stratosphere-troposphere exchange and sedimentation. . Here there are multiple processes by which sulfate aerosols can then affect clouds through the microphysics, MG2 [34],and chemistry parameterizations. Aerosol activation (acting as nuclei for condensation) can affect cloud reflectivity and lifetime [35]. Ice homogenous nucleation (the formation of ice from supercooled liquid) affects cirrus clouds and their forcing with high uncertainty [36].

## Slide 48: Simulation Plan
Simulations will be performed for 5 simulated years.
Runs are being performed on NERSC (Cori, Perlmutter) and Sandia HPC (Skybridge, Boca)
1 resolution E3SM can achieve:
  18 SYPD per 58 AMD CPU nodes on Perlmutter at NERSC
May supplement 1 resolution with cheaper 7.5 resolution runs
Planned simulations expected to require O(107) CPU-hours!
Notes: Mention challenges of knowing in advance what to output and how often.
Boca = condo cluster

## Slide 49: Simulated Pathways Thrust Statistical Methods
Random forest regression (RFR):
Goal: use feature importances from Random Forests (RFs) to identify weighted pathways from one variable to another
F1,1
F1,2
FG,N
Fi,j
 | F1,1 | … | FG,N
F1,1 | 0.1 | … | 0.5
 | … | … | …
FG,N | 0.99 | … | 0.1
 | F1,1 | … | FG,N
F1,1 | 0.1 | … | 0.5
 | … | … | …
FG,N | 0.99 | … | 0.1
Create Pathway Graph
Train RF Regressors
Calculate Feature Importances
Inputs: time-series of various features or variables of interest (simulated or observed data)
Output: a list of “single-hop” paths that form a network/graph
  Graph can be queried to see what kinds of paths exist between features and their relative strengths
49
Raw data
Pruned feature importance graph using latitudinal bands
Thick edge = important feature
Team: M. Peterson, M. Brown, J. Nichol, W. Davis, I. Tezaur
Notes: Let me now dive into each of the sub-thrusts I mentioned a couple slides back, starting with statistical methods.
There are two classes of methods that will be pursued here.
The first is random forest regression or RFR. RFR is a technique for determining feature importance and finding associations in datasets using groups of decision trees trained using available data.
Often RFR is used as a prediction tool, but this is not what we are doing here. Here, the goal is to use feature importances from random forests to identify weighted pathways from one variable or feature, to another. The basic workflow we envision is shown here.
One starts with some raw climate data with N variables or features on a given grid.
The data gets grouped or clustered into G groups and a random forest is trained for each feature and each group.
Next, feature importances are calculated for each feature and group using the random forests.
Based on these feature importances, one can construct a pathways graph, as shown on the right.
By traversing this graph and looking at the relative values of the feature importances, one can identify not only pathways but also pathways strengths.
RFR has several synergies with other parts of the project. There is a synergy with the observational thrust, as RFR is applicable to both simulation as well as observational data. Additionally, there is a synergy with sub-thrust 3, anomaly detection as anomaly detection can help with the grouping part of the workflow, as well as with generating features for RFR.
Finally, I wanted to mention that we are not new to RFR – we have extensive experience with using RFR feature importance under an LDRD project that ended a year ago led by Kara Peterson. We will be leveraging a lot of our experience gained under this project.
RFR = technique for determining feature importance and finding associations in datasets
can extract which input features Fi,j contribute the most to output prediction
Determine pathway components strengths
Discover pathways: (i) perform a full pairwise analysis of input features generated by anomaly detection, (ii) ID dominant pairwise connections, (iii) connect them to obtain full pathway
Globe is gridded up in M cells - each cell has a set of N features
Combine cells into G groups, combine features within groups (average or sum)
Some Features may be redundant and need to be combined and/or removed - this could impact feature importance calculations
  Splitting the importance across multiple features
Train multiple RFs, one for each feature output
  The input is all the other features
  G x N total RFRs
Each Feature will have an importance from all the other features
We can identify the potential “strongest” pathways from one feature to another by traversing the graph
The vision here is to extend this approach for the purpose of discovering pathways by using it to perform a full pairwise analysis of input features generated by our anomaly detection thrust, identify dominant pairwise connections and connect them to give a full pathway.

## Slide 50: Simulated Pathways Thrust Statistical Methods
(b) Sensitivity analyses (SA)
Generate data for RFR, anomaly detection and Attribution thrust
Determine robustness of pathways to changes in SAI-/model-related inputs
Two kinds of sensitivity studies using different resolutions of E3SM:
  Vary eruption elements, e.g., mass, time, height, location (how Mt. Pinatubo could have been “how low can you go?”)
  Vary MAM4 aerosol and MG2 cloud microphysics model parameters
Right: global sensitivity analysis (GSA) results for surface temperature QOI using ULR E3SMv1 [Tezaur et al., 2022]
Above: ultra-low (ULR), medium-low (MLR) and standard 1 resolution E3SM grids
Team: I. Tezaur, K. Peterson, B. Wagman, H. Brown
Notes: ULR does 20-30 SYPD on 4 nodes of skybridge
ULR is about 100x faster than standard 1-degree resolution
ULR: 7.5-degree atmosphere
MLR: 1.9-degree atmosphere in v2 (ne16)
  2.7-degree atmosphere in v1 (ne11)

## Slide 51: Simulated Pathways Thrust Computational Monitoring
Profiling: finding pathways in-situ while running E3SM
Goal: instrument E3SM and develop Directed Acyclic Graphs (DAGs) of process interactions executed within code
Control runs (e.g., no Mt. Pinatubo eruption run) generate baseline.
CLDERA-tools performs statistical analysis by comparing QOIs inside code with baseline and tracking propagation of “anomalies” in real time.
Base DAG
Relevant physics dependencies
CLDERA-tools
In-situ operation
Pathway DAG
Anomalous dependency chain
Subroutine DAG
E3SM function dependencies
Inputs: baseline, “base DAG” (tells E3SM what to track)
Outputs: Time-evolving pathway DAG
Team: A. Steyer, J. Watkins, L. Bertagna, G. Harper, I. Tezaur
Month 6
Month 7
Months 8-9
Notes: Go/no-go: not trying to quantify it – yes/no answer

## Slide 52: Simulated Pathways Thrust Computational Monitoring
    Evaluate climatological dynamics (like “Age of Air”) and changes to those dynamics.
    Infer pathways/pathway changes by detecting tracer flow patterns/evolution using Lagrangian Coherent Structures (LCS): surface trajectories which exponentially attract or repel tracers.
  Passive tracers: do not feedback to the atmosphere, but can track source evolution
(b) Tracing: add tracers to E3SM, use them to evaluate E3SM and explore ways to repurpose them to identify source-impact pathways
Tracers
  Active (“tagged”) tracers: feedback into atmosphere through physics processes
    Enable tracking of relative contributions along nodes in pathway.
[Garaboa-Paz et al., 2015]
Team: B. Hillman, A. Steyer, E. Wenzel, B. Wagman, C. Jablonowski [U Michigan], J. Hollowed [U. Michigan], I. Tezaur
Notes: LCS:
Videos show advective transport of massless Lagrangian particles.
As time advances, passive scalar quantity evolves from an initially simple distribution to a complicated structure characterized by large gradients.
The characteristic feature of this flow field is a dominant LCS. The LCS can be identified by computing the number density of Lagrangian particles.
The particles move with the local Eulerian velocity, and they transport a passive scalar quantity (pure advection, no diffusion). The velocity field is an array of translating vorticies.
Color = dimensionless particle number density (red = high, blue = low).
Simulation run in Everett’s research code, which is incompressible NS (Eulerian grid) + smooth particle hydrodynamics solver (which provides particles)
To do this with an existing code, one would simply need to add particles that move with the local velocity. The number density can then be computed using a variety of procedures.
Enable separation of SO2 from Mt. Pinatubo vs. regular emissions in a single simulation, toward tracing radiative impact and secondary (downstream) products of eruption
Hunter: debate on how to use active tracers
- Unclear if we will do this – would it give more info than w/ and w/o simulations
Changes in Lagrangian Coherent Structures inform changes in large circulation patters, e.g,. Flow across the equator, changes in polar vortex and impact on NH winter warming
LCS = structures which exponentially attract or repel tracers

## Slide 53: Simulated Pathways Thrust Anomaly Detection*
Tracers
Goal: produce clusterings over climate simulations that can serve as foundations of pathway discovery
Approach: combine existing anomaly (event) detection algorithms [Davis et al., 2021] with clustering to enable spatio-temporal anomaly progression, defining pathways
Leverages “In-Situ Machine Learning for Intelligent Data Capture on Exascale Platforms” (ISML) project (PI: W. Davis)
Compressed ISML signatures used for clustering
Clusters used to inform pathway analysis
*Finds “interesting” (localized in space or time) events or outliers
Team: W. Davis, M. Carlson, I. Tezaur
Notes: Anomaly detection: finds “interesting” (localized in space or time) events or outliers
Will be used in this project to also create features for others to use to describe the evolution of the climate system, and identify structure/causality within data
Changepoint detection: separates data into segments, find sudden abrupt changes that persist, not necessarily outliers

## Slide 54: Observed Pathways Thrust What is an Observed Pathway?
54
Definition: observed pathways are interpreted as relationships (or correlations) between dependent climate processes (pathway nodes).
Objective: rather than finding pathways that have not been postulated, validate proposed pathways and quantify changes in the relationship between pathway nodes.
Approach: develop statistical methods that can account for the dynamic evolution of aerosols over space and time, multiple complementary sources of data and uncertainty.
SO2
H2SO4
Net Radiative Flux
Temperature Changes
Driving Science Questions:
What are the spatio-temporal signatures of the temp. change due to Mt. Pinatubo?
For how long after can we link sulfates created by Mt Pinatubo to climate effects? When does signal become too noisy or convoluted?
When and where do we first see changes due to the event? How precise can we get with uncertainties?

## Slide 55: Observed Pathways Thrust Available Satellite Data for Mt. Pinatubo
Instrument | Satellite | Measurements | Satellite Orbit | Data Collected
Total Ozone Mapping Spectrometer (TOMS) | Nimbus-7 | UV albedo (nadir) | Polar, sun-synchronous | SO2 mass and ozone (Bluth et al., 1992; McPeters et al., 1992)
Solar Backscatter Ultraviolet Spectral Radiometer (SBUV) | NOAA-11 | UV albedo (nadir) | Polar, sun-synchronous | SO2 mass and ozone (McPeters et al., 1992)
NOAA Advanced Very High Resolution Radiometer (AVHRR) | NOAA-10, -11, -12 | 4 Vis-IR channels (nadir) | Polar, sun-synchronous | Aerosol optical depth (Stowe et al., 1992; Long and Stowe, 1994), plume height (Lynch and Stephens, 1996), cloud cover (Stowe et al., 1999)
High Resolution Radiation Sounder (HIRS) | NOAA 6-17 | 19 IR channels (nadir) | Polar, sun-synchronous | SO2 mass and cloud-top height (Miles et al., 2017)
Stratospheric Aerosol and Gas Experiment (SAGE II) | Earth Radiation Budget Satellite (ERBS) | 5 channels, Vis—IR (limb scanning) | Polar | Aerosol optical depth/extinction, aerosol max heights, Ozone (McCormick and Veiga, 1992)
Microwave Sounding Unit (MSU) | NOAA-10,-11,-12 | 4 MW channels (nadir) | Polar, sun-synchronous | Surface-Upper Stratospheric temperature anomalies (Spencer et al., 1990; Dutton and Christy, 1992)
Improved Stratospheric and Mesospheric Sounder (ISAMS) | Upper Atmosphere Research Satellite (UARS) | 8 IR channels (limb scanning) | Near-Polar | Aerosol extinction, mass, and height (Lamberte et al., 1993)
Microwave Limb Sounder (MLS) | UARS | 4 MW channels (limb scanning) | Near-Polar | SO2 mass and temperature profiles (Read et al., 1993)
55

## Slide 56: Observed Pathways Thrust Available Reanalysis Data for Mt. Pinatubo
What is reanalysis data?
Blend of observations with past short-range weather/climate forecasts rerun with modern weather/climate forecasting models.
Generated using data assimilation techniques.
Provides the most complete picture of past weather and climate.
https://climate.copernicus.eu/climate-reanalysis
Available reanalysis data for Mt. Pinatubo eruption:
ERA-5 reanalysis
  1979-present
  Observations from various satellites, radiosonde data and surface observations
  Model input is from ECMWF (European Centre for Medium-Range Weather Forecasts) forecast model, which takes into account forcing from total solar irradiance, GHGs, ozone and some aerosols.
MERRA-2 reanalysis
  1979-present
  Uses similar observations to ERA-5
  Model input is from NASA Goddard Earth Observing System (GEOS) model
56

## Slide 57: Observed Pathways Thrust Data Fusion
Team: J. Li, A. McCombs, L. Shand
57
Goal: fuse observational datasets to obtain near-real time measurements and produce a spatio-temporally complete observational dataset with UQ
simple Kriging does not propagate uncertainty from different sources
  Lattice Kriging: nonparametric approach with multi-resolution basis function representations and Gaussian error structure [Nychka et al. 2017]
  Spatial Random Effects Model [Nguyen et al. 2012, 2013, 2017, 2018]
  Bayesian Hierarchical Framework using Integrated Nested Laplacian Approximation (INLA) [Campos et al. 2023]
Observational data
Observational data
Fused data
Challenge: observational data sets are incongruent, coming from different instruments and possessing different scales and different spatial and temporal ranges
Lattice Kriging Standard Error
Lattice Kriging Mean Temperature
Notes: Simple Kriging does not allow to appropriately propogate uncertainty from different data sources.
We are adapting existing methods, specifically LatticeKrig currently, considered a nonparametric approach which uses a multi-resolution basis function representation and a Gaussian error structure.
The spatial random effects model refers to the Ngyuen et al. (2012) approach but we have been having a hard time getting his code.
The Bayesian Hierarchical Framework is something we are pursuing this summer. It specifically refers to Bo Li and Moe Campos’ approach to data fusion which uses INLA to efficiently sample the posterior.
The prediction variability is the uncertainty estimates of the fused data product. The old version of the slide was an example of what it should not look like, i.e. uncertainty was higher where there is more data. the updated estimated using latticeKrig (an R package based on the Nychka et al. paper) estimate uncertainty more appropriately because you do see the pattern of high uncertainty where data is sparse.
All statistical models being considered are essentially a GP which is a very general class of models which assumes your error structure is Gaussian.

## Slide 58: Synthetic Test Case Formulation
Tiered Datasets, four formulations across
  Temporal trends
  Temporal trends on spatial grid
  Temporal trend on linearly-trended spatial grid
Characteristics
  Distinct numbers of couplings with both linear and nonlinear relationships
  Distinct lags
  Quasi-periodicity
  Noise degree
  Change in mean value
Temporal Trend
Temporal Trend in Space
Spatio-Temporal Trend
Linearly-trended Spatial Grid
Two Variable Changepoint Exemplar

## Slide 59: Idealized Test Case Formulations
Create realistic circulation with E3SM’s dynamic solver using idealizations for process physics/forcings
  Radiation: Newtonian temperature relaxation towards Teq
  Planetary boundary layer: Rayleigh friction & optional topography
Mimic Mt. Pinatubo eruption via a prescribed, time-limited injection of an SO2 and ash Gaussian plume
Develop series of correlated tracers for ‘toy’ chemistry, develop temperature/radiation feedbacks in plume, …
PDE solution: based on transient convection-diffusion-reaction PDE in 2D.
Input: variable winds, reaction functions for chemistry, realistic lifetimes, and variable source magnitudes/durations
Gaussian Plume Plus
Held-Suarez Williamson ++
Notes: Upper four plots show Plume plus model over time. X axis is x-direction, Y-axis is vertical direction (Z or height).
HSW:
- Replace complex physics package with simpler processes
- Optional topography

## Slide 60: Mt. Pinatubo Validation
Validation requires assessments of SAI-related processes in E3SM
  Conservation checks
  STE processes in E3SM (figure below)
  E3SM’s climatic response to Pinatubo
  Compare E3SM’s circulation to reanalysis products (ERA-5)
  Idealized tracer transport experiments
An identified pathway will be considered “correct” if it contains as “nodes” most of the known aerosol direct, indirect and downstream effects from Mt. Pinatubo eruption
Above: enhanced H20 vapor in 1992-93 (“tropical tape recorder”, CMIP6 E3SMv1 coupled historical simulations)
SOURCE
Atmospheric Circulation
IMPACTS
Notional Representation of Subset of Physical Processes
General Pathway
Aerosol Direct Effect
Aerosol Indirect Effect
Downstream Impacts
Radiation Diffusivity
Aerosol Sedimentation
Air Temperature
Net Primary Productivity
Cloud Brightness
H2O Nuclei
Combustion Aerosols
Volcanic
Eruption
Other Source Event
Other Source Event
Sulfate Aerosol Production
Sea
Level
Radiative Flux
Dust Storms
Easy
Hard
Aerosol Direct Effect
Temp changes
Aerosol Indirect Effect
Pathway Identification
Decreased Precipitation & GMSL
60

Notes: There are a lot of observational data we can validate against.
Using different approaches to find pathways will provide confidence in them
- Assess E3SM’s STE processes (e.g., tropical tape recorder)
- Evaluate E3SM’s climatic response to Pinatubo
Tropical tape recorder in water vapor
For assessing E3SM’s troposphere-stratosphere exchange processes
Major moisture source for stratosphere
An effect in which a seasonal cycle in the mixing ratio of a gas is imposed on air entering the stratosphere and is then transported upwards by the Brewer-Dobson circulation