## Slide 1: Accelerating mod/sim workflows through hybrid domain decomposition-based models and the Schwarz alternating method
Irina Tezaur1, Alejandro Mota1, Coleman Alleman1, Greg Phlipot2, Chris Wentland1, Francesco Rizzi3, Joshua Barnett4
ESCO 2024 June 10-14, 2024
SAND2024-06735C
1Sandia National Laboratories, 2MSC Software, 3NexGen Analytics, 4Cadence Design Systems

## Slide 2
Outline
Schwarz Alternating Method for Coupling of Full Order Models (FOMs) in Solid Mechanics
  Motivation & Background
  Quasistatic Formulation
    Numerical Examples
  Extension to Dynamics
    Numerical Examples
Schwarz Alternating Method for FOM-ROM* and ROM-ROM Coupling
  Motivation & Background
  Formulation
  Numerical Examples
Summary and Future Work
* Projection-based Reduced Order Model

## Slide 3
Outline
Schwarz Alternating Method for Coupling of Full Order Models (FOMs) in Solid Mechanics
  Motivation & Background
  Quasistatic Formulation
    Numerical Examples
  Extension to Dynamics
    Numerical Examples
Schwarz Alternating Method for FOM-ROM* and ROM-ROM Coupling
  Motivation & Background
  Formulation
  Numerical Examples
Summary and Future Work
* Projection-based Reduced Order Model

## Slide 4
Motivation for Coupling in Solid Mechanics
Concurrent multiscale coupling for predicting failure
Large scale structural failure frequently originates from small scale phenomena such as defects, microcracks, inhomogeneities and more, which grow quickly in unstable manner
Failure occurs due to tightly coupled interaction between small scale (stress concentrations, material instabilities, cracks, etc.) and large scale (vibration, impact, high loads and other perturbations)
Concurrent multiscale methods are essential for understanding and prediction of behavior of engineering systems when a small scale failure determines the performance of the entire system
Simplification of mesh generation
Creating a high-quality mesh for a single component can take weeks, making it “the single biggest bottleneck in analyses” [Sandia Lab News, 2020]!
Roof failure of Boeing 737 aircraft due to fatigue cracks. From imechanica.org
Schematic of difficult-to-mesh ratcheting mechanism with multiple threaded fasteners. From Parish et al., 2024.
Goal: develop a concurrent multiscale coupling method that is minimally-intrusive to implement into large HPC codes and can simplify the task of meshing complex geometries.
Notes: TODO: what is ratcheting mechanism?

## Slide 5
Requirements for Multiscale Coupling Method
Coupling is concurrent (two-way)
Ease of implementation into existing massively-parallel HPC codes
“Plug-and-play” framework: simplifies task of meshing complex geometries
  Ability to couple regions with different non-conformal meshes, different element types and different levels of refinement
  Ability to use different solvers/time-integrators in different regions
Scalable, fast, robust (we target real engineering problems, e.g., analyses involving failure of bolted components!)
Coupling does not introduce nonphysical artifacts
Theoretical convergence properties/ guarantees

## Slide 6: Schwarz Alternating Method for Domain Decomposition
Proposed in 1870 by H. Schwarz for solving Laplace PDE on irregular domains.
H. Schwarz (1843–1921)
Initialize:
Solve PDE by any method on w/ initial guess for transmission BCs on .
Iterate until convergence:
Solve PDE by any method on w/ transmission BCs on based on values just obtained for .
Solve PDE by any method on w/ transmission BCs on based on values just obtained for .
Crux of Method: if the solution is known in regularly shaped domains, use those as pieces to iteratively build a solution for the more complex domain.
Basic Schwarz Algorithm
2Lions, 1990. 3Zanolli et al., 1987.
overlapping
non-overlapping
Schwarz alternating method most commonly used as a preconditioner for Krylov iterative methods to solve linear algebraic equations.
Idea behind this work: using the Schwarz alternating method as a discretization method for solving multi-scale or multi-physics partial differential equations (PDEs).

## Slide 7: How We Use the Schwarz Alternating Method
AS A PRECONDITIONER FOR THE LINEARIZED SYSTEM
AS A SOLVER FOR THE COUPLED
FULLY NONLINEAR PROBLEM
7

## Slide 8
Outline
Schwarz Alternating Method for Coupling of Full Order Models (FOMs) in Solid Mechanics
  Motivation & Background
  Quasistatic Formulation
    Numerical Examples
  Extension to Dynamics
    Numerical Examples
Schwarz Alternating Method for FOM-ROM* and ROM-ROM Coupling
  Motivation & Background
  Formulation
  Numerical Examples
Summary and Future Work
* Projection-based Reduced Order Model

## Slide 9
Quasistatic Solid Mechanics Formulation
Energy functional defining weak form of the governing PDEs
: Helmholtz free-energy density
deformation gradient
: collection of internal variables (for plastic materials)
: density, : body force, : Piola-Kirchhoff stress
Euler-Lagrange equations, obtained by minimizing :
Quasistatics solves sequence of problems in which loading (body force) is incremented quasistatically w.r.t. pseudo time :
For
Solve with appropriate boundary conditions (BCs)
Increment pseudo time to obtain

## Slide 10
Overlapping Domain Decomposition
Non-overlapping Domain Decomposition
Relevant for multi-material and multi-physics coupling
Alternating Dirichlet-Neumann transmission BCs [Zanolli et al., 1987]
Robin-Robin transmission BCs also lead to convergence [Lions,1990]
relaxation parameter (can help convergence)
Dirichlet-Dirichlet transmission BCs [Schwarz, 1870; Lions, 1988]
Spatial Coupling via (Multiplicative) Alternating Schwarz
Model PDE:

## Slide 11
Overlapping Domain Decomposition
Non-overlapping Domain Decomposition
Relevant for multi-material and multi-physics coupling
Alternating Dirichlet-Neumann transmission BCs [Zanolli et al., 1987]
Robin-Robin transmission BCs also lead to convergence [Lions,1990]
relaxation parameter (can help convergence)
Dirichlet-Dirichlet transmission BCs [Schwarz, 1870; Lions, 1988]
Spatial Coupling via (Multiplicative) Alternating Schwarz
Part 1 of talk
Part 2 of talk
Model PDE:

## Slide 12: Additional Parallelism via Additive Schwarz
Multiplicative Overlapping Schwarz
Additive Overlapping Schwarz
Multiplicative Schwarz: solves subdomain problems sequentially (in serial)
Additive Schwarz: advance subdomains in parallel, communicate boundary condition data later
  Typically requires a few more Schwarz iterations, but does not degrade accuracy
  Parallelism helps balance additional cost due to Schwarz iterations
  Applicable to both overlapping and non-overlapping Schwarz
Model PDE:

## Slide 13: Additional Parallelism via Additive Schwarz
Multiplicative Overlapping Schwarz
Additive Overlapping Schwarz
Multiplicative Schwarz: solves subdomain problems sequentially (in serial)
Additive Schwarz: advance subdomains in parallel, communicate boundary condition data later
  Typically requires a few more Schwarz iterations, but does not degrade accuracy
  Parallelism helps balance additional cost due to Schwarz iterations
  Applicable to both overlapping and non-overlapping Schwarz
Model PDE:
Part 1 of talk
Part 2 of talk

## Slide 14
Overlapping Schwarz Coupling in Quasistatics
Advantages:
Conceptually very simple.
Allows the coupling of regions with different non-conforming meshes, different element types, and different levels of refinement.
Information is exchanged among two or more regions, making coupling concurrent.
Different solvers can be used for the different regions.
Different material models can be coupled if they are compatible in the overlap region.
Simplifies the task of meshing complex geometries for the different scales.
outer quasistatic loop

## Slide 15
Convergence Proof*
*A. Mota, I. Tezaur, C. Alleman. "The Schwarz Alternating Method in Solid Mechanics", CMAME 319 (2017), 19-51.
Notes: The proof effectively constructs a sequence of solutions phi^n and demonstrates that this sequence converges to the unique minimizer of the energy functional \Phi defining the single-domain problem, and combines concepts used in the analysis of Sobolev, Lions, and others, in studying the convergence of the Schwarz method.

## Slide 16
Implementation in Albany-LCM and Sierra/SM HPC Codes
The overlapping Schwarz alternating method has been implemented in two Sandia HPC codes: Albany-LCM and Sierra/SM
Albany-LCM1
Open-source parallel, C++, multi-physics, finite element code that relies heavily on Trilinos2 libraries
Parallel implementation of Schwarz alternating method uses the Data Transfer Kit (DTK)3
Sierra/Solid Mechanics (Sierra/SM)
Sandia proprietary production Lagrangian 3D code for finite element analysis of solids & structures
Schwarz alternating method was “implemented” in Sierra/SM using Arpeggio iterative coupling framework
We did not have to write any code in Sierra/SM to implement Schwarz!
1https://github.com/sandialabs/LCM.git. 2http://github.com/trilinos/Trilinos.git. 3https://github.com/ORNL-CEES/DataTransferKit.
Data Transfer Kit (DTK)
Notes: TODO: fill in slide.

## Slide 17
Outline
Schwarz Alternating Method for Coupling of Full Order Models (FOMs) in Solid Mechanics
  Motivation & Background
  Quasistatic Formulation
    Numerical Examples
  Extension to Dynamics
    Numerical Examples
Schwarz Alternating Method for FOM-ROM* and ROM-ROM Coupling
  Motivation & Background
  Formulation
  Numerical Examples
Summary and Future Work
* Projection-based Reduced Order Model

## Slide 18
Schwarz Iteration
Cuboid Problem
Coupling of two cuboids with square base (above).
Neohookean-type material model.

## Slide 19
Cuboid Problem: Convergence and Accuracy
Top right: convergence of the cuboid problem for different mesh sizes and fixed overlap volume fraction. The Schwarz alternating method converges linearly.
Bottom right: convergence factor as a function of overlap volume and different mesh. There is faster linear convergence with increasing overlap volume fraction.
Below: relative errors in displacement and stress w.r.t. single-domain reference solution. Errors are on the order of machine precision.

## Slide 20
Notched Cylinder
Notched cylinder that is stretched along its axial direction.
Domain decomposed into two subdomains.
Neohookean-type material model.

## Slide 21
The Schwarz alternating method is capable of coupling different mesh topologies.
The notched region, where stress concentrations are expected, is finely meshed with tetrahedral elements.
The top and bottom regions, presumably of less interest, are meshed with coarser hexahedral elements.
Notched Cylinder: TET - HEX Coupling

## Slide 22
Relative errors in displacement w.r.t. single-domain reference solution are dominated by geometric (rather than coupling) error.
Notched Cylinder: TET - HEX Coupling

## Slide 23: Laser Weld (Albany/LCM)
Laser weld specimen
Problem of practical scale.
Isotropic elasticity and J2 plasticity with linear isotropic hardening.
Identical parameters for weld and base materials for proof of concept, to become independent models.
Coupled Schwarz discretization
(50% reduction in model size)
Single domain discretization
Notes: ~200K dofs

## Slide 24: Laser Weld (Albany/LCM): Strong Scalability of Parallel Schwarz with DTK
Near-ideal linear speedup (64-1024 cores).
Data Transfer Kit (DTK)

## Slide 25: Laser Weld (Sierra/SM): Uniaxial Tension-Test Models
Single domain:
123,425 elements
Overlapping Schwarz:
29,254 coarse, 78,549 fine elements
Stress (Pa)
Load step
single domain
Schwarz (16 iters)
The domains for Schwarz coupling are meshed independently
This provides the ability to try different meshing schemes for each subdomain
No need to re-mesh entire domain
Schwarz gives accurate prediction of stress states if tight enough Schwarz tolerance is used
  Tight Schwarz tolerance needed due to large disparity between element sizes
For now, Schwarz is slower on this problem, but we are optimizing this

## Slide 26: Tensile Bar
The alternating Schwarz method can be used as part of a homogenization (upscaling) process to bridge gap b/w microscopic and macroscopic regions
  Microstructure embedded in ASTM tensile geometry (right).
  Fix microstructure, investigate ensemble of uniaxial loads.
  Fit flow curves with a macroscale J2 plasticity model (below).
macro-scale
micro-structure
macro-scale
Work by C. Alleman, J. Foulk,
D. Littlewood, G. Bergel
  Goal: study strain localization in microstructure.
Notes: The last quasistatic example is another production-type problem known as the tensile bar problem and is courtesy of my colleagues Coleman Alleman, Jay Foulk, Dave Littlewood and Guy Bergel. This problem illustrates an interesting use of the Schwarz alternating method, in particular, that the method can be used as a part of a homogenization or upscaling process to bridge the gap between microscopic and macroscopic regions. Here, Coleman and his collaborators took a tensile geometry and embedded in it a microstructure, shown in the middle, with the goal of studying strain localization in the microstructure. The crystal plasticity microscale model in the microstructure was coupled to a J2 plasticity macroscale model in the rest of the domain using Schwarz, and a set of calculations were performed under an ensemble of uniaxial loads. Upscaling was performed by fitting flow curves to this set of ensembles using the J2 plasticity macroscale model.

## Slide 27
Outline
Schwarz Alternating Method for Coupling of Full Order Models (FOMs) in Solid Mechanics
  Motivation & Background
  Quasistatic Formulation
    Numerical Examples
  Extension to Dynamics
    Numerical Examples
Schwarz Alternating Method for FOM-ROM* and ROM-ROM Coupling
  Motivation & Background
  Formulation
  Numerical Examples
Summary and Future Work
* Projection-based Reduced Order Model

## Slide 28
Solid Dynamics Formulation
Kinetic energy:
Potential energy:
Lagrangian:
Action functional:
Euler-Lagrange equations:
Semi-discrete problem following FEM discretization in space:

## Slide 29: Time-Advancement Within the Schwarz Framework
Step 0: Initialize
Controller time stepper
Time integrator for W1
Time integrator for W2
Model PDE:

## Slide 30: Time-Advancement Within the Schwarz Framework
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Integrate using
Controller time stepper
Time integrator for W1
Time integrator for W2
Model PDE:

## Slide 31: Time-Advancement Within the Schwarz Framework
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Step 2: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times .
Integrate using
Interpolate from to
Controller time stepper
Time integrator for W1
Time integrator for W2
Model PDE:

## Slide 32: Time-Advancement Within the Schwarz Framework
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Step 2: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times .
Step 3: Check for convergence at time .
Controller time stepper
Time integrator for W1
Time integrator for W2
Model PDE:

## Slide 33: Time-Advancement Within the Schwarz Framework
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Step 2: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times .
Step 3: Check for convergence at time .
If unconverged, return to Step 1.
Interpolate from to
Integrate using
Controller time stepper
Time integrator for W1
Time integrator for W2
Model PDE:

## Slide 34: Time-Advancement Within the Schwarz Framework
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Step 2: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times .
Step 3: Check for convergence at time .
If unconverged, return to Step 1.
If converged, set and return to Step 1.
Integrate using
Interpolate from to
Can use different integrators with different time steps within each domain!
Controller time stepper
Time integrator for W1
Time integrator for W2
Model PDE:

## Slide 35: Time-Advancement Within the Schwarz Framework
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Step 2: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times .
Step 3: Check for convergence at time .
If unconverged, return to Step 1.
If converged, set and return to Step 1.
Integrate using
Interpolate from to
Controller time stepper
Time integrator for W1
Time integrator for W2
Time-stepping procedure is equivalent to doing Schwarz on space-time domain [Mota et al. 2022].
Model PDE:

## Slide 36
Schwarz Alternating Method for Dynamic Multiscale Coupling: Theory
Like for quasistatics, dynamic alternating Schwarz method converges provided each single-domain problem is well-posed and overlap region is non-empty, under some conditions on .
Well-posedness for the dynamic problem requires that action functional be strictly convex or strictly concave, where is the Lagrangian.
  This is studied by looking at its second variation
We can show assuming a Newmark time-integration scheme that for the fully-discrete problem:
can always be made positive by choosing a sufficiently small
Numerical experiments reveal that requirements for stability/accuracy typically lead to automatic satisfaction of this bound.
*A. Mota, I. Tezaur, G. Phlipot. "The Schwarz alternating method for dynamic solid mechanics", IJNME, 2022.

## Slide 37
Outline
Schwarz Alternating Method for Coupling of Full Order Models (FOMs) in Solid Mechanics
  Motivation & Background
  Quasistatic Formulation
    Numerical Examples
  Extension to Dynamics
    Numerical Examples
Schwarz Alternating Method for FOM-ROM* and ROM-ROM Coupling
  Motivation & Background
  Formulation
  Numerical Examples
Summary and Future Work
* Projection-based Reduced Order Model

## Slide 38
Elastic Wave Propagation
Linear elastic clamped beam with Gaussian initial condition for the 𝑧-displacement.
Simple problem with analytical exact solution but very stringent test for discretization methods.
Test Schwarz with 2 subdomains: .
Left: Initial condition (blue) and final solution (red). Wave profile is negative of initial profile at time T = 1.0e-3.
Time-discretizations: Newmark (implicit, explicit)
Meshes: HEX, TET

## Slide 39
z-displacement
Table 1: Averaged (over times + domains) relative errors in z–displacement (blue) and z-velocity (green) for several different Schwarz couplings, 50% overlap volume fraction
LM = Lumped Mass, CM = Consistent Mass
z-velocity
 | Implicit-Implicit |  | Explicit(CM)-Implicit |  | Explicit(LM)-Implicit | 
Conformal HEX - HEX | 2.79e-3 | 7.32e-3 | 3.53e-3 | 8.70e-3 | 4.72e-3 | 1.19e-2
Nonconformal HEX - HEX | 2.90e-3 | 7.10e-3 | 2.82e-3 | 7.29e-3 | 2.84e-3 | 7.33e-3
TET - HEX | 2.79e-3 | 7.58e-3 | 3.52e-3 | 8.92e-3 | 4.72e-3 | 1.19e-2
Dynamic Schwarz coupling introduces no dynamic artifacts that are pervasive in other coupling methods!
Elastic Wave: Different Integrators, Same s

## Slide 40
Elastic Wave: Different Integrators, Different s
Figures above: Plots of displacement, velocity and acceleration for the elastic wave propagation problem using different time integrators (implicit and explicit) and different time steps (1e-2s and 2e-7s) for each subdomain, superimposed over the analytic single domain solution.
The analytic solution is indistinguishable from Schwarz solutions (hidden behind the solutions for (red) and (green))!
Displacement
Velocity
Acceleration

## Slide 41
Uniaxial aluminum cylindrical tensile specimen with inelastic J2 material model.
Domain decomposition into two subdomains (right): = ends, = gauge.
Nonconformal HEX + composite TET10 coupling via Schwarz.
Implicit Newmark time-integration with adaptive time-stepping algorithm employed in both subdomains.
Slight imperfection introduced at center of gauge to force necking upon pulling in vertical direction.
+
Tension Specimen

## Slide 42
Tension Specimen: Expected Result

## Slide 43
Tension Specimen: Displacement & EQPS*
Average of 3 Schwarz iterations/time step required for convergence to Schwarz tolerance of 1e-6.
y-displacement
EQPS*
*EQPS = Equivalent Plastic Strain
Notes: So, lets see what happens. The plots are showing the y-displacement and the nodal equivalent plastic strain in the specimen. You see a nice smooth transition of the solution between the two subdomains, and the method is able to simulate the necking behavior in the middle. It takes on average 3 Schwarz iterations/time step to achieve a relatively tight convergence tolerance of 1e-6.

## Slide 44
Bolted Joint Problem
bolts (Composite TET10), parts (HEX).
Inelastic J2 material model in both subdomains.
  steel
  steel component, aluminum (bottom) plate
Schwarz solution compared to single-domain solution on composite TET10 mesh.
BC: x-disp = 0.02 at T = 1.0e-3 on top of parts.
Run until T = 5.0e-4 w/ dt = 1e-5 + implicit Newmark with analytic mass matrix for composite tet 10s.
Problem of practical scale.

## Slide 45
Single
Schwarz
Bolted Joint Problem: Displacement

## Slide 46
Single
Schwarz
Bolted Joint Problem: Equivalent Plastic Strain (EQPS)

## Slide 47
Bolted Joint Problem: Convergence Rate
Figure above: Convergence behavior of the dynamic Schwarz algorithm for the bolted joint problem
Linear convergence rate is observed for dynamic Schwarz algorithm, as for the quasistatic Schwarz algorithm.

## Slide 48
Bolted Joint Problem: Performance
 | CPU times (64 procs*) | Avg # Schwarz iters | Max # Schwarz iters
Single Domain | 3h 34m |  | 
Schwarz | 2h 42m | 3.22 | 4
Single Domain (finer) | 17h 00m |  | 
Schwarz (finer mesh of bolts) | 29h 29m | 3.28 | 4
 | CPU times (64 procs*) | Avg # Schwarz iters | Max # Schwarz iters
Single Domain | 3h 34m |  | 
Schwarz | 2h 42m | 3.22 | 4
Single Domain (finer) | 17h 00m |  | 
Schwarz (finer mesh of bolts) | 29h 29m | 3.28 | 4
* On SNL ascicgpu15, 16, 17 machines (Intel Skylake CPU processor), Schwarz tol = 1e-6.
48
* On SNL ascicgpu15, 16, 17 machines (Intel Skylake CPU processor), Schwarz tol = 1e-6.

## Slide 49
* On SNL ascicgpu15, 16, 17 machines (Intel Skylake CPU processor), Schwarz tol = 1e-6.
49
Despite its iterative nature, Schwarz can actually be faster than single domain run for discretizations having comparable # of elements in the bolts.
Bolted Joint Problem: Performance
* On SNL ascicgpu15, 16, 17 machines (Intel Skylake CPU processor), Schwarz tol = 1e-6.
 | CPU times (64 procs*) | Avg # Schwarz iters | Max # Schwarz iters
Single Domain | 3h 34m |  | 
Schwarz | 2h 42m | 3.22 | 4
Single Domain (finer) | 17h 00m |  | 
Schwarz (finer mesh of bolts) | 29h 29m | 3.28 | 4
 | CPU times (64 procs*) | Avg # Schwarz iters | Max # Schwarz iters
Single Domain | 3h 34m |  | 
Schwarz | 2h 42m | 3.22 | 4
Single Domain (finer) | 17h 00m |  | 
Schwarz (finer mesh of bolts) | 29h 29m | 3.28 | 4

## Slide 50
* On SNL ascicgpu15, 16, 17 machines (Intel Skylake CPU processor), Schwarz tol = 1e-6.
Despite its iterative nature, Schwarz can actually be faster than single domain run for discretizations having comparable # of elements in the bolts.
  Even if the method is more computationally expensive for some resolutions, it may be preferred for its ability to rapidly change and evaluate a variety of engineering designs (our typical use case).
Bolted Joint Problem: Performance
* On SNL ascicgpu15, 16, 17 machines (Intel Skylake CPU processor), Schwarz tol = 1e-6.
 | CPU times (64 procs*) | Avg # Schwarz iters | Max # Schwarz iters
Single Domain | 3h 34m |  | 
Schwarz | 2h 42m | 3.22 | 4
Single Domain (finer) | 17h 00m |  | 
Schwarz (finer mesh of bolts) | 29h 29m | 3.28 | 4
 | CPU times (64 procs*) | Avg # Schwarz iters | Max # Schwarz iters
Single Domain | 3h 34m |  | 
Schwarz | 2h 42m | 3.22 | 4
Single Domain (finer) | 17h 00m |  | 
Schwarz (finer mesh of bolts) | 29h 29m | 3.28 | 4

## Slide 51
Despite its iterative nature, Schwarz can actually be faster than single domain run for discretizations having comparable # of elements in the bolts.
  Even if the method is more computationally expensive for some resolutions, it may be preferred for its ability to rapidly change and evaluate a variety of engineering designs (our typical use case).
Dynamic Schwarz converges in between 2-4 Schwarz iterations per time-step despite the overlap region being very small for this problem.
* On SNL ascicgpu15, 16, 17 machines (Intel Skylake CPU processor), Schwarz tol = 1e-6.
overlap region
Bolted Joint Problem: Performance
 | CPU times (64 procs*) | Avg # Schwarz iters | Max # Schwarz iters
Single Domain | 3h 34m |  | 
Schwarz | 2h 42m | 3.22 | 4
Single Domain (finer) | 17h 00m |  | 
Schwarz (finer mesh of bolts) | 29h 29m | 3.28 | 4
 | CPU times (64 procs*) | Avg # Schwarz iters | Max # Schwarz iters
Single Domain | 3h 34m |  | 
Schwarz | 2h 42m | 3.22 | 4
Single Domain (finer) | 17h 00m |  | 
Schwarz (finer mesh of bolts) | 29h 29m | 3.28 | 4

## Slide 52
Outline
Schwarz Alternating Method for Coupling of Full Order Models (FOMs) in Solid Mechanics
  Motivation & Background
  Quasistatic Formulation
    Numerical Examples
  Extension to Dynamics
    Numerical Examples
Schwarz Alternating Method for FOM-ROM* and ROM-ROM Coupling
  Motivation & Background
  Formulation
  Numerical Examples
Summary and Future Work
* Projection-based Reduced Order Model

## Slide 53: Motivation for ROM-ROM/ROM-FOM Couplings
The past decades have seen tremendous investment in simulation frameworks for coupled multi-scale and multi-physics problems.
Frameworks rely on established mathematical theories to couple physics components.
Most existing coupling frameworks are based on traditional discretization methods.
Monolithic (Lagrange multipliers)
Partitioned (loose) coupling
Iterative (Schwarz, optimization)
M1
M2
M3
M4
N3
N4
N1
N2
N5
N3
N4
N5
N2
N1
Mesh-based (FE, FV, FD)
Meshless (SPH, MLS)
Implicit, explicit
Eulerian, Lagrangian…
Complex System Model
Traditional Methods
Coupled Numerical Model
Ocean
(MPAS-O)
Atmos.
(EAM)
Sea Ice
(MPAS-SI)
Land Ice
(MALI)
Land
(ELM)
PDEs, ODEs
Nonlocal integral
Classical DFT
Atomistic, …
Notes: The past decades have seen a tremendous amount of investment in the development of simulation frameworks for coupled multi-scale and multi-physics problems. These frameworks rely on established mathematical theories to couple physics components discretized using so-called traditional discretization methods such as finite elements, finite volumes and finite differences. A prime example is the DOE’s global climate model, the Energy Exascale Earth System Model (E3SM), which couples 5 physics components (atmosphere, ocean, sea ice, land ice and land). Each component is developed separately according to the relevant physics, dynamics and numerical methods, and the components are coupled in a way that ensures stability, accuracy and conservation.

## Slide 54: Motivation for ROM-ROM/ROM-FOM Couplings
The past decades have seen tremendous investment in simulation frameworks for coupled multi-scale and multi-physics problems.
Frameworks rely on established mathematical theories to couple physics components.
Most existing coupling frameworks are based on traditional discretization methods.
Monolithic (Lagrange multipliers)
Partitioned (loose) coupling
Iterative (Schwarz, optimization)
M1
M2
M3
M4
N3
N4
N1
N2
N5
N3
N4
N5
N2
N1
PDEs, ODEs
Nonlocal integral
Classical DFT
Atomistic, …
Mesh-based (FE, FV, FD)
Meshless (SPH, MLS)
Implicit, explicit
Eulerian, Lagrangian, …
Complex System Model
Traditional Methods
Coupled Numerical Model
Ocean
(MPAS-O)
Atmos.
(EAM)
Sea Ice
(MPAS-SI)
Land Ice
(MALI)
Land
(ELM)
DMD=N3
ROM=N4
N1
PINN=N2
UDE=N5
Traditional + Data-Driven Methods
PINNs
Neural ODEs
Projection-based ROMs, …
Unfortunately, existing algorithmic and software infrastructures are ill-equipped to handle plug-and-play integration of non-traditional, data-driven models!
There is currently a big push to integrate data-driven methods into modeling & simulation toolchains.

## Slide 55
Alternating Schwarz-based coupling
Optimization-based coupling
Coupling via generalized mortar methods
Principal research objective:
Discover mathematical principles guiding the assembly of standard and data-driven numerical models in stable, accurate and physically consistent ways.
Principal research challenges: we lack mathematical and algorithmic understanding of how to
“Mix-and-match” standard and data-driven models from three-classes
  Class A: projection-based reduced order models (ROMs)
  Class B: machine-learned models, i.e., Physics-Informed Neural Networks (PINNs)
  Class C: flow map approximation models, i.e., dynamic model decomposition (DMD) models
Ensure well-posedness & physical consistency of resulting heterogeneous models.
Solve such heterogeneous models efficiently.
Three coupling methods:
Flexible Heterogeneous Numerical Methods (fHNM) Project
This talk.
This talk.
Notes: Class A and B are equation-based DDMs: they seek restrict a weak or strong form of the PDE to a finite-dimensional function space 𝑈_𝑖, spanned by a basis {𝑏_𝑖^𝑘 }_(𝑘=1)^(𝑁_𝑖 )
Class C DDMs are equation-free I/O relations 𝑢_𝑖 (𝑡)=〖𝐺_𝑖 (𝑓〗_𝑖,𝑢_(𝑖,0);𝑝_(𝑖,1),⋯,𝑝_(𝑖,𝑃)) with inputs (“ports”) 𝑝_(𝑖,𝑗).
TODO: add refs to other talks in MS.

## Slide 56: Projection-Based Model Order Reduction via the POD/LSPG* Method
56
Full Order Model (FOM):
Proper Orthogonal Decomposition (POD):
Solve ODE at different design points
1. Data Acquisition
2. Learning of Reduced Basis
3. Projection-Based Reduction
Number of time steps
Number of State Variables
Save solution data
Reduce the number of unknowns
Discretize FOM in time
Apply hyper-reduction and minimize residual
Hyper-reduction/sample mesh
ROM = projection-based Reduced Order Model HROM = Hyper-reduced ROM
*Least-Squares Petrov-Galerkin

## Slide 57
Outline
Schwarz Alternating Method for Coupling of Full Order Models (FOMs) in Solid Mechanics
  Motivation & Background
  Quasistatic Formulation
    Numerical Examples
  Extension to Dynamics
    Numerical Examples
Schwarz Alternating Method for FOM-ROM* and ROM-ROM Coupling
  Motivation & Background
  Formulation
  Numerical Examples
Summary and Future Work
* Projection-based Reduced Order Model

## Slide 58: Schwarz Extensions to FOM-ROM and ROM-ROM Couplings
58
Choice of domain decomposition
Overlapping vs. non-overlapping domain decomposition?
  Non-overlapping more flexible but typically requires more Schwarz iterations
FOM vs. ROM subdomain assignment?
  Do not assign ROM to subdomains where they have no hope of approximating solution
Snapshot collection and reduced basis construction
Are subdomains simulated independently in each subdomains or together?
Enforcement of boundary conditions (BCs) in ROM at Schwarz boundaries
Strong vs. weak BC enforcement?
  Strong BC enforcement difficult for some models (e.g., cell-centered finite volume, PINNs)
Optimizing parameters in Schwarz BCs for non-overlapping Schwarz?
Choice of hyper-reduction
What hyper-reduction method to use?
  Application may require particular method (e.g., ECSW for solid mechanics problems)
How to sample Schwarz boundaries in applying hyper-reduction?
  Need to have enough sample mesh points at Schwarz boundaries to apply Schwarz

## Slide 59
Outline
Schwarz Alternating Method for Coupling of Full Order Models (FOMs) in Solid Mechanics
  Motivation & Background
  Quasistatic Formulation
    Numerical Examples
  Extension to Dynamics
    Numerical Examples
Schwarz Alternating Method for FOM-ROM* and ROM-ROM Coupling
  Motivation & Background
  Formulation
  Numerical Examples
Summary and Future Work
* Projection-based Reduced Order Model

## Slide 60: 2D Inviscid Burgers Equation
Figure above: solution of component at various times
FOM discretization:
Spatial discretization given by a Godunov-type scheme with elements in each dimension
Implicit trapezoidal method with fixed
0
100
100
0
Problem setup:
Two parameters . Training: uniform sampling of by a grid. Testing: query unsampled point
Popular analog for fluid problems where shocks are possible, and particularly difficult for conventional projection-based ROMs
Notes: TODO: say something about how BCs implemented?

## Slide 61: Schwarz Coupling Details
61
Choice of domain decomposition
Overlapping DD of into 4 subdomains coupled via multiplicative Schwarz
Solution in is most difficult to capture by ROM
Snapshot collection and reduced basis construction
Single-domain FOM on used to generate snapshots/POD modes
Enforcement of boundary conditions (BCs) in ROM at Schwarz boundaries
BCs imposed strongly using Method 1 of [Gunzburger et al., 2007] at indices
  POD modes made to satisfy homogeneous DBCs:
  BCs imposed by modifying :
Choice of hyper-reduction
Energy Conserving Sampling & Weighting (ECSW) method for hyper-reduction
All points on Schwarz boundaries are included in the sample mesh
0
100
100
0
Notes: TODO: say how possible to do strong BC impl in FV method.
TODO: double check about all points on Schwarz boundaries being included in sample mesh with Joshua/Chris.

## Slide 62
0
100
100
0
FOM in as this is “hardest” subdomain for ROM
HROMs in , , capture 99% snapshot energy
Method converges in 3 Schwarz iterations per controller time-step
Errors O(0.1%) with 0 error in
2.26 speedup achieved over all-FOM coupling
1 SD
FOM-HROM-HROM-HROM Coupling
Subdomains | 99% SV Energy |  | 
 |  | MSE (%) | CPU time (s)
 |  | 0.0 | 95
 | 120 | 0.26 | 26
 | 60 | 0.43 | 17
 | 66 | 0.34 | 21
Total |  |  | 159
Subdomains | 99% SV Energy |  | 
 |  | MSE (%) | CPU time (s)
 |  | 0.0 | 95
 | 120 | 0.26 | 26
 | 60 | 0.43 | 17
 | 66 | 0.34 | 21
Total |  |  | 159
Further speedups possible via code optimizations, additive Schwarz and reduction of # sample mesh points.
Notes: 360: all-FOM case
Not possible for subdomain 2->4 to pollute 1 b/c of direction of propagation

## Slide 63: 2D Shallow Water Equations (SWE)
FOM discretization:
Spatial discretization given by a first-order cell-centered finite volume discretization with elements in each dimension
Implicit first order temporal discretization: backward Euler with fixed
Implemented in Pressio-demoapps (https://github.com/Pressio/pressio-demoapps)
Problem setup:
, Gaussian initial condition
Coriolis parameter for training, and for testing
Hyperbolic PDEs modeling wave propagation below a pressure surface in a fluid (e.g., atmosphere, ocean).
Figure above: FOM solutions to SWE for (left) and (right).
Notes: TODO: ask Chris re: temporal discretization

## Slide 64: Schwarz Coupling Details
64
Choice of domain decomposition
Non-overlapping DD of into 4 subdomains coupled via additive Schwarz
  OpenMP parallelism with 1 thread/subdomain
All-ROM or All-HROM coupling via Pressio*
Snapshot collection and reduced basis construction
Single-domain FOM on used to generate snapshots/POD modes
Enforcement of boundary conditions (BCs) in ROM at Schwarz boundaries
BCs are imposed approximately by fictitious ghost cell states
  Implementing Neumann and Robin BCs is challenging
Ghost cells introduce some overlap even with non-overlapping DD
  Dirichlet-Dirichlet non-overlapping Schwarz is stable/convergent!
Choice of hyper-reduction
Collocation for hyper-reduction: min residual at small subset DOFs
Assume fixed budget of sample mesh points at Schwarz boundaries
Ghost cells
Figure right: non-overlapping DD w/ ghost cells creating overlap
Figure above: sample mesh (yellow) and stencil (white) cells
Green: different from Burgers’ problem
*https://github.com/Pressio/pressio-demoapps
Notes: TODO: ask Chris what hyper-reduction is used now.

## Slide 65: Schwarz All-ROM Domain Overlap Study
65
Study of Schwarz convergence for all-ROM coupling as a function of := cell width of overlap region (not including ghost cells).
Dirichlet-Dirichlet coupling with no-overlap performs well with no convergence issues (movie, left) and errors comparable to Dirichlet-Dirichlet coupling with overlap (figure below, left)
Movie above: FOM (left), 4 subdomain ROM coupled via non-overlapping Schwarz (middle), and 4 subdomain ROM coupled via overlapping Schwarz (right) for predictive SWE problem with . All ROMs have POD modes.
Schwarz iterations decrease (very roughly) with (figure, right) whereas evaluating scales with
  there is no reason not to do non-overlapping coupling for this problem
Figures above: relative error and average # Schwarz iterations as a function of and Black : training, red : testing.
Notes: Q: Is it true that 80 POD modes/subdomain? Had K = 80 in Chris’s slides.

## Slide 66: Schwarz Boundary Sampling for All-HROM Coupling
66
Including too many Schwarz boundary points () in sample mesh given fixed budget of sample mesh points may lead to too few sample mesh points in interior
For SWE problem, we can get away with 10% boundary sampling (movie above, right-most frame)
Naïve/sparsely-sampled Schwarz boundary results in failure to transmit coupling information during Schwarz
Movie above: FOM (left), all HROM with (middle) and all HROM with (left). ROMs have modes and sample mesh points.
Figure above: example sample mesh with sampling rate
Key question: how many Schwarz boundary points need to be included in sample mesh when performing HROM coupling?
Notes: To clarify the sampling rate Nb, the value of Nb = 0 just means that there is no deliberate sampling at the interface; there is still roughly N * X% points sampled at the interface given a random sampling scheme. Nb is a fixed rate of sampling at the interface, regardless of the overall sampling rate. Nb = 10 means every tenth cell at the interface is sampled, or 10% of all interface cells (Nb = 5 is 20% of all interface cells, etc). The use of an integer for Nb was just stylistic, since N and Ns are also integers.
hris.

## Slide 67: Coupled HROM Performance
67
For a fixed ROM dimension, Schwarz delivers lower error and comparable cost!
There are noticeable cost savings relative to monolithic FOM!
Accuracy similar for predictive (red) and non-predictive (black) cases.
Solid:
Dashed:
Notes: To clarify the sampling rate Nb, the value of Nb = 0 just means that there is no deliberate sampling at the interface; there is still roughly N * X% points sampled at the interface given a random sampling scheme. Nb is a fixed rate of sampling at the interface, regardless of the overall sampling rate. Nb = 10 means every tenth cell at the interface is sampled, or 10% of all interface cells (Nb = 5 is 20% of all interface cells, etc). The use of an integer for Nb was just stylistic, since N and Ns are also integers.
hris.

## Slide 68: Teaser: 2D Euler Equations Riemann Problem
FOM discretization:
Spatial discretization given by a first-order cell-centered finite volume discretization with or elements in each dimension
Implicit first order temporal discretization: backward Euler with fixed
Implemented in Pressio-demoapps (https://github.com/Pressio/pressio-demoapps)
Problem setup:
, homogeneous Neumann BCs
Fix , ,
Vary ; IC from compatibility conditions*
  Training:
  Testing:
+
*Schulz-Rinne, 1993.
Preliminary results:
Schwarz can stabilize unstable monolithic ROM for fixed dimension (above)
Since shock traverses all parts of domain, achieving speedups with Schwarz is more difficult
Notes: TODO: ask Chris re: spatial discretization.

## Slide 69
Outline
Schwarz Alternating Method for Coupling of Full Order Models (FOMs) in Solid Mechanics
  Motivation & Background
  Quasistatic Formulation
    Numerical Examples
  Extension to Dynamics
    Numerical Examples
Schwarz Alternating Method for FOM-ROM* and ROM-ROM Coupling
  Motivation & Background
  Formulation
  Numerical Examples
Summary and Future Work
* Projection-based Reduced Order Model

## Slide 70
Summary
The Schwarz alternating method has been developed for concurrent multi-scale coupling of conventional and data-driven models.
Coupling is concurrent (two-way).
Ease of implementation into existing massively-parallel HPC codes.
“Plug-and-play” framework: simplifies task of meshing complex geometries!
  Ability to couple regions with different non-conformal meshes, different element types and different levels of refinement.
  Ability to use different solvers (including ROM/FOM) and time-integrators in different regions.
Scalable, fast, robust on real engineering problems
Coupling does not introduce nonphysical artifacts.
Theoretical convergence properties/guarantees.









## Slide 71: Ongoing & Future Work
71
Development fundamentally new approach for simulating multi-scale mechanical contact using the Dirichlet-Neumann Schwarz alternating method
  Contact constraints are replaced with boundary conditions applied iteratively at contact boundaries
Implementation of non-overlapping Schwarz in Sierra/SM
Working with analysts to apply Schwarz to problems of interest to Sandia missions
  Laser welds
  Fastener modeling for joints
  Salt caverns for oil storage
Rigorous analysis of why Dirichlet-Dirichlet BC “work” when employing non-overlapping Schwarz with discretizations that employ ghost cells
Extension to coupling of non-intrusive ROMs (dynamic mode decomposition, operator inference, neural networks)
Development of automated criteria to determine appropriate use of less refined or reduced-order models w/o sacrificing accuracy, enabling real-time transitions between different model fidelities
Contact boundaries and
Impact of two 3D beams having different meshes with Schwarz contact method. From [Mota et al., 2023].
From Murugesan et al., 2020.
Notes: TODO: fill in!

## Slide 72: Team & Acknowledgments
72
Irina Tezaur
Joshua Barnett
Alejandro Mota
Chris Wentland
Francesco Rizzi
Coleman Alleman
Greg Phlipot
Notes: TODO: update team.

## Slide 73: References
[1] A. Mota, I. Tezaur, C. Alleman. “The Schwarz Alternating Method in Solid Mechanics", Comput. Meth. Appl. Mech. Engng. 319 (2017), 19-51.
[2] A. Mota, I. Tezaur, G. Phlipot. “The Schwarz Alternating Method for Dynamic Solid Mechanics”, Comput. Meth. Appl. Mech. Engng. 121 (21) (2022) 5036-5071.
[3] J. Barnett, I. Tezaur, A. Mota. “The Schwarz alternating method for the seamless coupling of nonlinear reduced order models and full order models”, ArXiv pre-print, 2022. https://arxiv.org/abs/2210.12551
[4] W. Snyder, I. Tezaur, C. Wentland. “Domain decomposition-based coupling of physics-informed neural networks via the Schwarz alternating method”, ArXiv pre-print, 2023. https://arxiv.org/abs/2311.00224
[5] A. Mota, D. Koliesnikova, I. Tezaur. “A Fundamentally New Coupled Approach to Contact Mechanics via the Dirichlet-Neumann Schwarz Alternating Method”, ArXiv pre-print, 2023. https://arxiv.org/abs/2311.05643
Email: ikalash@sandia.gov
URL: www.sandia.gov/~ikalash

## Slide 74: Start of Backup Slides

## Slide 75
S.L. Sobolev (1936): posed Schwarz method for linear elasticity in variational form and proved method’s convergence by proposing a convergent sequence of energy functionals.
S.G. Mikhlin (1951): proved convergence of Schwarz method for general linear elliptic PDEs.
P.-L. Lions (1988): studied convergence of Schwarz for nonlinear monotone elliptic problems using max principle.
A. Mota, I. Tezaur, C. Alleman (2017): proved convergence of the alternating Schwarz method for finite deformation quasi-static nonlinear PDEs (with energy functional ) with a geometric convergence rate.
S.G. Mikhlin
(1908 – 1990)
S.L. Sobolev (1908 – 1989)
A. Mota, I. Tezaur, C. Alleman
Using the Schwarz alternating as a discretization method for PDEs is natural idea with a sound theoretical foundation.
Theoretical Foundation
P.- L. Lions (1956-)
Notes: A(F,Z) = Helmholtz free-energy density, Z = collection of internal variables, F = grad(phi) = deformation gradient, B = body force, T = traction on boundary
P = \partial A/\partial F = first Piola-Kirchoff stress
2nd equation is Euler-Lagrange equation

## Slide 76
Notched cylinder subjected to tensile load with an elastic and J2 elasto-plastic regions.
Coarse region is elastic and fine region is elasto-plastic.
The overlap region in the first mesh is nearer the notch, where plastic behavior is expected.
Overlap far from notch.
Overlap near notch.
Coupled regions
Coarse, elastic region
Fine, elasto-plastic region
Notched Cylinder: Coupling Different Materials
The Schwarz method is capable of coupling regions with different material models.

## Slide 77
When the overlap region is far from the notch, no plastic deformation exists in it: the coarse and fine regions predict the same behavior.
When the overlap region is near the notch, plastic deformation spills onto it and the two models predict different behavior, affecting convergence adversely.
Overlap far from notch.
Overlap near notch.
Notched Cylinder: Coupling Different Materials
Need to be careful to do domain decomposition so that material models are consistent in overlap region.

## Slide 78: Single Domain Predictive ROM
0
100
100
0
Uniform sampling of by a grid ⇒ 9 training parameters characterized by
  POD modes required to capture % snapshot energy
Queried but unsampled parameter point
Reduced mesh resulting from solving non-negative least squares problem defining ECSW gives elements (9.1% of elements).
Figure above: Reduced mesh of single domain HROM
Figure above: HROM and FOM results at various time steps
% SV Energy |  | MSE* (%) | CPU time* (s)
95 | 69 | 1.1 | 138
99 | 177 | 0.17 | 447
% SV Energy |  | MSE* (%) | CPU time* (s)
95 | 69 | 1.1 | 138
99 | 177 | 0.17 | 447
* Numbers in table are w/o hyper-reduction
Notes: Table shows ROM CPU times (no hyper-reduction)

## Slide 79: All-ROM Coupling
0
100
100
0
99% Singular Value (SV) Energy Retention
95% Singular Value (SV) Energy Retention
1 SD
Subdomains | 95% SV Energy |  |  | 99% SV Energy |  | 
 |  | MSE (%) | CPU time (s) |  | MSE (%) | CPU time (s)
 | 57 | 1.1 | 85 | 146 | 0.18 | 295
 | 44 | 1.2 | 56 | 120 | 0.18 | 216
 | 24 | 1.4 | 43 | 60 | 0.16 | 89
 | 32 | 1.9 | 61 | 66 | 0.25 | 100
Total |  |  | 245 |  |  | 700
Subdomains | 95% SV Energy |  |  | 99% SV Energy |  | 
 |  | MSE (%) | CPU time (s) |  | MSE (%) | CPU time (s)
 | 57 | 1.1 | 85 | 146 | 0.18 | 295
 | 44 | 1.2 | 56 | 120 | 0.18 | 216
 | 24 | 1.4 | 43 | 60 | 0.16 | 89
 | 32 | 1.9 | 61 | 66 | 0.25 | 100
Total |  |  | 245 |  |  | 700
Method converges in only 3 Schwarz iterations per controller time-step
Errors O(1%) or less
1.47 speedup over all-FOM coupling for 95% SV energy retention case
Notes: Q for Joshua:
- What are dx and dt in each subdomain? Are they the same or diff?
What is going on with last frame in movie??
Solutions look discontinuous at certain times…
Subdomain 1: 75.38 s 0.94 s
Subdomain 2: 61.52 s 0.91 s
Subdomain 3: 61.54 s 0.91 s
Subdomain 4: 77.02 s 0.93 s

## Slide 80: Schwarz Boundary Sampling for All-HROM Coupling
80
Key question: how many Schwarz boundary points need to be included in sample mesh when performing HROM coupling?

## Slide 81: Schwarz Boundary Sampling for All-HROM Coupling
81
Naïve/sparsely-sampled Schwarz boundary results in failure to transmit coupling information during Schwarz
Movie above: FOM (left) and all HROM with % (right). ROMs have modes and sample mesh points.
Figure above: example sample mesh with sampling rate
Key question: how many Schwarz boundary points need to be included in sample mesh when performing HROM coupling?
Notes: To clarify the sampling rate Nb, the value of Nb = 0 just means that there is no deliberate sampling at the interface; there is still roughly N * X% points sampled at the interface given a random sampling scheme. Nb is a fixed rate of sampling at the interface, regardless of the overall sampling rate. Nb = 10 means every tenth cell at the interface is sampled, or 10% of all interface cells (Nb = 5 is 20% of all interface cells, etc). The use of an integer for Nb was just stylistic, since N and Ns are also integers.
hris.

## Slide 82: Schwarz Boundary Sampling for All-HROM Coupling
82
Naïve/sparsely-sampled Schwarz boundary results in failure to transmit coupling information during Schwarz
Including too many Schwarz boundary points () in sample mesh given fixed budget of sample mesh points may lead to too few sample mesh points in interior
Movie above: FOM (left) and all HROM with % (right). ROMs have modes and sample mesh points.
Figure above: example sample mesh with sampling rate
Key question: how many Schwarz boundary points need to be included in sample mesh when performing HROM coupling?

## Slide 83: Schwarz Boundary Sampling for All-HROM Coupling
83
Naïve/sparsely-sampled Schwarz boundary results in failure to transmit coupling information during Schwarz
Including too many Schwarz boundary points () in sample mesh given fixed budget of sample mesh points may lead to too few sample mesh points in interior
Movie above: FOM (left) and all HROM with (right). ROMs have modes and sample mesh points.
Figure above: example sample mesh with sampling rate
Key question: how many Schwarz boundary points need to be included in sample mesh when performing HROM coupling?

## Slide 84: Schwarz Boundary Sampling for All-HROM Coupling
84
Naïve/sparsely-sampled Schwarz boundary results in failure to transmit coupling information during Schwarz
Including too many Schwarz boundary points () in sample mesh given fixed budget of sample mesh points may lead to too few sample mesh points in interior
Movie above: FOM (left) and all HROM with (right). ROMs have modes and sample mesh points.
Figure above: example sample mesh with sampling rate
Key question: how many Schwarz boundary points need to be included in sample mesh when performing HROM coupling?

## Slide 85: Schwarz Boundary Sampling for All-HROM Coupling
85
Naïve/sparsely-sampled Schwarz boundary results in failure to transmit coupling information during Schwarz
Including too many Schwarz boundary points () in sample mesh given fixed budget of sample mesh points may lead to too few sample mesh points in interior
Movie above: FOM (left) and all HROM with % (right). ROMs have modes and sample mesh points.
Figure above: example sample mesh with sampling rate
Key question: how many Schwarz boundary points need to be included in sample mesh when performing HROM coupling?

## Slide 86: Model Problem 3: 2D Euler Equations Riemann Problem
FOM discretization:
Spatial discretization given by a first-order cell-centered finite volume discretization with orelements in each dimension
Implicit first order temporal discretization: backward Euler with fixed
Implemented in Pressio-demoapps (https://github.com/Pressio/pressio-demoapps)
Problem setup:
, homogeneous Neumann BCs
Fix , ,
Vary ; IC from compatibility conditions*
  Training:
  Testing:
Figure above: FOM solutions to Euler Riemann problem for (left) and (right).
+
*Schulz-Rinne, 1993.
Preliminary results (WIP)
Notes: TODO: ask Chris re: spatial discretization.

## Slide 87: Schwarz Coupling Details
87
Choice of domain decomposition
Overlapping and non-overlapping DD of into 4 subdomains coupled via additive/multiplicative Schwarz
All-ROM or All-HROM coupling via Pressio*
Snapshot collection and reduced basis construction
Single-domain FOM on used to generate snapshots/POD modes
Enforcement of boundary conditions (BCs) in ROM at Schwarz boundaries
BCs are imposed approximately by fictitious ghost cell states
Dirichlet-Dirichlet BCs for both overlapping and non-overlapping
Choice of hyper-reduction
Collocation and gappy POD for hyper-reduction
Assume fixed budget of sample mesh points at Schwarz boundaries
Figure above: DD of into 4 subdomains
*https://github.com/Pressio/pressio-demoapps
Figure above: Slow decay of POD energy for Euler problem
Notes: TODO: ask Chris what hyper-reduction is used now.

## Slide 88: Model Problem 3: All-ROM Coupling + Overlapping Schwarz
For smaller basis sizes and larger , monolithic ROM is unstable whereas Schwarz ROM gives accurate solution!
Increased overlap degrades accuracy (top right)
Shock transmission error significantly increases with overlap
4.4 average # Schwarz iterations with additive Schwarz vs. 3.6 for multiplicative Schwarz
With additive Schwarz, can achieve lower error than monolithic ROM for same CPU time (bottom right)
Movie above: FOM (left), monolithic ROM (middle), and overlapping Schwarz ROM with (left) for
Notes: TODO: split into 2 slides – All-ROM and All-HROM.

## Slide 89: Model Problem 3: All-HROM Coupling + Non-Overlapping Schwarz
Hyper-reduction via collocation works better than gappy POD
Schwarz can give improved accuracy relative to monolithic ROM
Achieving cost-savings w.r.t. monolithic FOM is WIP
Movie above: FOM (left), HROM (middle) and Schwarz All-HROM (right) solution. HROMs have 5% sampling rate and 200 POD modes.
Figure above: monolithic vs. decomposed HROM errors with 5% sampling rate no overlap.
Preliminary results (WIP)
Figure above: collocation and gappy POD relative errors for K=200, 1% sampling rate.
Notes: TODO: split into 2 slides – All-ROM and All-HROM.

## Slide 90: Energy-Conserving Sampling and Weighting (ECSW)
Project-then-approximate paradigm (as opposed to approximate-then-project)
where is the number of degrees of freedom associated with each mesh element (this is in the context of meshes used in first-order hyperbolic problems where there are mesh elements)
selects degrees of freedom necessary for flux reconstruction
Equality can be relaxed

## Slide 91: ECSW: Generating the Reduced Mesh and Weights
Using a subset of the same snapshots used to generate the state basis , we can train the reduced mesh
Snapshots are first projected onto their associated basis and then reconstructed
We can then form the system
Where , must be the solution
Further relax the equality to yield non-negative least-squares problem:
subject to
Solve the above optimization problem using a non-negative least squares solver with an early termination condition to promote sparsity of the vector