## Slide 1: Domain decomposition-based coupling of subdomain-local reduced order models (ROMs) in fluid mechanics using the Schwarz alternating method
Computational Fluids Conference (CFC) 2025
Santiago, Chile. March 17-20, 2025
SAND2025-02170C
Chris Wentland1, Francesco Rizzi2, Joshua Barnett3, Irina Tezaur1, Alejandro Mota1
1Sandia National Laboratories, 2NexGen Analytics, 3Cadence Design Systems

## Slide 2: Motivation: Multi-scale & Multi-physics Coupling
Monolithic (Lagrange multipliers)
Partitioned (loose) coupling
Iterative (Schwarz, optimization)
M1
M2
M3
M4
N3
N4
N1
N2
N5
N3
N4
N5
N2
N1
Mesh-based (FE, FV, FD)
Meshless (SPH, MLS)
Implicit, explicit
Eulerian, Lagrangian…
Complex System Model
Traditional Methods
Coupled Numerical Model
Ocean
(MPAS-O)
Atmos.
(EAM)
Sea Ice
(MPAS-SI)
Land Ice
(MALI)
Land
(ELM)
PDEs, ODEs
Nonlocal integral
Classical DFT
Atomistic, …
There exist established rigorous mathematical theories for coupling multi-scale and multi-physics components based on traditional discretization methods (“Full Order Models” or FOMs).

Notes: The past decades have seen a tremendous amount of investment in the development of simulation frameworks for coupled multi-scale and multi-physics problems. These frameworks rely on established mathematical theories to couple physics components discretized using so-called traditional discretization methods such as finite elements, finite volumes and finite differences. A prime example is the DOE’s global climate model, the Energy Exascale Earth System Model (E3SM), which couples 5 physics components (atmosphere, ocean, sea ice, land ice and land). Each component is developed separately according to the relevant physics, dynamics and numerical methods, and the components are coupled in a way that ensures stability, accuracy and conservation.

## Slide 3: Motivation: Multi-scale & Multi-physics Coupling
Monolithic (Lagrange multipliers)
Partitioned (loose) coupling
Iterative (Schwarz, optimization)
M1
M2
M3
M4
N3
N4
N1
N2
N5
N3
N4
N5
N2
N1
PDEs, ODEs
Nonlocal integral
Classical DFT
Atomistic, …
Mesh-based (FE, FV, FD)
Meshless (SPH, MLS)
Implicit, explicit
Eulerian, Lagrangian, …
Complex System Model
Traditional Methods
Coupled Numerical Model
Ocean
(MPAS-O)
Atmos.
(EAM)
Sea Ice
(MPAS-SI)
Land Ice
(MALI)
Land
(ELM)
DMD=N3
ROM=N4
N1
PINN=N2
UDE=N5
Traditional + Data-Driven Methods
PINNs
Neural ODEs
Projection-based ROMs, …
There exist established rigorous mathematical theories for coupling multi-scale and multi-physics components based on traditional discretization methods (“Full Order Models” or FOMs).


Unfortunately, existing algorithmic and software infrastructures are ill-equipped to handle plug-and-play integration of non-traditional, data-driven models!

## Slide 4
Alternating Schwarz-based coupling
Optimization-based coupling
Coupling via generalized mortar methods
Principal research objective:
Discover mathematical principles guiding the assembly of standard and data-driven numerical models in stable, accurate and physically consistent ways.
Principal research goals:
“Mix-and-match” standard and data-driven models from three-classes
  Class A: projection-based reduced order models (ROMs)
  Class B: machine-learned models, i.e., Physics-Informed Neural Networks (PINNs)
  Class C: flow map approximation models, i.e., dynamic model decomposition (DMD) models
Ensure well-posedness & physical consistency of resulting heterogeneous models.
Solve such heterogeneous models efficiently.
Three coupling methods:
Flexible Heterogeneous Numerical Methods (fHNM) and Multi-faceted Mathematics for Predictive Digital Twins (M2dt) Projects
This talk.
This talk.
Notes: Class A and B are equation-based DDMs: they seek restrict a weak or strong form of the PDE to a finite-dimensional function space 𝑈_𝑖, spanned by a basis {𝑏_𝑖^𝑘 }_(𝑘=1)^(𝑁_𝑖 )
Class C DDMs are equation-free I/O relations 𝑢_𝑖 (𝑡)=〖𝐺_𝑖 (𝑓〗_𝑖,𝑢_(𝑖,0);𝑝_(𝑖,1),⋯,𝑝_(𝑖,𝑃)) with inputs (“ports”) 𝑝_(𝑖,𝑗).
TODO: add refs to other talks in MS.

## Slide 5: Outline
The Schwarz Alternating Method for Domain Decomposition-Based Coupling
Extension to FOM*-ROM# and ROM-ROM Coupling
Numerical Examples
  2D Shallow Water Equations (SWE)
  2D Burgers’ Equations
  2D Euler Equations
Ongoing/Future Work & Summary
*Full-Order Model. #Reduced Order Model.
Notes: Class A and B are equation-based DDMs: they seek restrict a weak or strong form of the PDE to a finite-dimensional function space 𝑈_𝑖, spanned by a basis {𝑏_𝑖^𝑘 }_(𝑘=1)^(𝑁_𝑖 )
Class C DDMs are equation-free I/O relations 𝑢_𝑖 (𝑡)=〖𝐺_𝑖 (𝑓〗_𝑖,𝑢_(𝑖,0);𝑝_(𝑖,1),⋯,𝑝_(𝑖,𝑃)) with inputs (“ports”) 𝑝_(𝑖,𝑗).
TODO: add refs to other talks in MS.

## Slide 6: Outline
The Schwarz Alternating Method for Domain Decomposition-Based Coupling
Extension to FOM*-ROM# and ROM-ROM Coupling
Numerical Examples
  2D Shallow Water Equations (SWE)
  2D Burgers’ Equations
  2D Euler Equations
Ongoing/Future Work & Summary
*Full-Order Model. #Reduced Order Model.
Notes: Class A and B are equation-based DDMs: they seek restrict a weak or strong form of the PDE to a finite-dimensional function space 𝑈_𝑖, spanned by a basis {𝑏_𝑖^𝑘 }_(𝑘=1)^(𝑁_𝑖 )
Class C DDMs are equation-free I/O relations 𝑢_𝑖 (𝑡)=〖𝐺_𝑖 (𝑓〗_𝑖,𝑢_(𝑖,0);𝑝_(𝑖,1),⋯,𝑝_(𝑖,𝑃)) with inputs (“ports”) 𝑝_(𝑖,𝑗).
TODO: add refs to other talks in MS.

## Slide 7: Schwarz Alternating Method for Domain Decomposition
Proposed in 1870 by H. Schwarz for solving Laplace PDE on irregular domains.
H. Schwarz (1843–1921)
Initialize:
Solve PDE by any method on w/ initial guess for transmission BCs on .
Iterate until convergence:
Solve PDE by any method on w/ transmission BCs on based on values just obtained for .
Solve PDE by any method on w/ transmission BCs on based on values just obtained for .
Crux of Method: if the solution is known in regularly shaped domains, use those as pieces to iteratively build a solution for the more complex domain.
Basic Schwarz Algorithm
2Lions, 1990. 3Zanolli et al., 1987.
overlapping
non-overlapping
Schwarz alternating method most commonly used as a preconditioner for Krylov iterative methods to solve linear algebraic equations.
Idea behind this work: using the Schwarz alternating method as a discretization method for solving multi-scale or multi-physics partial differential equations (PDEs).

## Slide 8: How We Use the Schwarz Alternating Method
AS A PRECONDITIONER FOR THE LINEARIZED SYSTEM
AS A SOLVER FOR THE COUPLED
FULLY NONLINEAR PROBLEM
8

## Slide 9
Spatial Coupling via (Multiplicative) Alternating Schwarz
Overlapping Domain Decomposition
Non-overlapping Domain Decomposition
Relevant for multi-material and multi-physics coupling
Alternating Dirichlet-Neumann transmission BCs [Zanolli et al. 1987]
Robin-Robin transmission BCs also lead to convergence [Lions 1990]
relaxation parameter (can help convergence)
Dirichlet-Dirichlet transmission BCs [Schwarz 1870; Lions 1988; Mota et al. 2017; Mota et al. 2022]
Model PDE:
  This talk: non-overlapping DD + Dirichlet-Dirichlet transmission BCs + cell-centered finite volume [Wentland et al., 2025]

## Slide 10: Additional Parallelism via Additive Schwarz
Multiplicative Overlapping Schwarz
Additive Overlapping Schwarz
Multiplicative Schwarz: solves subdomain problems sequentially (in serial)
Additive Schwarz: advance subdomains in parallel, communicate boundary condition data later
  Typically requires a few more Schwarz iterations, but does not degrade accuracy
  Parallelism helps balance additional cost due to Schwarz iterations
  Applicable to both overlapping and non-overlapping Schwarz
Model PDE:
This talk.

## Slide 11: Schwarz for Multiscale FOM-FOM Coupling in Solid Mechanics
“Plug-and-play” framework:
  Ability to couple regions with different non-conformal meshes, different element types and different levels of refinement to simplify task of meshing complex geometries.
  Ability to use different solvers/time-integrators in different regions.
Coupling is concurrent (two-way).
Ease of implementation into existing massively-parallel HPC codes.
Scalable, fast, robust (we target real engineering problems, e.g., analyses involving failure of bolted components!).
Coupling does not introduce nonphysical artifacts.
Theoretical convergence properties/guarantees.
Model Solid Mechanics PDEs:
Quasistatic:
Dynamic:
1 Mota et al. 2017; Mota et al. 2022. 2 https://github.com/sandialabs/LCM.
2

## Slide 12: Outline
The Schwarz Alternating Method for Domain Decomposition-Based Coupling
Extension to FOM*-ROM# and ROM-ROM Coupling
Numerical Examples
  2D Shallow Water Equations (SWE)
  2D Burgers’ Equations
  2D Euler Equations
Ongoing/Future Work & Summary
*Full-Order Model. #Reduced Order Model.
Notes: Class A and B are equation-based DDMs: they seek restrict a weak or strong form of the PDE to a finite-dimensional function space 𝑈_𝑖, spanned by a basis {𝑏_𝑖^𝑘 }_(𝑘=1)^(𝑁_𝑖 )
Class C DDMs are equation-free I/O relations 𝑢_𝑖 (𝑡)=〖𝐺_𝑖 (𝑓〗_𝑖,𝑢_(𝑖,0);𝑝_(𝑖,1),⋯,𝑝_(𝑖,𝑃)) with inputs (“ports”) 𝑝_(𝑖,𝑗).
TODO: add refs to other talks in MS.

## Slide 13: Projection-Based Model Order Reduction via the POD/LSPG* Method
13
Full Order Model (FOM):
Proper Orthogonal Decomposition (POD):
Solve ODE at different design points
1. Acquisition
2. Learning
3. Projection-Based Reduction
Number of time steps
Number of State Variables
Save solution data
ROM = projection-based Reduced Order Model HROM = Hyper-reduced ROM
Choose ODE temporal discretization
Reduce the number of unknowns
Minimize residual
Hyper-reduction/sample mesh
* Least-Squares Petrov-Galerkin

## Slide 14: Schwarz Extensions to FOM-ROM and ROM-ROM Couplings
14
Perform FOM simulation on a spatial domain and collect snapshots
Create domain decomposition of into overlapping or non-overlapping subdomains with overlap cells (could be 0).
Compute POD basis on each by restricting the snapshots to
For nonlinear problems, compute sample mesh on each .
  Collocation: minimize the residual at a small subset of DOFs
  Key question: how to sample Schwarz boundaries given fixed budget of sample mesh points?
Construct POD/LSPG ROM in each subdomain , transmit Schwarz BCs, apply Schwarz iteration procedure.
  Key question: how to impose Schwarz BCs in ROMs?
    BCs imposed approximately by fictitious ghost cells, as FOMs are based on cell-centered finite volume (CCFV) discretizations
  To maximize efficiency, we employ additive Schwarz with OpenMP parallelism (1 thread/subdomain)
Ghost cells
Yellow: residual cells, white: stencil cells

## Slide 15: Outline
The Schwarz Alternating Method for Domain Decomposition-Based Coupling
Extension to FOM*-ROM# and ROM-ROM Coupling
Numerical Examples
  2D Shallow Water Equations (SWE)
  2D Burgers’ Equations
  2D Euler Equations
Ongoing/Future Work & Summary
*Full-Order Model. #Reduced Order Model.
Notes: Class A and B are equation-based DDMs: they seek restrict a weak or strong form of the PDE to a finite-dimensional function space 𝑈_𝑖, spanned by a basis {𝑏_𝑖^𝑘 }_(𝑘=1)^(𝑁_𝑖 )
Class C DDMs are equation-free I/O relations 𝑢_𝑖 (𝑡)=〖𝐺_𝑖 (𝑓〗_𝑖,𝑢_(𝑖,0);𝑝_(𝑖,1),⋯,𝑝_(𝑖,𝑃)) with inputs (“ports”) 𝑝_(𝑖,𝑗).
TODO: add refs to other talks in MS.

## Slide 16: 3 Parametrized Hyperbolic Conservation Law Test Cases
Nonlinear hyperbolic fluid systems in Pressio/Pressio demo-apps*
  2D shallow water equations (SWE), vary Coriolis parameter ()
  2D viscous Burgers’ equations, vary diffusion parameter ()
  2D Euler equations, vary upper right pressure () in IC
Wave/shock propagation across interfaces high Kolmogorov -width
FOM discretization: first-order CCFV method, 300x300 mesh, BDF1
Consider decompositions of into four subdomains
SWE
Burgers’
Euler
* https://pressio.github.io, https://github.com/Pressio/pressio-schwarz
All results predictive: 5 training points, 4 (interpolative) testing points
SWE
Burgers’
Euler

## Slide 17: Unsampled ROMs: Impact of Subdomain Overlap
Key result: non-overlapping Schwarz iteration converges without a degradation in accuracy when using Dirichlet-Dirichlet Schwarz BCs!
This result is not true in general [Barnett et al., 2022; Mota et al., 2017; Mota et al. 2022]!
  Generally need alternating Dirichlet-Neumann or Robin-Robin BCs for non-overlapping Schwarz convergence.
  Dirichlet-Dirichlet works here due to implied overlap introduced into otherwise non-overlapping DD by ghost cells.
More Schwarz iterations are required for convergence with no overlap (as expected)
Non-overlapping incurs negligible convergence penalty for smooth problems (SWE)
Non-overlapping Schwarz avoids duplicate calculations in overlap region
2
It becomes more difficult to transmit shock across non-overlapping interface (Burgers, Euler)
SWE,
Burgers’,
Euler,
Red parameter values are predictive.
Ghost cells

## Slide 18: Unsampled ROMs: Stabilization Effects
Key result: domain decomposition + Schwarz coupling can stabilize an otherwise unstable monolithic solution
Blow up!
Movie above: monolithic vs. decomposed ROM for Euler problem with (predictive regime).

## Slide 19: Hyper-reduced ROMs: Impact of Boundary Sampling
Key result: given a fixed “budget” of sample mesh points, there is a (problem-dependent) optimal number of sample mesh points to allocate to the Schwarz boundaries vs. the subdomain interiors.
fixed interval at which Schwarz boundaries are sampled
For a fixed budget of sample mesh points , boundary points draw points away from interior (figure left)
Failure to deliberately sample the Schwarz boundary will also always lead to instabilities (movie left)
0

## Slide 20: Hyper-reduced ROMs: Accuracy
Monolithic FOM
Monolithic FOM
Monolithic FOM
Monolithic HROM
Monolithic HROM
Monolithic HROM
Schwarz HROM
Schwarz HROM
Schwarz HROM
Key result: predictive hyper-reduced ROMs (HROMs) with non-overlapping Dirichlet-Dirichlet Schwarz coupling are indistinguishable from corresponding monolithic ROMs/FOMs.
Top row: SWE
Middle row: Burgers’
Bottom row: Euler

## Slide 21: Hyper-reduced ROMs: Accuracy
Key result: Decomposed ROMs achieve lower error for the same trial basis size
and have no artifacts at Schwarz boundaries.
Left figure: average absolute spatial error fields for representative monolithic (top) and decomposed (bottom) hyper-reduced ROM with no overlap. Subdomain interfaces are marked with dashed lines.

## Slide 22: Hyper-reduced ROMs: Computational Cost
Key result: additive Schwarz enables speed-ups over corresponding coupled Schwarz FOM and sometimes over monolithic FOM.
Hyper-reduced ROMs generally achieve cost savings w.r.t. corresponding coupled Schwarz FOM
Cost savings using Schwarz ROMs over corresponding monolithic FOM are possible for SWE problem
  Coupled Schwarz FOMs are often only viable options for Sandia analysts due to meshing challenges
  Next step: try to improve this via adaptive Schwarz ROMs
Red parameter values are predictive.
SWE
Burgers’
Euler

## Slide 23: Outline
The Schwarz Alternating Method for Domain Decomposition-Based Coupling
Extension to FOM*-ROM# and ROM-ROM Coupling
Numerical Examples
  2D Shallow Water Equations (SWE)
  2D Burgers’ Equations
  2D Euler Equations
Ongoing/Future Work & Summary
*Full-Order Model. #Reduced Order Model.
Notes: Class A and B are equation-based DDMs: they seek restrict a weak or strong form of the PDE to a finite-dimensional function space 𝑈_𝑖, spanned by a basis {𝑏_𝑖^𝑘 }_(𝑘=1)^(𝑁_𝑖 )
Class C DDMs are equation-free I/O relations 𝑢_𝑖 (𝑡)=〖𝐺_𝑖 (𝑓〗_𝑖,𝑢_(𝑖,0);𝑝_(𝑖,1),⋯,𝑝_(𝑖,𝑃)) with inputs (“ports”) 𝑝_(𝑖,𝑗).
TODO: add refs to other talks in MS.

## Slide 24: New Project: Adaptive Hybrid modEls via domAin Decomposition (AHEAD)
Goals (for solid mechanics exemplars):
Simplify meshing via Schwarz + DD
Extend Schwarz to non-intrusive ROMs (Operator Inference, NN)
Development of automated criteria to determine appropriate use of less refined or reduced-order models without sacrificing accuracy, enabling real-time transitions between different model fidelities
Example sample DD and ROM/HFM assignment.
On-the-fly model switching in our DD workflow.

## Slide 25: New Project: Adaptive Hybrid modEls via domAin Decomposition (AHEAD)
Example sample DD and ROM/HFM assignment.
On-the-fly model switching in our DD workflow.
Goals (for solid mechanics exemplars):
Simplify meshing via Schwarz + DD
Extend Schwarz to non-intrusive ROMs (Operator Inference, NN)
Development of automated criteria to determine appropriate use of less refined or reduced-order models without sacrificing accuracy, enabling real-time transitions between different model fidelities

## Slide 26: New Project: Adaptive Hybrid modEls via domAin Decomposition (AHEAD)
Example sample DD and ROM/FOM assignment.
On-the-fly model switching in our DD workflow.
Goals (for solid mechanics exemplars):
Simplify meshing via Schwarz + DD
Extend Schwarz to non-intrusive ROMs (Operator Inference, NN)
Development of automated criteria to determine appropriate use of less refined or reduced-order models without sacrificing accuracy, enabling real-time transitions between different model fidelities

## Slide 27: Summary and Ongoing/Future Work
27
Summary:
Schwarz has been demonstrated for coupling of FOMs and (H)ROMs
Computational gains can be achieved by coupling HROMs and using the additive Schwarz variant
Interesting new results regarding interface sampling & non-overlapping transmission BCs for CCFV
Ongoing & future work:
Extension to other applications (fasteners, laser welds)
Rigorous analysis of why Dirichlet-Dirichlet BC “work” when employing non-overlapping Schwarz with discretizations that employ ghost cells
* https://pressio.github.io
Learning of “optimal” transmission conditions to ensure structure preservation
Extension of Schwarz to enabling coupling of non-intrusive ROMs (e.g., OpInf, Neural Networks)
Development of automated criteria to determine appropriate use of less refined or reduced-order models without sacrificing accuracy, enabling real-time transitions between different model fidelities
New project: AHEAD LDRD

## Slide 28: Team & Acknowledgments
28
Irina Tezaur
Joshua Barnett
Chris Wentland
Francesco Rizzi
Will Snyder
Former Intern from Virginia Tech [Schwarz + PINNs]
Ian Moore
Intern from Virginia Tech
[Schwarz + OpInf]
Alejandro Mota
Eric Parish
Anthony Gruber
AHEAD/M2dt
Notes: TODO: add Ian.

## Slide 29: References & Codes
[1] A. Mota, I. Tezaur, C. Alleman. “The Schwarz Alternating Method in Solid Mechanics", Comput. Meth. Appl. Mech. Engng. 319 (2017), 19-51.
[2] A. Mota, I. Tezaur, G. Phlipot. “The Schwarz Alternating Method for Dynamic Solid Mechanics”, Comput. Meth. Appl. Mech. Engng. 121 (21) (2022) 5036-5071.
[3] J. Barnett, I. Tezaur, A. Mota. “The Schwarz alternating method for the seamless coupling of nonlinear reduced order models and full order models”, ArXiv pre-print, 2022. https://arxiv.org/abs/2210.12551
[4] W. Snyder, I. Tezaur, C. Wentland. “Domain decomposition-based coupling of physics-informed neural networks via the Schwarz alternating method”, ArXiv pre-print, 2023. https://arxiv.org/abs/2311.00224
[5] A. Mota, D. Koliesnikova, I. Tezaur. “A Fundamentally New Coupled Approach to Contact Mechanics via the Dirichlet-Neumann Schwarz Alternating Method”, ArXiv pre-print, 2023. https://arxiv.org/abs/2311.05643
[6] C. Wentland, F. Rizzi, J. Barnett, I. Tezaur. “The role of interface boundary conditions and sampling strategies for Schwarz-based coupling of projection-based reduced order models, J. Comp. Appl. Math, 2025 (in press). https://doi.org/10.1016/j.cam.2025.116584
[7] Pressio: https://pressio.github.io
[8] Pressio demo-apps: https://github.com/Pressio/pressio-demoapps
[9] Pressio demo-apps + Schwarz: https://github.com/Pressio/pressio-schwarz
[10] Norma: https://sandialabs/Norma.jl
ikalash@sandia.gov
www.sandia.gov/~ikalash
This talk!

## Slide 30: Start of Backup Slides

## Slide 31: Time-Advancement Within the Schwarz Framework
Step 0: Initialize
Controller time stepper
Time integrator for W1
Time integrator for W2
Model PDE:
Notes: TODO? Change equations?

## Slide 32: Time-Advancement Within the Schwarz Framework
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Integrate using
Controller time stepper
Time integrator for W1
Time integrator for W2
Model PDE:

## Slide 33: Time-Advancement Within the Schwarz Framework
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Step 2: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times .
Integrate using
Interpolate from to
Controller time stepper
Time integrator for W1
Time integrator for W2
Model PDE:

## Slide 34: Time-Advancement Within the Schwarz Framework
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Step 2: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times .
Step 3: Check for convergence at time .
Controller time stepper
Time integrator for W1
Time integrator for W2
Model PDE:

## Slide 35: Time-Advancement Within the Schwarz Framework
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Step 2: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times .
Step 3: Check for convergence at time .
If unconverged, return to Step 1.
Interpolate from to
Integrate using
Controller time stepper
Time integrator for W1
Time integrator for W2
Model PDE:

## Slide 36: Time-Advancement Within the Schwarz Framework
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Step 2: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times .
Step 3: Check for convergence at time .
If unconverged, return to Step 1.
If converged, set and return to Step 1.
Integrate using
Interpolate from to
Can use different integrators with different time steps within each domain!
Controller time stepper
Time integrator for W1
Time integrator for W2
Model PDE:

## Slide 37: Time-Advancement Within the Schwarz Framework
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Step 2: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times .
Step 3: Check for convergence at time .
If unconverged, return to Step 1.
If converged, set and return to Step 1.
Integrate using
Interpolate from to
Controller time stepper
Time integrator for W1
Time integrator for W2
Model PDE:
Time-stepping procedure is equivalent to doing Schwarz on space-time domain [Mota et al. 2022].

## Slide 38: Schwarz for Multiscale FOM-FOM Coupling in Solid Mechanics
1 Mota et al. 2017; Mota et al. 2022.
Figure above: tension specimen simulation coupling composite TET10 elements with HEX elements in Sierra/SM.
Figures right: bolted joint simulation coupling composite TET10 elements with HEX elements in Sierra/SM.
Single
Schwarz
Schwarz
Single
y-displacement
EQPS

## Slide 39: 2D Inviscid Burgers Equation
Figure above: solution of component at various times
FOM discretization:
Spatial discretization given by a Godunov-type scheme with elements in each dimension
Implicit trapezoidal method with fixed
0
100
100
0
Problem setup:
Two parameters . Training: uniform sampling of by a grid. Testing: query unsampled point
Popular analog for fluid problems where shocks are possible, and particularly difficult for conventional projection-based ROMs
Notes: TODO: say something about how BCs implemented?

## Slide 40: Schwarz Coupling Details
40
Choice of domain decomposition
Overlapping DD of into 4 subdomains coupled via multiplicative Schwarz
Solution in is most difficult to capture by ROM
Snapshot collection and reduced basis construction
Single-domain FOM on used to generate snapshots/POD modes
Enforcement of boundary conditions (BCs) in ROM at Schwarz boundaries
BCs imposed strongly via Method 1 of [Gunzburger et al., 2007] at indices
  POD modes made to satisfy homogeneous DBCs:
  BCs imposed by modifying :
Choice of hyper-reduction
Energy Conserving Sampling & Weighting (ECSW) method for hyper-reduction
All points on Schwarz boundaries are included in the sample mesh
0
100
100
0
Figure above: ECSW augmented reduced mesh
Figure above: 4 subdomain overlapping DD
Notes: TODO: say how possible to do strong BC impl in FV method.
TODO: double check about all points on Schwarz boundaries being included in sample mesh with Joshua/Chris.

## Slide 41: All-ROM Coupling
0
100
100
0
99% Singular Value (SV) Energy Retention
95% Singular Value (SV) Energy Retention
1 SD
Subdomains | 95% SV Energy |  |  | 99% SV Energy |  | 
 |  | MSE (%) | CPU time (s) |  | MSE (%) | CPU time (s)
 | 57 | 1.1 | 85 | 146 | 0.18 | 295
 | 44 | 1.2 | 56 | 120 | 0.18 | 216
 | 24 | 1.4 | 43 | 60 | 0.16 | 89
 | 32 | 1.9 | 61 | 66 | 0.25 | 100
Total |  |  | 245 |  |  | 700
Subdomains | 95% SV Energy |  |  | 99% SV Energy |  | 
 |  | MSE (%) | CPU time (s) |  | MSE (%) | CPU time (s)
 | 57 | 1.1 | 85 | 146 | 0.18 | 295
 | 44 | 1.2 | 56 | 120 | 0.18 | 216
 | 24 | 1.4 | 43 | 60 | 0.16 | 89
 | 32 | 1.9 | 61 | 66 | 0.25 | 100
Total |  |  | 245 |  |  | 700
Method converges in only 3 Schwarz iterations per controller time-step
Errors O(1%) or less
1.47 speedup over all-FOM coupling for 95% SV energy retention case
Notes: Q for Joshua:
- What are dx and dt in each subdomain? Are they the same or diff?
What is going on with last frame in movie??
Solutions look discontinuous at certain times…
Subdomain 1: 75.38 s 0.94 s
Subdomain 2: 61.52 s 0.91 s
Subdomain 3: 61.54 s 0.91 s
Subdomain 4: 77.02 s 0.93 s

## Slide 42
0
100
100
0
FOM in as this is “hardest” subdomain for ROM
HROMs in , , capture 99% snapshot energy
Method converges in 3 Schwarz iterations per controller time-step
Errors O(0.1%) with 0 error in
2.26 speedup achieved over all-FOM coupling
1 SD
FOM-HROM-HROM-HROM Coupling
Subdomains | 99% SV Energy |  | 
 |  | MSE (%) | CPU time (s)
 |  | 0.0 | 95
 | 120 | 0.26 | 26
 | 60 | 0.43 | 17
 | 66 | 0.34 | 21
Total |  |  | 159
Subdomains | 99% SV Energy |  | 
 |  | MSE (%) | CPU time (s)
 |  | 0.0 | 95
 | 120 | 0.26 | 26
 | 60 | 0.43 | 17
 | 66 | 0.34 | 21
Total |  |  | 159
Further speedups possible via code optimizations, additive Schwarz and reduction of # sample mesh points.
Notes: 360: all-FOM case
Not possible for subdomain 2->4 to pollute 1 b/c of direction of propagation

## Slide 43: Outline
The Schwarz Alternating Method for Domain Decomposition-Based Coupling
Extension to FOM*-ROM# and ROM-ROM Coupling
Numerical Examples
  2D Burgers Equation
  2D Shallow Water Equations
  Teaser: 2D Euler Equations Riemann Problem
Summary & Future Work
*Full-Order Model. #Reduced Order Model.
Notes: Class A and B are equation-based DDMs: they seek restrict a weak or strong form of the PDE to a finite-dimensional function space 𝑈_𝑖, spanned by a basis {𝑏_𝑖^𝑘 }_(𝑘=1)^(𝑁_𝑖 )
Class C DDMs are equation-free I/O relations 𝑢_𝑖 (𝑡)=〖𝐺_𝑖 (𝑓〗_𝑖,𝑢_(𝑖,0);𝑝_(𝑖,1),⋯,𝑝_(𝑖,𝑃)) with inputs (“ports”) 𝑝_(𝑖,𝑗).
TODO: add refs to other talks in MS.

## Slide 44: 2D Shallow Water Equations (SWE)
FOM discretization:
Spatial discretization given by a first-order cell-centered finite volume discretization with elements in each dimension
Implicit first order temporal discretization: backward Euler with fixed
Implemented in Pressio-demoapps (https://github.com/Pressio/pressio-demoapps)
Problem setup:
, Gaussian initial condition
Coriolis parameter for training, and for testing
Hyperbolic PDEs modeling wave propagation below a pressure surface in a fluid (e.g., atmosphere, ocean).
Figure above: FOM solutions to SWE for (left) and (right).
Notes: TODO: ask Chris re: temporal discretization

## Slide 45: Schwarz Coupling Details
45
Choice of domain decomposition
Non-overlapping DD of into 4 subdomains coupled via additive Schwarz
  OpenMP parallelism with 1 thread/subdomain
All-ROM or All-HROM coupling via Pressio*
Snapshot collection and reduced basis construction
Single-domain FOM on used to generate snapshots/POD modes
Enforcement of boundary conditions (BCs) in ROM at Schwarz boundaries
BCs are imposed approximately by fictitious ghost cell states
  Implementing Neumann and Robin BCs is challenging
Ghost cells introduce some overlap even with non-overlapping DD
  Dirichlet-Dirichlet non-overlapping Schwarz is stable/convergent!
Choice of hyper-reduction
Collocation for hyper-reduction: min residual at small subset DOFs
Assume fixed budget of sample mesh points at Schwarz boundaries
Ghost cells
Figure right: non-overlapping DD w/ ghost cells creating overlap
Figure above: sample mesh (yellow) and stencil (white) cells
Green: different from Burgers’ problem
*https://github.com/Pressio/pressio-demoapps
Notes: TODO: ask Chris what hyper-reduction is used now.

## Slide 46: Schwarz All-ROM Domain Overlap Study
46
Study of Schwarz convergence for all-ROM coupling as a function of := cell width of overlap region (not including ghost cells).
Dirichlet-Dirichlet coupling with no-overlap performs well with no convergence issues (movie, left) and errors comparable to Dirichlet-Dirichlet coupling with overlap (figure below, left)
Movie above: FOM (left), 4 subdomain ROM coupled via non-overlapping Schwarz (middle), and 4 subdomain ROM coupled via overlapping Schwarz (right) for predictive SWE problem with . All ROMs have POD modes.
Schwarz iterations decrease (very roughly) with (figure, right) whereas evaluating scales with
  there is no reason not to do non-overlapping coupling for this problem
Figures above: relative error and average # Schwarz iterations as a function of and Black : training, red : testing.
Notes: Q: Is it true that 80 POD modes/subdomain? Had K = 80 in Chris’s slides.

## Slide 47: Schwarz Boundary Sampling for All-HROM Coupling
47
Including too many Schwarz boundary points () in sample mesh given fixed budget of sample mesh points may lead to too few sample mesh points in interior
For SWE problem, we can get away with 10% boundary sampling (movie above, right-most frame)
Naïve/sparsely-sampled Schwarz boundary results in failure to transmit coupling information during Schwarz
Movie above: FOM (left), all HROM with (middle) and all HROM with (left). ROMs have modes and sample mesh points.
Figure above: example sample mesh with sampling rate
Key question: how many Schwarz boundary points need to be included in sample mesh when performing HROM coupling?
Notes: To clarify the sampling rate Nb, the value of Nb = 0 just means that there is no deliberate sampling at the interface; there is still roughly N * X% points sampled at the interface given a random sampling scheme. Nb is a fixed rate of sampling at the interface, regardless of the overall sampling rate. Nb = 10 means every tenth cell at the interface is sampled, or 10% of all interface cells (Nb = 5 is 20% of all interface cells, etc). The use of an integer for Nb was just stylistic, since N and Ns are also integers.
hris.

## Slide 48: Coupled HROM Performance
48
For a fixed ROM dimension, Schwarz delivers lower error and comparable cost!
There are noticeable cost savings relative to monolithic FOM!
Accuracy similar for predictive (red) and non-predictive (black) cases.
Solid:
Dashed:
Notes: To clarify the sampling rate Nb, the value of Nb = 0 just means that there is no deliberate sampling at the interface; there is still roughly N * X% points sampled at the interface given a random sampling scheme. Nb is a fixed rate of sampling at the interface, regardless of the overall sampling rate. Nb = 10 means every tenth cell at the interface is sampled, or 10% of all interface cells (Nb = 5 is 20% of all interface cells, etc). The use of an integer for Nb was just stylistic, since N and Ns are also integers.
hris.

## Slide 49: Hyper-reduced ROMs: Impact of Boundary Sampling
Key result: given a fixed “budget” of sample mesh points, there is a (problem-dependent) optimal number of sample mesh points to allocate to the Schwarz boundaries vs. the subdomain interiors.
There is a delicate balance of ensuring BC transmission together with an accurate interior solutions
More extensive boundary sampling is required for problems with shocks (Burgers, Euler)
SWE,
Burgers’,
Euler,
Red parameter values are predictive.

## Slide 50: Teaser: 2D Euler Equations Riemann Problem
FOM discretization:
Spatial discretization given by a first-order cell-centered finite volume discretization with or elements in each dimension
Implicit first order temporal discretization: backward Euler with fixed
Implemented in Pressio-demoapps (https://github.com/Pressio/pressio-demoapps)
Problem setup:
, homogeneous Neumann BCs
Fix , ,
Vary ; IC from compatibility conditions*
  Training:
  Testing:
+
*Schulz-Rinne, 1993.
Preliminary results:
Schwarz can stabilize unstable monolithic ROM for fixed dimension (above)
Since shock traverses all parts of domain, achieving speedups with Schwarz is more difficult
Notes: TODO: ask Chris re: spatial discretization.

## Slide 51
Summary
The Schwarz alternating method has been developed for concurrent multi-scale coupling of conventional and data-driven models.
Coupling is concurrent (two-way).
Ease of implementation into existing massively-parallel HPC codes.
“Plug-and-play” framework: simplifies task of meshing complex geometries!
  Ability to couple regions with different non-conformal meshes, different element types and different levels of refinement.
  Ability to use different solvers (including ROM/FOM) and time-integrators in different regions.
Scalable, fast, robust on real engineering problems
Coupling does not introduce nonphysical artifacts.
Theoretical convergence properties/guarantees.









## Slide 52: Bonus: PINN-PINN and PINN-FOM coupling
52
PDE loss
BC loss
Data loss
Loss )
Input
Hidden Layers
Output
Loss
Minimize
Neural Network
Goal: investigate the use of the Schwarz alternating method as a means to couple Physics-Informed Neural Networks (PINNs)
Scenario 1: use Schwarz to train subdomain PINNs (offline)
Scenario 2: use Schwarz to couple pre-trained subdomain PINNs/NNs (online)
Will Snyder
Summer Intern
Virginia Tech
Focus thus far
Related work: Li et al., 2019, Li et al., 2020, Wang et al., 2022.

## Slide 53: Bonus: PINN-PINN coupling
53
1D steady advection-diffusion equation on
PINNs are notoriously difficult to train for higher Peclet numbers!
Can Schwarz help?
Schwarz PINN training algorithm:
Loop over subdomains until convergence of Schwarz method
  Train PINN in with loss
  Communicate Dirichlet data between neighboring subdomains
  Update boundary data on from neighboring subdomains
  If strong enforcement of Dirichlet BC (SDBC), set
  If weak enforcement of Dirichlet BC (WDBC), set where is chosen s.t. and is chosen s.t.
Overlapping DD: with boundary

## Slide 54: Bonus: PINN-PINN coupling
How Dirichlet boundary conditions are handled has a large impact on PINN convergence
Convergence not improved in general with increasing overlap
Increasing # subdomains in general will increase CPU time
WDBC
SDBC on
SDBC on
Notes: Class A and B are equation-based DDMs: they seek restrict a weak or strong form of the PDE to a finite-dimensional function space 𝑈_𝑖, spanned by a basis {𝑏_𝑖^𝑘 }_(𝑘=1)^(𝑁_𝑖 )
Class C DDMs are equation-free I/O relations 𝑢_𝑖 (𝑡)=〖𝐺_𝑖 (𝑓〗_𝑖,𝑢_(𝑖,0);𝑝_(𝑖,1),⋯,𝑝_(𝑖,𝑃)) with inputs (“ports”) 𝑝_(𝑖,𝑗).
TODO: add refs to other talks in MS.

## Slide 55: Bonus: PINN-PINN coupling
Using SDBCs and data loss helps with PINN/NN convergence and accuracy
Notes: Class A and B are equation-based DDMs: they seek restrict a weak or strong form of the PDE to a finite-dimensional function space 𝑈_𝑖, spanned by a basis {𝑏_𝑖^𝑘 }_(𝑘=1)^(𝑁_𝑖 )
Class C DDMs are equation-free I/O relations 𝑢_𝑖 (𝑡)=〖𝐺_𝑖 (𝑓〗_𝑖,𝑢_(𝑖,0);𝑝_(𝑖,1),⋯,𝑝_(𝑖,𝑃)) with inputs (“ports”) 𝑝_(𝑖,𝑗).
TODO: add refs to other talks in MS.

## Slide 56: Bonus: PINN-FOM coupling
PINN-FOM coupling gives rapid PINN convergence for arbitrarily high Peclet numbers
PINN-FOM couplings works with both WDBC and SDBC configurations
PINN subdomain
FOM subdomain
Notes: PINN-FOM coupling works for both the WDBC and SDBC configurations.
Class A and B are equation-based DDMs: they seek restrict a weak or strong form of the PDE to a finite-dimensional function space 𝑈_𝑖, spanned by a basis {𝑏_𝑖^𝑘 }_(𝑘=1)^(𝑁_𝑖 )
Class C DDMs are equation-free I/O relations 𝑢_𝑖 (𝑡)=〖𝐺_𝑖 (𝑓〗_𝑖,𝑢_(𝑖,0);𝑝_(𝑖,1),⋯,𝑝_(𝑖,𝑃)) with inputs (“ports”) 𝑝_(𝑖,𝑗).
TODO: add refs to other talks in MS.

## Slide 57
S.L. Sobolev (1936): posed Schwarz method for linear elasticity in variational form and proved method’s convergence by proposing a convergent sequence of energy functionals.
S.G. Mikhlin (1951): proved convergence of Schwarz method for general linear elliptic PDEs.
P.-L. Lions (1988): studied convergence of Schwarz for nonlinear monotone elliptic problems using max principle.
A. Mota, I. Tezaur, C. Alleman (2017): proved convergence of the alternating Schwarz method for finite deformation quasi-static nonlinear PDEs (with energy functional ) with a geometric convergence rate.
S.G. Mikhlin
(1908 – 1990)
S.L. Sobolev (1908 – 1989)
A. Mota, I. Tezaur, C. Alleman
Using the Schwarz alternating as a discretization method for PDEs is natural idea with a sound theoretical foundation.
Theoretical Foundation
P.- L. Lions (1956-)
Notes: A(F,Z) = Helmholtz free-energy density, Z = collection of internal variables, F = grad(phi) = deformation gradient, B = body force, T = traction on boundary
P = \partial A/\partial F = first Piola-Kirchoff stress
2nd equation is Euler-Lagrange equation

## Slide 58
Convergence Proof*
*A. Mota, I. Tezaur, C. Alleman. "The Schwarz Alternating Method in Solid Mechanics", CMAME 319 (2017), 19-51.
Notes: The proof effectively constructs a sequence of solutions phi^n and demonstrates that this sequence converges to the unique minimizer of the energy functional \Phi defining the single-domain problem, and combines concepts used in the analysis of Sobolev, Lions, and others, in studying the convergence of the Schwarz method.

## Slide 59
Schwarz Alternating Method for Dynamic Multiscale Coupling: Theory
Like for quasistatics, dynamic alternating Schwarz method converges provided each single-domain problem is well-posed and overlap region is non-empty, under some conditions on .
Well-posedness for the dynamic problem requires that action functional be strictly convex or strictly concave, where is the Lagrangian.
  This is studied by looking at its second variation
We can show assuming a Newmark time-integration scheme that for the fully-discrete problem:
can always be made positive by choosing a sufficiently small
Numerical experiments reveal that requirements for stability/accuracy typically lead to automatic satisfaction of this bound.
*A. Mota, I. Tezaur, G. Phlipot. "The Schwarz alternating method for dynamic solid mechanics", IJNME, 2022.

## Slide 60: Energy-Conserving Sampling and Weighting (ECSW)
Project-then-approximate paradigm (as opposed to approximate-then-project)
where is the number of degrees of freedom associated with each mesh element (this is in the context of meshes used in first-order hyperbolic problems where there are mesh elements)
selects degrees of freedom necessary for flux reconstruction
Equality can be relaxed

## Slide 61: ECSW: Generating the Reduced Mesh and Weights
Using a subset of the same snapshots used to generate the state basis , we can train the reduced mesh
Snapshots are first projected onto their associated basis and then reconstructed
We can then form the system
Where , must be the solution
Further relax the equality to yield non-negative least-squares problem:
subject to
Solve the above optimization problem using a non-negative least squares solver with an early termination condition to promote sparsity of the vector