## Slide 1: Accelerating analyst workflows via alternating Schwarz-based coupling and (non-intrusive Operator Inference-based) model order reduction
I. Tezaur1, E. Parish1, A. Gruber1, I. Moore1,2, C. Wentland1, C. Rodriguez3, A. Mota1
1Sandia National Laboratories, USA. 2Virginia Tech, USA. 3Columbia University, USA
SIAM PP 2026 March 2-6, 2026 Berlin, Germany
SAND2026-17036C

## Slide 2
Preliminaries
  Motivation
  The Schwarz Alternating Method (SAM) for Multi-Scale Coupling
  Non-Intrusive Operator Inference (OpInf)
Overlapping SAM for OpInf Reduced Order Model (ROM) Coupling
  Methodology
  Numerical Examples
Non-overlapping SAM for OpInf ROM Coupling
  Methodology
  Numerical Example
Summary
Ongoing & Future Work
Outline

## Slide 3
Preliminaries
  Motivation
  The Schwarz Alternating Method (SAM) for Multi-Scale Coupling
  Non-Intrusive Operator Inference (OpInf)
Overlapping SAM for OpInf Reduced Order Model (ROM) Coupling
  Methodology
  Numerical Examples
Non-overlapping SAM for OpInf ROM Coupling
  Methodology
  Numerical Example
Summary
Ongoing & Future Work
Outline

## Slide 4: Motivation: Multiscale & Multiphysics Coupling for Predictive Digital Twins
Monolithic (Lagrange multipliers)
Partitioned (loose) coupling
Iterative (Schwarz, optimization)
M1
M2
M3
M4
N3
N4
N1
N2
N5
N3
N4
N5
N2
N1
PDEs, ODEs
Nonlocal integral
Classical DFT
Atomistic, …
Mesh-based (FE, FV, FD)
Meshless (SPH, MLS)
Implicit, explicit
Eulerian, Lagrangian, …
Complex System Model
Traditional Methods
Coupled Numerical Model
Ocean
(MPAS-O)
Atmos.
(EAM)
Sea Ice
(MPAS-SI)
Land Ice
(MALI)
Land
(ELM)
DMD=N3
ROM=N4
N1
PINN=N2
UDE=N5
Traditional + Data-Driven Methods
PINNs
Neural ODEs
Projection-based ROMs, …

There exist established rigorous mathematical theories for coupling multiscale/multiphysics components based on traditional discretization methods (FOMs).
Multiphysics
Notes: TODO: change title? Say in outline slide that limiting to overlapping.

## Slide 5: Motivation: Multiscale & Multiphysics Coupling for Predictive Digital Twins
Monolithic (Lagrange multipliers)
Partitioned (loose) coupling
Iterative (Schwarz, optimization)
M1
M2
M3
M4
N3
N4
N1
N2
N5
N3
N4
N5
N2
N1
PDEs, ODEs
Nonlocal integral
Classical DFT
Atomistic, …
Mesh-based (FE, FV, FD)
Meshless (SPH, MLS)
Implicit, explicit
Eulerian, Lagrangian, …
Complex System Model
Traditional Methods
Coupled Numerical Model
Traditional + Data-Driven Methods
PINNs
Neural ODEs
Projection-based ROMs, …
There exist established rigorous mathematical theories for coupling multiscale/multiphysics components based on traditional discretization methods (FOMs).

Deficiencies of data-driven models and couplings involving them:
  Existing coupling methods for high-fidelity models may not work out-of-the-box when including data-driven models
  ROMs can suffer from lack of robustness, stability and accuracy, and cannot be easily refined to achieve a specified accuracy

DMD=N3
ROM=N4
N1
PINN=N2
UDE=N5
Multiscale
Notes: TODO: change title? Say in outline slide that limiting to overlapping.

## Slide 6: Motivation: Multiscale & Multiphysics Coupling for Predictive Digital Twins
Monolithic (Lagrange multipliers)
Partitioned (loose) coupling
Iterative (Schwarz, optimization)
M1
M2
M3
M4
N3
N4
N1
N2
N5
N3
N4
N5
N2
N1
PDEs, ODEs
Nonlocal integral
Classical DFT
Atomistic, …
Mesh-based (FE, FV, FD)
Meshless (SPH, MLS)
Implicit, explicit
Eulerian, Lagrangian, …
Complex System Model
Traditional Methods
Coupled Numerical Model
Traditional + Data-Driven Methods
PINNs
Neural ODEs
Projection-based ROMs, …
There exist established rigorous mathematical theories for coupling multiscale/multiphysics components based on traditional discretization methods (FOMs).

Deficiencies of data-driven models and couplings involving them:
  Existing coupling methods for high-fidelity models may not work out-of-the-box when including data-driven models
  ROMs can suffer from lack of robustness, stability and accuracy, and cannot be easily refined to achieve a specified accuracy

Proposed solution: domain decomposition- (DD-) based coupling via SAM & (soon) online model switching
DMD=N3
ROM=N4
N1
PINN=N2
UDE=N5
Multiscale
Notes: TODO: change title? Say in outline slide that limiting to overlapping.

## Slide 7
Preliminaries
  Motivation
  The Schwarz Alternating Method (SAM) for Multi-Scale Coupling
  Non-Intrusive Operator Inference (OpInf)
Overlapping SAM for OpInf Reduced Order Model (ROM) Coupling
  Methodology
  Numerical Examples
Non-overlapping SAM for OpInf ROM Coupling
  Methodology
  Numerical Example
Summary
Ongoing & Future Work
Outline

## Slide 8: Schwarz Alternating Method (SAM)
Proposed in 1870 by H. Schwarz for solving Laplace PDE on irregular domains.
2Lions, 1990. 3Zanolli et al., 1987.
overlapping
non-overlapping
SAM most commonly used as a preconditioner for linear solvers.
Idea behind this work: using SAM as a discretization/ coupling method for solving multiscale PDEs.
Initialize:
Solve PDE by any method on w/ initial guess for transmission boundary conditions (BCs) on .
Iterate until convergence:
Solve PDE by any method in w/ BCs on from just-obtained solution.
Solve PDE by any method in w/ BCs on from just-obtained solution.
Basic Schwarz Algorithm
H. Schwarz
Crux of Method: if the solution is known in regularly shaped domains, use those as pieces to iteratively build a solution for the more complex domain.
Original driving application: simplifying meshing in solid mechanics.
Enables coupling* of subdomains with different non-conformal meshes, element types, levels of refinement, time-steppers, solvers and models
*Mota et al., 2017; Mota et al., 2022.

## Slide 9
Overlapping Domain Decomposition
Non-overlapping Domain Decomposition
Relevant for multi-material and multiphysics coupling
Alternating Dirichlet-Neumann transmission BCs [Zanolli et al., 1987]
Robin-Robin transmission BCs also lead to convergence [Lions,1990]
relaxation parameter (can help convergence)
Dirichlet-Dirichlet transmission BCs [Schwarz, 1870; Lions, 1988]
DD-based Coupling via SAM
Model PDE:
More flexible but slower to converge
Easier implementation and faster convergence
Notes: TODO: rework this slide to have generic DN and RR formulation

## Slide 10
Preliminaries
  Motivation
  The Schwarz Alternating Method (SAM) for Multi-Scale Coupling
  Non-Intrusive Operator Inference (OpInf)
Overlapping SAM for OpInf Reduced Order Model (ROM) Coupling
  Methodology
  Numerical Examples
Non-overlapping SAM for OpInf ROM Coupling
  Methodology
  Numerical Example
Summary
Ongoing & Future Work
Outline

## Slide 11: Projection-Based Model Order Reduction via the POD/Galerkin Method
11
Full Order Model (FOM):
Proper Orthogonal Decomposition (POD):
Solve ODE at different design points
1. Acquisition
2. Learning
3. Projection-Based Reduction
Number of time steps
Number of State Variables
Save solution data
Reduce the number of unknowns
Perform Galerkin projection
+
Hyper-reduce nonlinear terms
Hyper-reduction/sample mesh
ROM = projection-based Reduced Order Model HROM = Hyper-reduced ROM
Disadvantage: intrusive!

## Slide 12: Non-Intrusive Model Order Reduction via OpInf*
12
Key Idea Behind OpInf: circumvent the burden of implementing intrusive ROMs in HPC codes by combining projection-based ROM and machine learning (ML).
FOM:
OpInf ROM:
snapshots of
Reduced basis
(e.g., linear POD or quadratic manifold basis)
: snapshots generated from projected simulation data
: low-dimensional operators defining ROM dynamical system
* [Peherstorfer & Willcox, 2016] + many subsequent refs
Nuances:
OpInf can be applied to nonlinear problems by transforming the nonlinear PDEs into PDEs with a polynomial functional form (“lifting” [Qian et al., 2019]) or assuming a polynomial functional form for the ROM
The OpInf least-squares (LS) minimization problem often requires regularization to be solvable, e.g., Tikhonov regularization
Structure preservation (e.g., symmetry constraints) can be incorporated into the OpInf LS minimization problem

## Slide 13
Preliminaries
  Motivation
  The Schwarz Alternating Method (SAM) for Multi-Scale Coupling
  Non-Intrusive Operator Inference (OpInf)
Overlapping SAM for OpInf Reduced Order Model (ROM) Coupling
  Methodology
  Numerical Examples
Non-overlapping SAM for OpInf ROM Coupling
  Methodology
  Numerical Example
Summary
Ongoing & Future Work
Outline

## Slide 14: Overlapping SAM-based Coupling for Non-Intrusive OpInf ROMs
14
OpInf ROM in :
(
Offline stage:
Create DD of into overlapping subdomains
Perform a SAM-coupled all-FOM simulation on
Compute POD basis on each
Assume a functional form for your ROM in , informed by the functional form of the corresponding FOM
  Key question: how to impose Schwarz BCs in OpInf ROMs?
Notes: The proposed approach is most similar to the recent work by Farcas et al. [9], which develops a DD-based coupling of subdomain-local OpInf ROMs by learning appropriate reduced operators responsible for the coupling, and demonstrates the method on a formidable three-dimensional (3D) combustion problem. In this approach, each subdomain problem is solved once rather than by performing an iteration to convergence as done within our Schwarz framework. As a result, the subdomain-local solutions must be extended to the full domain and smoothly combined to achieve a continuous solution

## Slide 15: Overlapping SAM-based Coupling for Non-Intrusive OpInf ROMs
15
OpInf ROM + Schwarz BCs in :
(
Schwarz Dirichlet BC term
Motivated by implementation of Dirichlet BCs in FEM
Offline stage:
Create DD of into overlapping subdomains
Perform a SAM-coupled all-FOM simulation on
Compute POD basis on each
Assume a functional form for your ROM in , informed by the functional form of the corresponding FOM
  Key question: how to impose Schwarz BCs in OpInf ROMs?
    Boundary transmission enters through learned source term added to OpInf ROM dynamical system
Notes: The proposed approach is most similar to the recent work by Farcas et al. [9], which develops a DD-based coupling of subdomain-local OpInf ROMs by learning appropriate reduced operators responsible for the coupling, and demonstrates the method on a formidable three-dimensional (3D) combustion problem. In this approach, each subdomain problem is solved once rather than by performing an iteration to convergence as done within our Schwarz framework. As a result, the subdomain-local solutions must be extended to the full domain and smoothly combined to achieve a continuous solution

## Slide 16: Overlapping SAM-based Coupling for Non-Intrusive OpInf ROMs
16
Offline stage:
Create DD of into overlapping subdomains
Perform a SAM-coupled all-FOM simulation on
Compute POD basis on each
Assume a functional form for your ROM in , informed by the functional form of the corresponding FOM
  Key question: how to impose Schwarz BCs in OpInf ROMs?
    Boundary transmission enters through learned source term added to OpInf ROM dynamical system
    Further reduction achieved by expanding in its own POD basis and approximating where
Schwarz Dirichlet BC term
Motivated by implementation of Dirichlet BCs in FEM
OpInf ROM + Schwarz BCs in :
(
Notes: The proposed approach is most similar to the recent work by Farcas et al. [9], which develops a DD-based coupling of subdomain-local OpInf ROMs by learning appropriate reduced operators responsible for the coupling, and demonstrates the method on a formidable three-dimensional (3D) combustion problem. In this approach, each subdomain problem is solved once rather than by performing an iteration to convergence as done within our Schwarz framework. As a result, the subdomain-local solutions must be extended to the full domain and smoothly combined to achieve a continuous solution

## Slide 17: Overlapping SAM-based Coupling for Non-Intrusive OpInf ROMs
17
Offline stage:
Create DD of into overlapping subdomains
Perform a SAM-coupled all-FOM simulation on
Compute POD basis on each
Assume a functional form for your ROM in , informed by the functional form of the corresponding FOM
  Key question: how to impose Schwarz BCs in OpInf ROMs?
    Boundary transmission enters through learned source term added to OpInf ROM dynamical system
    Further reduction achieved by expanding in its own POD basis and approximating where
Compute OpInf operators and in each subdomain by solving regularized OpInf LS minimization problem
Schwarz Dirichlet BC term
Motivated by implementation of Dirichlet BCs in FEM
OpInf ROM + Schwarz BCs in :
(
Notes: The proposed approach is most similar to the recent work by Farcas et al. [9], which develops a DD-based coupling of subdomain-local OpInf ROMs by learning appropriate reduced operators responsible for the coupling, and demonstrates the method on a formidable three-dimensional (3D) combustion problem. In this approach, each subdomain problem is solved once rather than by performing an iteration to convergence as done within our Schwarz framework. As a result, the subdomain-local solutions must be extended to the full domain and smoothly combined to achieve a continuous solution

## Slide 18: Overlapping SAM-based Coupling for Non-Intrusive OpInf ROMs
18
Offline stage:
Create DD of into overlapping subdomains
Perform a SAM-coupled all-FOM simulation on
Compute POD basis on each
Assume a functional form for your ROM in , informed by the functional form of the corresponding FOM
  Key question: how to impose Schwarz BCs in OpInf ROMs?
    Boundary transmission enters through learned source term added to OpInf ROM dynamical system
    Further reduction achieved by expanding in its own POD basis and approximating where
Compute OpInf operators and in each subdomain by solving regularized OpInf LS minimization problem
Schwarz Dirichlet BC term
Motivated by implementation of Dirichlet BCs in FEM
OpInf ROM + Schwarz BCs in :
(
Online stage:
Apply Schwarz iteration procedure, with Schwarz BC transfer via pre-learned boundary contributions
Notes: The proposed approach is most similar to the recent work by Farcas et al. [9], which develops a DD-based coupling of subdomain-local OpInf ROMs by learning appropriate reduced operators responsible for the coupling, and demonstrates the method on a formidable three-dimensional (3D) combustion problem. In this approach, each subdomain problem is solved once rather than by performing an iteration to convergence as done within our Schwarz framework. As a result, the subdomain-local solutions must be extended to the full domain and smoothly combined to achieve a continuous solution

## Slide 19
Preliminaries
  Motivation
  The Schwarz Alternating Method (SAM) for Multi-Scale Coupling
  Non-Intrusive Operator Inference (OpInf)
Overlapping SAM for OpInf Reduced Order Model (ROM) Coupling
  Methodology
  Numerical Examples
Non-overlapping SAM for OpInf ROM Coupling
  Methodology
  Numerical Example
Summary
Ongoing & Future Work
Outline

## Slide 20: Tension Specimen (Overlapping SAM, Predictive)
20
NORMA.JL
QOpInf = Quadratic OpInf
 |  | FOM-FOM | FOM-QOpInf | QOpInf-QOpInf
rel errs | displacement |  | 3.44e-4 | 5.73e-4
 | velocity |  | 1.72e-2 | 1.83e-2
 | stress |  | 3.41e-4 | 8.53e-4
rel errs | displacement |  | 2.50e-4 | 4.41e-4
 | velocity |  | 1.86e-2 | 1.96e-2
 | stress |  | 2.40e-3 | 6.00e-3
CPU time |  | 8h 19m 29.5s | 1h 21m 25.9s | 4m 42.1s
Mean/max # Schwarz iters |  | 32.0/32 | 7.03/8 | 7.74/8
 |  | FOM-FOM | FOM-QOpInf | QOpInf-QOpInf
 | displacement |  | 3.44e-4 | 5.73e-4
 | velocity |  | 1.72e-2 | 1.83e-2
 |  |  | 3.41e-4 | 8.53e-4
 | displacement |  | 2.50e-4 | 4.41e-4
 | velocity |  | 1.86e-2 | 1.96e-2
 |  |  | 2.40e-3 | 6.00e-3
CPU time |  | 8h 19m 29.5s | 1h 21m 25.9s | 4m 42.1s
Mean/max # Schwarz iters |  | 32.0/32 | 7.03/8 | 7.74/8
FOM-FOM
FOM-QOpInf
Hyperelastic (Neohookean) tension specimen pulled from top
TET10 – HEX8 overlapping coupling with implicit Newmark with same
Quadratic OpInf (QOpInf) models with M=2 POD modes, capturing 99.9999% snapshot energy
All results are predictive w.r.t. DBC applied at top of holder
von Mises stress
Notes: TODO: add movies!

## Slide 21: Tension Specimen (Overlapping SAM, Predictive)
von Mises stress
21
NORMA.JL
QOpInf = Quadratic OpInf
 |  | FOM-FOM | FOM-QOpInf | QOpInf-QOpInf
rel errs | displacement |  | 3.44e-4 | 5.73e-4
 | velocity |  | 1.72e-2 | 1.83e-2
 | stress |  | 3.41e-4 | 8.53e-4
rel errs | displacement |  | 2.50e-4 | 4.41e-4
 | velocity |  | 1.86e-2 | 1.96e-2
 | stress |  | 2.40e-3 | 6.00e-3
CPU time |  | 8h 19m 29.5s | 1h 21m 25.9s | 4m 42.1s
Mean/max # Schwarz iters |  | 32.0/32 | 7.03/8 | 7.74/8
 |  | FOM-FOM | FOM-QOpInf | QOpInf-QOpInf
 | displacement |  | 3.44e-4 | 5.73e-4
 | velocity |  | 1.72e-2 | 1.83e-2
 |  |  | 3.41e-4 | 8.53e-4
 | displacement |  | 2.50e-4 | 4.41e-4
 | velocity |  | 1.86e-2 | 1.96e-2
 |  |  | 2.40e-3 | 6.00e-3
CPU time |  | 8h 19m 29.5s | 1h 21m 25.9s | 4m 42.1s
Mean/max # Schwarz iters |  | 32.0/32 | 7.03/8 | 7.74/8
Relative errors of (1e-4)-(1e-3) are achieved for the displacement and von Mises stress ()
FOM-FOM
FOM-QOpInf
Hyperelastic (Neohookean) tension specimen pulled from top
TET10 – HEX8 overlapping coupling with implicit Newmark with same
Quadratic OpInf (QOpInf) models with M=2 POD modes, capturing 99.9999% snapshot energy
All results are predictive w.r.t. DBC applied at top of holder
von Mises stress
Notes: TODO: add movies!

## Slide 22: Tension Specimen (Overlapping SAM, Predictive)
FOM-FOM
FOM-QOpInf
22
NORMA.JL
QOpInf = Quadratic OpInf
 |  | FOM-FOM | FOM-QOpInf | QOpInf-QOpInf
rel errs | displacement |  | 3.44e-4 | 5.73e-4
 | velocity |  | 1.72e-2 | 1.83e-2
 | stress |  | 3.41e-4 | 8.53e-4
rel errs | displacement |  | 2.50e-4 | 4.41e-4
 | velocity |  | 1.86e-2 | 1.96e-2
 | stress |  | 2.40e-3 | 6.00e-3
CPU time |  | 8h 19m 29.5s | 1h 21m 25.9s | 4m 42.1s
Mean/max # Schwarz iters |  | 32.0/32 | 7.03/8 | 7.74/8
 |  | FOM-FOM | FOM-QOpInf | QOpInf-QOpInf
 | displacement |  | 3.44e-4 | 5.73e-4
 | velocity |  | 1.72e-2 | 1.83e-2
 |  |  | 3.41e-4 | 8.53e-4
 | displacement |  | 2.50e-4 | 4.41e-4
 | velocity |  | 1.86e-2 | 1.96e-2
 |  |  | 2.40e-3 | 6.00e-3
CPU time |  | 8h 19m 29.5s | 1h 21m 25.9s | 4m 42.1s
Mean/max # Schwarz iters |  | 32.0/32 | 7.03/8 | 7.74/8
Impressive 6.13 and 106 speedups are achieved via FOM-QOpInf and QOpInf-QOpInf couplings, respectively!
Relative errors of (1e-4)-(1e-3) are achieved for the displacement and von Mises stress ()
Hyperelastic (Neohookean) tension specimen pulled from top
TET10 – HEX8 overlapping coupling with implicit Newmark with same
Quadratic OpInf (QOpInf) models with M=2 POD modes, capturing 99.9999% snapshot energy
All results are predictive w.r.t. DBC applied at top of holder
von Mises stress
Notes: TODO: add movies!

## Slide 23: Tension Specimen (Overlapping SAM, Predictive)
23
NORMA.JL
QOpInf = Quadratic OpInf
 |  | FOM-FOM | FOM-QOpInf | QOpInf-QOpInf
rel errs | displacement |  | 3.44e-4 | 5.73e-4
 | velocity |  | 1.72e-2 | 1.83e-2
 | stress |  | 3.41e-4 | 8.53e-4
rel errs | displacement |  | 2.50e-4 | 4.41e-4
 | velocity |  | 1.86e-2 | 1.96e-2
 | stress |  | 2.40e-3 | 6.00e-3
CPU time |  | 8h 19m 29.5s | 1h 21m 25.9s | 4m 42.1s
Mean/max # Schwarz iters |  | 32.0/32 | 7.03/8 | 7.74/8
 |  | FOM-FOM | FOM-QOpInf | QOpInf-QOpInf
 | displacement |  | 3.44e-4 | 5.73e-4
 | velocity |  | 1.72e-2 | 1.83e-2
 |  |  | 3.41e-4 | 8.53e-4
 | displacement |  | 2.50e-4 | 4.41e-4
 | velocity |  | 1.86e-2 | 1.96e-2
 |  |  | 2.40e-3 | 6.00e-3
CPU time |  | 8h 19m 29.5s | 1h 21m 25.9s | 4m 42.1s
Mean/max # Schwarz iters |  | 32.0/32 | 7.03/8 | 7.74/8
Impressive 6.13 and 106 speedups are achieved via FOM-QOpInf and QOpInf-QOpInf couplings, respectively!
Speedup largely due to huge reduction in # Schwarz iterations
Relative errors of (1e-4)-(1e-3) are achieved for the displacement and von Mises stress ()
FOM-FOM
FOM-QOpInf
Hyperelastic (Neohookean) tension specimen pulled from top
TET10 – HEX8 overlapping coupling with implicit Newmark with same
Quadratic OpInf (QOpInf) models with M=2 POD modes, capturing 99.9999% snapshot energy
All results are predictive w.r.t. DBC applied at top of holder
von Mises stress
Notes: TODO: add movies!

## Slide 24: Torsion (Overlapping SAM, Reproductive & Predictive)
24
 |  | FOM-FOM | QOpInf-FOM reproductive | QOpInf-FOM predictive
rel errs | displacement |  | 2.67e-3 | 4.32e-2
 | velocity |  | 3.56e-2 | 1.49e-1
rel errs | displacement |  | 1.13e-3 | 2.44e-2
 | velocity |  | 1.12e-2 | 9.52e-2
CPU time |  | 39m 11.8s | 1m 40.2s | 1m 39.5s
Mean/max # Schwarz iters |  | 3.0/3 | 2.0/2 | 2.0/2
 |  | FOM-FOM | QOpInf-FOM reproductive | QOpInf-FOM predictive
 | displacement |  | 2.67e-3 | 4.32e-2
 | velocity |  | 3.56e-2 | 1.49e-1
 | displacement |  | 1.13e-3 | 2.44e-2
 | velocity |  | 1.12e-2 | 9.52e-2
CPU time |  | 39m 11.8s | 1m 40.2s | 1m 39.5s
Mean/max # Schwarz iters |  | 3.0/3 | 2.0/2 | 2.0/2
NORMA.JL
FOM-FOM
QOpInf-FOM
Neohookean material model
TET4 – HEX8 overlapping coupling with implicit-explicit Newmark having different
QOpInf-FOM coupled models with M=27 and M=30 POD modes, capturing 99.9999% snapshot energy
Prediction w.r.t. initial velocity (rotation speed/direction)
(Linear) OpInf-FOM coupling insufficient
QOpInf = Quadratic OpInf
Notes: TODO: add movies

## Slide 25
25
 |  | FOM-FOM | QOpInf-FOM reproductive | QOpInf-FOM predictive
rel errs | displacement |  | 2.67e-3 | 4.32e-2
 | velocity |  | 3.56e-2 | 1.49e-1
rel errs | displacement |  | 1.13e-3 | 2.44e-2
 | velocity |  | 1.12e-2 | 9.52e-2
CPU time |  | 39m 11.8s | 1m 40.2s | 1m 39.5s
Mean/max # Schwarz iters |  | 3.0/3 | 2.0/2 | 2.0/2
 |  | FOM-FOM | QOpInf-FOM reproductive | QOpInf-FOM predictive
 | displacement |  | 2.67e-3 | 4.32e-2
 | velocity |  | 3.56e-2 | 1.49e-1
 | displacement |  | 1.13e-3 | 2.44e-2
 | velocity |  | 1.12e-2 | 9.52e-2
CPU time |  | 39m 11.8s | 1m 40.2s | 1m 39.5s
Mean/max # Schwarz iters |  | 3.0/3 | 2.0/2 | 2.0/2
NORMA.JL
FOM-FOM
QOpInf-FOM
QOpInf = Quadratic OpInf
Relative errors are of (1e-3)-(1e-2) for displacement and velocity!
Torsion (Overlapping SAM, Reproductive & Predictive)
Neohookean material model
TET4 – HEX8 overlapping coupling with implicit-explicit Newmark having different
QOpInf-FOM coupled models with M=27 and M=30 POD modes, capturing 99.9999% snapshot energy
Prediction w.r.t. initial velocity (rotation speed/direction)
(Linear) OpInf-FOM coupling insufficient
Notes: TODO: add movies

## Slide 26: Torsion (Overlapping SAM, Reproductive & Predictive)
26
 |  | FOM-FOM | QOpInf-FOM reproductive | QOpInf-FOM predictive
rel errs | displacement |  | 2.67e-3 | 4.32e-2
 | velocity |  | 3.56e-2 | 1.49e-1
rel errs | displacement |  | 1.13e-3 | 2.44e-2
 | velocity |  | 1.12e-2 | 9.52e-2
CPU time |  | 39m 11.8s | 1m 40.2s | 1m 39.5s
Mean/max # Schwarz iters |  | 3.0/3 | 2.0/2 | 2.0/2
 |  | FOM-FOM | QOpInf-FOM reproductive | QOpInf-FOM predictive
 | displacement |  | 2.67e-3 | 4.32e-2
 | velocity |  | 3.56e-2 | 1.49e-1
 | displacement |  | 1.13e-3 | 2.44e-2
 | velocity |  | 1.12e-2 | 9.52e-2
CPU time |  | 39m 11.8s | 1m 40.2s | 1m 39.5s
Mean/max # Schwarz iters |  | 3.0/3 | 2.0/2 | 2.0/2
NORMA.JL
FOM-FOM
QOpInf-FOM
QOpInf = Quadratic OpInf
~23.5 speedups are achieved via QOpInf-FOM couplings
Relative errors are of (1e-3)-(1e-2) for displacement and velocity!
Neohookean material model
TET4 – HEX8 overlapping coupling with implicit-explicit Newmark having different
QOpInf-FOM coupled models with M=27 and M=30 POD modes, capturing 99.9999% snapshot energy
Prediction w.r.t. initial velocity (rotation speed/direction)
(Linear) OpInf-FOM coupling insufficient
Notes: TODO: add movies

## Slide 27: Bolted Joint (Overlapping SAM, Reproductive)
27
Figure above: convergence w.r.t. basis size for reproductive FOM-COpInf coupling
NORMA.JL
Hyper-elastic (Saint-Venant Kirchhoff) problem with TET10 – HEX8 meshes
Loading is applied to top part of bolted join
Cubic OpInf (COpInf) coupled models
Hybrid couplings require fewer Schwarz iterations to converge
Convergence w.r.t. basis size is observed for reproductive FOM-QOpInf couplings (right)

## Slide 28: Bolted Joint (Overlapping SAM, Predictive): Displacements
28
FOM-FOM
FOM-COpInf
0.69% rel err (parts)
3.51% rel err (bolts)
COpInf-COpInf (best)
0.98% rel err (parts)
4.41% rel err (bolts)
COpInf-COpInf (worst)
12.9% rel err (parts)
12.5% rel err (bolts)
Models generally achieve relative errors of (1%) in displacement.
1.65speedup
6.12speedup
NORMA.JL
COpInf = Cubic OpInf

## Slide 29: Bolted Joint (Overlapping SAM, Predictive): von Mises Stresses
29
FOM-FOM
FOM-COpInf
7.74% rel err
COpInf-COpInf (best)
12.4% rel error
COpInf-COpInf (worst)
30.9% rel error
All models correctly predict locations of maximum von Mises stress (failure).
1.65speedup
6.12speedup
High errors do not necessarily mean result cannot be informative.
NORMA.JL
COpInf = Cubic OpInf
Notes: .

## Slide 30
Preliminaries
  Motivation
  The Schwarz Alternating Method (SAM) for Multi-Scale Coupling
  Non-Intrusive Operator Inference (OpInf)
Overlapping SAM for OpInf Reduced Order Model (ROM) Coupling
  Methodology
  Numerical Examples
Non-overlapping SAM for OpInf ROM Coupling
  Methodology
  Numerical Example
Summary
Ongoing & Future Work
Outline

## Slide 31: Non-overlapping SAM-based Coupling for Non-Intrusive OpInf ROMs
31
Alternating Dirichlet-Neumann non-overlapping SAM (dynamic linear elastic problem)

## Slide 32: Non-overlapping SAM-based Coupling for Non-Intrusive OpInf ROMs
32
Alternating Dirichlet-Neumann non-overlapping SAM (dynamic linear elastic problem)

## Slide 33: Non-overlapping SAM-based Coupling for Non-Intrusive OpInf ROMs
33
Alternating Dirichlet-Neumann non-overlapping SAM (dynamic linear elastic problem)
Dirichlet problem: learn , ,
Use snapshots of displacement, acceleration and Dirichlet data to train ROM
Neumann problem: learn , , ,
Use snapshots of displacement, acceleration, Dirichlet data and tractions to train ROM
OpInf ROMs

## Slide 34
Preliminaries
  Motivation
  The Schwarz Alternating Method (SAM) for Multi-Scale Coupling
  Non-Intrusive Operator Inference (OpInf)
Overlapping SAM for OpInf Reduced Order Model (ROM) Coupling
  Methodology
  Numerical Examples
Non-overlapping SAM for OpInf ROM Coupling
  Methodology
  Numerical Example
Summary
Ongoing & Future Work
Outline

## Slide 35: Linear Elastic Wave Propagation (Non-Overlapping SAM, Reproductive)
35
1D linear elastic clamped beam with Gaussian initial condition for the displacement.
Simple problem with analytical exact solution but very stringent test for discretization methods.
Test non-overlapping SAM w/ 2 subdomains:
Above: representative OpInf-FOM coupling result
Good accuracy and moderate speedups over FOM-FOM coupling are possible. Larger speedups expected in multi-D.
Notes: .

## Slide 36: Work in Progress: Accelerating Non-Overlapping SAM via Transmission Condition Design
36
Risk: non-overlapping Schwarz can be slow to converge w/ Dirichlet-Neumann TCs.
Mitigation: explore optimized Robin-Robin transmission conditions (TCs).
Non-overlapping SAM with optimized Robin-Robin TCs can give to faster convergence (29% less Schwarz iterations), lower errors (by up to 25%), and more stable/accurate time-predictive ROMs than non-overlapping SAM with Dirichlet-Neumann TCs.
tuning parameters
Automatic tuning of possible using Bayesian optimization via GPTune.
C. Rodriguez (Columbia U)
Notes: .

## Slide 37
Preliminaries
  Motivation
  The Schwarz Alternating Method (SAM) for Multi-Scale Coupling
  Non-Intrusive Operator Inference (OpInf)
Overlapping SAM for OpInf Reduced Order Model (ROM) Coupling
  Methodology
  Numerical Examples
Non-overlapping SAM for OpInf ROM Coupling
  Methodology
  Numerical Example
Summary
Ongoing & Future Work
Outline

## Slide 38
Summary
The Schwarz alternating method has been developed for concurrent multiscale coupling of conventional and data-driven models.
Coupling is concurrent (two-way).
Ease of implementation into existing massively-parallel HPC codes.
“Plug-and-play” framework: simplifies task of meshing complex geometries!
  Ability to couple regions with different non-conformal meshes, different element types and different levels of refinement.
  Ability to use different solvers (including ROM/FOM) and time-integrators in different regions.
Scalable, fast, robust on real engineering problems
Coupling does not introduce nonphysical artifacts.
Theoretical convergence properties/guarantees.









## Slide 39
Preliminaries
  Motivation
  The Schwarz Alternating Method (SAM) for Multi-Scale Coupling
  Non-Intrusive Operator Inference (OpInf)
Overlapping SAM for OpInf Reduced Order Model (ROM) Coupling
  Methodology
  Numerical Examples
Non-overlapping SAM for OpInf ROM Coupling
  Methodology
  Numerical Example
Summary
Ongoing & Future Work
Outline

## Slide 40
Ongoing & Future Work
Performance Improvements
Acceleration of Schwarz via optimized Robin-Robin TCs
Acceleration of Schwarz via Aitken and Anderson Acceleration
Asynchronous additive Schwarz on GPUs
Automated & Adaptive Schwarz
Automated optimization of meshes/DD with multiple constraints
Automated criteria to determine appropriate use of less refined or reduced-order models w/o sacrificing accuracy
Schwarz for ROM/Data-Driven Model Coupling
Non-overlapping Schwarz + OpInf
Schwarz + Deep NN-OpInf ROMs
Schwarz + kernel-based ROMs (w/ Ionut Farcas, Virginia Tech)
Fully non-intrusive adaptive ROM-FOM coupling (w/ K. Willcox & N. Aretz, UT Austin)
On-the-fly switching between ROMs and FOMs
Implementation in Sandia’s production code, SIERRA/SM
Schwarz + multiphysics coupling
Thank you! Questions?

## Slide 41: References on SAM for FOM-ROM and ROM-ROM Coupling
Schwarz Couplings Involving Non-Intrusive OpInf ROMs:
I. Tezaur, E. Parish, A. Gruber, I. Moore, C. Wentland, A. Mota. “Hybrid coupling with operator inference and the overlapping Schwarz alternating method”. ArXiv pre-print, 2025. https://arxiv.org/abs/2511.20687
  Implementation: Norma.jl Julia code (https://github.com/sandialabs/Norma.jl)
C. Rodriguez, I. Tezaur, A. Mota, A. Gruber, E. Parish, C. Wentland. “Transmission Conditions for the Non-Overlapping Schwarz Coupling of Full Order and Operator Inference Models”, CSRI Summer Proceedings 2025, Sandia National Laboratories. https://arxiv.org/abs/2509.12228
  First application of non-overlapping Schwarz to OpInf-FOM and OpInf-OpInf coupling that we are aware of
I. Tezaur J. Barnett I. Moore E. Parish C. Wentland A. Gruber C. Rodriguez W. Snyder G. Sambataro
NORMA.JL
Contact: Irina Tezaur (ikalash@sandia.gov)
Notes: TODO: add new paper to be submitted. Add QR codes.

## Slide 42
Contact
ikalash@sandia.gov
www.sandia.gov/~ikalash
NORMA.JL

## Slide 43: Other References on SAM for FOM-ROM and ROM-ROM Coupling
Schwarz Couplings Involving Intrusive Projection-Based ROMs:
J. Barnett, I. Tezaur, A. Mota. “The Schwarz alternating method for the seamless coupling of nonlinear reduced order models and full order models”, CSRI Summer Proceedings 2023, Sandia National Laboratories. https://arxiv.org/abs/2210.12551
C. Wentland, F. Rizzi, J. Barnett, I. Tezaur. “The role of interface boundary conditions and sampling strategies for Schwarz-based coupling of projection-based reduced order models”, J. Comput. Appl. Math., 465 116584, 2025
Schwarz Couplings Involving Physics-Informed Neural Networks (PINNs):
W. Snyder, I. Tezaur, C. Wentland. “Domain decomposition-based coupling of PINNs via the Schwarz alternating method”, CSRI Summer Proceedings 2023, Sandia National Laboratories. https://arxiv.org/abs/2311.00224
I. Tezaur J. Barnett I. Moore E. Parish C. Wentland A. Gruber C. Rodriguez W. Snyder G. Sambataro
Notes: TODO: add new paper to be submitted. Add QR codes.

## Slide 44: Start of Backup Slides

## Slide 45
Coupling is concurrent (two-way)
“Plug-and-play” framework: simplifies task of meshing complex geometries
  Ability to couple regions with different non-conformal meshes, different element types and different levels of refinement
  Ability to use different solvers/time-integrators in different regions
  Ability to mix-and-match conventional and data-driven models in different regions
Ease of implementation into existing massively-parallel HPC codes
Scalable, fast, robust (we target real engineering problems, e.g., analyses involving failure of bolted components!)
Coupling does not introduce nonphysical artifacts
Theoretical convergence properties/ guarantees
Requirements for Multiscale Coupling Method
A great method theoretically may not make it if it is too difficult to implement in production codes.
Figure above: schematic of difficult-to-mesh ratcheting mechanism with multiple threaded fasteners. From Parish et al., 2024.

## Slide 46
Coupling is concurrent (two-way)
“Plug-and-play” framework: simplifies task of meshing complex geometries
  Ability to couple regions with different non-conformal meshes, different element types and different levels of refinement
  Ability to use different solvers/time-integrators in different regions
  Ability to mix-and-match conventional and data-driven models in different regions
Ease of implementation into existing massively-parallel HPC codes
Scalable, fast, robust (we target real engineering problems, e.g., analyses involving failure of bolted components!)
Coupling does not introduce nonphysical artifacts
Theoretical convergence properties/ guarantees
Requirements for Multiscale Coupling Method
Creating a high-quality mesh can take weeks or longer, making it “the single biggest bottleneck in [mod/sim] analyses” [Sandia Lab News, 2020]
Above: schematic of difficult-to-mesh ratcheting mechanism with multiple threaded fasteners. From Parish et al., 2024.

## Slide 47: Projects on Coupling for Predictive Hybrid Models
Three projects:
FHNM: Flexible Heterogeneous Numerical Methods [LDRD, FY22-FY24]
M2dt: Multi-faceted Mathematics for Predictive Digital Twins [ASCR, FY23-FY27]
AHEAD: Adaptive Hybrid modEls via domAin Decomposition [LDRD, FY25-FY27]
Principal research objective:
Develop rigorous methods to enable the “plug-and-play” coupling of standard and data-driven models from the following classes
  Class A: intrusive projection-based ROMs
  Class B: machine-learned models
  Class C: flow map approximation models, i.e., dynamic model decomposition (DMD)
  Class D: non-intrusive operator inference (OpInf) ROMs
Three classes of coupling methods:
Alternating Schwarz-based coupling [FHNM, M2dt, AHEAD]
Optimization-based coupling [FHNM, M2dt]
Coupling via generalized mortar methods [FHNM, M2dt]
Notes: Class A and B are equation-based DDMs: they seek restrict a weak or strong form of the PDE to a finite-dimensional function space 𝑈_𝑖, spanned by a basis {𝑏_𝑖^𝑘 }_(𝑘=1)^(𝑁_𝑖 )
Class C DDMs are equation-free I/O relations 𝑢_𝑖 (𝑡)=〖𝐺_𝑖 (𝑓〗_𝑖,𝑢_(𝑖,0);𝑝_(𝑖,1),⋯,𝑝_(𝑖,𝑃)) with inputs (“ports”) 𝑝_(𝑖,𝑗).
TODO: add refs to other talks in MS.

## Slide 48: Projects on Coupling for Predictive Hybrid Models
Three projects:
FHNM: Flexible Heterogeneous Numerical Methods [LDRD, FY22-FY24]
M2dt: Multi-faceted Mathematics for Predictive Digital Twins [ASCR, FY23-FY27]
AHEAD: Adaptive Hybrid modEls via domAin Decomposition [LDRD, FY25-FY27]
Principal research objective:
Develop rigorous methods to enable the “plug-and-play” coupling of standard and data-driven models from the following classes
  Class A: intrusive projection-based ROMs
  Class B: machine-learned models
  Class C: flow map approximation models, i.e., dynamic model decomposition (DMD)
  Class D: non-intrusive operator inference (OpInf) ROMs this talk
Three classes of coupling methods:
Alternating Schwarz-based coupling [FHNM, M2dt, AHEAD] this talk
Optimization-based coupling [FHNM, M2dt]
Coupling via generalized mortar methods [FHNM, M2dt]
Why? Less intrusive to integrate into production codes.
Notes: Class A and B are equation-based DDMs: they seek restrict a weak or strong form of the PDE to a finite-dimensional function space 𝑈_𝑖, spanned by a basis {𝑏_𝑖^𝑘 }_(𝑘=1)^(𝑁_𝑖 )
Class C DDMs are equation-free I/O relations 𝑢_𝑖 (𝑡)=〖𝐺_𝑖 (𝑓〗_𝑖,𝑢_(𝑖,0);𝑝_(𝑖,1),⋯,𝑝_(𝑖,𝑃)) with inputs (“ports”) 𝑝_(𝑖,𝑗).
TODO: add refs to other talks in MS.

## Slide 49: Time-Advancement within the Schwarz Framework
Step 0: Initialize
Model PDE:
Controller time stepper
Time integrator in
Time integrator in

## Slide 50: Time-Advancement within the Schwarz Framework
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Model PDE:
Integrate using
Controller time stepper
Time integrator in
Time integrator in

## Slide 51: Time-Advancement within the Schwarz Framework
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Step 2: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times .
.
Model PDE:
Integrate using
Interpolate from to
Controller time stepper
Time integrator in
Time integrator in

## Slide 52: Time-Advancement within the Schwarz Framework
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Step 2: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times .
Step 3: Check for convergence at time .
Model PDE:
Controller time stepper
Time integrator in
Time integrator in

## Slide 53: Time-Advancement within the Schwarz Framework
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Step 2: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times .
Step 3: Check for convergence at time .
If unconverged, return to Step 1.
Model PDE:
Interpolate from to
Integrate using
Controller time stepper
Time integrator in
Time integrator in

## Slide 54: Time-Advancement within the Schwarz Framework
Step 0: Initialize
Step 1: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times
Step 2: Advance solution from time to time using time-stepper in with time-step using solution in interpolated to at times .
Step 3: Check for convergence at time .
If unconverged, return to Step 1.
If converged, set and return to Step 1.
Model PDE:
Interpolate from to
Integrate using
Controller time stepper
Time integrator in
Time integrator in
Can use different integrators with different time steps within each domain!
Time-stepping procedure is equivalent to doing Schwarz on space-time domain [Mota, IT, et al. 2022].

## Slide 55: Bolted Joint (Overlapping SAM, Predictive): Animations
55
FOM-FOM
~53m
COpInf-COpInf
~8.5m
COpInf = Cubic OpInf

## Slide 56: References on SAM for FOM-ROM and ROM-ROM Coupling (cont’d)
Schwarz Couplings Involving Intrusive Projection-Based ROMs:
J. Barnett, I. Tezaur, A. Mota. “The Schwarz alternating method for the seamless coupling of nonlinear reduced order models and full order models”, CSRI Summer Proceedings 2023, Sandia National Laboratories. https://arxiv.org/abs/2210.12551
C. Wentland, F. Rizzi, J. Barnett, I. Tezaur. “The role of interface boundary conditions and sampling strategies for Schwarz-based coupling of projection-based reduced order models”, J. Comput. Appl. Math., 465 116584, 2025
Schwarz Couplings Involving Physics-Informed Neural Networks (PINNs):
W. Snyder, I. Tezaur, C. Wentland. “Domain decomposition-based coupling of PINNs via the Schwarz alternating method”, CSRI Summer Proceedings 2023, Sandia National Laboratories. https://arxiv.org/abs/2311.00224
I. Tezaur J. Barnett I. Moore E. Parish C. Wentland A. Gruber C. Rodriguez W. Snyder G. Sambataro
Notes: TODO: add new paper to be submitted. Add QR codes.

## Slide 57: Current Research Directions
Production Applications
4-way multiscale coupling in salt caverns for Strategic Petroleum Reserve (SPR)
Schwarz coupling for J-integral around crack front on pressure vessel
Multiscale coupling for stronglinks
Schwarz multiphysics coupling for electronics package survivability
Performance Improvements
Acceleration of Schwarz
Asynchronous additive Schwarz on GPUs
Automated & Adaptive Schwarz
Automated optimization of meshes/DD with multiple constraints
Automated criteria to determine appropriate use of less refined or reduced-order models w/o sacrificing accuracy
Schwarz for ROM/Data-Driven Model Coupling
Non-overlapping Schwarz + OpInf
Schwarz + Deep NN-based ROMs
Schwarz + kernel-based ROMs
Fully non-intrusive ROM-FOM coupling (w/ K. Willcox & N. Aretz, UT Austin)
On-the-fly switching between ROMs and FOMs
Implementation in SIERRA/SM
Schwarz for salt cavern coupling.
Courtesy of T. Ross.
Notes: Q for Alejandro: what is SPR?

## Slide 58: How We Use the Schwarz Alternating Method
AS A PRECONDITIONER FOR THE LINEARIZED SYSTEM
AS A SOLVER FOR THE COUPLED
FULLY NONLINEAR PROBLEM
58

## Slide 59
S.L. Sobolev (1936): posed Schwarz method for linear elasticity in variational form and proved method’s convergence by proposing a convergent sequence of energy functionals.
S.G. Mikhlin (1951): proved convergence of Schwarz method for general linear elliptic PDEs.
P.-L. Lions (1988): studied convergence of Schwarz for nonlinear monotone elliptic problems using max principle.
A. Mota, I. Tezaur, C. Alleman (2017): proved convergence of the alternating Schwarz method for finite deformation quasi-static nonlinear PDEs (with energy functional ) with a geometric convergence rate.
S.G. Mikhlin
(1908 – 1990)
S.L. Sobolev (1908 – 1989)
A. Mota, I. Tezaur, C. Alleman
Using the Schwarz alternating as a discretization method for PDEs is natural idea with a sound theoretical foundation.
Theoretical Foundation
P.- L. Lions (1956-)
Notes: A(F,Z) = Helmholtz free-energy density, Z = collection of internal variables, F = grad(phi) = deformation gradient, B = body force, T = traction on boundary
P = \partial A/\partial F = first Piola-Kirchoff stress
2nd equation is Euler-Lagrange equation

## Slide 60
Theory: Overlapping SAM for Quasistatic Multiscale Coupling*
* Mota, IT, et al., 2017.
Notes: The proof effectively constructs a sequence of solutions phi^n and demonstrates that this sequence converges to the unique minimizer of the energy functional \Phi defining the single-domain problem, and combines concepts used in the analysis of Sobolev, Lions, and others, in studying the convergence of the Schwarz method.

## Slide 61
Theory: Overlapping SAM for Dynamic Multiscale Coupling*
Like for quasistatics, dynamic alternating Schwarz method converges provided each single-domain problem is well-posed and overlap region is non-empty, under some conditions on .
Well-posedness for the dynamic problem requires that action functional be strictly convex or strictly concave, where is the Lagrangian.
  This is studied by looking at its second variation
We can show assuming a Newmark time-integration scheme that for the fully-discrete problem:
can always be made positive by choosing a sufficiently small
Numerical experiments reveal that requirements for stability/accuracy typically lead to automatic satisfaction of this bound.
* Mota, IT, et al., 2022.

## Slide 62: Additional Parallelism via Additive Schwarz
Multiplicative Overlapping Schwarz
Additive Overlapping Schwarz
Multiplicative Schwarz: solves subdomain problems sequentially (in serial)
Additive Schwarz: advance subdomains in parallel, communicate boundary condition data later
  Typically requires a few more Schwarz iterations, but does not degrade accuracy
  Parallelism helps balance additional cost due to Schwarz iterations
  Applicable to both overlapping and non-overlapping Schwarz
Model PDE:
This talk
Notes: Chris observed ~3x speedup with additive.

## Slide 63
How to Apply Schwarz to Dynamics?
In the literature the Schwarz method is applied to dynamics by using space-time discretizations.
Overlapping non-matching meshes and time steps in dynamics.
Pro : Can use non-matching meshes and time-steps (see right figure).
Con : Unfeasible given the design of our current codes and size of simulations.
Ease of implementation is a very important requirement!

## Slide 64
2 subdomains
4 subdomains
8 subdomains
Overlapping SAM scaling study from 2 to 8 subdomains
Linear elastic cuboid problem, pulled from top at rate of
Overlap size varied: 0.4, 0.2 (above) and 0.1
Same mesh resolution of 0.1 in all subdomains
Linear convergence observed w.r.t. # subdomains
Scaling with Respect to the Number of Subdomains
Generally, we do not target cases with >5-6 subdomains

## Slide 65: Schwarz Extensions to FOM-ROM and ROM-ROM Couplings
65
Choice of domain decomposition
Overlapping vs. non-overlapping domain decomposition?
  Non-overlapping more flexible but typically requires more Schwarz iterations
FOM vs. ROM subdomain assignment?
  Do not assign ROM to subdomains where they have no hope of approximating solution
Snapshot collection and reduced basis construction
Are subdomains simulated independently in each subdomains or together?
Enforcement of boundary conditions (BCs) in ROM at Schwarz boundaries
Strong vs. weak BC enforcement?
  Strong BC enforcement difficult for some models (e.g., cell-centered finite volume, PINNs)
Optimizing parameters in Schwarz BCs for non-overlapping Schwarz?
Choice of hyper-reduction
What hyper-reduction method to use?
  Application may require particular method (e.g., ECSW for solid mechanics problems)
How to sample Schwarz boundaries in applying hyper-reduction?
  Need to have enough sample mesh points at Schwarz boundaries to apply Schwarz

## Slide 66: 3D Linear Elastic Notched Cylinder Problem
66
Geometry is linear elastic notched cylinder pulled from top dynamically to time at rate of with
Demonstration of SAM’s ability to couple disparate meshes, element types and models: TET10 + FOM (notched region) and HEX8 + Linear OpInf with modes (top region)
Linear OpInf trained on snapshots in time
Reproductive problem for now
 | Mean/max # Schwarz iters | Max -disp rel error | Max -disp rel error
FOM-FOM | 5.83/9 |  | 
FOM-OpInf () | 5.09/8 | 2.9e-3 | 4.2e-3
FOM-OpInf () | 5.48/9 | 3.8e-4 | 4.3e-4
FOM-OpInf () | 5.54/9 | 1.3e-4 | 2.2e-4
FOM-OpInf () | 5.52/9 | 3.1e-5 | 3.6e-5
 | Mean/max # Schwarz iters |  | 
FOM-FOM | 5.83/9 |  | 
 | 5.09/8 | 2.9e-3 | 4.2e-3
 | 5.48/9 | 3.8e-4 | 4.3e-4
 | 5.54/9 | 1.3e-4 | 2.2e-4
 | 5.52/9 | 3.1e-5 | 3.6e-5
Key result: regularization parameter influences accuracy & convergence. Coupled models are remarkably accurate! Schwarz is not introducing coupling error/artifacts.
(TET10 + FOM)
(HEX8 + OpInf)
FOM-FOM
FOM-OpInf
Movies above: -displacement solutions for FOM-FOM and FOM-OpInf (, )
Notes: TODO: make movie faster! Try predictive?

## Slide 70
Work in Progress: Accelerating Non-Overlapping Schwarz
Risk: non-overlapping Schwarz can be slow to converge w/ Dirichlet-Neumann TCs.
Mitigation: explore accelerating Dirichlet-Neumann Schwarz via Aitken and Anderson acceleration.
Classical relaxation:
Aitken acceleration:
Anderson acceleration:
from optimization problem
Relax
Aitken
Anderson =1
Anderson =2
Anderson =3
Relax
Aitken
Anderson =1
Anderson =2
Anderson =3
Non-overlapping Dirichlet-Neumann Schwarz
G. Sambataro
5
Aitken acceleration can reduce the # of Schwarz iterations by 3 and has virtually no tuning knobs.
Minimal tuning knobs improves usability.
Notes: TODO: fill in this slide with Giulia’s results.

## Slide 71: Work in Progress: SAM-based Coupling for Non- Intrusive NN-based Models
Motivation: finite deformation mechanics does not admit a polynomial structure
Limits capacity of polynomial-based OpInf models
Approach: Develop a neural-network-based OpInf model-reduction strategy
Can represent general nonlinearities
Enforces structure by designing NN operators to parameterize a positive definite stiffness matrix
Fully differentiable ML software enables standard and dynamics-constrained training
Pros: Enables accurate models for strong nonlinearities
Cons: Higher offline cost
71
FOM-FOM
FOM-SP NN
FOM-QOpInf
Offline (traditional) training
Dynamics-constrained training (rollout)
Training paradigms
NN modeling strategy
Structure is enforced via SPD parameterization of stiffness:
, : NN models for stiffness and boundary forcings
, : Learnable parameters
Future work: Hamiltonian parameterizations
Enforced structure significantly improves performance
s.t.
E. Parish A. Gruber
Notes: Most mechanics problems do not admit polynomial structure, which limits the capacity of linear/quadratic OpInf
We’re developing an NN-based OpInf strategy to overcome these limitations
We’re enforcing structure in the inferred operators by learning structured parameterizations of, e.g., the stiffness matrix. This in general gives far superior accuracy to just using a standard feed forward neural network.
With modern ML software, we can do both a standard training approach as well as an ODE-constrained approach (Ben P.’s group calls this rollouts)
Pros are higher accuracy for complex nonlinear problems, and cons are higher offline training cost.