## Slide 1: Machine Learning Applications for Defeaturing and Model Preparation
Steven Owen, Tim Shead, Shawn Martin, Armida Carbajal
July 25, 2022
Sandia Machine Learning, Deep Learning Workshop
July 25-28, 2022
Albuquerque, NM
SAND2021-8928 C

## Slide 2: Rapid CAD to Simulation with Machine Learning
Example workflow
Break into subsystems for teaming and/or avoid large model size
Remove parts that are irrelevant and not normally modeled for a specific physics
Fix bad geometry
Remove small features
Remove gaps, overlaps, misalignments
Tet mesh
Identify and prepare specific categories of mechanisms (Bolts, Springs, Bearings, etc.)
Compute preloads on bolts, springs, etc.
Prepare input deck
Commercial Truck CAD Model
3545 volumes
81,283 surfaces
208,203 curves
133,461 vertices
2

## Slide 3: Rapid CAD to Simulation with Machine Learning
3
Machine Learning for Analysis Preparation:
Reduce/Eliminate most tedious tasks
Guide user to next step
Present user with smart options
User validates ML-solutions
Standardization between analysts
Commercial Truck CAD Model
3545 volumes
81,283 surfaces
208,203 curves
133,461 vertices

## Slide 4: Rapid CAD to Simulation with Machine Learning
Example workflow
Break into subsystems for teaming and/or avoid large model size
Remove parts that are irrelevant and not normally modeled for a specific physics
Fix bad geometry
Remove small features
Remove gaps, overlaps, misalignments
Tet mesh
Identify and prepare specific categories of mechanisms (Bolts, Springs, Bearings, etc.)
Compute preloads on bolts, springs, etc.
Prepare input deck
Defeaturing for Meshing
1
Classification and Reduction
2
4
Commercial Truck CAD Model
3545 volumes
81,283 surfaces
208,203 curves
133,461 vertices

## Slide 5: Defeaturing
32,559 tets
397,258 tets
CAD part from designer
Defeaturing
90 CAD operations performed in Cubit by "expert" user
CAD part for simulation
595 surfaces
1506 curves
994 vertices
5

## Slide 6: Machine Learning driven Defeaturing
Predict local mesh quality
  Scaled Jacobian
  In-Radius
  Deviation
Find the most problematic features in the CAD Model
1
For a given local geometry operation
  Collapse Curve
  Remove Surface
  Blunt Tangency
  Etc..
Predict local mesh quality after operation
  Scaled Jacobian
  In-Radius
  Deviation
Find solution that yields best mesh quality
2
For a given local topology
  Small Curve
  Small Surface
  Sharp Angle at Vertex
6

## Slide 7: Example defeaturing operations
remove surface
tweak replace surface
composite surfaces
collapse curve
tweak remove topology curve
tweak remove topology surface
remove cone
blunt tangency
begin state
end state
begin state
end state
7

## Slide 8: Machine Learning for Defeaturing
Machine Learning
8
Output: Mesh
quality metrics
“labels”
32,559 tets
Input: CAD Model
Local geometry/topology
“features”

## Slide 9: Machine Learning for Defeaturing
Machine Learning Methods
.csv file
Machine Learning
Models
Training Data
Characterize problems
  Features
  Labels
Python Script + Cubit
Train many CAD models
Diverse problems
One row in .csv per problem
Non-runtime
scikit-learn
Python open source
Machine Learning libraries
Ensembles of Decsion Trees (EDT)
Make predictions
Small Binary
Used Run-time in C++ Code
Access via C-Python interface
9

## Slide 10: Training Data Features
Curve Length
Surface Area
Angle at vertex
Angle at curves
Valence at vertex
Number of loops
Hydraulic Radius
Etc…
Topology-Based Features
10

## Slide 11: Training Data Labels
Scaled Jacobian
Function of angles at vertices
Scaled -1.0 to 1.0
Independent of mesh size
Ratio with equilateral tet with target edge length
Scaled 0.0 to 1.0
Sensitive to mesh size
In-Radius Ratio
r
triangle/quad
geometry
deviation
Deviation
Distance from triangle centroid to closest point on geometry
Scaled by target mesh size
Ensure mesh "matches" geometry
11

## Slide 12: Training Data Labels
Small Curve
12

## Slide 13: Training Data Labels
Small Curve
13

## Slide 14: Training Data Labels
Local Tets at Geometric Curve
Topology
Small Curve
14

## Slide 15: Training Data Labels
Before
After
Min SJ = 0.250
Min SJ = 0.227
Min IR = 0.027
Min IR = 0.267
Scaled Jacobian
In-radius
15
Collapse Curve
Before
After
Collapse Curve

## Slide 16: Machine Learning Study
94 single-part CAD models
16
Owen, Steven; Shead, Timothy M.; Martin, Shawn , “CAD Defeaturing Using Machine Learning”, 28th International Meshing Roundtable (IMR), Buffalo, New York, USA, October 14-17, 2019
Patent Granted March 2022

## Slide 17: Machine Learning Study – EDT (Ensembles of Decision Trees)
Scaled Jacobian
Scaled In-radius
Scaled Deviation
Mean Absolute Error (MAE)
17

## Slide 18: Defeaturing for Meshing Example
18

## Slide 19: Rapid CAD to Simulation with Machine Learning
19
Machine Learning for Analysis Preparation:
Defeaturing
  Predicts potential problems in mesh
  Predicts tools that will best improve
  Allows user to select and validate
Part Classification
  Identifies common mechanism types
  Tools to quickly reduce to analysis-ready
  In-situ training on user-defined categories
Commercial Truck CAD Model
3545 volumes
81,283 surfaces
208,203 curves
133,461 vertices