## Slide 1: Safety for Learning-based Differentiable Predictive Control
Wenceslao Shaw Cortez, Data Scientist
w.shawcortez@pnnl.gov
Jan Drgona, Aaron Tuor, Mahantesh Halappanavar, Draguna Vrabie

## Slide 2: Motivation: Safety-Critical Control
Increased automation in human environments
  Robots
  Automated vehicles
Prevent system damage
Task specifications (not just stability)
Safety is Critical

## Slide 3: Model Predictive Control (MPC)
Model Predictive Control
Advanced optimal control
First devised for process control in 1970’s
Handles constraints and optimality
Computationally expensive
Cost:
Model:
Constraints:

## Slide 4: Differentiable Predictive Control (DPC)
From data to optimized control policy
MPC
DPC
Drgona, Jan, Karol Kis, Aaron Tuor, Draguna Vrabie, and Martin Klauco. “Deep Learning Alternative to Explicit Model Predictive Control for Unknown Nonlinear Systems.” 2021. http://arxiv.org/abs/2011.03699.
  Theoretical connection with MPC
  Offline computation, no online optimization
  Time-varying reference/constraints
Handles constraints and optimality
Computationally expensive

## Slide 5: Differentiable Predictive Control (DPC)
From data to optimized control policy
  Limited guarantees of stability/constraint satisfaction
  No robustness to perturbations (e.g. model uncertainty)
Drgona, Jan, Karol Kis, Aaron Tuor, Draguna Vrabie, and Martin Klauco. “Deep Learning Alternative to Explicit Model Predictive Control for Unknown Nonlinear Systems.” 2021. http://arxiv.org/abs/2011.03699.
  Theoretical connection with MPC
  Offline computation, no online optimization
  Time-varying reference/constraints

## Slide 6: Zeroing Control Barrier Functions (ZCBFs)
Define a ‘corrective action’ to ensure safety
System dynamics:
Barrier function and safe set:
Provides robustness to perturbations
Safety control:
Ames, A.D., X. Xu, J.W. Grizzle, and P. Tabuada. “Control Barrier Function Based Quadratic Programs for Safety Critical Systems.” IEEE Transactions on Automatic Control 62, no. 8 (2017): 3861–76.
subject to:
Aim: Combine with DPC for guaranteed safety

## Slide 7: ZCBF Implementation
Nominal Control
Nominal + Proposed Control
subject to:
  Barrier function implementation
  QP-based controller
  Allows any desired control to be implemented
Extension:
Time-varying constraints
Sampled-data systems
Minimally invasive for reduced computation

## Slide 8: Modified ZCBFs+DPC
Time-varying constraints
“Ring” condition, reduces use of computational resources
Sampled-data result
ZCBF+DPC Controller:
(t)
Type equation here.
subject to:
If :
If :
Time slice
*if DPC is trained ‘properly’, the ZCBF never interferes
*Ensures robustness and safety

## Slide 9: DPC: Training with Barriers
Type equation here.
DPC
Finite-difference approximation:
Barrier Condition:
  Software products:
  https://github.com/pnnl/neuromancer
  https://github.com/pnnl/slim

## Slide 10: ZCBF and DPC Implementation
Barrier only
DPC only (poorly trained)
ZCBF+DPC (poorly trained)
ZCBF+DPC (ideally trained)

## Slide 11: Future Directions
Extend to more general systems, higher order:
Synthesize ZCBFs via learning methods with guarantees
Certify safety for learning-based controllers

## Slide 12: Implementation
Demonstration 1: Nominal Control Only

## Slide 13
Demonstration 2: Proposed Control Law