## Slide 1: Using Reinforcement Learning to Control Grid Operation from Near-blackout to High Stability while Continuing to Serve Load
Stephen J. Verzi, Ross Guttromson, Ace Sorensen, Birk Jones
Sandia National Laboratories
2022 Machine Learning / Deep Learning Workshop
July 25-28, 2022
SAND2022-9013 PE
This work is currently funded through the DOE/OE Advanced Grid Modernization (AGM) Program under the guidance of Dr. Ali Ghassemian.

## Slide 2: Problem Statement and Solutions Researched
  Grid operating security studies are typically employed to establish operating boundaries, ensuring secure and stable operation for a range of operations under NERC guidelines. However, if these boundaries are violated, the existing system security margins will be largely unknown. As an alternative to the use of complex optimizations over dynamic conditions, this work employs the use of reinforcement-based machine learning to identify a sequence of secure state transitions which place the grid in a higher degree of operating security with greater static and dynamic stability margins. The approach requires the training of a machine learning agent to accomplish this task using modeled data and employs it as a decision support tool under severe, near- blackout conditions.

## Slide 3: Outline
  Project Purpose
  Technical Approach
  Results
  Conclusions/Summary
  Future Work
  Acknowledgments and Contacts

## Slide 4: Project Objective and Purpose
In the infrequent occurrence when grid operations depart from planned criteria, how do we move to a ‘good’ operating point?
Where are we? Where do we want to go? What path do we take?
During near blackout conditions, grid operators may have an opportunity to restore the system to a safe condition if a real-time decision support tool is available.
This project investigates the development of a real-time decision support tool for that purpose.
Image from North American Electric Reliability Corporation (NERC), Reliability Concepts document, pg 40.

## Slide 5: General Method
The solution method uses Deep Neural Networks (DNNs) to represent the sequence of control actions and dispatches needed for the grid to increase its stability margins.
Our approach offers the potential of a speedy solution to this problem, with a low risk of non-convergence. The solution will not be proven optimal, although it will be demonstrated to be feasible and ‘good’ during off-line testing.
Based on recent work conducted at Sandia
Markov decision process (MDP):
(states, actions, transition function, reward function)

## Slide 6: General Method
The solution method uses Deep Neural Networks to represent the sequence of control actions and dispatches needed for the grid to increase its stability margins.
Our approach offers the potential of a speedy solution to this problem, with a low risk of non-convergence. The solution will not be proven optimal, although it will be demonstrated to be feasible and ‘good’ during off-line testing.
Based on recent work conducted at Sandia
DQN
Discrete 3D grid sample navigation environment

## Slide 7: Defining the State Space and Security Metrics
  We started with data sampled from a 3 generator system model (ℛ^3 control dimensions) and associated multi-dimension security scores
Proof-of-concept: power grid model (ℛ^3)
Security Metrics
Bus Voltage
Line Flow
Transient Stability
Small Signal Stability
Normalize each such that
1 is feasible,
0 is failure, and
between 0 and 1 is penalty

## Slide 8: Actions and State Transitions
  Actions (7)
    Increase/decrease single generator output or keep all the same
    For 3 control dimensions (G1, G2, G3) the action set is
      {stay, decrease G1, increase G1, decrease G2, increase G2, decrease G3, increase G3}
    In the 3D visualizations this set is
      {stay, backward, forward, left, right, down, up}
  State Transitions
    Effect on grid state managed by power flow model
    Exhaustively sampled using 25 discrete values (i.e., cardinality of state space is 25^3)

## Slide 9: Reward Objective Function
Feasibility of state
Load for (dispatch) state
  , then re-normalize
  , then re-normalize

## Slide 10: Security / Stability Metrics
Overlapping Power Grid Stability Level Curves
Individual Power Grid Stability
Level Curves

## Slide 11: Security / Stability -> Reward Objective
2D Slice of Reward (Learning Objective)
Overlapping Power Grid Stability Level Curves

## Slide 12: Security / Stability -> Reward Objective
2D Slice of Reward (Learning Objective)
Overlapping Power Grid Stability Level Curves

## Slide 13: Security / Stability -> Reward Objective
2D Slice of Reward (Learning Objective)
Overlapping Power Grid Stability Level Curves

## Slide 14: Feasibility (3D) & Reward (2D slice) Objective
3D Reward Space
2D Slice of Reward (Learning Objective)
Optimum (3D) discretized feasible load is at (2.24,0.80,2.88)

## Slide 15: Feasibility (3D) & Reward (2D slice) Objective
3D Reward Space
2D Slice of Reward (Learning Objective)
Optimum (3D) discretized feasible load is at (2.24,0.80,2.88)

## Slide 16: Feasibility (3D) & Reward (2D slice) Objective
3D Reward Space
2D Slice of Reward (Learning Objective)
Optimum (3D) discretized feasible load is at (2.24,0.80,2.88)

## Slide 17: Learning Results (Objective )
Results in discretized 25x25x25 navigation space (15,000 episodes)
Optimum (3D) discretized feasible load is at (2.24,0.64,3.04) & (2.24,0.80,2.88)
Final state | Trained RL agent | Random player | Greedy player
Penalty | 39.4% | 38.5% | 35.4%
Failure | 2.0% | 43.4% | 0.0%
Feasible | 58.6% | 18.2% | 64.6%
Optimum / Feasible | 451 / 3038 | 1 / 941 | 384 / 3348
Feasible: all stabilities are >= 1.00
Failure: any stability is <= 0.00
Penalty: all other states
Total % | Category
31.8 | Feasible (green)
35.1 | Failure (red)
33.2 | Penalty (yellow)
15625
4968
5477
5180
episode = 50 actions
Training Progress
episode
final reward

## Slide 18: Learning Results (Objective )
Results in discretized 25x25x25 navigation space (15,000 episodes)
Optimum (3D) discretized feasible load is at (2.24,0.64,3.04) & (2.24,0.80,2.88)
Final state | Trained RL agent | Random player | Greedy player
Penalty | 0.1% | 37.7% | 1.7%
Failure | 2.2% | 44.1% | 0.0%
Feasible | 97.7% | 18.2% | 98.3%
Optimum / Feasible | 445 / 5061 | 0 / 943 | 443 / 5092
Feasible: all stabilities are >= 1.00
Failure: any stability is <= 0.00
Penalty: all other states
Total % | Category
31.8 | Feasible (green)
35.1 | Failure (red)
33.2 | Penalty (yellow)
15625
4968
5477
5180
episode = 50 actions
Training Progress
episode
final reward

## Slide 19: Learning Results (Objective )
Results in discretized 25x25x25 navigation space (15,000 episodes)
Optimum (3D) discretized feasible load is at (2.24,0.64,3.04) & (2.24,0.80,2.88)
Final state | Trained RL agent | Random player | Greedy player
Penalty | 0.1% | 39.0% | 1.7%
Failure | 1.5% | 43.8% | 0.0%
Feasible | 98.4% | 17.2% | 98.3%
Optimum / Feasible | 398 / 5096 | 1 / 890 | 443 / 5092
Feasible: all stabilities are >= 1.00
Failure: any stability is <= 0.00
Penalty: all other states
Total % | Category
31.8 | Feasible (green)
35.1 | Failure (red)
33.2 | Penalty (yellow)
15625
4968
5477
5180
episode = 50 actions
Training Progress
episode
final reward

## Slide 20: Learning Results (Objective w/ Prioritized Replay)
Results in discretized 25x25x25 navigation space (15,000 episodes)
Optimum (3D) discretized feasible load is at (2.24,0.64,3.04) & (2.24,0.80,2.88)
Final state | Trained RL agent | Random player | Greedy player
Penalty | 0.0% | 39.0% | 1.7%
Failure | 1.3% | 44.1% | 0.0%
Feasible | 98.7% | 16.9% | 98.3%
Optimum / Feasible | 593 / 5115 | 1 / 876 | 443 / 5092
Feasible: all stabilities are >= 1.00
Failure: any stability is <= 0.00
Penalty: all other states
Total % | Category
31.8 | Feasible (green)
35.1 | Failure (red)
33.2 | Penalty (yellow)
15625
4968
5477
5180
episode = 50 actions
Training Progress
episode
final reward

## Slide 21: Learning Results – Reward and Load Served ()
Percent of optimal and penalized final load served (15,000 episodes)
Penalized final load served
Final state | Trained RL agent | Random player | Greedy player
Average percent of optimal load served | 56.7% | 13.7% | 59.8%
Optimal (3D) discretized feasible load is 6.167

## Slide 22: Learning Results – Reward and Load Served ()
Percent of optimal and penalized final load served (15,000 episodes)
Penalized final load served
Final state | Trained RL agent | Random player | Greedy player
Average percent of optimal load served | 93.3% | 13.8% | 89.4%
Optimal (3D) discretized feasible load is 6.167

## Slide 23: Learning Results – Reward and Load Served ()
Percent of optimal and penalized final load served (15,000 episodes)
Penalized final load served
Final state | Trained RL agent | Random player | Greedy player
Average percent of optimal load served | 94.6% | 12.9% | 89.4%
Optimal (3D) discretized feasible load is 6.167

## Slide 24: Learning Results – Reward and Load Served ()
Percent of optimal and penalized final load served (15,000 episodes, w/ prioritized replay)
Penalized final load served
Final state | Trained RL agent | Random player | Greedy player
Average percent of optimal load served | 92.9% | 12.8% | 89.4%
Optimal (3D) discretized feasible load is 6.167

## Slide 25: Feasibility Space – 3D Navigation
Discretized 25x25x25 feasibility space (, , and )
Optimum (3D) discretized feasible load is at (2.24,0.80,2.88)

## Slide 26: Example 3D Navigation ()
Example navigation for 3 different starting states (15,000 episodes)

## Slide 27: Example 3D Navigation ()
Example navigation for 3 different starting states (15,000 episodes)

## Slide 28: Example 3D Navigation ()
Example navigation for 3 different starting states (15,000 episodes)

## Slide 29: Example 3D Navigation ()
Example navigation for 3 different starting states (15,000 episodes, w/ prioritized replay)

## Slide 30: Example 3D Navigation Movie ()
Example navigation for 3 different starting states (15,000 episodes)

## Slide 31: Example 3D Navigation Movie ()
Example navigation for 3 different starting states (15,000 episodes)

## Slide 32: Example 3D Navigation Movie ()
Example navigation for 3 different starting states (15,000 episodes)

## Slide 33: Example 3D Navigation Movie ()
Example navigation for 3 different starting states (15,000 episodes, w/ prioritized replay)

## Slide 34: Conclusions
We demonstrated the feasibility of this approach
We verified that reinforcement learning can better achieve objectives than
  Random state walk
  Greedy state transition
Higher-fidelity navigation requires more training
Recent paper accepted and presented at IEEE KPEC 2022
  Presenting at IEEE PES GM (July 19th)
  Other manuscripts in progress

## Slide 35: Future Work
Scalability of State Space Dimensions- Map reduction without losing fidelity
Modify solution from discrete space to continuous space
Evaluation of tool across multiple scenarios – Checking solution accuracy against many constraints
Use of Transfer Learning – Allows a DNN to be trained for a specific system without starting from a blank DNN
DNN partitioning – Provides metadata, allowing insights into each solution (geography, type of security constraint, etc.)

## Slide 36: Our Team – Sandia
  Stephen J. Verzi (co-PI)
  Ross Guttromson (co-PI)
  Asael “Ace” Sorensen (deep reinforcement machine learning)
  Christian “Birk” Jones (grid modeling)
  The authors would like to acknowledge project support and sponsorship by Dr. Ali Ghassemian of the Department of Energy’s (DOE) Office of Electricity (OE) Advanced Grid Modeling (AGM) program.
Sandia National Laboratories is a multimission laboratory managed and operated by National Technology and Engineering Solutions of Sandia LLC, a wholly owned subsidiary of Honeywell International Inc. for the U.S. Department of Energy’s National Nuclear Security Administration under contract DE-NA0003525.

## Slide 37: Thank You
  Questions?
References
Y. Zhou, B. Zhang, C. Xu, T. Lan, R. Diao, D. Shi, Z. Wang, and W. Lee "A data-driven method for fast AC optimal power flow solutions via deep reinforcement learning," Journal of Modern Power Systems and Clean Energy, vol. 8, no. 6, pp. 1128-1139, 2020. https://doi.org/10.35833/MPCE.2020.000522
Y. Zhang, J. Wu, Z. Chen, Y. Huang, and Z. Zheng, "Sequential node/link recovery strategy of power grids based on Q-learning approach," in 2019 IEEE International Symposium on Circuits and Systems (ISCAS), pp. 1-5, 2019. doi: 10.1109/ISCAS.2019.8702107
M. Mandich, "Power System Stability Assessment with Supervised Machine Learning," Masters thesis, University of Tennessee, 2021.
Power System Toolbox. (2008). Cherry Tree Scientific Software.
J. D. Glover, M. S. Sarma, and T. Overbye, Power System Analysis & Design, SI Version. Stamford, CT: Cengage Learning, 2012. ISBN: 978-1-111-42579-1
P. Kundur, Power System Stability and Control. New York, NY: McGraw-hill, 1994. ISBN: 978-0-070-35948-1
C. J. Watkins and P. Dayan, "Q-learning," Machine learning, vol. 8, no. 3-4, pp. 279-292, 1992. https://doi.org/10.1007/BF00992698
V. Mnih, K. Kavukcuoglu, D. Silver, A. Graves, I. Antonoglou, D. Wierstra, and M. Riedmiller, "Playing atari with deep reinforcement learning," arXiv preprint arXiv:1312.5602, 2013.
T. Bailey, J. Johnson, and D. Levin, "Deep reinforcement learning for online distribution power system cybersecurity protection," in 2021 IEEE International Conference on Communications, Control, and Computing Technologies for Smart Grids (SmartGridComm), pp. 227-232, 2021. https://doi.org/10.1109/SmartGridComm51999.2021.9631991
A. Paszke et al., "Pytorch: An imperative style, high-performance deep learning library," Advances in neural information processing systems, vol. 32, pp. 8026-8037, 2019.
R. S. Sutton, and A. G. Barto, Reinforcement Learning: An Introduction, Cambridge, MA: A Bradford Book, 2018. ISBN: 978-0-262-03924-6
Verzi, S., Guttromson, R., & Sorensen, A. (2022). “Using Reinforcement Learning to Increase Grid Security Under Contingency Condition,” To appear in the proceedings of the Kansas Power & Energy Conference (KPEC) 2022. https://www.kpec-ksu.org/program.