## Slide 1: Conditional Diffusion Models for Interlocking Metasurface Design
Sandia National Laboratories
Nathan Brown (5575), Benjamin Young (1851), Brad Boyce (1800), Philip Noell (1851)
Presented by Nathan Brown – nkbrown@sandia.gov
SAND2024-09712C

## Slide 2: What are interlocking metasurfaces (ILMs)?
Robust
Architected
Non-Permanent
Integrated
joining technology
suitable for
complex surfaces
dissimilar materials
extreme environments
(Bolmin 2023)
ILMs overcome many limitations of existing joining methods
(Brown 2023)

## Slide 3: Tailoring Material Properties
Mechanical and thermal properties controlled by ILM’s unit cell design, constitutive material, and unit cell interaction
3
2
1
0
0
10
5
Effective Tensile Strain (%)
Effective Tensile Stress (MPa)
Tension
Sliding T-slots
Snapping T-slots
Failure Criteria
Stress Uniformity
Von Mises Stress
(MPa)
Thermal Manipulation

## Slide 4: How do we design ILMs?
Human Intuition
Parametric Optimization
Genetic Algorithm
“Sliding T-slot”
Based on designer’s expertise
No additional optimization
Parameterized T-slot
Gradient-based optimization
Maximize Strength: Tension, Shear, Weighted-sum
Feasible Designs
Evolutionary optimization
16x8 mirrored discretized design domain
Single and Multi-Objective Optimization (Tension/Shear)
Feasible Designs
Iterative Evolution
Side A
Side B
Side A
Side B
Side A
Side B
Pros: Fast, Simple
Cons: Biased, Not generalizable
Pros: Data-driven, Efficient
Cons: Domain restricted, Not generalizable, Local optima
Pros: Gradient-free, greater design freedom
Cons: Inefficient, Not generalizable
Can we implement a generalizable tool to rapidly design ILMs with customizable thermo-mechanical properties???

## Slide 5: Conditional Diffusion Models (CDMs)
Conditional Diffusion Model: Generative AI method to generate data by iteratively refining random noise, guided by specific conditions or inputs, to produce highly realistic/practical outputs
Used for “text-to-art” generation
(MidJourney)
(Gemini)
Text Description
Testing
Training
“Front facing photo of large breed dog”

## Slide 6: CDMs as an Engineering Design Tool
Use the denoising process to go from complete noise to a viable design candidate
Replace “text-description” with performance criteria  Desired Thermo-mechanical properties
Sequentially add Gaussian noise over T timesteps
Sequentially denoise via diffusion model over T timesteps
Model Training
Model Testing
Desired Thermo-Mechanical Properties
Thermo-mechanical properties

## Slide 7: Generating Training Data
Training data comprised of ILM unit cell design and corresponding thermo-mechanical properties
  Randomly generated ~18k designs and determine properties using finite element analysis (FEA)
  Voxelized 12x12 design domain, each element either Macor, Al6061, or void
Thermo-Mechanical Properties
1. Tensile Resultant Force
3. Heat Mitigation
Top surface resultant force at material yielding
Top surface resultant force at material yielding
Average bottom surface nodal temperature
Macor
Al6061
Macor
Al6061
Macor
Al6061
2. Shear Resultant Force
Heat to 500 °C
Free Convection

## Slide 8: Putting the “Conditional” in CDM
Conditions determined based on thermo-mechanical responses of 18k training samples
Set up Magnitude, Angle, Thermal conditions for each design  40 Total Conditions  [0,39]
   4 Magnitude Conditions  [0,3]
   5 Angle Conditions  [0,4]
   2 Thermal Conditions -> [0,1]
Increasing Magnitude Condition
Increasing Angle Condition
0
1
2
3
0
1
2
3
4

## Slide 9: Generalized Design Generation
The ability to achieve desired properties was highly condition dependent
  Generally, more training samples results in better predictions
The model was prompted to generate designs based on 500 random condition numbers
  Generate design via CDM  Tested Design via FEA  Compare FEA result to condition bounds
Conditions | Avg. Success Rate
All Conditions | 61.4%
Angle | 76.4%
Magnitude | 82.5%
Thermal | 95.9%
All Conditions
Heat Transfer
Angle
Magnitude

## Slide 10: “Pareto Front” Approach – 40 conditions
Testing the model to produce extremes results in plethora of high performing design solutions
Able to produce designs with high mechanical strength while achieving varying thermal responses

## Slide 11: Insight into designing ILMs
Rapidly producing ILM designs with custom thermo-mechanical properties can guide/inspire human designers when implementing ILMs
  Taller, more dendritic  Strong in tension
  Shorter, studier  Strong in shear
  More Al6061  Higher Temps/More Conductive
Tension Dominated
Balanced
Shear Dominated
High Temps/Conductive
Low Temps/Resistive
Macor
Al6061
Macor
Al6061
Macor
Al6061
Macor
Al6061
Macor
Al6061
Macor
Al6061

## Slide 12: Conclusions
Interlocking metasurfaces (ILMs) are a mechanically robust, non-permanent, environmentally durable alternative to traditional joining technologies
ILMs’ mechanical and thermal properties are dependent on feature topology
Conditional diffusion models can rapidly design ILM unit cells with customizable thermo-mechanical properties, but can be influenced by the variability in training data
Used as a stand-alone design tool or used to influence human designers

## Slide 13: Thank you!
I look forward to your question!
Nathan Brown – nkbrown@sandia.gov