## Slide 1: SOS Workshop 2000 Interconnect Technology Session
Roland Paul
Supercomputing Systems AG
Tnet

## Slide 2: Tnet Switch: Technical data
12 port full crossbar switch
100 + 100 MB/s per link (MPI data)
Micropackets (max. 128 Bytes)
64k computational nodes
Very low error rate (BER <10-19)
Multicast routing
Any topology possible (switch prevents deadlocks)
Remote configurable
Network performance monitoring

## Slide 3: Tnet Features
Expandability
  Standard electrical to optical Adapters
Remote managebility
  Switch can be updated and configured remotely
One communication subsystem
  MPI and Hardware developed together
Reliability
  The T-Net retransmission protocol
Performance
  MPI multicast on the network
  Address translation on NIC
  micropackets
Flexibility
  Any Network topology possible

## Slide 4: Tnet retransmission protocol
Transmission
Data
Received
Data
Buffer
Buffer
Controller
CRCC
Buffer
Buffer
Controller
Virtual backchannel
for Acknowledges or Retransmission commands
Gigabit
Transmission

## Slide 5: Swiss-T1 Baby
Reliability:
  Installed: August 99
  Accepted: October 99
  Crashes since acc.: 0
  unscheduled downtime: 0 %
Performance:
  MPI bandwidth: 50 MB/s
  MPI latency: 20 s
  The application performance measured was equal to CPlant/Siberia and close to Quadrics/AlphaServer SC

## Slide 6: Swiss-T1: Current Tnet machine
64 21264@500MHz
32 GB Main Memory
32 Bit TNet NIC:
  75 MB/s
  18 s
64 Bit TNet NIC:
  180 MB/s bidir.
  13 s

## Slide 7
Tnet Expandability
Plug and play electrical to optical interface (MIA)

## Slide 8: Tnet Remote managebility
Powerswitch
Terminal server
Tnet Switch

## Slide 9: Tnet Summary
A high reliability of the Tnet HW and SW was shown on the Swiss-T1 Baby
The Application performance in Swiss-T1 Baby is comparable to other clusters
The Network performance of Swiss-T1 with Tnet64 NIC will be 300% higher than Baby
MPI implementation verified with Intel suite
Going optical is easy and relatively inexpensive
The network topologies with rings are allowed and actually work