## Slide 1
The Status of Clusters at LLNL
Bringing Tera-Scale Computing to a Wide Audience at LLNL and the Tri-Laboratory Community
Mark Seager
Fourth Workshop on Distributed Supercomputers
March 9, 2000

## Slide 2: Overview
Architecture/Status of Blue-Pacific and White
  SST Hardware Architecture
  SST Software Architecture (Troutbeck)
  MuSST Software Architecture (Mohonk)
  Code development environment
  Technology integrations strategy
Architecture of Compaq clusters
  Compass/Forest
  TeraCluster98
  TeraCluster2000
Linux cluster

## Slide 3: SST Hyper-Cluster Architecture
Sector S
Sector Y
Sector K
24
24
24
Each SP sector comprised of
488 Silver nodes
24xTB3 links to 6xHPGN
System Parameters
3.89 TFLOP/s Peak
2.6 TB Memory
62.5 TB Global disk
6 HPGN
HiPPI
2.5 GB/node Memory
24.5 TB Global Disk
8.3 TB Local Disk
1.5 GB/node Memory
20.5 TB Global Disk
4.4 TB Local Disk
1.5 GB/node Memory
20.5 TB Global Disk
4.4 TB Local Disk
FDDI
6
6
12
High-speed external connections
6xTB3 @ 150 MB/s bi-dir
12xHIPPI-800 @ 100 MB/s bi-dir
6xFDDI @ 12.5 MB/s bi-dir

## Slide 4: I/O Hardware Architecture of SST
System Data and Control Networks
488 Node IBM SP Sector
56 GPFS
Servers
432 Thin Silver Nodes
Each SST Sector
Has local and two global I/O file systems
2.2 GB/s delivered global I/O performance
3.66 GB/s delivered local I/O performance
Separate SP first level switches
Independent command and control
Full system mode
Application launch over full 1,464 Silver nodes
1,048 MPI/us tasks, 2,048 MPI/IP tasks
High speed, low latency communication between all nodes
Single STDIO interface
GPFS
GPFS
GPFS
GPFS
GPFS
GPFS
GPFS
GPFS
24 SP Links to
Second Level
Switch

## Slide 5: LoadLeveler Pool Layout Geared Toward Servicing Large Parallel Jobs
PBATCH
393
GPFS Servers 56
System
5
PDEBUG 32
Login
2
PBATCH
425
GPFS Servers 56
System
5
Login
2
PBATCH
425
GPFS Servers 56
System
5
Login
2
HPGN
K
S
Y
Each sector independently scheduled
  Cross sector runs accomplished by dedicating nodes to the user/job
Normal production limited to size constraints of single PBATCH partition. Can only support THREE simultaneous 256 jobs!
  S = 425 = 256 + 128 + 41
  K = 425 = 256 + 128 + 41
  Y = 393 = 256 + 128 + 9

## Slide 6: I/O Hardware Architecture of MuSST (PERF)
512 NH-2 Node IBM SP
16 GPFS
Servers
484 NH-2 PBATCH Nodes
MuSST (PERF) System
4 Login/Network nodes w/16 GB SDRAM
8 PDEBUG nodes w/16 GB SDRAM
258 w/16GB, 226 w/8GB PBATCH nodes
12.8 GB/s delivered global I/O performance
5.12 GB/s delivered local I/O performance
24 Gb Ethernet External Network
Programming/Usage Model
Application launch over ~492 NH-2 nodes
16-way MuSPPA, Shared Memory, 32b MPI
4,096 MPI/US tasks, 8,192 MPI/IP tasks
Likely usage is 4 MPI tasks/node with 4 threads/MPI task
Single STDIO interface
GPFS
GPFS
GPFS
GPFS
GPFS
GPFS
GPFS
GPFS
8 NH-2 PDEBUG Nodes
Login
Net
Jumbo
NFS/Login
Login
Net
Jumbo
NFS/Login
Login
Net
Jumbo
NFS/Login
Login
Net
Jumbo
NFS/Login
System Data and Control Networks
Notes: This new baseline reflects the new baseline I/O configuration as of 2/29/2000
Each Login/Network node has six Gb Enets. Two Gb Enets are in the PCI slots on the NH-2 node and do not support transfers with jumbo frames (login traffic and slower FTP). Four other Gb Enets are installed in two RIO drawers and will be dedicated to FTP traffic over sub-nets at LLNL that support jumbo frames. This is specifically targeted at the SGI visualization services and also the archive.

## Slide 7: TeraCluster System Architecture
QSW, Gb EtherNet, 100BaseT EtherNet
128x4 Node 0.683 TF Sierra System
~12 CFS
Servers
~114 Regatta Compute Nodes
System I/O Requirements
<10 ms, 200 MB/s MPI latency and Bandwidth over QSW
Support 64 MB/s transfers to Archive over Gb-Enet and QSW links
19 MB/s POSIX serial I/O to any file system
  except to local OS and swap
Over 7.0 TB of global disk in RAID5 with hot spares
0.002 B/s/F/s = ~1.2 GB/s delivered parallel I/O performance
  MPI I/O based performance with a large sweet spot
  64 < MPI tasks < 242
Separate QSW, Gb and 100BaseT EtherNet networks
  GFE Gb EtherNet switches
Consolidated consoles
CFS
CFS
CFS
CFS
~2 Login nodes
with Gb-Enet
Fail-Over
Fail-Over
CFS
CFS
Fail-Over
Final Config
August2000

## Slide 8: Phase1 TeraCluster System HW/SW Architecture
1x128 QSW & 4x32 CFS Node Sierra System
~30 Regatta Compute Nodes in each CFS partition
System Architecture
ES40 compute nodes have 4 EV67 @ 667 MHz and 2 GB memory
ES40 login nodes have 4 EV67 @ 667MHz and 8 GB memory
Support 64 MB/s transfers to Archive over Gb-ENet
19 MB/s POSIX serial I/O to local file system
CFS ONLY used for system functions. NFS home directories
Three 18.2 GB SCSI local disks for system images, swap, /tmp and /var/tmp
Consolidated consoles
JURA Kit 48
1 CFS
Server
CFS
RMS/QSW and CFS Partitions
Switch is 128-way
Single RMS partition for capability (and capacity)
  Running with three partitions (64, 42, 14)
Current CFS only scales to 32-way partition
CFS
Fail-Over
CFS
CFS
Fail-Over
CFS
CFS
Fail-Over
CFS
CFS
Fail-Over

## Slide 9: Smaller Clusters at LLNL
IBM GA clusters
  Blue - 442 Silver node (1,768xPPC604@332MHz) TB3 switch system on Open Network
  Open/Classified HPSS servers
IBM Technology Integration, Support & Prototype Clusters
  Baby – 8 Silver Wide – Problem isolation and SW eval
  ER – 24 Silver Thin & 4 Silver Wide - hot spares, workload simulators
  16 THIN2 nodes – System admin
  Snow – 16 NH-1/Colony/Mohonk (128xPower3@210MHz) prototype
Compaq GA
  TeraCluste98 – 24 DS40 (96xEV56@500MHz) - Open network
  Compass – 8 DS8400 (80xEV5@440MHz) - Open network
  Forest – 6 DS8400 (60xEV56@500MHz) - SCF
  SierraCluster – 38 ES40 (152xEV67@667MHz) - SCF
Compaq Technology Integration, Support and Linux Clusters
  SandBox – 8 ES40 (EV6@500MHz) - Problem isolation and SW eval
  LinuxCluster – 8 ES40 (EV6@500MHz) - Linux development