## Slide 1
HPC at CEA/DAM
The TERA 1 super computer
RFP 06/1999
Order to COMPAQ 02/2000
Intermediary machine .5 Tflops
  delivered 12/2000
  open to use 02/2001
  fully operational 06/2001
  (CRAY T90 stoped)
Final machine 5 peak teraflops
  power on 4/12/2001
  1.13 TF sustained 13/12/2001
  3.98 LINPACK 04/2002 4 on TOP500
  open to all users 09/2002
  fully operational 12/2002
  (Intermediary machine stoped)
Jean Gonnord
Program Director for Numerical Simulation
CEA/DAM
Thanks to Pierre Leca, François Robin
And all CEA/DAM/DSSI Team

## Slide 2: TERA 1 Supercomputer
December 2001
608(+32)*4 (1 Ghz)
5 Tflops
(1 Tflops)
3 TB
50 TB
(7.5 GB/s)
600 kW
Installation
Nodes
Peak performance
(sustained requested)
Main Memory
Disks
(Bandwidth)
Power
Main features
170 frames, 90 km of cables
608 compute nodes
50 TB of disks
Compute
Node
Compute
Node
Compute
Node
Compute
Node
Compute
Node
Compute
Node
I/O
Node
I/O
Node
I/O
Node
32 I/O nodes

## Slide 3: Key elements of the TERA computer
608 computational nodes – 8 Glops
(4 processors per node)
800 disks
72 Gb
36 switches
2560 links at 400 Mb/s

## Slide 4
Each link
represents
8 cables
(400 MB/s)
64 ports
to nodes
80 ports
to lower
level
64 ports
to higher
level
QSW Networks (dual rail)
36 switches (128 ports) - 2560 links

## Slide 5: TERA Benchmark
Euler Equations of gaz dynamics solved in a 3D Eulerian mesh
December 12, 2001 : 1,32 Tflops on 2475 processors 10 billion cells
A "demo applicaction" able to reach very high performances
Show that the whole system
can be used by a single application
Show what really means 1 sustained Tflops !
11 million cells
16 proc EV7
35 hours
B. Meltz

## Slide 6: One year after - First Return of Experience (key words : robustness and scalability)

## Slide 7: Production Codes (1)
Four important codes requires a large part of computing power :
  Currently : A,B,C, D (D under construction)
  Old codes have been thrown away with the CRAY T90
A, B and D have been designed from the start for parallel systems (MPI)
C has been designed for vector machines
  With minor modifications it has been possible to produce an MPI version scalable to 8 processors

## Slide 8: Production Codes (2)
Relative performance to T90 (1 proc to 1 proc) is between 0.5 and 2
Good speed-up for A and B up to 64/128 procs depending on problem size
Speed-up of C reaches 4 for 8 processors
D scales to 1000+ processors
For users, it is now possible to work much faster than before :
  Availability of a large number of processors + Good code performances
  From weeks to days, from days to hours
  More computations in parallel (parametric studies)

## Slide 9: Advances in weapon simulation
Computation time (est.) CRAY T90 : more than 300 hours
Two nights on 64 processors TERA = 1 month on CRAY T90

## Slide 10: Advances in simulation of instabilities
2000
0.5 millions of cells
400h*12 processors
IBM SP2
2000
6 millions of cells
450h*16 processors
COMPAQ
2001
15 millions of cells
300h*32 processors
COMPAQ
2002
150 millions of cells
180h*512 processors
HP
Author : M. Boulet

## Slide 11: Advances in RCS computation
1990
2003
1997
ARLENE
ARLENE
ARLAS
CRAY T3D/T3E
 Parallelism
 New numerical methods
 EID formulation
 Multipoles
 Domain decomposition
 Direct/iterative solver
CRAY
YMP
TERA
TERA
ARLENE
ARLAS
2000
30 000
500 000
30 000 000
Number of
Unknown
ODYSSEE
Cone shaped object at 2 Ghz :
  104 000 unknown
  Matrix size : 85.5 GB
Authors : M. Sesques, M. Mandallena (CESTA)

## Slide 12
Pu239 --> U235 (88 keV) + He (5.2 MeV)
=> Default creation : type and number ?
Tool : Molecular dynamics (DEN/SRMP ; DAM/DSSI)
200 000 time steps
4 weeks of computation
32 processors of TERA
Also 20 106 atoms on 128 procs
5 nm
9 M atomes
20 keV
85 ps
interstitiel
remplacement
lacune
Author : P. Pochet (CVA)
Physics code : Plutonium Ageing

## Slide 13: Physics codes
Simulation of laser beam propagation in LMJ (D. Nassiet)
  2.5 day for 1 processor
  Less than 1 hour for 64 procs
Laser-Plasma interaction (E. Lefebvre)
  2D scalable to 256 procs
  3D for the future
And many others …in material simulation, wave propagation ...
00:00:00
00:07:12
00:14:24
00:21:36
00:28:48
00:36:00
00:43:12
00:50:24
00:57:36
64
128
256
512
1024
Nombre de processeurs
Temps (HH:MM:SS)

## Slide 14: HERA hydro computation : 15 µm mesh (15,5 cm x 15,5 cm)
Reference computation EULER
100 millions cells
AMR Computation
~3,5 millions cells
20 732 CPU hours
256 processors
81 h
140 CPU hours
1 processor
140 h
Auteurs : H. Jourdren - Ph. Ballereau - D. Dureau (DIF)

## Slide 15: Major technical issues
Global File System
  Reliability
  Performances
Hardware reliability
Adapt simulation codes and environnement tools to :
  Unreliable environment
  Cluster Architecture
System administration
Network security

## Slide 16: Global File System (1)
Reliability :
  Intermediate system (Sierra 2.0)
    Since April 2002 a lot of file corruptions (at that time parallel load had greatly increased on the machine, 1+TB/day)
    The major bug was fixed September 2002, others remain we are waiting for other bug fixes
      Very long time to get a fix
      Problem difficult to reproduce + Galway/Bristol
  Same bugs exist on the final system (Sierra 2.5)
    Apparently corrected with Sierra 2.5
    But re appearing (at a low level) with the very heavy load of the machine during the last weeks

## Slide 17: Global File System (2)
Performances
  For large IO, we are almost at contractual level (6.5 GB/s vs 7.5 GB/s).
    HP can solve the problem by adding more hardware or by having Ios use both rails
  For small IO, performances are VERY far from contractual level (0,07 GB/s vs 1.5 GB/s !)
    It is probably necessary to work a lot on PFS to solve this problem

## Slide 18: Hardware Reliability
Interposer Change on EV68 (Final system)
  Major problem with EV68 processorts starting end of 2001
    Up to 30 CPUs failure per day
  Interposer change : April 4 to April 9
    (2560 processors + spare)
    Now : less than 2 CPU per week
DIMM failures
HSV110 failures
Still some SOPF :
  Administration network
  Quadrics Rails

## Slide 19
Weekly CPU Average Failure Rate
(For first 7 weeks = 4.4 Modules/Week)
(Total of 31 CPU Modules)
Predicted Weekly Failure Rate
for this System Configuration
1.25 Modules/Week
Rev F Upgrade
Completed 4/11

## Slide 20: Adapt tools to new environment
Make CEA/DAM software as "bullet proof" as possible
  Check all IO operations
  If problem, wait and retry
  Use the "commit" paradigm as much as possible
  Log all messages on central logs (don't rely on users for reporting the problems)
  If everything goes wrong : try to inform the user as efficiently as possible of the damages

## Slide 21: System Administration
Boot, shutdown, system update (patches), …
  Too long
Global commands, system update
  Unreliable
Need tools to check software level on all nodes
  Even maintain global date
Need tools to monitor the load of the system

## Slide 22: A real success, but ...
Necessity to adapt simulation codes and environnement software to Cluster Architecture (make it bullet proof !)
IO and Global File System
  Reliability
  Performances (scalability)
System administration
CONCLUSION