## Slide 1: Facilitating Atmospheric Source Inversion via Operator Regression
SAND2022-9339 C
SIAM Mathematics of Planet Earth
July 15, 2022
Joseph Hart, Mamikon Gulian, Indu Manickam, Laura Swiler
Sandia National Laboratories

## Slide 2: Atmospheric Source Inversion
Inferring sources from impacts is ill-posed.
Spatially localized sources create global impacts.
Climate model complexity prohibits direct inversion.
Operator surrogates may enable inversion.
Spatiotemporal data improves information content.

## Slide 3: Goals and Tiered Verification
Infer operators for tracer evolution generated by E3SM.
Energy Exascale Earth System Model (E3SM) is developed by US DOE.
Use operator surrogate to enable inversion.
End goal: source inversion for Mount Pinatubo eruption.
Question about data, dimension reduction, operator architecture, etc.
Start with a synthetic transport model infer a volcanic source.
Ocean
(MPAS-O)
Atmosphere
(EAM)
Sea Ice
(MPAS-SI)
Land Ice
(MALI)
Land
(ALM)

## Slide 4: Overview of the Workflow
Simulation Data
Observed Data
Expert Knowledge
Operator Approximation
Likelihood
Prior
Posterior
Unobserved Source

## Slide 5: Overview of the Workflow
Simulation Data
Observed Data
Expert Knowledge
Operator Approximation
Likelihood
Prior
Posterior
Unobserved Source

## Slide 6: Simulation Data Generation
Choose possible sources over time steps,
sources are functions of time,
corresponding to the states ,
for simulation runs
where is typically small.

## Slide 7: Overview of the Workflow
Simulation Data
Observed Data
Expert Knowledge
Operator Approximation
Likelihood
Prior
Posterior
Unobserved Source

## Slide 8: Operator Approximation: Learning Formulation
Input the initial condition and source ,
to predict time snapshots .
Approximate the flow map
and compose it to predict the time history
Given data pairs , approximate .

## Slide 9: Operator Approximation: Dimension Reduction
Principal component analysis (PCA) to compress the spatial dimension.
Coordinates
State Snapshots
Modes
number
of spatial nodes
d
number
Of
PCA modes
r

## Slide 10: Operator Approximation: Reduced Operator
PCA Projection
PCA Reconstruction
The flow map is defined in dimensions.
Learn a reduced operator in dimensions.
Approximate via a Neural Network trained on time step pairs.

## Slide 11: Operator Approximation: Network Architecture
,)
Impose structure through PCA modes and time discretization.
,) is a dense 2 layer feed forward network with parameters .
Many hyperparameters:
  Number of PCA modes
  Network depth
  Activation function
  Learning rate
  Loss function
  etc

## Slide 12: Operator Approximation: Prediction, Loss, and Training
Training data is all time steps
Training loss is prediction error for p time steps:
denotes p compositions of .
Guild enables efficient experiment tracking.
Use validation set error to determine hyperparameters.

## Slide 13: Operator Approximation: Experiment Tracker
Validation set relative error.
Automation many training instances.
Number of loss compositions is crucial.
Error variability over 10 runs.
Increasing P decreases variability.

## Slide 14: Overview of the Workflow
Simulation Data
Observed Data
Expert Knowledge
Operator Approximation
Likelihood
Prior
Posterior
Unobserved Source

## Slide 15: Prior and Likelihood
Assume Gaussian prior and noise models:
the misfit depends on data as
with observation operator illustrated by the x’s,
and model prediction .

## Slide 16: Maximum A Posteriori Probability (MAP) Point
Bayes rule gives the posterior distribution,
to characterize the probability of the possible sources.
Determine the maximum probability point,
or equivalently minimize the negative log of the posterior

## Slide 17: Maximum A Posteriori Probability (MAP) Point
Minimization using a Newton-CG Trust Region algorithm.
Evaluate Neural Network Jacobian using algorithmic differentiation.
Solve discretized adjoint equations to compute the exact gradient and Gauss-Newton Hessian.
Cost per optimization iterate is one ,) evaluation plus Jacobian for each time step.

## Slide 18: Posterior Sampling
Laplace approximation: assume is Gaussian.
Mean is computed via optimization: .
Covariance is the inverse Hessian of ) evaluated at .
Leverage data sparsity for low rank approximation.
Laplace approximation is an efficient first step.
Markov Chain Monte Carlo methods are alternatives.

## Slide 19: Overview of the Workflow
Simulation Data
Observed Data
Expert Knowledge
Operator Approximation
Likelihood
Prior
Posterior
Unobserved Source

## Slide 20: Plume Model Problem
Change in SO2 concentration with respect to time
Diffusion
Wind
Gravity
Chemistry
Volcano source
No outflow
Zero initial SO2 concentration

## Slide 21: Data Generation
Training data from 3 different source terms.
Validation data from a 4th source term.
Testing data from a 5th source term.
Train flow map approximation to infer testing data source.

## Slide 22: An Example of the Data
Altitude (km)
Downrange Longitude (km)
Volcano
Atmosphere SO2 Concentration

## Slide 23: Operator Approximation
Compress nodes to PCA modes with relative error.
Operator approximation achieves prediction error.

## Slide 24: Posterior Samples
Black curve is the testing data.
Blue curve is the MAP point.
Grey curves are approximate posterior samples.
Capture source well.
Overestimates uncertainty later in time.

## Slide 25: Conclusions and Ongoing Work
Next Steps
Maturing hyperparameter optimization.
Transitioning toward climate models and data.
Advanced samplers for non-Gaussian posteriors.
End Goals
Capturing spatial structure to better inform inversion.
Identification of pathways to identify a reduced climate system.
Final demonstration to characterize Mount Pinatubo eruption.