## Slide 1: Joint Architecture Standard
Quick Start Guide
SAND2018-9952 TR
UNCLASSIFIED UNLIMITED RELEASE
UNCLASSIFIED UNLIMITED RELEASE

## Slide 2: Objective of this Guide
The Joint Architecture Standard (JAS) offers an adaptable, scalable solution for space-based processing applications that emphasizes the following principles:
  Node-based approach utilizing reconfigurable hardware
  Communications utilizing industry-standard protocols
  Modular design to support a wide range of requirements
  Easy integration of new technologies with minimal impact to established interfaces
This guide is designed to introduce JAS and demonstrate the mapping of mission requirements to a JAS-based system using the JAS Toolbox (JT)
The information contained in this guide will cover:
  An overview of JAS
  A description of essential hardware elements
  JAS software approach
  System design example
UNCLASSIFIED UNLIMITED RELEASE
UNCLASSIFIED UNLIMITED RELEASE

## Slide 3: JAS Overview
The JAS standard emphasizes the following key principles: | 
Reusability | General-purpose nodes with reconfigurable processing hardware support multiple applications
 | Layered software approach allows applications to be abstracted from hardware interfaces and encourages re-use of common software services
 | Significant reduction in NRE resulting in lower cost and shorter schedules
Scalability | Processing capability scales by adding nodes based on requirements
 | Mission-specific needs can be accommodated using expansion modules, such as mezzanines on node hardware
 | Parameterized mechanical designs adapt to arbitrary node counts
Interoperability | Standard communications protocols ease integration of hardware from multiple vendors, and permits the use of COTS for evaluation, testing, and prototyping
 | Generic hardware designs for nodes can readily map functionality to COTS hardware to streamline development
 | Standard hardware functions provides a common front-end interface to every node
Reliability | M-of-N redundancy reduces the penalty of additional hardware compared to traditional A-B redundancy schemes
UNCLASSIFIED UNLIMITED RELEASE
UNCLASSIFIED UNLIMITED RELEASE

## Slide 4: JAS Essential Elements
Mission requirements drive the selection of JAS elements to include within a system instance
The following essential elements must be included:
  Communication Interfaces (physical, preferably serial)
  Protocols to communicate over the physical interface
  Network-connected nodes that implement the communication interface and protocols
  Network routing and addressing scheme(s)
Realization of these elements can be achieved through instances of hardware profiles in the JT
  Standard node types (e.g., CH, RP, PS)
  Expansion modules (e.g. mezzanines and rear transition modules)
  System Monitoring and Communications (SMAC) functions
UNCLASSIFIED UNLIMITED RELEASE
UNCLASSIFIED UNLIMITED RELEASE
Notes: The idea is to not shoe-horn the design, and to allow some flexibility on the designer.
The following slides will introduce and define what is meant by the elements that realize the system instance.

## Slide 5: JAS Nodes
Three general-purpose node types, two for processing and one for power
Processing nodes are reconfigurable and have expansion capability to support mission-specific functions
Configuration and Host (CH)
Microprocessor-based processing
Reconfigurable Processing (RP)
FPGA-based processing
Power Supply (PS)
Note: The example nodes shown here utilize the VPX standard, but any interconnect standard may be used.
UNCLASSIFIED UNLIMITED RELEASE
UNCLASSIFIED UNLIMITED RELEASE
Notes: CH Node:
Microprocessor-based node
Flash memory for program and data storage
SDRAM and SRAM for operational memory
Rad-hard local power conversion (POL)
Mezzanine slot for expansion
Common network front-end (SMAC)
RP Node:
FPGA-based node, programmed by network
SDRAM and SRAM for operational memory
Rad-hard local power conversion (POL)
Mezzanine slot for expansion
Common network front-end (SMAC)
PS Node:
Rad-hard spacecraft-to-system voltage conversion
Distributes common power voltage (usually 5V) to nodes
Generates any needed specialized analog voltages
Networked, but no processing capability
Common network front-end (SMAC)

## Slide 6: JAS SMAC and Expansion Capabilities
The System Monitoring and Communications (SMAC) functions are implemented on every node
  Provides network connectivity between processing elements, controls node power and discrete signals, and provides state of health for node hardware
  Having a common SMAC design on every node provides a consistent front-end interface that reduces software complexity
  SMAC functions can be implemented in either hardware or software
Expansion capabilities provide mission-specific hardware and interfaces to standard nodes
  Expansion boards may take the form of mezzanines, Rear Transition Modules (RTMs)1, backplane-integrated cards, etc.
Systems can be instantiated using two or three node types and expansion capabilities for specialized functions
1 Note: The example expansion modules shown here utilize VITA standards, but any standard may be used.
UNCLASSIFIED UNLIMITED RELEASE
UNCLASSIFIED UNLIMITED RELEASE

## Slide 7: JAS Software and Communications
JAS provides a standard set of software and communication services to applications
A layered architecture abstracts applications from data links, making them more reusable
Software services interface to network protocols based on communication needs
  JAS packet service for sending messages between applications
  Memory access service for remote access to hardware
  Synchronization service for broadcasting events such as time
Data Link Layer
SpaceWire, RapidIO, Ethernet
Application Layer
Network Protocol Layer
JRDDP, JEEP, RMAP, SRIO, UDP
Subnetwork Service Layer
JAS Packet service
Memory access service
Synchronization service
JAS Provided
UNCLASSIFIED UNLIMITED RELEASE
UNCLASSIFIED UNLIMITED RELEASE
Notes: JAS Reliable Data Delivery Protocol (JRDDP), JAS Efficient Exchange Protocol (JEEP), Remote Memory Access Protocol (RMAP), Serial RapidIO (SRIO), User Datagram Protocol (UDP)

## Slide 8: Mapping System Requirements to JAS
First step is to identify high-level system characteristics:
  Data flow into (e.g. sensors) and out of (e.g. downlink) the system
  Processing algorithms
  Long-term data storage needs
  Command and telemetry interfaces
  Reliability considerations
  Environments
UNCLASSIFIED UNLIMITED RELEASE
UNCLASSIFIED UNLIMITED RELEASE
Notes: Entry Criteria: JAS is assumed to be the implementation solution for the system instance

## Slide 9: Identifying Required Hardware
Identify the required number and types of nodes:
  At least one CH node is needed for a spacecraft/host interface
  Dedicated nodes may be needed to interface to sensors
  Map implementation of processing algorithms to CH and/or RP nodes
  Additional nodes for reliability
Identify expansion capabilities that augment existing CH or RP capabilities
  Mezzanines, RTM, or dedicated cards
  Additional memory capacity
  Host spacecraft or sensor interfaces
Model the data flow within the system to identify any limiting factors
  Sensor to data processing algorithms
  Minimum required memory bandwidth
  Ensure sufficient network throughput, especially in cases of node failure where additional routing of mission data to spare nodes is needed
UNCLASSIFIED UNLIMITED RELEASE
UNCLASSIFIED UNLIMITED RELEASE

## Slide 10: Mapping Communications
Communication interfaces will be driven by ICDs:
  Sensor, Host Vehicle, Flight-to-Ground, etc.
Intra-payload communication links use network protocols for routing data
  Quality-of-service resources can be used as needed (reliability, priority, guaranteed bandwidth)
  Multiple networks can be used within the same system (e.g. SpaceWire, Serial RapidIO (SRIO), etc.)
Standard packet formats enable applications to communicate across any network
  Coordinate packet definitions as needed
  Command, Control, and SOH reporting
  Mission data and telemetry
Network topology selection affects reliability in the event of failures
  Redundant links in the right topology is a key factor
  Modeling tools aid in evaluating tradeoffs
UNCLASSIFIED UNLIMITED RELEASE
UNCLASSIFIED UNLIMITED RELEASE
Notes: Interface Control Document (ICD)

## Slide 11: Simple Mission Example
Let’s go through a simple mission example assuming basic system requirements:
  The Customer requires a payload with two focal plane arrays (FPA)
  Each FPA has a maximum output bandwidth of 5 Gbps
  Host vehicle provides 28V power and a MIL-STD-1553 interface for communications
  Payload performs target tracking and recognition by classifying targets against pre-determined signatures
UNCLASSIFIED UNLIMITED RELEASE
UNCLASSIFIED UNLIMITED RELEASE

## Slide 12: Host Interface and Power
Host interface uses an instantiation of a CH node
  A mezzanine is added to support MIL-STD-1553
  CH handles host communications, SOH collection, node command & configuration, and data downlink
Software library for SpaceWire communication
  Communication Protocols
  Memory Access and Packet services
PS node instantiation converts 28V power provided by the host vehicle to usable levels for distribution to the nodes
SpaceWire
CH Profile defines processor-based modules
EXP Profile defines mezzanine card
PS Profile defines power supply node
COMM Profile defines protocols
UNCLASSIFIED UNLIMITED RELEASE
UNCLASSIFIED UNLIMITED RELEASE

## Slide 13: FPA Interface
FPA interfaces are instantiations of RP nodes
FPA 1 requires multiple external biases
  FPA bias generation on RTM
FPA 2 requires a single 5V supply
  FPA bias generation on mezzanine card
High-Speed network based on SRIO
  Transfer image data from sensors to sensor data processing nodes
RP Profile defines FPGA-based modules
EXP Profile defines RTM & mezzanine card
SRIO
UNCLASSIFIED UNLIMITED RELEASE
UNCLASSIFIED UNLIMITED RELEASE

## Slide 14: Sensor Data Processing
Sensor processing nodes are an instantiation of a RP node
Determine the number of nodes based on bandwidth requirements
  Estimated using SE Tools
Shared memory node is an instantiation of a RP node
  Used for storing intermediate or final results
  A mezzanine card provides the required memory size and type
Nodes are interconnected via SRIO
SRIO
RP Profile defines FPGA-based modules
EXP Profile defines RTM & mezzanine card
UNCLASSIFIED UNLIMITED RELEASE
UNCLASSIFIED UNLIMITED RELEASE

## Slide 15: Mission Data Processing
Event/target classification algorithms developed in C are best suited for a processor
Multiple CH nodes are used to perform classification in parallel
Data is read from shared memory node via SpaceWire
Results are sent to host interface node via SpaceWire for downlink
Non-Volatile memory node (comprised of CH node plus non-volatile memory mezzanine card) may store results if downlink is not immediately available
CH Profile defines processor-based modules
SpaceWire
UNCLASSIFIED UNLIMITED RELEASE
UNCLASSIFIED UNLIMITED RELEASE

## Slide 16: Next Steps
Utilize the JAS Toolbox to implement your mission requirements into a JAS-based instance https://jastoolbox.sandia.gov
For further system examples and modeling tools, see the Systems Engineering Toolbox https://collaborate.sandia.gov/sites/JAS_SE_Toolbox
Contact for questions and/or feedback:
  Mellisa Heller, mmhelle@sandia.gov
  David Lee, dslee@sandia.gov
  Mathew Napier, mpnapie@sandia.gov
UNCLASSIFIED UNLIMITED RELEASE
UNCLASSIFIED UNLIMITED RELEASE