## Slide 1: Introduction to CUBIT®
Corey Ernst
Cubit ® 100
CUBIT
Geometry and
Mesh Generation Toolkit
Sandia’s Geometry and Meshing Toolkit
SAND2022-15021 PE
Notes: SAND2022-3937 TR
Details Title: SIERRA 100 CUBIT Training Tracking No: 1493464 SAND No: SAND2022-3937 TR Review Type: FORMAL Submittal Type: Training Contact: Hensley,Trevor Michael Submit By: Hensley,Trevor Michael Date Submitted: 03/28/2022 10:55 AM Status: APPROVED
Uploaded File: - Sierra100-Cubit.pptx Document scientific or technical in nature: Yes LDRD Funded: No Project: Technical Review? Yes Technical Review File: - Keywords: CUBIT SIERRA100 Authors Hensley, Trevor (SNL); Owen, Steve (SNL)

## Slide 2
CAD Tool
Cubit ®
Simulation
Creo
Solidworks
SierraSM
SierraTF
SierraSD
Abaqus
Nastran
Dyna
etc.
Geometry Modification
Meshing
Boundary Conditions
Mesh Modification
Mesh Quality
Scripting
Geometry
Mesh
ACIS
STEP
Exodus
Cubit ® Scope

## Slide 3: User Interfaces
Command Line
Graphical User Interface
Command Line w/Graphics Only
Batch Processes (Journal Files)
Better Performance
Harder to Use
Interactive, Intuitive
More tools available
Easy to learn/use

## Slide 4
Windows (64 bit)
Linux (64 bit)
Downloads
https://cubit.sandia.gov/
click on Downloads
Enter Password
Sandia CEE
Linux LAN
Add /projects/cubit to your PATH
Type cubit at linux prompt.
Password
Sandia: Your Kerberos password
Others: from Cubit ® License
Platforms

## Slide 5
Cubit ® online help from
https://cubit.sandia.gov/documentation
Tip of the Day: Lots of valuable nuggets at CUBIT™ startup
Command Panels: Help on specific command
cubit-help@sandia.gov
User Documentation from the Help Menu (same as online help)
Dedicated support email. Usually 24 hr response time
Online Help

## Slide 6
For Sandia Staff
(with Access to SRN)
https://wiki.sandia.gov/display/CKB
Shortcut to Knowledge base:
Windows and Linux Browser, Type:
Searchable database with videos, articles, how-to, troubleshooting, etc..
Includes all Sandia CompSim tools including Cubit ®
Online Help
cubit-help

## Slide 7: Getting Started
Corey Ernst
Cubit ® 100 Tutorials
CUBIT
Geometry and
Mesh Generation Toolkit
2
SAND2022-15021 PE

## Slide 8: Exercise 2.1 Getting Started
Solid Model
Import the geometry from a file
Set the mesh size to 0.5
Set the mesh scheme to sweep
Create a hexahedral mesh
Delete mesh
Set the mesh scheme to tetmesh
Create a tetrahedral mesh
Hex Mesh
Tet Mesh

## Slide 9: Exercise 2.1 Import the Solid Model
Use the File – Import menu to import the file “ra.sat”
Click Finish
2
1
1
2

## Slide 10: Exercise 2.1 Set the Mesh Size
1
2
1
2
3
Click Volume Selection Filter Icon
click on the part
Set the Requested Size on the property panel to 0.5 and hit Return
3

## Slide 11: Exercise 2.1 Set the Mesh Size
2
1
2
3
Click Volume Selection Filter Icon
click on the part
Set the Requested Size on the property panel to 0.5 and hit Return
3
1

## Slide 12: Exercise 2.1 Create a Hexahedral Mesh
Click the Mesh Button
1
2
Select the Sweep scheme from the dropdown menu next to Mesh Scheme
1
2

## Slide 13: Exercise 2.1 Create a Tetrahedral Mesh
Click the Mesh Button
1
2
Delete the mesh and reset the volume by clicking on the Reset Button
1
2
3
Choose the Tetmesh scheme from the dropdown menu next to Mesh Scheme
3

## Slide 14: Graphical User Interface Basics
Corey Ernst
Cubit ® 100 Tutorials
CUBIT
Geometry and
Mesh Generation Toolkit
3
SAND2022-15021 PE

## Slide 15
Graphics Window
Pulldown Menu Commands
Toolbars
Model Tree
Properties Page
Command Window
Command Panel
Power Tools
Tip: Use the Tools->Options (Windows) or Cubit->Preferences (Mac) to customize the look and feel of the GUI and graphics
Tip: Drag and drop windows to customize workspace.
With 2 monitors try moving the command window or panel to its own monitor to maximize space.
Cubit ® Graphical User Interface

## Slide 16
Reset
Open a Cubit ® file
Save to a Cubit ® file
Import from a geometry file
Export to a geometry file
Open the journal editor
Play a journal file
Play/Record an ID-less journal file
Pause current journal file
Custom toolbar editor
Cubit ® Main Toolbar

## Slide 17
perspective on/off
Zoom in, out, and fit
redisplay
Check point save/undo
Display modes
Toggle Scale
Custom selection tools
Display Composite Surface Curves
Slice Tool
Display BCs
Curve valence (Display merges)
Show Overlaps
Tip: Make sure icon is selected to ensure undo will work
Cubit ® Display Toolbar

## Slide 18
Toggles what kind of entity is available for graphical selection
Tip: Pickwidgets (edit fields in command dialogs) “hijack” selection filters so that only the expected entity type is selectable
Groups
Bodies (More than one volume grouped together)
Volumes
Surfaces
Curves
Vertices
Nodes
Edges
Quads and Tris
Hexes and Tets
Geometry Entities
Mesh Entities
Entity Selection Filters
Boundary Layers

## Slide 19
List Type
Current Selection (Same as Graphics Window Selection)
Expand tree to show graphics window selection(s)
Hierarchical view of current parts in your model
Lists of Boundary Conditions
Tip: Rename any geometry entity by clicking on its current name in the Model Tree
The Model Tree

## Slide 20
Navigation Modes:
Full Navigation
Breadcrumb Navigation
Access to all Cubit ® commands available via hierarchical menu structure
Select any button to reveal next level of buttons
Displays full path to command
(more compact than full navigation)
Select text in path to navigate to commands
Tip: Change the navigation mode from the Options (Windows) Preferences (Mac) panels. Select Command Panels and check the Use Full Navigation toggle
Command Panels

## Slide 21
Press an Icon to enter a new mode
- Geometry: Create, modify, cleanup…
- Mesh: Intervals, schemes, smoothing…
- Boundary Conditions
- Analysis Setup: Export mesh
- Post Processing: Customizable shortcut
Full Navigation Mode
Command Panels

## Slide 22
Drop Down Menu
  Select the type of operation (sub-action).
ID Input Field (Pickwidget)
  You can type IDs here, or fill the box by picking
Command Options Input
Apply Button
  Cubit™ command syntax generated
  Executes command and applies the current options.
Command Help (opens browser)
Automatically Reset the dialog after Apply
Tip: Some commands have a preview button.
A quick way to display results of command without making permanent changes to model
Almost all Cubit ® commands can be executed from command panel dialogs
Command Panels

## Slide 23
Cubit ® commands entered and information displayed
Cubit ® command syntax:
Cubit> create cylinder radius 3 height 10
Cubit> create brick x 10 y 10 z 10
Cubit> cylinder rad 3 hei 10
Cubit> brick x 10
List of all Cubit ® commands executed in session
Tip: Enter partial command and type “?” to display full syntax for command
Commands are case insensitive and can be abbreviated
Cubit ® Command Line Window

## Slide 24
Information is updated when a new entity is selected
Action Buttons: Immediate actions performed on current selection(s)
  Preview Mesh : Displays preview of nodes on curves
  Mesh: generate a mesh with current settings
  Smooth: smooth the mesh with current settings
  Mesh Quality: Display mesh quality with default metric
  Delete Mesh: delete the mesh from selection (keep settings)
  Reset Entity: reset all settings for selection (including deleting mesh)
  Delete: Delete the selected geometry
Information about the current selection(s)
Tip: Some attributes can be directly edited in the properties page. Examples:
Name of entity
Color of entity
Meshing Scheme
Requested mesh size
Properties Page

## Slide 25
Specialized tools for performing diagnostics and managing your model
Click to change to a different Power Tool
Cubit ® Power Tools
ITEM Wizard: Step-by-step workflow from CAD to mesh
Diagnose Geometry: Find and fix potential problems in geometry
Diagnose Meshability: Check whether geometry can be meshed
Defeature Geometry: Tool for defeaturing (experimental)
Compare Mesh: Check for overlap between geometry and mesh
Assemblies: Manage assembly metdata
Diagnose Mesh Quality: Check mesh quality
Tip: The Diagnose Geometry Power Tool contains new machine learning capabilities for defeaturing and part classification
Power Tools

## Slide 26: Exercise 3.1 Become Familiar with the Interface
1
Create a prism:
height = 10
number of sides = 5 radius = 5
2
Use tool bar buttons to visualize the prism:
transparent
smooth
wire frame
Use selection tools to select a:
vertex
curve
surface
volume
3
Mesh the prism with hexes and select a:
node
edge
quad (face)
hex
4
0
Reset from the command window:
CUBIT> mesh vol 1
CUBIT> reset

## Slide 27: The Basic Cubit ® Workflow
Steven Owen
Cubit ® 100 Tutorials
CUBIT
Geometry and
Mesh Generation Toolkit
4
SAND2022-15021 PE

## Slide 28
Import Solid Model
1
Simplify Geometry
2
Decompose Geometry
3
Imprint & Merge
4
Set Schemes
& Intervals
5
Mesh
6
Check
Quality
7
Apply B.C.s
8
Export
Mesh
9
The Cubit ® Workflow

## Slide 29
Select “piston.stp”
Import Solid Model
1
Set the file filter type
to STEP (*.stp *.step)
Import the STEP file
“piston.stp” from the
cubit100 directory
File->Import
1
2
3

## Slide 30
Select Finish
Import Solid Model
1
Import the STEP file
“piston.stp” from the
cubit100 directory
4

## Slide 31
3
Select volume (or enter all in the field)
Click Preview to display a preview of the plane
Cutting plane Preview
1
2
2
Simplify Geometry
Cut the model into
quarters to take
advantage of
symmetry
Choose Webcut With YZ Plane
1
Click Mode-Geometry
Click Entity-Volume
2
Click Action-Webcut
5
6
7
3
4
4
Select Coordinate Plane from the menu
5
6
Define and preview a cut through the part
7

## Slide 32
Execute the webcut command by pressing Apply
2
Simplify Geometry
Cut the model into
quarters to take
advantage of
symmetry
Two separate and unconnected bodies
Two separate and unconnected bodies
8

## Slide 33
Change cutting plane to the XY Plane
2
Simplify Geometry
Cut the model into
quarters to take
advantage of
symmetry
Cutting plane Preview
Preview the cutting plane
Define and preview the second cut through the model
9
10

## Slide 34
Execute the webcut by pressing Apply
11
2
Simplify Geometry
Cut the model into
quarters to take
advantage of
symmetry
Four separate and unconnected bodies

## Slide 35
Pick three of the four volumes from the graphics window
Execute the delete command by pressing Apply
Change from Action-Webcut to Action-Delete
12
13
14
2
Simplify Geometry
Cut the model into
quarters to take
advantage of
symmetry
12
13
14
Delete 3 of the 4 volumes

## Slide 36
2
Simplify Geometry
Cut the model into
quarters to take
advantage of
symmetry
Simplified model ready for decomposition

## Slide 37
1
3
Click Entity-Volume
Select volume (all)
4
5
3
Decompose Geometry
Cut the model into
sweepable volumes
1
2
4
5
7
6
2
Click Action-Webcut
3
Select Cylinder Radius from dropdown menu
Enter Radius 1.5
Select Axis as Vertex Pair
6
7
Select the two vertices as shown to define the cylinder axis
7
Define a Cylindrical Webcut

## Slide 38
Webcut
Preview
3
Decompose Geometry
Cut the model into
sweepable volumes
Click Preview to see a preview of the cutting cylinder
8
9
Preview and Apply the Cylinder Webcut
8
9
Click Apply to cut the volume

## Slide 39
10
Click Entity-Volume
14
Select the surface as shown to define the cutting plane
14
Select the volume to cut (all or 1)
13
3
Cut the model into
sweepable volumes
10
11
12
14
13
Decompose Geometry
Click Action-Webcut
Select Plane Surface from the drop down menu
11
12
Define a cutting plane from a planar surface

## Slide 40
15
Webcut
Preview
16
3
Cut the model into
sweepable volumes
Decompose Geometry
Preview and Apply the planar webcut
Click Preview to see a preview of the cutting plane
Click Apply to cut the volume
15
16

## Slide 41
3
Cut the model into
sweepable volumes
Volumes are now individually sweepable
sweep direction 1
sweep
direction 2
sweep direction 3
Decompose Geometry

## Slide 42
4
Imprint &
Merge
Vol 1
Vol 2

## Slide 43
Vol 1
Vol 2
4
Imprint &
Merge
Volumes are independent -- by default, will not share nodes where they meet

## Slide 44
Vol 1
Vol 2
4
Imprint &
Merge
Imprint

## Slide 45
Vol 1
Vol 2
4
Imprint &
Merge
Surface 10
Surface 9

## Slide 46
4
Imprint &
Merge
Vol 1
Vol 2
Surface 9
Merge
Volume 1 and 2 both share Surface 9

## Slide 47
4
Imprint &
Merge
Vol 1
Vol 2
Surface 9
Volume 1 and 2 both share mesh on Surface 9

## Slide 48
4
Imprint &
Merge
Vol 1
Vol 2
Volume 1 and 2 both share mesh on Surface 9
Surface 9

## Slide 49
4
Imprint &
Merge
Vol 1
Vol 2
After imprint and merge volumes will share nodes at their interface when meshed.

## Slide 50
4
Imprint &
Merge
1
2
Click Entity-Volume
3
Click Action-Imprint and Merge
Select Imprint/Merge from dropdown menu
4
Click Apply
Select volumes
5
Connect volumes
together to ensure a
continuous FEA mesh
will be generated
1
2
3
5
4
Imprint and Merge the volumes

## Slide 51
5
Set Schemes
& Intervals
Define the meshing
schemes and the mesh
size on the geometry
that will be used
1
1
Click Mode-Mesh
2
2
Click Entity-Volumes
3
3
Click Action-Intervals
4
4
Click Automatic Sizing from dropdown menu
5
Select volumes all
5
6
6
Drag the slider until the desired resolution is set (see preview in graphics window)
Preview of
nodes on
the curves
Preview and set the mesh size

## Slide 52
5
Set Schemes
& Intervals
Define the meshing
schemes and the mesh
size on the geometry
that will be used
Set the Meshing scheme to Automatically Calculate
7
7
Click Action-Mesh
8
9
10
10
Click Automatically Calculate from dropdown menu
8
Select the volumes (all)
9
Click Apply Scheme

## Slide 53
6
Mesh
Create the hex mesh
on the volumes
1
Mesh the Volumes
1
Click the Mesh Button

## Slide 54
7
Check Quality
Element Shape Metrics
-0.5
0.0
0.5
1.0
0
1
2
3
0
1
2
3
0
1
2
3
0
1
2
3
-0.5
0.0
0.5
1.0
0
1
2
0
1
2
0
1
2
1
2
Quads
Triangles
Best Quality
Worst Quality

## Slide 55
7
Check Quality
Check to see if the
quality of your elements
are reasonable for
analysis
1
1
Click Mode-Mesh
2
2
Click Entity-Volumes
3
3
Click Action-Quality
4
4
Select Volumes (all)
Display color-coded elements based on the Shape quality metric
5
5
6
6
Select the Shape quality metric from the dropdown menu
Check the Display Graphical Summary check box
7
7
8
8
Check the Draw Mesh Elements check box
Click Apply

## Slide 56
8
Apply B.C.s
Blocks
Sidesets
Nodesets
Grouping of Elements with Common Properties
Normally define elements with same Material
Element can be in only one block
Common element type (i.e. hex8, tet10, etc)
Grouping of Quads on Hexes (3D),
Edges on Quads (2D)
Normally describe force over an area (ie. Pressure loading)
Side can be in any number of sidesets
Grouping of Nodes
Normally describe force at a point (ie. Point source loading, constraint)
Node can be in any number of nodesets

## Slide 57
8
Apply B.C.s
Designate where
materials and boundary
conditions will be
applied on the model
1
1
Click Mode – Analysis Groups and Materials
2
2
Click Entity-Blocks
3
3
Click Action - Create
4
4
Enter Block ID 100
Define a Material Block with ID=100
5
5
6
Select Volume
6
Select the volumes to add to the block (all)
7
7
Click Apply to create the new block 100

## Slide 58
8
Apply B.C.s
Designate where
materials and boundary
conditions will be
applied on the model
1
2
3
3
Click Action – Element Type
Define the element type for Block 100 as HEX8
1
2
Enter Block ID 100
Select Volumes
4
4
Select Hex8
5
5
Click Apply

## Slide 59
8
Apply B.C.s
Designate where
materials and boundary
conditions will be
applied on the model
1
2
3
3
Click Entity-Sidesets
Create a Sideset representing a distributed load
1
2
Choose Action – Create Sideset
Enter a Sideset ID of 1
4
4
Select Surface
5
5
Pick the surfaces as shown where the distributed load should be applied
5
6
6
Click Apply

## Slide 60
9
Export Mesh
Create an FEA Mesh
File to be used in
an analysis
1
2
3
3
Click Mode - Export
Export a Genesis file containing mesh, blocks and sidesets
1
2
Click Operation-Export Mesh
Choose Genesis from the dropdown menu
4
4
Click Browse. Enter the file name “qtr_piston.g” in a directory of your choosing
5
5
6
6
Select Export All to export all block ids
Click Apply

## Slide 61: Usability Tools
Steven Owen
Cubit ® 100 Tutorials
CUBIT
Geometry and
Mesh Generation Toolkit
5
SAND2022-15021 PE

## Slide 62
Cubit ® Database File contains:
Geometry
Meshing Schemes
Intervals
Virtual Geometry
Mesh
Boundary Conditions
Snapshot of the current state of the model
Choose Save or Save As… to save or create a .cub file
Choose Open to read a .cub file
Deletes existing data and Resets your Cubit ® session with the new data from the .cub file
Save
Open
The Cubit ® .cub File

## Slide 63
Cubit ® Journal File contains:
Sequential list of Cubit ® commands
Comments
APREPRO Scripts
Complete list of sequential commands used to regenerate a desired state of a model
Create/Edit Journal
Playback Journal File
On start-up, Cubit ® automatically creates a new .jou file and logs every command in the session to the file
Automatic Journal File Creation
Default location is the installation directory
Named cubitXX.jou and historyXX.jou
Tip: Set a custom location for automatic journals files in Tools->Options… (Cubit->Preferences… on Mac) under History
The Cubit ® Journal File

## Slide 64
Journal File Editor
Interactive Editor for Cubit ® journal files
Can also use any text editor
Edit the current session
Import the History Tab: record of all commands to date in the session
Add, delete or edit the Cubit ® commands
Play commands
Highlight and right click on one or more commands
Use the Play Selected menu item
Python Scripting
Toggle between Cubit ® command language and python scripting
Import the current CUBIT™ session for editing in the Journal Editor
Open the Journal File Editor
Creating and Editing Journal Files
1
2
2

## Slide 65: Exercise 5.1
Open the Journal File editor
Open the file ”lecture4.jou” in the journal editor
Try editing and running commands from the journal editor
Save a .cub file. Name it “lecture4.cub”
Reset and open file “lecture4.cub”
2
3
1
5
Generate and Run a Journal File
Save a .cub File
Reset and run “lecture4.jou” from the command window
4
CUBIT> play "lecture4.jou"
6

## Slide 66
All geometry entities can be given 1 or more names
Reasons to use names
  More intuitive in commands
  More persistent than IDs - saved to SAT
  Can group entities by name
  Names propagate during webcuts, can track original parts (Gear becomes Gear and Gear@A when split)
To change names
  Geometry Tree View: Right-Click menu, “Rename”
  Property Panel: Edit “Name” value
  Command line: <entity> name “<name>”
CUBIT> mesh stronglink
CUBIT> draw stronglink
CUBIT> volume 1 name “stronglink”
a
b
c
a
b
Tip: Using names can avoid conflicts with new versions of CUBIT if IDs change
Entity Names

## Slide 67
group "assembly1" add vol 1 2 4
group "bad-hexes" equals quality vol 1 high 0.3
assembly1 remove vol 4
To create/edit groups from the command line
To create groups from the Geometry Tree
Right-Click on Groups in the Geometry Tree
1
2
1
2
Select Create New Group
3
3
Enter a unique new group name
Groups
Adds volume 1,2 and 4 to group named assembly1
Adds hexes with quality < 0.3 to group bad-hexes
Removes volume 4 from group assembly1

## Slide 68
Right-click after selecting entity in the Graphics Window
Add to Group/BC/Part
Remove from Group/BC/Part
Choose an existing group to add/remove to and Click OK
Groups

## Slide 69
Speeds up frequently used tasks
Focus should be in Graphics Window (click any open space)
Examples:
Control-s
Speed save the model to filename.cub.X
Increments X each time cntrl-s is executed
l (lower case L)
When a geometry entity is selected, lists its attributes to the command window
e
When a geometry entity is selected, echoes the ID of the entity to the command line
x, y or z
Displays a slice of the interior mesh elements in the x, y or z planes. Use j and k to move the slice plane
i
Toggle the visibility of the current selection
TAB
Toggle the selection to other entities obscured by surfaces/volumes in front
h
Display list of available keyboard shortcuts*
*Some keyboard shortcuts are only available in the command line version of CUBIT™
Keyboard Shortcuts (Hotkeys)
Display hotkeys from the Help menu

## Slide 70
Undo
Turn on Undo
Wireframe
True Hidden Line
Hidden Line
Transparent
Shaded
Display Modes
Display Geometry
Display Mesh
Display BCs
Composite View
Refresh Graphics
Zoom In
Zoom Out
Zoom to Fit
Toggle Perspective
Toggle Scale
Toggle Clipping Plane
Toggle Clipping Manipulation
Show Curve Valences
Select enclosed/extended
Box/Poly Selection
X-Ray Selection
Locate Overlapping
Surfaces
Display Tools
Display Boundary layers

## Slide 71
Toggle Slice Mode
Toggle Slice Tool
Slice Tool

## Slide 72
1
Select Custom Toolbar Editor from the Tools menu, or use the toolbar shortcut.
1
2
2
Click the ‘+’ button under the Toolbars column.
Create a series of frequently used commands and assign them to a button in the toolbar
Custom Toolbars

## Slide 73
Give the new toolbar a name and file location and click OK.
With the new toolbar selected, click the ‘+’ button under the Buttons column.
3
3
4
4
5
5
Choose ‘Tool Button’ as the new button type and click OK.
Custom Toolbars

## Slide 74
Give the new button a name.
Enter any series of CUBIT™ commands that will be executed any time you hit the button
6
7
8
6
7
8
Click OK to save the toolbar
and button.
You should see a new toolbar and icon appear with the other toolbars
Select this button to execute your custom commands
Custom Toolbars

## Slide 75
You should see a new toolbar icon for the panel.
Select this button to open the corresponding Command Panel.
Create shortcuts to frequently-used Command Panels.
1
2
3
1
2
3
Open any command panel.
Right-click on any blank space in the panel and select Add to Toolbar from the context menu.
Select the custom toolbar you want to add the shortcut to. Click OK in the editor to confirm.
Custom Toolbars

## Slide 76: Geometry Tools
Steven Owen
Cubit ® 100 Tutorials
CUBIT
Geometry and
Mesh Generation Toolkit
6
SAND2022-15021 PE

## Slide 77
Start by defining vertices
Connect them with curves
Create a surface from a loop of curves
Create a volume from a closed set of surfaces
1
2
3
4
Bottom-Up Geometry Creation

## Slide 78: Exercise 6.1
Open the Journal File editor
Open the file ”plate_general_contact.jou” in the journal editor
Select and run the commands to generate nodes (up to line 43)
Select and run commands to build surfaces (line 102 to 123)
Select and run the remainder of the journal file to mesh and assign boundary conditions
2
3
1
5
Bottom-up Geometry Creation
Select and run commands to build curves (line 45 to 100)
4
6
Vertices
Curves
Surfaces
Tip: Use the attribute option when creating blocks to set SHELL and BEAM traits such as thickness, offset, beam orientation, etc. (see lines 170 to 193)
Tip: Use the aprepro syntax {Id(“vertex”)} to get the ID of the last vertex that was created

## Slide 79
Geometry Primitives
Created centered at origin
Use transformations to position
Click Entity - Volumes
1
2
Click Mode-Geometry
3
Click Operation - Create Geometry
4
Select a Primitive shape to create
1
2
3
4
Primitive Creation

## Slide 80
1
2
3
Move the volume to align with another entity
Align
Move
Translate the volume a specified distance and direction
Reflect
Reflect the volume about a specified plane
Rotate
Rotate the volume about a specified axis
Scale
Scale the volume by a factor in x, y and/or z
CUBIT™ is “Unit-less”
Hint: Use Scale to change Units
Align the volume using the 3-step method
Three-step Align
Click Entity - Volumes
1
2
Click Mode-Geometry
3
Click Operation - Transform Geometry
4
Select a transformation method
4
Geometry Transformations

## Slide 81
Click Entity-Volumes
1
2
Click Mode-Geometry
3
Click Operation-Boolean Operations
Perform Boolean operations between volumes
Subtract
Union
Intersect
1
2
3
4
Select a Boolean operation method
Boolean Operations
4

## Slide 82: Exercise 6.2
Create a cube (brick) 10 units
Create a cylinder with radius 3 height 10
Move the cylinder in z by 5 units
Generate a hex mesh
2
3
1
5
Subtract the cylinder from the brick
4
Create this geometry and mesh with hexes
Basic Geometry Primitive Creation and Booleans
brick x 10
cylinder rad 3 height 10
vol 2 mov z 5
subtract vol 2 from 1
mesh vol 1

## Slide 83
Remove surface and extend its neighbors
Often used to enable hex meshing using sweep scheme
2
3
1
4
1
2
3
4
Mode - Geometry
Operation – Modify Geometry
Entity - Surfaces
Select the Remove option
Alternative Method
In Graphics window:
Select surface
Right Click
Select Remove Option
Remove Surface

## Slide 84
Web-cutting slices through your geometry creating additional volumes
Web-cutting is most often used to enable sweeping
4
1
2
3
Many different options for web-cutting
Each brings up a separate command panel
2
3
1
4
Mode - Geometry
Operation – Webcutting
Entity - Volume
Select a webcut method from drop-down
Webcut

## Slide 85
Slice with a plane defined from 3 vertices
2
3
1
3
4
Select Plane from Vertex
Select 3 vertices (plane will pass through vertices)
Select a volume to cut
Often used to facilitate sweeping
1
2
Click - Apply
3 vertices
4
Webcut – Plane from 3 Vertices

## Slide 86
Slice with a plane normal to a curve
2
3
1
4
3
4
Select Plane from Curve
Select a curve (plane will be normal to curve)
Select a volume to cut
Often used to facilitate sweeping
5
1
2
Select Near Vertex Method
5
Select a vertex (plane will pass through vertex)
vertex
curve
6
6
Click - Apply
plane normal to curve
Webcut – Plane from Curve

## Slide 87: Exercise 6.3 Defeaturing and Webcutting
Import “knuckle.sat”
2
3
1
5
4
Remove small surfaces
Webcut where necessary
Imprint and merge
Mesh with size of 1.5
6
Export the mesh as an exodus file “knuckle.g” (We will use it later)

## Slide 88: Meshing Schemes
Steven Owen
Cubit ® 100 Tutorials
CUBIT
Geometry and
Mesh Generation Toolkit
7
SAND2022-15021 PE

## Slide 89
The Cubit ® Workflow
Import Solid Model
1
Simplify Geometry
2
Decompose Geometry
3
Imprint & Merge
4
Set Schemes
& Intervals
5
Mesh
6
Check
Quality
7
Apply B.C.s
8
Export
Mesh
9

## Slide 90
Cubit ® Provides a number of different surface mesh schemes. Choosing the best scheme depends on the shape and number of curves in the surface. Your choice also depends on how you plan to mesh the volume.
Surface Meshing Schemes
TriMesh
Map
SubMap
Pave
TriPrimitive
Polyhedron
Hole
Circle

## Slide 91
Cubit ® Provides a number of different volume mesh schemes. Similar to Surface Scheme Selection, Volume Scheme Selection is based on the shape of the geometry and the requirements of the analysis code.
Map
Sweep
SubMap
Polyhedron
Sphere
TetMesh
Sculpt Parallel
Volume Meshing Schemes
TetPrimitive

## Slide 92
Volume and Surface Schemes can be manually applied from the Property Page or from the Cubit ® Volume/Surface Meshing Command Panels.
By choosing Automatically Calculate, Cubit ® will attempt to select the best mesh scheme for the surface
Scheme priority will be set based on characteristics of geometry.
Cubit ® Property Page
Auto Scheme Selection
1. Map
2. SubMap
3. Sweep
1. Map
2. SubMap
4. Pave
3. TriPrim
Cubit ® Surface Meshing
Command Panel
Volumes
Surfaces

## Slide 93: Exercise 7.1 Meshing Schemes
Reset and import schemes.sat
Set mesh size to 1.00
Use the Auto Calc and mesh all surfaces and volumes and check the auto-selected schemes
Reset volumes and experiment with different surface and volume meshing schemes. For example:
1
2
3
4
mesh volume all
surface 9 scheme circle
mesh surface 9
mesh vol 2
surface 17 scheme hole rad_intervals 4
mesh surface 17
mesh vol 3
Volume 2
Volume 3
volume 5 scheme polyhedron
mesh vol 5
Volume 5

## Slide 94
Source surfaces
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source Surfaces
One or more surfaces
Can be meshed with any Quad Scheme (Pave, Map)
Target Surface
Must be a single surface
Must be unmeshed
Matches topology of source surfaces
Sweep Scheme

## Slide 95
Linking surfaces
Linking surfaces
Linking surfaces
Linking surfaces
Linking Surfaces
Must be “Mappable”
Connect Sources with Target
Sweep Scheme

## Slide 96
Most frequently used meshing scheme
Normally requires geometry to be decomposed to apply sweeping (webcutting)
Sweep Scheme

## Slide 97
Setting Source and target Surfaces
1
2
3
4
Navigate to Volume Scheme Selection Command Panel
Shortcut from property panel to scheme selection
Choose Sweep Scheme
Pick Sources and Targets
Apply Scheme
1
2
3
4
Sweep Scheme

## Slide 98: Exercise 7.2 Sweeping
Import “schemes.sat”
2
3
1
4
Isolate volume 14
Sweep Option 1:
Use the sweep scheme command panel to set source and target surfaces so that resulting mesh looks like Sweep Option 1
Sweep Option 2:
Do the same for Sweep option 2.
(Important: Use 3 source surfaces and one target surface)
Volume 14
Sweep Option 1
Sweep Option 2

## Slide 99
Ideal for non-mechanical/
organic shapes
Overlay Grid Method
Uses Cartesian Grid as Base Mesh
Adjusts nodes to geometry
Inserts Layer of Hexes
But can be used for any geometry
Sculpt

## Slide 100
Sculpt is a separate companion application to Cubit ®.
Can be run from Cubit ® GUI or in batch from OS command line
Parallel application uses MPI to run on multiple cores/processors
See Cubit 200 for more details/exercises
Does not use Scheme, instead uses Sculpt Parallel command.
Sculpt
3
1
2
If you get an error
Check your working directory with “pwd”
Ensure your working directory has write permissions
Change directories or create a new directory

## Slide 101: Exercise 7.3 Sculpt
Import the stl file “eros_asteroid.stl” (change the file filter to “stl”)
Preview the overlay grid resolution
Mesh
Use the slice tool to view the interior hexes
Delete mesh and experiment with alternate sizes
2
1
Navigate to sculpt panel
3
4
3
1
5
5
4
3
6

## Slide 102
Arbitrary geometry
Mostly push-button/automatic
May still require geometry clean-up
Tetmesh Scheme

## Slide 103: Exercise 7.4 Tet Meshing
Import model
Import ACIS file driver.sat OR cad6.sat
driver.sat
cad6.sat
1
1

## Slide 104: Exercise 7.4 (continued) Tet Meshing
Mode - Mesh
Entity - Volume
Action - Mesh
Select Volume to Mesh (1)
Choose Tetmesh Scheme
Apply the Tetmesh Scheme
Click the Mesh Button
OR
Volume 1 scheme tetmesh
Mesh Volume 1
From Cubit ® Command Window
1
2
3
4
5
6
7
1
2
3
4
5
6
7

## Slide 105: Defeaturing
Steven Owen
Cubit ® 100 Tutorials
CUBIT
Geometry and
Mesh Generation Toolkit
8
SAND2022-15021 PE

## Slide 106
The Cubit ® Workflow
Import Solid Model
1
Simplify Geometry
2
Decompose Geometry
3
Imprint & Merge
4
Set Schemes
& Intervals
5
Mesh
6
Check
Quality
7
Apply B.C.s
8
Export
Mesh
9

## Slide 107
Defeaturing
Geometry from CAD design tools can include many unnecessary features
May be too complex for hex meshing
May require too many elements resulting in long run times
Customer may only want approximate, fast turn-around
32,559 tets
397,258 tets
CAD part from designer
Defeaturing
CAD part for simulation
595 surfaces
1506 curves
994 vertices
107

## Slide 108
GUI Tools
Select Surface in graphics window
Right Click
A list of available selection tools will be offered based on the selected surface
Select Similar | Selects other entities with the same geometric description (volume, area, length, topology)
Select Blend Chain | Selects other surfaces in the same blend chain that have the same radius of curvature
Select Cavity | Selects other surfaces in the same cavity collection. Surfaces bounded by curves where the external angle is greater than 180 degrees.
Select Hole | Selects other surfaces that are within the same hole definition
Select by Name | Selects other entities with the same name. Includes entities with the same name prefix prior to the "@" character if it exists.

## Slide 109: Exercise 8.1 Defeaturing with the GUI
Import the acis file “anc101.sat”
Use the GUI selections and remove operation to simplify so it looks like the image below
Measure the volume before defeaturing
Use the sweep scheme to mesh the defeatured volume
1
2
3
4
list volume 1 geometry
Make a note of the volume of volume 1
Find the volume of the defeatured geometry. Compute the percent difference in volume
5

## Slide 110
Geometry Power Tools are located in the second tab of the PowerTools window.
Geometry Power Tool

## Slide 111
Pick volumes to analyze
Run geometry analysis (disabled until Options… selected)
Geometry analysis output
Additional Geometry Operations
Update analysis after each geometry operation
Select Geometry Diagnostics (Click Here first)
Show Documentation
Display Solution Window
Geometry Power Tool Panel

## Slide 112
Add Additional Diagnostics that use machine learning
Threshold values for Diagnostics
Diagnostic Checks (select only those you want to perform)
Generate diagnostic threshold values automatically
Select Done to return to Power Tool
Fast way to select or unselect diagnostics
Geometry Power Tool Options Panel

## Slide 113
Import anc101.sat
Enter “all” or “1” for volumes to analyze
Select “Options…”
Select “Auto Size”
Select “Select All”
Select “Done”
Select “Analyze”
You should see results in the power tool that look similar to those shown.
Geometry Power Tool Example
1
2
3
4
5
6
7
2
3
7
4
5
6

## Slide 114
Click triangle to expand “Small Surfaces” Diagnostic
Select Surface 94
Right Click to display context menu
Select “Fly In” to zoom into surface 94
Surface 94
Visualize/Selection Options
Relevant Cubit Commands (Jump to Command Panel)
Remove small curves and surfaces
Geometry Power Tool Example
1
2
3
4

## Slide 115
Surface 94
Select Remove Surface
(Command Panel Appears)
Click Apply
Before Surface Remove
After Surface Remove
Note: Surface 94 is auto populated in pickwidget
Remove small curves and surfaces
1
2
Geometry Power Tool Example

## Slide 116
Click Power Tools Tab to return to Geometry Power Tool
Note: Surface 94 and it’s small curves are shown (deleted)
Click Analyze to regenerate diagnostics
Note: Check Auto Update to auto. regenerate every time model changes (slow for large models)
Try the same procedure to remove surface 95
Remove small curves and surfaces
1
2
1
2
3
Geometry Power Tool Example

## Slide 117
Custom Solutions – Remove bad angles
Select Show Solutions
Custom Solution Window
Shows specific solutions for selected entity (vertex 95)
Expand “Bad Vertex Angles” Diagnostic
Select vertex 95 and “Fly-in”
Single Click: Preview and visualize custom solutions
Blunt Tangency Add Material Angle 15
Blunt Tangency Remove Material Angle 30
Collapse Angle 45
Double Click: Execute the solution
Note: Right Click on Solution for additional options (Jump to command panel)
Try same procedure on Vertex 94
Geometry Power Tool Example
1
2
3
4
5
6

## Slide 118
Geometry Traits – Remove chamfer
Expand “Chamfer Chains” Diagnostic
Select and fly into Chain 1
Double Click “Remove Surface” Solution
Geometry Power Tool Example
1
2
3

## Slide 119
Geometry Traits – Remove holes
Note: Holes are not currently displayed because they all have a radius larger than the “hole radius threshold”. Go back to the Options panel to manually change this value.
Click on the Options button
Enter “10” for the “Hole Radius” threshold
Click Done
Click Analyze
Right Click on Holes and “Select All”
Use the “Remove All Holes…” menu option to delete holes with one command
Geometry Power Tool Example
1
2
3
4
5
6

## Slide 120: Exercise 8.2 Geometry Power Tool
Import acis “knuckle.sat”
Mesh with tets using size 2.0
Delete Mesh
Use the Geometry Power Tool to assist in defeaturing. Suggested operations:
Remove Close Loops
  Surface 17
  Surface 15
Heal Bad Geometry
  Bad Curves
Mesh with tets using size 2.0
Delete Mesh and save acis geometry file “knuckle-defeatured.sat”
2
1
3
4
5
6
Original Geometry
Defeatured Geometry

## Slide 121
Predict local mesh quality
  Scaled Jacobian
  In-Radius
  Deviation
Find the most problematic features in the CAD Model
1
For a given local geometry operation
  Remove Surface
  Tweak Replace Surface
  Composite Surfaces
  Collapse Curve
  Etc..
Predict local mesh quality after operation
  Scaled Jacobian
  In-Radius
  Deviation
Find solution that yields best mesh quality
2
For a given local topology
  Small Curve
  Small Surface
  Sharp Angle at Vertex
121
Defeaturing using Machine Learning
tweak remove topology curve
tweak remove topology surface
blunt tangency
remove surface
tweak replace surface
composite surfaces
collapse curve
begin state
end state
121

## Slide 122
Click to add additional diagnostics that use machine learning
Settings used only with Machine Learning Diagnostics
Diagnostics available without ML Models Loaded
1. Predict tet mesh quality on the CAD before meshing
2. Classify volumes based on their predicted function
Two new diagnostics that use Machine Learning:
Without ML
With ML
Geometry Power Tool with Machine Learning

## Slide 123
Import anc101.sat
Enter "all" or "1" for volumes to analyze
Select "Options…"
Select "Auto Size"
Select "Tetmesh Poor Quality Metrics"
Unselect the remainder of the diagnostics
Select "Done"
Select "Analyze"
Geometry Power Tool ML Example
1
2
3
5
6
7
2
3
4
4
5
6
7
8
8

## Slide 124
List of entities predicted to have poor Scaled Jacobian
List of entities predicted to have poor Inradius ratio
r
Predicted minimum Scaled Jacobian near Curve 64
Predicted minimum Inradius ratio near Curve 64
Curve 64
Geometry Power Tool ML Example

## Slide 125
Click Show Solutions
List of proposed solutions for Curve 64 ordered by Scaled Jacobian prediction
Best predicted Solution: Remove Surface 94
Predicted Scaled Jacobian: 0.3977
ML generated Solutions for Curve 64
Right Click:
Execute the solution
Jump to Command Panel
Visualize solution
Single Click: Preview Solution
Double Click: Execute Solution
1
2
Geometry Power Tool ML Example
2

## Slide 126: Exercise 8.3 ML Defeaturing
Import the acis file B3.sat
Mesh with tets using a size of 1.0
Display and record minimum scaled Jacobian and/or Inradius metric. Note the minimums and where the worst quality elements occur
Delete the mesh
Use the Geometry Power Tool with ML to defeature the model
Mesh the volume again and check mesh quality. How has the mesh quality changed
1
2
3
4
5
6