## Slide 1: Tet Meshing Tips
Corey Ernst
CUBIT™ 200 Tutorials (Supplemental)
CUBIT
Geometry and
Mesh Generation Toolkit
SAND2023-13172PE

## Slide 2: Tetmeshing Basics
Tetmeshing using Cubit®
Part I: Geometry Preparation
Part II: Meshing

## Slide 3: Tetmeshing Basics
Part I: Geometry Preparation

## Slide 4: Tetmeshing Basics
Two user Interfaces
Graphical User Interface – Fast, Intuitive.
Commands (Cubit® and python) -- Easy to play back, archive, logging of all operations.
Most operations in the GUI will output a command to the command window (bottom right).
Use commands to build up playable script files.
If you don’t know the command, use the GUI to create the command.
GUI
Commands

## Slide 5: Tetmeshing Basics
Geometry Preparation
Delete irrelevant volumes
Regularize to remove extraneous geometry
Remove small surfaces/holes/cavities/lettering
Find and simplify conical surface at bolt hole bottoms
Use blunt tangency to remove sharp angles
Use the simplify command to combine surfaces (compositing)

## Slide 6: Tetmeshing Basics
Geometry Preparation (modification)
Very seldom is geometry preparation done in single step
Mesh quality almost always drives the geometry modifications
Think of geometry modification as one step in an iterative meshing loop
Import/Create Geometry
Modify Geometry
Evaluate Mesh Quality
Mesh
Smooth Mesh
Export Mesh
Iterative loop
Quality good
Quality poor

## Slide 7: Tetmeshing Basics
Delete irrelevant geometry
GUI
Commands
delete {volume <ids>}
Example
delete volume all except 1

## Slide 8: Tetmeshing Basics
Regularize to simplify geometry
Removes unnecessary topology, which in effect reverses the imprint operation. This can help clean up the model from extra features that are unnecessary for the geometric definition of the model.
before
after

## Slide 9: Tetmeshing Basics
Regularize to simplify geometry
Removes unnecessary topology, which in effect reverses the imprint operation. This can help clean up the model from extra features that are unnecessary for the geometric definition of the model.
Command
Regularize {body <ids>|group <ids>|volume
<ids>|surface <ids>|curve <ids>|vertex <ids>}[keep {curve <ids>|vertex <ids>}]
Example
regularize volume all
GUI

## Slide 10: Tetmeshing Basics
Remove small geometric features
Removing small features (defeaturing) increases element size and quality
If small features are not removed, poor quality elements are generated.
A higher quality mesh is generated when small features are removed.

## Slide 11: Tetmeshing Basics
Remove small surfaces (GUI)
Select small surface
Right-click -> Select Similar Surfaces

## Slide 12: Tetmeshing Basics
Remove small surfaces (GUI)
Select small surface
Right-click -> Select Similar Surfaces
Right-click -> Remove

## Slide 13: Tetmeshing Basics
Remove small surfaces (GUI)
Select small surface
Right-click -> Select Similar Surfaces
Right-click -> Remove
Surfaces are removed!!

## Slide 14: Tetmeshing Basics
Remove blend chains (GUI)
Select small surface
Right-click -> Select Blend Chain

## Slide 15: Tetmeshing Basics
Remove blend chains (GUI)
Select small surface
Right-click -> Select Blend Chain
Right-click -> Remove

## Slide 16: Tetmeshing Basics
Remove blend chains (GUI)
Select small surface
Right-click -> Select Similar Surfaces
Right-click -> Remove
Blends are removed!!

## Slide 17: Tetmeshing Basics
Removing surfaces (Command line)
Remove Surface Commands;
Select surface <ids> include similar
Remove Surface <id_range> [blend_chain] [cavity] [EXTEND|noextend]
[keepsurface] [keep] [TOGETHER | individual | connected_sets] [preview]
Example
select surface 24 include similar
remove surface in selection
Find and Remove Blend Chain Commands:
Select Surface <ids> include blend_chain
Remove Surface <id_range> [blend_chain] [cavity] [EXTEND|noextend] [keepsurface]
[keep] [TOGETHER | individual | connected_sets] [preview]
Example
select surface 24 include similar
remove surface in selection

## Slide 18: Tetmeshing Basics
Removing surfaces (Command line python)
std::vector<int> get_similar_surfaces(std::vector<int> surface_ids,
double tol = 1e-3,
bool use_percent_tol = true,
bool on_similar_vols = true);
std::vector< std::vector<int> > get_blend_chains(int surface_id);
Example
small_surfs = cubit.get_similar_surfaces([223, 126])
cubit.cmd(‘remove surface ‘ + ‘ ‘.join(map(str, small_surfs)))
Example
blend_surfs = cubit. get_blend_chains(223)
cubit.cmd(‘remove surface ‘ + ‘ ‘.join(map(str, blend_surfs)))

## Slide 19: Tetmeshing Basics
Find and simplify conical surfaces at bolt hole bottoms
Use the geometry power tool to quickly find all conical surfaces
Make sure the Power Tools is visible:
View -> Power Tools
Once in the power tool, set the options to look for cone surfaces

## Slide 20: Tetmeshing Basics
Find and Simplify conical surfaces at bolt hole bottoms
Use the geometry power tool to quickly find all conical surfaces
Click ‘Analyze’ and then expand and select the results
Right-click on the results and then select ‘Tweak Cone’
The ‘tweak cone’ panel automatically appears and is populated with all the cone surfaces. Click ‘apply’ and they are converted to planar surfaces.

## Slide 21: Tetmeshing Basics
Find and Simplify conical surfaces at bolt hole bottoms
Use python commands
std::vector<int> get_cone_surfaces(std::vector<int> target_volume_ids);
Example
vol_id = 1
cone_surfs = cubit.get_cone_surfaces(1)
cubit.cmd(‘tweak surface’ + ‘ ‘.join(map(str, cone_surfs)) + ‘ cone’)

## Slide 22: Tetmeshing Basics
Defeaturing – using GUI
Use the power tool to find sharp angles as you did to find cone surfaces

## Slide 23: Tetmeshing Basics
Defeaturing – using GUI
Use Cubit’s blunt tangency commands to remove sharp angles.

## Slide 24: Tetmeshing Basics
Find and Simplify Sharp Vertices
Use python commands
std::vector<std::vector<double>> get_sharp_angle_vertices(
std::vector<int> target_volume_ids,
double upper_bound,
double lower_bound);
Example
vol_ids = [1,2,3]
sharp_verts_info = cubit.get_sharp_angle_vertices(vol_ids, 5.0, 0.0)
sharp_verts = sharp_verts_info[0]
cubit.cmd(‘blunt tangency tweak vertex ’ + ‘ ‘.join(map(str, sharp_verts)))

## Slide 25: Tetmeshing Basics
Simplifying Geometry Using Compositing
Combines surfaces together.
Mesh is not constrained to intermediate curves.
Improves mesh quality.
Does not change CAD model. Can be easily removed.
Subsequent simplify methods use compositing to simplify model.
Original surfaces
Meshed w/o composites
Meshed with composites

## Slide 26: Tetmeshing Basics
Simplify Geometry
Use the ‘simplify’ command to automatically composite neighboring surfaces, eliminating many curves
GUI
Command
Simplify {Volume|Surface|Curve} <Range> [Angle <Value>]
[Respect {Surface <id_range> | Curve <id_range> |
Vertex <id_range> | Imprint}] [local_normals] [Preview]
Example
simplify volume 1

## Slide 27: Tetmeshing Basics
Simplify Geometry
Use the ‘local_normals’ option to combine adjacent surfaces that have nearly identical normal at shared curves
Command
Simplify {Volume|Surface|Curve} <Range> [Angle <Value>]
[Respect {Surface <id_range> | Curve <id_range> |
Vertex <id_range> | Imprint}] [local_normals] [Preview]
Example
simplify volume 1 local_normals

## Slide 28: Tetmeshing Basics
Composite Geometry
To combine surfaces in a more manual approach, use compositing (which simplify does automatically underneath)
In the GUI, select the surfaces, then right-click and select composite
Or use the composite command panel
Command
Composite Create Surface <id_range> [angle <degrees>] [nocurves]
[keep [angle <degrees>] [vertex <id_list>]]
Example
composite create surface 6 2 12

## Slide 29: Tetmeshing Basics
Exercise 1:
Use the defeaturing techniques on the ‘pump.cub’ model
Set ‘trimesh geometry sizing off’
Tetmesh with a size of 0.1.
Defeaturing steps
Delete irrelevant volumes
Regularize to remove extraneous geometry
Remove small surfaces/holes/cavities/lettering
Find and simplify conical surfaces at bolt hole bottoms
Use blunt tangency to remove sharp angles
Use the simplify command to combine surfaces (compositing)
Hint: Use the Geometry Power Tool to:
find small features to remove
find/simplify conical surfaces at bolt hole volumes
sharp angles to use blunt tangency on
Don’t defeature the larger fillets and rounds on underside. Use compositing on them to create large surfaces in the two cavities on the underside.
pump.cub

## Slide 30: Tetmeshing Basics
Part II: Meshing

## Slide 31: Tetmeshing Basics
Geometry Preparation
Set mesh size
Important triangle and tet meshing settings
Set up element blocks
Determine element quality
Improve element quality
Anisotropic tetmeshing
Setting mesh parameters in script file
Export the mesh
tetmesher add mid_edge_nodes on

## Slide 32: Tetmeshing Basics
Set Mesh Size
For triangle/tet meshing, the mesh size can be can be set on volumes, surface, curves, and vertices.
GUI for setting size on volumes
Commands
{Volume|Surface|Curve|Vertex} <range> [Interval] Size <size>
Example
Volume 1 size 0.23

## Slide 33: Tetmeshing Basics
Important triangle and tet meshing settings
The following settings help to further control element size:
Geometry sizing
Triangle gradation
Tet growth factor
Tetmeshing optimization

## Slide 34: Tetmeshing Basics
Geometry Sizing
Geometry sizing adjusts the mesh size so that areas of high curvature receive more elements. It is the default behavior for triangle meshing.
With geometry sizing, triangle meshing will satisfy the smaller of the two size constraints: A) user-defined size or B) size needed to satisfy the geometry approximation angle (15 degrees by default)

## Slide 35: Tetmeshing Basics
Geometry Sizing
Geometry sizing adjusts the mesh size so that areas of high curvature receive more elements. It is the default behavior for triangle meshing.
With geometry sizing, triangle meshing will satisfy the smaller of the two size constraints: A) user-defined size or B) size needed to satisfy the geometry approximation angle (15 degrees by default)
geometry sizing on
Notice small elements result to satisfy geometry approximation angle of 15
Surface size 0.07 for both surfaces
geometry sizing off
Elements respect respected regardless of high curvature

## Slide 36: Tetmeshing Basics
Geometry Sizing
on/off toggle
angle control
GUI
Commands
[surface <ids>] [group <ids>] scheme trimesh
[meshgems] [geometry approximation angle <value=15>] [minimum size <value>]
[set] Trimesher Geometry Sizing {ON|off}
Example
surface 1 scheme trimesh geometry approximation angle 17
set trimesher geometry sizing on

## Slide 37: Tetmeshing Basics
Trimesh Gradation
Triangle gradation controls the rate of growth from small large.
Triangle sizes increase from the small features or mesh
The larger the gradation, the faster the transition
Gradation 1.1
Gradation 1.3
Command
[Set] Trimesher Surface Gradation <value>
GUI

## Slide 38: Tetmeshing Basics
Tet Growth Factor
Controls how fast the tetrahedra sizes transition from small to large within the volume.
Tet sizes increase from the small features or mesh
The larger the gradation, the faster the transition
Growth factor 1.75
Growth factor 1.05
Command
Volume <id_range> Tetmesh growth_factor <1.0 to 10.0 = 1.05>
GUI

## Slide 39: Tetmeshing Basics
Tetmeshing optimization
Controls the degree of optimization used to automatically improve element quality.
Optimization level is an integer in the range 0 to 6
none (0), light (1), medium (2), standard (3), strong (4), heavy (5), and extreme (6)
Higher values will result in greater computation time, however may result in improved mesh quality.
Command
[Set] Tetmesher Optimize Level <level>
GUI

## Slide 40: Tetmeshing Basics
Adding mid edge node during tetmeshing
Automatically creates quadratic edge nodes while generating the tets
Internal, mid edge nodes can be placed optimally by the Meshgems tetmesher, improving element quality.
If this capability is not used, interior mid edge nodes are placed at the midpoint
Command
[Set] Tetmesher Add mid_edge_nodes {on|OFF}
This option is currently not available but will soon be.

## Slide 41: Tetmeshing Basics
Element Blocks
In tetmeshing, element blocks are usually created from volumes
GUI
Command
block <id> [ADD|remove] {group|volume|surface|curve|hex|tet|pyramid|face|tri|edge|node} <id_range> [name <name>]
Example
block 1 volume 1

## Slide 42: Tetmeshing Basics
Element Type of Block Element
Once the blocks are created, element type can be assigned.
If the element type of tet is not assigned, tets will be linear tetra4s
If the element type of a block has higher-order nodes, the node are added at meshing time.
If the volume is already meshed, the nodes are added when setting the element type of the block
GUI
Commands
Block <block_id_range> Element Type <type> [Axisymmetric]
*** Nodes: *** {sphere}
*** Curves: *** {bar | bar2 | bar3 | beam | beam2 | beam3 |
truss | truss2 | truss3 | spring | flatquad}
*** Surfaces: *** {quad | quad4 | quad5 | quad8 | quad9 |
shell | shell4 | shell8 | shell9 |
tri | tri3 | tri6 | tri7 |
trishell| trishell3 | trishell6 | trishell7 |
thexshell | flatwedge | flathex}
*** Volumes: *** {hex | hex8 | hex9 | hex20 | hex27 |
pyramid | pyramid5 | pyramid8 | pyramid13 | pyramid18 |
tetra | tetra4 | tetra8 | tetra10 | tetra14 | tetra15 |
wedge | wedge6 | wedge15 | wedge16 | wedge20 | wedge21}
Example
block 1 element type tetra10

## Slide 43: Tetmeshing Basics
Determining Quality
Several metrics exist for determining element quality
Use the ‘low’ and ‘high’ parameters to isolate poor quality elements
GUI
Commands
Quality { Tet | Volume | Group | Block } <id_range>
[ GLOBAL | Individual ]
{ Algebraic | Allmetrics | Altitude | Aspect Ratio Bet | Aspect Ratio Gam
| Condition No. | Distortion | Element Volume | Inradius | Jacobian
| Mass Increase Ratio | Mean Ratio | Normalized Inradius | Node Distance
| Relative Size | Scaled Jacobian | Shape | Shape and Size
| Timestep | Traditional }
[ High <value> ] [ Low <value> ] [ Top <number> ] [ Bottom <number> ]
[ Draw [HISTOGRAM] [Mesh] [Monochrome] [Add] ]
[ List [Detail] [Ids] [Verbose Errors] [Geometry]]
Example
quality 1 volume 1 scaled jacobian

## Slide 44: Tetmeshing Basics
Improving Element Quality
Modify geometry, as illustrated in Part I. Poor quality elements often reveal additional areas in the geometry that were previously overlooked and need more simplification.
Additional approaches to improve element quality are:
Mesh Smoothing
Collapsing poor quality elements
Removing overconstrained tets
Tri/tet remeshing
Node constraint smart

## Slide 45: Tetmeshing Basics
Mesh Smoothing
Smoothing can occur on volumes, surfaces, or curves, for example: smooth volume 1
Smoothing can also occur on a set of elements, for example: smooth hex 1 to 200
Using commands, set the smooth scheme, then smooth.
Using GUI, select the smooth scheme then apply.
GUI Volume Smoothing
Commands
Volume <range> Smooth Scheme {Laplacian|Equipotential} [Free]
Smooth volume <range>
Example
volume 1 smooth scheme Laplacian
smooth volume 1
Before smooth
After smooth
smooth

## Slide 46: Tetmeshing Basics
Collapsing poor quality elements
Poor quality triangle and tets can be removed with a collapse operation, merging two adjacent nodes of an element
Collapses are performed only if lower quality does not result in the surrounding elements
The metric used in the quality determination can be user-specified
Triangle connected to tets or that are constrained to geometry vg cannot be collapsed
Before collapse
After collapse
Commands
Collapse Edge <ids> [SCALED JACOBIAN|Aspect Ratio|Shape|Shape and Size]
Collapse Tri <ids> [SCALED JACOBIAN|Aspect Ratio|Shape|Shape and Size]
Collapse Tet <ids> [Interior] [Altitude|Aspect Ratio|
Aspect Ratio Gam|Distortion|Inradius|Jacobian|Normalized Inradius|Node
Distance|SCALED JACOBIAN|Shape|Shape and Size|Timestep]
Example
#get all tets with aspect ratio > 20
group ‘bad_tets’ add quality tet all aspect ratio low 20
collapse tet in bad_tets aspect ratio

## Slide 47: Tetmeshing Basics
Node constraint smart
Mid-edge nodes are typically snapped to curved geometry
Sometimes lower quality can result because of this.
Setting node constraint to smart prevents snapping node if quality degrades enough
Mesh accuracy is sacrificed for mesh quality
Node constraint ‘smart’
Node not snapped if below quality
Better quality
Node constraint ‘on’
Node always snapped
Poor quality
Normalized inradius quality = 0.11
Normalized inradius quality = 0.18
Command
Set Node Constraint [{on|off|smart [tet quality
{NORMALIZED INRADIUS|distortion}] [threshold
{<threshold=0.3>}]}]
Example
Set node constraint smart tet quality normalized inradius threshold 0.4

## Slide 48: Tetmeshing Basics
Removing Overconstrained Tets
Overconstrained tets have all four nodes on the surface
Typically very flat and poor quality
Once identified, they can be removed
Identification techniques for finding these tets not covered here
Command
Remove Overconstrained tet <ids>
After
Before

## Slide 49: Tetmeshing Basics
Tri/Tet Remeshing
Convenient way to replace (remesh) a localized set of poor quality triangles or tets, instead of remeshing an entire surface/volume.
Tris/tets can be specified by id or found by exceeding quality metrics
Layers of neighbor elements can be included using the ‘inflate’ parameter
If remeshing triangles, they cannot be in tets
Commands
Remesh Tet <id_range> | [quality <tet_metric>
[less than|greater than] <value> ...] [inflate
<value>][size <value>][FIXED|free][preview]
Remesh Tri <id_range> | [quality <tri_metric>
[less than|greater than] <value> ...] [inflate
<value>][preview]
Example
Remesh tri 195 inflate 1
tri 195
Set of tris to remesh, defined by ‘inflate 1’
Before remesh
After remesh

## Slide 50: Tetmeshing Basics
Two-Layer Anistropic Tetmeshing
Useful for meshing thin-walled structures
Reduces degrees of freedom in the in-plane direction, where resolution not needed
Set mesh size larger than wall thickness
Triangle and tet meshers internally split any mesh edge with both nodes on the boundary
‘split overconstrained’ options split mesh spanning surface and volume boundaries to produce two layers
Use sparingly on small surfaces because it can produce many small elements
Commands
[Set] Trimesher Split Overconstrained Edges {on|off}
[set] tetmesher optimize { { [level <value>] [overconstrained {[edges {on|off}]
[tetrahedra {on|off}]}] [sliver {on|off}] } | default }
Example
reset
create cylinder radius 1 z 2
create cylinder radius 0.9 z 2
sub 2 from 1
volume 1 size 0.25
volume 1 scheme tetmesh
set trimesher split overconstrained edges on
set tetmesher optimize overconstrained edges on
mesh volume 1
draw tet with z_coord < 0 # to see the cross section
Isotropic
65,000 elements
Anisotropic
4,700 elements
Two-Layers Through Thickness Mesh

## Slide 51: Tetmeshing Basics
Setting mesh parameters in script file
Once you find meshing parameters that work well, consider setting them using a set of Cubit commands
This helps to ensure consistent behavior
#trimesh settings
set trimesher surface gradation 1.05
set trimesher geometry sizing off
#tetmesh settings
Set tetmesher optimize level 6
Set node constraint smart threshold 0.25
trimesher surface gradation 1.05

## Slide 52: Tetmeshing Basics
Export Mesh
To export the mesh in Exodus format use the GUI or commands
GUI
Command
Export [Genesis | Mesh] '<filename>' [Dimension {2|3}] [Block <id_list>]
[Qualityfile] [no_ids] [Overwrite] [XML ['<xml_filename>’]]
Example
export mesh ‘final_mesh.g’

## Slide 53: Rocket example
Steve Owen
Trevor Hensley
CUBIT™ 200 Tutorials (Supplemental)
CUBIT
Geometry and
Mesh Generation Toolkit
SAND2023-XXXX

## Slide 54: Thermal Fluid Example
Remove Hardware
Remove Holes
Remove Overlaps
Remove Gaps
Fix Misalignments
Remove small curves and surfaces
Imprint and Merge
Check for small curves and surfaces
Mesh
Check Quality
Fix Geometry if necessary (revisit 1-8)
Generate Enclosures for TF
Boundary Conditions
Journaling, Python Scripting
Geometry: rocket.stp
Procedure
Journal File: rocket.jou
Python Script: rocket.py