## Slide 1: SIERRA/Aria Interactive Demo
Sierra/TF Team
SAND2022-4258 TR
UNCLASSIFIED // UNLIMITED RELEASE
Thermal & Multiphysics Analysis

## Slide 2: Contents
Loading the mesh and input files in SAW
Construct several thermal conduction models to demonstrate basic capabilities in Sierra/Aria
  Simple transient heat conduction with fixed temperature boundaries
  Nonlinear properties and custom flux boundary conditions
  Convective flux boundary conditions
  Radiative flux boundary conditions
  Post-processing
  Multi-physics equation coupling
Visualization in Paraview

## Slide 3: Launching SAW
Right click on the desktop
Choose “Open Terminal”
Type /projects/dart/wb/wb and press enter
Launch SAW (if it’s not already open)
  Click an icon for it if available
  Launch from the command line
Pick a SAW perspective
  “Team (default)” is often most useful for Aria
  “SIERRA Editing” is also decent (but hides the Project Navigator view)
    Add it back with Window » Show View » Other » General » Navigator
alias saw='/projects/dart/wb/wb'
Add this to your ~/.bashrc file if you are like me and can never remember where SAW is
Using SAW is not required to use Aria. Many current Aria users launch commands from the terminal and use a text editor of their choice to edit the input file.
This training will use SAW as a Sierra Editor, but will have terminal commands shown for reference.
example terminal command

## Slide 4: Loading the training files in SAW
Create a new project titled “Sierra100_TF”
1. Click ‘Local-Only Project’ to create an empty project.
2. Right-click on the project and select “Import…”
3. Select the General->File System import option
4. Import from /projects/sierra100/TF directory

## Slide 5: Hands-On Session 1: Basic Heat Conduction
We will start with a basic transient heat conduction problem.
  Open the aria folder and double-click on the heat_cond.i template file.
  We will fill in missing sections as we go through this module. Slides with interactive portions will indicate so in the top right with bold red text.
If you fall behind, the complete version is in heat_cond_session1.i.
  The final version has required syntax in order to run an analysis.

## Slide 6
Hands-On Session 1: Basic Heat Conduction
ClampA
ClampB
CenterRod
Three named blocks
Five named sidesets
EndA
EndB
EndASides
EndBSides
RodSurf
Constant properties
Fixed temperatures on ends
Single material on all blocks
Notes: Using the meshed model we will analyze the Steady-Conduction problem shown.

## Slide 7
All commands lines have
“Scope”
Domain, Procedure or Region
What Scope are we in?
Outline View
Hands-On Session 1: Input File Structure
Notes: The domain is the outer scope.
How does one know what scope we’re in? Use the Outline View

## Slide 8
Domain Level Will Contain Items
That Pertain to All Sierra Applications
Domain Level is defined by
“Begin SIERRA - End SIERRA
Hands-On Session 1: Domain Level
Begin Sierra Aria
Title Aria Heat Conduction Training Model
Notes: The domain

## Slide 9
#-----------------------------------------------
# Define material properties to be used
#-----------------------------------------------
Begin Aria Material aluminum
Density = Constant value = 2770
Specific Heat = Constant value = 800
Thermal Conductivity = Constant value = 175
Heat Conduction = Generalized
End Aria Material aluminum
Transient heat conduction requires
Density
Specific heat
Thermal conductivity
A model for heat flux
Material Name
Hands-On Session 1: Material Properties
Follow along to add specifications to your input file
Format for material properties
PROPERTY = MODEL [MODEL ARGS]
Density = Constant value = 100
Specific Heat = Polynomial order=1 C0=1 C1=1 variable=density
Thermal conductivity = User_Function name = my_fcn X = time
Viscosity = Scalar_String_Function f = "2*temperature"
Refer to the user manual Chapter 4 for a complete list of all available properties and models
(we’ll cover this in more detail in Session 2)
Notes: The domain

## Slide 10
$---------------------------------------------------
$ Specify mesh name and settings
$---------------------------------------------------
Begin Finite Element Model FEModel
Database Name = mesh.g
Use Material aluminum for ClampA ClampB CenterRod
End Finite Element Model FEModel
Associate Materials with Mesh Geometry
Comments
$ or #
Material to assign to blocks
Mesh file
Hands-On Session 1: Domain Level
Follow along to add specifications to your input file
Notes: The previous example had one element block but most real problems will contain many element blocks.

## Slide 11
#-----------------------------------------------
# Linear Solver
#-----------------------------------------------
Begin tpetra equation solver solve_temperature
Begin Preset Solver
Solver Type = Thermal_Symmetric
End
End
Many Solvers are Available in Aria
Direct Solvers
Iterative Solvers
Preset Solvers (common configurations)
Solver block name
Hands-On Session 1: Domain Level

## Slide 12: Hands-On Session 1: Solution Control
$---------------------------------------------------
$ Define temporal solution parameters
$---------------------------------------------------
Begin Solution Control Description
Use System Main
Begin System Main
Begin Transient Solution_block_1
Advance AriaRegion
End
End
$---------------------------------------------------
$ Specify time integration settings
$---------------------------------------------------
Begin Parameters for Transient Solution_Block_1
Start Time = 0.0 # seconds
Termination Time = 600.0 # seconds
Begin Parameters for Aria Region AriaRegion
Time Step Variation = Adaptive
Initial Time Step Size = 0.05
Time Integration Method = BDF2
Maximum Time Step Size = 20.0
Minimum Time Step Size = 0.01
Predictor-Corrector Tolerance = 0.01
End
End
End
Time Block
Parameters
Use adaptive time stepping
Set solution as transient (can use “Begin Sequential” here for a steady state problem)
Set start and end times
Predictor-corrector tolerance controls how the time step size changes
Notes: The solution of a transient problem is much more complex than that of a steady problem.
Here we are using adaptive time stepping.
A large number of parameters are available for controlling the transient solution and those
can be found in the Aria user manual.

## Slide 13
$------------------------------------------------------
$ Region domain - EQs, BCs, ICs, post-processing
$------------------------------------------------------
Begin Aria Region AriaRegion
$---------------------------------------------------
$ Define linear and nonlinear solver parameters
$---------------------------------------------------
Use Linear Solver solve_temperature
Nonlinear Solution Strategy = Newton
Maximum Nonlinear Iterations = 10
Nonlinear Residual Tolerance = 1.e-6
$-----------------------------------------------------------
$ Specify which mesh model to use for this region
$-----------------------------------------------------------
Use Finite Element Model FEModel
Define solver settings for this Region
Hands-On Session 1: Aria Region
References linear solver block defined earlier
Define nonlinear solution strategy (Newton), tolerance, and maximum nonlinear iterations
Define which mesh to use

## Slide 14
Hands-On Session 1: Governing Equation
Follow along to add specifications to your input file
$---------------------------------------------------
$ Specify equations to solve
$---------------------------------------------------
EQ Energy for Temperature on all_blocks using Q1 with Mass Diff
Equation being solved
Heat Conduction = Generalized
Recall that in our material model we defined
Mass
Diff
Pick equation to solve (Energy)
Select valid DOF for the equation (Temperature)
Select element order (Q1 = linear elements)
Select equation terms

## Slide 15: Hands-On Session 1: Initial Conditions
Define the initial condition (required for transient problems)
$---------------------------------------------------
$ Specify initial conditions
$---------------------------------------------------
IC for Temperature on all_blocks = constant value = 300 # K
Select which DOF to apply the IC on
Select where to apply the IC
Select the model to use for the IC
Note: model selection format here is the same pattern as for material properties
[…] = MODEL [MODEL_ARGS]
Check the user manual for a complete list of models, common ones include: constant, user_function, scalar_string_function
Follow along to add specifications to your input file

## Slide 16: Hands-On Session 1: Boundary Conditions
Define fixed temperatures on the end sidesets
$---------------------------------------------------
$ Specify boundary conditions
$---------------------------------------------------
BC Dirichlet for temperature on EndA = constant value = 300 # K
BC Dirichlet for temperature on EndB = scalar_string_function f="350+100*sin(t/300)" # K
Select which DOF to apply the Dirichlet BC on
Select where to apply the BC
Select the model to use for the BC
Note: model selection format here is the same pattern as for material properties
[…] = MODEL [MODEL_ARGS]
Check the user manual for a complete list of models, common ones include: constant, user_function, scalar_string_function
EndA
EndB
Follow along to add specifications to your input file

## Slide 17: Hands-On Session 1: Solution Output
Specify an Exodus output file
$---------------------------------------------------
$ Define contents of Exodus output file
$---------------------------------------------------
Begin Results Output AriaOutput
Title Aria: Transient Training Model
Database Name = heat_cond.e
At Step 0 Interval = 5
Nodal Variables = Solution->Temperature as T
End
Variables to output
Output every 5 steps (can also set output at a time interval)
Output file name
Notes: A successful steady state analysis will have one nonlinear solution step.

## Slide 18: Hands-On Session 1: Launch Aria Job
Let’s launch an Aria job from within the SAW interface:
  Right click the input file » Submit Job » Sierra
  Check the box next to mesh.g to use it with the simulation.
  Choose the “Run in sub-directory” option if you want to keep jobs from overwriting old results
  Choose “Local” for the machine, and set the number of processors on the “Machine” tab
  Select only “Purge Modules” on the “Code Parameters” tab
  Click “Run”
module load sierra
launch –n 4 aria –i heat_cond.i

## Slide 19
Transient solution_block_1: dt = 0.05
Transient Solution_Block_1, step 1, time 5.0000e-02, time step 5.0000e-02, 0.00% complete
Memory Usage: current = 302419968 (288.4 M), high-water-mark = 421240832 (401.7 M)
DEFAULTING PREDICTOR-CORRECTOR_BEGIN_AFTER_STEP = 3.
Equation System AriaRegion->main:
* Step : Transient, Strategy: NEWTON, Time: 5.00e-02, Step: 5.00e-02
* Matrix: Solver: "solve_temperature", Unknowns: 6122, Nonzeros: 83476
* Mesh : Processor 0 of 1: 30689 of 30689 elems, 6122 of 6122 nodes
N O N L I N E A R L I N E A R
---------------------- --------------------------------------
Step Resid Delta Itns Status Resid Asm/Slv Time
---- -------- -------- ---- -------- -------- ---------------
1 2.27e+03 5.80e+02 10 ok 4.07e-07 2.8e-02/2.6e-03
2 9.25e-04 2.83e-04 14 ok 3.20e-07 2.8e-02/2.9e-03
3 2.96e-10 NoOp 2.7e-02
Termination reason: 2.95766e-10 < nonlinear_residual_tolerance(1e-06),
and 0 < nonlinear_correction_tolerance(1e-06)
Nonlinear Residual
Change from last solution
or initial guess
Solver Residual
Assemble and Solve time
Find the log file in your ‘run-<username>-01’ folder and double-click to open it.
Hands-On Session 1: Log File Output
Notes: Open the log file to see details of how the solution went.

## Slide 20: Hands-On Session 1: Log File Output
---------------------------------------------------
There were no errors encountered during parse
There was 1 warning encountered during parse
There were no errors encountered during execution
There were no warnings encountered during execution
+----+----+----+----+----+----+----+----+----+----+----+----+----+----+----+----
SIERRA execution successful.
For region AriaRegion
Number of timesteps (failed) : 0
Number of timesteps ( total) : 190
Number of nonlinear iterations ( total) : 394
Memory Usage: current = 311021568 (296.6 M), high-water-mark = 421838848 (402.3 M)
Ideally no failed steps
Warning
and
Error
Summary
Notes: A good check of how the overall solution went is summarized at the end of transient simulation log file.
Another useful piece of information is the memory usage.

## Slide 21: Hands-On Session 1: What Can One Output?
Variables available for output are listed in the log file
preceding the solution step output
Aria Region "Aria_region" has the following fields available for output:
NODE_RANK Fields:
* physical_coordinates
* pp->HEAT_CONDUCTION
* predicted_solution->TEMPERATURE
* solution->TEMPERATURE
* time_derivative_at_time->TEMPERATURE
FACE_RANK Fields:
* thermal_contact_status
ELEMENT_RANK Fields:
* current_element_volume
* volume_change_ratio
Global Variables:
* p_inner

## Slide 22: Hands-On Session 1: Visualize Results
Find the output files (heat_cond.e.4.x) in the Project Navigator
Right click on the root file (.e.4.0) » Visualize » Launch ParaView » Run
Select the variables to show and click “Apply”
Go to the last time step (1), then pick “T” to view the temperature (2)
1
2
3
4
If you show “T” first, the color scale will be off when you go to the final time. Use the “rescale” button (3) to fix it.
Click “Play” (4) to watch the temperature evolve.
module load viz
paraview heat_cond.e.4.0

## Slide 23: Hands-On Session 1: Visualize Results
Click the Clip filter (1) then “Apply” to cut the model in half
1
2
Select “Surface with Edges” (2) to view the mesh

## Slide 24: Hands-On Session 2: Multiple Materials & Flux Boundaries
ClampA
ClampB
CenterRod
Three named blocks
Five named sidesets
EndA
EndB
EndASides
EndBSides
RodSurf
Temperature-dependent properties
Fixed temperatures on one end and varying heat flux on the other
Different material on center rod
If you fall behind, the complete version is in heat_cond_session2.i

## Slide 25
Begin Aria Material aluminum
Density = Constant value = 2770
Specific Heat = Constant value = 800
Thermal Conductivity = Constant value = 175
Heat Conduction = Generalized
End Aria Material aluminum
Begin Aria Material ss304
Density = Constant value = 8000
Specific Heat = Polynomial Variable=Temperature order=1 C0=500 C1=0.1
Thermal Conductivity = User_Function name=ssteel_k_function X=temperature
Heat Conduction = Generalized
End Aria Material ss304
Begin Definition for Function ssteel_k_function
Type is Piecewise Linear
Begin Values
#T (K) k (W/mK)
173.15 10.8857
273.15 13.3978
373.15 16.3285
773.15 21.7714
973.15 25.9582
3500.0 25.9582
End Values
End Definition for Function ssteel_k_function
Hands-On Session 2: Material Properties
Follow along to add specifications to your input file
Add a new material, including some more complicated properties
Specific Heat = Scalar_String_Function f = "500 + 0.1*temperature"
Alternate Cp Model:
Notes: The domain

## Slide 26: Hands-On Session 2: How to find valid commands?
Option 1: Using SAW
Click on the text of the property you want to find a model for (e.g. “Thermal conductivity”)
Look in the drop-down menu in the SAW “Settings” window

## Slide 27: Hands-On Session 2: How to find valid commands?
Option 2: Using the Aria User Manual PDF
Right click in the input file in SAW and choose “View User Guide” or use the link below
Use the PDF menu to go to Chapter 4 – Material Properties » T » Thermal Conductivity
Click on a specific model to read the documentation
https://compsim.sandia.gov/compsim/Docs/Sierra/5.6/GeneralRelease/

## Slide 28
$---------------------------------------------------
$ Specify mesh name and settings
$---------------------------------------------------
Begin Finite Element Model FEModel
Database Name = mesh.g
Use Material aluminum for ClampA ClampB
Use Material ss304 for CenterRod
End Finite Element Model FEModel
Assign the new material to the “CenterRod” block
Hands-On Session 2: Assign Materials
Follow along to add specifications to your input file
ClampA
ClampB
CenterRod

## Slide 29: Hands-On Session 2: Boundary Conditions
Define a sinusoidal function for flux on EndB
$---------------------------------------------------
$ Specify boundary conditions
$---------------------------------------------------
BC Dirichlet for temperature on EndA = constant value = 300 # K
BC Flux for Energy on EndB = scalar_string_function f = "-5e4*sin(t/300)"
Select which Equation to apply the Flux BC on
Select the model to use for the BC
Note: Sign convention for flux BCs is positive = outflux
Check the user manual for a complete list of flux BC models, common ones include: constant, user_function, scalar_string_function
EndA
EndB
Follow along to add specifications to your input file

## Slide 30: Hands-On Session 2: Post-Process Flux
$---------------------------------------------------
$ Post-processing
$---------------------------------------------------
Postprocess integrated_flux of equation energy on EndA as FluxA
Postprocess integrated_flux of equation energy on EndB as FluxB
Use the integrated_flux post-processor to get a global variable
Select which equation to get flux of
Define the output variable name
$---------------------------------------------------
$ Define contents of Exodus output file
$---------------------------------------------------
Begin Results Output AriaOutput
Title Aria: Transient Training Model
Database Name = heat_cond.e
At Step 0 Interval = 5
Nodal Variables = Solution->Temperature as T
Global Variables = FluxA
Global Variables = FluxB
End
Add the globals to output
Follow along to add specifications to your input file

## Slide 31: Hands-On Session 2: Launch Aria Job
Let’s launch an Aria job from within the SAW interface:
  Right click the input file » Submit Job » Sierra
  Check the box next to mesh.g to use it with the simulation.
  Choose the “Run in sub-directory” option if you want to keep jobs from overwriting old results
  Choose “Local” for the machine, and set the number of processors on the “Machine” tab
  Click “Run”

## Slide 32: Hands-On Session 2: Visualize Results
Find the output files (heat_cond.e.4.x) in the Project Navigator
Right click on the root file (.e.4.0) » Visualize » Launch ParaView » Run
Select the variables to show and click “Apply”
Plot Global Variables:
Filters » Data Analysis » Plot Global Variables Over Time » Apply

## Slide 33: Hands-On Session 3: Convective Flux Boundaries
ClampA
ClampB
CenterRod
Three named blocks
Five named sidesets
EndA
EndB
EndASides
EndBSides
RodSurf
Temperature-dependent properties
Fixed temperatures on one end and flux on the other
Different material on center rod
Convection on outer surfaces
If you fall behind, the complete version is in heat_cond_session3.i

## Slide 34: Hands-On Session 3: Convection
h (w/m2 K)
Buoyancy driven (free/natural convection) flows 5-25
Forced convection flows
  Gases 25-250
  Liquids 50-20,000
Flows with phase change (boiling and condensation) 2,400-100,000
Three distinct usages of the engineering model arise:
Natural convection and forced convection are currently supported

## Slide 35: Hands-On Session 3: Convection
Heat transfer to a surrounding fluid occurs through a thermal boundary layer at the solid surface. Rigorous modeling of this process requires a CFD numerical analysis.
This process is often simulated with a simplified model of
the surface heat flux,
h - convective coefficient
T - surface temperature
Tref - fluid reference temperature

## Slide 36: Hands-On Session 3: Convection
where is the thermal conductivity of the fluid and
is a characteristic length scale of the problem
A number of correlations exist for the Nusselt number .
These coefficients are often obtained through experimental correlations
Analytically the convective coefficients are shown to be
functions of the Nusselt number, Nu
Free/Natural convection – Nu(Ra) Raleigh Number
Forced convection – Nu(RePr) Reynolds and Prandtl Number

## Slide 37: Hands-On Session 3: Convection
Aria has several ways of modeling convective flux
Pre-Computed h
Bulk Node + Correlation
Advective Bar + Correlation
Full CFD Solve
Calculate a constant h or use a simple expression.
Use a prescribed reference temperature.
This is what we will do today
Use a convective correlation from the built-in library.
Solve an energy equation for a single fluid temperature.
Use a convective correlation from the built-in library.
Solve an energy equation for varying fluid temperature with a simple 1D flow model.
Couple with a full non-isothermal CFD solve

## Slide 38: Hands-On Session 3: Boundary Conditions
Use mesh groups to apply a BC to a group of sidesets
$---------------------------------------------------
$ Specify boundary conditions
$---------------------------------------------------
BC Dirichlet for temperature on EndA = constant value = 300 # K
BC Flux for Energy on EndB = Constant value = -5e4
Mesh Group clamp_conv = EndASides EndBSides
BC Flux for Energy on clamp_conv = Nat_Conv H=5 T_ref=250
BC Flux for Energy on RodSurf = Nat_Conv H=10 T_ref=250
“Model” here is “Nat_Conv”
The “Nat_Conv” model takes H and T_Ref parameters
Define a mesh group
EndA
EndB
Follow along to add specifications to your input file
EndASides
EndBSides
RodSurf
Change to a constant flux

## Slide 39: Hands-On Session 3: Post-Process Flux
$---------------------------------------------------
$ Post-processing
$---------------------------------------------------
Postprocess integrated_flux of equation energy on EndA as FluxA
Postprocess integrated_flux of equation energy on EndB as FluxB
Postprocess integrated_flux of equation energy on clamp_conv as ClampConvLoss
Postprocess integrated_flux of equation energy on RodSurf as RodConvLoss
Postprocess value of expression heat_conduction on all_blocks as HeatFlux
Postprocess value of expression energy_flux on RodSurf as ConvFlux
Add new flux post-processors
Post-process some fields
Heat conduction is the quantity defined in the material model (Fourier’s law)
Energy flux is the applied boundary flux (convection)
Heat Conduction = Generalized
Recall that in our material model we defined
Follow along to add specifications to your input file

## Slide 40: Hands-On Session 3: Post-Process Flux
$---------------------------------------------------
$ Define contents of Exodus output file
$---------------------------------------------------
Begin Results Output AriaOutput
Title Aria: Transient Training Model
Database Name = heat_cond.e
At Step 0 Interval = 5
Nodal Variables = Solution->Temperature as T
Nodal Variables = ConvFlux
Nodal Variables = HeatFlux
Global Variables = FluxA
Global Variables = FluxB
Global Variables = ClampConvLoss
Global Variables = RodConvLoss
End
Add the globals to output
Add the new fields
Follow along to add specifications to your input file

## Slide 41: Hands-On Session 3: Launch Aria Job
Let’s launch an Aria job from within the SAW interface:
  Right click the input file » Submit Job » Sierra
  Check the box next to mesh.g to use it with the simulation.
  Choose the “Run in sub-directory” option if you want to keep jobs from overwriting old results
  Choose “Local” for the machine, and set the number of processors on the “Machine” tab
  Click “Run”

## Slide 42: Hands-On Session 3: Visualize Results
Find the output files (heat_cond.e.4.x) in the Project Navigator
Right click on the root file (.e.4.0) » Visualize » Launch ParaView » Run
Select the variables to show and click “Apply”
Go to the last time step (1), then pick “ConvFlux” to view the convective flux (2). Rescale (3) if needed.
1
2
3

## Slide 43: Hands-On Session 3: Visualize Results
1
2
Slice the domain (1) and click “Apply”, then apply a Glyph filter (2)
Choose “heatflux_” for the orientation and scale array, and set a scale factor of 1e-7.
Click “Apply”.

## Slide 44: Hands-On Session 4: Radiative Flux Boundaries
ClampA
ClampB
CenterRod
Three named blocks
Five named sidesets
EndA
EndB
EndASides
EndBSides
RodSurf
Temperature-dependent properties
Fixed temperatures on one end and flux on the other
Different material on center rod
Convection & radiation on outer surfaces
If you fall behind, the complete version is in heat_cond_session4.i

## Slide 45: Hands-On Session 4: Far-Field Radiative Flux BC
Stefan Boltzmann constant - s
Emissivity - e
Form Factor/View Factor - F
Notes: Most of us are familiar with radiative exchange between two surfaces. This follows directly from
exchange between single facets of the the enclosure. Here the relevant view factor must be known.

## Slide 46: Hands-On Session 4: Radiation
Calculate a constant view factor.
Use a prescribed reference temperature.
This is what we will do today
Aria has several ways of modeling radiative flux
Pre-Computed View Factor to Uniform Environment
Enclosure Radiation
Participating Media Radiation
Compute view factors and perform a full radiosity solve on defined enclosures.
Supports closed or partial (open to an external environment) enclosures.
Can be expensive for large enclosures.
Couple with Nalu to use a discrete ordinates approach to solve a participating media radiation equation.
Requires a meshed enclosure.
Least tightly coupled option to energy equation.

## Slide 47: Hands-On Session 4: Boundary Conditions
Enclose mathematical operations inside {} to have aprepro evaluate them (e.g. {0.9*5.67e-8})
You can also define variables inside {} for aprepro to use
$---------------------------------------------------
$ Specify boundary conditions
$---------------------------------------------------
BC Dirichlet for temperature on EndA = constant value = 300 # K
BC Flux for Energy on EndB = Constant value = -5e4
Mesh Group clamp_conv = EndASides EndBSides
Mesh Group rad_surfs = all_surfaces - EndA - EndB
BC Flux for Energy on clamp_conv = Nat_Conv H=5 T_ref=250
BC Flux for Energy on rod_conv = Nat_Conv H=10 T_ref=250
# emissivity = {e = 0.9}
# sigma = {sigma = 5.67e-8}
BC Flux for Energy on rad_surfs = Rad T_ref=250 Crad = {e*sigma}
“Model” here is “Rad”
The “Rad” model takes Crad and T_Ref parameters
EndA
EndB
Follow along to add specifications to your input file
EndASides
EndBSides
RodSurf
Define a new mesh group

## Slide 48: Hands-On Session 4: Post-Process Flux
$---------------------------------------------------
$ Post-processing
$---------------------------------------------------
Postprocess integrated_flux of equation energy on EndA as FluxA
Postprocess integrated_flux of equation energy on EndB as FluxB
Postprocess integrated_flux of equation energy on clamp_conv as ClampConvLoss
Postprocess integrated_flux of equation energy on RodSurf as RodConvLoss
Postprocess value of expression heat_conduction on all_blocks as HeatFlux
Postprocess value of expression energy_flux on RodSurf Model Nat_Conv as ConvFlux
Postprocess value of expression energy_flux on RodSurf Model Rad as RadFlux
By default “energy_flux” is the sum of all boundary energy fluxes
We can use the “Model” argument to get the flux from specific BC models
Follow along to add specifications to your input file

## Slide 49: Hands-On Session 4: Post-Process Flux
$---------------------------------------------------
$ Define contents of Exodus output file
$---------------------------------------------------
Begin Results Output AriaOutput
Title Aria: Transient Training Model
Database Name = heat_cond.e
At Step 0 Interval = 5
Nodal Variables = Solution->Temperature as T
Nodal Variables = ConvFlux
Nodal Variables = HeatFlux
Nodal Variables = RadFlux
Global Variables = FluxA
Global Variables = FluxB
Global Variables = ClampConvLoss
Global Variables = RodConvLoss
End
Add the new field
Follow along to add specifications to your input file

## Slide 50: Hands-On Session 4: Launch Aria Job
Let’s launch an Aria job from within the SAW interface:
  Right click the input file » Submit Job » Sierra
  Check the box next to mesh.g to use it with the simulation.
  Choose the “Run in sub-directory” option if you want to keep jobs from overwriting old results
  Choose “Local” for the machine, and set the number of processors on the “Machine” tab
  Click “Run”

## Slide 51: Hands-On Session 4: Visualize Results
Find the output files (heat_cond.e.4.x) in the Project Navigator
Right click on the root file (.e.4.0) » Visualize » Launch ParaView » Run
Select the variables to show and click “Apply”
Go to the last time step (1), then pick “RadFlux” to view the radiative flux (2). Rescale (3) if needed.
1
2
3

## Slide 52: Hands-On Session 4: Visualize Results
Choose “Clip” (1) and click “Apply” (clipping normal 1 0 0)
1
Important: Select the original data set again in the pipeline browser (heat_cond.e.4.0)
Choose “Clip” (1) again, change the normal to -1 0 0, then click “Apply”
1

## Slide 53: Hands-On Session 4: Visualize Results
Select “ConvFlux” for the second clipped geometry to compare convective and radiative flux along the center rod

## Slide 54: Hands-On Session 5: Multiphysics Coupling
ClampA
ClampB
CenterRod
Three named blocks
Five named sidesets
EndA
EndB
EndASides
EndBSides
RodSurf
Temperature-dependent properties
Fixed temperatures on both ends
Different material on center rod
Convection & radiation on outer surfaces
Electrical current and joule heating
If you fall behind, the complete version is in heat_cond_session5.i

## Slide 55
Begin Aria Material aluminum
Density = Constant value = 2770
Specific Heat = Constant value = 800
Thermal Conductivity = Constant value = 175
Heat Conduction = Generalized
Electrical Conductivity = Constant Value = 10000 # S/m
Current Density = Ohms_Law
End Aria Material aluminum
Begin Aria Material ss304
Density = Constant value = 8000
Specific Heat = Polynomial Variable=Temperature order=1 C0=500 C1=0.1
Thermal Conductivity = User_Function name=ssteel_k_function X=temperature
Heat Conduction = Generalized
Electrical Conductivity = Constant Value = 0.1 # S/m
Current Density = Ohms_Law
End Aria Material ss304
Hands-On Session 5: Material Properties
Follow along to add specifications to your input file
Electrical transport equation requires an electrical conductivity and a current density (flux) model for each material
Notes: The domain

## Slide 56
#-----------------------------------------------
# Linear Solver
#-----------------------------------------------
Begin tpetra equation solver solve_temperature
Begin Preset Solver
Solver Type = Multiphysics
End
End
Hands-On Session 5: Update Solver
The “Thermal” and “Multiphysics” solvers use more robust preconditions – “Multiphysics” does well for this problem.
Follow along to add specifications to your input file

## Slide 57
Hands-On Session 5: Governing Equation
Follow along to add specifications to your input file
$---------------------------------------------------
$ Specify equations to solve
$---------------------------------------------------
EQ Energy for Temperature on all_blocks using Q1 with Mass Diff Src
EQ Current for Voltage on all_blocks using Q1 with Diff
Equations being solved
Current Density = Ohms_Law
Recall that in our material model we defined
Diff
Pick equation to solve (Current)
Select valid DOF for the equation (Voltage)
Add source term to energy equation
= Electrical conductivity
Mass
Diff
Src
This will construct a single linear system with both equations and all coupling sensitivities.
You can also build multiple linear systems by putting different equations into “Equation System” blocks in the Region. In this case, each equation system will be solved in the order they appear in the input file.

## Slide 58
Hands-On Session 5: Source Term
Follow along to add specifications to your input file
$---------------------------------------------------
$ Specify source terms
$---------------------------------------------------
Source for Energy on all_blocks = joule_heating
Source model is “joule_heating” – takes no additional arguments
Check the Aria user manual for a list of all available source models for each equation

## Slide 59: Hands-On Session 5: Boundary Conditions
Change ends to fixed temperature
Evaluate how much the object is heated by current
$---------------------------------------------------
$ Specify boundary conditions
$---------------------------------------------------
BC Dirichlet for temperature on EndA = constant value = 300 # K
BC Dirichlet for temperature on EndB = constant value = 300 # K
Mesh Group clamp_conv = EndASides EndBSides
Mesh Group rad_surfs = all_surfaces - EndA - EndB
BC Flux for Energy on clamp_conv = Nat_Conv H=5 T_ref=250
BC Flux for Energy on rod_conv = Nat_Conv H=10 T_ref=250
# emissivity = {e = 0.9}
# sigma = {sigma = 5.67e-8}
BC Flux for Energy on rad_surfs = Rad T_ref=250 Crad = {e*sigma}
BC Dirichlet for Voltage on EndA = constant value = 0
BC Flux for Current on EndB = constant value = -100 # Amps/m2
EndA
EndB
Follow along to add specifications to your input file
EndASides
EndBSides
RodSurf

## Slide 60: Hands-On Session 5: Post-Process Energy Source
$---------------------------------------------------
$ Post-processing
$---------------------------------------------------
Postprocess integrated_flux of equation energy on EndA as FluxA
Postprocess integrated_flux of equation energy on EndB as FluxB
Postprocess integrated_flux of equation energy on clamp_conv as ClampConvLoss
Postprocess integrated_flux of equation energy on RodSurf as RodConvLoss
Postprocess value of expression heat_conduction on all_blocks as HeatFlux
Postprocess value of expression energy_flux on RodSurf Model Nat_Conv as ConvFlux
Postprocess value of expression energy_flux on RodSurf Model Rad as RadFlux
Postprocess value of expression energy_source on all_blocks as Esrc
Postprocess value of expression current_density on all_blocks as Current
By default “energy_source” is the sum of all energy source terms
We can use the “Model” argument to get specific source models (not needed here)
Follow along to add specifications to your input file

## Slide 61: Hands-On Session 5: Update Output
$---------------------------------------------------
$ Define contents of Exodus output file
$---------------------------------------------------
Begin Results Output AriaOutput
Title Aria: Transient Training Model
Database Name = heat_cond.e
At Step 0 Interval = 5
Nodal Variables = Solution->Temperature as T
Nodal Variables = Solution->Voltage as V
Nodal Variables = Current
Nodal Variables = ConvFlux
Nodal Variables = HeatFlux
Nodal Variables = RadFlux
Nodal Variables = Esrc
Global Variables = FluxA
Global Variables = FluxB
Global Variables = ClampConvLoss
Global Variables = RodConvLoss
End
Add the new fields
Follow along to add specifications to your input file

## Slide 62: Hands-On Session 5: Launch Aria Job
Let’s launch an Aria job from within the SAW interface:
  Right click the input file » Submit Job » Sierra
  Check the box next to mesh.g to use it with the simulation.
  Choose the “Run in sub-directory” option if you want to keep jobs from overwriting old results
  Choose “Local” for the machine, and set the number of processors on the “Machine” tab
  Click “Run”

## Slide 63: Hands-On Session 5: Visualize Results
Find the output files (heat_cond.e.4.x) in the Project Navigator
Right click on the root file (.e.4.0) » Visualize » Launch ParaView » Run
Select the variables to show and click “Apply”
Go to the last time step (1), then pick “T” to view the temperature (2). Rescale (3) if needed.
1
2
3

## Slide 64: Hands-On Session 5: Visualize Results
Do a slice (1), click “Apply”, then select the Esrc (2) energy source variable.
2
1
As expected, the Joule heating source is concentrated in the low conductivity rod

## Slide 65: Hands-On Session 5: Visualize Results
Make a Glyph (1) of the current vector (set scale factor to 1e-5)
1
What would the current flow look like if the rod had high conductivity and the clamps had low conductivity?

## Slide 66: Hands-On Session 6: Advanced Post-processing
ClampA
ClampB
CenterRod
Three named blocks
Five named sidesets
EndA
EndB
EndASides
EndBSides
RodSurf
Temperature-dependent properties
Fixed temperatures on both ends
Different material on center rod
Convection & radiation on outer surfaces
Electrical current and joule heating
Post-processing points and functions
If you fall behind, the complete version is in heat_cond_session6.i

## Slide 67: Hands-On Session 6: Advanced Post-processing
ClampA
ClampB
CenterRod
Get temperature at rod center
Get average rod temperature in Celsius
Calculate and output a custom function of voltage and temperature
(0,0,0)

## Slide 68: Hands-On Session 6: Post-Process Point & Function
$---------------------------------------------------
$ Post-processing
$---------------------------------------------------
…
Postprocess value of expression energy_source on all_blocks as Esrc
Postprocess value of expression current_density on all_blocks as Current
Begin data probe Tpoints
Nodal_Location solution->temperature location = 0 0 0 label Trod
End
Postprocess average of function "temperature-273.15" on CenterRod as TavgC
Postprocess value of function "voltage / (density*specific_heat*temperature)" on all_blocks as VEratio
We have used string functions in a few different contexts. What is allowed?
Variables time (t), position (x,y,z), or any provided material property or equation DOF
Many standard math functions (sin/cos/exp/log) plus some non-standard helpers (ramps, smooth transitions, min/max)
Boolean logic
  300 + (x>3)*4
  40 + (y<2 ? 5 : 6)
Follow along to add specifications to your input file
Common reduction types: integral, average, min, max

## Slide 69: Hands-On Session 6: Heartbeat Output
$---------------------------------------------------
$ Define contents of Exodus output file
$---------------------------------------------------
Begin Results Output AriaOutput
Title Aria: Transient Training Model
…
Nodal Variables = VERatio
End
Begin Heartbeat AriaTxtOutput
Stream name = stats.csv
Format = csv
At Step 0 increment = 1
Variable is Global time
Variable is Global FluxA
Variable is Global FluxB
Variable is Global ClampConvLoss
Variable is Global RodConvLoss
Variable is Global Trod
Variable is Global TavgC
End
Follow along to add specifications to your input file
Heartbeat block outputs a text file – can include global variables here

## Slide 70: Hands-On Session 6: Launch Aria Job
Let’s launch an Aria job from within the SAW interface:
  Right click the input file » Submit Job » Sierra
  Check the box next to mesh.g to use it with the simulation.
  Choose the “Run in sub-directory” option if you want to keep jobs from overwriting old results
  Choose “Local” for the machine, and set the number of processors on the “Machine” tab
  Click “Run”

## Slide 71: Hands-On Session 6: Visualize Results
Find the output files (heat_cond.e.4.x) in the Project Navigator
Right click on the root file (.e.4.0) » Visualize » Launch ParaView » Run
Select the variables to show and click “Apply”
Go to the last time step (1), then pick “VERatio” to view the custom function (2). Rescale (3) if needed.
1
2
3

## Slide 72: Hands-On Session 6: Visualize Results
time, FluxA, FluxB, ClampConvLoss, RodConvLoss, Trod, TavgC
0.00000e+00, 0.00000e+00, 0.00000e+00, 0.00000e+00, 0.00000e+00, 3.00000e+02, 2.68500e+01
5.00000e-02, 3.10933e-02, 2.47897e-02, -1.06856e+01, -2.33230e+00, 3.00097e+02, 2.69007e+01
1.00000e-01, 1.06762e-01, 1.00397e-01, -1.05773e+01, -2.33697e+00, 3.00194e+02, 2.69511e+01
1.50000e-01, 1.67032e-01, 1.62250e-01, -1.05090e+01, -2.34161e+00, 3.00291e+02, 2.70015e+01
1.78008e-01, 1.95941e-01, 1.92050e-01, -1.04832e+01, -2.34421e+00, 3.00345e+02, 2.70296e+01
2.34023e-01, 2.48029e-01, 2.45288e-01, -1.04435e+01, -2.34939e+00, 3.00454e+02, 2.70858e+01
Check the stats.csv file – includes Trod and TavgC columns

## Slide 73: Conclusion
Final questions?
Consultation on features you’re interested in?

## Slide 74: Hands-On Open Session: General Usage
Finding syntax for other features?
User Manual
SAW or Sierra Editor

## Slide 75: Hands-On Open Session: Command Syntax View
There are a large number of Region level input commands
In the Editor Mode One can
select commands to be
Imported into the input file