## Slide 1: Overview of the Zapotec Training Course
Computational Shock and Multi-Physics (1431)
Sandia National Laboratories
Albuquerque NM
Sandia is a multiprogram laboratory operated by Sandia Corporation, a Lockheed Martin Company, for the United States Department of Energy under contract DE-AC04-94AL85000.
Monte Alban Ruins
The Zapotecs were an ancient civilization that thrived in the Oaxaca Valley between 500 BC and 1500 AD. They were the first to develop the Mesoamerican calendar.
Notes: The Zapotecs were an ancient civilization that thrived in the Valley of Oaxaca in western Mexico between 500 BC and 1500 AD. The civilization began its decline around 700 AD for unknown reasons.
Before getting started, give administrative remarks:
- Restroom location
- Coffee, juice, food, ...

## Slide 2: What is Zapotec?
Zapotec is a coupled Euler-Lagrange computer code
In practice, we couple two production codes, CTH and Sierra/SM
  CTH: Eulerian shock physics code
  Sierra/SM: explicit Lagrangian, finite element code
Zapotec handles the interaction between Eulerian and Lagrangian materials in the problem
CTH, Sierra/SM, and Zapotec developed at Sandia National Laboratories
Notes: Get a survey of student backgrounds, i.e., experience with CTH or FE codes (Sierra/SM, Sierra/SMeD, Dyna, Abaqus, or EPIC).

## Slide 3: History
1985 CTH
1989 Pronto3D
1994 Zapotec (CTH-EPIC)
  Serial link, funded by DTRA and SNL
  Focus on penetration applications
1996 Zapotec linked with Pronto3D (SNL LDRD)
1997 Parallel CTH (SNL CSRF, DOD/DOE MOU)
1998 Parallel Pronto3D (ASCI, DOD/DOE MOU)
1999 Parallel Zapotec (ASCI, SNL CSRF, ARL)
2001-2005 Development of Zapotec through ARL and ERDC
2014 Start of work to link Zapotec to Sierra/SM
2015-2016 Funding from ERDC to finish Sierra/SM coupling
Notes: Time line for Zapotec development. Original Zapotec development started around 1994, with the algorithm implementation done by John Prentice, Quetzal Computational Associates.

## Slide 4: Zapotec Collaborators
John Prentice (SCI-TAC LLC)
Paul Yarrington (SNL)
Don Peterson (SNL, retired)
Steward Silling (SNL)
Richard Koteras (SNL)
Courtenay Vaughan (SNL)
Ray Bell (SNL)
Sue Goudy (SNL)
Steve Attaway (SNL)
Bob Cole (Orion International Technologies)
Greg Bessette (ERDC)
Arne Gullerud (SNL)
Jeromy Hollenshead (SNL)
Sierra/SM code team
Others…

## Slide 5: Course Objectives
Provide an introduction to Zapotec
  Methodology
  Problem development and application
  Hands-on examples to illustrate code features
This course will NOT provide training for CTH and Sierra/SM
  Focus only on aspects directly related to Zapotec
  Training for those codes are available elsewhere
You will NOT be experts after taking this course
This class will provide the background to develop and run Zapotec applications

## Slide 6: Export Controlled Information
CTH, Sierra/SM, and Zapotec have been designated as Export Controlled Information (ECI)
  Export is defined as transmission of information to citizens of foreign countries (including U.S. allies)
  Dissemination of CTH, Sierra/SM, and/or Zapotec is regulated via their respective Software Licensing Agreements and by all applicable United States laws, regulations, rules, and decrees, including, but not limited to, the U.S. Foreign Corrupt Practices Act, the Export Administration Act, the U.S. Anti-Boycott Laws, and the International Traffic in Arms Regulations (ITAR)
  Violations of the export control laws are subject to administrative, civil, and criminal penalties
The software is ECI; however, this class is unlimited release

## Slide 7: Zapotec Overview

## Slide 8: Objectives
Introduction to Zapotec
Overview of the coupling algorithm
Problem development and typical applications

## Slide 9: Overview
Coupled Euler-Lagrange computer code
  In practice we couple two production codes, CTH and Sierra/SM
  Only consider 3D applications
  Units are centimeter-gram-seconds (CGS)
Typical Zapotec applications
  Impact/Penetration
  Blast loading on structures
  Hypervelocity impacts
  Vulnerability and safety analyses
Notes: We use a coupled approach to solve a class of problems not readily handled by Eulerian or Lagrangian methods alone. The class of problems we want to solve with Zapotec usually involve large material deformations, high strain rates, and multi-body contact. Also, the materials in the problem generally exhibit vastly differing strengths and degrees of deformation. It is the later physical characteristic which drives the need for a coupled solution approach.

## Slide 10: Lagrangian vs. Eulerian
Lagrangian
  Treatment of a continuum variable from a frame of reference fixed w.r.t. the material
  In a Lagrangian mesh, nodes and material points are coincident, i.e., the mesh moves with the material
Eulerian
  Treatment of a continuum variable from a fixed frame of reference with the reference mesh chosen to coincide with the spatial coordinates
  In an Eulerian mesh, nodes are fixed in space while material points move through the reference mesh
Notes: Before discussing Zapotec further, it is useful to first define Lagrangian and Eulerian methods.
There are a number of Lagrangian methods (e.g., finite elements, finite difference, meshless methods). Throughout this course, when we refer to Lagrangian methods, we are really referring to the finite element method. The same holds for Eulerian methods, where references to Eulerian really mean a reference to CTH.

## Slide 11: Why consider a coupled approach?
Lagrangian methods
  Major Strengths
    Material interfaces explicitly defined -> well-suited for contact-impact problems
    Ideal for complex, structural response applications
  Major Weakness
    Large material deformations -> large mesh distortions -> degrades solution accuracy and can stop the calculation
Eulerian methods
  Major Strengths
    Can handle large material deformations and/or mixing of materials
    Ideal for hydrodynamic applications
  Major Weakness
    Modeling constitutive response for structural analysis problems
    Treatment of multi-body contact
We use coupled methods to solve problems not readily handled by either Lagrangian or Eulerian methods alone, i.e., those problems in the gray area
Notes: Here are some strengths and weaknesses of Lagrangian and Eulerian methods.
Strength of Lagrangian methods:
Material interfaces are explicitly defined. This allows us to correctly enforce the contact conditions between materials, i.e., enforcement of the no penetration condition and frictional effects.
Lagrangian methods are well suited for large, complex, multi-body structural analysis applications.
Also, since the mesh moves with the material, there are advantages for material modeling since the history of deformation is known.
Speed of computation
Weakness of Lagrangian methods:
Mesh distortion degrades solution accuracy, potentially leading to a negative volume computation that stops the calculation
Mesh generation is difficult and time consuming. Specification of boundary and initial conditions can also be time consuming.
Strength of Eulerian methods:
With Eulerian methods, the material flows through the mesh. Thus, these methods are well suited to model large material deformations and mixing.
They are ideal for hydrodynamic applications, which is from where they originated.
Problems are easy to setup.
Weakness of Eulerian methods:
Material interfaces are reconstructed, not tracked. This poses difficulties in treatment of contact-impact problems since the contact conditions cannot be explicitly enforced.
Material modeling is not well done for structural response applications (e.g., elastic-plastic material response), especially when the problem involves history-dependent materials.
Calculations are expensive – large memory requirements, slow execution
Why coupled?
With Zapotec, we are targeting certain classes of problems that are not readily solved using Euler or Lagrangian methods alone. We generally encounter these problems when the constituent materials exhibit vastly differing strengths (or degrees of deformation). E.g., consider an earth penetration example. The penetrator is a stiff structure, exhibiting low to moderate deformations. The target is soft by comparison and will exhibit large material deformations and flow. With a coupled approach, we can choose the best solution method for modeling various material in the problem. For earth penetration, the penetrator is modeled as Lagrangian because deformations are moderate and structural response is of primary interest to the analyst. We model the target (earth) as Eulerian since this solution method best handles the large material deformations.

## Slide 12: What are we coupling with Zapotec?
CTH
  Eulerian shock physics code
Sierra/SM
  Explicit, Lagrangian finite element code
Zapotec couples interaction between Lagrangian and Eulerian materials
Notes: There are many implementations of coupled methods. With Zapotec, we tightly couple two existing, production codes: CTH and Sierra/SM.
In the problem development, we define materials as Lagrangian or Eulerian. The coupling algorithm then handles the interaction between the two material types.

## Slide 13: Zapotec Background The Coupled Algorithm in Time
CTH and Sierra/SM are run sequentially, cycle by cycle
Algorithm permits Sierra/SM subcycling
CTH
Sierra/SM
ΔtCTH
ΔtSierra/SM
tn
tn+1
t
Sierra/SM and CTH Calculation
Zapotec Coupling
Notes: Before discussing the details of the coupling algorithm, it is first useful to look at the coupled treatment in time. At time tn, we get data from CTH and Sierra/SM, work on that data, then send back the updated data to the two codes. CTH and Sierra/SM then move forward in time independently to tn+1. In general, CTH will have a larger stable time step. We permit Sierra/SM subcycling to improve efficiency and accuracy.

## Slide 14: The Zapotec Coupling Algorithm
Coupled treatment conducted in two steps, referred to as material insertion and force application
Material insertion step updates CTH data
Force application step updates Sierra/SM data
Notes: Zapotec performs two steps in the coupled treatment. We refer to these as material insertion and force application.

## Slide 15: The Zapotec Coupling Algorithm Material Insertion Step
Remove pre-existing Lagrangian material from the CTH mesh
Get updated Lagrangian data
Insert Lagrangian material into CTH mesh
  Compute volume overlaps
  Map Lagrangian data – mass, momentum, sound speed, stress, internal energy
Lagrangian
Material
CTH Mesh
tn
L1
L2
P L,inserted = (VO,L1 PL1 + VO,L2 PL2) / VO
V overlap = VO = VO,L1 + VO,L2
Notes: At the beginning of the coupled treatment, we have Lagrangian material that was previously inserted into the CTH mesh. We remove this material so that the CTH mesh contains only Eulerian materials. Once this is done, we get the current (updated) Lagrangian data and insert it into the CTH mesh. Material insertion first involves computing the overlap of Lagrangian elements with CTH cells. After the element/cell overlaps are determined, we insert the Lagrangian data (mass, momentum, sound speed, stress, internal energy) into the CTH mesh. In general, we have CTH cells that are overlapped by several Lagrangian elements. We weight the Lagrangian data, usually by volume, for cell insertion. For example, consider pressure where we weight the Lagrangian pressures by their volume-fraction overlap prior to insertion.

## Slide 16: The Zapotec Coupling Algorithm Force Application Step
Remove pre-existing Lagrangian material from the CTH mesh
Get updated Lagrangian data
Insert Lagrangian material into CTH mesh
  Compute volume overlaps
  Map Lagrangian data
Compute external force on Lagrangian surface
  Determine surface overlaps
  Compute surface tractions based on Eulerian stress state
  Compute normal force on element surface (element-centered force)
  If friction, compute tangential force as ft = fns
  Distribute forces to nodes
Lagrangian
Material
CTH Mesh
tn
fn = (t · nL ) Aoverlap nL
fI = NI fn
Notes: With the material insertion step, we have updated the CTH data. Now we need to assess the loading on the Lagrangian materials.
First determine the overlap of Lagrangian surface elements with cells in the CTH mesh. For a given surface element, we compute the surface tractions based on the stress state in the neighboring Eulerian material. The surface normal and element area is known, allowing us to readily compute the normal force on a surface element. These forces are element-centered. We distribute these forces to the nodes in standard FE fashion. Once this is done for all surface elements, we pass the data back to Sierra/SM as a set of external nodal forces.

## Slide 17: Highlight of Zapotec Capabilities
Supports two Sierra/SM element types for material insertion
  8-node hexahedral element
  4-node shell element
Compatible with CTH-AMR capability
Can model response of complex, thin-shell structures
Element death (a.k.a. erosion) accounted for in the force application step
Donation
  Material from “dying” Lagrangian elements contributed to CTH
  “Donated” material treated as Eulerian for duration of calculation
Parallel implementation

## Slide 18: Typical Zapotec Applications
Earth Penetrating Weapons
Anti-Armor Applications
(Eroding Rods)
Air Blast Loading on a
Reinforced Concrete (RC)
Building
Hypervelocity Impact
Notes: The class of problems solved with Zapotec usually involves materials of vastly differing strengths. For example, consider an earth penetration problem. The loading on the penetrator can lead to significant deformation and potentially high shock levels on any on-board components. In turn, the penetrator deformation affects the stress field in the neighboring target material.

## Slide 19: Problem Development
Sierra/SM Data
Input File (*.i)
Model File (*.g)
Zapotec
CTH Data
Input File
Zapotec Data
Input File
List of coupling files
Results Data
CTH Results (spcth,hscth)
Sierra/SM Results (*.e, *.h)
Notes: Data development for Zapotec is complex. There are three sets of input data, inputs for CTH, Sierra/SM, and Zapotec. There is also a zapotec list file that lists the names of each of the core input files. The Zapotec input file describes the relationship between the Eulerian and Lagrangian materials in the problem. Once these inputs are developed, the user can then run Zapotec. Because we are using off-the-shelf codes (i.e., Sierra/SM and CTH), it is implied the user has extensive working knowledge of CTH and Sierra/SM.
CTH and Sierra/SM have vastly differing plotting databases. Paraview is rhe recommended visualization tool, since it can read both CTH and Sierra/SM outputs.
Need to make point that Sierra/SM is linked to a separate CTH source. Knowledge of the location of this source is important in setting the CTHPATH variable, required for all runs.

## Slide 20: Example: Blast Loading on RC Structure
Lagrangian Structure
  Reinforced concrete and bricks
Eulerian air and explosive
Sierra/SM contact between bricks and other structural elements
CTH: ~4.5M cells
Sierra/SM: ~ 285K elements
Notes: Air blast loading on a concrete structure is an excellent example in problem development for Zapotec. The structure is composed of reinforced concrete columns and slabs; the walls are made up of stacked bricks. We model the structure as Lagrangian, allowing for potential contact between the bricks and any load-bearing members. The surrounding air and explosive charge are modeled as Eulerian.

## Slide 21: Example: Blast Loading on RC Structure
Notes: The explosive detonates with the shock and explosive products interacting with the structure later in time. This is illustrated in these snapshots of pressure at various times.

## Slide 22: Example: Blast Loading on RC Structure
Notes: This is a better snapshot depicting the coupled interaction. We could have modeled this problem using a one-way coupling. In a one-way coupling, we would apply a blast load onto a rigid structure (or surface). This generally leads to an over-prediction of the load magnitudes, which in turn, leads to an over-prediction of structure deformations. In a tightly coupled approach like Zapotec, the structure response can affect the flow field. In turn, this affects the loads on the structure.

## Slide 23: Zapotec Command File and Problem Development

## Slide 24: Objectives
Describe Zapotec input data
Introduce Zapotec terminology
Describe data flow and code execution

## Slide 25: Coupling File List
This lists the other files that will be needed:
  Sierra/SM input file
  CTH input file
  Zapotec coupling file
This is the “input” for the zapotec command:
  Run command: sierra zapotec -i <zapotec file list>
Syntax:
  cth input deck = <name>
  cth run id = <name>
  sierra input deck = <name>
  zapotec input deck = <name>

## Slide 26: Zapotec Command File
Name specified in coupling file (often just zapotec.inp)
Simple, free-field format using keyword inputs
Provides overall program control
  E.g., termination time, plot frequency
Defines relationships between Eulerian and Lagrangian materials in the problem
  The user must still setup the CTH and Sierra/SM inputs separately

## Slide 27: Example Zapotec Command File
* num_eul = 1 * material_map eulerian 2 = lagrangian 10 * max_subcycles = 20
* force sset 200 210
material 10 * plot time = 0.0 interval = 5.0e-6
*
restart
time = 5.0e-6 interval = 5.0e-6
stop_time = 20.0e-6
Notes: This is representative of a typical Zapotec input file. Commands in this file define relationships between Euler and Lagrange materials in the problem as well as provide some directives for overall program control. For the remainder of this training module, we will discuss individual Zapotec commands.

## Slide 28: Control Data
Code termination based on time
Set termination times in CTH and Sierra/SM to a large value
  CTH command file
  Sierra/SM command file
Can limit Sierra/SM subcycling (default is 50)
stop_time = 20.0e-6
control
tstop = 999.0
endcontrol
termination time = 999.0
max_subcycles = 20
Notes: Code termination (or analysis duration) can be controlled by Zapotec. To do so, the user must set the termination times in CTH and Sierra/SM to values greater than the Zapotec stop time/cycle.
Zapotec permits Lagrangian subcycling to improve computational efficiency and accuracy. The user can control the amount of subcycling using the max_subcycles command.

## Slide 29: Control Data (Cont’d)
“Coupling” keyword set can be used to terminate the CTH coupling at a prescribed time, allowing Sierra/SM to run independently
Useful for applications involving air blast loading on structures
“Multistep” option provides more generality
  Options: Independent, coupled, lagrangian, eulerian
  Can toggle analysis on/off as desired
coupling
tcutoff = <time>
ncutoff = <no. steps>
tcutoff
F
t
Reduce force linearly
over ncutoff time steps
multistep
time = 0.0 type = independent
time = 20.0e-6 type = coupled
time = 100.0e-6 type = lagrangian
Notes: Useful for applications involving air blast on structures:
the duration of the positive phase pressure pulse is small compared with the structure’s time to respond
Avoid late time mixing of air and explosive products in CTH portion of calculation. This mixing can lead to unstable behavior and a sudden increase in material specific energies, which in turn, lead to non-physical pressure states.

## Slide 30: Output Control
Zapotec can control the plot frequency, i.e., intermittent writing of spatial results data to CTH and Sierra/SM plot files. E.g.,
Zapotec CANNOT control the data written to the plot files
  The user must specify what data are written in the CTH and Sierra/SM input files
  In CTH, this is done with the “spy” command block. The spy block must duplicate the output frequencies specified in the Zapotec coupling file (hope to fix this soon)
  In Sierra/SM, this is done with the “results output” command block, but does not need any output frequency specified, since Zapotec controls the output
Zapotec CANNOT control history/tracer data
  The user must specify history data in the CTH and Sierra/SM input files
  In CTH, use “spyhis” commands within the “spy” command block
  In Sierra/SM, use the “history output” block
plot
time = 0.0 interval = 5.0e-6
Notes: Zapotec can control plot frequency, but it cannot control what data is plotted.

## Slide 31: Restart Control
Zapotec can also control the frequency of writing restart data E.g.,
Note: Dummy restart input must still be
specified in the CTH and Sierra/SM input files
  Sets aside internal memory for writing restart data
  In CTH, use the “restt” command with a large value
  In Sierra/SM, use “restart data” command block, but no frequency of output is required
restart
time = 5.0e-6 interval = 5.0e-6

## Slide 32: Material Assignments
Material assignments can be complicated, since Euler and Lagrange materials are defined in separate files (i.e., in the CTH and Sierra/SM input files)
In the CTH input file
  Materials are categorized as follows
    Permanent CTH material: True CTH material
    Donated material: Lagrangian material converted to a CTH material via element death in Sierra/SM
    Placeholder material: Sets aside internal memory in the CTH database for inserted Lagrangian materials
  Require sequential ordering of these materials
    Permanent CTH materials 1  m  nperm
    Donated materials nperm+1  m  neuler
    Placeholder materials n euler+1  m  ntotal
  Implies material IDs are sequentially ordered
  Constitutive data must be specified for all materials
    See “eos”,“epdata”, and “pfrac” commands in CTH User Manual

## Slide 33: Material Assignments (Cont’d)
In the Sierra/SM input file
  Materials can be associated with a unique block ID (i.e., materials need not be sequentially ordered)
  Constitutive data must be specified for all Lagrangian materials
In the Zapotec input file
  The user must specify the number of Eulerian materials in the problem (neuler)
    Note: neuler = nperm + ndonated < ntotal
  The user must specify the relation between Euler and Lagrange materials in the problem. This is done using the material and donation maps
    Material map – maps Lagrangian materials into CTH placeholder locations
    Donation map – maps donated Lagrangian materials into CTH donated material locations
  Not all Lagrangian materials have to be mapped into the CTH mesh. Can obtain a substantial saving in volume overlap computations by mapping only those Lagrangian materials that can interact with Eulerian materials – but make sure not to leave anything important out!
  Multiple Lagrangian materials can be mapped into the same CTH placeholder location. This reduces memory requirements within CTH.

## Slide 34: An Example of Material Assignments
Hypervelocity impact of a long rod into a finite thickness target
Rod is Lagrangian
  Sierra/SM block ID = 10
Target is Eulerian
  CTH material ID = 1
  CTH Placeholder material is 3
Specify element death in Sierra/SM with death criterion based on failure strain
  Dead elements are donated to CTH
  CTH donated material ID = 2
num_eul = 2 *ntotal = 3, nperm = 1, ndonated = 1, nplaceholder = 1
material_map
eul = 3 lag = 10 *maps Lagrangian mat 10 to CTH mat 3
donation_map
eul = 2 lag = 10 *maps donated Lagrangian mat 10 to CTH mat 2
Lagrangian
Rod
Eulerian
Target
Donated
Material

## Slide 35: Force Application Data
The user must specify the Lagrangian materials that can interact with (or contact) Eulerian materials in the problem
  This is the Euler-Lagrange contact problem
  Not to be confused with Lagrange-Lagrange contact
Lagrangian material surfaces are specified as block IDs
  The block IDs provide a list of Lagrangian surface elements on the exterior surface of a Lagrangian material. These surface definitions are automatically generated within Zapotec AND are updated as Lagrangian elements die. This does currently require that a contact block exist within the Sierra input that includes all the blocks to be coupled (best just to include all blocks) in order to support this surface definition
  Sideset surfaces are not currently supported
force
material = 10

## Slide 36: Other Useful Zapotec Commands
Comments can be placed anywhere in the file using *, % , $, or !
All keywords following the “exit” command are ignored
The “ambient_pres” command specifies the initial pressure in CTH; is subtracted off before being applied to Lagrangian material
The “eliminate_excess” command removes overlapped Eulerian material at the startup of the calculation. Useful when modeling complex Lagrangian material geometries overlapping a large, homogeneous Eulerian domain. E.g.,
+
=
Eulerian
Air
Lagrangian
Structure
Air
Air

## Slide 37: Zapotec Data Flow
Sierra/SM Data
Command File (*.i)
Model File (*.g)
Results Data
CTH Results (spct*,hsct*)
Sierra/SM Results (*.e, *.h)
Zapotec
CTH Data
Command File
CTHGEN Restart File
Zapotec Data
Command File
File List
Notes: Data development for Zapotec is complex. There are three sets of input data, inputs for CTH, Sierra/SM, and Zapotec. There is also a zapotec file list file that lists the inputs for the other codes. The Zapotec input file describes the relationship between the Eulerian and Lagrangian materials in the problem. Once these inputs are developed, the user can then run Zapotec. Because we are using off-the-shelf codes (i.e., Sierra/SM and CTH), it is implied the user has some working knowledge of CTH and Sierra/SM.
CTH and Sierra/SM have vastly differing plotting databases. Paraview is the recommended platform for visualization, since it can read in outputs from both CTH and Sierra/SM.

## Slide 38: Zapotec Problem Development and Code Execution
Setup environment to run Sierra/SM codes
Build CTH and Sierra/SM problem inputs separately
Run Zapotec
  Set CTHPATH variable to point to the CTH distribution linked to Sierra
    > setenv CTHPATH <path to CTH used for linking>
  Run Sierra execution command:
    > sierra –j <num procs> …queueing commands… zapotec -i <zapotec file list file>
Notes: Note: the number of processors used for CTH, Sierra/SM, and Zapotec must be the same.

## Slide 39: Zapotec: A Coupled Euler/Lagrange Computer Program Hands-on Exercise:

## Slide 40: Advice For Users (The Lore)
Needs to be developed

## Slide 41: Thought Exercise Problem Development for Zapotec

## Slide 42: Objective
“Paper” exercise to illustrate Zapotec problem development for various applications
Class participation is required, so wake up

## Slide 43: Examples – Zapotec Problem Development
Earth
Low Velocity Penetration
Into Earth
Steel Penetrator
With On-Board
Components
V
Low Velocity Penetration
Into Overburden Composed
of Rock Rubble and Soil
Steel Penetrator
With On-Board
Components
V
Rock
Rubble
Soil

## Slide 44: Examples – Zapotec Problem Development
Penetration into RC Slab
V
Rebar
Concrete
Long Rod Impacting Flat Plate
at Ordnance or Hyper-velocities
V
Notes: RC = reinforced concrete

## Slide 45: Examples – Zapotec Problem Development
Air Blast on Thin-Box Structure
Explosive
Air
Thin-Box
Structure
Air Blast on RC Structure
Explosive
Air
RC Structure
Internal
Component
Notes: RC = reinforced concrete

## Slide 46: Examples – Zapotec Problem Development
Wind Loading on RC Structure
RC Structure
Internal
Component
Hypervelocity Impact of a Flyer
Against a Thin Bumper Shield
Radiographs
Bumper
Flyer
Witness
Plate
VISAR
V
Notes: There are many problems where Zapotec is inappropriate. The flyer plate impact is best modeled with CTH alone, while the wind loading is best modeled with a FE code (likely an implicit method, i.e., NOT Sierra/SM). The bottom line – know the physical problem and choose the best solution approach for modeling it.