## Slide 1: SIERRA203: SIERRA/SM Implicit Training Solving Implicit Statics and Dynamics Analyses with SIERRA/SM
SAND2023-13271PE
SIERRA Solid Mechanics Team Presented By: Kevin Manktelow, 8755
Date: Feb. 26-29, 2023 Location: SNL/CA, Building 926/Room 253
Controlled by: Sandia National Laboratories, Kevin Manktelow

## Slide 2
Date | Slide Version | Release | Notes
8/17/2023 | 1.0 | 5.14 | Initial version
10/11/2023 | 1.1 | 5.16 | Add CUI Markings; version for 11/27 class.
Release Notes

## Slide 3
Course Description
This hands-on course introduces solid mechanics analysts to the implicit solver in SIERRA/SM. The course begins with foundational descriptions of implicit problems and how they are fundamentally different from explicit problems. We then progress into more complex topics to include time stepping, the core implicit solver, and the multi-level solver with some focus on contact problems. The course concludes with a few special topics including implicit dynamics solutions as well as some troubleshooting techniques and tricks to get a converged solution. We hope that the training provides new users with the skills and confidence to solve implicit problems with SIERRA/SM, while experienced users may gain a new perspective on their existing analysis techniques, debugging strategies, and time to ask questions.
Course Outline
Day 1: (4 hours, ~50 slides, ~7 examples)
Introduction to implicit problems in finite element analysis
Implicit problem solving: linear and nonlinear
Day 2: (4 hours, ~60 slides, ~4 examples)
Time stepping in implicit
Deep dive into the core solver
Day 3: (4 hours, ~40 slides, ~3 examples)
Introduction to the multi-level solver and implicit contact
Introduction to implicit dynamics
Day 4: (4 hours, ~50 slides, ~1 example)
Troubleshooting, tips and tricks for implicit problems
Closing thoughts, and time for questions

## Slide 4
By a show of hands …
Do you have experience with both explicit and implicit numerical integration methods?
Have you ever programmed finite element methods?
Have you used nonlinear solution methods before?
Have you used implicit FEM solvers in other codes?
I’ve used other codes, but I don’t know what kind of solver they used?
Class survey

## Slide 5: Prerequisites
You are welcome to execute the examples using SAW or a Linux terminal as desired
Applications used throughout training
MATLAB
module load apps/matlab
SIERRA
module load sierra
ParaView
module load viz
CUBIT
<no module needed>
Previous SIERRA experience (SIERRA100 level)
Read/understand a SIERRA input deck
Execute SIERRA/SM (adagio)
Visualize results (ParaView/EnSight)
Software familiarity
Familiarity with MATLAB (useful but not necessary)
Linux environment or Workbench (edit input decks, run code and visualize results)

## Slide 6: Class overview
We are going to start simple and build up complexity
This class focuses on implicit solutions using the SIERRA/Solid Mechanics code.
The SIERRA/Solid Mechanics code has many names. Let’s address that.
SIERRA/Solid Mechanics = SIERRA/SM
SIERRA/SM  adagio
adagio is the executable name
presto  typically means “explicit” (e.g. “begin presto region”)
We’re working on clarity for this…

## Slide 7: Class overview
We take a practical approach
Minimal (but sufficient) theory to introduce and anchor concepts
Examples of syntax and their connection to theory
Hands-on examples throughout the course (so get ready to work!)
  Many examples contain additional exercises to allow more advanced users to explore the capabilities and potential of the code.
Tips, tricks, and commentary on practical usage interleaved throughout
Class materials are mostly standalone, but are intended to be accompanied with live presentation and discussion.

## Slide 8: Other training materials are available and fantastic!
There are many additional training materials accessible, some outdated but still very relevant
https://compsim.sandia.gov/compsim/Docs/Sierra/preRelease/GeneralRelease/index.html
Look under “Intro to SIERRA/SM”
A few recommended to start with:
Implicit Solver – Part I
Implicit Solver – Part II
Implicit Solve r– FETI Solver
Implicit and Explicit Quasistatic Contact
Contact: Under the Hood
User’s Guide: Syntax and usage guidelines
Theory Manual: Feature background and explanation of capabilities and limitations

## Slide 9: MODULE 1: Motivation: Why Implicit?

## Slide 10: Section overview
Discuss why we want to use implicit methods
Get a hands-on comparison between implicit an explicit solution methods
Briefly see how to convert between implicit and explicit
Review available documentation
We will …

## Slide 11: Implicit vs. explicit, what to use and when (notional)
Time scale of event to be simulated
Model complexity
Explicit
Implicit
Explicit with mass scaling
A few contributors to model complexity:
Number of elements
Nonlinearities
Contact constraints
Complex materials
High speed impact
Rolling tire under load
Full system model environment analyses
Testing a component
Other factors:
Element size is critical!
Is a static solution state important?
Is quantifying error important?
How resolved do fields need to be? (smaller elements become increasingly problematic for explicit)
Implicit
(High mesh refinement)
Simple/toy problems
ns
s
ms
s
min.
hr.
days

## Slide 12: Let’s start off with a hands-on motivating example
Ex01: Compare explicit and implicit solvers
Find the final displacement from the applied load . Run in serial (np=1).
Run SIERRA on the explicit input deck. Look in the log file to estimate the time to completion. (Hint: CTRL+C to kill the job if you don’t want to wait for it to finish)
>> adagio -i paperclip_explicit.i
Run SIERRA on the implicit input deck. Look in the log file to see the total time to completion.
>> adagio -i paperclip_implicit.i
Visualize the results output file in paraview. Determine what the maximum tip displacement is. How does it change over time?
>> paraview output.e
Extra credit: Try to get an explicit solution through any means necessary.
t
fixed

## Slide 13: Example 01: Results and discussion (implicit solution)
Time
Tip Displacement
Analysis Type | Wallclock Time
Explicit | ~160 hr.
Implicit | 25 sec.

## Slide 14: Example 01: Results and discussion (explicit “solution”)
Time
Tip Displacement
Time
Energy
Too much kinetic energy for a static solution!
Density x 1,000,000
Solution time: ~10 minutes
Be cautious when using explicit time integration to solve static problems! It will give you “an answer”.

## Slide 15: A rapid tour of converting between explicit and implicit
Different time stepping blocks.
Implicit must specify either the NUMBER of steps or the time increment SIZE.
We declare specific instructions on how to solve the problem, via a solver command block.
More detail on all of this later …

## Slide 16: Where to find more information
Access latest manuals at compsim.sandia.gov
Go to “Documentation Portal”
Select release version
Access “User Manuals/Solid Mechanics/User’s Guide”

## Slide 17: A note on the nomenclature we’re using
“adagio” and “presto” are musical terms meaning “slow” and “fast” tempo, respectively
Initially, probably referred to time scales of problems to be solved
Adagio implies “implicit”
Presto implies “explicit”
Historically, adagio and presto were two different codes excuted with commands:
  >> adagio –i implicit_input_deck.i
  >> presto –i explicit_input_deck.i
Around ~2010, the SIERRA/SM team consolidated the executables to improve code re-use, among other things. We were left with a single executable (adagio).
adagio executable  SIERRA/SM (but not necessarily implicit!)
The terminology still persists and can cause confusion (we are working on this).
For example:
  begin adagio {region|procedure} and begin presto {region|procedure} are synonyms in the code and do exactly the same things.
  Suggest using a convention and sticking to it for simplicity.
Our user guide annotates some features with the rabbit and turtle to indicate contents that may only be relevant to one analysis type.

## Slide 18: In summary…
SIERRA/SM
(adagio)
Implicit solver
(adagio)
Explicit solver
(presto)
Use for slow rate analyses
Requires solving a system of equations to move rapidly through time.
Use for rapid loading rates
Model complexity is more easily handled
Bottom line: Implicit and Explicit solvers serve different purposes. Selecting the correct solver is a critically important part of the analysis process.

## Slide 19: MODULE 2: Back to Basics – Part 1: Implicit Problem Solving

## Slide 20: Section overview
Use a simple 1D example
Learn about implicit and explicit solvers
Learn about different types of implicit solution
Solve our 1D example in SIERRA/SM
We will …

## Slide 21: Solving a simple mass-spring system
Equations of motion
Solve for the final static displacements and

## Slide 22: Solving a simple mass-spring system
Expressed more generally as vectors
Expressed as a linear system of equations
Solve for the final static displacements and

## Slide 23: The explicit solve (a very brief over-simplification)
=
Re-write in 1st-order form (only first time derivative appears)
Make approximation for time derivatives and integrate
pick initial conditions and time step…
march forward in time ...

## Slide 24: The explicit solve (a very brief over-simplification)
Step 0
Step 1
Step 2

## Slide 25: Example 02: A concrete example for explicit integration
Ex02: Solve using explicit time integration
File: two_dof_system.m
Use MATLAB to perform numerical integration of the 2-DOF system.
Try different time steps. What happens for ? ?
What are the likely final static displacements and ?
Extra credit: Add damping into the solution to reach a quasi-static state. Hint: damping forces are often proportional to velocity.
Let = 0.5,

## Slide 26: The explicit solve: a numerical solution
dt = 0.01
dt = 1.0

## Slide 27: The explicit solve: reaching “steady state”
Damped solution
Phase portrait for
Observe that a solution with some damping reaches a “quasi-static” solution.
Some form damping is necessary to eliminate “ringing.”
Solution time must be long enough to reach steady-state.
The solution we want

## Slide 28: The implicit solve: straight to the point!
We seek static solutions, so time derivatives are all zero.
Solve the linear system of equations. Done!
(… but this is often easier said than done.)

## Slide 29: Example 03: A direct solution approach
Ex03: Solve implicitly using MATLAB
File: two_dof_system_direct.m
Run the example to obtain a static solution.
How is this similar to our explicit solution?
How is this different than our explicit solution?
Extra credit: Experiment with different values of . What happens with:
(very soft) (no spring) (very stiff)
Let = 0.5,

## Slide 30: The implicit solve: example 03 discussion
Typical output:
The answer is exact.
There is no time-dependence.
Our system must be “well-conditioned”
  … Large disparities in stiffness are bad and make numerical solution challenging or impossible.
Our system must be non-singular
  … Or else a unique solution does not exist
Equivalent MATLAB statement. The “\” operator is magic. It simply solves the linear system. We will not explore how.
Analytic solution

## Slide 31: Solving our 2DOF with SIERRA/SM

## Slide 32: Solving our 2DOF with SIERRA/SM Implicit
It turns out our system represents discretization of a continuum that parallels a finite-element analysis.
Let’s derive some comparable parameters for our SIERRA/SM analysis
Unit cubes
Total dimensions = 2x1x1
Effective stiffness (approx):
Effective modulus (approx):

## Slide 33: Solving our 2DOF with SIERRA/SM Implicit: Input Deck
begin sierra
begin material generic
density = 1.0
begin parameters for model elastic
youngs modulus = 1
poissons ratio = 0.0
end
end
begin finite element model two_bricks
database name = two_dof_bricks.g
begin parameters for block block_1
material = generic
model = elastic
end
begin parameters for block block_2
material = generic
model = elastic
end
end
begin adagio procedure proc1
begin time control
begin time stepping block tb1
start time = 0.0
begin parameters for adagio region region1
time increment = 1.0
end
end
termination time = 1.0
end
Define a material equivalent to our springs. Note, we must specify a density, even though we seek a static solution!
Density is used to compute mass for output in the log file and some boundary conditions (e.g. gravity)
Unlike our analytical solution, we must specify time in SIERRA/SM implicit analyses.
This is more important in highly-nonlinear analyses, where we need to apply the boundary conditions or loads slowly.
Our problem is nearly linear by construction
Start time = 0.0 (arbitrary)
Termination time = 1.0 (arbitrary, no rate effects)
Time increment = 1.0 (attempt to solve in a single “load step”)
Required for implicit analyses!

## Slide 34: Solving our 2DOF with SIERRA/SM Implicit: Input Deck
begin adagio region region1
use finite element model two_bricks
begin distributed force
surface = top
function = sierra_constant_function_one
component = x
scale factor = -0.1
end
begin fixed displacement
surface = bottom
component = x y z
end
begin solver
end
begin results output
database name = output.e
at step 0, increment = 1
nodal displacement
end
end #region
end #procedure
end #sierra
Define the force
Set fixed displacements. This constraint is important!
(Recall what happens if ?)
Required for implicit analyses!
This is the simplest possible solver definition and uses all default options.
A solver is the most critical component in implicit analyses and tells SIERRA/SM how to find a solution which satisfies equilibrium.
There are many options we will explore later
There are options because there are many types of solid mechanics problems.
There is unfortunately not a magic solver setting that will solve all of our problems.

## Slide 35: Example 04: Solve the 2DOF with SIERRA
Ex04: Solve implicitly using SIERRA
File: solve_2dof.i
Run the example to obtain a static solution.
  >> adagio -i solve_2dof.i
Visualize the results in ParaView.
  >> paraview output.e
Do the results make sense? How are they similar/different?
Extra credit: Modify the input deck to use different materials for block_1 and block_2. Experiment with different elastic moduli for block_2. What happens with:
(soft) (very soft)
Let = 0.5,

## Slide 36: Example 04: Results and discussion
Our results are different than the MATLAB solution! Why?
output.e
solve_2dof.log
The log file is essential to understanding how to solve implicit problems.
We will explore what all of this means in more detail later

## Slide 37: Example 04: Results and discussion continued
Why was our answer different than we expected?
SIERRA/SM is a fully nonlinear code. The nonlinear geometry and deformation causes the answer to differ from our intuition derived from linear principles. It is not possible to disable this nonlinear behavior.
Our approximation for an equivalent Young’s modulus (in lieu of a spring constant) came from linear elasticity assumptions

## Slide 38: Example 04: Results and discussion continued
Extra credit solution: Why couldn’t we solve the problem with softer materials?
block_1
block_2
E1=E2=1.0
block_1
block_2
E1=1.0
E2 = 0.1
block_1
block_2
E1=1.0
E2 = 0.1
Too soft! The force causes an element to invert (effectively become inside-out).
This is a primary cause of the “ComputeInternalForce” error you may encounter.
Implicit solutions algorithms need to “search” for the solution. Occasionally they find displacement configurations that they cannot recover from.

## Slide 39: In summary…
Explicit Solver
We can’t see very far ahead.
Take many small steps so you don’t run into something.
Implicit Solver
We’re blindfolded and searching for the target
Get to any solution, then take the blindfold off and check how you did.

## Slide 40: MODULE 3: Back to Basics – Part 2: The Nonlinearity Problem
And how iterative solution can help!

## Slide 41: Section overview
Explore what nonlinearity means for solution techniques
Extend our mass-spring example to include nonlinearity
Solve our 1D example in MATLAB iteratively
Learn about SIERRA’s iterative solvers
We will …

## Slide 42: Nonlinearity comes in all shapes and sizes (and it makes solving a lot harder)
Material Nonlinearity
Constitutive laws that cannot be expressed with linear operators
Large Deformations and Rotations
Cause nonlinear terms in governing equations
Material failure
Fracture and/or removal of material during analysis
… and contact, constraints, buckling, …. the list goes on.

## Slide 43: Nonlinearity in our 2DOF spring-mass system
+
This nonlinear term prevents us from expressing this as a linear system of equations!
Because we cannot express the system using linear operators, we cannot use linear solution techniques and instead must try something else.

## Slide 44: Nonlinearity: Defining the residual
+
We instead express as a vector-valued function
We define a “residual” vector for a static solve
The equality is strictly true for a solution , but only approximately true near solutions.

## Slide 45: The residual guides us to a solution
We need to solve this system of nonlinear equations for unknowns and
The residual provides us a measure of how force imbalance between the internal and external forces. We require equality for equilibrium.
The residual also informs our solver algorithm how to iterate.
“Large” residuals are bad. “Small” residuals are good!

## Slide 46: The residual is a critical ingredient for nonlinear solvers
Practically speaking, all solution strategies for nonlinear equations are “iterative” in nature. Some examples:
Newton-Raphson methods
Trust Region methods
Conjugate-Gradient methods
Arc-Length methods
SIERRA/SM primarily employs Conjugate Gradient (CG) methods, but has some capability for Newton and Trust-Region methods.
Arc-Length methods can be useful in buckling and “softening” type nonlinearities. SIERRA/SM currently does not offer this solver type.
Evaluate Residual )
Is small enough?
Pick initial conditions
Strategically update the solution
no
Solved, accept as the solution
yes
Most methods follow an iterative pattern that looks approximately like this

## Slide 47: An example of residual evolution (a generic problem)
User-specified tolerance
Check initial conditions,
update solution
Check residual, update
Check residual, update
Check residual, update
Check residual, update
Residual is less than tolerance, accept as our solution!
Because the residual is so important to solving nonlinear problems, it is almost always viewable in solver output somewhere.

## Slide 48: Residual field on a SIERRA/SM tension specimen
“Residual” is a nodal vector field in SIERRA/SM, available for output in any analysis
Every (solid) node has 3 values: residual_{x,y,z} beams and shells have rotational components.
Can be useful to visualize which parts of the model may be struggling to converge
Use “iteration plot” command in “begin cg” block to visualize residual and solution iterations.
Solver iterations
Residual norm for whole model less than tolerance, solution accepted
Update load, check residual imbalance

## Slide 49: Example 05: Solve the nonlinear 2DOF system in MATLAB
Ex05: Solve nonlinear system with iterative solver
File: two_dof_system_implicit_iterative.m
Run the MATLAB script to solve the nonlinear system.
Find the solver output. Do the values for f(x) make sense? (Hint: f(x) is the residual squared).
What tolerance do you need to obtain a solution in 3 iterations?
Extra credit: Explore what a softening nonlinearity does to the solution process by setting . How does the solve change when we reduce the load to ?
Let = 0.5,

## Slide 50: The implicit iterative solve: results and discussion
Solver output for each iteration
Our solution. Note has displaced less due to “hardening” of the spring
Explanation of why the solver thinks it’s done. These checks can be quite complex.
The analyst must interpret this!
Residual squared
How many times we had to evaluate our nonlinear function (why is this important?)
Solver-specific details

## Slide 51: Nonlinear solutions: hardening vs. softening nonlinearity
Displacement (Strain)
Force (Stress)
Hardening nonlinearity
Softening nonlinearity
…
The softening nonlinearity wreaks havoc! This is very similar to material failure, negative hardening, or some rate-dependence schemes in complex constitutive models in SIERRA/SM.

## Slide 52: A quick look at solver tolerances in SIERRA/SM
begin adagio region <region_name>
begin solver
begin cg
target residual = <real>
target relative residual = <real>
reference = <external|internal|belytschko>(external)
end
end
end
Solution acceptance is controlled by two residual tolerance metrics
Residual: L2 norm of the nodal residual field
Relative Residual = Residual normalized by some measure of force (“reference” force)
The reference force is typically one of:
External: L2 norm of the externally-applied force vector (or boundary reaction forces)
Internal: L2 norm of the internal force vector (useful for thermally-loaded structure, e.g. bi-material strip)
Belytschko: max(, ,, )
The solution is immediately accepted when either of the target residual values is reached.
Belytschko reference is a safe alternative to the default External and is recommended.

## Slide 53: Example 06: Add a simple CG solver block
Ex06: Add a conjugate gradient solver to the SIERRA input deck
File: solve_2dof.i
Find the “begin solver” command block.
  Add a “begin cg / end cg” command block to the solver
  Inside the “begin cg” block, specify a “target relative residual = 1.0e-12”
  Inside the “begin cg” block, specify “iteration print = 1”
Run adagio on the input file. Review the solution and the log file. (Hint: use the “-o” option to save log files to different names)
  Set “target relative residual = 1.0e-6”. Is the solution still acceptable?
  Set “iteration print = 100”. How is the log file different?
Extra credit: Output the “force_external” nodal variable to the results file and prove that the residual reference in the log file is consistent.
Let = 0.5,

## Slide 54: Example 06: Results and discussion
"iteration print” controls how frequently information is printed
The number of iterations in a single CG load step can easily be 1000+ for real applications. The number of iterations required generally scales with the number of nodes (among other things). Limiting the printing of the residual information can make it more readable.
The solution is terminated after we’ve reached our target relative residual, annotated with a “<T”

## Slide 55: Example 06: Results and discussion
The residual reference is derived from the L2 norm of the external nodal forces
Load is distributed over 4 nodes
The relative residual is usually the most useful quantity for assessing convergence because it alleviates us from thinking about the unit system of the analysis.
Our initial iteration must have started with zero displacements

## Slide 56: Example 07: Watch the CG solver work
Ex07: Use “iteration plot” to watch the solver work
File: paperclip_implicit.i
Find the “begin solver” command block.
  Inside the “begin cg” block, specify “iteration plot = 10”
Run adagio on the input file. Review the solution and the log file.
  >> adagio -i paperclip_implicit.i
Visualize the output. Animate the solution to watch the CG solver iterate.
>> paraview paperclip.e
Extra credit: How big of a time step can you take? Play with the maximum number of iterations preconditioner update frequency to start with. (Hint: it’s possible to solve this in a single step, but it’s difficult!)
Extra extra credit: SIERRA/SD is capable of solving a linearized variation of this problem with very little user input. Run salinas on the included *.inp file. Compare the results.
t
fixed

## Slide 57: Example 07: Results and discussion
Iteration plot provides a useful tool to visualize the “path” the solver takes to the solution.
Use iteration plot to identify the possible source of convergence issues:
  Regions with high nodal residual are suspect
  Elements that are nearly inverted (output shape fields)
Beware that the output can become quite large!
Tip deflection
(zoom on step 0)
Tip deflection

## Slide 58: Example 07: Results and discussion
Eigenvalues of the paperclip (undeformed configuration, computed with SIERRA/SD)
A “rule of thumb”: convergence of iterative methods becomes more difficult as the spectral spread increases.
Typically this includes “thin” structures (e.g. beams) and is less of an issue for thick structures (e.g. an engine block)
You will typically not compute this ratio. However, being aware of the consequences is useful.

## Slide 59: Extra credit solutions
begin solver
begin cg
target relative residual = 1.0e-3
maximum iterations = 1000
iteration reset = 20
line search secant 1.e-3
begin full tangent preconditioner
iteration update = 20
end
end
end
begin solver
begin newton solver
target relative residual = 1.0e-3
maximum iterations = 25
end
end
begin solver
begin cg
target relative residual = 1.0e-3
maximum iterations = 25
beta method = newton
begin full tangent preconditioner
iteration update = 1
end
end
end
Strategy #1
Strategy #2
Strategy #3
(Text hidden in box)
b
e
g
i
n
r
e
p
c
d
n
o
d
i
i
t
o
e
n
r
Getting an implicit solution can sometimes feel like solving a puzzle.
This doesn’t change.
This class won’t change that .
… but with practice and awareness, solving the implicit puzzle becomes easier.

## Slide 60: Extra credit solution… the search for convergence

## Slide 61: Extra, extra credit: Solve the linear variant and compare
Linear solution (SIERRA/SD)
Solved implicitly.
Solve time ~0.07s
Tip displacement ~0.48 [in]
Nonlinear solution (SIERRA/SM)
Solved implicitly.
Solve time ~60 sec.
Tip displacement ~0.46 [in]
SIERRA provides both linear and nonlinear implicit solvers. Consider your options and needs to select the best tool for the job.

## Slide 62: In summary…
Nonlinearities make life harder
  The residual is a key metric
  Iterative solver strategies
The conjugate gradient method is the primary solver in SIERRA/SM
  Read the Sierra/SM Theory Manual, Ch. 13 for details on solver theory and implementation
We specified a basic solver block in SIERRA/SM
  Tolerances and references
  Definition of convergence
We saw how to visualize and debug the solver
  Iteration plot
  Iteration print

## Slide 63: MODULE 4: Implicit Time Stepping
What it means, how to do it, and improving robustness

## Slide 64: Section overview
See what time stepping means for a “static” solution
Learn about configuring the time stepping
Learn about the “DURING” keyword for fine-tuning our line commands
Learn about how time stepping influences results and performance
Configure and try adaptive time stepping to improve robustness
We will …

## Slide 65: Solving implicit [quasi-]static problems with SIERRA/SM
Time
Reaction Force
Time
Displacement
Most nonlinear problems of interest cannot be solved directly to the final solution.
Nonlinearities introduce path-dependence, constraints, and nonlinear evolution (e.g. plasticity) that require solving at multiple points in time to get to our final solution.

## Slide 66: The role of time-stepping in SIERRA/SM Implicit
Load Step 1
Load Step 2
Load Step 3
Step =
Step = Δ𝑡
Evaluate loads and BCs at t
Step =
Step = Δ𝑡
Evaluate loads and BCs at t
Step =
Step = Δ𝑡
Evaluate loads and BCs at t
Load Step N
Step =
Step = Δ𝑡
Evaluate loads and BCs at t
…
…
t=0.0
t=0.1
t=0.2
t=1.0
The analyst sub-divides time into segments based on the nonlinearities present in the model. These segments are referred to as Load Steps in SIERRA/SM.
Time need not start at 0.0
Time “t” is often non-physical and simply regarded as a load parameter
  Implicit dynamics and rate-dependent materials are exceptions
  Common to ramp load linearly from 0 to 1
A very common time range to solve static problems is t = [0, 1] simply for convenience
The multi-level solver capability further divides a load step into multiple “model problems”

## Slide 67: The role of time-stepping in SIERRA/SM Implicit
begin sierra
begin adagio procedure myImplicitSolve
begin time control begin time stepping block step_1
start time = <real>
begin parameters for adagio region adagioRegion
time increment = <real>
number of time steps = <int>
end
end
termination time = <real>
end
...
end
end
Load Step 1
Load Step 2
Load Step 3
Step =
Step = Δ𝑡
Evaluate loads and BCs at t
Step =
Step = Δ𝑡
Evaluate loads and BCs at t
Step =
Step = Δ𝑡
Evaluate loads and BCs at t
Load Step N
Step =
Step = Δ𝑡
Evaluate loads and BCs at t
…
…
t=0.0
t=0.1
t=0.2
t=1.0

## Slide 68: Time blocks can be used strategically
begin sierra
begin adagio procedure myImplicitSolve
begin time control
begin time stepping block step_1
start time = 0.0
begin parameters for adagio region adagioRegion
number of time steps = 40
end
end
begin time stepping block step_2
start time = 5.0
begin parameters for adagio region adagioRegion
number of time steps = 100
end
end
begin time stepping block step_3
start time = 5.1
begin parameters for adagio region adagioRegion
number of time steps = 10
end
end
termination time = 10.0
end
...
end
end
Simple plasticity evolution. Solve with moderate step size.
Shear band formation, difficult to solve. Take many small steps.
Total failure, no load. Take large steps for visualization

## Slide 69: The “DURING” keyword for input decks
begin adagio region <region_name>
begin solver
begin cg
target residual = <real> DURING <time_period_list>
target relative residual = <real> DURING <time_period_list>
reference = <external|internal|belytschko>(external) DURING <time_period_list>
end
end
end
Syntax:
The DURING keyword can be append to most solver-related line commands.
Such commands can appear multiple times.
begin adagio region r1
begin solver
begin cg
target relative residual = 1.0e-3 DURING step_1 step_2
reference = belytschko DURING step_1 step_2
target residual = 0.5 DURING step_3
reference = residual DURING step_3
end
end
end
Example usage:
step_1
step_2
step_3
“step_3” is primarily rigid body motion with no loading. It would have a very low “reference” value and might cause unnecessary solver iteration with a relative residual.
Tip: Use this strategy to optimize your solver-related settings when you’ll be running a similar problem repeatedly:
Uncertainty analyses
Multiple design iterations
Multiple mesh refinements

## Slide 70: Time step size is important
Load Step 1
Load Step 2
Load Step 3
Step =
Step = Δ𝑡
Evaluate loads and BCs at t
Step =
Step = Δ𝑡
Evaluate loads and BCs at t
Step =
Step = Δ𝑡
Evaluate loads and BCs at t
Load Step N
Step =
Step = Δ𝑡
Evaluate loads and BCs at t
…
…
t=0.0
t=0.1
t=0.2
t=1.0
All of our time steps must converge! If a step fails to solve, adagio terminates with an error message. Time step size plays a key role in achieving convergence.
spectrum
Many small timesteps
Solve each step faster
Resolve nonlinearities better
May take longer to solve (but may be faster!)
A few large timesteps
More solver iterations per step, harder to solve
Risk of not resolving phenomena of interest
May solve faster (but may fail a lot, resulting in wasted iterations!)
A good starting point

## Slide 71: Handling failed time steps: adaptive time stepping
t=0.35
Load Step 1
Load Step 2
Load Step 3
Load Step 3
Load Step 4
…
Load Step N
t=1.0
t=0.2
t=0.1
t=0.0
t=0.25
Error or failed to converge, cut back and try again
begin sierra
begin adagio procedure myImplicitSolve
...
begin adagio region region_1
begin adaptive time stepping
cutback factor = 0.5
maximum failure cutbacks = 10
end
end
...
end
end
If still not progressing after 10 cutbacks, usually an indication of model form error
Bad material model
Badly-shaped elements
Loss of stability
Factor of 0.5x is usually a good starting point.
A simple recipe for failed timesteps
This is not default behavior

## Slide 72: Adaptive time stepping basics
Solve a load step
Success?
Increment time
Reduce timestep
no
yes
Review convergence. Too easy?
no
yes
Grow timestep
Hold timestep
just right
The “begin adaptive time stepping” command block allows advanced configuration of the time step growth strategy. A simple cutback strategy is often very effective.

## Slide 73: Adaptive time stepping options
(5.14 Manual)
More advanced usage of adaptive time stepping is possible (but will not be discussed at this time)
Recommended reading for adaptive time stepping is section 4.10.2 of the user manual

## Slide 74: Example 08: Adaptive time stepping to the rescue
Prescribed axial displacement
4.8 in
2.6 in
Given this notional “soda/pop/coke/beer” can, determine the load-displacement relationship for the given axial deformation.

## Slide 75: Example 08: Adaptive time stepping to the rescue
Ex08: Use adaptive time stepping to get through a hard solve
File: cylinder_crush.i
Run adagio on the input file. Review the log file to see why it failed.
>> adagio -i cylinder_crush.i
Adjust the time step size, or use an adaptive time stepping command block of your choosing to solve the problem to 100% completion. Watch the log file as it solves. Visualize the results:
>> paraview output.e
3. Look in the log file to see how many converged
Extra credit: Turn off the fixed rotational displacements boundary condition on the “top” sideset. Are your results any different? Do we need this boundary condition? Adjust solver settings you are familiar with to optimize the solve.
Extra extra credit: Make your paraview results look “nice” by applying two successive filters: ExtractSurface->Generate Surface Normals. Adjust the feature angle to your liking in the final filter.

## Slide 76: Example 08: Results and discussion – the log file
Time stepping information
Load step information, percent complete
“>A” indicates our residual is greater than what is acceptable, once we hit the maximum number of iterations (100)
Typical “failure to converge” message

## Slide 77: Example 08: Results and discussion – some deformation
(Two of several possible shapes you may have seen)
Both of the above solutions, among others, are valid solutions. Buckling can happen in many structures of interest, and can lead to multiple solutions or solutions which are sensitive to solver settings and boundary conditions.

## Slide 78: Example 08: Results and discussion – some deformation
Summary of load steps.
Tip: Make sure number of acceptable problems is acceptable!
Last load step takes us from 98.8% to 100% completion
Analysis speed: completed 44 (successful) steps in 14.8 seconds
Timing summary: Often this can guide you to how to speed up your analysis.

## Slide 79: In summary…
Implicit time stepping plays a direct role in achieving converged solutions.
Nonlinear analyses apply the loads and boundary conditions incrementally.
Time step size is a key ingredient for achieving convergence.
The “DURING” keyword helps tailor our solver to different regimes in our analysis.
Adaptive time stepping allows us to adjust the time step size based on the difficulty of the problem.
  Re-trying with a smaller timestep is simple and effective.

## Slide 80: MODULE 5: The Solver: Inputs and Outputs
Basic solver details and dialing in the settings

## Slide 81: Section overview
Learn a little about SIERRA/SM’s core solver
Review some of the most relevant implicit solver input deck sections
Review some of the most relevant log file outputs
Try some implicit settings out
We will …

## Slide 82: What a new staff member feels when approaching an implicit solver
The analyst’s ergo-chair
Acceptable residual dial
Target residual dial
Target relative residual dial
Implicit contact switchboard
Call Nate and Kendall

## Slide 83: Getting the settings “right” can be hard work
Chart: Why Are Solver Settings So Hard!
| Implicit Contact | Complex Materials | Large Element Count | Shell-Like Structures | Implicit Dynamics and Rigid Bodies
Default Settings | 2 | 2 | 2 | 2 | 2
Settings 1 | 4 | 2 | 2 | 1 | 1
Settings 2 | 1 | 2 | 3 | 2 | 5
Settings 3 | 1 | 2 | 5 | 3 | 2
SIERRA/SM is used for a wide array of modeling needs.
Unfortunately, solution techniques and needs vary.
The default settings are good for a large class of problems, but may not be sufficient or optimal for your analysis.
Understanding the controls available to you is critically-important to success.

## Slide 84: SIERRA/SM’s solver: Preconditioned conjugate gradient
SIERRA/SM solves each load step (model problem) with a nonlinear preconditioned conjugate gradient (NL-PCG or NLPCG) method.
This module will only scratch the surface.
Recommend reading:
  Solid Mechanics Theory Manual, Ch. 13 “Nonlinear Equation Solving” for more information
  “An Introduction to the Conjugate Gradient Method Without the Agonizing Pain” – Jonathon Richard Shewchuk – strongly recommended reading for CG.
We will summarize salient topics in Ch. 13 here
We will focus on high-level concepts and practical usage topics (informed by theory – hence the utility in some background of how the solver works)

## Slide 85: The iterative solution of nonlinear problems
We are generally interested in solving a system of equations in the form:
The path to a solution is an iterative process, which always leaves questions:
How many iterations do we need?
How close is “close-enough”?
How do we update displacements from iteration “j” to “j+1”?

## Slide 86: Methods for updating our displacement each iteration
Newton-Raphson Method (13.4)
Steepest-Descent Algorithm (13.5)
Conjugate Gradient Methods (13.6)
Uses local tangent stiffness to update displacements
Robust in most cases
Memory requirement grows quickly with model size
Forming tangent stiffness is time consuming
“In-development” solver available in SIERRA/SM
Displacement update iterates seek direction that minimizes energy
Low memory requirement
Inefficient
Highly-sensitive to conditioning
Can be reproduced in SIERRA/SM with appropriate solver commands
Displacement updates are “conjugate” to one-another
Low memory requirement
Evolved from steepest-descent, but more efficient per-iteration
Sensitive to conditioning
Practical use requires a preconditioner
Primary solver in SIERRA/SM

## Slide 87: Methods for updating our displacement each iteration
Newton-Raphson Method (13.4)
Steepest-Descent Algorithm (13.5)
Conjugate Gradient Methods (13.6)
begin adagio region region_1
begin solver
begin newton solver
end
end
end
This is a “developer” solver. It is unsupported, but exists and is documented in the in-development manual.
** Also possible to do with CG solver block **
begin adagio region region_1
begin solver
begin cg
iteration reset = 1
end
end
end
begin adagio region region_1
begin solver
begin cg
end
end
end
Mostly of academic interest. Transforms CG-algorithm into steepest-descent.
Simple, but powerful, default NL-PCG solver.

## Slide 88: Solver configuration – setting target residuals
begin adagio region region_1
begin solver
begin cg
# CONVERGENCE COMMANDS
target residual = <real>
target relative residual = <real>
acceptable residual = <real>
acceptable relative residual = <real>
reference = external|internal|belytschko|residual
minimum iterations = <int>
maximum iterations = <int>
iteration print = <int>
iteration plot = <int>
end [cg]
end [solver]
end [adagio region]
Define what “solved” means. This is critical! Too high and the solution is wildly inaccurate; too low and we may never reach a solution (or be way too accurate for practical usage)
A relative residual of 1.0e-3 is typically sufficient for most engineering analyses.
A target (absolute) residual is usually not necessary, except for some cases with rigid body modes present or no external forcing.
Acceptable residuals provide a mechanism to permit a larger residual once the maximum number of solver iterations is achieved. This prevents solver failure by accepting the fact that a particular model problem was “hard”.

## Slide 89: Solver configuration – setting a reference
begin adagio region region_1
begin solver
begin cg
# CONVERGENCE COMMANDS
target residual = <real>
target relative residual = <real>
acceptable residual = <real>
acceptable relative residual = <real>
reference = external|internal|belytschko|residual
minimum iterations = <int>
maximum iterations = <int>
iteration print = <int>
iteration plot = <int>
end [cg]
end [solver]
end [adagio region]
Define what quantity normalizes our [absolute] residual. EXTERNAL is default. BELYTSCHKO is often a better option.
= L2 norm of absolute residual
= L2 norm of specified reference force vector
= Scalar relative residual measure used for convergence test
The RESIDUAL option uses the initial value of the residual on iteration 1 for a reference. Can be useful for loading/unloading situations.

## Slide 90: Solver configuration – limiting the iterations
begin adagio region region_1
begin solver
begin cg
# CONVERGENCE COMMANDS
target residual = <real>
target relative residual = <real>
acceptable residual = <real>
acceptable relative residual = <real>
reference = external|internal|belytschko|residual
minimum iterations = <int>
maximum iterations = <int>
iteration print = <int>
iteration plot = <int>
end [cg]
end [solver]
end [adagio region]
Define how many iterations are permitted.
Setting a minimum is usually not helpful. Setting a MAXIMUM can be critically-important in achieving convergence and solving efficiently.
Too few iterations and the load step won’t converge.
Too many iterations and “hard” problems may iterate for a long time before testing against an acceptable residual (and still not converge).

## Slide 91: Solver configuration – diagnostic output
begin adagio region region_1
begin solver
begin cg
# CONVERGENCE COMMANDS
target residual = <real>
target relative residual = <real>
acceptable residual = <real>
acceptable relative residual = <real>
reference = external|internal|belytschko|residual
minimum iterations = <int>
maximum iterations = <int>
iteration print = <int>
iteration plot = <int>
end [cg]
end [solver]
end [adagio region]
Iteration Print: Only effects how often the residual and iteration information is printed to the log file for the core CG solve. Default is 25.
Adjusting this value up/down can help with visualizing the log file and assessing the effectiveness of the preconditioner.
Iteration Plot: Diagnostic use only! Writes out the state of the model to the results file(s) every “N” iterations. Useful for debugging and understanding how the solver is attempting to iterate to a solution.

## Slide 92: The preconditioned conjugate gradient
SIERRA/SM always uses a pre-conditioner to improve the effectiveness of the iterative CG solver.
What does a preconditioner do?
(We’re glossing over all kinds of conditions here, like M should be symmetric positive-definite, etc.)
(…Because of fancy math, see recommended reading for details)
Hard to solve, potentially ill-conditioned system
First solve this, better-conditioned system of equations for
Then solve this for
Precondition with
A “good” preconditioner makes the system of equations easier to solve by improving the conditioning of the system (eigenvalue spread, eigenvalue clustering). Note: the actual implementation of preconditioner in SIERRA/SM requires computing .

## Slide 93: Preconditioner options in SIERRA/SM
A preconditioner is always used in SIERRA/SM. A good preconditioner in our context “looks” like the local tangent stiffness matrix.
A good preconditioner will:
Reduce the number of iterations required for convergence
Might be expensive to compute (memory + cpu)
Might be re-usable between load steps
SIERRA/SM has two types of preconditioners:
nodal preconditioner – fastest and “cheapest” available. ON by default.
full tangent preconditioner – most effective option, but most expensive. OFF by default. May not be effective for very large (“system” type) models.
SIERRA/SM offers multiple preconditioner options, but the best option is problem-dependent.
(best := fastest to solve and/or the one that converges)

## Slide 94: Preconditioner options in SIERRA/SM
Nodal Preconditioners
Full Tangent Preconditioner
begin adagio region region_1
begin solver
begin cg
... other cg commands ...
preconditioner = ELASTIC|PROBE|BLOCK_INITIAL(ELASTIC)
end
end
end
begin adagio region region_1
begin solver
begin cg
... other cg commands ...
preconditioner = tangent
begin full tangent preconditioner
... configuration ...
end
end
end
end
Option A: “quick and dirty”
Option B: allows for more tailoring.
Prefer this method.
Elastic: Use current elastic material properties. Updated each model problem. May be useful if material properties are evolving (e.g. temperature-dependent)
Probe: Numerical probing of the stress-strain constitutive law to form a nodal stiffness matrix. May be useful if constitutive models have considerable plasticity/nonlinearities. Slightly more expensive than Elastic.
Block_Initial: Like Elastic, but only updated once at the beginning of the analysis. Very inexpensive, but typically less effective.
(Other options available but not shown)
Preconditioner = tangent: Quickly-specify a full tangent preconditioner in abbreviated syntax. Not terribly useful, prefer the full syntax.
Begin full tangent preconditioner / end: Specify a full tangent preconditioner command block which allows further configuration of the preconditioner. Further configuration can be used to tailor efficiency and accuracy of the preconditioner.

## Slide 95: The “Full Tangent” preconditioner and its log file output
The full tangent preconditioner is highly-effective at reducing the residual when compared with a nodal preconditioner:
Comes at a cost of both -- memory and CPU
Can be tailored to specific problems (update frequency, when to use)
Can be mixed with the nodal preconditioners
Colloquially referred to as “FETI” (Finite-Element Tearing and Interconnectivity solver) – “Are you using FETI?” (FEH-TEE)
The preconditioner was updated during this iteration. You may notice a temporary performance reduction while this occurs.
The goal is to update as little as possible, while reducing the residual as quickly as possible.
The preconditioner was applied, and it only took 1 linear iteration (a direct solve) to “apply” it (compute ). In parallel, this requires an iterative solve and the number of iterations is reported here.
The full tangent preconditioner is sensitive to rigid body modes in a “coarse” system. If any are detected, they are reported here.

## Slide 96: The “Full Tangent” preconditioner and its log file output
The full tangent preconditioner annotates the log files with a status. The only good status is “U”.
Tip: If you consistently see “M500” appearing in your log file, there is likely something wrong in your model. Alternatively, you need to adjust FETI’s linear solver settings to allow additional iterations or increase FETI’s internal solver tolerance.
Good
Bad
Bad

## Slide 97: The “Full Tangent” preconditioner
begin full tangent preconditioner
iteration print = <int>
iteration update = <int>
small number of iterations = <int>
minimum smoothing iterations = <int>
adaptive strategy = switch|update|none(switch)
tangent diagonal scale = <real>
... many other options not shown ...
end
A common subset of options available for the full tangent preconditioner is listed below
Same as in the CG solver block. Defaults to 1 when the full tangent preconditioner is used.
Can be used in combination with iteration printing commands for the CG solver.
Example usage:
Print every 100 iterations when using the nodal preconditioner, but print ever 5 iterations when using the full tangent preconditioner.

## Slide 98: The “Full Tangent” preconditioner
begin full tangent preconditioner
iteration print = <int>
iteration update = <int>
small number of iterations = <int>
minimum smoothing iterations = <int>
adaptive strategy = switch|update|none(switch)
tangent diagonal scale = <real>
... many other options not shown ...
end
A common subset of options available for the full tangent preconditioner is listed below
Update frequency. This controls how often the “U” appears in the log file.
Each update requires forming the tangent stiffness matrix for the current model configuration (memory-intensive) and then application of the preconditioner to the system (cpu-intensive).
Updating frequently can improve robustness at the expense of performance.

## Slide 99: The “Full Tangent” preconditioner
begin full tangent preconditioner
iteration print = <int>
iteration update = <int>
small number of iterations = <int>
minimum smoothing iterations = <int>
adaptive strategy = switch|update|none(switch)
tangent diagonal scale = <real>
... many other options not shown ...
end
A common subset of options available for the full tangent preconditioner is listed below
Controls re-use of the currently-available preconditioner. If a model problem solves in fewer than <int> iterations, the preconditioner is judged as effective and will be re-used in the subsequent model problem.
This saves us from expensive preconditioner calculations, and can easily decrease solve times by 2x-3x.
The trade-off is a risk that not frequently updating the preconditioner may lead to convergence difficulty in some difficult problems.

## Slide 100: The “Full Tangent” preconditioner
begin full tangent preconditioner
iteration print = <int>
iteration update = <int>
small number of iterations = <int>
minimum smoothing iterations = <int>
adaptive strategy = switch|update|none(switch)
tangent diagonal scale = <real>
... many other options not shown ...
end
A common subset of options available for the full tangent preconditioner is listed below
Allows mixed use of the nodal preconditioner and full tangent preconditioner.
When specified, apply the default “nodal” preconditioner <int> number of times before switching to the full tangent preconditioner.
Two common use-cases:
Use the nodal preconditioner for very simple problems, often without need to form a full tangent preconditioner (performance)
Get the model into a “better state” such that the full tangent preconditioner is more effective.

## Slide 101: The “Full Tangent” preconditioner
begin full tangent preconditioner
iteration print = <int>
iteration update = <int>
small number of iterations = <int>
minimum smoothing iterations = <int>
adaptive strategy = switch|update|none(switch)
tangent diagonal scale = <real>
... many other options not shown ...
end
A common subset of options available for the full tangent preconditioner is listed below
If the full tangent preconditioner becomes ineffective (as measured by iteration-to-iteration convergence rate), we can either:
Update the preconditioner
Switch to a nodal preconditioner
Do nothing and hope it gets better
In practice, once a model begins converging so badly that this is necessary it’s usually more effective to just cut the time step with adaptive time stepping.

## Slide 102: The “Full Tangent” preconditioner
begin full tangent preconditioner
iteration print = <int>
iteration update = <int>
small number of iterations = <int>
minimum smoothing iterations = <int>
adaptive strategy = switch|update|none(switch)
tangent diagonal scale = <real>
... many other options not shown ...
end
A common subset of options available for the full tangent preconditioner is listed below
“Tangent diagonal scale” is a technique used to adjust the preconditioner by introducing some additional stiffness to the diagonal of the preconditioner matrix.
This can be an effective technique when rigid body modes are present (e.g. in contact problems before constraints become sufficiently “active” to constrain motion).
Values here in the range [1.0e-3, 1.0e-7] are typical.
This can occasionally increase robustness at the expense of decreasing the convergence rate, but effectiveness is not guaranteed!

## Slide 103: Example 09: Fun with solver settings
Prescribed displacement causes bending and plastic deformation in the plate
A bar introduces constraints (MPCs) that help localize the forming process
The customer needs to form a thin bracket by bending an initially-flat plate.
We need to help determine the maximum plastic strain and final deformation.
Fixed top of bar
Plate dimensions (inches): 10x5x0.125

## Slide 104: Example 09: Fun with solver settings
Ex09: Experiment with different solver settings to achieve convergence
File: plate_with_hole.i
Review the input deck. Find the “INITIAL MESH MODIFICATION” and “TIED MPC” sections. Is their purpose clear?
Add a simple CG solver that uses a maximum of 300 iterations. Solve. Did it converge? Feel free to experiment with the solver settings further.
Add full tangent preconditioner and set the maximum iterations to 100. Solve. Did it converge? Feel free to experiment with the solver settings further.
Add a hybrid preconditioner. Configure the full tangent preconditioner to use 200 smoothing iterations, followed by up to 25 iterations using the full tangent preconditioner.
Visualize the results. Are they beautiful? Does the deformation look right?
Extra credit: Try your solver settings on the refined mesh (plate_with_hole_refined.g):
Does the refined mesh produce a better-looking solution?
Use the included selective-deviatoric section (named “sd”) for block_1 and solve again. How does this impact performance? How does it impact the solution?

## Slide 105: Example 09: Results and discussion – Nodal Preconditioner
begin adagio region region_1
begin solver
begin cg
target relative residual = 1.0e-3
maximum iterations = 300
iteration print = 50
end
end
end
The CG solver with nodal preconditioner is ineffective here. Possibly due to the conditioning of the system.
Maximum iterations
“>A” designates we did not reach our acceptable residual

## Slide 106: Example 09: Results and discussion – Tangent Preconditioner
begin adagio region region_1
begin solver
begin cg
target relative residual = 1.0e-3
maximum iterations = 100
begin full tangent preconditioner
end
end
end
end
The CG solver with full tangent preconditioning is ineffective. After 8 iterations, we switch to the nodal preconditioner and eventually cutback and fail to converge.
Switches to nodal preconditioner
Update FETI

## Slide 107: Example 09: Results and discussion – Hybrid configuration
begin adagio region region_1
begin solver
begin cg
target relative residual = 1.0e-3
maximum iterations = {200 + 25}
iteration print = 50
begin full tangent preconditioner
minimum smoothing iterations = 200
end
end
end
end
A combined preconditioner is highly-effective here. An initial timestep cuts back, but then solves to completion. After some “smoothing iterations”, the full tangent preconditioner drops the residual by 4 orders of magnitude in 11 iterations.
Switches to FETI
“<T” indicates converged

## Slide 108: Example 09: Our coarse and refined solutions
This is truly terrible deformation that is a result of hourglassing.
Confirm by checking the hourglass_energy and internal_energy element variables.
Well, it’s solved.. But 100 elements weren’t enough.
Hybrid settings solve time = 6 sec.
Default settings solve time = 22 sec.
Well, it’s solved.. but it’s still not quite right.
Hybrid settings solve time = 64 sec.
Default settings solve time = Painfully slow

## Slide 109: Example 09: Extra credit – an SD hex solution
UG Hex, Refined Mesh (24 sec)
SD Hex, Refined Mesh (540 sec)
There’s a long-standing rule in FEA: get at least 3 elements through the thickness. This example should convince you that might not be a sufficient condition. The SD hex can help, but we pay the price in solve time!

## Slide 110: Example 09: Log file information
The Internal Force calculation is the primary algorithm effected by the element type.
Using an SD hex element type increases the time spent here by a factor of ~8x due to having 8 integration points instead of 1.

## Slide 111: Example 09: Fine-tuning the solver settings
An observation: Every second time step was failing. After cutting back once, the load step succeeded.
Increase number of time steps to 40
Decrease number of CG iterations:
  50 nodal preconditioner
  50 full tangent preconditioner
X
C
X
C
X
C
Load step 1
Load step 1, attempt 2
Load step 2
Load step 2, attempt 2
Load step 3
Load step 3, attempt 2
X
Load step 4, and so on ...
A truth: The implicit performance is driven primarily by the number of iterations required of the solver to achieve the desired convergence.
A remedy: Adjust the time step so that we are more likely to succeed in converging, thus eliminating wasted effort (iterations):
  New solve time = 190 sec
  Old solve time = 540 sec
Discussion: We may need to solve this problem multiple times to optimize it. When is the time and effort worth it?

## Slide 112: Predictors and line searching: the final ingredients
Gradient descent (green) vs. conjugate gradient (red)
[Image from Wikipedia]
Our initial point plays a large role in efficient CG iteration. Our previous solution can predict a starting point.
This only happens once at the beginning of the load step.
Each iteration, we choose a direction. We must also choose a step length.
This needs to happen once per CG iteration.
The Predictor
The Line Search

## Slide 113: The predictor: options and syntax
begin adagio region region_1
begin solver
begin load step predictor
type = scale_factor|secant(secant)
scale factor = <real>(1.0)
end
begin cg
...
end
end
end
Velocity field at step 1
Step 1 solution
Step 2 predicted configuration
Secant: Default predictor scheme computes an optimal “scale factor” in the direction of the predicted configuration.
Scale_Factor: Manual setting of the scale factor, extrapolated from current velocity field.
Off: Not a real option – use “Scale_Factor” type with a specified scale factor of 0.0.
Tip: Occasionally the default (“secant”) may not work well; manually setting or turning the predictor off can sometimes help. This can often be the case with contact problems for which the predictor is totally agnostic.
Syntax:

## Slide 114: The predictor: when things go wrong
Tip: Occasionally the default secant may not work well; manually setting or turning the predictor off can sometimes help. This can often be the case with contact problems.
Predictor is evaluated nominally at this point in the analysis, after load step information is printed.
The predictor can fail by inverting elements. This will lead to an error and a failed timestep.
Example

## Slide 115: The line search: options and syntax
Energy evaluated along the “search direction”. We want to find the minimum: the “line search” algorithm helps with this.
System energy contours, given coordinates
Next displacements along this vector
begin adagio region region_1
begin solver
begin cg
line search secant (<real>scale_factor)
line search backtrack (...options...)
end
end
end
Secant: Default strategy. Usually very effective.
Backtrack: An alternative, more configurable option. Can be more robust in some cases.
(Other options available but not shown)
Tip: Occasionally the default line search will fail, this is usually accompanied by an error message about “maximum cutbacks” reached. Modifying the line search strategy can sometimes help resolve errors or improve convergence. Using “line search secant 1.0e-3” or “line search secant 1.0e-6” can help in some problems.
Syntax:

## Slide 116: The line search: when things go wrong
Current solution: Hex/quad element patch with a severely distorted element.
(Hex Shape = 0.01)
Line search result:
Increased distortion causes element inversion
(Hex Shape = -0.05)
SIERRA/SM, by default, makes attempts (20) to find a solution without inverted elements along the search direction. However, if you see this message it’s likely a clue that something else in the analysis may need further inspection. Use “iteration plot” and various element shape metrics to further diagnose. Even if an uninverted solution is found, it usually means the step size is so small that future solution progress may be minimal.
Multiple attempts to find a step length if the solution at is inverted

## Slide 117: Example 10: Predictors and tension specimens
Our system model requires material constitutive models to be fit, and we’re using tension specimen models to reduce testing requirements.
Units are: Force: Newtons
Distance: Meters
Time: Seconds
Quarter symmetry model boundary conditions
Prescribed displacements

## Slide 118: Example 10: The effect of a load step predictor
Ex10: Experiment with predictor settings
File: tension_specimen.i
The predictor is disabled this input deck by default. Run the input and watch the log file as it progresses. (Kill the run with CTRL+C if you get tired of watching it).
  Open the file with “less <filename>” at a command prompt
  Press “SHIFT+F” to follow the log file (or hold down “END”)
Enable the predictor by setting “SCALE FACTOR = 1.0” in the “LOADSTEP PREDICTOR” command block. How does the convergence change?
Extra credit: The constitutive model used in this example is rate-dependent. Investigate how “time” plays a role in the quasi-static solution here by changing the loading rate. The input deck has an APREPRO variable at the top of the file called “load_rate_scale”:
Run an analysis with load_rate_scale = 10.0
Run an analysis with load_rate_scale = 0.1
How do the results differ from the nominal scale factor of 1.0? Did this impact convergence?

## Slide 119: Example 10: Results and discussion
No load step predictor: 190 sec., 31k iterations
~160 iter/sec.
With load step predictor: 17 sec., 2.5k iterations
~150 iter/sec.
The load step predictor can dramatically increase the effectiveness of CG solvers.

## Slide 120: Example 10: Extra credit – rate-dependence
Rate-dependence means something – a material constitutive model in this case – depends on time.
Therefore, the same displacement applied over different time ranges will produce different results.
We often refer to implicit as a quasi-static solution because of this.
Time stepping does matter to the solution when there is rate-dependence!
1094 iters
(0 failed mp)
5949 iters
(8 failed mp)
3334 iters
(2 failed mp)

## Slide 121: Build your own solver!
begin solver
begin cg
end
end
begin adaptive time stepping
maximum failure cutbacks = 5
cutback factor = 0.5
end
One of the beautiful aspects of the SIERRA/SM solver structure is that it provides considerable flexibility to compose unique “solvers” with behavior that caters to a specific problem. Here are a few:
There is almost no reason not to include adaptive time stepping. Really. More than 5 or 10 cutbacks is usually unnecessary. If after 10 cutbacks you’re not converged, you probably aren’t going to.
This will solve many of your problems, and is a good place to start. Get rid of that old input deck you’ve been copying a solver block from. Delete it, it’s causing you more harm than good!
The target residuals are set to reasonable values for engineering needs.
The maximum number of iterations is adjusted based on the number of nodes in the problem, permitting more iterations for larger problems.
Sometimes useful for:
Simple models
Quick analyses that do not need optimizing

## Slide 122: Build your own solver!
begin solver
begin cg
target relative residual = 1.0e-3
acceptable relative residual = 5.0e-3
reference = belytschko
maximum iterations = 40
begin full tangent preconditioner
small number of iterations = 20
end
end
end
begin adaptive time stepping
maximum failure cutbacks = 5
cutback factor = 0.5
end
The full tangent preconditioner is powerful and can reduce the residual quickly, but it’s expensive.
A moderate “small number of iterations” (20) allows re-use of the full tangent preconditioner across model problems, increasing efficiency.
The “small number of iterations” (20) is set relative to the “maximum iterations” (40).
Sometimes useful for:
Most small to medium sized models

## Slide 123: Build your own solver!
begin solver
begin cg
target relative residual = 1.0e-3
acceptable relative residual = 5.0e-3
reference = belytschko
maximum iterations = {400 + 50}
iteration print = 50
begin full tangent preconditioner
iteration print = 5
minimum smoothing iterations = 400
small number of iterations = 420
adaptive strategy = update
end
end
end
begin adaptive time stepping
maximum failure cutbacks = 5
cutback factor = 0.5
end
A nodal preconditioner will be applied for the first 400 iterations, followed by a full tangent preconditioner for 50 iterations (maximum). APREPRO is used to make this algebra clearer.
If convergence is reached within the first 420 iterations, we will reuse the preconditioner.
If the full tangent preconditioner becomes ineffective, we’ll update it again.
Iteration print commands help limit the printing so we can see progress in the residual reduction at a glance.
Sometimes useful for:
Hard-to-converge models which are potentially ill-conditioned.
Small to medium sized models; some large models.

## Slide 124: Build your own solver!
begin solver
begin cg
target relative residual = 1.0e-3
acceptable relative residual = 5.0e-3
reference = belytschko
maximum iterations = 2000
iteration print = 200
end
end
begin adaptive time stepping
maximum failure cutbacks = 5
cutback factor = 0.5
end
A simple nodal preconditioner can be very effective by itself.
This isn’t much different than default settings. However we limit the maximum number of iterations to 2000: this allows us to cut back the timestep if convergence appears unlikely so we don’t waste time on ineffective solver iterations.
Sometimes useful for:
Large system models
Badly-conditioned models
Models with feature sets that do not “play nicely” with FETI.
  Spot welds
  Line welds
  Some constraints

## Slide 125: Build your own solver!
begin solver
begin cg
target relative residual = 2.0e-3
acceptable relative residual = 1.0e-2
reference = belytschko
maximum iterations = 300
iteration print = 20
line search backtrack
begin full tangent preconditioner
minimum smoothing iterations = 200
iteration update = 20
iteration print = 1
end
end
end
begin adaptive time stepping
maximum failure cutbacks = 10
cutback factor = 0.5
end
An increased residual is potentially more forgiving of hard-to-converge problems.
We allow some nodal preconditioner smoothing iterations (200), which can be increased depending on model size.
A full tangent preconditioner then takes over, updating after every 20 iterations.
We allow up to 10 time step cutbacks in the event of convergence issues.
Finally, a “backtrack” line search strategy may add robustness; but try “line search secant” (default) as an alternative.
Sometimes useful for:
Medium-sized models that may be hard to converge.
Performance issues caused by frequent full tangent updates are not an issue.

## Slide 126: In summary…
Solving an implicit problem can often be a bit of an art.
SIERRA/SM primarily uses a conjugate gradient solver
  It’s the most efficient for problems of interest to SNL
The SM solver has a few key ingredients
  Convergence measures
  Preconditioner
  Load step predictor
  Line search method
There are no “silver-bullet” solver settings that will work for every type of problem
A few strategies to monitor and improve solver speed and convergence rate

## Slide 127: MODULE 6: The Multilevel Solver and Implicit Contact
Solving the real problems

## Slide 128: Section overview
Learn about SIERRA’s multi-level solver from the perspective of implicit contact
Scratch the surface of SIERRA’s contact implementation
Learn relevant input deck syntax and log file output
Practice solving some implicit contact problems
We will …

## Slide 129: An example of the multilevel solver in action: open die forging
Kevin in a former life
Kevin after paying his dues on the floor
Really hot metal
Steel dies

## Slide 130: Implicit quasistatic solution of open die forging
Total analysis time: ~3 minutes (1 proc)
Total simulated time: ~1 minute
Nearly real-time analysis (as configured)!
Likely intractable for explicit solution, despite simplicity
Still too long to use as a training example, but:
See “ex20_multilevel_solver_contact_open_die_forging” for input deck details.

## Slide 131: A quick review of a simple nonlinear solve
Given an applied force of , what is the displacement of the spring?
Iterative solution variables
= Residual at iteration
= Displacement at iteration
= Tangent stiffness at iteration
(within tolerance)
In a “Multi-level Solver”, this iterative process is a model problem solution.

## Slide 132: What’s a “multilevel solver?”
Complex nonlinearities/discontinuities are not amenable to more direct solution approaches.
In short, “multilevel” solver just means solving a bunch of simpler problems and building complexity.
Two ways of viewing the multilevel solver:
The traditional “user guide” view
Model problem 0
Model problem 1
Model problem 2
Model problem N
…
Load step 0
Alternative perspective
Level 1 updates
Applied loads
Real
behavior
“Controlled” behavior

## Slide 133: What’s a “multilevel solver?”
Complex nonlinearities/discontinuities are not amenable to more direct solution approaches.
In short, “multilevel” solver just means solving a bunch of simpler problems and building complexity.
Two ways of viewing the multilevel solver:
The traditional “user guide” view
Model problem 0
Model problem 1
Model problem 2
Model problem N
…
Load step 0
Model problem 0
Model problem 1
Model problem 2
Model problem N
…
Load step 1
Model problem 0
Model problem 1
Model problem 2
Model problem N
…
Load step 2
Alternative perspective (multiple time steps)

## Slide 134: What’s a Level 1 solve?
Model problem 0
Model problem 1
Model problem 2
Model problem N
…
Load step 0
Model problem 0
Model problem 1
Model problem 2
Model problem N
…
Load step 1
Model problem 0
Model problem 1
Model problem 2
Model problem N
…
Load step 2
Model problem 0
Model problem 1
Model problem 2
Model problem N
…
Load step 0
A single time step is composed of multiple smaller model problems.
Think of the performance impact of adding a level 1 solver control!
A single time step is composed of multiple simpler Level 0 Model Problems. These are solved using the “Core” CG solver.
Level 1 Update: Depending on the control Type, some quantity is slightly changed or updated.
Unlike simpler analyses, we need not fail the solve for large residuals. We simply accept high residuals in hopes that subsequent updates lead to better model problems.
We check overall residual for Level 1 convergence after each model problem.

## Slide 135: The multi-level solver has considerable flexibility
There are several solver controls available:
  Control Contact: Holds the potential contact set constant. Helps adjust for discontinuity introduced by contact.
  Control Failure: Restrict the amount of material allowed to fail (via element death) in a single time step. (Remove the most damaged element first).
  Control Damped Solve: Temporary elastic constraints are inserted into the model that gradually fade away, assisting with implicit contact seating.
  Control Stiffness: Adjust material volumetric response each model problem. Used for nearly-incompressible materials and disparate stiffnesses.
Multiple solver controls can be updated at the same level
Potentially 100’s of solver controls and options to fine-tune according to analysis needs
Up to 2 different levels of control.

## Slide 136: Why does implicit contact need a level 1 update?
Contact is a chicken-and-egg problem. We need to know the final solved state to know what’s in contact… but we need to know what’s in contact to solve any model problem. So we iterate.
Prescribed Displacement
Coulomb Friction
Rigid Platen
Elastic-Plastic Material
Model Problem 100:
Converged  We now know the solution at N+1
Model Problem 0:
We prescribe the given displacements
iterate
Each model problem, we examine a set of contact constraints and determine how much force needs to be applied to enforce our constraint (zero penetration)
At model problem 0, we don’t know if this node should actually be in contact in our final solution at N+1!

## Slide 137: “Level 1 Solver controls” vs. “Level 1 controls”
Contact is a “Level 1” control (or Level 2, just not a Level 0)
Contact enforcement, the interactions, and various implementation details are all controlled in the “begin contact definition” command block.
  The details of control contact and its implementation are regretfully beyond the scope of this training.
  The configuration of contact has an intimate connection to the ability to solve contact.
The Level 1 Solver controls are configured in the “begin control contact” command block. Here, we configure things like:
  How many iterations are allowed for the level 1 solver?
  What tolerance do we want to converge to?

## Slide 138: Level 1 solver controls (a few of many)
begin solver
begin cg
# core model problem convergence and solve
target relative residual = <real>
acceptable relative residual = <real>
...
end
begin control contact
# convergence commands
target residual = <real>
target relative residual = <real>
acceptable residual = <real>
acceptable relative residual = <real>
lagrange acceptable gap = <real>
lagrange acceptable relative gap = <real>
# iteration limits
minimum iterations = <int>
maximum iterations = <int>
# diagnostic output
iteration plot = <int>
end control contact
end
Some of the most common syntax for a control contact configuration
Define a solver settings for each model problem. The level 0 model problems should be solved to a tighter/lower residual than the level 1 problem. Recommended is 10x lower.
The acceptable residual should be arbitrarily large so that badly-posed model problems are “accepted” and thus permit the level 1 solver to update and try again.
Define what “solved” means for the load step. These commands mean the same thing as the core solver, but are checked after each level 1 update. Additionally, we can require convergence on the “contact gap.”
Set practical limits on the number of iterations (model problems) to solve each load step. If we reach the maximum iterations without achieving convergence, the load step fails.
Debug. Same as CG solve. Optionally output model state every “N” level 1 solve iterations.
Level 0
Level 1

## Slide 139: Additional resources on compsim.sandia.gov
Strongly recommend browsing the additional training resources available for additional perspective

## Slide 140: Example 11: Implicit contact with the multilevel solver
M10 bolts
Compliant structure:
Implicit helps to preload these bolts. It’s very difficult to estimate stiffness of the structure being preloaded a priori.
Top plate
Bottom plate
5.2cm

## Slide 141: Example 11: Implicit contact with the multilevel solver
Ex11: Preload the bolted joint
File: bolt_preload.i
Use the default solver. Run the input and watch the log file as it progresses.
  How many model problems does the first load step take?
  What tolerance did the level 0 solver converge to? What about the level 1 solver?
  Optionally, visualize the results.
“Loosen” the level 1 relative tolerance to 0.05. Compare with default solver settings.
  Add a level 1 solver block to the solver (begin control contact / end)
  Set target relative residual = 0.05 for the level 1 solver. Set it to 0.005 for the cg solver.
  Optimize the solve speed by using a full tangent preconditioner.
Extra credit: The multilevel solver can sometimes be avoided. Use Tied MPCs combined with a Procedural Transfer to further optimize the preload calculation by first preloading in a “tied” state (procedure 1), and transferring the results for a final solve with contact enabled (procedure 2). You should be able to improve the solution speed by at least 50%.

## Slide 142: Example 11: Results and discussion – default solver
Level 1 solver summary. Details, in this case, refer to the contact controls.
Level 1 converged, so start next load step.
Model problem converged to default 1.0e-4 relative tolerance
Load step 0: converged to default 1.0e-3 relative tolerance
11 model problems to solve load step 0
Summary of solver performance

## Slide 143: Example 11: Results and discussion – loosen tolerance
begin solver
begin cg
target relative residual = 0.005
begin full tangent preconditioner
small number of iterations = 10
end
end
begin control contact
target relative residual = 0.05
end control contact
end
Level 1 Tolerance | Solve Time
0.05 | 10 sec
0.001 | 30 sec
Solution for both relative tolerance of 0.05 and 0.001 look very similar.
Solution difference between relative tolerances obtained by subtracting solution (tol=0.001) from solution (tol=0.05).
Optimized solver syntax for this problem
exodiff file1.e file2.e diff.e

## Slide 144: Example 11: Extra credit – procedural transfer optimization
begin tied mpc
tied faces = bottom_plate
tied nodes = top_plate
end
begin tied mpc
tied faces = bottom_plate
tied nodes = bolt_thread
end
begin tied mpc
tied faces = bolt_head
tied nodes = top_plate
end
First procedure:
Remove contact definition
Remove control contact from solver block
Remove or rename results output file
Add TIED MPCs to replace contact constraints:
Second procedure:
Basically a duplicate of the original problem
Remove preload command block
Use a different region name
One time step to let contact “settle”
Add a procedural transfer command block:
begin adagio procedure proc2
begin procedural transfer
include all blocks
end
...
other procedural commands
...
end
Description | Solve Time
One procedure | 10 sec
Two procedures, initially solve with MPCs | 5 sec
50% speed improvement by strategically setting up the analysis to eliminate the level 1 solver iterations.
Very likely a much larger speed-up could be had on a bigger problem.

## Slide 145: In summary…
Extremely nonlinear problems require a multi-level solver in SIERRA/SM
The multilevel solver …
  Converts difficult nonlinear problems into a series of easier-but-still-nonlinear problems
  Adds nested level of solves
Adding a multilevel solve control increases the amount of iteration necessary to solve a problem
Increases time necessary to solve
Convergence depends strongly on all of the inner solves working well
  Example: badly-behaved material models can appear as “contact convergence issues”
Level 1 Solver controls
Level 0 core Solver
Preconditioner Update
Material model solver
(Nesting minions, for sale on Etsy)
Element formulation

## Slide 146: MODULE 7: Implicit Dynamics
Bridging the gap between explicit and implicit

## Slide 147: Section overview
Learn about the differences between implicit dynamics and implicit statics
Learn how to enable implicit dynamics in SIERRA/SM
Learn about implicit dynamics input deck settings
Practice using implicit dynamics
We will …

## Slide 148: A gratuitous example of implicit dynamics
Simulation Description:
Free-falling block on a stack of 1/16” thickness aluminum cans.
Gravity loading
300ms total time
3 hr. simulation
Two time blocks:
  Free fall: 5ms
  Crush event: 0.5ms
Solid elements, UG Hex

## Slide 149: Another example of implicit dynamics
Simulation Description:
Free-falling rubber chain links
Gravity loading
30 min. simulation time
General contact
Fictitious rubber-like neohookean material
Solid elements, composite tetrahedral

## Slide 150: What is “implicit dynamics?”
Expressed more generally as vectors
Expressed as a linear system of equations
Recall our toy mass-spring system example, where perhaps we also have damping terms
Statics:
Dynamics:
Implicit dynamics solutions keep the inertial force term which, among other things, is responsible for wave propagation. Moreover, the system of equations is solved implicitly through time.
Keep!
Delete!

## Slide 151: The many types of dynamics solutions
Dynamic
Solutions
Linear
SIERRA/SD
Nonlinear
SIERRA/SM
Direct Methods
Modal Methods
Direct Methods
Explicit
Implicit
Explicit
Implicit
“I need to solve a dynamics problem…”
Implicit
Basic analysis need
Determine relevant physics
Determine solution strategy
Select time integration method
Uncommon
Standard SIERRA/SD “direct transient”, but also a form of “implicit dynamics”
Standard SIERRA/SD “modal transient”
Standard SIERRA/SM “explicit dynamics”
Standard SIERRA/SM “implicit dynamics”

## Slide 152: Basic types of dynamics solutions in SIERRA/SM
Linear, Implicit Dynamics
Physics are approximately linear (e.g. some structural shock/blast environments)
Fast solution, need only solve a linear system
Good for short to moderate duration events (typical usage ~1ms – 10s)
Somewhat limited damping capability
Includes all frequencies in the response, numerically damps non-physical high frequency response
Linear, Modal Transient
Linearized physics are further approximated within a limited low-frequency range (e.g. vibration testing of a component/structure)
Requires an eigenvector solution type first
Very fast time integration
Best for longer time durations (typical usage ~1s – 100s)
Customized damping possible
Nonlinear, Explicit Dynamics
Best solution type for highly-nonlinear events (e.g. crash/impact events)
Typical usage is short duration events (~1ns – 1s)
No implicit solve, but time step is constrained by numerical stability limits
Limited damping options – damping decreases the stable time step.
“High frequency noise” is unavoidable due to lack of numerical damping in time integration
Nonlinear, Implicit Dynamics
Best solution type for moderately complex nonlinear events of longer duration (e.g. blast wave response of a nonlinear structure)
Typical usage is long duration events (1s – 10hr)
Nonlinear implicit solve limits solution speed
Can sometimes be used to help obtain quasi-static solutions by eliminating rigid body mode issues

## Slide 153: A cursory theory of time integration
Start with some spatial discretization of the underlying PDE
(note: still continuous in time)
Discretize time. Multiple strategies here – some well-known include:
Newmark-Beta
Hilbert-Hughes-Taylor (default in SIERRA/SM)
Generalized Alpha (available in SIERRA/SM)
displacement at time step ‘’ velocity ( acceleration ()
HHT Discretization
The time integration scheme above creates three new parameters: (, , ). These parameters control some important properties of the time integration scheme.
Explicit (notional)

## Slide 154: The time integration coefficients
By strategically discretizing time into smaller increments , , , …. we introduced three new coefficients:
These coefficients control properties of the time integration scheme:
Second-order accuracy (we want this)
Numerical dispersion (undesirable)
Numerical dissipation (desirable at high frequencies)
Implicit vs. explicit solution (based on need)

## Slide 155: Additional references
SIERRA/SM User’s Guide and Theory Manual. Practical usage guidelines and implementation theory. See also references therein.
SIERRA/SD Theory Manual. Outline of the generalized alpha method available in both SIERRA/SM and SIERRA/SD.
“Fundamental Principles Defining the Implicit Dynamics Context”. A nice write-up from previous trainings with some very practical discussions.
The Finite Element Method (Ch. 9). A widely-available textbook with detailed discussion and development of time integration schemes.

## Slide 156: The time integration coefficients (continued)
HHT
Recall the HHT Discretization (other discretization strategies such as the Generalized Alpha Method are not presented in detail), reproduced here for reference:
Coefficients | Scheme | Unconditionally Stable | Properties
 | Central Difference | No | SIERRA/SM explicit time integration. Stability limited by time step size.
 | Trapezoid rule (HHT) | Yes | Simple implicit time integration, default in SIERRA/SD. No high frequency damping.
 | HHT | Yes | Default time integration scheme in SIERRA/SM. Balanced damping and dispersion.
 | HHT | Yes | Maximal high frequency damping settings. Can be useful in quasi-static analyses.
Coefficients | Scheme | Unconditionally Stable | Properties
 | Central Difference | No | SIERRA/SM explicit time integration. Stability limited by time step size.
 | Trapezoid rule (HHT) | Yes | Simple implicit time integration, default in SIERRA/SD. No high frequency damping.
 | HHT | Yes | Default time integration scheme in SIERRA/SM. Balanced damping and dispersion.
 | HHT | Yes | Maximal high frequency damping settings. Can be useful in quasi-static analyses.

## Slide 157: Enabling implicit time integration in SIERRA/SM
begin adagio region <region_name>
begin implicit dynamics
use {HHT|GENERALIZED ALPHA INTEGRATION}(HHT)
alpha = <real>(-0.1)
beta = <real>(0.3025)
gamma = <real>(0.6)
contact timestep = {on|off}(on)
end
end
Select a time integration scheme. HHT provides good performance as a default. It is typically not necessary to adjust this.
Select integrator coefficients. Typically the defaults work well. Coefficients may be selected to optimize numerical dissipation or numerical damping in specialized cases. Incorrect parameters can effect the accuracy of the time integration. Relationships exist between parameters; see user manual for details.
Link timestep with contact. This line command enables the time integrator to limit the time step in hopes of resolving contact accurately. On by default, but may be turned off provided the results are confirmed accurate.
*see user manual for additional syntax details
Common syntax options
Most analyses need only an empty implicit dynamics command block.

## Slide 158: Selecting an implicit dynamics time step size
Considerations for time step size
Time step dictates algorithmic damping and dispersion at each frequency
Too small of a time step might introduce error due to high frequency noise and round-off
Too large of a time step might accumulate error and suppressing true response
An overly-simple rule of thumb: Aim for 100x-1000x the explicit critical time step.
Additional considerations:
Consider the frequency of interest or forcing frequency content,
  (period of interest)
  (a different “rule of thumb”)

## Slide 159: Example 12: Pseudo-blast wave propagation scenario
4 in.
~16 in.
Fictitious weapon case
A blast wave passes over a weapon case.
A component is to be mounted inside, estimate the displacement as a result of the blast.
Determine displacement here

## Slide 160: Example 12: Implicit dynamics
Ex12: Use implicit dynamics to predict the dynamics of a weapon case
Extra credit: Add a viscous damping block. Use a mass damping coefficient of 600 and a stiffness damping coefficient of 10.0e-6 as a starting point. Re-run the analysis. What advantage does and implicit dynamics solver give compared to an explicit solver?
File: case_blast.i
Add implicit dynamics to the input deck.
  Run the analysis
  Visualize the results. The pressure wave can be visualized in ParaView by loading the sideset named “case_exterior” as well as the face variable “pressure”.
  Select a node and plot the displacement vector in ParaView
Determine the case frequency that has been excited.
  Find two or more displacement peaks to estimate the period of oscillation
  Divide the period of oscillation by ~10 or 20 to estimate a minimum time increment.
  If desired, re-run the analysis using a larger or smaller time step to see how the results compare.
Why might using a BELYTSCHKO reference here be useful over the default EXTERNAL?

## Slide 161: Example 12: Results and discussion – time increment
Plot time history somewhere in the middle of the case
A minimum implicit dynamics timestep to capture an 8kHz response is . We need to know something about our structure and/or loading to estimate this.

## Slide 162: Example 12: Results and discussion – log file
Log file annotation that we are using implicit dynamics
Blast wave traversing.
External force vector from applied blast loading gives reference of ~340lb
Convergence in 3 iter.
Blast wave traversal nearly complete. External force vector from applied blast loading gives reference of ~48lb
Convergence in 4 iter.
Blast wave has passed.
No external forcing or reactions. Default behavior results in unit reference of 1lb.
Convergence in 6 iter.
Using belytschko reference results in:
190 fewer iterations
20% - 30% faster
Trade-off: larger converged absolute residual

## Slide 163: Example 12: Results and discussion
begin viscous damping
include all blocks
mass damping coefficient = 600
stiffness damping coefficient = 10e-6
end cg
A feature of implicit dynamics is that time integration is unconditionally stable. A practical benefit of that is the ability to apply nearly any type of damping.
In contrast, explicit time stepping methods are typically used without damping because of the dramatic decrease in stable time step size as damping is increased.
Undamped results ()
Solve time: ~80s
Damped results
()
Solve time: ~160s

## Slide 164: In summary…
Implicit dynamics is another tool in the analyst toolbox to solve specific types of problems.
Implicit dynamics integrates the equations of motion in time by including inertial forces.
Time stepping schemes are unconditionally stable (provable for linear systems)
Implicit dynamics is very easy to toggle on/off in SIERRA/SM
  Useful for exploring the effects of inertia in a particular problem.
  Useful for handling rigid body modes
Implicit dynamics can be computationally expensive when paired with a multilevel solver.
  Typically need many small time steps
  Each time step typically needs many level 1 solver iterations! This adds up quickly!

## Slide 165: MODULE 8: Pitfalls, Debugging, Tips & Tricks
Making sure the model is fit for implicit

## Slide 166: Section overview
Learn about some common pitfalls, and how to deal with them
Review techniques for debugging using the log file
Learn about implicit solutions for large models
Explore debugging strategies and solutions through example
Well will re-iterate some previously discussed topics
We will …

## Slide 167: Common pitfalls for implicit quasi-statics
P
Buckling
Load
Displacement
Snap Through
P
Potential Failure
Nearby Failure Conditions
Load
Displacement
Thread Disengagement
Zone of solution difficulty
Zone of solution difficulty

## Slide 168: Common pitfalls for implicit quasi-statics
Pn
Pt
Friction coefficient μ
Pt
Displacement
Slip
Stick
Stick/Slip
Impact ‘door stop’
Rate-dependent material models
Multiple constraints on nodes (e.g. where contact intersects kinematic BC’s)
Sharp material non-linearity and/or incompressible materials
P-delta effects
Poorly-shaped elements in input mesh
Initial overlap in input mesh (use “Overlap Removal”; inspect mesh after)
Thermal-Mechanical coupling
Zone of solution difficulty

## Slide 169: Example 13: Failure to converge on a simple mesh!
Ex13: Figure out why a simple solution fails
File: column.i
Run the input file for both meshes. The input deck is parameterized using APREPRO to easily run both meshes individually from the command line:
  >> adagio -i column.i -D ‘mesh=beam1.g’ -o column.beam1.log
  >> adagio -i column.i -D ‘mesh=beam2.g’ -o column.beam2.log
Look at the log file element shape quality metrics. Find the section titled ELEMENT SHAPE QUALITY INFORMATION and note the ORIGINAL MESH MIN QUALITY value for both meshes.
Extra credit: Fix the input deck so it works with both meshes. Some potential solutions:
Use a uniform gradient solid section
Use a smaller time step
Edit the mesh in CUBIT by using the volume smoothing tool. Export the fixed mesh.
beam1.g
beam2.g
Extra extra credit: Use the CG solver line command “developer command: iteration plot on failure” to write out the results of the mesh at a failed time step. Visualize the results in ParaView by selecting the “element_quality” field. Can you see why the solve is failing more clearly now?

## Slide 170: Example 13: Results and discussion – mesh quality
column.beam1.log
column.beam2.log
“Good quality” mesh is more likely to converge without issues. Best quality is 1.0
“Bad quality” mesh is likely to trigger solve failures. Worst quality is <= 0.0
On average we have a very high quality mesh, but just a few bad elements in the wrong place at the wrong time can trigger failure.

## Slide 171: Example 13: Results and discussion – what’s going on
Original mesh starts with terribly-distorted elements. The SD Hex is less forgiving of this situation than the UG hex, which only requires an integration point in the center of the element.
Once boundary conditions are applied, the mesh distortion becomes so bad that the elements are inverted (“negative volume”).

## Slide 172: Beware of “Solver DNA”
There exist many (~100) additional solver commands and options, E.g.:
Alter how aggressively Lagrange multipliers (constraint stiffness) are updated
Alter how difficult it is for constraints to change state from captured to released
Reset tolerances, Line search options, beta methods, etc.
However, Beware of ‘Solver DNA’
Often complex solver parameters are moved from one analysis to the next where the original reason for the option is lost
Many times better convergence is obtained going back to simple defaults
Often simplifying physical setup is more effective for convergence (adding constraints, staging loads to limit non-linearity, displacement rather than force control, etc.)
Don’t copy your neighbors solver settings!

## Slide 173: Working with large models (1/2)
Large and complex models pose some particular challenges for implicit
Memory requirements:
  Full tangent preconditioner may run out of memory
  Potential remedy: use fewer processes per node (“--ppn“ option to sierra script)
Solve speed – full tangent preconditioner:
  Full tangent preconditioner may be very slow to update or apply (“U” in the log file)
  Typically run on multiple processors, and more processors increase the number of linear iterations required to solve the coarse grid in FETI. More iterations  More time  Less efficient solution.
Solve speed – Nodal preconditioner
  More nodes may require more CG iterations.
  More iterations  More time  Less efficient solution.

## Slide 174: Working with large models (2/2)
Large models with complexity (e.g. contact, many blocks):
  Anything that’s hard already is made worse by adding contact.
  Likelihood of very poor conditioning (very large, very small elements)
  Overlap is very likely.
  Potential for issues multiplies with number of blocks.
Recommendations:
  Start small. Build and test individual subassemblies using simpler loads and boundary conditions to verify no issues.
  Combine assemblies and build incrementally.
  Use restart files if solution speed is too slow to complete in queue time.

## Slide 175: Use the log file for debugging
The log file should be a primary source for debugging
Look for error and/or warning messages. Eliminate them!
  Warning messages almost always indicate a problem
If using adaptive time stepping, look for cutbacks
  Search the log file for “cutting back”
  This is often where the trouble started: inverted or poorly-shaped elements, contact lost, loss of static equilibrium, etc.
Look for acceptable tolerances (“<A”) achieved instead of target tolerances (“<T”)
  Why?
  Can it be avoided somehow?

## Slide 176: Log file debugging: model problem solve
===========================================================================================================
Begin load step = 0 Solution period Apst_Procedure_p1 is 0.0% complete
Old Time Time Step New Time Stop Time CPU Time(s) Wall Time(s)
0.0000e+00 1.0000e+00 1.0000e+00 1.0000e+00 8.1388e-01 2.0306e-02
-----------------------------------------------------------------------------------------------------------
LINEAR MP RELATIVE EXTERNAL
RBM ITER ITER RESIDUAL RESIDUAL REFERENCE ENERGY DISPLACEMENT
-----------------------------------------------------------------------------------------------------------
- - 0 1.534e+11 9.714e-01 1.579e+11 - -
0 U 1 1 5.045e+10 6.957e-01 7.252e+10 5.301e+08 7.486e+00
0 1 2 2.802e+10 4.079e-01 6.870e+10 1.865e+08 5.993e-01
0 1 3 8.507e+09 1.272e-01 6.690e+10 1.025e+06 1.696e-01
0 1 4 1.399e+09 2.112e-02 6.621e+10 3.374e+03 1.777e-03
0 1 5 6.609e+08 9.969e-03 6.630e+10 6.803e+03 1.677e-04
0 1 6 2.010e+08 3.031e-03 6.632e+10 8.050e+01 4.362e-05
0 1 7 7.116e+07 1.073e-03 6.631e+10 4.210e-01 9.116e-06
0 1 8 3.546e+07 5.348e-04 6.630e+10 4.855e-02 1.109e-06
0 1 9 1.414e+07 2.133e-04 6.631e+10 1.567e-02 2.213e-07
0 1 10 4.935e+06 7.443e-05<T 6.631e+10 1.533e-03 2.833e-08
2-norm of nodal force imbalance
Reference quantity (external force, energy, etc.)
Alternative Convergence Criteria
Residual normalized by reference quantity
Rigid body modes of preconditioner
Tangent re-calculation (“U”pdate)
convergence status

## Slide 177: Log file debugging: model problem solve
===========================================================================================================
Begin load step = 0 Solution period Apst_Procedure_p1 is 0.0% complete
Old Time Time Step New Time Stop Time CPU Time(s) Wall Time(s)
0.0000e+00 1.0000e+00 1.0000e+00 1.0000e+00 8.1388e-01 2.0306e-02
-----------------------------------------------------------------------------------------------------------
LINEAR MP RELATIVE EXTERNAL
RBM ITER ITER RESIDUAL RESIDUAL REFERENCE ENERGY DISPLACEMENT
-----------------------------------------------------------------------------------------------------------
- - 0 1.534e+11 9.714e-01 1.579e+11 - -
0 U 1 1 5.045e+10 6.957e-01 7.252e+10 5.301e+08 7.486e+00
0 1 2 2.802e+10 4.079e-01 6.870e+10 1.865e+08 5.993e-01
0 1 3 8.507e+09 1.272e-01 6.690e+10 1.025e+06 1.696e-01
0 1 4 1.399e+09 2.112e-02 6.621e+10 3.374e+03 1.777e-03
0 1 5 6.609e+08 9.969e-03 6.630e+10 6.803e+03 1.677e-04
0 1 6 2.010e+08 3.031e-03 6.632e+10 8.050e+01 4.362e-05
0 1 7 7.116e+07 1.073e-03 6.631e+10 4.210e-01 9.116e-06
0 1 8 3.546e+07 5.348e-04 6.630e+10 4.855e-02 1.109e-06
0 1 9 1.414e+07 2.133e-04 6.631e+10 1.567e-02 2.213e-07
0 1 10 4.935e+06 7.443e-05<T 6.631e+10 1.533e-03 2.833e-08
Rigid Body Modes (RBM’s):
If =0: no rigid body modes detected by solver
If >0:
  Add BC’s to constrain free DOF’s in one or more element blocks
  Use ITERATION PLOT to find any missed RBM’s
  If loss of contact, element death, etc. cause static problem to become dynamic: try using explicit dynamics, implicit dynamics, or control damped solve

## Slide 178: Log file debugging: model problem solve
===========================================================================================================
Begin load step = 0 Solution period Apst_Procedure_p1 is 0.0% complete
Old Time Time Step New Time Stop Time CPU Time(s) Wall Time(s)
0.0000e+00 1.0000e+00 1.0000e+00 1.0000e+00 8.1388e-01 2.0306e-02
-----------------------------------------------------------------------------------------------------------
LINEAR MP RELATIVE EXTERNAL
RBM ITER ITER RESIDUAL RESIDUAL REFERENCE ENERGY DISPLACEMENT
-----------------------------------------------------------------------------------------------------------
- - 0 1.534e+11 9.714e-01 1.579e+11 - -
0 U 1 1 5.045e+10 6.957e-01 7.252e+10 5.301e+08 7.486e+00
0 1 2 2.802e+10 4.079e-01 6.870e+10 1.865e+08 5.993e-01
0 1 3 8.507e+09 1.272e-01 6.690e+10 1.025e+06 1.696e-01
0 1 4 1.399e+09 2.112e-02 6.621e+10 3.374e+03 1.777e-03
0 1 5 6.609e+08 9.969e-03 6.630e+10 6.803e+03 1.677e-04
0 1 6 2.010e+08 3.031e-03 6.632e+10 8.050e+01 4.362e-05
0 1 7 7.116e+07 1.073e-03 6.631e+10 4.210e-01 9.116e-06
0 1 8 3.546e+07 5.348e-04 6.630e+10 4.855e-02 1.109e-06
0 1 9 1.414e+07 2.133e-04 6.631e+10 1.567e-02 2.213e-07
0 1 10 4.935e+06 7.443e-05<T 6.631e+10 1.533e-03 2.833e-08
Tangent Update:
Benefits: much better convergence rate when problem is non-linear
Drawbacks: computationally expensive
When to try more frequent updates: no RBM’s but residual is stagnating
Indicator that it is beneficial: residual drops significantly at each update
Tips:
  Try changing ITERATION UPDATE: controls tangent update frequency
  Try changing SMALL NUMBER OF ITERATIONS: avoids updates at start of load step when previous load step converged quickly

## Slide 179: Log file debugging: model problem solve
===========================================================================================================
Begin load step = 0 Solution period Apst_Procedure_p1 is 0.0% complete
Old Time Time Step New Time Stop Time CPU Time(s) Wall Time(s)
0.0000e+00 1.0000e+00 1.0000e+00 1.0000e+00 8.1388e-01 2.0306e-02
-----------------------------------------------------------------------------------------------------------
LINEAR MP RELATIVE EXTERNAL
RBM ITER ITER RESIDUAL RESIDUAL REFERENCE ENERGY DISPLACEMENT
-----------------------------------------------------------------------------------------------------------
- - 0 1.534e+11 9.714e-01 1.579e+11 - -
0 U 1 1 5.045e+10 6.957e-01 7.252e+10 5.301e+08 7.486e+00
0 1 2 2.802e+10 4.079e-01 6.870e+10 1.865e+08 5.993e-01
0 1 3 8.507e+09 1.272e-01 6.690e+10 1.025e+06 1.696e-01
0 1 4 1.399e+09 2.112e-02 6.621e+10 3.374e+03 1.777e-03
0 1 5 6.609e+08 9.969e-03 6.630e+10 6.803e+03 1.677e-04
0 1 6 2.010e+08 3.031e-03 6.632e+10 8.050e+01 4.362e-05
0 1 7 7.116e+07 1.073e-03 6.631e+10 4.210e-01 9.116e-06
0 1 8 3.546e+07 5.348e-04 6.630e+10 4.855e-02 1.109e-06
0 1 9 1.414e+07 2.133e-04 6.631e+10 1.567e-02 2.213e-07
0 1 10 4.935e+06 7.443e-05<T 6.631e+10 1.533e-03 2.833e-08
Solution Iterations:
When to increase maximum iterations: residual still dropping at max
When to decrease maximum iterations: residual bottoming out before max
When to use minimum iterations >0: residual <T but still substantially decreasing (in this case, increasing min iterations can convergence of subsequent steps)

## Slide 180: Log file debugging: model problem solve
===========================================================================================================
Begin load step = 0 Solution period Apst_Procedure_p1 is 0.0% complete
Old Time Time Step New Time Stop Time CPU Time(s) Wall Time(s)
0.0000e+00 1.0000e+00 1.0000e+00 1.0000e+00 8.1388e-01 2.0306e-02
-----------------------------------------------------------------------------------------------------------
LINEAR MP RELATIVE EXTERNAL
RBM ITER ITER RESIDUAL RESIDUAL REFERENCE ENERGY DISPLACEMENT
-----------------------------------------------------------------------------------------------------------
- - 0 1.534e+11 9.714e-01 1.579e+11 - -
0 U 1 1 5.045e+10 6.957e-01 7.252e+10 5.301e+08 7.486e+00
0 1 2 2.802e+10 4.079e-01 6.870e+10 1.865e+08 5.993e-01
0 1 3 8.507e+09 1.272e-01 6.690e+10 1.025e+06 1.696e-01
0 1 4 1.399e+09 2.112e-02 6.621e+10 3.374e+03 1.777e-03
0 1 5 6.609e+08 9.969e-03 6.630e+10 6.803e+03 1.677e-04
0 1 6 2.010e+08 3.031e-03 6.632e+10 8.050e+01 4.362e-05
0 1 7 7.116e+07 1.073e-03 6.631e+10 4.210e-01 9.116e-06
0 1 8 3.546e+07 5.348e-04 6.630e+10 4.855e-02 1.109e-06
0 1 9 1.414e+07 2.133e-04 6.631e+10 1.567e-02 2.213e-07
0 1 10 4.935e+06 7.443e-05<T 6.631e+10 1.533e-03 2.833e-08
Convergence Status:
When to tighten target: residual still dropping; or, later step fails to converge
When to loosen target: current target is small and never achieved
When to tighten acceptable: CG is outer loop of single-/multi-level solve and observably bad solution(s) accepted; later step fails
When to loosen acceptable: CG is inner loop of multi-level solve (e.g. to avoid erroring-out when control contact has a bad model problem)

## Slide 181: Log file debugging: model problem solve
Residual / Relative Residual:
If stagnating at a large value:
  Another indicator of potential RBM’s
  Add BC’s to constrain free DOF’s in one or more element blocks
  Use ITERATION PLOT to find any missed RBM’s
  If loss of contact, element death, etc. cause static problem to become dynamic: try using explicit dynamics, implicit dynamics, or control damped solve
------------------------------------------------------------------------------------------
LINEAR MP RELATIVE EXTERNAL
RBM ITER ITER RESIDUAL RESIDUAL REFERENCE ENERGY DISPLACEMENT
------------------------------------------------------------------------------------------
0 1 1 2.616e-06 2.677e-02 9.772e-05 4.940e-24 7.156e-34
0 1 2 2.616e-06 2.677e-02 9.772e-05 4.940e-24 7.156e-34
0 1 3 2.616e-06 2.677e-02 9.772e-05 4.940e-24 7.156e-34
0 1 4 2.616e-06 2.677e-02 9.772e-05 4.940e-24 7.156e-34
0 1 5 2.616e-06 2.677e-02 9.772e-05 4.940e-24 7.156e-34

## Slide 182: Log file debugging: control contact
----------------------------------------------------------
MAX GAP = 8.096e-01 PREVIOUS = 0.000e+00
MAX RELATIVE GAP = 1.457e+00 PREVIOUS = 0.000e+00
NUM INTERACTIONS = 82
RELEASED INTERACTIONS = 52
CAPTURED INTERACTIONS = 30
DUBIOUS INTERACTIONS = 0
RELATIVE LMULT CHANGE = 1.000e+00
ACTIVE SET CHANGE
----------------------------------------------------------
CONTACT ITERATION = 0, STEP 0
ABSOLUTE RESIDUAL = 6.587e+10
RELATIVE RESIDUAL = 5.414e-01
Max gap/overlap in any captured interaction
Max gap/overlap compared to face size
Number of evaluated interactions (constant over load step)
2-norm of linear solve residual +
contact gap residual (gap times stiffness)
Released = open no stiffness
Captured = closed, have stiffness
Dubious = changing states
Indicates change in dubious / captured / released interactions
Max change in constraint force among all active interactions

## Slide 183: Log file debugging: control contact
----------------------------------------------------------
MAX GAP = 8.096e-01 PREVIOUS = 0.000e+00
MAX RELATIVE GAP = 1.457e+00 PREVIOUS = 0.000e+00
NUM INTERACTIONS = 82
RELEASED INTERACTIONS = 52
CAPTURED INTERACTIONS = 30
DUBIOUS INTERACTIONS = 0
RELATIVE LMULT CHANGE = 1.000e+00
ACTIVE SET CHANGE
----------------------------------------------------------
CONTACT ITERATION = 0, STEP 0
ABSOLUTE RESIDUAL = 6.587e+10
RELATIVE RESIDUAL = 5.414e-01
Max Gap / Max Relative Gap; Lagrange Multiplier Change:
If oscillating or stagnating at a large value:
  Use smaller load step
  Eliminate discontinuous or large changes in BC’s
  Evaluate log file and visualize previous load steps to see if the cause is a previously poor contact solution
  Try solver settings that help avoid inherently discontinuous behavior of contact: e.g. Lagrange multiplier settings in control contact, AL penalty factor in contact interactions

## Slide 184: Log file debugging: control contact
----------------------------------------------------------
MAX GAP = 8.096e-01 PREVIOUS = 0.000e+00
MAX RELATIVE GAP = 1.457e+00 PREVIOUS = 0.000e+00
NUM INTERACTIONS = 82
RELEASED INTERACTIONS = 52
CAPTURED INTERACTIONS = 30
DUBIOUS INTERACTIONS = 0
RELATIVE LMULT CHANGE = 1.000e+00
ACTIVE SET CHANGE
----------------------------------------------------------
CONTACT ITERATION = 0, STEP 0
ABSOLUTE RESIDUAL = 6.587e+10
RELATIVE RESIDUAL = 5.414e-01
Interactions:
If # dubious interactions never converges to zero and/or, # released/captured interactions continuously change over many contact iterations:
  Use smaller load step, smoother BC’s, different AL settings
  Evaluate log file and visualize previous load steps to see if the cause is a previously poor contact solution
  Previously static contact solution could be going dynamic: try explicit dynamics, implicit dynamics, more BC’s to maintain static equilibrium, and/or control damped solve

## Slide 185: Log file debugging: control contact
----------------------------------------------------------
MAX GAP = 8.096e-01 PREVIOUS = 0.000e+00
MAX RELATIVE GAP = 1.457e+00 PREVIOUS = 0.000e+00
NUM INTERACTIONS = 82
RELEASED INTERACTIONS = 52
CAPTURED INTERACTIONS = 30
DUBIOUS INTERACTIONS = 0
RELATIVE LMULT CHANGE = 1.000e+00
ACTIVE SET CHANGE
----------------------------------------------------------
CONTACT ITERATION = 0, STEP 0
ABSOLUTE RESIDUAL = 6.587e+10
RELATIVE RESIDUAL = 5.414e-01
Contact Iterations:
Reasonable # of iterations: ~5 to ~50
When to increase max. iterations:
  Residual still steadily decreasing at max. iterations
  Contacts are unstable or frequently changing over time
  Other aspects of problem are temporally non-linear: boundary conditions, thermal conditions, plasticity, failure, …
How to decrease iterations necessary for convergence:
  Smaller load step size
  Come into current load step with a good initial state (evaluate solutions from previous load steps)

## Slide 186: Log file debugging: control contact
----------------------------------------------------------
MAX GAP = 8.096e-01 PREVIOUS = 0.000e+00
MAX RELATIVE GAP = 1.457e+00 PREVIOUS = 0.000e+00
NUM INTERACTIONS = 82
RELEASED INTERACTIONS = 52
CAPTURED INTERACTIONS = 30
DUBIOUS INTERACTIONS = 0
RELATIVE LMULT CHANGE = 1.000e+00
ACTIVE SET CHANGE
----------------------------------------------------------
CONTACT ITERATION = 0, STEP 0
ABSOLUTE RESIDUAL = 6.587e+10
RELATIVE RESIDUAL = 5.414e-01
Absolute / Relative Residual:
Recommendation is to place Control Contact at the outer-most loop (highest level) of the multi-level solve
Therefore, these residuals represent the quality of the solution of each load step
  This impacts: solution state and contact interactions used for subsequent load steps, amount of gap/overlap, etc.

## Slide 187: Other debugging tools
Every problem is different but almost all require one or more of the following in addition to log file parsing:
Visualization. What to look for:
  Unintended gaps and overlaps
  Objects passing through each other where contact is expected
  Non-smooth contact_status and/or contact_force fields
Use ITERATION PLOT in solver command blocks
  This outputs fields for each solution iteration
  Look for when & where the problem is first going awry
Try explicit dynamics to separate implicit solver issues from other issues: contact, BC’s, mesh, material model stability, etc.
Output mesh after INITIAL OVERLAP REMOVAL to detect possible poorly-shaped or inverted elements from the removal process (see user guide for debug output syntax)
Problem simplification/isolation: coarsen mesh, remove blocks, use elastic materials, create restart checkpoints, etc. This can really expedite finding a resolution and simplify communication with the SIERRA/SM support team.

## Slide 188: Additional troubleshooting tips in User Guide: Appendix F

## Slide 189: Debugging example 1: Resistance forge weld
Modeled Physics & Numerics
  Elastoviscoplastic material model
  Electrical-thermal-mechanical coupling
  Curved contact interface
  Multiple constraints (some nodes in symmetry plane also in contact)
  Material softening due to heating
  Contact interactions transitioning from frictional to glued
Applied displacement on top surface in –z direction
Fixed surface
Original problem experiencing issues:
Simplified problem for debugging

## Slide 190: Debugging example 1: Resistance forge weld
Issue: run crashes
Explore the log file:
  Error caught in material model
  Multiple time step cutback attempts due to inverted elements before crash
  No issue with electrical-thermal
Visualize results
  Last converged solution looks wrong
  Finding first occurrence of time step cutbacks can point you to the first accepted bad result
Attempted fixes:
  Increase max iterations of model problem (no noticeable improvement).
  Tighten contact solver tolerance(no noticeable improvement).
  Ungroup interactions (big improvement)
Possibly triggered by a bad solution on the previous step or sudden increase in time step? Code fails to recover from error and run crashes
Time step cutbacks seen also early on in the simulation but code recovered. Time step too big?

## Slide 191: Debugging example 1: Resistance forge weld
Issue: run crashes
Explore the log file:
  Error caught in material model
  Multiple time step cutback attempts due to inverted elements before crash
  No issue with electrical-thermal
Visualize results
  Last converged solution looks wrong
  Finding first occurrence of time step cutbacks can point you to the first accepted bad result
Attempted fixes:
  Increase max iterations of model problem (no noticeable improvement).
  Tighten contact solver tolerance(no noticeable improvement).
  Ungroup interactions (big improvement)
Load step = 45
Last converged state
Load step = 6
Bad solution early on cascades into other potentially bad solutions

## Slide 192: Debugging example 1: Resistance forge weld
Load step = 45
Last converged state
Load step = 6
Bad solution early on cascades into other potentially bad solutions
Issue: run crashes
Explore the log file:
  Error caught in material model
  Multiple time step cutback attempts due to inverted elements before crash
  No issue with electrical-thermal
Visualize results
  Last converged solution looks wrong
  Finding first occurrence of time step cutbacks can point you to the first accepted bad result
Attempted fixes:
  Increase max iterations of model problem (no noticeable improvement).
  Tighten contact solver tolerance(no noticeable improvement).
  Ungroup interactions (big improvement)

## Slide 193: Debugging example 1: Resistance forge weld
Begin Interaction mech_int1
surfaces = block_1, block_2
friction Model = nfd
developer command: group interactions = false
End
begin nodal field dependent friction model nfd
contact transition reduction method = min
initial contact transition value = 0.1 # not bonded
End
Load step = 6
Load step = 6
Issue: run crashes
Explore the log file:
  Error caught in material model
  Multiple time step cutback attempts due to inverted elements before crash
  No issue with electrical-thermal
Visualize results
  Last converged solution looks wrong
  Finding first occurrence of time step cutbacks can point you to the first accepted bad result
Attempted fixes:
  Increase max iterations of model problem (no noticeable improvement).
  Tighten contact solver tolerance(no noticeable improvement).
  Ungroup interactions (big improvement)

## Slide 194: Debugging example 1: Resistance forge weld
Load step = 45
Last converged state
Load step = 79
Last converged state
Issue: run crashes
Explore the log file:
  Error caught in material model
  Multiple time step cutback attempts due to inverted elements before crash
  No issue with electrical-thermal
Visualize results
  Last converged solution looks wrong
  Finding first occurrence of time step cutbacks can point you to the first accepted bad result
Attempted fixes:
  Increase max iterations of model problem (no noticeable improvement).
  Tighten contact solver tolerance(no noticeable improvement).
  Ungroup interactions (big improvement)

## Slide 195: Debugging example 1: Resistance forge weld
Bonded interface
Load Step = 79
The option to ungroup interactions is still in development
Our tests have not justified making it the default
It improves the contact solution for some problems, such as this one with non-planar faces in contact.
Issue: run crashes
Explore the log file:
  Error caught in material model
  Multiple time step cutback attempts due to inverted elements before crash
  No issue with electrical-thermal
Visualize results
  Last converged solution looks wrong
  Finding first occurrence of time step cutbacks can point you to the first accepted bad result
Attempted fixes:
  Increase max iterations of model problem (no noticeable improvement).
  Tighten contact solver tolerance(no noticeable improvement).
  Ungroup interactions (big improvement)

## Slide 196: Debugging example 2: Stiff block on soft block
Modeled Physics & Numerics
Implicit quasi-statics
Large difference in stiffness between contacting blocks
Different mesh sizes between contacting blocks
Large deformation contact
Corner contact
Stick-slip transition
Mean-quadrature hex8
Hyperelastic hourglass control
Initial setup:
contact lost & solver fails at 33% of simulation

## Slide 197: Debugging example 2: Stiff block on soft block
Debugging Process
Observed that corners of cube were penetrating the most
  Changed from face_face to node_face for better corner contact
Aided contact by manually defining most robust side a and side b surfaces:
  Coarse mesh  side a
  Fine mesh  side b
Observed intermittent loss of force_contact of some nodes
  Manually increased search tolerance on interaction (“normal tolerance = <real>”)
Final setup:
better contact enforcement & simulation runs to completion

## Slide 198: Debugging example 3: Pressurized can
Modeled Physics & Numerics
Mean-quadrature hex8
Elasto-visco-plastic constitutive model
Thermal-mechanical (temp-dependent material)
External heating above lid
Ramped internal pressure
Frictional contact between all parts
Contact seating
Transition from static to dynamic as lid/threads disengage due to pressure & thermal softening
Multiple stick-slip transitions
fastener
lid
wall
P(t)
plastic strain
Final state: threads disengaged

## Slide 199: Debugging example 3: Pressurized can
begin implicit dynamics
# switch from statics to dynamics
# before lid starts disengaging
active periods = p2
end
begin adaptive time stepping
cutback factor = 0.5
maximum failure cutbacks = 4
end adaptive time stepping
begin contact definition sliding
skin all blocks = on
begin friction model const_friction
friction coefficient = 0.3
end friction model const_friction
begin interaction defaults
general contact = on
self contact = off
friction model = const_friction
al penalty = 0.005
end interaction defaults
end contact definition sliding
### continued ...
Input Deck Settings of a Successful & Efficient Analysis
begin solver
begin loadstep predictor
type = scale_factor
scale factor = 0.0
end loadstep predictor
begin control contact
target relative residual = 1.0e-4 acceptable relative residual = 1.0e-3
maximum iterations = 50
end control contact
begin cg
target relative residual = 5.0e-5
acceptable relative residual = 1.0e3
maximum iterations = 30
reference = belytschko
begin full tangent preconditioner
nodal preconditioner = probe
minimum smoothing iterations = 5
small number of iterations = 20
end full tangent preconditioner
end cg
end solver

## Slide 200: Debugging example 3: Pressurized can
begin implicit dynamics
# switch from statics to dynamics
# before lid starts disengaging
active periods = p2
end
begin adaptive time stepping
cutback factor = 0.5
maximum failure cutbacks = 4
end adaptive time stepping
begin contact definition sliding
skin all blocks = on
begin friction model const_friction
friction coefficient = 0.3
end friction model const_friction
begin interaction defaults
general contact = on
self contact = off
friction model = const_friction
al penalty = 0.005
end interaction defaults
end contact definition sliding
### continued ...
begin solver
begin loadstep predictor
type = scale_factor
scale factor = 0.0
end loadstep predictor
begin control contact
target relative residual = 1.0e-4 acceptable relative residual = 1.0e-3
maximum iterations = 50
end control contact
begin cg
target relative residual = 5.0e-5
acceptable relative residual = 1.0e3
maximum iterations = 30
reference = belytschko
begin full tangent preconditioner
nodal preconditioner = probe
minimum smoothing iterations = 5
small number of iterations = 20
end full tangent preconditioner
end cg
end solver
Input Deck Settings of a Successful & Efficient Analysis
In the following slides we explore what happens if these settings are used but with one command modified.

## Slide 201: Debugging example 3: Pressurized can
begin implicit dynamics
active periods = p2
end
Implicit Dynamics vs. Quasi-statics When Threads Disengage
# begin implicit dynamics
# active periods = p2
# end
fails: immediately before threads disengaging
runs to completion
last converged solution

## Slide 202: Debugging example 3: Pressurized can
begin interaction defaults
…
al penalty = 0.005
end interaction defaults
Non-default AL Penalty vs. Default
begin interaction defaults
…
# default [al penalty = 1.0]
end interaction defaults
fails: contact seating unsuccessful in first step
runs to completion
last solver iteration from iteration plot

## Slide 203: Debugging example 3: Pressurized can
Skin All Blocks w/ General Contact vs. Specifying Surface-Surface Interactions
contact surface cs5 contains surface_5
contact surface cs6 contains surface_6
begin interaction threads
master = surf_5
slave = surf_6
friction model = const_friction
end interaction threads
... [ring-lid and lid-wall interactions]
fails: inverted elements in first step
runs to completion
begin contact definition sliding
skin all blocks = on
begin interaction defaults
general contact = on
...
last solver iteration from iteration plot

## Slide 204: Debugging example 3: Pressurized can
begin loadstep predictor
type = scale_factor
scale factor = 0.0
end loadstep predictor
Not Using Predictor vs. Using Predictor
begin loadstep predictor
type = scale_factor
scale factor = 1.0
end loadstep predictor
fails: 2 steps before threads disengage
runs to completion
last converged solution

## Slide 205: Debugging example 3: Pressurized can
begin cg
...
begin full tangent preconditioner
...
minimum smoothing iterations = 5
end full tangent preconditioner
end cg
Using Smoothing Iterations vs. Not Using Smoothing Iterations
begin cg
...
begin full tangent preconditioner
...
# default [minimum smoothing iterations = 0]
end full tangent preconditioner
end cg
runs to completion
run time = 5000 sec.
runs to completion
run time = 1300 sec.
~4X slowdown

## Slide 206: Debugging example 3: Pressurized can
begin cg
...
begin full tangent preconditioner
...
small number of iterations = 20
end full tangent preconditioner
end cg
Using Small Number of Iterations vs. Not Using Small Number of Iterations
begin cg
...
begin full tangent preconditioner
...
# default [update tangent every step]
end full tangent preconditioner
end cg
runs to completion
run time = 2700 sec.
runs to completion
run time = 1300 sec.
~2X slowdown

## Slide 207: In summary…
Implicit solvers are demanding:
  Have good element quality
  Should be well-conditioned
  Proper constraints and BCs
  No mesh overlap
Implicit solvers can be finicky
  Every problem is like a new puzzle
  Solver settings for one problem will likely not be applicable to another.
The log file is your #1 source for understanding and debugging implicit solutions.
implicit
,
Implicit solvers are powerful, but demanding tools.

## Slide 208: Closing thoughts
We’ve covered a lot of topics and you should have a better feeling for a few things
What an implicit analysis is doing
The difference between explicit and implicit solvers
“Implicit dynamics” vs. “implicit quasi-statics”
Some strategies for configuring the implicit multi-level solver
Some techniques available for troubleshooting
We’ve made several recommended references for further reading about these topics.
We encourage you to familiarize yourself with these references
Background knowledge of the theoretical underpinnings is very useful

## Slide 209: Closing thoughts – When all else fails…
Even though we’ve done an amazing job presenting this material, we expect you’ll still have trouble from time to time!
Please contact us: sierra-help@sandia.gov
Even better – include a small minimum “failing” example by narrowing down the issue for us. Convince yourself there is an issue by removing complexity from your model. We want this to be a partnership to find resolutions as quickly as possible.
Include an input file (*.i) and mesh file (*.g). Optionally, a log file.
Avoid “include” files if possible when requesting help – they’re often forgotten and can delay resolution.
Avoid sending complex workflows if at all possible. We want to help debug your issue, but we might get stuck trying to understand a custom workflow of complex pre/post-processing scripts or processes.
We’re constantly trying to improve the SIERRA/SM product, help us help you!

## Slide 210: Closing thoughts
There are still dozens of topics we’d love to cover in the future!
Adaptive time stepping advanced configuration and usage techniques
Element death and control failure in implicit solutions
Implicit contact implementation details and options
Level 1 solve options: control failure, control damped solve
More …
We hope you’ve found the class useful for your work!

## Slide 211: Thank you for your participation! Any unanswered questions?